AH10233 Control-break - example of changing interrupt vector            
                                                                        
11/11/85                                                                
BASIC Interpreter by Microsoft                     (6025010)            
BASIC Compiler Version 1.0 (DOS)                   (6024003)            
Portable Personal Computer System Unit/Keyboard    (5155068)            
Personal Computer AT System Unit/Keyboard (5170068, 5170099)            
Personal Computer XT System Unit/Keyboard          (5160087)            
PCjr System Unit/Keyboard                 (4860004, 4860067)            
Personal Computer System Unit/Keyboard             (5150114)            
BASIC Compiler Version 2.0 (DOS)                   (6024216)            
PCjr BASIC (Cartridge)                             (6024101)            
                                                                        
KEYWORDS: INFORMATION                                                   
Following   is  a  program  that  demonstrates  changing  an            
interrupt  vector  from  BASIC.  The vector being changed is            
the Control-break interrupt vector (interrupt number 1B, the            
Keyboard  break  interrupt) located at hex address 6C-6F, or            
decimal   108-111.   The  vector  will  be  changed  to  the            
Dummy_Return   vector,  which   effectively   disables   the            
Control-break   key.  Please  see  the  Technical  Reference            
manual  for  your  system  unit  for  more information about            
interrupt vectors.                                                      
                                                                        
    10 CLS:DEFINT A-I                                                   
    20 DIM A(4)                                                         
    30 DEF SEG=0                                                        
    40 FOR I=1 TO 4                                                     
    50 A(I)=PEEK(107+I) 'Save old interrupt vector                      
    60 NEXT I                                                           
    70 LOCATE 10,18                                                     
    80 PRINT "Press any key to inhibit control-break";                  
    90 A$=INKEY$:IF A$="" THEN GOTO 90                                  
    100 POKE 108,83 'Set to dummy_return vector..                       
    110 POKE 109,255                                                    
    120 POKE 110,0                                                      
    130 POKE 111,18                                                     
    140 LOCATE 15,18                                                    
    150 PRINT "Control-break now inhibited - try it";                   
    160 LOCATE 16,27                                                    
    170 PRINT "(Press spacebar to exit)";                               
    180 A$=INKEY$:IF A$=" " THEN 190 ELSE 180                           
    190 FOR I=1 TO 4                                                    
    200 POKE 107+I,A(I) 'Reset old vector                               
    210 NEXT I                                                          
    220 LOCATE 20,20                                                    
    230 PRINT "Control-break is back on - try it";                      
    240 GOTO 240                                                        
              *** END OF DOCUMENT  ***                                  
                                                                        
Note :  This modification or recommendation has not been subjected to   
        exhaustive testing and may not, in all circumstances, provide   
        a complete solution.                                            
sting and may not, in all circumstances, prov