The McDonnell Douglas FA-18 "Hornet" began flight test in the late 1970s, 
    and a production line was set-up quickly after that.  The Hornet is the U.S. 
    Navy's close-in air-superiority fighter that defends aircraft carrier task forces.
    The Hornet is the Marine Corps' premier attack aircraft, supporting its ground 
    forces.  Whether used by the Navy or Marine Corps, the Hornet is the same 
    plane;  the "F" and "A" designations simply describe its role as a fighter jet 
    or an attack jet.

    The Hornet is a small, relatively low-cost, twin-engine, single-seat jet aircraft 
    which makes it appealing to the Navy and Marines.  The F/A-18 Hornet first 
    flew in November of 1978, but did not officially enter into service until 1983.  
    Australia and Canada also selected the Hornet because of its low cost and 
    versatility.  Another factor in Canada's choice of the Hornet (designated CF-
    18) was that Canada, like the U.S. Navy, uses the "hose and drogue" method 
    of aerial refueling, rather than the "flying boom" method used by the U.S. Air 
    Force.  The Hornet has two engines for increased reliability and can fly to a 
    maximum speed of more than 1,100 MPH at high altitudes or about 750 MPH 
    at low ones.  With an internal fuel load of 1,700 gallons, the plane has a 
    combat radius of about 660 miles for an attack mission.

    The Hornet's armament includes a 20 millimeter cannon mounted on the top
    center of the nose.  This mounting differs from the F-14, F-15, and F-16, which 
    mount the cannon on the side of the fuselage.  In its fighter configuration, the 
    Hornet, like the Falcon, carries AIM-9 Sidewinder air-to-air missiles on wingtip 
    racks.  Other weapons, such as the AIM-7 Sparrow, are carried underwing.  
    For attack/fighter bomber missions, the F/A-18 Hornet's armorer can select 
    from conventional or nuclear bombs and HARM antiradar missiles or Maverick
    air-to-ground missiles.  For its naval attack mission, the Hornet can also carry 
    the AGM-109 Harpoon, a sea-skimming, antiship missile.

    With the Navy and the Marine Corps being the leading edge of military power
    worldwide, it is a surity that when called upon, the F/A-18 will be in the front 
    line leading the way.