NOTE: It seems like "Windows 3.11 for Workgroups" does not need any of
      the following changes.

Windows 3.1 installation tips
=============================

To use Terminate with windows we provide a TERMINAT.PIF and a TERMINAT.ICO.
But you must also make some adjustments to the windows setup first.

Edit SYSTEM.INI

Under [386Enh]:

Com1AutoAssign=0

Under the windows menu: Main / Control Panel / 386 Enhanced

You should read NEVER WARN at the comport you use.

The comport used for modem must not be autoassigned by windows. If you
use COM4, just enter Com4AutoAssign=0

Change the values to match the correct address for the comports.

COM1BASE=3F8h
COM2BASE=2F8h
COM3BASE=3E8h
COM4BASE=2E8h

Other values that can be changed, try reading the docs for windows.

COMIrqSharing=true (This has only effect on EISA and Microchannel machines)
COMBoostTime=10
COM1Buffer=1024
COM2Buffer=1024
COM3Buffer=1024
COM4Buffer=1024

If your modem has a 16550 UART you also have to install another
communication driver to support 16550 UART FIFO in DOS-windows.
Use a driver like CHCOMB.386 (CHCOMB.ARJ which can be downloaded from DAN BBS.

To use the soundblaster card enter under [386Enh]:
DMABUFFERSIZE=059

If you have many problems using the Windows coms-driver you could use the
communication ports directly by changing WIN.INI to:

COM1:=COM1.DOS or
COM2:=COM2.DOS or
COM3:=COM3.DOS or
COM4:=COM4.DOS

Information from Microsoft:

Windows cannot use a serial port if the address is to the right of the
missing port. An example of this problem could be that the modem is on
COM4 and COM3 is not physical present.

Without a physical COM3 the BIOS will find COM4 on address 02E8 and will
call it COM3 in the BIOS field. This confuses Windows so it cannot find
COM4 and thinks that COM3 is on 02E8/IRQ4.

This behaviour is normal for many BIOS's and can be fixed with COMxIRQ=-1
in SYSTEM.INI under the [386Enh] section. For this example should the
following line be inserted in SYSTEM.INI:

  COM3IRQ=-1