ÚÂÄÄ¿ Ú¿ ÂÂÄÄ¿
                                 Ã´    Ã´ Ã´  ³
                                 ÀÁÄÄÙ ÀÙ ÁÁÄÄÙ
 
                    Chief's IDE Drive Identification Utility
 
                                  Version 1.01
 
                 Copyright (C) 1993 by Chief Data Recovery Ltd.
                              All Rights Reserved.
 
 
    INTRODUCTION
    ÄÄÄÄÄÄÄÄÄÄÄÄ
       CID is an IDE (AT-BUS) identification  utility which  displays all
       information anout  an IDE  drive that  is installed  in the system
       even if it is not defined in the CMOS SETUP.
 
       CID Allows you  to view  the information  and to  print it to your
       local attached printer.
 
 
    REQUIREMENTS
    ÄÄÄÄÄÄÄÄÄÄÄÄ
       CIS Requires  an   AT  compatible  machine  with  80286 of  higher
       processor.  It will  not run on XT's and may hang them if you try.
       About 40KB of  free conventional memory and DOS 3.10 or higher are
       also required.
 
 
    OPERATION
    ÄÄÄÄÄÄÄÄÄ
       CID shoud run from  the DOS  prompt by typing the program name and
       pressing the ENTER key.
 
       CID except the  following command  line parameters  in its command
       line:
 
       /? - Display brief usage screen.
       /M - Run in Mono mode (Black & White, Monochrom or LCD).
       /1 - Select drive 1. Default is drive 0.
 
       During the display  of all the drive information you may press the
       F2 key to print  the  information to  your local  printer (LPT1:).
       pressing F1 key  will  display  breif  information aand  copyright
       notice.
 
       Version 1.01 adds the  option to  view the drive's partition table
       to verify that the  drive is  properly installed and the partition
       information match the drive installation parameters.  Pressing the
       SPACE key will toggle  the partition  table view  and the extended
       IDE information.
 
       The toggle mode  is also  available in  the help window to display
       general help,  active keys list and valid command line parameters.
 
 
    WARRANTY
    ÄÄÄÄÄÄÄÄ
       None, Whatsoever. CID is a free program and as such no warranty is
       supplied. You may freely use and distribute CID with no charge and
       at your own risk. CID was tested on several machines and performed
       as specified.
 

    HISTORY
    ÄÄÄÄÄÄÄ
       Version 1.00 - Initial Release.
       Version 1.01 - Added  partition   table  view  and  expanded  help
                      screens.
 
    COMMENTS
    ÄÄÄÄÄÄÄÄ
       Comments,  questions  and  other  information  may be  obtained by
       connecting Chief Data Recovery Ltd. in the following ways:
 
          Chief Data Recovery Ltd.               Phone: +972-8-400-070
          P.O.Box 499 / 15th Habanim St.         Fax  : +972-8-403-295
          Nes-Ziona 70400, ISRAEL.               BBS  : +972-3-9667562
 
          CompuServe ID: 100274,73
          FidoNet : 2:403/138
 
                                   -= EOF =-