Contents



               Chapter 1  The Virtual 386 Write Protect Device       1
                  1.1  Basic Information . . . . . . . . . . . . . . 1
                     1.1.1  Description  . . . . . . . . . . . . . . 1
                  1.2  Introduction  . . . . . . . . . . . . . . . . 1
                     1.2.1  Worlds first Shareware VIRTUAL Device
                            Driver . . . . . . . . . . . . . . . . . 2
                     1.2.2  Low Overhead . . . . . . . . . . . . . . 2
                     1.2.3  Protecting old DOS applications  . . . . 2
                     1.2.4  Optional features & additional options
                            when you register  . . . . . . . . . . . 2
                     1.2.5  Advantages . . . . . . . . . . . . . . . 3
                     1.2.6  Updated Features:  . . . . . . . . . . . 3
                     1.2.7  Updates  . . . . . . . . . . . . . . . . 3
                     1.2.8  Warnings and cautions  . . . . . . . . . 3
                     1.2.9  Trojan and Virus Programs  . . . . . . . 4
                     1.2.10  Background  . . . . . . . . . . . . . . 4
                  1.3  Known problems  . . . . . . . . . . . . . . . 4
                     1.3.1  Entering DOS . . . . . . . . . . . . . . 4
                  1.4  Installation  . . . . . . . . . . . . . . . . 5
                     1.4.1  Copying and naming files . . . . . . . . 5
                     1.4.2  Verifying Installation . . . . . . . . . 6
                  1.5  Features  . . . . . . . . . . . . . . . . . . 6
                  1.6  Restrictions  . . . . . . . . . . . . . . . . 6
                  1.7  Control Program . . . . . . . . . . . . . . . 7
                     1.7.1  Installation . . . . . . . . . . . . . . 7
                     1.7.2  Use  . . . . . . . . . . . . . . . . . . 7
                     1.7.3  Messages . . . . . . . . . . . . . . . . 7
                     1.7.4  Exiting  . . . . . . . . . . . . . . . . 7
                  1.8  Optional Features . . . . . . . . . . . . . . 7
                  1.9  DOS Utilities that are protected by VWPD  . . 8
                     1.9.1  Always Protected . . . . . . . . . . . . 8
                     1.9.2  Protected when write protect is on . . . 8
                  1.10  Advanced Information . . . . . . . . . . . . 8
                     1.10.1  Terminate Task  . . . . . . . . . . . . 8
                     1.10.2  Miscellaneous . . . . . . . . . . . . . 8
                     1.10.3  DOS and Windows Tested  . . . . . . . . 8
                     1.10.4  Custom Windows and OS/2 programming . . 9
                     1.10.5  Supplementary Documentation . . . . . . 9
                  1.11  How to contact for information . . . . . . . 9








                                          i













                                      Chapter 1

                        The Virtual 386 Write Protect Device


          1.1  Basic Information


          Title: Prevents disk corruption and crashes in Windows

          Keywords: VWPD CORRUPT CHKDSK CRASH DISK PROTECT WINDOWS
          SHAREWARE NETWORK TROJAN VIRUS FORMAT

          1.1.1  Description

          VWPD prevents disk corruption from occuring when using CHKDSK
          while Windows is running(see Windows User's Guide p.54). It has a
          write protect feature which can be toggled on/off by the included
          control program. Test suspected Trojan and virus programs with
          secure write protect, enabled(runs in Protected Mode at Ring 0).
          Requires MS Windows 386 Enhanced mode. Documentation included.
          Network compatible. Simple installation. Download in 3 min.


          1.2  Introduction


          The "Virtual Write Protect Device" is a MS Windows 386 Enhanced
          Mode virtual device driver.

          The VWPD protects your hard disk drive from DOS low level sector
          writes. Utilities like PC Tools Compress, Norton's SD, Golden
          Bow's VOPT and disk repair and modification utilities will
          receive an error("disk write protected"), if you attempt to run
          them while MS Windows is running(Enhanced Mode only). The VWPD
          also protects your hard disk from low level formatting and if you
          have used the control program (VWPDCTRL.EXE) to turn on the write
          protect feature you are protected from Interrupt 13h writes.

          Not only are you protected from these common utilities but any
          virus which might attack your system by the same method will be
          stopped dead in it's tracks.

          VWPD is a very simple system. There is the device
          driver(VWPD.386) and there is the control program(VWPDCTRL.EXE).
          Write protect for Interrupt 26 hex is always on.
          Write protect for hard disk formats(INT 13h) is always on.













          Write protect for low level writes(INT 13h) can be toggled on/off
          by the control program.

          This is NOT, repeat NOT an ordinary Windows Device Driver. They
          run at ring 1. VWPD runs at ring 0. It is more secure than code
          that runs at ring 1. Ordinary code that runs at rings 1,2 or 3
          can not touch this driver.  The only way code can run at ring 0
          is be loaded at the time Windows starts up.

          1.2.1  Worlds first Shareware VIRTUAL Device Driver

          I have good reason to be believe that this is the first virtual
          device driver for MS Windows ever released to the Shareware
          market.

          The effort and cost of doing a virtual device driver is not
          trivial. It may be some time before anyone becomes crazy enough
          to do another one.

          If there are any contenders for the worlds first, speak up or
          forever hold your peace. In 20 years no one will care who was
          first! Maybe in 3 weeks.

          For those of you interested in the INNER workings of MS Windows I
          am presently working on a tool similar to David Maxey's "INTRSPY"
          program. The TSR part of intrspy will be replaced by a virtual
          device driver. Then we can watch the protected mode interrupts go
          by. (Intrspy comes with the book "Undocumented DOS" by Andrew
          Schulman, et all).

          1.2.2  Low Overhead

          The performance overhead for this protection is very low. When
          normal programs are running there is minimal overhead. When one
          of these special utilities that uses INT 26h is running it is
          blocked and there is essentially no overhead.

          1.2.3  Protecting old DOS applications

          Our other shareware program system "Windows Safe" requires that
          any DOS program that you do not want to run while Windows is
          running must have a small utility added to the disk to block it
          from running. If you use 386 Enhanced Mode, then VWPD will
          protect you on a SYSTEM WIDE basis. It is not necessary to
          protect each program individually, if what you are trying to
          prevent is low level sector writes to the disk.

          So...what you save is disk space. You gain ease of installation
          and you get virus protection; all at the same time.

          1.2.4  Optional features & additional options when you register

          Custom enhancements and site licenses for larger firms.




                                        - 2 -








          When you register and pay the requested $20 fee you receive an
          enhanced VWPD with many addition features.

          The program which we have provided you in effect for free is not
          a demo or crippled in ANY way. Feel free to use it. I won't waste
          my breath, telling you to register.

          So... I will tell you that you will receive an enhanced kit to
          make it easier for you protect your system from inadvertent and
          malicious disk writes.

          If you would like the additional features, then grab the order
          blank, print it out and send it in.

          1.2.5  Advantages

          Requires only small amount of extra memory to run.
          Not a TSR.
          Prevents many crashes in Windows, especially useful for network
          administrators.

          1.2.6  Updated Features:

          Warning Messages         5-25-91
          Toggle Messages          5-27-91
          Improved Documentation   5-30-91
          DOS Only write protect   6-09-91
          Fixes to version #'s     6-09-91   + warning message
          Fix DOS only bug         6-17-91   Drv. # 1.02, Ctrl. 1.01

          1.2.7  Updates

          VWPD is likely to be enhanced for quite a while as Windows itself
          is being modified and as I discover more refined ways of
          providing the same or improved protection.

          If you have an early version of VWPD V. 1.0. Be sure to look for
          an improved version (1.5) sometime about 7-1-91. I will post it
          to Compuserve and maybe a few other places.

          1.2.8  Warnings and cautions

          I have tested the VWPD system carefully. I believe that VWPD
          should work with ANY application in any situation. However, there
          is no foolproof system against viruses.

          During use, VWPD does absolutely no writing to your disk(s).

          Does not protect Network or RAM disks (drives).

          The device driver and it's control program have been installed
          here and running for about a month(5-30-91). The documentation
          and the control program are a bit rough looking but the driver




                                        - 3 -








          itself seems to be quite stable. Be sure to look for an update
          about 7-1-91.

          If you encounter any problems with the system be sure to let me
          know.

          1.2.9  Trojan and Virus Programs

          The VWPD should be capable of stopping any DOS or Windows program
          that contains a Trojan or virus. The control program is a
          protected mode Windows program and is moderately safe from a DOS
          application. The VWPD itself runs at ring 0 and can only be
          controlled by a protected mode program and the interface to it is
          not documented or published to make it more difficult to bypass
          it.

          Beware of a virtual device driver that contains or is a virus or
          Trojan horse. As long as the ring 0 code in Windows does not
          contain and does not become contaminated by a virus, then Windows
          is much more secure than plain DOS. A Windows Virtual Device
          Driver could become contaminated if the disk file were to be
          modified, but a virus would have tough time changing memory
          during the time Windows was running.

          To test a suspected virus program.

          First turn write protection on using the control program. Also,
          turn warning messages ON, so that you will KNOW that a write was
          attempted. Then run the suspected program. If a write to the disk
          is attempted you will know.

          1.2.10  Background

          VWPD is a general purpose tool that allows you to control writes
          to your disks. Some OLD DOS applications such as disk repair
          utilites should not be run from inside Windows. VWPD provides
          automatic protection for some of these programs. Users that
          accidently run programs like this from inside Windows can cause
          Windows to crash.

          The crash protection described is not complete but it will save
          you some headaches. Utilities that are not safe are those that
          bypass INT 26h and use INT 13h.


          1.3  Known problems


          1.3.1  Entering DOS

          Pageswap device driver causes a write to occur when opening a DOS
          window.

          This can be stopped by:



                                        - 4 -








          Checking the "DOS Only" box when turning on write protect.

          Opening the DOS window before turning on write protect.

          OR:

          Set paging off in the system.ini file. See the installation
          section below.  "paging=FALSE". To turn paging back on set
          "paging=TRUE".


          1.4  Installation


          1.4.1  Copying and naming files

          This is a special WINDOWS Virtual Device Driver. Not a DOS device
          driver that would go in the CONFIG.SYS file.

          To install the Virtual Write Protect Driver(VWPD.386) a line must
          be added to the SYSTEM.INI file located in the Windows directory.
          This line must be placed in the "[386Enh]" section. The line
          should look like this:

          device=vwpd.386


          For instance:

          [386Enh]

          device=vwpd.386

          paging=FALSE

          VCPIWarning=FALSE
          SystemROMBreakPoint=False
          FileSysChange=False
          ebios=ebios.386
          display=*vddvga
          keyboard=*vkd
          mouse=*vmd
          ...
          (etc.)
          ...



          The following information is based on information in the
          sysini2.txt file and explains the general method for adding a
          device.

          ------------------------------------------------------------
          Device=<filename>



                                        - 5 -








            Default: none (Setup assigns appropriate values based on
                       your system configuration.)
            Purpose: Specifies which virtual devices are being used
                     with Windows in 386 enhanced mode. This value
                     appears as the name of a specific virtual device file.
                     Filenames usually include the .386 extension. Multiple
                     device lines are required to run Windows in 386
                     enhanced mode.
            To change: Use Notepad to edit the SYSTEM.INI file.



          Copy the device driver VWPD.386 to the Windows system
          subdirectory. Copy the VWPDCTRL.EXE program to your windows
          subdirectory.

          1.4.2  Verifying Installation

          The simplest way to verify correct installation is to attempt to
          use a disk defragmentor. When run it should stop and report that
          the disk is write protected!

          (not yet provided)The installation disk contains a program
          specifically provided to test that the driver is working. It
          reads one sector off the disk and attempts to write it back
          exactly as it found it. The sector used is the last sector on the
          disk. Not an important sector in a FAT or directory.


          1.5  Features


          Network compatible. Helps prevent Windows from crashing.
          User Transparent
          Simple Installation
          Virus "resistant".
          Very low overhead.
          Contains NO code that can damage your system.


          1.6  Restrictions


          Disks: floppies are NOT protected from formatting.

          Backup programs that do sector reads are not protected. Such
          programs should not be run if the disk can be modified(written
          to) while the backup is in progress.









                                        - 6 -








          1.7  Control Program


          VWPD comes with control program that allows you to turn write
          protection on and off.

          It also has a status box to inform you as to the state of the
          device driver.

          1.7.1  Installation

          Copy the VWPDCTRL.EXE file to your windows subdirectory.

          1.7.2  Use

          To turn write protect on/off and toggle warning messages click on
          the "control" menu item. Toggle the appropriate options on or
          off. If the OK button is selected and write protect is set on;
          then VWPDCTRL will minimize itself automatically.

          The DOS Only button allows write protect to be set on, for DOS
          windows only.

          1.7.3  Messages

          VWPD will display only one message if messaging is enabled and
          write protect is on. Due to the fact that messages are brought
          from disk and disk interrupts are NOT re-entrant, in order to put
          up a message it is necessary to queue the message. This means
          that there is a delay before the message appears on the screen.
          In the case of 486 cpu it's about 1/2 second.

          1.7.4  Exiting

          Failure to close VWPDCTRL or turn write protect off before
          attempting to exit Windows will cause several annoying system
          write protect messages to be generated. The consequence of this
          is usually not harmful, but should be avoided.


          1.8  Optional Features


          A version with enhanced features is under development. This will
          provide options to protect individual floppies drives when 386
          mode Windows is running, as well as some other features.

          Read Sector protection.
          Format protection (by floppy)
          Low level write protection by task.
          Protection for all writes, by task.
          Toggle protection on/off by task, by function, by drive.
          I/O port protection.
          Hiding Windows from a virus.



                                        - 7 -








          Call for information.


          1.9  DOS Utilities that are protected by VWPD


          1.9.1  Always Protected

          CHKDSK
          RECOVER

          (Tested in DOS 3.30)If run from Windows while VWPD is installed
          these programs will not write to the disk. They are safe to use.

          1.9.2  Protected when write protect is on

          DOS FORMAT is protected.
          PC Tools Format is  protected.
          FDISK is protected.


          1.10  Advanced Information


          1.10.1  Terminate Task

          VWPD can be used if you want to test a specific program, possibly
          containing a virus. If an attempt is made to write to the disk, a
          warning message will be displayed. You may choose to continue
          (OK) or cancel in which case the task that was running will be
          closed. If you choose to cancel, after our warning message you
          will also get a Windows error message telling you that you must
          reboot. This not necessary, the message is in error. You may
          safely continue(this last statement is being tested, but believed
          to be correct).

          1.10.2  Miscellaneous

          VWPD is a virtual device driver, NOT a program. It runs at ring 0
          which means that no program can modify it while it is running.
          Ring 0 is a hardware feature of the 80386, 80486 processors. This
          driver does NOT work in standard or real modes.

          Windows in standard (286) mode is not as vulnerable to ill-
          behaved applications as enhanced mode is. At this time we do not
          offer a driver that works in 286 mode.

          1.10.3  DOS and Windows Tested

          Tested under DOS 3.30 and Windows 3.0a on a 80486 processor.
          Tested under DOS 5.0.

          Requires DOS 3.x or higher. Windows 3.x or higher(386 Enhanced
          mode)



                                        - 8 -








          Works with DOS 3.x, 4.x and 5.x
          Runs only on 386 and above machines. Will not run on
          8088,8086 or 80286.

          1.10.4  Custom Windows and OS/2 programming

          We do applications and device drivers, call or write for
          information.

          Old DOS applications should be modified to be Windows aware. If
          you have a DOS product and need technical help to update it, we
          can do the job

          1.10.5  Supplementary Documentation

          The registered kit contains a subdirectory that has several files
          totaling over 60,000 characters of documentation, most of it
          related to network issues.

          See also:
          Byte Magazine, Networking Windows, Mar. 91, p.299-307.
          Your Windows directory (win3?), the text file: networks.txt.


          Provided as is, without a warranty.


          1.11  How to contact for information


          Mom's Software
          Box 449. 391 So. Pacific St.
          Rockaway, OR 97136
          503-355-2281
          CIS 71171,47






















                                        - 9 -