Proposed Specification for MIXER API
		 copyright Media Vision (c) 1991
		   version 0.6b -- Ken Nicholson

		  	

MCIMIXER.DRV	MCI interface to the mixer driver
MMMIXER.DLL  	Multimedia Mixer DLL
MVMIXER.DRV	Media Vision Mixer driver


THE MULTIMEDIA MIXER DLL

The Multimedia Windows Mixer DLL, as proposed by Media Vision, is a
library of generalized routines that provides a common,	device-independent
interface to software controllable mixers.  Its design is based on the uses
and functionality of real world audio mixers.

This DLL gives the MultiMedia application programmer control over a complete
range of audio capabilites.  Every conceivable audio mixing, patching,
equalization and amplification need can be handled by this DLL and its API.
It is capable of supporting mixing features far beyond those available
with today's PC hardware.


WHY A MULTIMEDIA MIXER ?

The Multimedia PC Specification version 1 (May 13,1991) calls for 
"On-board analog audio mixing capabilities," requiring "... input
from three (recommended four) sources and [must] present the sources as
a stereo, line-level audio signal at the back panel. ... Individual
audio source and master digital volume control registers and extra
line-level audio sources are highly recommended."

Such hardware requires a set of standard functions calls (API's) that
will handle volume changes in a device-independent and extensible way.
Furthermore, there are a number of issues, apart from the setting of
an input's or an output's volume levels, that should be handled in a
standard way.  Functions such as equalization, special effects, patch
changes, device association, connection mapping, smooth timed transitions,
power-up settings and device sharing were not addressed by the November Beta
release of the Multimedia Windows Development Kit.

What is provided? The WAVEOUT and MIDIOUT drivers have Get- and SetVolume
entry points for control of a device's output volume.  In addition, the
Multimedia Extensions define an AUX device type that allows
applications to get and set the volumes of additional devices.  The
only two types of AUX devices defined are CD audio and auxillary
input.

In the current design of the Multimedia Extensions, there is no link
between an AUX device and the audio device associated with it.  It
may be assumed, when there is only one AUX device, that it controls
the audio output of the CD-ROM drive.  But in the presence of multiple
AUX devices there is no mechanism for an application to determine 
which AUX device to control to change the CD volume.  Varying
AUX-to-Device association will cause chaos for application writers.

This raises the question of volume control for devices in general.
Most consumer audio devices (cassette decks, turntables, video disk
players, televisions) don't have a variable line output. These
devices rely on a mixer or integrated amplifier to control the volume
level.  The term "attenuator" is applied to controls that vary the
line output of a device. 

Attenuation of PCM and MIDI audio output is not something users need
concern themselves with and therefore volume control functions do not
belong in waveout and midiout drivers; volume control is properly a
mixing function.  Users and multimedia authors will want to individually
adjust the relative volumes of a number of device outputs and this is the
primary need for a mixer.  The Mixer API solves this problem by supporting
volume controls on each of any number of mixer inputs as well supporting
volume controls for each mixer output.

Some professional audio mixers feature a myriad of knobs to enhance or
alter input audio.  Among these are controls for bass, midrange and treble, 
controls to add reverb, effects and stereo-mono crossover.  In fact, Media
Vision's Pro-Audio Spectrum supports many of these features.  The
existing Multimedia Windows API's don't address these features.

Another feature of the MMMIXER.DLL API set is its ability to maintain and
coordinate mixer patch information.  A mixer device that supports
software selectable input patching would allow any one of several audio
devices to be "patched" to a mixer input.  Similarly an application
can interrogate the mixer API to find out which devices are connected
to which mixer inputs.

Fading the volume up of one sound source while fading out the volume
of another seems such an intrinsically necessary function for multimedia
that we have incorporated it into the DLL.  Without this feature, the
application programmer would be required to send auxSetVolume
messages in "ping-pong" fashion to the devices to be cross-faded.

Some users will have powered speakers with no volume control. MMWindows
start-up sounds are capable of producing DEAFENING DECIBELS OF DIN. 
Mixer drivers conforming to this spec read WIN.INI to determine the
desired start-up, or mixer reset, volume settings.

Frequently an application will fill the entire screen and on occasion
a Multimedia application will suprise the user with unexpectedly loud
audio.  Such moments find the user frantically trying to bring up the
volume control application in order to lower the volume.  An equally 
dismaying situation is starting a multimedia application only to
discover that the volumes are too low for the sound to be audible.
The MMMIXER.DLL intercepts the CTRL-ALT-U and CTRL-ALT-D sequences
and translates them into driver volume up and down calls.  This
allows the user to quickly change volumes up and down.

Media Vision has developed the Multimedia Windows DLL to address these and
other issues in audio control on the MPC.  We gratefully acknowledge 
Microsoft and especially the members of the Multimedia Windows
Development Team for their advice and assistance in developing the
Multimedia Mixer DLL and the Media Vision Mixer driver.
					    

MEDIA VISION IMPLEMENTATION

The Multimedia Mixer DLL is capable of supporting virtually any type
of mixing hardware.  The limitations of the Pro AudioSpectrum mixing 
hardware should not be confused with the capabilities of the
Multimedia Mixer DLL.

MVMIXER.DRV is implemented as a single Mixer device.  This mixer has
seven input lines and two output lines.  The Pro AudioSpectrum 16 has
new mixer circuitry that allows 8 input lines.

The standard input lines are by default patched to:
1) FM SYNTHESIZER	      5) MICROPHONE
2) RECORD MONITOR    	      6) WAVE (PCM)
3) AUXILLARY INPUT	      7) PC speaker
4) INTERNAL CD		      8) Snd Blaster WAVE (mono PCM)	

On the Pro AudioSpectrum and Pro AudioSpectrum Plus, Input #2 is the mix
of all devices being routed to Output #2.  For the Pro AudioSpectrum 16,
Input #2 becomes a second internal CD connector.

Each input can be connected to one (but not both) of the two outputs.
1) PLAY	  (Line Out)
2) RECORD (Wave In)

Output #1, apart from supporting volume control, supports treble and
bass, loudness, stereo enhance and mute.
Output #2  supports volume control on the Pro-16 only.  	

Input #2 should not be patched to Output #2. 
Input #6 should be patched to Output #2 during playback for proper
waveform filtering.  This is only necessary on the 8-bit Pro
AudioSpectrum.

mixGetDevCaps returns the following structure:
    
MIXERCAPS MVMixer= {
    MM_MEDIAVISION,             // manufacturer id
    MM_PROAUD_MIXER,		// product id
    (VERSION) 0x100,  		// version of the driver
    "Pro AudioSpectrum",	// product name (NULL terminated string)
    7,				// number of inputs  supported.
    2,				// number of outputs supported.
    9, 				// number of input patches supported.
    3,				// number of output patches supported.
    MIXERCAP_MANUALPATCHSWITCH,	// supports some manual   patching
    NULL			// reserved
    };



A Line Capabaility structure for the Pro Audio Spectrum Mixer
would look like this:
{
wNumber	    =0;   	   	// This is the current caps for input # 0
dwDeviceType=MIX_MICROPHONE	// Microphone currently patched;
	    +MIX_USER_CONNECTED;// Requires user to plug it in (for prompting)
wNumSoftPatches=1;	   	// This input always patched to the Microphone
wPatchNumber=0;	   		// the only mic
wNumChannels=2;	   		// The mic is actually mono with a splitter
dwSupport   =MIX_SUPPORT_LRVOLUME	// supported functionality 
szIOname    ="Line 1: Microphone Jack"	// Input Name
szPname     ="MIC";		  	// patch name 
}



Each Mixer has a built in number of INPUT and OUTPUT patches. They
are referenced by an ordinal number starting from zero.  Patch number
zero is always defined as NO CONNECT.

Here is the capability structure for Output #1:

{
wPatchNumber =1;	      	  // This patch's ordinal number
dwDeviceType =MIX_AMPLIFIER|	  // device connected is amplifier
	      MIX_LISTENER|	  // all output patches are listeners
              MIX_USER_CONNECTED; // requires a cable connection
dwLineNumbers=1<<0; 		  // bit-field, lines connectable to
szPname[]    ="MASTER";		  // patch name (NULL terminated string)
dwAssociation=NULL;   		  // HIWORD=type, LOWORD=device
dwReserved1  =NULL;  	  	  // reserved for future use
} 



//////////////////////////////////////////////////////////////////////
//////////////////////////////////////////////////////////////////////



		        MIXER API OVERVIEW



MIXER GENERAL FUNCTIONS:

mixGetNumDevs 		- returns the number of mixer devices
mixGetDevCaps 		- provides information on mixer device capability
mixOpen 		- opens mixer device
mixClose		- closes mixer device
mixGetErrorText 	- gets a text string corresponding to error number

MIXER PRESET FUNCTIONS:

mixReset		- resets mixer inputs, volumes, patches etc.
mixGetState 		- gets current state of the mixer device
mixSetState		- sets mixer state with optional timed fade
mixGetFadeStatus	- returns time remaining of current fadeprocess

// INPUT TO OUTPUT CONNECTION 

mixGetConnections	- gets the connection map of an input or output
mixSetConnections	- sets input to output connection map

// LINE CONTROLS
mixGetControl		- gets the setting of a line's control
mixSetControl		- sets the level of a line's control
mixGetLineInfo		- gets functionality and current status of a line

// PATCH CALLS
mixGetPatch		- gets a line's patch number
mixSetPatch		- sets a line's patch information
mixGetPatchInfo		- returns information on a standard mixerpatch

// DEVICE ORIENTED CALLS
mixGetDeviceName	- converts device type to device name
mixGetDeviceLines	- finds which lines have a specified device 
mixSetDeviceConnections	- performs abstract device connection
mixGetDeviceConnections - determines device types connected







MIXER DEVICE GENERAL FUNCTIONS

mixGetNumDevs 		- returns the number of mixer devices
mixGetDevCaps 		- provides information on mixer device capability
mixOpen 		- opens mixer device
mixClose		- closes mixer device
mixGetErrorText 	- gets a text string corresponding to error number


______________________________________________________________________


Syntax		WORD mixGetNumDevs(void)
		This function retrieves the number of mixer devices
		present in the system.

Parameters	None

Return Value	Returns the number of mixer devices present in the
		system

______________________________________________________________________

Syntax		mixGetDevCaps(wDeviceID, lpCaps, wSize)

Parameters	WORD  wDeviceID
		  Identifies the mixer device to be queried.

		LPMIXERCAPS  lpCaps
		  Specifies a far pointer to a MIXERCAPS structure. 
		  This structure is filled with information about the
		  capabilities of the device.			

		WORD  wSize	
		  Specifies the size of the MIXERCAPS structure.

Return Value	When the wDeviceID is non-zero, the return value will
		be MIXERR_NOERR (zero) if the function was successful.
		If wDeviceID is zero, the return value is the size of 
		the drivers MIXERCAPS structure.

Comments	Use mixGetDevCaps to determine the number of mixer
		devices present in the system.  The Device ID specified
		by wDeviceID varies from zero to one less than the number
		of devices present. Only wSize bytes(or less of information
		will be copied to the location pointed to by lpCaps.  If
		wSize is 0, nothing will be copied and MMSYSERR_NOERROR is
		returned.


See Also	mixGetNumDevs
______________________________________________________________________

Syntax		mixOpen(lphMixer, wDeviceID, dwFlags)
		
		This function opens a specified mixer device.
		

Parameters	LPHMIXER lphMixer
		  Specifies a far pointer to an HMIXER handle.  This
		  location is filled with a handle identifying the
		  opened mixer device.
		

		WORD  wDeviceID

		DWORD dwFlags
		  Specifies flags for opening the device


Return Value	Returns zero if the function was successful. 
		Otherwise, it returns an error. 

Comments	Use mixOpen before making any control/enquiry calls
		to the mixer driver.
		

See Also	mixClose
______________________________________________________________________

Syntax		mixClose(hMixer)

Parameters	HMIXER	hMixer

Return Value	Returns zero if the function was successful. 
		Otherwise, it returns an error. Possible errors are:

		MMSYSERR_INVALHANDLE
		   Specified device handle is invalid.

See Also	mixOpen
______________________________________________________________________

Syntax		mixGetErrorText(wError, lpText, wSize)
	
		This function retrieves a textual description of the
		error identified by the specified error number.

Parameters	WORD  wError
		  Specifies the error number.

		LPSTR lpText
		  Specifies a far pointer to a buffer which is filled
		  with the textual error description.

		WORD  wSize
		  Specifies the length of the buffer pointerd to by
		  lpText.

Return Value	Returns the length of the string copied to zero if the function was successful. 
		  
______________________________________________________________________





MIXER PRESET FUNCTIONS

mixReset		- resets mixer inputs, volumes, patches etc.
mixGetState 		- gets current state of the mixer device
mixSetState		- sets current state of the mixer device
mixGetFadeStatus	- returns time remaining of current fadeprocess


______________________________________________________________________

Syntax		mixReset(hMixer)

		Resets the mixer to a default state.  The default
		state is read from the WIN.INI file.

Parameters	HMIXER	hMixer
		  Identifies the mixer device to be reset.


Return Value	Returns zero if the function was successful. 
		Otherwise, it returns an error.

See Also	mixOpen, mixGetSetup, mixSetSetup

______________________________________________________________________

Syntax		mixGetState(hMixer, lphMixerState, lpwSize)

		Returns a handle to a structure containing the
		current state of the mixer.  The structure is
		defined by the device.

Parameters	HMIXER	 hMixer
		  Identifies the mixer device to be used.

		LPHANDLE lphMixerState
		  Specifies a far pointer to a handle to where the mixer
		  state information is saved.

		LPWORD   lpwSize
		  Specifies a far pointer to a word where the size of
		  the mixer state information is stored.


Return Value	Returns zero if the function was successful. 
		Otherwise, it returns an error. Possible errors are:

		MIXERR_BADMIXERPTR	null pointer to mixer
		  
Comments	This function is used to save the current state of 
		the specified mixer device.  

See Also	mixSetState
______________________________________________________________________

Syntax		mixSetState(hMixer,lpMixerState,wSize,dwTime,
			    dwFlags,dwCallback);
	
		Restores the mixer to a saved state.

Parameters	HMIXER	hMixer
		  Identifies the mixer device to be used.

		LPMIXERSTATE lpMixerState
		  Handle to a mixer state structure as returned by
		  the mixGetState function.

		WORD	wSize
		  Size of the mixer state structure.

		DWORD	dwTime
		  The high word is delay time in tenths of seconds.
		  The low word is the duration of the fade in tenths
		  of seconds.  A dwTime value of zero results in an
		  instant mixer setting.

		DWORD	dwFlags
		  MIX_FADE_OVERRIDE	override a fade in progress
		
		DWORD	dwCallback
		  Address of a procedure to be called when fade is
		  complete.  Note: this has not yet been implemented


Return Value	Returns zero if the function was successful. 
		Otherwise, it returns an error. Possible errors are:

		MIXERR_FADEINPROGRESS	
		  
		  
Comments	If wSize is not correct, this function will be
		rejected.

See Also	mixGetState, mixGetFadeStatus

______________________________________________________________________

Syntax		mixGetFadeStatus(hMixer,lpdwTime)

Parameters	HMIXER	 hMixer
		  Identifies the mixer device to be used.

		LPDWORD  lpdwTime
		  The high word is the delay time remaining in tenths
		  of seconds.
		  The low word is the fade time remaining in tenths
		  of seconds.
		  An lpdwTime value of zero indicates no fade is in
		  progress.

Return Value	Returns zero if the function was successful. 

Comments	Status indicators displaying the time remaining of
		a fade may wish to call this function upon receipt of
		any of the following MIXER MESSAGES:

		  WM_MIX_CONTROLCHANGED	  
		  WM_MIX_CONNECTIONCHANGED  
		  WM_MIX_PATCHCHANGED	  

See Also 	mixSetState
		

______________________________________________________________________





// INPUT TO OUTPUT CONNECTION 

mixGetConnections	- gets the connection map of an input or output
mixSetConnections	- sets input to output connection map

______________________________________________________________________

Syntax		mixGetConnections(hMixer,WORD wLine, LPDWORD lpdwConnections);

Parameters	HMIXER	 hMixer
		  Identifies the mixer device to be used.

		WORD 	 wLine
		  The low byte indicates the mixer line to get the
		  connections information for.
		  The high byte indicates whether the line is an
		  input line or an output line. The following 
		  macros (equates) are used for the high byte:
		      MIX_INPUT	
		      MIX_OUTPUT

		LPDWORD  lpdwConnections
		  A far pointer to a DWORD where the connection
		  information is to be stored.  Each bit of the
		  double word represents a mixer line.  If the
		  bit is 1, wLine is connected to that line.
		  For example, assume wLine=0x0000, indicating Input
		  Line #1.  If that Input line is connected to Output
		  Line #0, bit 0 of *lpdwConnections will be set.
		  Logically, connection information can only be
		  maintained for a mixer with a maximum of 32 inputs
		  and 32 outputs.	

Return Value	Returns zero if the function was successful. 
		Possible Errors:
		    MIXERR_INVALINPUT 	   illegal input line	
		    MIXERR_INVALOUTPUT	   illegal output line 

Comments	

See Also 	mixSetConnections
		

______________________________________________________________________


Syntax		mixSetConnections(Mixer,WORD wLine, DWORD dwConnections);

Parameters	HMIXER	 hMixer
		  Identifies the mixer device to be used.
			       '
		WORD 	 wLine
		  The low byte indicates the mixer line to get the
		  connections information for.
		  The high byte indicates whether the line is an
		  input line or an output line. The following 
		  macros (equates) are used for the high byte:
		      MIX_INPUT	
		      MIX_OUTPUT
		  	
		DWORD  dwConnections
		  This parameter specifies the connection map for the
		  given line of the mixer.  If wLine refers to an
		  input Line, the outputs specified by this parameter
		  will be connected to that input. Bit 0 refers to
		  line 0, bit 1 to line 1, etc.


Return Value	Returns zero if the function was successful. 
		Possible Errors:
		    MIXERR_INVALINPUT 	   illegal input line	
		    MIXERR_INVALOUTPUT	   illegal output line 

Comments	This function allows inputs to be selectively patched
		to one or more outputs.  It also allows outputs to
		be connected to one or more inputs.  This function
		allows the caller to say "connect input lines 1, 3 and 5
		to output #1" or "connect input line 4 to outputs 1 and 2"
		If the hardware cannot support all connections requested,
		the mixer driver will connect the lower numbered lines
		first.  Calling mixGetConnections after	mixSetConnections
		is recommended for verification of requested connections.

See Also 	mixGetConnections
		

______________________________________________________________________





// LINE CONTROLS
mixGetControl		- gets the setting of a line's control
mixSetControl		- sets the level of a line's control
mixGetLineInfo		- gets support functionality of a line

______________________________________________________________________

Syntax		mixGetControl(hMixer, wLineNum, dwControl, lpdwSetting);

Parameters	HMIXER	hMixer
		  Identifies the mixer device to be used.

		WORD  	wLineNum
		  The low byte indicates the mixer line to get the
		  connections information for.
		  The high byte indicates whether the line is an
		  input line or an output line. The following 
		  macros (equates) are used for the high byte:
		      MIX_INPUT	
		      MIX_OUTPUT

		DWORD	dwControl
		  Specifies the control to get the setting of.
		  Here is the current list of possible controls:

		      MIX_SUPPORT_LRVOLUME       left-right volume control
		      MIX_SUPPORT_ALC	       	 Auto Level Control
		      MIX_SUPPORT_BMT	       	 B-M-T equalization
		      MIX_SUPPORT_CROSSOVER      crossover change
		      MIX_SUPPORT_LOUDNESS       loudness equalization
		      MIX_SUPPORT_MUTE	       	 channel mute
		      MIX_SUPPORT_REVERB	 reverb 
		      MIX_SUPPORT_STEREOENHANCE  stereo enhance 
		      MIX_SUPPORT_CUSTOM1	 custom effect #1
		      MIX_SUPPORT_CUSTOM2	 custom effect #2
		      MIX_SUPPORT_CUSTOM3	 custom effect #3

		LPDWORD lpdwSetting
		  Specifies a far pointer to a location that will be
		  filled with the current Control setting.  For
		  stereo controls, the high-order word of this
		  location contains the left channel setting and
		  the low-order word contains the right channel setting.
		  A value of 0xFFFF represents full intensity and a value
		  of 0x0000 is full cutout.

Return Value	Returns zero if the function was successful. 
		Otherwise, it returns an error. Possible errors are:

		    MIXERR_INVALINPUT 	   illegal input line	
		    MIXERR_INVALOUTPUT	   illegal output line 
		    MIXERR_NOTSUPPORTED	        control not supported 	

		  
See Also	mixSetControl
______________________________________________________________________

Syntax		mixSetControl(hMixer, wLineNum, dwControl, dwSetting)

Parameters	HMIXER	hMixer
		  Identifies the mixer device to be used.

	 	WORD	wLineNum
		  The low byte indicates the mixer line to get the
		  connections information for.
		  The high byte indicates whether the line is an
		  input line or an output line. The following 
		  macros (equates) are used for the high byte:
		      MIX_INPUT	
		      MIX_OUTPUT
		  Specifies the input to set Control for

		DWORD	dwControl
		  Specifies the control to set
		  Here is the current list of possible controls:

		      MIX_SUPPORT_LRVOLUME       left-right volume control
		      MIX_SUPPORT_ALC	       Auto Level Control
		      MIX_SUPPORT_BMT	       B-M-T equalization
		      MIX_SUPPORT_CROSSOVER      crossover change
		      MIX_SUPPORT_LOUDNESS       loudness equalization
		      MIX_SUPPORT_MUTE	       channel mute
		      MIX_SUPPORT_REVERB	       reverb 
		      MIX_SUPPORT_STEREOENHANCE  stereo enhance 
		      MIX_SUPPORT_CUSTOM1	       custom effect #1
		      MIX_SUPPORT_CUSTOM2	       custom effect #2
		      MIX_SUPPORT_CUSTOM3	       custom effect #3

		DWORD	dwSetting
		  Specifies a far pointer to a location that will be
		  filled with the current Control setting.  For
		  stereo controls, the high-order word of this
		  location contains the left channel setting and
		  the low-order word contains the right channel setting.
		  A value of 0xFFFF represents full intensity and a value
		  of 0x0000 is full cutout.

Return Value	Returns zero if the function was successful. 
		Otherwise, it returns an error. Possible errors are:

		    MIXERR_INVALINPUT 	   illegal input line	
		    MIXERR_INVALOUTPUT	   illegal output line 
		    MIXERR_NOTSUPPORTED	   control not supported 	
		  
See Also	mixGetControl, CONTROL SETTING NOTES

_____________________________________________________________________


Syntax		mixGetLineInfo(hMixer, wLineNum, lpInfo, wSize);

		Retrieves information about the specified input's
		capabilities.

Parameters	HMIXER	hMixer
		  Identifies the mixer device to be used.

		WORD  	wLineNum
		  The low byte indicates the mixer line to get the
		  connections information for.
		  The high byte indicates whether the line is an
		  input line or an output line. The following 
		  macros (equates) are used for the high byte:
		      MIX_INPUT	
		      MIX_OUTPUT

		LPMIXERLINEINFO  lpInfo
		  Specifiies a far pointer to be filled with the capability
		  information for the specified input.

		WORD  wSize	
		  Specifies the size of the LPMIXERLINEINFO structure.


Return Value	Returns zero if the function was successful. 

Comments	

See Also	

______________________________________________________________________



// PATCH CALLS
mixGetPatch		- gets a line's patch number
mixSetPatch		- sets a line's patch information
mixGetPatchInfo		- returns information on a standard mixerpatch

______________________________________________________________________

Syntax		mixGetPatch(hMixer,wLineNum, lpwPatchNum);

		Returns information regarding a specific input patch
		that can be selected into an input

Parameters	HMIXER	hMixer
		  Identifies the mixer device to be used.

		WORD  	wLineNum
		  The low byte indicates the mixer line to get the
		  connections information for.
		  The high byte indicates whether the line is an
		  input line or an output line. The following 
		  macros (equates) are used for the high byte:
		      MIX_INPUT	
		      MIX_OUTPUT

		LPWORD	lpwPatchNum
		  Destination for the patch number.  A value of -1
		  signifies a user-defined patch.			  
		  
Return Value	Returns zero if the function was successful. 
		Otherwise, it returns an error. Possible errors are:
		
		    MIXERR_INVALINPUT 	   illegal input line	
		    MIXERR_INVALOUTPUT	   illegal output line 

Comments	The range of wPatchNum must be from 0 to 1 less than
		the number of software patches returned in 
		mixGetDevCaps.

See Also	mixSetPatch, mixGetPatchInfo

______________________________________________________________________

Syntax		mixSetPatch(hMixer,wLine, wPatchNum,lpPatch,wSize);

		Allows the user to set the patch of an input to
		another device.  

Parameters	HMIXER	hMixer
		  Identifies the mixer device to be used.

		WORD  	wLine
		  The low byte indicates the mixer line to get the
		  connections information for.
		  The high byte indicates whether the line is an
		  input line or an output line. The following 
		  macros (equates) are used for the high byte:
		      MIX_INPUT	
		      MIX_OUTPUT
							   
		WORD	wPatchNum
		  Specifies the patch number to set.  Each mixer
		  driver has a number of internal patches that
	  	  are selected by this parameter.	
		  
		LPPATCHINFO lpInfo
		  If this parameter is not NULL, the wPatchNum
		  parameter is ignored and the PATCHINFO structure
		  pointed to is used to set the patch information.
		  The patch number assigned will be -1;	

		WORD    wSize
		  Specifies size of PATCHINFO structure


Return Value	Returns zero if the function was successful. 
		Otherwise, it returns an error. Possible errors are:
		  
		    MIXERR_INVALINPUT 	   illegal input line	
		    MIXERR_INVALOUTPUT	   illegal output line 
		    MIXERR_PATCHMISMATCH   patch-to-line mismatch

Comments	The MIX_USER_CONNECTED bit may be OR'd with the patch
		type to indicate a patch that is to be connected by
		the user rather than one that is selected via
		software control.  Applications should check this bit
		at initialization time to advise users to make the
		external connection.  If the patch number of a user-
		connected patch is illegal, the driver's default
		patch for that line will be used.
		
See Also	mixGetPatchInfo, mixGetPatch
______________________________________________________________________

Syntax		mixGetPatchInfo(hMixer,wPatchNum,lpInfo,wSize);

		Returns information about a pre-defined patch.

Parameters	HMIXER	hMixer
		  Identifies the mixer device to be used.

		WORD	wPatchNum
		  Specifies the patch number to set.  Each mixer
		  driver has a number of internal patches that
	  	  are selected by this parameter.
		  
		LPPATCHINFO lpInfo
		  If this parameter is not NULL, the wPatchNum
		  parameter is ignored and the PATCHINFO structure
		  pointed to is used to set the patch information.

		WORD    wSize
		  Specifies size of PATCHINFO structure


Return Value	Returns zero if the function was successful. 
		Otherwise, it returns an error. Possible errors are:
		  
		    MIXERR_INVALPATCH 	   patch number out of range

Comments	The current patch information for a line is  
		available by calling mixGetLineInfo.  Now that 
		patch information is stored in WIN.INI, the default
		patch information is automatically overridden.  In
		most cases the wPatchNum will be -1.  User defined
		patch information is not returned by this call.

		
See Also	mixGetPatch, mixSetPatch, mixGetLineInfo
______________________________________________________________________

// DEVICE ORIENTED CALLS
mixGetDeviceName	- converts device type to device name
mixGetDeviceLines	- finds which lines have a specified device 
mixSetDeviceConnections	- performs abstract device connection
mixGetDeviceConnections - determines device types connected

______________________________________________________________________

Syntax		mixGetDeviceName(dwDeviceType, lpDeviceName, wSize);

		Returns information regarding a specific input patch
		that can be selected into an input

Parameters	DWORD	dwDeviceType
		  A 32-bit value indication the device type

		LPSTR	lpDeviceName
		  points to the destination for the device name

		WORD  	wSize
		  buffers size pointed to by lpDeviceName	
		  If wSize <= MIX_DEVICESHORTNAME, the three letter
		  standard device mnemonic string will be copied to 
		  the buffer.  In all cases wSize will be the limit
		  of characters copied.
		  
Return Value	Returns zero if the function was successful. 
		
Comments	The device short name is intended for display in
		dialog boxes and in win.ini's mixer configuration
		settings.  

See Also	mixGetDeviceLines, mixGetDeviceConnections

______________________________________________________________________


Syntax		mixGetDeviceLines(hMixer,lpDeviceLines);
		
///  Given a device type, this function will report the lines that the given
///  device is connected to.  If the association is not NULL, only
///  lines with the same association will be reported.  Otherwise, all
///  devices of the given type are reported on. 
///

Parameters	HMIXER	hMixer
		  Identifies the mixer device to be used.

		LPDEVICELINES lpDeviceLines
		  far pointer to DEVICELINES data structure

		struct {
		DWORD 	dwDeviceType;	 // aka technology
		WORD	wNumDevices;	 // return value: # lines with device found
		DWORD	dwLines;	 // return value: line map
		DWORD	dwAssociation;	 // for exclusive search
		} DEVICELINES;

typedef DEVICELINES FAR *LPDEVICELINES;

		  
		  
Return Value	Returns zero if the function was successful. 

Comments	Be sure that the dwAssociation element of the
		DEVICELINES structure is NULL unless you intend
		to find a specific device line of which the
		association has been established.

See Also	mixGetDeviceConnections, mixGetPatchInfo

______________________________________________________________________

Syntax		mixGetDeviceConnections(hMixer,lpDeviceConnect);


		Given a device type, this function will return device
		types that the given device type is connected to.  
		Input device types will yield reporting of output device
		types connected and vice versa.  If the associationType
		is given, only devices with the same association
		will be reported.  Otherwise, all devices of the given
		type are reported on.


Parameters	HMIXER	hMixer
		  Identifies the mixer device to be used.


		LPDEVICECONNECT	lpDeviceConnect
		  long pointer to DEVICECONNECT structure

		typedef struct{  
		DWORD dwInputDeviceType;
		DWORD dwOutputDeviceType;
		DWORD dwInputAssociation;
		DWORD dwOutputAssociation;
		} DEVICECONNECT;

		  
Return Value	Returns zero if the function was successful. 
		Otherwise, it returns an error. Possible errors are:
		
		    MIXERR_INVALSTRUCTPTR  null lpDeviceConnect

Comments	An output device type is one that can be connected to
		a mixer output and is distingquished by having the
		MIX_LISTENER bit set in its dwDeviceType field.	 

See Also	mixSetDeviceConnections

______________________________________________________________________

Syntax		mixSetDeviceConnections(hMixer,lpDeviceConnect)

		Given two device types, input and output, this function
		will attempt to connect the two types.  If the
		associationType and associationValue fields are not NULL,
		only devices with the same association will be
		connected.  

Parameters	HMIXER	hMixer
		  Identifies the mixer device to be used.

		LPDEVICECONNECT	lpDeviceConnect
		  long pointer to DEVICECONNECT structure

		typedef struct{  
		DWORD dwInputDeviceType;
		DWORD dwOutputDeviceType;
		DWORD dwInputAssociation;
		DWORD dwOutputAssociation;
		} DEVICECONNECT;


Return Value	Returns zero if the function was successful. 
		Otherwise, it returns an error. Possible errors are:
		
		    MIXERR_INVALSTRUCTPTR  null lpDeviceConnect
Comments	

See Also	mixGetDeviceConnections

______________________________________________________________________






CONTROL SETTING NOTES

The functions mixGetControl and mixSetInputControl
have a dwControl parameter and a dwSetting parameter.

Following the example set by Microsoft's volume settings, each
control setting will have associated with it a double word value
for specifying its setting.

dwControl		 description			format	
---------		 -----------			------

MIX_SUPPORT_VOLUME	 volume control           	LLLL:RRRR scalar
MIX_SUPPORT_LRVOLUME       left-right volume control	LLLL:RRRR scalar
MIX_SUPPORT_ALC		 Auto Level Control		LLLL:RRRR on/off
MIX_SUPPORT_BMT		 B-M-T equalization		--BB:MMTT scalar
MIX_SUPPORT_CROSSOVER	 crossover change     		MIXCROSSCAPS
MIX_SUPPORT_LOUDNESS	 loudness equalization		LLLL:RRRR on/off
MIX_SUPPORT_MUTE		 mute - don't change volume	LLLL:RRRR on/off
MIX_SUPPORT_REVERB	 reverb 			LLLL:RRRR scalar
MIX_SUPPORT_STEREOENHANCE  stereo enhance 		LLLL:RRRR on/off
MIX_SUPPORT_CUSTOM1	 custom effect #1		LLLL:RRRR on/off
MIX_SUPPORT_CUSTOM2	 custom effect #2		LLLL:RRRR scalar

Scalars are unsigned values from 0-65535 except in the case of BMT
where they are unsigned values from 0-255.  These values should be
interpolated to match the mixer hardware's scale.

On/Off values are ON for any non-zero value.

//////////////////////////////////////////////////////////////////////



MCI INTERFACE

Media Vision is now providing an MCI driver for controlling the mixer
hardware.  For many of you, this will make the control of mixing
functions much easier than it ever has been.

MCI, as you must know, stands for Media Control Interface.  In the
case of a mixer, there is no media (medium).  When we speak of 
CDs, wave files, MIDI, we connote some sort of media transport,
(ie. position within the data, support for PLAY, STOP, REWIND, etc)

A PLAY command sent to a mixer does not make sense.  In fact most MCI
commands have little meaning for a mixer.

Still, MCI is powerful.  One of its outstanding features is its
ability to convert strings into driver commands.  We have, therefore,
developed an MCI driver for Multimedia Windows.

The documentation for the MCI mixer is found in the file
mcimixer.doc.

//////////////////////////////////////////////////////////////////////

MIXER NOTES:

The mixSetState function allows timed fades.  If it would be useful
to developers we can add the capability for timed fades to the
mixSetControl function.  Let us know if you want this.  Soon.

User-defined patches are not accessible through mixGetPatchInfo.
The mechanism of user-defined patches may change in the future.


//////////////////////////////////////////////////////////////////////
GLOSSARY:

line - a stereo input or output of a mixer

patch - the association of a line to a particular sound producing
	or recording device

connection - this term refers to a mixer's internal input-to-output
 	routing of an audio signal 	

control	- the capability to modify an audio signal (ie volume)

cross-fade  - fading one or more controls up while fading other out
	


//////////////////////////////////////////////////////////////////////