as68 - 68000 Assembler, version 1.01


               (c) copyright 1982 Steve Passe  all rights reserved





                           Table of Contents


          Chapter 1 Introduction                                 1

          Chapter 2 Usage                                        5

          Chapter 3 Pseudo-ops                                   9

          Chapter 4 Mnemonics                                    12

          Chapter 5 Expressions                                  15

          Chapter 6 S File Format                                17

          Chapter 7 Error Messages                               19

          Chapter 8 Differences                                  23








          as68 Manual                                     Introduction
          









                                    Chapter 1

                                  Introduction




            The  as68  assembler is a disk to disk assembler  for  the
          Motorola  68000  micrprocessor  chip.   Written   in  the  c
          programming language, it may be used as a cross assembler on
          any  machine  supporting c, or  as  a  native  assembler  if
          compiled  with  a  c  that   produces  68000  output.   It's
          directives and mnemonic  set  closely  follow  that  of  the
          Motorola Resident Structured Assembler.

          

          Source Program

            The  input  to  the  assembler  is  an  ascii  text  file,
          consisting of a series of statements written in the assembly
          language.  Each statement consists of  one  or  more  fields
          within a line. 

            The assembler is free format within each line, i.e.  there
          is  no  need  to  start a specific field of a statement in a
          particular  column.   Fields are separated from one  another
          with whitespace (tabs or spaces). 

          

          Statements

            There are 3 basic statement types.  The most common  is an
          assembly language instruction or mnemonic. It is  a  command
          to the  assembler  to  produce  a  machine operation code to
          carry out a specific  action.   The second type of statement
          is  called an assembly directive  or  pseudo-op.  Pseudo-ops
          tell  the assembler how to assemble the program.  The  third
          statement  type  is  called  a comment. It is ignored by the
          assembler,  it's  purpose being to allow the  programmer  to
          insert descriptions of what  the  code  is  doing within the
          text of the source program.  Comments may exist as the final
          field of the other two statement types. 



                                       -1-
          






          as68 Manual                                     Introduction
          




          

          Instruction Statements

            An instruction statement  consists  of  from  one  to four
          fields:

          

          [label] <mnemonic> [operand] [comment]

            Label Field

            The first field, the label field, is optional.  It is used
          to  create  a  symbolic  name  for  the  address of the code
          generated by  the  following assembler mnemonic.  This label
          is  stored  in  the  symbol  table  and any references to it
          evaluate to the associated address.  The label field  may be
          the  only  field  of a statement and  multiple,  label  only
          fields  may  follow one another.  In all cases the  label(s)
          will  evaluate  to the address of the first mnemonic  to  be
          assembled after the label(s) is specified. 

            Labels are composed of alphanumeric  characters and may be
          up  to  30 characters long.  All characters of a  label  are
          significant,  as  is the case of alphabetic characters (i.e.
          "Foo" is different  than  "foo").  The  first character of a
          label  must  be  either  alphabetic  or  the  character  '.'
          (period).   Following   characters   may  also  include  the
          underscore (_), dollarsign ($), and the digits '0' thru '9'.

            Labels starting in any other than the first column must be
          terminated  with a colon (:). Certain symbols  are  reserved
          for  the  use of the assembler and thus may not be  used  as
          labels.   These  include  "SP",  "USP",  "SR",  "CCR",  "A0"
          through "A7" and "D0" through "D7".

            Mnemonic Field

            The  second  field is the mnemonic or assembly instruction
          field.  It will always be  present  in a statement except in
          the  case  of a label only statement (label only  statements
          might more properly be  described as assembler directives). 
          If  the  line  is  unlabeled  the  mnemonic  field  must  be
          preceeded by whitespace. 

            A  mnemonic  will consist of from 3 to 5 ascii characters,
          the  case of  which  is  not  significant.   This  assembler
          recognizes  the  standard  Motorola  instruction  set.   The



                                       -2-
          






          as68 Manual                                     Introduction
          



          complete mnemonic instruction set is described in chapter 4,
          "Mnemonics". Many  68000  instructions may work on different
          data sizes.  The desired data size is specified by appending
          a length modifier or data size code to the mnemonic.  A '.b'
          extension  specifies a data size of byte (8 bits) while '.l'
          will cause the data size to be  a  long  word (32 bits).  No
          extension will cause the data size to be a word  (16 bits). 
          A  '.w'  extension  may  be used for  data  sizes  of  word,
          although  this  size  is  the  default  and as such the '.w'
          modifier is unnecessary. 

            Operand Field

            The operand field is necessary  only  for those statements
          whose mnemonic requires  an operand(s).  It will contain one
          or two operands.  When two operands are present they must be
          separated  with  a  comma  (no  whitespace  allowed  between
          operands).  The first of two  operands  is refered to as the
          source operand while the second is the destination operand. 

            Comment Field

            The comment field is optional  and  consists  of  all text
          following the above fields. 

          

          Directives

            Label Field

            Labels used  with  directive statements follow the general
          rules   of  those  used  in  assembly  statements  with  one
          important exception:    they  may  only  be  used  with  the
          following directives:

            1.  EQU

            2.  SET

            3.  DC

            4.  DS

            5.  MACRO (unimplimented in ver.  1.xx)

            Directive Field

            The  directive  field  contains  an   instruction  to  the
          assembler as to how the program should  be  assembled.  This



                                       -3-
          






          as68 Manual                                     Introduction
          



          includes such things as the base  address  of  the  program,
          setting  of  symbol  values,  allocation of  program  memory
          storage,  conditional  assembly,  etc.  The complete list of
          available  assembly  directions   is  given  in  chapter  3,
          "Pseudo-ops".

            Operand Field

            The operand field of a directive statement will consist of
          zero  or  more  operands,  as  needed  by  the pseudo-op  in
          question.  Multiple operands are separated with a comma (,).
          No whitespace may exist between operands. 

            Comment Field

            The comment field is identical to that used in instruction
          statements and is optional. 

          

          Comments

            Comments may exist alone as separate statements.   In such
          cases an asterisk, (*), must be the  first  character on the
          line. 

          


























                                       -4-
          






          as68 Manual                                            Usage
          









                                    Chapter 2

                                      Usage




          

          Cp/m

            The command line format is:

          

          as68 [sourcedisk:]<sourcefile>[.ext] [option[ option]]

          where:

          

          sourcedisk     is the optional disk specifier for the source
                         program file.  If not  given  the source disk
                         defaults to the logged in disk. 

          sourcefile     is the source file  name.   It  must meet all
                         cp/m requirements for a legal file name. 

          ext              is  an   optional   cp/m   file   extension
                         identifier.  By default the assembler expects
                         source files to have an ext of ".sa".

          option          is  one  of  several   possible  options  in
                         assembly.  Whitespace must  separate multiple
                         options  when they occur.  Individual options
                         are described below. 

          

          Options

            The following options are available:

          



                                       -5-
          






          as68 Manual                                            Usage
          




            -  e, destination of error messages.  If absent all  error
               messages  will  go  to  the  console  by  default.   If
               present,  one or more of the following destinations may
               be specified:

                 *  c, error messages to the console. 

                 *    e,   error   messages    to    a    file   named
                    "sourcefile.err".  A disk specifier may follow the
                    'e' option extension.   Otherwise the default disk
                    is the source  file  disk.   For  example,  'eec:'
                    would    send   error   messages   to   the   file
                    "c:sourcefile.err".

                 *  f, errors reported in listing. 

                 *  l, error messages to the cp/m list device. 

            -   l,  destination  of  assembly listing.  If  absent  no
               listing  is  made.  One or more of the following option
               extensions are available:

                 *  c, listing to console. 

                 *  f, listing to a cp/m file.  The file will be named
                    "sourcefile.ls" and will reside  on  the same disk
                    as  the  source   file   unless  overridden  by  a
                    following disk identifier.  For example,  to place
                    the listing on both the console and  the  b  disk,
                    use 'lcfb:'.

                 *  l, listing to cp/m list device. 

            -  o, type and destination of object file.  If not present
               the object file will be in Motorola 'S' FILE format and
               will be placed on the same disk as the source file. 

                 *  s, object to a  cp/m file.  The file will be named
                    "sourcefile.mx",  the  output   file  will  be  in
                    Motorola's 'S' FILE format.  A disk designator may
                    follow the 's'  option  (i.e.  'osd:'),  specifing
                    that the output file should  go  to other than the
                    sourcefile disk (in the above  example it would go
                    to drive d). 

                 *  x, no object file to be made. 

               s,  set  the  symbol  table  size.   The  symbol  table
               requires 8 bytes plus the length of the symbol for each



                                       -6-
          






          as68 Manual                                            Usage
          



               entry.  The argument should be  in  decimal bytes.  The
               symbol  table  defaults  to  2000 bytes  (decimal).  To
               reserve 3500 bytes the option would be: 's3500'.

            -  t, truncate source code lines  in listing.  This option
               will cause the source code lines sent to any  open list
               channel  to  be truncated at the normal  wrap  position
               (see  option  'w'  below).  It defaults to being off, a
               't' in the command line will turn it on. 

            -  w,  set  the  value  of wrap.  Source code lines in the
               listing(s) will normally be 'wrapped' to the  next line
               if  they  extend  beyond the column number specified by
               this option.  If  the  't' option is active this option
               specifies  the column beyond  which  source  lines  are
               truncated.  The default value of 'w' is  80, but can be
               set  between  60 and any reasonable number of columns. 
               Note  that  this  number  should be set to the width of
               your list device, it is  not  the  number of columns of
               source code to a  line  (i.e.  a  value of 80 allows 40
               characters  of source per line after accounting for the
               40 columns used by the line/loc/code fields). 

          

          Examples

          

            -  as68 foo lf ecf<cr> would assemble foo.sa and create:

                 *  foo.ls, the listing file. 

                 *   foo.err,  the  error file (as well as send  error
                    messages to the console and the listing file). 

                 *  foo.ro, the s file object (by default). 

            This would be the normal assembly invocation. 

            -  as68 bar ox ecfb:<cr> would assemble bar.sa and create:

                 *  b:bar.err, the error file  on  drive  b: (and send
                    error messages to console). 

            No object or list would  be created.  This method would be
               used  during  assemblies  that  one knows will generate
               some errors.  Since  the  source comes from a: and only
               one file is created, on  b:,  the  disk  access time is
               minimized  and sufficient information is placed in  the



                                       -7-
          






          as68 Manual                                            Usage
          



               error  file  to  allow correction of the  source.   The
               error file will be much smaller than  a  list file with
               errors  and  thus  will  be  quicker  to  write  during
               assembly  and  easier  to  scan  during  correction  of
               source. 

          

          Other Systems

            The  code  presently  supports  only  the  cp/m  operating
          system.  Some work would have to be done in the command line
          parser to bring it up on other operating systems. 

          






































                                       -8-
          






          as68 Manual                                       Pseudo-ops
          









                                    Chapter 3

                                   Pseudo-ops




          

          Assembly Control

            The following assembler directives are used to control the
          assembly:

          

          ORG            is used to specify the absolute memory origin
                         of the code to be  assembled.  The operand is
                         an  expression  that  evaluates to an address
                         within the first 64 kilobytes of memory space
                         (0 thru $FFFF). Any memory references outside
                         this range will cause an assembly  error.  Be
                         aware  that  the   68000  chip  sign  extends
                         absolute  short  addresses.    Thus   address
                         references  above  32k  ($8000)  will  access
                         hardware memory in  the range of $FF8000 thru
                         $FFFFFF.  This  pseudo-op   will   cause  the
                         assembler  to  generate  code  using absolute
                         short addressing.

          ORG.L          is also used to  specify  the absolute memory
                         origin.  However, in  this  case  the  entire
                         address range of the 68000 is usable  (0 thru
                         $FFFFFF). The assembler  will  generate  code
                         using absolute long addressing. 

          RORG            causes  the  assembler to  generate  program
                         counter  relative  code.   The  memory  range
                         restrictions of the "ORG" directive apply. 

          RORG.L          causes  the  assembler  to  generate program
                         counter relative code  as  above, however the
                         expression in the  operand field may evaluate
                         to  any  value  within  the  68000's  address



                                       -9-
          






          as68 Manual                                       Pseudo-ops
          



                         range. 

          END             signals  the  end  of  the assembly language
                         program. 

          

          Symbol Definition

            The  following  directives   control   the  definition  of
          symbols:

          

          EQU            defines a symbol and sets it's  value to that
                         of  the  operand.   This  symbol   value   is
                         permanent,  i.e.   it cannot be changed later
                         in a program.   The  operand may be a complex
                         expression    but    cannot    make   forward
                         references. 

          SET            defines or redefines a symbol and  sets  it's
                         value to that  of  the operand.  The value is
                         temporary and may be reset with another 'SET'
                         directive.  Again, forward references are not
                         allowed. 

          

          Memory Allocation

            These directives are  used  to  reserve  and/or initialize
          memory:

          

          DC               fills   memory  locations   with   constant
                         value(s).    An  extension  of  '.B'   causes
                         individual  bytes to be filled with the value
                         of the operand(s).  An extension of '.L' will
                         cause  the operands to be evaluated as 32 bit
                         values, which are placed in  4  byte  blocks,
                         one for each  operand.   No extension or '.W'
                         signifies  that  the  operand(s)  are  to  be
                         evaluated as 16 bit values, each being stored
                         in  consecutive  2  byte locations.  Word and
                         long word values are  aligned on even address
                         boundries.    DC.B   directives  causing  the
                         location  counter  to  end  on an odd address
                         will pad  1 byte with a zero value unless the



                                      -10-
          






          as68 Manual                                       Pseudo-ops
          



                         next source statement is another DC.B.

          DS             reserves memory  locations.   Again,  a  data
                         size extension  may  be  appended  to 'DS' to
                         specify either byte or long word allocation. 
                         The  operand specifies  the  number  of  data
                         cells to reserve, i.e.   if the extension was
                         '.L' and the operand evaluated to 5, forty (5
                         * 4  bytes  for  a  long word) bytes would be
                         reserved.  Word alignment is not automatic as
                         in  the  dc  directive.  To  force  alignment
                         after  a  DS.B  statement  use   a   "ds   0"
                         statement. 

          

          List Controls

            These directives are used to control the listing output:

          

          LIST           causes listing  output  (if  enabled from the
                         command line) to be sent to  each of the open
                         list channels.  LIST is active by default and
                         remains   so   until  a  NOLIST   pseudo   is
                         encountered. 

          NOLIST         causes listing output to be turned  off until
                         a LIST pseudo is encountered. 

          

          Macro Commands

            Macro commands are not implimented in version 1.xx of this
          assembler. 

          














                                      -11-
          






          as68 Manual                                        Mnemonics
          









                                    Chapter 4

                                    Mnemonics




            The mnemonics used by this assembler follow  the  standard
          mnemonic instruction set as defined  by  Motorola. Mnemonics
          may exist in  either upper or lower case in the source file,
          the assembler makes no distinctions. 

          

          ABCD           add binary coded decimal

          ADD            add binary

          ADDQ           add quick binary,  operand in range of 1 thru
                         8

          ADDX           add binary with extend

          AND            logical and

          ASL            arithmetic shift left

          ASR            arithmetic shift right

          Bcc            branch conditionally

          BCHG           bit test and change

          BCLR           bit test and clear

          BRA            branch unconditional

          BSET           bit test and set

          BSR            branch to subroutine

          BTST           bit test

          CHK            check register against boundaries



                                      -12-
          






          as68 Manual                                        Mnemonics
          




          CLR            clear operand

          CMP            compare

          CMPM           compare memory

          DBcc           test condition, decrement and branch

          DIVS           signed divide

          DIVU           unsigned divide

          EOR            exclusive or

          EXG            exchange registers

          EXT            sign extend

          JMP            jump to address

          JSR            jump to subroutine

          LEA            load effective address

          LINK           link and allocate

          LSL            logical shift left

          LSR            logical shift right

          MOVE           move

          MOVEM          move multiple registers

          MOVEP          move peripheral data

          MOVEQ          move quick, operand in range og -128 thru 127

          MULS           signed multiply

          MULU           unsigned multiply

          NBCD           negate binary coded decimal

          NEG            negate

          NEGX           negate with extend

          NOP            no operation



                                      -13-
          






          as68 Manual                                        Mnemonics
          




          NOT            bitwise compliment

          OR             logical or

          PEA            push effective address

          RESET          reset external devices

          ROL            rotate left

          ROR            rotate right

          ROXL           rotate left with extend

          ROXR           rotate right with extend

          RTE            return from exception

          RTR            return and restore condition codes

          RTS            return from subroutine

          SBCD           subtract binary coded decimal

          Scc            set conditional

          STOP           stop

          SUB            subtract binary

          SUBQ           subtract quick binary, operand in range  of 1
                         thru 8

          SUBX           subtract binary with extend

          SWAP           swap register halves

          TAS            test and set operand

          TRAP           trap

          TRAPV          trap on overflow

          TST            test an operand

          UNLK           unlink

          




                                      -14-
          






          as68 Manual                                      Expressions
          









                                    Chapter 5

                                   Expressions




          

          Expressions

            Expressions consist of one or  more  symbols  combined  by
          binary and/or unary (algebraic) operators.  Possible symbols
          include:

          

            -  Symbols defined with the EQU and SET directives.

            -  Program labels.

            -  Numeric values.

            -  The asterisk, ('*'), which equates to the present value
               of the program location counter.

            Algebraic Operators include:

          

            -  arithmetic operators:

                 *  multiplication: '*'

                 *  division: '/'

                 *  addition: '+'

                 *  subtraction: '-'

            logical operators:

                 *  logical (bitwise) AND: '&'




                                      -15-
          






          as68 Manual                                      Expressions
          



                 *  logical (bitwise) OR: '!'

                 *  left shift: '<<'

                 *  right shift: '>>'

            unary operators:

                 *  unary minus: '-'

                 *  location counter value: '*'

          

          Symbols

            Symbols are composed of alphanumeric characters and may be
          up to 30  characters  long.   All  characters of a label are
          significant,  as  is the case of alphabetic characters (i.e.
          "Foo" is different  than  "foo").  The  first character of a
          label  must  be  either  alphabetic  or  the  character  '.'
          (period).   Following   characters   may  also  include  the
          underscore (_), dollarsign ($), and the digits '0' thru '9'.

            Numbers may be represented as either decimal, hexadecimal,
          or binary:

          

            -   decimal  numbers are represented by the  normal  ascii
               digits '0' thru '9'.

            -  hexadecimal numbers  start  with  a  dollar  sign ('$')
               followed by the ascii digits '0' thru '9' and the ascii
               characters 'A' thru 'F'.

            -  binary numbers start with a percent sign ('%') followed
               by the ascii digits '0' and '1'.

          













                                      -16-
          






          as68 Manual                                    S File Format
          









                                    Chapter 6

                                  S File Format




            A  Motorola  "S  file" is similar in structure to an Intel
          hex file.  It consists of a series of ascii records, each in
          the following format:

          

            -   The  record start character, an uppercase  ascii  'S',
               followed by an ascii numeral, '0' thru '9':

            -

                 *  a '0' for the file header record. 

                 *  a '1' for records with short (16 bit) addresses. 

                 *  a '2' for records with medium (24 bit) addresses. 

                 *  a '3' for records with long (32 bit) addresses. 

                 *  ......

                 *  a '9' for the tail record. 

            -   The  third  and  forth  bytes  forming  an  ascii  hex
               representation  of  the number of bytes in the body  of
               the record:

                 *   an address field consisting of 4, 6, or  8  ascii
                    bytes representing the load address of  the record
                    (record types S1, S2, S3, respectively). 

            -  The body of the record consists  of  up  to 16 bytes of
               data, each byte represented as 2 ascii hex bytes. 

            -   A  checksum  byte,  again  represented  by  two  ascii
               characters:




                                      -17-
          






          as68 Manual                                    S File Format
          



            -

                 *  The checksum for each record (except the last, S9)
                    is   the   least  significant  byte  of  the   1's
                    compliment of the sum of the byte  values  of  the
                    count,  address, and data fields.  (ie, everything
                    in the record except 'Sx').

                 *    The   checksum   on    the    'S9'   record   is
                    undefined/non-existant. 

          









































                                      -18-
          






          as68 Manual                                   Error Messages
          









                                    Chapter 7

                                 Error Messages




          

            -   1:  statement  parsing  error.  The occurrance of this
               error indicates that  the  line  totally  confuses  the
               parser and no  further  diagnostic comments (legitimate
               comments anyway) can be made. 

            -  2: bad character in  mnemonic-psdo  field.   An illegal
               character exists in the word  present  in  the mnenonic
               field,  see   chapter   1,   introduction,  instruction
               statements. 

            -  3: instruction or pseudo not  found  in tables.  Unless
               error  2 is also generated  the  instr/pseudo  word  is
               properly formed (i.e. no illegal characters are  in it)
               but not a recognized instruction. 

            -  4: bad character in macro field.  Version 1.xx does not
               recognize macros! 

            -   5:  macro not found in macro table(s).  Again,  macros
               are not yet recognized. 

            -   6: improper use of label.  Most often this error flags
               the use of a label on a pseudo op  line  that  does not
               allow  the use of labels.  See chapter 1, introduction,
               directives:label field. 

            -   7:  can't  evaluate  operand.   The  assembler  cannot
               evaluate the value of an operand.   This  may be caused
               by  a variety  of  reasons  such  as  imbedded  spaces,
               unrecognized operators, unbalanced  parenthesis,  etc. 
               Additional  errors  will  usually be reported that will
               help clarify the problem. 

            -   8: can't evaluate equ operand.  As above, generated in
               the case of an EQU statement. 



                                      -19-
          






          as68 Manual                                   Error Messages
          




            -  9: can't evaluate set operand.  As above, generated  in
               the case of an SET statement. 

            -  10: attempt to redefine a permanent symbol.  The symbol
               was  previously  defined  via an EQU statement and thus
               cannot be changed. 

            -  11: symbol table full.  This is a  fatal error and will
               cause the assembly to abort.  You may try again setting
               an optional symbol table size  from  the command line. 
               See chapter 2, usage, options:s. 

            -   12:  unrecognized  operand.  A legal operand cannot be
               formed from the data in the operand field. 

            -  13: symbol not defined in symbol table.  The symbol was
               not  encountered  in  the  program up to  this  point. 
               Remember that forward references are not allowed in EQU
               and SET pseudo statements. 

            -  14: label out  of  range  for current addressing mode. 
               The value of the label is outside  the  limits  of  the
               current  statement.   This  usually is  an  attempt  to
               reference an address beyond the 32k bytes range imposed
               in  the  short  addressing  mode.    See   chapter   3,
               pseudo-ops, assembly control. 

            -  15: operand  1  is not valid for instruction type.  The
               first operand encountered is not  a  valid  operand for
               this particular instruction/addressing mode. 

            -   16:  operand 2 is not valid for instruction type.  The
               second operand encountered is not a valid  operand  for
               this particular instruction/addressing mode. 

            -  17: operand 1 is not correctly  formed.   This  may  be
               caused  by illegal use of operators, undefined  labels,
               etc.  The assembler may  or may not attempt to evaluate
               the  second  operand.  If it does you are  not  assured
               that it will do so correctly.  For  more  on  this  see
               error #18.

            -  18: operand 2 is not correctly formed.  This may be for
               any of  the reasons stated above for error 17. Remember
               that it could  be incorrectly evaluated if error 17 was
               also generated and  that  the  second  operand  may  be
               incorrectly formed but not reported as such after error
               17  occurs.   This  is  dependant   on   the  assembler
               correctly determining where the poorly formed operand 1



                                      -20-
          






          as68 Manual                                   Error Messages
          



               ends and operand 2 starts. 

            -  19: code  building  function  failed.   The binary code
               building function has  failed  to  properly construct a
               sequence  of  code  for the statement.  Thie error will
               usually   be   followed   with  additional   error   #s
               pinpointing the problem. 

            -  20: 3 bit immediate data value out of  bounds, i.e.  it
               is greater than 7 or less than 0.

            -  21: 8 bit bit field specifier out of range. 

            -  22: 32 bit bit field specifier out of range. 

            -  23: attempt to generate a bit field specifier failed. 

            -  24: count operand out of range (1-8).

            -   25: destination register specifier illegal or  out  of
               range. 

            -  26: source or destination register specifier illegal or
               out of range. 

            -  27: attempt  to generat register mask list from operand
               failed. 

            -   28:  operand  failed to evaluate to a proper source or
               destination effective address. 

            -   29:  illegal destination effective  address,  probably
               label or label with index reference. 

            -  30: illegal destination effective address. 

            -   31:  illegal  multiple  destination effective address,
               either label,  label  with  index,  or address register
               indirect with predecrement or postincrement. 

            -   32: illegal jump effective  address,  usually  address
               register indirect with predecrement or postincrement. 

            -  33: 4 bit vector out of range. 

            -   34: expected address displacement failed  to  evaluate
               correctly. 

            -  35: 8 bit displacement out of range (-128 thru 127)




                                      -21-
          






          as68 Manual                                   Error Messages
          



            -  36: 16  bit  displacement  out  of  range  (-32768 thru
               32766)

            -   37:  extent   word   of  operand  failed  to  evaluate
               correctly. 

            -  38: 8 bit operand out of range (-128  thru 255, sign is
               responsibility of programmer). 

            -  39: 8 bit extension word value out of  range (-128 thru
               255).

            -   40:  16  bit  extension word out of range (-32768 thru
               65535).

            -   41:  32  bit  extension  word  value   out   of  range
               (overflow).

            -  42: attempt to generate a  16  bit displacement failed,
               probably out of range. 

            -  43: attempt to generate an 8  bit  displacemnt  failed,
               check range. 

          




























                                      -22-
          






          as68 Manual                                      Differences
          









                                    Chapter 8

                                   Differences




            This list  must be considered incomplete and will be added
          to as the facts are brought to my attention. 

          

          In General

          

            -   As68 allows addresses assembled  under  an  rorg.l  or
               org.l condition to be coerced  into  a short address by
               enclosing the entire expression in a set of parenthesis
               followed  by  '.s'.  This  allows  references  to   the
               first/last 32k  with  a  code  sequence that is 2 bytes
               shorter than the long address mode.  As an example:



                       org.l   $8000

               outport equ     $ffa000         * port mapped into last
                                               * page of address space

                       move.b  d0,outport      * will generate 6 bytes of
					       * code, while
                       move.b  d0,(outport).s  * will only generate 4 bytes
					       * of code
          

          Motorola Resident Structured Assembler

          

            -  Motorola allows forward short  branch  instructions  to
               default  to  either  long or  short  addressing.   as68
               always  uses  long  or  short  addressing,  forward  or
               backward,   dependant  on  the  presence  of  the  '.s'
               modifier  on the mnemonic.  Motorola will determine the



                                      -23-
          






          as68 Manual                                      Differences
          



               necessary   value  (short  or  long)  automatically  on
               backward references. 

            -  The value shown in  listings  for the DS pseudo-op will
               reflect the number  of  bytes  reserved in the Motorola
               listing while the as68 listing  will  report the number
               of  elements  reserved.  For example the line:  ds.w  2
               will have a value of 0002 in the as68 listing while the
               Motorola listing will report a value of 0004

          

          Digital Research Assembler

          

            -  Pseudo-ops are required to  start  with a period (.) by
               the Digital assembler while  as68  follows the Motorola
               conventions. 

            -  Digital expects a default source file extention of ".s"
               where as68 expects ".sa"

          





























                                      -24-
          






          as68 Manual                                      Differences
          
























































                                      -25-
          













                                      Index


          !  15
          &  15
          *  16
          .b extension  3, 10
          .l extension  3, 10
          .w extension  3, 10
          <<  16
          >>  16
          absolute long addressing  9
          absolute short addressing  9
          AND  15
          arithmetic operators  15
          assembly control  9
          assembly options  5
          binary  16
          comment  3, 4, 4
          cp/m  5
          data size code  3
          datasize code  10
          DC  3, 10
          decimal  16
          destination operand  3
          Digital Research Assembler  24
          directive  3, 3
          DS  3, 11
          END  10
          EQU  3, 10
          expression  15
          hexadecimal  16
          instruction  2
          label  2, 3, 15
          left shift  16
          LIST  11
          list controls  11
          location counter  15, 16
          logical operators  15
          MACRO  3, 11
          macro commands  11
          memory allocation  10
          mnemonic  2
          mnemonics  12
          Motorola 'S' FILE  6
          Motorola Resident Structured Assembler  23
          NOLIST  11
          numbers  15, 16
          operand  3, 4
          operators  15












          OR  15
          ORG  9
          ORG.L  9
          program counter relative  9
          right shift  16
          RORG  9
          RORG.L  9
          S file  17
          SET  3, 10
          source operand  3
          source program  1
          statement  1
          symbol  15, 16
          symbol definition  10
          unary minus  16
          unary operators  16

          EQU  3, 10