AS8, a Z8 Crossassembler
		========================

	by:	H.-G. Willers
		Gartenstrasse 11
		D-8047 Karlsfeld
		WEST GERMANY


		This document dated 11-jan-90


			Intro
			=====

	This document briefly describes the features
	of my crossassembler for the Z8 microprocessor,
	called AS8.

	This assembler is based on some code found in
	a crossassembler for the Z80 microprocessor as
	published on the DECUS tape 11-SP-18.
	The code was polished up (e.g. adding a hashtable
	for the symbols instead of linear search) and
	many bugs were fixed.

	The resulting code acts as a skeleton for my
	assemblers like this one: AS8.

	The source code was compiled, using:

	o  Mark Williams Let's C (Vers. 3.0.2)

	o  Microsoft QuickC (Vers. 1.01)

	o  System 5.3 UNIX C for 68020

	o  Interactive UNIX 386 3.2 2.1

	To compile and link under Mark Williams C the file
	'time.c' contains some hacks to simulate the missing
	library functions.


	The code is provided on an 'as is' basis.

	No responsibility for any malfunction of the
	assembler per se or any assembled program can
	be taken. You use it at your own risk.

	Please send comments and improvements to the
	author at the above address.



		Commandline Syntax
		==================

	AS8 is invoked by the following commandline:

	as8 [-nl] sourcefile.ext

	The options mean:

	-l	generates a listing named sourcefile.l

	-n	do not generate an object file

	In the process of producing a name for the
	object file or the listing file the extension
	of the sourcefile is stripped. Any possible
	restrictions of filename use in a given
	operating system may apply.	


		Source Syntax
		=============

	The syntax of a source line for AS8 is as follows:
	
	label:	opc	src, dst	/ comment

	The 'label' is optional; if used, it must be followed
	by a colon.

	'Opc' is the memonic representation for the
	instruction to be used.

	The source and destination operands are written
	as source first, then destination.

	Comments are introduced by the character '/'.

	Multiple statements per line are separated by ';',
	for example:	nop ; nop ; nop


		Symbols
		=======

	A symbol in as8 is a entity with a label set by
	a label or a direct assignment. The number of
	characters per symbol is 33 as distributed.
	It can be changed by adjusting the defined
	constant 'NCPS' to the desired value.

	Symbols can consist of the characters of
	the ASCII character set, but must begin with either
	a-z, A-Z, or the characters '.' or '_' (see
	the routine 'isidc(c)' ).

		Local Labels
		============

	There are 9 local labels: 1 - 9. references in the
	forward direction are indicated by a 'f', appended
	to the label number, references backwards are
	indicated by a trailing 'b'.
	For example:

	1:	nop
		sob	w16,1b		/ label 1 backwards
		...

		call	2f		/ label 2 forward
		...

	2:	ret

	Each local label is reassigned to its new value
	when reused.


		Number Representation
		=====================

	The default radix is decimal. The allowed digits
	range from 0 - 9.

	Base 16 numbers (hex) are denoted by a leading '0x'.
	For example: 0x20 is the same as 32.

	Base 8 numbers (octal) are denoted by a leading '0'.
	For example:  012 is the value of the ascii character CR.

	Base 2 numbers are preceeded by a '0B'.
	For example:  0B01010101 is the same as 0x55.



		Literals
		========


	Literal constants are enterd by the character ' ,
	followed by the desired ASCII character.



		Expressions
		===========

	Expressions are made up from numbers (or symbols)
	and arithmetic operators.

	Expression evaluation is done from left to right.
	This order can be changed by parenthesis with '[ .. ]'.

	The binary arithmetic operators are + , -, *, and %.
	The operator '%' in AS8 means / ( because comments
	are introduced by '/' ).

	The bitwise logical operators are

		&   bitwise AND
		|   bitwise inclusive OR
		^   bitwise exclusive OR
		>   right shift
		<   left shift

	The following unary operators are supported:

		-   two's complement
		!   one's complement



		Pseudo Operators
		================


	.byte	symbol

	Generates one byte consisting of the value of 'symbol'.

	Example:

	.byte	0x20		/ one byte (ascii space)


	.word	symbol

	Generates one word consisting of the value of 'symbol'.
	The word is generated with the byte ordering of the Z8:
	nameley the upper 8 bits first (big endian byte ordering).

	Example:

	.word	0x1000		/ generates the bytes 0x10 and 0


	.ascii	string

	Generates the named string as a sequence of ascii characters.
	The first character of the string is taken as a terminator.
	The string ends, when the terminator is found again.

	Example:

	.ascii	"Hi there!"	/ ascii string


	.asciz	string

	Generates the named string as a sequence of ascii characters.
	The string is followed by a null-character. The first character
	of the string is taken as a terminator.	The string ends, when
	the terminator is found again.

	Example:

	.asciz	"Hi there!"	/ ascii string with trailing zero


	.blkb	count [, value]

	Space for 'count' bytes is left free. If the optional 'value'
	is not given, null bytes are taken for filling; bytes
	with the 'value' are taken otherwise.

	Examples:

	.blkb	100, 0x20	/ 100 (decimal) bytes of content 0x20
				/ are filled up
	.blkb	0x1000		/ 4096 bytes of content 0


	.page

	The listing is advanced by one page.


	.title	string

	The title line for the listing is set. The string starts
	with a terminator, which also end the string.

	Example:

	.title	"simple demo"


	.hlist

	Sets the radix for number output in the listing to
	hex.


	.olist

	Sets the radix for number output in the listing to
	octal.


	.list

	Starts listing generation. This is the default state.


	.nlist

	Stops listing generation.


	.end	symbol

	The entrypoint of the loaded program is set to 'symbol'.
	The start record of the produced intel-hex-tape is set
	to this value.

	Example:

	.end	_main		/ program starts at _main



		Location Counter
		================

	The location counter is set by the assignment of '.' to
	the desired value.

	Example:

	.	=	0x1000		/ sets the location counter
					/ to 0x1000


		Addressing Modes
		================

	(See file z8tst.z8 for clarification)

	Register:		r0 - r255

	Working Register:	w0 - w15

	Register Indirect:	e.g. ...  (r0)

	Working Register Ind.:	e.g. ...  (w6)

	Indexed:		e.g.	mov  r100(w0),w1

	Immediate:		e.g.	add  $1,w0

	Direct, relative	indicated by a label



		Instruction Description
		=======================

	AS8	ZILOG      switch in 'xasm'	base opcode
	---	-----      ----------------

	ccf	ccf		S_OP0		0xef
	di	di		S_OP0		0x8f
	ei	ei		S_OP0		0x9f
	reti	iret		S_OP0		0xbf
	nop	nop		S_OP0		0xff
	rcf	rcf		S_OP0		0xcf
	ret	ret		S_OP0		0xaf
	scf	scf		S_OP0		0xdf

	srp	srp		S_OP2		0x31

	clr	clr		S_OP3		0xb0
	com	com		S_OP3		0x60
	da	da		S_OP3		0x40
	dec	dec		S_OP3		0
	pop	pop		S_OP3		0x50
	push	push		S_OP3		0x70
	rl	rl		S_OP3		0x90
	rlc	rlc		S_OP3		0x10
	rr	rr		S_OP3		0xe0
	rrc	rrc		S_OP3		0xc0
	sra	sra		S_OP3		0xd0
	swap	swap		S_OP3		0xf0

	call	call		S_OP4

	jmp	jp  DA		S_OP5		0x8d
	jcs	jp  c,DA	S_OP5		0x7d
	jcc	jp  nc,DA	S_OP5		0xfd
	jeq	jp  z,DA	S_OP5		0x6d
	jne	jp  nz,DA	S_OP5		0xed
	jpl	jp  pl,DA	S_OP5		0xdd
	jmi	jp  mi,DA	S_OP5		0x5d
	jov	jp  ov,DA	S_OP5		0x4d
	jnov	jp  nov,DA	S_OP5		0xcd
	jge	jp  ge,DA	S_OP5		0x9d
	jlt	jp  lt,DA	S_OP5		0x1d
	jgt	jp  gt,DA	S_OP5		0xad
	jle	jp  le,DA	S_OP5		0x2d
	juge	jp  uge,DA	S_OP5		0xfd
	jult	jp  ult,DA	S_OP5		0x7d
	jugt	jp  ugt,DA	S_OP5		0xbd
	jule	jp  ule,DA	S_OP5		0x3d

	br	jr  DA		S_OP6		0x8b
	bcs	jr  c,DA	S_OP6		0x7b
	bcc	jr  nc,DA	S_OP6		0xfb
	beq	jr  z,DA	S_OP6		0x6b
	bne	jr  nz,DA	S_OP6		0xeb
	bpl	jr  pl,DA	S_OP6		0xdb
	bmi	jr  mi,DA	S_OP6		0x5b
	bov	jr  ov,DA	S_OP6		0x4b
	bnov	jr  nov,DA	S_OP6		0xcb
	bge	jr  ge,DA	S_OP6		0x9b
	blt	jr  lt,DA	S_OP6		0x1b
	bgt	jr  gt,DA	S_OP6		0xab
	ble	jr  le,DA	S_OP6		0x2b
	buge	jr  uge,DA	S_OP6		0xfb
	bult	jr  ult,DA	S_OP6		0x7b
	bugt	jr  ugt,DA	S_OP6		0xbb
	bule	jr  ule,DA	S_OP6		0x3b
	sob	djnz  wr,RA	S_OP7		0x0a

	add	add		S_OP8
	adc	adc		S_OP8		0x10
	sub	sub		S_OP8		0x20
	sbc	sbc		S_OP8		0x30
	or	or		S_OP8		0x40
	and	and		S_OP8		0x50
	tcm	tcm		S_OP8		0x60
	tm	tm		S_OP8		0x70
	cmp	cmp		S_OP8		0xa0
	xor	xor		S_OP8		0xb0

	mov	ld  dst,src	S_OP9

	incw	incw		S_OP10		0xa0
	decw	decw		S_OP10		0x80

	inc	inc		S_OP11		0x20
	dec	dec		S_OP12

	movp	ldc     'move from/to program memory'
	movd	lde     'move from/to data memory'
	movpi	ldci    'move from/to prog. mem autoincr.
	movdi	ldei	'move from/to data mem autoincr.'


		Error Messages
		==============

	Errors in the source code are flagged in the listing
	and in the terminal output by a one letter indicator.

	This is a list of the error indicators:

	a	assembly error
		o branches out of range
		o 'srp' with wrong value
		o illegal addressing modes

	e	argument not even (e.g. working reg. pair)

	m	symbol multiply defined

	o	undefined opcode name

	p	phase error: labels do not have the
		same values in pass1 and pass2 of assembly

	q	questionable syntax:
		o digit without ':'
		o .ascii or .asciz directive with no args
		o '[' and ']' not paired
	
	r	types of arithmetic expression do not
		match

	t	value of a byte to be output is
		out of range

	u	symbol undefined

	z	object buffer overflow

		Disclaimer
		==========

	The original source code (Z80 crossassembler as found
	on DECUS 11-SP-18) is to the best of my knowledge in
	the public domain.

	My software for AS8 (opcode handling, misc. changes)
	is hereby released into the public domain.

	All registered trade marks belong to their owners.