January 29, 1990


RED VERSION 7.0 TECHNICAL NOTES

RED first made its appearance in 1983, in an article published in the
January issue of Dr. Dobb's Journal.  Although some features of RED
have been surpassed by developments in user interfaces, many technical
features of RED still merit study.


Improvements Made to this Version
			
Substantial improvements and modifications have been made in version 7.0.

o RED now will compile with the two most popular compilers for MS-
DOS, Microsoft C v5.0 and Turbo C v2.0.  Make and link files have been
included for both compilers.

o The source code has been revised for modern ANSI style C compilers.
Function prototypes and other modern stylistic devices are used
throughout.

o Several changes improve the speed and portability of the source code.  A
number of buffer routines have been replaced by macros for greater speed.
 For maximum portability, the assembly language screen handler has been
completely rewritten to use BIOS calls rather than direct manipulation of
PC hardware.  In spite of this, the screen routines remain very fast.

o The code has been instrumented with the Sherlockt debugging macros.
These macros provide flexible debugging information and came in handy
while porting RED to Turbo C and Microsoft C.  Documentation for
Sherlock is included on this disk.

These technical notes contain four main sections.  Section one discusses
the technical aspects of RED that still remain interesting after almost 7
years--notably fast screen update and fast file handling for even very large
files. Section two lists some areas where RED falls short of the current
generation of editors and word processors. Section three contains some
reflections on the programming style used in RED.  Finally, section four
explains how to port RED to other machines.


What's Still Valuable about RED

RED contains two chief technical accomplishments:  the screen is updated
quickly and arbitrarily large files are handled quickly.  These results were
produced without sacrificing portability.  In addition, RED's code is small
enough so that it can be compiled with the small memory model.  RED is
lean and quick.

RED's editing routines tell the screen update routines how to update the
screen, not just what to update.  This results in more complicated edit
routines but much faster screen refreshes.  In addition, an "interrupt-
driven" screen update policy was adapted.  Output lines are not printed
immediately but are instead queued by setting some variables in the system
module, redsys.c.  Lines were output to the screen whenever the keyboard
polling loop in syscin found no keyboard activity.

RED's file buffering routines, in files redbuf1.c through redbuf4.c, form
the largest and most complicated part of RED.  I'm still pleased with these
buffer routines--they handle arbitrarily large files quickly and efficiently.  I
believe that the scheme used in RED compares favorably with such file
access methods as B* trees.

Designing such a buffering scheme is far from easy.  Fast screen scrolling
demands that sequential lines of text be accessed quickly.  Inserting and
deleting line must be fast.  In particular, the time to move forward and back
one line, or to insert or delete a line should be constant, i.e., it should not
depend at all on the size of the file.  Loading a file and saving a file, or
finding an arbitrary line of the file should require time which is
proportional to the size of the file.  Disk storage must not become
fragmented, no matter how much editing is done to a file.  Finally, the
buffer routines must work well with as few as ten 1K file buffers and must
be able to use hundreds of buffers effectively if they are available.  RED's
buffer routines meet all these criteria.

Central to the operation of the buffer routines is the work file.  The file to
be edited is copied to work file format when the file is first loaded.  Once
the price for this file conversion has been paid, all other file operations
become very fast.

The work file is organized as a doubly-linked list of fixed-length blocks.
Each block contains a block header, one or more complete text lines, and a
variable-length index table, one entry per text line.  Lines are not permitted
to be split across lines, so when a line becomes too long to fit in a block, a
new block must be created and linked into the list.  Adjacent blocks are
merged at key points so that unneeded blocks never build up.  It is never
necessary to compact the work file.  The precise algorithms for splitting
and joining adjacent blocks forms the key code in the RED text editor.

Superimposed on these splitting and joining algorithms is a fairly
straightforward least-recently-used virtual memory algorithm.  Blocks are
swapped into and out of memory as required.  The code makes complex
assumptions about which buffers are in memory while buffers are being
split and joined.  In retrospect, a "locked" bit would be good to add to the
entries in the slot table.  Then the code would fail more gracefully if not
enough buffers were allocated:  there would be no unlocked block to swap
out.

10 buffers are guaranteed to work in all cases.  For small memory models,
about 40 buffers in memory at once will be the maximum.  The advantage
of having more than 40 buffers would be more than offset by the
disadvantages of using the large data memory models.


How RED is Showing its Age

RED was designed in an era when most displays were black and white and
no inexpensive terminals supported more than one type style.  Multiple
windows were unheard of.

RED's greatest current weaknesses are its crude methods for selecting text
In particular, the move and copy commands operate only on lines of text
that are selected by entering a range of numbers.  This is an area where
RED is a bit unpleasant to work with.  RED contains no support for a
mouse, er, "pointing device."

The find and change command could be improved a bit.  Besides searching
for attributes such as type style or size, RED would benefit by better
handling of multi-line patterns.  It would also be valuable to be able to
search and replace more complicated patterns such as those used by the
famous grep utility.

As far as the source code goes, if I were writing RED today I would use
some of the insights behind object oriented programming to create multiple
instances of objects such as internal files, buffers, windows etc.
However, the design of RED would probably not change very much as the
result.  Much greater changes would be forced by the user interface
considerations such as multiple fonts.


Professional Programming Style

RED's organization and style can provide a valuable example for beginning
and intermediate programming students.  For a fascinating series of
interviews with famous programmers and a discussion of how they work
and what they think about, I highly recommend the book, Programmers at
Work, by Susan Lammers, copyright 1986, 1989 by Tempus Books of
Microsoft Press.  Many of the issues examined in this book are reflected in
RED's source code.

The most important part of RED's design is its organization into modules.
Except for the buffer routine module, which spans four source files, each
module is contained in a single source file.  The determination of which
routines belonged in which module was a dominant factor in RED's overall
design.

A system module such as embodied in RED has become a feature of all my
large projects.  The system module concept has been very successful: it is
the key to easy portability and fast operation.  As an examination of the file
redsys.c will show, the system module is still needed, even in the era of
so-called "standard" ANSI libraries.

As the book Programmers at Work shows, programmers spend a lot of
time thinking about the details of programs: naming conventions, program
format, layout and appearance, comments, bracketing conventions,
simplicity.  RED shows a consistent style that treats these issues as
important.


Porting RED to other Machines

This section tells you how to modify RED's source code to work with
other compilers and operating systems.  You need not read this chapter if
you already have a working copy of RED;  indeed, you should be an
experienced C programmer to attempt such a task.

Compiling the source code should be easy, but getting the compiled code to
run may be more difficult because every run-time library contains its own
quirks.  RED solves this problem as follows:  all calls to the operating
system are made indirectly through the file redsys.c.  For instance, instead
of calling the fopen() library routine, RED's code calls the sysfopen()
routine.  The job of sysfopen(), and all the other functions in redsys.c, is
to massage its parameters as required in order to keep the local run-time
library happy.  Thus, only redsys.c needs to be changed for different
libraries.
On time-sharing machines the biggest problem may be to find or create
raw, asynchronous system calls which get input from the terminal.  Raw
input is not automatically echoed by the operating system.  Rather than
waiting for a keyboard key to be pressed, an asynchronous input system
call returns a "character not ready" status if nothing is ready.

You shouldn't have to make any changes to the source code except to the
files red.h and redsys.c.  Be particularly leery of modifying the buffer
routines.


Trouble Shooting

Debugging RED is much easier if you have the Sherlock debugging
package.  I estimate that I would have saved at least three months of
debugging had I invented Sherlock before I wrote RED.  Sherlock certainly
came in handy when porting RED to Turbo C and Microsoft C.

You need not remove the Sherlock macros even if you don't own Sherlock.
Just rename the file dummysl.h to be sl.h.  All the Sherlock macros will
then expand to do-nothing code.

If RED crashes after you modify redsys.c you should do the following:
Always keep in mind as you follow these steps that you are looking for
bugs in redsys.c, not in RED's buffer routines.  

First, make sure the sysalloc() function is working properly, which
involves checking sysinit() as well. Storage allocation is a particularly non-
standard part of any library.  Note that sysalloc() is called only by bufinit()
at the start of RED's execution.

Many problems with the library routines will crash RED's buffer routines
on files redbuf1.c through redbuf4.c.  When that happens, RED dumps
information to the screen.  Now comes the fun part.  You are going to
deduce which errant library routines on redsys.c cause the buffer routines
to crash.  Exercise the buffer routines in a controlled manner as follows:

o Get the check_block() and bufdump() routines working.  These functions
are very effective debugging tools because they stop erroneous execution at
the earliest point possible.  They are called whenever any block is changed.

o Get read_file() working.  This is most easily done by inserting a call to
exit() at the very end of the read_file() routine, loading a file using RED's
load command and then using DDT to look at the work file.  See whether
the work file has the proper format as described on file redbuf.h.

o Once the read_file() routine is working, use the save command to test the
write_file() routine.  Examine the newly created file using DDT, or load the
file into an editor you know is solid.

o Test the bufdel() and the combine() routines.  It is important to do this
before inserting lines of text because the insert logic calls the delete logic.
Thus, testing the delete code first is simpler.  Read a large file into RED,
then delete lines in all sorts of orders.

o Finally, test bufins() and split_block() by inserting and replacing lines.
The inject command is a way of inserting a large number of lines quickly,
but the load command is not--it uses separate logic.