as68 - 68000 Assembler, version 1.02


(c) copyright 1982 Steve Passe  all rights reserved
Modified to support CC68K C Compiler by Brian Brown, Nov 1989


TABLE OF CONTENTS
Chapter 1 Introduction           1
Chapter 2 Usage                  6
Chapter 3 Pseudo-ops             8
Chapter 4 Mnemonics             11
Chapter 5 Expressions           13
Chapter 6 S File Format         15
Chapter 7 Error Messages        16
Chapter 8 Differences           18









CHAPTER 1
INTRODUCTION
The as68 assembler is a disk to disk assembler for the Motorola 68000
microprocessor chip. Written in the c programming language, it may be used as
a cross assembler on  any machine supporting c, or as a native assembler if
compiled with a c that produces 68000 output. It's directives and mnemonic set
closely follow that of the Motorola Resident Structured Assembler. It has been
altered to accept assembler output from the 68000 C Compiler. This
modification was performed by B Brown at the Central Institute of Technology,
Heretaunga, New Zealand in 1989.



SOURCE PROGRAM
The input to the assembler is an ascii text file, consisting of a series of
statements written in the assembly language. Each statement consists of one or
more fields within a line.


The assembler is free format within each line, i.e. there is no need to start
a specific field of a statement in a particular column. Fields are separated
from one another with whitespace (tabs or spaces).




STATEMENTS
There are 3 basic statement types. The most common is an assembly language
instruction or mnemonic. It is a command to the assembler to produce a machine
operation code to carry out a specific action.


The second type of statement is called an assembly directive or pseudo-op.
Pseudo-ops tell the assembler how to assemble the program.


The third statement type is called a comment. It is ignored by the assembler,
it's purpose being to allow the programmer to insert descriptions of what the
code is doing within the text of the source program. Comments may exist as the
final field of the other two statement types.


INSTRUCTION STATEMENTS
An instruction statement consists of from one to four fields:

  [label] <mnemonic> [operand] [comment]



LABEL FIELD
The first field, the label field, is optional. It is used to create a symbolic
name for the address of the code generated by the following assembler
mnemonic. This label is stored in the symbol table and any references to it
evaluate to the associated address.


The label field may be the only field of a statement and multiple, label only
fields may follow one another. In all cases the label(s) will evaluate to the
address of the first mnemonic to be assembled after the label(s) is specified.


Labels are composed of alphanumeric characters and may be up to 30 characters
long. All characters of a label are significant, as is the case of alphabetic
characters (i.e. "Foo" is different than "foo").


The first character of a label must be either alphabetic or the character '.'
(period). Following characters may also include the underscore (_), dollarsign
($), and the digits '0' thru '9'.


Labels starting in any other than the first column must be terminated with a
colon (:). Certain symbols are reserved for the use of the assembler and thus
may not be used as labels. These include "SP", "USP", "SR", "CCR", "A0"
through "A7" and "D0"
through "D7".



MNEMONIC FIELD
The second field is the mnemonic or assembly instruction field. It will always
be present in a statement except in the case of a label only statement (label
only statements might more properly be described as assembler directives). If
the line is unlabeled the mnemonic field must be preceeded by whitespace.


A mnemonic will consist of from 3 to 5 ascii characters, the case of which is
not significant. This assembler recognizes the standard Motorola instruction
set. The complete mnemonic instruction set is described in chapter 4,
"Mnemonics". Many 68000 instructions may work on different data sizes.


The desired data size is specified by appending a length modifier or data size
code to the mnemonic. A '.b' extension specifies a data size of byte (8 bits)
while '.l' will cause the data size to be a long word (32 bits). No extension
will cause the data size to be a word (16 bits).  A '.w' extension may be used
for data sizes of word, although this size is the default and as such the '.w'
modifier is unnecessary.



OPERAND FIELD
The operand field is necessary only for those statements whose mnemonic
requires an operand(s). It will contain one or two operands. When two operands
are present they must be separated with a comma (no whitespace allowed between
operands).

The first of two operands is refered to as the source operand while the second
is the destination operand.



COMMENT FIELD
The comment field is optional and consists of all text following the above
fields.



DIRECTIVES
Label Field - Labels used with directive statements follow the general rules
              of those used in assembly statements with one important
              exception: they may only be used with the following directives:

                 1. EQU
                 2. SET
                 3. DC
                 4. DS

Directive Field - The directive field contains an instruction to the assembler
              as to how the program should be assembled. This includes such
              things as the base address of the program, setting of symbol
              values, allocation of program memory storage, conditional
              assembly, etc. The complete list of available assembly
              directions is given in chapter 3, "Pseudo-ops".

Operand Field - The operand field of a directive statement will consist of
              zero or more operands, as needed by the pseudo-op in question.
              Multiple operands are separated with a comma (,). No whitespace
              may exist between operands.

Comment Field - The comment field is identical to that used in instruction
              statements and is optional.

Comments - Comments may exist alone as separate statements. In such cases
              an asterisk, (*), must be the first character on the line.



CHAPTER 2
USAGE

Command Line Format - The command line format is:

        as68 <sourcefile>[.ext] [option[ option]]

where:

 sourcefile     is the source file name.
 ext            is an optional file extension identifier. By default the
                assembler expects source files to have an ext of ".asm".
 option         is one of several possible options in assembly. Whitespace
                must separate multiple options when they occur. Individual
                options are described below.


OPTIONS
The following options are available:

 e,       destination of error messages. If absent all error messages will go
          to the console by default. If present, one or more of the following
          destinations may be specified:
                c       error messages to the console.
                e       error messages to a file named "sourcefile.err".
                f       errors reported in listing.

 l       destination of assembly listing. If absent no listing is made. One or
         more of the following option extensions are available:
                c       listing to console.
                f       listing to a file named "sourcefile.ls"

 o       type and destination of object file. If not present the object file
         will be in Motorola 'S' FILE format.
                s       object to a file named "sourcefile.s19"
                x       no object file to be made.

 s       set the symbol table size. The symbol table requires 8 bytes plus
         the length of the symbol for each entry. The argument should be in
         decimal bytes. The symbol table defaults to 2000 bytes (decimal). To
         reserve 3500 bytes the option would be: 's3500'.

 t       truncate source code lines in listing. This option will cause the
         source code lines sent to any open list channel to be truncated at
         the normal wrap position (see option 'w' below). It defaults to
         being off, a 't' in the command line will turn it on.

 w       set the value of wrap. Source code lines in the listing(s) will
         normally be 'wrapped' to the next line if they extend beyond the
         column number specified by this option. If the 't' option is active
         this option specifies the column beyond which source lines are
         truncated. The default value of 'w' is 80, but can be set between 60
         and any reasonable number of columns. Note that this number
         should be set to the width of your list device, it is not the number
         of columns of source code to a line (i.e. a value of 80 allows 40
         characters of source per line after accounting for the 40 columns
         used by the line/loc/code fields).




OTHER SYSTEMS
The code presently supports the MSDOS operating system. Some work would have
to be done in the command line parser to bring it up on other operating
systems.





CHAPTER 3
PSEUDO-OPS

Assembly Control
The following assembler directives are used to control the assembly:

 ORG    is used to specify the absolute memory origin of the code to be
        assembled. The operand is an expression that evaluates to an
        address within the first 64 kilobytes of memory space (0 thru
        $FFFF). Any memory references outside this range will cause an
        assembly error. Be aware that the 68000 chip sign extends
        absolute short addresses. Thus address references above 32k
        ($8000) will access hardware memory in the range of $FF8000
        thru $FFFFFF. This pseudo-op will cause the assembler to
        generate code using absolute short addressing.

 ORG.L  is also used to specify the absolute memory origin. However, in
        this case the entire address range of the 68000 is usable (0 thru
        $FFFFFF). The assembler will generate code using absolute long
        addressing.

 RORG   causes the assembler to generate program counter relative code.
        The memory range restrictions of the "ORG" directive apply.

 RORG.L causes the assembler to generate program counter relative code as
        above, however the expression in the operand field may evaluate
        to any value within the 68000's address range.

 END    signals the end of the assembly language program.



SYMBOL DEFINITION
The following directives control the definition of symbols:

 EQU    defines a symbol and sets it's value to that of the operand. This
        symbol value is permanent, i.e. it cannot be changed later in a
        program. The operand may be a complex expression but cannot
        make forward references.

 SET    defines or redefines a symbol and sets it's value to that of the
        operand. The value is temporary and may be reset with another
        'SET' directive. Again, forward references are not allowed.



MEMORY ALLOCATION
 These directives are used to reserve and/or initialize memory:

 DC     fills memory locations with constant value(s). An extension of '.B'
        causes individual bytes to be filled with the value of the operand(s).
        An extension of '.L' will cause the operands to be evaluated as 32
        bit values, which are placed in 4 byte blocks, one for each operand.

        No extension or '.W' signifies that the operand(s) are to be
        evaluated as 16 bit values, each being stored in consecutive 2 byte
        locations. Word and long word values are aligned on even address
        boundries.

        DC.B directives causing the location counter to end on an odd
        address will pad 1 byte with a zero value unless the next source
        statement is another DC.B.


 DS     reserves memory locations. Again, a data size extension may be
        appended to 'DS' to specify either byte or long word allocation.

        The operand specifies the number of data cells to reserve, i.e. if
        the extension was '.L' and the operand evaluated to 5, forty (5 * 4
        bytes for a long word) bytes would be reserved. Word alignment is
        not automatic as in the dc directive. To force alignment after a
        DS.B statement use a "ds 0" statement.


LIST CONTROLS
These directives are used to control the listing output:

 LIST   causes listing output (if enabled from the command line) to be
        sent to each of the open list channels. LIST is active by default
        and remains so until a NOLIST pseudo is encountered.

 NOLIST causes listing output to be turned off until a LIST pseudo is
        encountered.




CHAPTER 4
MNEMONICS
The mnemonics used by this assembler follow the standard mnemonic instruction
set as defined by Motorola. Mnemonics may exist in either upper or lower case
in the source file, the assembler makes no distinctions.

 ABCD   add binary coded decimal
 ADD    add binary
 ADDQ   add quick binary, operand in range of 1 thru 8
 ADDX   add binary with extend
 AND    logical and
 ASL    arithmetic shift left
 ASR    arithmetic shift right
 Bcc    branch conditionally
 BCHG   bit test and change
 BCLR   bit test and clear
 BRA    branch unconditional
 BSET   bit test and set
 BSR    branch to subroutine
 BTST   bit test
 CHK    check register against boundaries
 CLR    clear operand
 CMP    compare
 CMPM   compare memory
 DBcc   test condition, decrement and branch
 DIVS   signed divide
 DIVU   unsigned divide
 EOR    exclusive or
 EXG    exchange registers
 EXT    sign extend
 JMP    jump to address
 JSR    jump to subroutine
 LEA    load effective address
 LINK   link and allocate
 LSL    logical shift left
 LSR    logical shift right
 MOVE   move
 MOVEM  move multiple registers
 MOVEP  move peripheral data
 MOVEQ  move quick, operand in range og -128 thru 127
 MULS   signed multiply
 MULU   unsigned multiply
 NBCD   negate binary coded decimal
 NEG    negate
 NEGX   negate with extend
 NOP    no operation
 NOT    bitwise compliment
 OR     logical or
 PEA    push effective address
 RESET  reset external devices
 ROL    rotate left
 ROR    rotate right
 ROXL   rotate left with extend
 ROXR   rotate right with extend
 RTE    return from exception
 RTR    return and restore condition codes


 RTS    return from subroutine
 SBCD   subtract binary coded decimal
 Scc    set conditional
 STOP   stop
 SUB    subtract binary
 SUBQ   subtract quick binary, operand in range of 1 thru 8
 SUBX   subtract binary with extend
 SWAP   swap register halves
 TAS    test and set operand
 TRAP   trap
 TRAPV  trap on overflow
 TST    test an operand
 UNLK   unlink



CHAPTER 5
EXPRESSIONS
Expressions consist of one or more symbols combined by binary and/or unary
(algebraic) operators. Possible symbols include:

 - Symbols defined with the EQU and SET directives.
 - Program labels.
 - Numeric values.
 - The asterisk, ('*'), equates to the present value of the program location
   counter.


ALGEBRAIC OPERATORS INCLUDE:
 - arithmetic operators:
 * multiplication: '*'
 * division: '/'
 * addition: '+'
 * subtraction: '-'


LOGICAL OPERATORS:
 * logical (bitwise) AND: '&'
 * logical (bitwise) OR: '!'
 * left shift: '<<'
 * right shift: '>>'


UNARY OPERATORS:
 * unary minus: '-'
 * location counter value: '*'


SYMBOLS
Symbols are composed of alphanumeric characters and may be up to 30 characters
long. All characters of a label are significant, as is the case of alphabetic
characters (i.e. "Foo" is different than "foo"). The first character of a
label must be either alphabetic or the character '.' (period). Following
characters may also include the underscore (_), dollarsign ($), and the digits
'0' thru '9'.


Numbers may be represented as either decimal, hexadecimal, or binary:
 - decimal numbers are represented by the normal ascii digits '0' thru '9'.
 - hexadecimal numbers start with a dollar sign ('$') followed by the ascii
   digits '0' thru '9' and the ascii characters 'A' thru 'F'.
 - binary numbers start with a percent sign ('%') followed by the ascii digits
   '0' and '1'.




CHAPTER 6
S FILE FORMAT
A Motorola "S file" is similar in structure to an Intel hex file. It consists
of a series of ascii records, each in the following format:

 - The record start character, an uppercase ascii 'S', followed by an ascii
   numeral, '0' thru '9':
         * a '0' for the file header record.
         * a '1' for records with short (16 bit) addresses.
         * a '2' for records with medium (24 bit) addresses.
         * a '3' for records with long (32 bit) addresses.
         * ......
         * a '9' for the tail record.
 - The third and forth bytes forming an ascii hex representation of the number
   of bytes in the body of the record:
        * an address field consisting of 4, 6, or 8 ascii bytes representing
          the load address of the record (record types S1, S2, S3,
          respectively).
 - The body of the record consists of up to 16 bytes of data, each byte
   represented as 2 ascii hex bytes.
 - A checksum byte, again represented by two ascii characters:
         * The checksum for each record (except the last, S9) is the least
           significant byte of the 1's compliment of the sum of the byte
           values of the count, address, and data fields. (ie, everything in
           the record except 'Sx').
         * The checksum on the 'S9' record is undefined/non-existant.




CHAPTER 7
ERROR MESSAGES

 - 1: statement parsing error. The occurrance of this error indicates that the
      line totally confuses the parser and no further diagnostic comments
      (legitimate comments anyway) can be made.
 - 2: bad character in mnemonic-psdo field. An illegal character exists in the
      word present in the mnenonic field, see chapter 1, introduction,
      instruction statements.
 - 3: instruction or pseudo not found in tables. Unless error 2 is also
      generated the instr/pseudo word is properly formed (i.e. no illegal
      characters are in it) but not a recognized instruction.
 - 4: bad character in macro field. Version 1.xx does not recognize macros!
 - 5: macro not found in macro table(s). Again, macros are not yet recognized.
 - 6: improper use of label. Most often this error flags the use of a label on
      a pseudo op line that does not allow the use of labels. See chapter 1,
      introduction, directives:label field.
 - 7: can't evaluate operand. The assembler cannot evaluate the value of an
      operand. This may be caused by a variety of reasons such as imbedded
      spaces, unrecognized operators, unbalanced parenthesis, etc. Additional
      errors will usually be reported that will help clarify the problem.
 - 8: can't evaluate equ operand. As above, generated in the case of an EQU
      statement.
 - 9: can't evaluate set operand. As above, generated in the case of an SET
      statement.
 - 10: attempt to redefine a permanent symbol. The symbol was previously
       defined via an EQU statement and thus cannot be changed.
 - 11: symbol table full. This is a fatal error and will cause the assembly to
       abort. You may try again setting an optional symbol table size from the
       command line. See chapter 2, usage, options:s.
 - 12: unrecognized operand. A legal operand cannot be formed from the data in
       the operand field.
 - 13: symbol not defined in symbol table. The symbol was not encountered in
       the program up to this point. Remember that forward references are not
       allowed in EQU and SET pseudo statements.
 - 14: label out of range for current addressing mode. The value of the label
       is outside the limits of the current statement. This usually is an
       attempt to reference an address beyond the 32k bytes range imposed in
       the short addressing mode. See chapter 3, pseudo-ops, assembly control.
 - 15: operand 1 is not valid for instruction type. The first operand
       encountered is not a valid operand for this particular
       instruction/addressing mode.
 - 16: operand 2 is not valid for instruction type. The second operand
       encountered is not a valid operand for this particular
       instruction/addressing mode.
 - 17: operand 1 is not correctly formed. This may be caused by illegal use of
       operators, undefined labels, etc. The assembler may or may not attempt
       to evaluate the second operand. If it does you are not assured that it
       will do so correctly. For more on this see error #18.
 - 18: operand 2 is not correctly formed. This may be for any of the reasons
       stated above for error 17. Remember that it could be incorrectly
       evaluated if error 17 was also generated and that the second operand
       may be incorrectly formed but not reported as such after error 17
       occurs. This is dependant on the assembler correctly determining where
       the poorly formed operand 1 ends and operand 2 starts.


 - 19: code building function failed. The binary code building function has
       failed to properly construct a sequence of code for the statement. This
       error will usually be followed with additional error #s pinpointing the
       problem.
 - 20: A 3 bit immediate data value out of bounds, i.e. it is greater than 7
       or less than 0.
 - 21: 8 bit bit field specifier out of range.
 - 22: 32 bit bit field specifier out of range.
 - 23: attempt to generate a bit field specifier failed.
 - 24: count operand out of range (1-8).
 - 25: destination register specifier illegal or out of range.
 - 26: source or destination register specifier illegal or out of range.
 - 27: attempt to generat register mask list from operand failed.
 - 28: operand failed to evaluate to a proper source or destination effective
       address.
 - 29: illegal destination effective address, probably label or label with
       index reference.
 - 30: illegal destination effective address.
 - 31: illegal multiple destination effective address, either label, label
       with index, or address register indirect with predecrement or
       postincrement.
 - 32: illegal jump effective address, usually address register indirect with
       predecrement or postincrement.
 - 33: 4 bit vector out of range.
 - 34: expected address displacement failed to evaluate correctly.
 - 35: 8 bit displacement out of range (-128 thru 127)
 - 36: 16 bit displacement out of range (-32768 thru 32766)
 - 37: extent word of operand failed to evaluate correctly.
 - 38: 8 bit operand out of range (-128 thru 255, sign is responsibility of
       programmer).
 - 39: 8 bit extension word value out of range (-128 thru 255).
 - 40: 16 bit extension word out of range (-32768 thru 65535).
 - 41: 32 bit extension word value out of range (overflow).
 - 42: attempt to generate a 16 bit displacement failed, probably out of
       range.
 - 43: attempt to generate an 8 bit displacemnt failed, check range.



CHAPTER 8
DIFFERENCES
This list must be considered incomplete and will be added to as the facts are
brought to my attention.


In General
 - As68 allows addresses assembled under an rorg.l or org.l condition to be
   coerced into a short address by enclosing the entire expression in a set of
   parenthesis followed by '.s'. This allows references to the first/last 32k
   with a code sequence that is 2 bytes shorter than the long address mode. As
   an example:


 org.l $8000
 outport equ $ffa000   * port mapped into last  * page of address space
 move.b d0,outport     * will generate 6 bytes of code while
 move.b d0,(outport).s * will only generate 4 bytes of code



MODIFIED
        format of movem instruction.

                movem /d4/d5/, (a7)+

                NOTE the trailing /