Host Mode
                      The Softerm Host mode provides a general-purpose,
                      unattended, remote access mode which can be used
                      interactively by other terminals and systems.  This is
                      similar to an electronic BBS.

                      Capabilties
                      o Automatically answer incoming calls (with optional
                        password protection provided by the SOFTERM.PWD file
                        created with the PWDEDIT utility program)
                      o Send and receive files using any protocol supported
                        by Softerm
                      o Function as a server for the Kermit-Server and
                        Softrans file transfer protocols (meaning that a
                        command to initiate the file transfer is not
                        required)
                      o Process DOS-type commands, such as:  DIR, TYPE,
                        DELETE, RENAME
                      o Process Script files automatically or on demand

                      Enter Host Mode
                      Host mode is initiated by running the HOST() command
                      from a Script file, such as:

                      > HOST (20,30,hangup,yes,'automenu.scr')

                      Note:  Host mode will go into effect with the current
                      Speed, Data Bits, Stop Bits, Parity and Duplex
                      parameters.

                      Operation
                      When Host mode is in effect, Softerm will wait for a
                      connection to be established.  If the optional logon
                      processing is specified, a caller must supply a
                      recognized username and password before Softerm
                      displays the READY prompt and responds to valid
                      commands.

                      Once initiated, Softerm will wait for a connection to
                      be established if one is not already present, display
                      a READY message after processing an optional logon,
                      and wait for requests received through remote terminal
                      interaction, or the Softrans or Kermit protocols.

                      A system in the Host mode functions in a passive
                      manner, responding only to requests from the calling
                      terminal or system.  Host mode allows completely
                      unattended operation.  If logging is active, all
                      commands processed, including error messages, will be
                      recorded in the log file.







                      The TIMEOUT assignable system variable (in the Script
                      language) does not affect file transfer operations
                      initiated from the Host mode which has fixed or
                      profiled timeout and retry parameters for all
                      protocols supported.  The Softrans and Kermit
                      protocols and Xmodem receive operations use a 10-
                      second timeout interval and allow for 5 retries.
                      Xmodem send operations will timeout after
                      approximately 70 seconds.  The Character protocol uses
                      a 30-second timeout on transmit and a 60-second
                      timeout on receive.

                      The Host mode also provides an option to automatically
                      run a script file on connecting after a successful
                      login.  This can be used to display user welcome
                      messages, instructions on how to perform various user-
                      defined operations, or a security automatic callback
                      capability.

                      Important
                      To provide caller interaction, such as displaying a
                      menu and waiting for a key, you will need to use the
                      XMIT:WAIT Script file command.  To simply display a
                      welcome message, you could use the file transfer SEND
                      command using Character protocol.

                      The CALL command is provided to run script files
                      interactively when requested by remote users.  The
                      TERMINATE command lets a remote user terminate the
                      Host mode to interact directly with the script file
                      which initiated the Host mode.

                      Once the Host mode is initiated, it normally will
                      remain active until terminated locally.

                      Optional Logon and Password Processing

                      Softerm provides an optional logon security feature
                      to restrict access to the Host mode.  It includes the
                      capability to assign a default directory to each
                      user, and to restrict the type of commands each
                      caller can process while using the Host mode.

                      To implement this feature, a special password file
                      called SOFTERM.PWD must be created in the same
                      directory as Softerm's system read files.  The
                      password file is created with PWDEDIT.EXE, a GUI
                      utility program supplied with Softerm Modular.  Note:
                      PWDEDIT is documented completely through the online
                      Help system.  Just press F1 or select the Help
                      pushbutton.






                                              - 2 -







                      SOFTERM.PWD is a fixed-format ASCII file that appears
                      similar to the following if the DOS TYPE command is
                      used:

                      C:\SOFTERM>TYPE SOFTERM.PWD
                      Jones, John        M_Ambrosius
                                    <

                      Although access restrictions won't appear, names and
                      passwords do.

                      Upper- and lower-case characters, except spaces, are
                      valid in the username and password fields and must be
                      matched exactly when entered by a remote user.  Each
                      user name must be unique.  Multiple entries with the
                      same user name are not valid and only the first
                      occurrence can be matched.

                      When a remote user connects to a system in Host mode,
                      and a SOFTERM.PWD file is found in the system
                      directory, the following logon sequence is processed:

                      Host displays   User types
                      Login           Username followed by CR
                      Password        Password followed by CR
                                      (echo is suppressed during entry of
                                      the password)
                      Ready           Any valid host mode command

                      Important:  Username and Password are case sensitive.
                      For example, if the Username was created as SETH, it
                      must be entered in upper- case characters.

                      If an error is made when entering the Username or
                      Password, press Esc to cancel the entry and repeat
                      the prompt.  If either the Username or Password is
                      invalid when entered, the logon sequence will be
                      repeated.  After four unsuccessful attempts to logon,
                      a disconnect will occur.

                      Once a successful logon has been completed, any valid
                      Host mode command or Softrans and Kermit file
                      transfer can be processed subject to access restric-
                      tions indicated in the password file for the user.
                      After a Host mode session is complete, the remote
                      user can use the BYE command to terminate and
                      disconnect, or the LOGOUT command to terminate and
                      restart processing without disconnecting.









                                              - 3 -







                      Host Mode Interactive Commands

                      The Host mode responds to interactive commands which
                      are entered in the terminal communications mode at
                      the remote system or terminal.  The READY prompt
                      indicates it is ready to receive a command.

                      The host will respond to Ctrl S requests to stop the
                      display of data and Ctrl Q requests to resume the
                      display of data (such as when a file is TYPEd).

                      If you wish to cancel the entire command line, just
                      press Esc.  Host mode will "beep", and display a new
                      READY prompt for any command not recognized.  To
                      cancel the display of a typed file or directory list,
                      press Ctrl C.  If you press Ctrl S to stop the
                      display of a typed file or directory list, the Host
                      mode will timeout after 30 seconds and redisplay the
                      READY prompt.

                      Many of the Host mode interactive commands require
                      arguments.  The command and argument must be
                      separated by at least one space.

                      Important
                      All commands are issued by the caller and tell Host
                      mode to do something.  For instance, to send a file,
                      the caller must instruct Host mode to prepare to
                      receive a file.

                      Exceptions to the Rule
                      Because Host mode acts as a server for the Softrans
                      and Kermit-Server file transfer protocols, there are
                      no commands to send and receive using those
                      protocols.  The caller simply needs to initiate the
                      file transfer operation.

                      Unless stated otherwise, the following will be true
                      for all operations:

                      1. If no path is specified, file transfers will use
                         the current directory.
                      2. If the optional Host mode logon processing is in
                         effect, the command is restricted by the access
                         restriction code and the path specified for the
                         file is validated for the current username.
                      3. Unless supported by the protocol, wildcard
                         characters (* and ?) should not be used in the
                         Source field on SEND operations.








                                              - 4 -







                      Interactive Commands

                      The following commands are entered by the caller to
                      the Host system:

                      ACCEPT [-,&] d:\path\filename
                      Used by the caller to send a file using character
                      protocol.  The filename argument specifies the name
                      of the file to receive the data.

                      If the very first character of the path\filename is a
                      hyphen (-), the file will replace a file of the same
                      name on the Host system.  Example:

                          ACCEPT -C:\SOFTHOST\TEST.TXT

                      If the very first character of the path/filename is
                      an ampersand (&), the file will append to a file of
                      the same name on the Host system.  Example:

                          ACCEPT &C:\SOFTHOST\TEST.TXT

                      If a file of the same name exists and neither special
                      character is used, the transfer will fail.

                      The host will display a GO> prompt when the system is
                      ready to accept data.  Characters can be typed by the
                      caller or a file can be transferred using character
                      protocol.

                      The ACCEPT command is terminated by a Ctrl Z
                      character or a 60-second timeout.

                      BYE
                      Terminate the current Host mode session and dis-
                      connect.

                      CALL d:\path\filename 1='string1'...5='string5'
                      Run a script file and then return to the Host mode.
                      If logon processing is in effect, all subsequent
                      commands will observe the access restrictions for the
                      current user.

                      Note:  We recommend that the CALLed script file does
                      not end with the CONVERSE command.  This command
                      places the Host Mode machine in Online terminal
                      emulation mode with unpredictable results.

                      The command line may include optional switches to
                      specify the contents of the Script Variables SV1-SV5
                      used in the script file as follows:






                                              - 5 -







                      Switch      Function
                      1='string'  Replaces SV1 in script file
                      .   .   .   .   .   .
                      5='string'  Replaces SV5 in script file

                      Note:  The quote marks are optional and would be
                      necessary only if the string contained embedded
                      spaces.

                      Up to 5 strings can be specified which are
                      substituted for dummy arguments in the script file
                      when the script file is run.  Each string may be up
                      to 64 characters in length.  A dummy argument is
                      defined in the script file as SV followed by a number
                      from 1 through 5.  Thus, wherever SV1 occurs in the
                      script file, it will be replaced by the string
                      defined for the SV1= switch in the CALL command line.
                      Note:  The maximum length of the command line is
                      restricted to 128 characters.

                      CD d:\path
                      Change the current default directory used for file
                      names specified in file transfer operations used in
                      the Host mode.  The new default directory, including
                      a drive specifier and directory path, is entered as
                      an argument on the command line.  If the optional
                      Host mode logon processing is in effect, the command
                      is restricted by the access restriction code for the
                      current username.

                      CURRENT
                      Display the default directory for file transfer
                      operations used in the Host mode.  It initially is
                      set to the current default directory when the HOST()
                      command is processed, or to the subdirectory in the
                      password file for the current user.

                      DELETE d:\path\filename
                      Remove an unwanted file from disk.  If no drive or
                      directory path is entered, the file is deleted from
                      the current directory.  You can use the wildcard
                      characters ? and * in the filename and in the
                      extension.

                      This command can be abbreviated to DEL.

                      DIR d:\path\filename
                      The DIR command displays a list of the filenames in a
                      specified directory.  If no drive or directory path
                      is specified, all files in the current default
                      directory will be listed.  The wildcard characters *
                      and ? may be used in the filename and extension
                      parameters to list a subset of the files in the
                      specified directory.



                                              - 6 -







                      ECHO <On or Off>
                      This command turns echo mode for the ACCEPT command
                      on or off.  If the argument is specified as ON,
                      characters transmitted to the host using an ACCEPT
                      command will be echoed back to the remote terminal or
                      system for visual confirmation.  If the argument is
                      specified as OFF, characters received are not echoed.
                      The echo mode defaults to ON.

                      HELP
                      If the HOSTMODE.HLP file is available, the HELP
                      command will display information about using the host
                      mode and a list of commands.

                      KSEND d:\path\filename
                      Prepare the Host system to send a file using the
                      Kermit protocol.  This command can be used by remote
                      Kermit programs unable to access a Kermit server.
                      The command is equivalent to a Kermit protocol SEND
                      command.  The wildcard characters * and ? may be used
                      in the filename or extension to allow multiple files
                      to be sent using a single command.

                      LF <On or Off>
                      This command turns the line feed mode for the TYPE
                      and ACCEPT Host mode commands on or off.  If the
                      argument is specified as ON, the host will add line
                      feed characters after carriage returns in transmitted
                      or echoed data.  If the argument is specified as OFF,
                      no line feed characters are added.  The line feed
                      mode initially is set to ON.

                      LOGOUT
                      Terminate the current Host mode session and
                      restart with logon processing without a disconnect.

                      RECEIVE <profile_name or protocol_name> filename
                      Prepare the Host system to receive the designated
                      file using the specified File Transfer profile or
                      File Transfer Protocol.  If a profile and a protocol
                      share the same name, the command will use the
                      profile.

                      Note:  This method lets you use the Honeywell- Kermit
                      protocol with the desired GCOS Mapping setting by
                      using the appropriate profile.

                      RENAME d:\path\filename1 d:\path\filename2
                      Change the name of a file in the current or a
                      specified directory.  The first file name entered
                      with optional drive and path specification is the
                      file to be renamed, and the second file name is the
                      new name.  A drive or path specification is not




                                              - 7 -







                      allowed in the new filename.  The ? and *  wildcard
                      characters are allowed.

                      This command can be abbreviated to REN.

                      SEND <profile_name or protocol_name> filename
                      Prepare the Host system to send the designated file
                      using the specified File Transfer profile or File
                      Transfer Protocol.  If a profile and a protocol share
                      the same name, the command will use the profile.

                      Note:  This method lets you use the Honeywell- Kermit
                      protocol with the desired GCOS Mapping setting by
                      using the appropriate profile.

                      TERMINATE
                      Terminate Host mode processing to interact directly
                      with the script file from which the HOST() command
                      was started.  If the optional Host mode logon
                      processing is in effect, the command is restricted by
                      the access restriction code.

                      TYPE d:\path\filename
                      Cause a file to be typed or displayed by the Host
                      system.  The command is equivalent to a character
                      protocol SEND command.  The display can be cancelled
                      by entering Ctrl C.

                      XRCV d:\path\filename
                      Prepare the Host system to receive the designated
                      file using the Xmodem protocol.  The filename
                      specifies the file to receive the data.

                      Note:  The caller may send the file using Xmodem,
                      Xmodem-CRC or Xmodem(Large Block) and the Host system
                      will detect and adjust for the error correction
                      method and block size.

                      XSEND d:\path\filename
                      Prepare the Host system to send the designated file
                      using the Xmodem protocol.

                      X1KSEND d:\path\filename
                      Prepare the Host system to send the designated file
                      using the Xmodem (Large Block) protocol.

                      YGRCV [d:\path\filename]
                      Prepare the Host system to receive the designated
                      file using the Ymodem-G protocol.  The wildcard
                      characters * and ? may be used in the filename or
                      extension to allow multiple files to be transferred
                      using a single command.





                                              - 8 -







                      If the optional drive, path and file name are not
                      specified, the command will use the data in the
                      protocol header block.

                      YRCV [d:\path\filename]
                      Prepare the Host system to receive the designated
                      file using the Ymodem protocol.  The wildcard
                      characters * and ? may be used in the filename or
                      extension to allow multiple files to be transferred
                      using a single command.

                      If the optional drive, path and file name are not
                      specified, the command will use the data in the
                      protocol header block.

                      Note:  The caller may send the file using Ymodem or
                      Ymodem (Large Block) and the Host system will detect
                      and adjust for the block size.

                      YSEND d:\path\filename
                      Prepare the Host system to send the designated file
                      using the Ymodem protocol.  The wildcard characters *
                      and ? may be used in the filename or extension to
                      allow multiple files to be transferred using a single
                      command.

                      Note:  The caller may specify Ymodem-G to receive the
                      file and the Host system will detect and adjust for
                      the block size and transmission method.

                      Y1KSEND d:\path\filename
                      Prepare the Host system to send the designated file
                      using the Ymodem (Large Block) protocol.  The
                      wildcard characters * and ? may be used in the
                      filename or extension to allow multiple files to be
                      transferred using a single command.

                      Note:  The caller may specify Ymodem-G to receive the
                      file and the Host system will detect and adjust for
                      the block size and transmission method.

















                                              - 9 -







                      Softerm-to-Softerm File Transfers

                      System-to-system file transfers using Softerm are
                      accomplished by placing a port on one of the two
                      systems in the Host mode using the HOST() command.
                      The other system then can establish a connection with
                      the agreed upon serial parameters.  Once connected,
                      the system in Host mode will transmit the READY
                      message to the other system.

                      The system in Host mode will respond to commands
                      entered by the remote system through terminal
                      interaction, or to Softrans and Kermit file transfer
                      commands SEND and RECEIVE entered from the File Menu
                      or script file processing.










































                                             - 10 -