- SpeedRamsey.asm - A fifteen minutes hack - © 1993 by Holger Lubitz -

            *** Sets the skip bit in the Rev G Ramsey ***

Intro

Well, I had played around with the skip bit earlier - but it took some
posts to comp.sys.amiga.hardware by people eagerly waiting for this to
convince me to release it.  Isn't Usenet great ?  :)

The  reason  I didn't release it immediately is that the fastest RAM I
could get had only 70 ns.  The skip mode needs 60 ns or faster RAM for
proper  function.   I have only been able to test this by removing all
banks but one from my Amiga.  If I have all four banks installed, this
doesn't  work.   Probably  the additional capacitive load is enough to
slow down a signal by 1 ns, causing this to break.  I don't know.

However,  if you got 60 ns DRAM, you should be fine even with all four
banks  populated.  In my Amiga, running SpeedRamsey reduces the memory
latency  as measured by AIBB 6.1 from 8.1 to 7.1, for a speed increase
of roughly 10%.


How to use it

Just start it.  From Version 1.2 upwards, you can either start it from
WB  or from the CLI (no interesting icon yet, sorry).  You get version
information,  an  author  notice  and a short message telling you what
SpeedRamsey  did,  if  anything.  If you don't have a Rev G ramsey, it
will complain about that and do nothing.


How it works

This  tiny  little  program  is  a  very  simple  tiny little program.
However,  you  need  to  know about Ramsey to understand what it does.
Ramsey  appears  only  in  the  supervisor  data  space.   It  has two
byte-wide registers, one at $DE0003 and one at $DE0043.  The first one
is read-write, and this is where you configure Ramsey.  The second one
is read-only, it offers version information.

Currently  there  are  only two versions of Ramsey.  The Rev G Ramsey,
which  is  the  revision  you  find  in all Amiga 4000s, allows you to
select a mode called skip mode.  More on this later.

The older Rev D Ramsey used in the A3000 doesn't support the skip mode
this  program  is setting.  It uses the very same bit to select memory
width.   But  because  nobody  ever  used  1Mx1 DRAM in the A3000, and
probably  also  because  bits  in  the only configuration register are
somewhat  precious, the bit got reassigned for the skip mode in Rev G.
This makes it important to check for the right Rev of Ramsey.  I don't
even  want to think about the crash you'd get by setting this bit on a
Rev D Ramsey.  Trying it out is certainly not recommended.

So,  after  we  checked  for Rev G by comparing with $0F (a $0D in the
version  register  signals a Rev D Ramsey, by the way), we fiddle with
the  bit and return from the supervisor mode, having set a return code
for  the  rest  of  the program, which puts out an appropriate message
and,  if started from the CLI, sets the return code (to 0 for bit set,
5 for bit reset, 15 for no Rev G Ramsey found).


Why it works and what skip mode really means

The  skip  mode  speeds  up  RAM  access from five clocks each to four
clocks  each  by  skipping  the  last  cycle.   Some  people call this
60-ns-mode  because  you need 60 ns DRAM or faster to ensure that this
works and doesn't crash your Amiga. 


My own experience

You  might  succeed in running this with slower DRAM, depending on how
many  banks  you've  populated  and  who manufactured the SIMMs you're
using.   Some  seem  to have higher safety margins than others.  In my
machine, setting the skip bit with only one bank populated (I am using
Micron 1Mx32 SIMMs with 70 ns access time) works.  Setting it with all
four banks populated crashes my machine (see Intro).

You  can't  damage your Amiga, but be prepared for a cold reboot if it
doesn't  work.  Just try it - but don't have anything important in the
background when you do so.  You have been warned.


Frequently asked questions

* Is the Ramsey setting permanent ?

(here was a slightly incorrect answer in earlier doc revisions because
it wasn't really thought out. Sorry for that)

No,  the  setting  survives  a reset, but has to be set manually after
each  power  on.   You  might want to put it in your User-Startup once
you're  sure  that  your memory is fast enough.  Since SpeedRamsey was
designed  to  toggle  the bit and doesn't support parameters to set or
reset it (yet), you have to trick around a bit.  Here's how:

speedramsey >nil: ; toggles the bit, sets warn if reset
if warn
  speedramsey >nil: ; if reset, toggles it again
endif

I agree that this is not nice, but it works for now. 

It  isn't  really  possible  to  make  the setting permanent (in other
words,   survive  a  cold  reboot).   However,  the  functionality  of
SpeedRamsey  might  get included in the OS one day, who knows (I could
imagine setting the bit, testing if the RAM still works, and resetting
it  if  it  doesn't,  but  you  can  probably only do that from ROM or
Chipram - ah, wait, now THEREs an idea - maybe for a future version of
SpeedRamsey, right now I'm very busy updating the docs :)

* Can I damage my machine by using SpeedRamsey ?

No.  At least not as far as I know.  If it crashes, just switch it off
and on again.

* Does this work on my (insert specific A4000 model) ?

This  should  work on any A4000 with 60 ns DRAM.  It doesn't matter if
you  have  a 030 or 040 model.  Only one person with 4 banks and 60 ns
DRAM reported a crash.  I'd really like to find out why.

* I have only slower DRAM - should I try it anyway ?

See  question  2.   Just  try it out, you can't damage your machine by
doing so.  If it works, fine (use a RAM test program just to be sure),
if it doesn't switch it off and archive SpeedRamsey for later use when
you've gotten faster DRAM.


Distribution

Permission  for  non-commercial distribution of the unmodified archive
is  hereby  granted.   It  must contain SpeedRamsey itself, its source
code   SpeedRamsey.asm,   this  doc  file  SpeedRamsey.doc,  the  icon
SpeedRamsey.info  and the questionnaire SpeedRamsey.survey, and _only_
those  (_no_  stupid  .displaymes  in archives with my software!) Fred
Fish is explicitly allowed to include this in his library.

If you release anything based on this source, please give credit.


Bugs, Suggestions, etc.

You   can   contact   me  electronically  by  using  my  eMail-Address
hal@caty.north.de.   If  you don't have eMail yet, get access to it or
lose.  After all, we are in the nineties now, aren't we ?


History

1.0  (12-Aug-1993) First Usenet release
 
The original SpeedRamsey.  Size of program:  72 bytes.

1.1  (13-Aug-1993) Second Usenet release

Mainly updated docs because of questions I got by eMail.

Also  made  program slightly shorter, SpeedRamsey now checks for Rev G
and  only  sets  the  bit on Rev G.  It used to do so on any Non-Rev-D
Ramsey, but who knows what this bit will do in the future ?  Optimised
code slightly when changing this.

The  bit  is  now  flipped  instead of set.  Running SpeedRamsey again
resets  the  system  to  the  old  state.   However, you still have no
indication  what  happened  other  than  checking  by  running AIBB or
similar.  I really need to put in messages soon :)

Size of program:  68 bytes.  (Isn't assembler great ?)

     (14-Aug-1993) Not released

Well, I just _had_ to include the messages.  Now SpeedRamsey tells you
what  it  did.   It  even tells you if you haven't got a Rev G Ramsey.
Also added WB startup code that opens an own window to write into.

Size  of  program  with text and startup stuff:  Still only 396 bytes,
but pretty large compared to 1.1 - additional comfort has its price :)

     (15-Aug-1993) Not released

Slight changes to the documentation

1.2  (16-Aug-1993) Third (and last) Usenet Release

Updated FAQ list.  Some more doc changes.  Added questionnaire because
one  person  reported a crash with 60 ns DRAM.  Please fill it out and
return  it,  regardless  if SpeedRamsey worked for you or not.  I need
that  information  to  find  out under which conditions SpeedRamsey is
safe and under which it is not.

1.2a (17-Aug-1993) First Aminet Release

Corrected  FAQ  list.   The  first  answer was not totally correct and
could  be  misunderstood,  too.   Also offers a workaround for putting
SpeedRamsey into the User-Startup now.

SpeedRamsey now contains version information, which increased its size
slightly.  Size of program: 408 bytes.


To do list

Parameters for explicit setting/resetting of the skip mode bit 
function  check  if  possible  (I'll  have  to  look into this) 
maybe setting/resetting the other Ramsey bits.