Chapter 15: PRINTING MSP FILES


     EASIGRAF saves images of the graphs it produces to disk
     in the format used by Microsoft Paint, a program supplied
     free with Microsoft Windows. So that other programs can
     tell what format a file is, you should give it the
     extension .MSP when you save it from EASIGRAF. The MSP
     file can then be read in and altered by the Paint
     program, or it can be read in by any other program which
     can deal with MSP files, for example the more recent
     versions of WordPerfect. After the MSP file has been read
     into one of these programs and any desired adjustments
     made, the program can be used to print it out in the
     usual way. (Note that newer versions of Microsoft Paint
     by default expect the file to be in a format called BMP
     rather than MSP, but an option to read in MSP files
     instead is still available.)

     It is possible to print out MSP files directly without
     first reading them into one of the above programs by
     using a small utility program supplied called PRMSP.EXE.
     However note that this utility may not work on MSP files
     which have been saved from some versions of Paint
     (because the format as been changed). There should be no
     problem in using PRMSP to print out the MSP files
     produced by EASIGRAF.


     15:1. Using PRMSP.EXE

     If you do not own Microsoft Paint then you can print out
     the saved file directly from disk to an Epson- or
     IBM-compatible dot matrix printer or a laser printer
     using a small program supplied called PRMSP. It is
     distributed in the self-extracting archive UTILS.EXE. To
     use it, supposing you have saved your graph picture with
     the name SAVED.MSP you should type:

     PRMSP SAVED.MSP

     and the file will be printed.

     The full details of the options available with PRMSP are
     as follows:

     PRMSP infile.msp [outfile.prn] [/flag1 /flag2 etc.]

     infile.msp - the name of the saved MSP file to be printed
     out.

     outfile.prn - the name of a file to be printed to which
     will contain the correct printer codes. This is optional
     and if no name is given then the printer (PRN) will be
     used instead.

     /I - this flag means print to an IBM-compatible printer
     instead of an Epson-compatible printer.

     /P - this flag means print the graph with the paper in
     "portrait" orientation - across the page - instead of the
     default "landscape" orientation - down the page. Note
     
       115 

        Printing MSP files  
     
     that in earlier versions of PRMSP this had the opposite
     effect because it was taken to refer to the orientation
     of the diagram rather than the paper.

     /H - high density - will work with an Epson-compatible
     24-pin printer to give a picture three times smaller the
     default, or twice as small on a Hewlett-Packard
     compatible laser printer.

     /D - draught mode - should be quicker but lower quality
     for dot matrix printers in high density mode or
     "portrait" orientation. On Hewlett-Packard compatible
     laser printers prints out double normal size.

     /Snumber - this flag means print "number" spaces before
     each line of the picture - use it to control where the
     graph appears on the page. The default is 6. (Only for
     dot matrix printers.)

     /Lnumber - this flag controls the line spacing on the
     printer, as used by the ESC A command. It is a value for
     lines per inch. By default "number" is set to 8, but if
     the lines of your graph come out separated or
     overlapping, then using this flag may help you to adjust
     the line-spacing to produce a better picture. (Only for
     dot matrix printers.)

     /Fnumber - this flag lets you determine whether a line
     feed (new line) character is sent to your printer with
     each carriage return character. If number is 0 then no
     line feed is sent, if it is 1 then a line feed is sent.
     The default is 1. If your graph comes out "double-spaced"
     - with gaps between each line - then specifying /F0 may
     cure the problem. (Only for dot matrix printers.)

     /FF - send a form feed (new page) after printing the
     file. (You must use this flag on the last file you print
     on a laser printer, but other files can be printed onto
     the same page first.)

     /HP - produce output for a Hewlett-Packard compatible
     laser printer.

     /PS - produce output for a PostScript printer.

     For Hewlett-Packard or PostScript printers only:

     /OXnumber - x origin, default 72. Measured in points
     (1/72") approximately from the left hand edge of the
     page.

     /OYnumber - y origin from the bottom edge of an A4 page,
     default 72 in "portrait" orientation for the bottom left
     corner, or 720 in "landscape" orientation for the top
     left corner of the graph.

     For PostScript printers only:

     /SXnumber - x scale, default 1.0.



     
       116 

        Printing MSP files  
     
     /SYnumber - y scale, default 1.0.

     /ROnumber - rotation about origin, default 0.0.

     Example use of PRMSP:

     PRMSP HISTO.MSP /HP /OY100 /OX200

     Print HISTO.MSP to a Hewlett-Packard compatible printer
     with origin at 200,100.

     PRMSP MYGRAPH.MSP /PS /SX0.5 /SY3 /RO75

     Print MYGRAPH.MSP to a PostScript printer, twice as
     narrow and three times as high as normal, rotated through
     75 degrees.

     PRMSP ANOVA.MSP TEMP.PRN /S12 /I

     Print the file ANOVA.MSP out to the file TEMP.PRN, in a
     format suitable for sending to an IBM-compatible dot
     matrix printer, with twelve spaces to the left instead of
     the default 6. Then later TEMP.PRN could be printed by
     entering:

     PRINT TEMP.PRN

     The advantage of this is that by using the DOS PRINT
     command printing occurs in background - you can get on
     with other things while the graph is being printed.

     Notes

     Except in the case of PostScript printers, PRMSP cannot
     work if your computer does not send 8 data bits to the
     printer. This is sometimes altered by the MODE command
     which is usually in the AUTOEXEC.BAT file - see your DOS
     manual for details - if your printer is on a serial cable
     rather than the ordinary "Centronics" parallel cable.
     Also make sure that your printer is set to receive 8 bits
     rather than 7 - see your printer manual if you have
     problems.

     You must always use the /FF flag when you wish to produce
     output from a laser printer, otherwise the image will be
     stored in the printer's memory but will never be
     displayed. However you may wish to print a number of
     graphs onto different parts of the same page and then
     only use the /FF flag with the last one.













     
       117