OzGIS                                           
                                                                                
                                V8.8                                            
                                                                                
                           (September 1992)                                     
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                         Geismar Holdings Pty Ltd.                              
                                                                                
                         QMDD Box 6108                                          
                         Queanbeyan,                                            
                         Australia 2620.                                        
                                                                                


                                                                       2
               PREFACE                                                          
                                                                                
OzGIS is a software system for displaying geographically referenced data as     
coloured maps on graphics display devices. The maps portray the data            
values associated with geographic zones by uniform colours, site data by        
different sized symbols, and line data by different line types.                 
The system can be used to analyze socio-economic and demographic                
data produced by censuses and surveys and to support management decisions       
associated with for example marketing, sales, site and personnel location,      
and advertising. Other spatial data such as environmental data can be displayed.
                                                                                
The software was originally developed as part of a research project at the      
Division of computing Research of the Commonwealth Scientific and Research      
Organisation (CSIRO) in Canberra for a mapping product called COLOURMAP.        
                                                                                
Software development started in 1979 with the purchase of hardware that had     
been developed for the DIDS mapping system in the White House in Washington DC. 
This hardware consisted of a PDP11 mini-computer and a DeAnza display system.   
The display featured a 12bit frame buffer, 4096 value primary look-up table and 
cascaded 256 value colour table. This enabled maps of up to 4000 zones (e.g.    
USA Counties) to be displayed and manipulated very rapidly, and is the best     
hardware so far produced.                                                       
                                                                                
The environment changed over several years, with moves to larger PDP11 systems  
and to VAX and CDC machines. Several display systems were used, Tektronix,      
Jupiter and RAMTEK, and maps were generated on plotters and film recorders. The 
system was also available on CSIRONET, an Australia-wide computer network with  
Control Data and FACOM host computers. The 1981 ABS Census data could be        
accessed via the SIR/CENSYS system on the Cyber 845. A system was developed to  
handle the Census district boundaries digitised by the Division of National     
Mapping, to enable windowing, line simplification and aggregation for production
of geographic map data files. The SAS system was available on the FACOM 180 for 
statistical analysis and display of map data.                                   
                                                                                
The first year of development was supported by Techway, and APASCO supported    
the development of techniques for retail applications. APASCO used the system   
and hardware for several years as part of their consulting activities to churn  
out thousands of maps.                                                          
                                                                                
 The Division of computing research was split into the CSIRONET computing bureau
and the new Division of Information Technology in 1985. Later, CSIRONET was     
given to private industry. The mapping project was abandoned.                   
                                                                                
The software was resurrected in late 1990 and ported to the IBM PC to produce   
the current system.                                                             
                                                                                
 The purpose of the Guide is to introduce the facilities of OzGIS. The Guide is 
intended to complement the messages and assistance given during the operation of
OzGIS.                                                                          
                                                                                
 The user should understand the techniques of statistical data analysis and     
computer mapping, and also have an elementary understanding of colour           
representations.                                                                
                                                                                
This manual describes the  IBM PC version. Some of the facilities that were     
available on the PDP11 and VAX systems have not yet been ported.                
                                                                                


                                                                       3
                                                                                
                                                                                
                                                                                
Geismar Holdings is a Canberra based software company offering consulting and   
contract programming services in the areas of:                                  
                                                                                
. C and FORTRAN programming                                                     
. Spatial databases                                                             
. Scientific applications                                                       
. Graphics                                                                      
. UNIX workstation, minicomputer and PC environments                            
                                                                                


                                                                       4
                    1. OzGIS INTRODUCTION                                
                       ==================
 
                                                                                
                                                                                
This chapter gives an overview of the programs in the OzGIS system, the concepts
behind the design of the system, and something about the software.              
                                                                                
                                                                                
                                                                                

  1. 1 Programs                                          
       --------
 
                                                                                
                                                                                
The system consists of several modules:                                         
                                                                                
OzEnter  - for entry of data files into the system.                             
OzData   - preparation of data for mapping                                      
OzZone   - formation of zones / polygons structure from line segments           
OzGIS    - interactive display and analysis                                     
OzCensus - Display and analysis of Census type data (subset of OzGIS)           
OzGISco  - maths coprocessor version of OzGIS                                   
OzMap    - output of saved displays on plotters and printers and to files       
OzTerr   - definition of territories from zones                                 
OzProj   - map projections                                                      
                                                                                
Being tested are:                                                               
                                                                                
OzSpat   - spatial operations                                                   
OzDigit  - digitising                                                           
WINDOWS3.1 version                                                              
                                                                                
Start by using OzCensus; its a simpler version of OzGIS suitable for            
Census-type mapping.                                                            

  1. 2 Concepts                                          
       --------
 
 OzGIS aims to accept basic data files and to provide most of the facilities    
required for the analysis and display of attribute data as maps. The            
analyst has to be able to rapidly use the facilities, so OzGIS provides an      
interactive user interface. The user interacts via menus and is aided by on-line
assistance.                                                                     
                                                                                
 Visual inspection of choropleth maps is the intuitive way to interpret the     
spatial features of data. An analyst needs to be able to rapidly display and    
manipulate maps to aid his understanding. OzGIS was designed to enable maps to  
be changed within seconds so the analyst does not lose his train of thought.    
                                                                                
 OzGIS enables the analyst not just to display a map, but to generate the map   
that best shows the features of the attribute data. A hardcopy map can be       
generated as the final operation as a record or for dissemination.              
                                                                                
Easy to use systems are either trivial systems, or have a small number of       
options. The enormous number of options within OzGIS means that it takes        


                                                                       5
some time to understand everything. However, maps can be produced quite simply  
by using only a small number of options and by using the system defaults.       
                                                                                
                                                                                
 OzGIS can be considered as one system of a facility for analysis and display   
of Census type data. The various components are:                                
                                                                                
 - Database systems for manipulation and retrieval of attribute data            
 - Systems for generation of map boundary data                                  
 - Statistical analysis systems with graphic display and reporting facilities   
 - Mapping systems with analysis and hardcopy facilities.                       
                                                                                
Hence you may use:                                                              
a CAD package for digitising geographic data                                    
a database system for storing attribute data                                    
a spreadsheet for manipulating numeric data                                     
a statistics program for analysis                                               
etc                                                                             
                                                                                
                                                                                
 It is expected that an analyst would have access to a PC close to his          
office. The PC/workstation may be connected via a computer network to           
provide access to large host machines. The host machines would contain the      
database systems from which map data could be extracted, and other systems for  
analysis and hard-copy generation.                                              
                                                                                

  1. 3 Environment                                       
       -----------
 
 OzGIS requires advanced raster display systems for rapid display of maps.      
Unfortunately PC display systems are extremely limited in capability. In        
particular only a maximum of 256 colours are available (on 512K super VGA       
boards). OzGIS is able to generate maps on most graphic devices by using polygon
fill to colour map zones. This faciity also allows for hardcopy generation of   
maps previewed on raster displays.  PC display systems do not have hardware     
polygon fill, so map display is slow.                                           
                                                                                
 OzGIS is based on the GKS graphics standard. The standard provides device      
independence, and the basic graphic capabilities of lines, text and fill. OzGIS 
does contain its own set of GKS-type routines which can be used to interface to 
display devices with hardware fill capabilities or to other device independent  
packages. The INTERACTOR graphics package is used for the interactive version,  
and the SCIPLOT package for hardcopy map production.                            
                                                                                
 OzGIS is a large FORTRAN program. It will run on computer systems with a       
FORTRAN 77 compiler and about a mega-byte of memory. The system is well         
structured, so by using overlays and reducing capabilities (array sizes) the    
software can be implemented in smaller memory machines. Hence OzGIS is          
reasonably portable.  The PC version is heavily overlayed to fit it into the    
artificial 640K limit imposed by the DOS operating system.                      
                                                                                
The WINDOWS version (under development) will enable extended memory to be       
used. A PC with at least 4Meg of RAM and a mouse will be required. The          
interface to the API is coded in 'C'.                                           
                                                                                
Generally the speed of the system is dependent on hardware:                     
                                                                                


                                                                       6
Processor 286 -> 386 -> 486                                                     
Disk speed                                                                      
Floating point processor                                                        
Extra memory for RAM disk                                                       
                                                                                
INTERACTOR is a graphics package produced by:                                   
                                                                                
Interactive Software Services,                                                  
25 St Michael's Close,                                                          
Penkridge,                                                                      
Stafford. ST19 5AD.                                                             
U.K.                                                                            
                                                                                
We have found INTERACTOR very good, and the support is excellent.               
                                                                                
SCIPLOT is a plotting package produced by:                                      
                                                                                
MicroGlyph Systems,                                                             
PO Box 474,                                                                     
Lexington, MA 02173,                                                            
U S A                                                                           


                                                                       7
                    2. SUMMARY                                           
                       =======
 
                                                                                
                                                                                
This chapter provides an overview of the facilities provided by the OzGIS       
suite of programs.                                                              
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
OzGIS was designed to:                                                          
                                                                                
. facilitate the interpretation of the spatial distributions of data            
. prepare maps to be output on printers and plotters                            
. assist the analysis and modelling of spatial relationships in data            
                                                                                
The system can therefore be used to analyse socio-economic data produced        
by censuses and surveys and to support management decisions associated with     
for example Government planning, marketing, sales, site and personnel           
location, advertising and natural resources.                                    
                                                                                
Products:                                                                       
                                                                                
. Zone maps displaying polygons that are filled (with colours, patterns or      
  hatching) to show the distribution of attribute data                          
. Line maps displaying lines in different line patterns to show the attribute   
  data distribution                                                             
. Site maps displaying symbols at locations where the symbol sizes show the     
  attribute data distribution                                                   
. Bivariate maps showing filled zones for two attribute files                   
. Zone and line maps showing lines overlayed on zones for two attribute files   
  Zone and site maps showing site symbols overlayed on zones for two attribute  
  files                                                                         
. Geographic maps displaying polygons, line segments, symbols or site names     
  according to feature codes but without reference to attribute files           
. Histograms showing the number of items (zones, lines or sites) assigned       
  to each class, or the number of items within value intervals (distribution)   
  or the attribute values sorted in ascending order                             
. Scatter diagram for two attributes                                            
. Map statistics                                                                
. Map reports                                                                   
                                                                                
Files:                                                                          
                                                                                
. Data files are raw Ascii data files in a variety of external formats. Standard
  GIS formats and formats from Census Bureaus and Mapping Agencies are          
  supported                                                                     
. Geographic files describe geographic data in terms of the graphic elements    
  zones, polygons,line networks, line segments, and points                      
. Attribute files contain the values of attributes (variates, statistics,       
  variables) referenced to zones, line or site names.                           
. Names files contain a list of zones, lines or sites that defines a region     
  of interest                                                                   
. Combine files define new items in terms of zones for aggregation              
. Marker files define simple shapes as polygons for display as symbols          


                                                                       8
. Saved display files contain the information to regenerate a complete map      
. Device files define the graphics devices and their capabilities; colours,     
  fonts, line types, hatching, markers etc                                      
. Parameter files contain special data for some processing.                     
. Presentation files define a series of maps for demonstrations.                
                                                                                
User Interface:                                                                 
                                                                                
. Menu / windows interface                                                      
. Help facility                                                                 
. Trace information                                                             
. File interrogation, audits, deletion                                          
. Tutorials                                                                     
                                                                                
Data processing                                                                 
                                                                                
. Subsetting of geographic files                                                
. Line segment simplification                                                   
. Joining short line segments for polygons                                      
. Amalgamation of geographic and attribute data                                 
. New attributes by arithmetic and logical expression                           
. Building zones structure from line segments                                   
. Generation of names files                                                     
. Generation of template attribute data files                                   
. Map projections                                                               
. Address matching                                                              
                                                                                
Quantisation                                                                    
                                                                                
. Classification methods: equal value, quantiles, specified intervals,          
  specified number, refined, sequential colour, mean and standard deviations,   
  nested means, natural breaks, percentiles, fixed                              
. Quantisation over value ranges                                                
. Quantisation for lists of items                                               
. Independent quantisation for one or two files                                 
                                                                                
Map regions                                                                     
                                                                                
. Display of several geographic files at the same time, joined together or      
  as multiple regions                                                           
. Windowing and viewporting for layout                                          
. Coordinate grids                                                              
. Overlays of line segments, polygons, names and symbols                        
                                                                                
Attribute selection                                                             
                                                                                
. Sequentially off attribute file                                               
. By position in file                                                           
. By description                                                                
                                                                                
Map enhancement                                                                 
                                                                                
. Specification of legend contents                                              
. Addition of text                                                              
. Addition of histograms showing distributions, sorted values or quantisation   
  results                                                                       
. Addition of scatter diagrams to bivariate maps                                
. Overlay of mean and standard deviation, median and regression curves on       


                                                                       9
  diagrams                                                                      
                                                                                
Hardcopy Map Production                                                         
                                                                                
. HP compatible plotters                                                        
. Many dot matrix printers                                                      
. Postscript laser printers                                                     
. HPGL, CGM and word processor files                                            
                                                                                
Applications                                                                    
                                                                                
. Territory assignment                                                          
. Site catchments (not available yet)                                           
                                                                                
Environment                                                                     
                                                                                
. Requires minimum of IBM PC compatible with hard disk, 640K RAM and EGA.       
. Preferred hardware is AT compatible with 512K super VGA card giving 256       
  colours at at least 640 x 480 resolution. 1Mbyte boards with Trident or       
  Tseng Labs 4000 chipsets are recommended.                                     
. MS DOS operating system                                                       
                                                                                
Under Development                                                               
                                                                                
. WINDOWS 3.1 version                                                           
. Spatial operations (polygon overlay etc)                                      
. Digitising (being ported from Vax)                                            


                                                                      10
                    3. SYSTEM CONFIGURATION                              
                       ====================
 
                                                                                
                                                                                
This chapter describes how to set up the OzGIS system and how to make the       
best use of your hardware.                                                      
                                                                                
                                                                                
                                                                                
                                                                                

  3. 1 Introduction                                      
       ------------
 
Various parameter files have to be set up correctly before the system can be    
used, as OzGIS supports a range of video boards. This should be quite straight  
forward for standard EGA and VGA boards, but as there are no standards for      
super VGA boards the procedure may get involved.                                
                                                                                
The configuration is worth spending the time on as it is very important to      
display maps as fast as possible and to use the highest display resolution      
possible. If you plan to do a lot of mapping it is worth purchasing good        
hardware (its optional).                                                        
                                                                                
Resolution is provided by using Super VGA boards.                               
                                                                                
Speed is provided by:                                                           
                                                                                
. Super VGA boards with 256 colours (512K or 1 Mbyte RAM on the board)          
. Using an extra 1MByte of RAM as a RAM disk.                                   
. Math coprocessor                                                              
. fast processors (386 / 486)                                                   
                                                                                
The other hardware worth having is a mouse. While the arrows on the keyboard    
can be used, they are slow.                                                     
                                                                                
                                                                                
FOLLOW THE INSTRUCTIONS CAREFULLY!                                              
                                                                                
                                                                                

  3. 2  DOS system files                                 
       -----------------
 
The start-up command file AUTOEXEC.BAT will have to be modified so the programs 
can be accessed by changing the path statement to reference /ozgis. e.g.        
                                                                                
PATH C:\DOS;C:\PROGS;C:\OZGIS                                                   
                                                                                
                                                                                
The system file CONFIG.SYS has to have:                                         
                                                                                
FILES=20                                                                        
BUFFERS=20                                                                      
                                                                                
These changes to the DOS system files will not take effect until the system is  


                                                                      11
re-booted.                                                                      

  3. 3  Standard EGA and VGA boards                      
       ----------------------------
 
If you have a super VGA board SKIP this section.                                
                                                                                
You need to be aware of the resolution of your video card. This is one of:      
                                                                                
350 lines of 640 pixels for EGA                                                 
480 lines of 640 pixels for VGA                                                 
                                                                                
Both boards have 16 colours.                                                    
                                                                                
You now need to check two configuration files:                                  
                                                                                
All the following take place in the \ozgis directory.                           
                                                                                
                                                                                
The file \OZGIS\OZGIS.INI is the initialisation file for the system.            
This file has to be modified using your word-processor.                         
                                                                                
The file should be well commented, and modifications should be fairly obvious.  
Ensure that you dont alter the columns used i.e. the file is not free format!   
                                                                                
The first three lines should be either:                                         
                                                                                
for the EGA board                                                               
                                                                                
       640         Number of pixels across EGA screen                           
       350         Number of lines on screen                                    
        16         Number of colours                                            
                                                                                
                                                                                
or for the VGA board                                                            
                                                                                
       640         Number of pixels across VGA screen                           
       480         Number of lines on screen                                    
        16         Number of colours                                            
                                                                                
                                                                                
                                                                                
The file \OZGIS\INTERACT.INI is the initialisation file for the interactor      
graphics package. This file has to be modified using your word-processor.       
                                                                                
The file should be well commented, and modifications should be fairly obvious.  
                                                                                
If a standard VGA card is being used, nothing may have to be changed.           
                                                                                
If an EGA card is being used the display type may have to be set via            
the DISPLAY= parameter (colours will be strange).                               
                                                                                
                                                                                


                                                                      12

  3. 4  Super VGA boards                                 
       -----------------
 
The recommended display is a super VGA board with the ability to display 256    
colours at a resolution of at least 640 X 480, as this enables maps of up to    
240 zones to be manipulated rapidly by changing the colours via the colour      
look-up table. 16 colour displays require the map polygons to be redrawn every  
time the colours change (e.g. by displaying another attribute).                 
                                                                                
Hence you should use the highest resolution available with your board and       
monitor that gives 256 colours. (this may not be true if you are mapping e.g.   
environmental data without attribute data or have maps of more than 240 zones   
when resolution may be more important).                                         
                                                                                
First determine the resolution and number of colours you want to use. This will 
depend on the amount of memory on your board and the chipset. If in doubt read  
your video board manual or ask your computer shoppe.                            
                                                                                
In order of preference the resolutions are:                                     
                                                                                
Pixels Lines Colours                                                            
                                                                                
1024   768   256         (1MByte boards)                                        
 800   600   256         (512K boards)                                          
 640   480   256         (512K boards with standard monitor)                    
 800   600    16         (256K board)                                           
                                                                                
If your board has only 256K of memory you should consider adding more memory,   
but in the meantime use the highest resolution possible for 16 colours          
                                                                                
The boards supported by the graphics package are:                               
                                                                                
    Chipset     Chipset   640x350   640x400   640x480   800x600  1024x768       
                Number                                                          
    Tseng 3000    0          y                   y         y                    
    Tseng 4000    1          y         y         y         y         y          
    Paradise      2                    y         y                              
    Video 7       3                    y         y         y                    
    Everex        4          y         y         y         y                    
    ATI           5                    y         y         y                    
    Trident       6                    y         y         y         y          
    Chips & Tech  7                    y         y         y                    
    Ahead B       8                    y         y         y                    
    Oak           9                              y         y                    
                                                                                
The precise combination of modes available on any given board varies            
according to the manufacturer and the amount of video RAM available.            
The 640x480 and 800x600 modes require 512k and the 1024x768 mode requires       
1 megabyte.                                                                     
                                                                                
                                                                                
You now need to modify two configuration files in the \ozgis directory.         
                                                                                
                                                                                
The file \OZGIS\OZGIS.INI is the initialisation file for the system.            
This file has to be modified using your word-processor.                         


                                                                      13
                                                                                
The file should be well commented, and modifications should be fairly obvious.  
                                                                                
The first three lines have to be the resolution and number of colours e.g.      
                                                                                
       800         Number of pixels across VGA screen       (640 - 1024)        
       600         Number of lines on screen                (350 - 768)         
       256         Number of colours                        (16 or 256)         
                                                                                
Ensure that you dont alter the columns used i.e. the file is not free format!   
                                                                                
                                                                                
The file \OZGIS\INTERACT.INI is the initialisation file for the interactor      
graphics package. This file has to be modified using your word-processor.       
                                                                                
The file should be well commented, and modifications should be fairly obvious.  
                                                                                
                                                                                
The display type may have to be set via the DISPLAY= parameter.                 
                                                                                
Super VGA boards require registers to be initialised. Look through the list and 
find yours. If its not there you may have to use the system as a standard VGA   
as described in the previous section, but first look in your video board manual 
to see if there is information about the registers to be used to set modes. If  
there is you may be able to set up an appropriate mode command as described     
in the following paragraphs (try it to see if it works).                        
                                                                                
All you have to do is to is enable a command that corresponds to your video card
                                                                                
                                                                                
e.g. if you have a 1Meg TSENG Labs ET4000 card you will find the following      
entry:                                                                          
                                                                                
REM mode13  = 56 0 0 0 1 1024 768 (1024x768 256-colour graphics)  C             
                                                                                
All you have to do is remove the "REM " from the front (dont forget the blank   
i.e. left align it).                                                            
                                                                                
You would normally also remove the comment too, so you end up with:             
                                                                                
mode13  = 56 0 0 0 1 1024 768  C                                                
                                                                                
(the "C" on the end is require with a mouse to tell the system to generate a    
cursor as mouse drivers normally do not do that with super VGAs).               
                                                                                
                                                                                
Try and find the corresponding entry for your board. If you are still confused  
try reading the appendix.                                                       
                                                                                
                                                                                
The OzGIS system is now configured for your super VGA board.                    

  3. 5 Maths Coprocessor                                 
       -----------------
 
If you have a maths coprocessor you can use a different version of the main     
OZGIS program.                                                                  
                                                                                


                                                                      14
You need to modify the batch files \ozgis\ozgis.bat and \ozgis\ozcensus.bat to  
use the program ozgisco instead of ozgisprg.                                    

  3. 6 Extra RAM                                         
       ---------
 
If you have more than 1 Mbyte of RAM you can speed up display of menus and      
other windows enormously by using a RAM disk.                                   
                                                                                
You put a command in your config.sys file like:                                 
                                                                                
DEVICE=C:\DOS\RAMDRIVE.SYS 1024 /E                                              
                                                                                
This then gives you a pseudo disk drive in RAM, so its very fast. The drive     
identifier is one more than you are using e.g. if you have one disk drive       
called C: then the RAM disk drive will be D:                                    
                                                                                
After you have put in the command, reboot you PC and type "DIR D:" to check     
that you got it right (see your DOS manual).                                    
                                                                                
Now modify the \ozgis\interact.ini file to define the two save files to be on   
the RAM drive. The entries should look something like:                          
                                                                                
TEMPMENU   = D:\menu.tmp                                                        
TEMPWINDOW = D:\window.tmp                                                      
                                                                                

  3. 7 Mouse                                             
       -----
 
If you have a mouse it must be installed in the standard way.                   
                                                                                
The driver must be call MOUSE.COM (for the system to detect it).                
                                                                                
Mouse drivers usually only work with standard VGA and EGA. If you are operating 
in super VGA modes you would have to set the mode command in                    
\ozgis\interact.ini with a "C" on the END (as already described) for the cursor 
to appear.                                                                      

  3. 8 Hardcopy configuration                            
       ----------------------
 
Configuration for production of hard-copy maps via OzMap is described in the    
appendix.                                                                       

  3. 9 Digitiser                                         
       ---------
 
Configuration for digitising is described in the relevant chapter               


                                                                      15
                    4. OzEnter DATA ENTRY                                
                       ==================
 
                                                                                
                                                                                
Map data are imported as data files into the OzGIS system.                      
                                                                                
This chapter shows how to use the OzEnter program.                              
                                                                                
                                                                                
                                                                                
                                                                                

  4. 1 Introduction                                      
       ------------
 
                                                                                
Most data are entered into OzGIS as external data files. Examples are Census    
data and Census digitised boundaries. These files come from Census Bureaux,     
Mapping agencies, data supply companies or your own data-base systems.          
Some data can be prepared or modified with word processors or spreadsheets.     
                                                                                
OzEnter supports data files in several formats. If your format is not supported 
you have to convert it into one of the supported formats or the OzGIS standard  
format for the type of file.                                                    
                                                                                
The files are entered into the system via the OzEnter program which checks the  
data and writes them to internal files.                                         
                                                                                
The main menu enables selection of the type of file:                            
                                                                                
INPUT GEOGRAPHIC FILES                                                          
INPUT ATTRIBUTE FILES                                                           
INPUT A NAMES FILE                                                              
INPUT A COMBINE FILE                                                            
INPUT A DEVICE FILE                                                             
INPUT A MARKER FILE                                                             
                                                                                
Choosing a menu item may generate another menu e.g. for GEOGRAPHIC FILES        
                                                                                
INPUT A STANDARD FORMAT GEOGRAPHIC FILE                                         
INPUT NEW FORMAT SAS GEOGRAPHIC FILE                                            
INPUT OLD FORMAT SAS GEOGRAPHIC FILE                                            
INPUT A DLG-3 OPTIONAL FORMAT GEOGRAPHIC FILE                                   
INPUT A GINA FORMAT GEOGRAPHIC FILE                                             
INPUT A TIGER FORMAT GEOGRAPHIC FILE                                            
INPUT A DIME FORMAT GEOGRAPHIC FILE                                             
INPUT A DXF FORMAT GEOGRAPHIC FILE                                              
    .                                                                           
    .                                                                           
    .                                                                           
    .                                                                           
                                                                                
where DLG-3, TIGER, DXF etc are different data formats.                         
                                                                                
                                                                                
In all cases, data entry requires giving the name of your data file and         


                                                                      16
supplying the name to be used for the internal file.                            
                                                                                
                                                                                
Data files usually have names that finish with the extension DAT.               
e.g. LONDON.DAT, A:SALES.DAT.                                                   
                                                                                
The one time a full file name can be given within OzGIS is when reading a data  
file, as it is sometimes inconvenient to rename files (but typing L for a list  
of files will only list those with extension .DAT). For example you may have    
TIGER files from the US Census bureau on CD-ROM. Then you could read the files  
directly by giving the complete file name e.g. E:/18/003/TGR18003.F42           
                                                                                
Often data files will need further processing by the OzData program before used 
for mapping e.g. attribute data may need manipulating by arithmetic expressions 
or geographic line segments may need thinning and forming into polygons.        
                                                                                
Future versions of the OzGIS system may have incompatible internal file formats 
so always keep important data files.                                            
                                                                                
The system comes with many of the system files already entered e.g. device      
files. The data files are also provided.                                        

  4. 2 Example of data entry                             
       ---------------------
 
You will often have a file of attribute data (such as population Census         
data) and a file of digitised boundary data for mapping (e.g. TIGER):           
                                                                                
We will look at data for Australia. There are two data files:                   
                                                                                
OZ-G.DAT are the digitised boundary data, (Australian Statistical Divisions)    
OZ-A.DAT are the attribute data                                                 
                                                                                
to run the OzEnter program type:                                                
                                                                                
cd \ozdemo                                                                      
ozenter                                                                         
                                                                                
A menu will appear like:                                                        
                                                                                
1 TUTORIALS & SYSTEM INFORMATION                                                
2 INPUT GEOGRAPHIC FILES                                                        
3 INPUT ATTRIBUTE FILES                                                         
4 INPUT A NAMES FILE                                                            
5 INPUT A COMBINE FILE                                                          
6 INPUT A DEVICE FILE                                                           
7 INPUT A MARKER FILE                                                           
                                                                                
You select the options by moving up and down with the arrows and pressing Enter 
or by typing the number.                                                        
                                                                                
The system trace is usually turned on so messages will appear on the screen     
during processing.                                                              
                                                                                
                                                                                
                                                                                
First enter the digitised boundary data:                                        
---------------------------------------                                         


                                                                      17
                                                                                
                                                                                
Select the option to INPUT GEOGRAPHIC FILES                                     
                                                                                
The next menu appears:                                                          
                                                                                
1 INPUT A STANDARD FORMAT GEOGRAPHIC FILE                                       
2 INPUT NEW FORMAT SAS GEOGRAPHIC FILE                                          
3 INPUT OLD FORMAT SAS GEOGRAPHIC FILE                                          
4 INPUT A DLG-3 OPTIONAL FORMAT GEOGRAPHIC FILE                                 
5 INPUT A GINA FORMAT GEOGRAPHIC FILE                                           
6 INPUT A TIGER FORMAT GEOGRAPHIC FILE                                          
7 INPUT A DIME FORMAT GEOGRAPHIC FILE                                           
8 INPUT A DXF FORMAT GEOGRAPHIC FILE                                            
9 INPUT AUSLIG SEGMENTS FORMAT CENSUS BOUNDARY FILE                             
                                                                                
This enables geographic data to be read in in a variety of "standard" formats.  
                                                                                
The test data is in the OzGIS standard format so choose                         
INPUT A STANDARD FORMAT GEOGRAPHIC FILE                                         
                                                                                
A  data input window now appears for you to specify a file name. You type in    
what you want and then type enter:                                              
                                                                                
give the input data file as OZ-G                                                
give the output geographic file as OZ                                           
                                                                                
The data file will be processed, and a standard geographic file created.        
                                                                                
The trace message at the bottom of the screen describes what is going on.       
                                                                                
Now type Esc to go back to the first menu.                                      
                                                                                
                                                                                
                                                                                
Now enter the attribute data:                                                   
-----------------------------                                                   
                                                                                
select the option to INPUT ATTRIBUTE FILES                                      
                                                                                
A new menu appears:                                                             
                                                                                
1 INPUT A STANDARD FORMAT ATTRIBUTE FILE                                        
2 INPUT A LOTUS 1-2-3 FORMAT ATTRIBUTE FILE                                     
3 INPUT A DATABASE (SIMPLE) FORMAT ATTRIBUTE FILE                               
4 INPUT A LAMM FORMAT ATTRIBUTE FILE                                            
5 INPUT USA CENSUS STF 1A FILES FOR TRACT/BNA                                   
6 INPUT USA CENSUS STF 1A FILES FOR BLOCK GROUPS                                
7 INPUT ATLAS DATA FILES                                                        
                                                                                
The data are in standard form so:                                               
                                                                                
Select INPUT A STANDARD FORMAT ATTRIBUTE FILE                                   
                                                                                
give the input data file as OZ-A                                                
give the output attribute file as OZ                                            
                                                                                
3. The data files are now entered so -                                          


                                                                      18
                                                                                
type F10 to exit                                                                
                                                                                
                                                                                
If you type DIR "OZ.*" you will find that there are two new files there:        
                                                                                
OZ.ATT is the attribute file and                                                
OZ.GEO is the geographic file.                                                  
                                                                                
You (almost) never give a full file name within OzGIS - the system appends      
a file extension to the name according to the file type.                        
                                                                                

  4. 3 Demonstration Files                               
       -------------------
 
The OzGIS system is supplied with a complete set of sample external             
data files so that the user can become familiar with the system.  These         
files can be inspected to clarify the file formats.                             
                                                                                
The files are usually in the directory \OZDEMO                                  

  4. 4 Example geographic and attribute data             
       -------------------------------------
 
Generally there will be two data files for each map; a file that describes the  
map boundaries and another for attribute data. The example files are:           
                                                                                
1. Far East Asia                                                                
                                                                                
Attribute file - FEA-A                                                          
Geographic file- FEA-G                                                          
                                                                                
                                                                                
2. Lowe electorate (Sydney)                                                     
                                                                                
Attribute files- LOWE-A1 and LOWE-A2                                            
Geographic files- LOWE-G (zones), LOWE-S1, LOWE-S2 (sites)                      
                                                                                
These files are already entered (supplied with the system).                     
                                                                                
3. Australia                                                                    
                                                                                
Attribute file - OZ-A                                                           
Geographic file- OZ-G                                                           
                                                                                
These files have already been input in the demonstration chapter.               
                                                                                
                                                                                
Other files may also be supplied:                                               
                                                                                
Washington DC Census Tract/BNA and TIGER lines                                  
                                                                                
Africa in Atlas format                                                          
                                                                                
Hawaii in DLG-3 optional format                                                 


                                                                      19

  4. 5 Example device files                              
       --------------------
 
The characteristics of devices and the appearance of maps are given by display  
files. Data files are provided for all the device files supplied with the       
system. There are two sets for 16 and 256 colour video boards, and also sets    
for hatching and colour simulation on plotters etc.                             
                                                                                
Files are already entered on the system and have already been used.             

  4. 6 Marker data files                                 
       -----------------
 
These have already been entered, and are supplied with the system. They are     
circle, diamond, hbar, nabla, plus, square, triangle, vbar. (You can of course  
have your own markers).                                                         
                                                                                

  4. 7 Colour names data (no longer used)                
       ----------------------------------
 
This option has been removed as DOS limits were being exceeded.                 
                                                                                
A colour names file X11-BGR.DAT is supplied and is useful for colour definition.
                                                                                


                                                                      20
                    5. BASIC CHOROPLETH MAPPING EXAMPLE                  
                       ================================
 
                                                                                
                                                                                
This chapter gives an introduction to the map display programs.                 
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                

  5. 1 OzCensus                                          
       --------
 
The main display and analysis program is OzGIS.                                 
                                                                                
A much simpler version of OzGIS is provided called OzCensus.                    
                                                                                
This version is suitable for simple mapping of Census type data and is          
recommended for use while learning to use the system.                           
                                                                                
OzCensus has two or three menus and about twenty menu options while the full    
OzGIS version has about fifty menus and a few hundred menu options.             
                                                                                
When you want to do more advanced mapping use OzGIS!                            

  5. 2 Example Choropleth Map                            
       ----------------------
 
The most common application is the display of data such as Census data as       
coloured polygons. Here the processes necessary to display such data are        
described.                                                                      
                                                                                
Census data enables you to display maps that show where people live who         
are of different nationalities, ages, income groups etc. These maps are         
used for applications such as retail marketing to find where potential          
customers are located or for government planning to decide where to build       
facilities like schools.                                                        
                                                                                
You will probably have a file of attribute data (such as population Census      
data) and a file of digitised boundary data for mapping (e.g. TIGER):           
                                                                                
We will look at the data data for Australia. There are two data files:          
                                                                                
OZ-G.DAT are the digitised boundary data, (Australian Statistical Divisions)    
OZ-A.DAT are the attribute data                                                 
                                                                                
An example of entering these data files with the OzEnter program has been       
given in the last chapter.                                                      
                                                                                
Both the attribute file and geographic file are called OZ. Different types of   
files can have the same name.                                                   
                                                                                
                                                                                
                                                                                
To start the Census mapping program type:                                       


                                                                      21
                                                                                
cd \ozdemo                                                                      
ozcensus                                                                        
                                                                                
The first menu appears:                                                         
                                                                                
1 TUTORIALS & SYSTEM INFORMATION                                                
2 DISPLAY A NEW MAP                                                             
                                                                                
                                                                                
choose the option to "DISPLAY A NEW MAP".                                       
                                                                                
give the attribute file name as OZ.                                             
                                                                                
When asked for the geographic file name input "L". A list of the available files
will appear (type Enter or Esc to exit). Give the geographic file name as OZ.   
                                                                                
The data are now processed, the map is displayed, and the next menu appears.    
                                                                                
You now have a default map with legend and distribution diagram. The legend     
has the numbers of zones in each class on the left and the class value ranges   
to the right of the coloured boxes.                                             
                                                                                
The new menu is:                                                                
                                                                                
1 TUTORIALS & SYSTEM INFORMATION                                                
2 DISPLAY A NEW MAP                                                             
3 ADD TEXT TO MAP                                                               
4 DISPLAY THE NEXT SEQUENTIAL ATTRIBUTE                                         
5 SELECT AN ATTRIBUTE FOR DISPLAY BY NUMBER                                     
6 CHANGE THE NUMBER OF CLASSES                                                  
7 CHANGE THE QUANTISATION METHOD                                                
8 DISPLAY ATTRIBUTE STATISTICS                                                  
9 LIST ZONES SELECTED WITH BOX-CURSOR                                           
0 SAVE DISPLAY FOR HARDCOPY MAP GENERATION WITH OzMap                           
                                                                                
                                                                                
Now investigate some of the options:                                            
                                                                                
Choose the option to DISPLAY THE NEXT SEQUENTIAL ATTRIBUTE                      
                                                                                
If you only have 16 colours the system does not display the map until you       
request regeneration. This enables several options to be changed before the     
slow polygon drawing takes place.                                               
                                                                                
If the map does not change type F3 to regenerate the map.                       
                                                                                
                                                                                
Select the option to SELECT AN ATTRIBUTE FOR DISPLAY BY NUMBER.                 
Type 0 to get a list.                                                           
                                                                                
A list of the attribes available will appear in a window.                       
                                                                                
Type Esc to return to the question. Type in a number to select an attribute.    
(type F3 to regenerate if necessary)                                            
                                                                                
                                                                                
Now investigate some of the function keys:                                      


                                                                      22
                                                                                
(You should print the file FNKEYS.DOC for a template.)                          
                                                                                
Type F1 to get a help message. Esc is usually used to return.                   
                                                                                
F2 hides the menu; type Esc to redisplay it.                                    
                                                                                
F3 regenerates the map when required                                            
                                                                                
F4 enables files to be audited and maintained. Type F4 and select the option to 
interrogate files. Select geographic files and use the file name OZ (the one    
displayed). Type Esc three times to return to main menu (Esc is used to return  
to the previous menu).                                                          
                                                                                
F6 enables the user interaction to be controlled; try turning on partial trace  
(level 1) which causes a series of messages to appear at the bottom of the      
screen telling you what the system is doing, but not as many as level 2.        
The initial trace levels for all programs are set in the \ozgis\ozgis.ini file. 
                                                                                
F8 causes a jump back to the previous main menu. This enables skipping back     
several levels. You will find that at main menus this is the only way to exit.  
(Irrelevant with the tiny number of menus in OzCensus).                         
                                                                                
F10 is used to exit from the program. Dont use it yet!                          
                                                                                
Back at the main menu, select CHANGE THE NUMBER OF CLASSES.                     
                                                                                
change the number of classes to 10.                                             
(type F3 to regenerate if necessary)                                            
                                                                                
Select the option to CHANGE THE QUANTISATION METHOD.                            
                                                                                
Another menu will appear.                                                       
                                                                                
QUANTISATION TUTORIAL                                                           
USE EQUAL VALUE INTERVALS                                                       
USE QUANTILES                                                                   
USE SELECTED CLASS INTERVALS                                                    
USE SELECTED NUMBER OF ZONES PER CLASS                                          
USE REFINED EQUAL VALUE INTERVALS                                               
USE PSEUDO CONTINUOUS-COLOUR                                                    
USE THE MEAN AND STD DEVIATION METHOD                                           
USE THE NESTED MEANS METHOD                                                     
USE THE NATURAL BREAKS METHOD                                                   
USE SELECTED PERCENTILES                                                        
USE SELECTED CLASS RANGE PERCENTILES                                            
USE INTERACTIVE SELECTION OF CLASS INTERVAL,                                    
USE EQUIVALENCE CLASSES                                                         
USE CURRENT CLASS RANGES                                                        
USE CURRENT NO PER CLASS                                                        
                                                                                
These options are very important as they enable the map to show the data in a   
way relevant to the purpose of the analysis.                                    
                                                                                
For example, to select deciles:                                                 
                                                                                
Choose USE QUANTILES and set the number of classes to 10. The legend            
will now describe the 10 colours in the map. (Type F3 to display)               


                                                                      23
                                                                                
Type Esc to go back to the main menu.                                           
                                                                                
Choose the option to DISPLAY ATTRIBUTE STATISTICS.                              
                                                                                
Basic statistics will be displayed in a window for the displayed map.           
                                                                                
Type return (or Esc) to remove the window.                                      
                                                                                
Choose the option to LIST ZONES SELECTED WITH BOX-CURSOR.                       
This will enable the current values for the displayed zones to be listed.       
                                                                                
A cursor will appear on the screen which indicates the bottom left position.    
Place it using either the arrows (type Enter to select the position) or the     
mouse (left button to select). A box cursor then appears to select the other    
corner. All zones are listed that have a minimum bounding rectangle (MBR)       
                                                                                
that intersects the selected window.                                            
                                                                                
                                                                                
Type F10 to exit.                                                               

  5. 3 Summary                                           
       -------
 
You now have seen simple examples of the processes to produce maps.             
                                                                                
1. you obtain your data as files in a standard format.                          
                                                                                
2. you usually set up a directory on the same disk as \OZGIS and put the data   
files there.                                                                    
                                                                                
3. You use the OzEnter program to input the files.                              
                                                                                
4. You use either OzCensus or OzGIS to display the data.                        
                                                                                
But ......... this is very simple                                               
                                                                                
You may want to use OzData to do some data preparation before mapping.          
                                                                                
You may have geographic data as line segments and need to use OzZone to         
form the polygons.                                                              
                                                                                
You may want to display other types of maps or diagrams with OzGIS.             
                                                                                
You may want to output prepared maps to a printer, plotter or file with OzMap.  
                                                                                
and so on.                                                                      
                                                                                


                                                                      24
                    6. INTERACTIVE USER INTERFACE TO OzGIS               
                       ===================================
 
                                                                                
                                                                                
The user controls OzGIS by responding to menus, questions and                   
commands presented on the PC screen.                                            
                                                                                
This chapter describes these forms of user communication.                       
                                                                                
                                                                                
                                                                                

  6. 1 Menus                                             
       -----
 

  6. 1. 1 Menu format                                       
          -----------
 
      Menus are presented in the format below.  The MENU HEADER                 
contains the previous menu item selected, or in the case of a main menu         
the system title.                                                               
                                                                                
               [MENU HEADER]                                                    
                1:  [menu item 1]                                               
                2:  [menu item 2]                                               
                         :                                                      
                         :                                                      
                         :                                                      
                n:  [menu item n]                                               
                                                                                
Menu items are numbered sequentially from one.  A selection is made by typing in
the character next to the item. Alternatively the arrows can be used to move up 
or down and Enter typed to select.                                              
                                                                                
You will find that some programs (e.g. OzGIS) have lots of menus, and it is     
difficult at first to know where you are in the menu "tree". To make it more    
confusing the menus are dynamic e.g. adding something to a map can cause a new  
menu iten to appear that allows you to delete that item.                        
                                                                                
The general approach is: if the current menu does not have the option you want  
type Esc to go back to the previous menu and so on.                             
                                                                                
                                                                                

  6. 1. 2 Function keys                                     
          -------------
 
      User interaction is provided at every menu by typing function keys:       
                                                                                
      (print out \ozgis\fnkeys.doc for a template)                              
                                                                                
                                                                                
      F1    presents "help" or informative messages about the menu items        
            and describes the effect of selection of the items                  
                                                                                


                                                                      25
      F2    enables the menu to be removed so it does not obscure the display.  
            Esc will display it again.                                          
                                                                                
      F3    regenerates the map after parameters have changed. Enter must be    
            typed to display the next menu.                                     
                                                                                
      F4    permits interrogation and maintenance of OzGIS files.               
            A menu is presented with the following options:                     
                                                                                
               -  delete a file                                                 
               -  interrogate the header of a file                              
               -  generate a list of files.                                     
                                                                                
      F6    permits the extent of user communication to be controlled.          
            A menu with the following options is presented:                     
                                                                                
               -  turn user assistance messages on/off                          
               -  turn trace messages from tasks on/off                         
               -  turn the bell to signal cursor operation on/off               
               -  turn on debug (useful for reporting errors)                   
                                                                                
            The default of the option for user assistance messages is "on"      
            (i.e., that the messages are displayed).                            
            The default of the option for trace messages depends on the module. 
            (it is useful for data entry and preparation)                       
            The debug option is for system testing, but may be useful to trace  
            faulty data problems. Output goes to the print file OZGIS.OUT       
                                                                                
      F8    exits from the current menu to the last major menu, which           
            depends on the stage of processing.                                 
                                                                                
      F10   quit the OzGIS session.                                             
                                                                                
Pressing the "Esc" key before entering any other character has one of           
two effects:                                                                    
                                                                                
      -  return to the previous menu                                            
or    -  repeat of the current menu ("F8" should be typed to return to the      
previous main menu)                                                             
The option taken depends upon the stage of processing.                          

  6. 1. 3 Stacking selections                               
          -------------------
 
Menus take quite a time to display as the underlying graphics has to be stored  
first. A series of selections can be made when the sequence of menu options is  
known, and the menus will not appear.                                           

  6. 2 Questions                                         
       ---------
 
      Questions are asked by OzGIS when data are required for an                
operation.  The user must supply the data by entering appropriate responses     
on the keyboard.                                                                
                                                                                
      The format of questions consists of the question, a possible range of     
values in brackets (if appropriate), a default value in parentheses (if         
appropriate) and terminated by a question mark.  The range of values and        


                                                                      26
default values indicate the form of the expected answer.  An example is:        
                                                                                
      -  request to replace an existing file:                                   
         DO YOU WANT TO REPLACE THE FILE [Y,N]?                                 
                                                                                
                                                                                
         The user must respond by typing either "Y" (for "YES") or "N"          
         (for "NO").                                                            
                                                                                
      The following single character responses provide assistance when          
answering questions:                                                            
                                                                                
      "H":  presents a "help" or informative message about the required         
            response.                                                           
                                                                                
      "E":  returns to the previous menu without further action.                
                                                                                
                                                                                
      Errors in responses are trapped and result in help messages being         
printed.  The user is asked the question again.                                 

  6. 3 Commands                                          
       --------
 
      Commands are issued by OzGIS when an operation has to be                  
performed by the user.  When the operation is completed, control returns to     
the appropriate menu.                                                           
                                                                                
      The format for commands consists of a directive, a possible range of      
values in brackets (if appropriate), a default value in the input field (if     
appropriate), terminated by a colon.  Examples are:                             
                                                                                
      -  to provide the number of classes:                                      
         TYPE NUMBER OF CLASSES [1-6] (4):                                      
                                                                                
         The number of classes must be in the range 1 to 6, and if              
         the user simply presses the "Enter" key a default value of 4 will      
         be selected.                                                           
                                                                                
      -  request for the name of a file:                                        
         TYPE FILENAME (TEST):                                                  
                                                                                
         The filename must be entered as a character string, or the             
         "Enter" key pressed to accept the default filename "TEST".             
                                                                                
      The following single character responses provide assistance when          
responding to commands:                                                         
                                                                                
      "L":  provides a list of data items that can be selected.                 
                                                                                
            e.g. for FILENAME, a list of available files will be printed.       
            e.g. for ATTRIBUTE DESCRIPTION, the names of attributes on the file 
            will be listed.                                                     
                                                                                
      "H":  presents a help or informative message about the desired            
            operation.                                                          
                                                                                
                                                                                


                                                                      27
      "E":  returns to the previous menu without further action.                
                                                                                
Errors in responses are trapped and cause a help message to be printed and      
the command to be repeated.                                                     

  6. 4 Graphic interaction                               
       -------------------
 
      Graphic interaction in OzGIS involves the use of the mouse and/or         
arrow keys to control the cursors on the monitor.                               
Use the left mouse button or type Enter to select the position.                 
                                                                                
      The user is directed to operate the mouse etc by the appearance of the    
cursor on the monitor and by an appropriate command on the screen.  The         
extent of the command depends on the current level of user communication        
(see F6  option)                                                                
                                                                                
There are two types of cursors:                                                 
                                                                                
1. a pointer to select a position of object                                     
2. a box to select a region. The bottom left corner is selected and then the    
   other.                                                                       

  6. 5 Pop-up                                            
       ------
 
The menus and windows operate in "pop-up" mode. This requires that the screen   
under the menu etc has to be saved to file before the menu appears so it can be 
restored. This is slow. Display speed can be increased by specifying the save   
files to be on RAM disk (if you have extended memory) by modifying the file     
name in the \ozgis\interact.ini file.                                           

  6. 6  Print file                                       
       -----------
 
Every program generates printout on a file OZGIS.OUT.                           
                                                                                
This includes:                                                                  
                                                                                
Reports                                                                         
Error messages                                                                  
Debug output                                                                    


                                                                      28
                    7. OzGIS FILES                                       
                       ===========
 
                                                                                
                                                                                
This Chapter describes the various files which are processed by                 
OzGIS.  Some of the files can be entered into OzGIS as data, and                
the external formats for these files are given later.  All of the               
files have internal formats, which are generated as part of the user            
interaction.                                                                    
                                                                                
                                                                                
                                                                                

  7. 1 File Origins                                      
       ------------
 
Data files usually come from Census bureaux, map data suppliers or your         
corporate database.                                                             
                                                                                
The file types will become obvious with use of the system.                      
                                                                                
External data files must be entered into OzGIS explicitly.  This                
operation permits OzGIS to generate internal representations of the             
data for efficient processing and to check the data.                            
                                                                                
The following kinds of files must be entered into OzGIS with                    
the OzEnter program:                                                            
                                                                                
      -  marker files                                                           
      -  device files                                                           
      -  presentation files                                                     
                                                                                
Certain files must be prepared explicitly within OzGIS under user               
direction.  These files are:                                                    
                                                                                
      -  saved display files                                                    
      -  catchment files (OzCatch)                                              
      -  time lapse files  (no longer available)                                
      -  palette files (no longer available)                                    
      -  hardcopy files  (no longer available)                                  
                                                                                
Some files can be prepared externally or internally.  These are:                
                                                                                
      -  geographic files                                                       
      -  name files                                                             
      -  combine files                                                          
      -  colour names file  (no longer available)                               
                                                                                
Some files are usually prepared with a word-processor.  These are:              
                                                                                
      -  presentation files                                                     
      -  parameter files                                                        
                                                                                


                                                                      29

  7. 2 File types                                        
       ----------
 
                                                                                
There are many different types of files used:                                   
                                                                                
(a)  Geographic Map files describe geographic (map) data in terms of            
     graphic elements - zones, polygons, line networks, line segments and       
     points.  The data can be drawn in geographic regions, or overlayed on      
     displayed maps.                                                            
                                                                                
     The files are generated by digitising base maps.  This is a                
     time-consuming soul-destroying task.  Fortunately digitised map data       
     are available for many commonly used maps e.g. states, postcodes,Census    
     districts.  Where special zones are required, they can often be            
     defined in terms of Census districts and the map boundaries obtained       
     by amalgamating the digitised Census boundary data (dropping internal      
     lines).  This has the additional advantage that Census data can also       
     be extracted for the amalgamated zones and used for comparisons with       
     the user's own attribute data.                                             
                                                                                
(b)  Attribute files contain the values of attributes (variates,                
     statistics, variables) referenced to zone, line or site names.  Each       
     file may contain a number of attributes for a fixed set of names.          
                                                                                
     Attribute files are processed to assign a class number to zones            
     (colour) or lines (line type) or sites (symbol sizes) in a displayed       
     map.                                                                       
                                                                                
     Attribute data files are usually generated via a standard database or      
     modelling system or by a user's own programs.                              
                                                                                
(c)  Names files contain a list of zones, lines or sites that defines a         
     geographic region of interest.  The files may be used to subset            
     geographic data.  It may also be used to restrict the set of               
     attributes to be quantised for a map, or alternatively the set of          
     zones lines or sites to be displayed on a map.                             
                                                                                
(d)  Combine files - define new items in terms of zones.  A file may define     
     new zones in terms of amalgamated base map zones or the influence of       
     surrounding zones on a site.                                               
                                                                                
     The file contains a list of names of the new zones or sites defined.       
                                                                                
     For each new item there is a list of the base map zones it is defined      
     by and a list of weights.                                                  
     New zones are defined by complete base map zones so the weights have       
     value 1.0 e.g. Sales Territories. Site Catchments are used to retrieve     
     data from underlying map zones so the weights give the proportions of      
     the zones (range 0-1).                                                     
                                                                                
(e)  Marker files - define simple shapes as single polygons for display as      
     markers.                                                                   
                                                                                
     The data are simply the (X,Y) points that are used to draw the             
     polygons.  The points are in the range -0.5 to +0.5 so the polygon can     


                                                                      30
     be easily scaled and displayed centred at a location.                      
                                                                                
(f)  Saved Display files contain the data to regenerate a complete display.     
     These files should be stored by the user upon completion of a display      
     for later recall.  Subsequent manipulation of the display is possible      
     after recall.                                                              
     There are two modes. The screen is usually saved so the map can be rapidly 
     displayed, but this is not relevant for later regeneration on plotters     
     etc.                                                                       
                                                                                
     Saved display files are the common level of storage and retrieval of       
     maps.  A user may build up a set of commonly displayed maps with all       
     the desired features that can be displayed and modified rapidly.           
     Saved display files are also used for presentations.                       
                                                                                
(g)  Presentation files contain references to a number of Saved Display         
     files.  The files are used to present a set of displays quickly,           
     usually for demonstration purposes.                                        
                                                                                
(h)  Time Lapse files contain a set of attributes for display as a time         
     lapse sequence.  All attributes are quantized in the same way by           
     OzGIS and must exist on the same file. e.g. data that has been             
     collected regularly, say weekly, can be displayed as a 'movie' to see      
     if there are any time-based spatial features.                              
     The format of the files is internal to OzGIS.  These facilities            
     are only available for colour display systems with large numbers of        
     colours.                                                                   
     (no longer available as PC hardware is inadequate)                         
                                                                                
(i)  Device files - define the graphic devices and their capabilities.          
     Each device is a GKS workstation.  Several files may exist for each        
     device giving different values for the graphic primitive attributes        
     (line type, text, colours, patterns etc.).  In particular, each file       
     contains sets of fill colours or patterns for single and bivariate         
     maps.                                                                      
                                                                                
                                                                                
(j)  Palette files contain a set of colours which can be selected for           
     display.  The set of colours is displayed as a palette during the          
     colour selection process.  Colour palette files can be modified and        
     generated by user interaction, but their format is internal to             
     OzGIS.                                                                     
     (no longer available)                                                      
                                                                                
(k)  Colour Names files contain a set of colour names and associated blue,      
     green and red (B,G,R) values for the display system.  The files enable     
     users to specify colours by typing a name (e.g. LIGHT RED) on the          
     keyboard.  Colour names files can be entered as external data files or     
     can be prepared by entering names and indicating the corresponding         
     colours.                                                                   
     (no longer available)                                                      
                                                                                
(l)  Hardcopy files - contain information to enable maps to be reproduced       
     off-line on other devices (with the vector program)                        
                                                                                
(m)  Parameter files - contain data for special operations e.g. entry of        
     US Census STF1A files, address matching. These files often come from       
     other systems.                                                             


                                                                      31
                                                                                
(n)  Catchment files - contain definitions of sites, boundaries of              
     catchments around sites, and catchment weights.  Catchment files are       
     interactively generated with reference to a base map.                      
     (not ported from the VAX)                                                  

  7. 3 File Names                                        
       ----------
 
OzGIS distinguishes the various types of files, so you can give the same name   
to files of different types e.g. you may have a geographic file called AFRICA   
and also a (probably related) attribute file called AFRICA and you may save the 
map using these files in a saved display file also called AFRICA.               
                                                                                
The system differentiates between files by adding an extension to the given     
file name e.g. the AFRICA attribute file would actually be AFRICA.ATT           
                                                                                
You generally dont have to worry too much about extensions, but they are:       
                                                                                
.ATT  attribute files                                                           
.CMB  combine files                                                             
.DAT  data files                                                                
.DEV  device files                                                              
.GEO  geographic files                                                          
.HRD  hardcopy files                                                            
.MRK  marker files                                                              
.PRM  parameter files                                                           
.PRS  presentation files                                                        
.SAV  saved display files                                                       
.SCR  screen dump for saved display files                                       
.TMP  temporary scratch files                                                   
                                                                                
The system just adds the extension on the end of the file name you give, so you 
can put any path on the front e.g. an input attribute file could be given as    
D:\TEST\AFRICA which the system translates to D:\TEST\AFRICA.ATT                
                                                                                
There is actually two exceptions - because data files are often obtained from   
elsewhere and you may want to input them directly off floppy disk or CD-ROM     
(where files cannot be renamed) you can give a full file name when specifying   
input data files in OzEnter. Similarly, parameter files often come from other   
systems with naming conventions, so a full file name can be given.              
                                                                                

  7. 4 Directories                                       
       -----------
 
There are two types of files, system and user.                                  
                                                                                
System files are held in the \OZGIS directory and can be specified as input     
files by putting '*' on the front of the file name.                             
                                                                                
For example, giving a device file as *C16SV3 is the same as giving it           
as \OZGIS\C16SV3                                                                
                                                                                
                                                                                
User files can be in any directory but it                                       
                                                                                
MUST BE ON THE SAME DISK AS \OZGIS !!!                                          


                                                                      32
                                                                                
Hence the \OZDEMO directory is set up on the same drive as \OZGIS               
                                                                                
The usual procedure when starting a mapping project is to set up a new          
directory, copy all data files to that directory and then use all the           
OzGIS programs in that directory.                                               
                                                                                
                                                                                


                                                                      33
                    8. DEVICE FILES                                      
                       ============
 
                                                                                
                                                                                
This chapter describes device files. It is very important to use a correct      
file for the number of colours of your EGA/VGA video card.                      
                                                                                
                                                                                
                                                                                
                                                                                
Device files control the appearance of maps:                                    
                                                                                
     . polygon colours and type of fill                                         
     . text colours, sizes and fonts                                            
     . line colours and styles                                                  
     . sequences of class colours or hatch patterns                             
     . menu and message colours                                                 
                                                                                
Experience showed that it is better to have fixed sets of definitions rather    
than allow the user to specify the display parameters.                          
                                                                                
Remember that the basic display definition (number of pixels, lines and colours)
was specified when configuring the system.                                      
                                                                                
There are sets of device files available:                                       
                                                                                
     . 16 or 256 colour sets                                                    
     . sets for standard maps and for bivariate maps                            
     . coloured polygon fill or hatching or colour simulation                   
                                                                                
The supplied files have a naming system e.g.                                    
                                                                                
      *C16SV5  is a 16 colour single variate device file                        
      *B256BV2 is a 256 colour bivariate device file                            
                                                                                
                                                                                
                                                                                
The best way to understand device files is to look at the contents, for         
example:                                                                        
                                                                                
First of all to run the OzGIS program type:                                     
                                                                                
cd \ozdemo                                                                      
ozgis                                                                           
                                                                                
Select the option to CHANGE DEVICE FILE                                         
                                                                                
Type "L" to get a list of the device files that are available.                  
                                                                                
First look at a 16 colour device file                                           
--------------------------------------                                          
                                                                                
Give the file as *C16SV1                                                        
                                                                                
Select the option to DISPLAY DEVICE CHARACTERISTICS                             
                                                                                


                                                                      34
You will now get a display that shows the text types (sizes and colours),       
lines (types and colours) and the various polygon fills as rectangles.          
                                                                                
Of particular interest are the class colours. The bottom set is a sequence of   
121 colours which is designed to give the appearance of increasing attribute    
values. In this device file for a 16 colour board the colours are in blocks,    
but for 256 colour boards all the colours will be different (and can be used    
for "continuous colour" maps). The set of colours above are a 7 x 7 set for     
bivariate maps. They actually map onto the same set as for single variate maps, 
so if bivariate maps are to be produced different device files should be used.  
                                                                                
Next a 16 colour bivariate file                                                 
-------------------------------                                                 
                                                                                
Now choose a bivariate device file *C16BV1 and display that. The bivariate      
sequence will show a progression of colour in each dimension.                   
                                                                                
There is a set of files for 16 colour displays, *C16SV1 to *C16SV9 for single   
variate maps, and *C16BV1 to *C16BV3 for bivariate maps.                        
                                                                                
Next 256 colour files (super VGA only)                                          
--------------------------------------                                          
                                                                                
There is also a set of files *C256SV1 to *C256SV9 and *C256BV1 to *C256BV3 for  
256 colour boards. If you have a suitable board display one of these. The       
colour sequence will now be the complete 121 colours.                           
                                                                                
Next hardcopy device files                                                      
-------------------                                                             
                                                                                
Other device files are also available, primarily for display on printers and    
plotters, but these can also be used on the display; try them!                  
                                                                                
*HATCHSV1 is for display of hatched single variate maps and *HATCHBV1 for       
bivariate maps.                                                                 
                                                                                
There is also a series of files CSIMSV1 ......, CSIMBV1... that were designed   
to simulate colours sequences on plotters.                                      
                                                                                
                                                                                
DEFAULT.DEV default device file                                                 
-------------------------------                                                 
                                                                                
You should now display a few of the single variate device files (*C16sv? or     
*C256SV?) and decide on one that you will use as the default device file.       
                                                                                
When you have decided on the default file type F10 to exit from OzGIS and:      
                                                                                
cd \ozgis                                                                       
copy C256SV6.DEV DEFAULT.DEV  (using the file you have chosen)                  
                                                                                
This will overwrite the device file that was supplied as the default with the   
system. Obviously you can select a different device file for display at         
any time, and you should do so for bivariate maps.                              
                                                                                
Colour sequences                                                                
----------------                                                                
                                                                                


                                                                      35
The colour sequences are designed to provide a colour progression that can      
help interpret the pregression in values in the attribute data.                 
                                                                                
The sequences were generated by sampling at equal intervals along curves        
through uniform colour space, and then transforming the values using a          
model for the colour response of colour / TV monitors.                          


                                                                      36
                    9. OzGIS MAP TYPES                                   
                       ===============
 
                                                                                
                                                                                
This chapter introduces  the various types of maps and diagrams that can be     
displayed by the OzGIS program.                                                 
                                                                                
                                                                                
                                                                                

  9. 1 Map Types                                         
       ---------
 
Several types of maps and diagrams can be displayed with OzGIS.                 
                                                                                
When you start the OzGIS program the first menu enables you to select the type  
of map or diagram that is required:                                             
                                                                                
DISPLAY ZONES FOR AN ATTRIBUTE FILE                                             
DISPLAY LINES FOR AN ATTRIBUTE FILE                                             
DISPLAY SITES FOR AN ATTRIBUTE FILE                                             
DISPLAY BIVARIATE ZONES FOR TWO ATTRIBUTE FILES                                 
DISPLAY ZONES & LINES FOR TWO ATTRIBUTE FILES                                   
DISPLAY ZONES AND SITES FOR TWO ATTRIBUTE FILES                                 
DISPLAY GEOGRAPHIC FILES (NO ATTRIBUTES)                                        
DISPLAY ATTRIBUTE FILES (DIAGRAMS)                                              
DISPLAY A SAVED-DISPLAY FILE                                                    
DISPLAY A PRESENTATION FILE                                                     
                                                                                
                                                                                

  9. 2 Attribute maps                                    
       --------------
 
     There are one or two streams of attribute processing for the types of      
maps available for zone, line and site attribute data:                          
                                                                                
     -  zones map                                                               
     -  lines map                                                               
     -  sites map                                                               
     -  two zone streams i.e. bivariate maps                                    
     -  zones and lines                                                         
     -  zones and sites                                                         
                                                                                
The type of map is selected before display and cannot be changed except         
by returning to this main menu.                                                 
                                                                                
Basic choropleth maps have already been demonstrated. These are selected        
within OzGIS by DISPLAY ZONES FOR AN ATTRIBUTE FILE. You can display maps       
with sized symbols in a similar way via DISPLAY SITES FOR AN ATTRIBUTE FILE, and
maps using different line types using DISPLAY LINES FOR AN ATTRIBUTE FILE.      
                                                                                
Here are some more examples... Remember you can type "L" to get a list of       
files when asked for a file name.                                               


                                                                      37

  9. 2. 1 Bivariate zones map Example                       
          ---------------------------
 
Bivariate maps enable you to compare two variables. For example you may         
want to compare your sales figures with Census data for the type of people      
you think are your customers.                                                   
                                                                                
Select DISPLAY BIVARIATE ZONES FOR TWO ATTRIBUTE FILES from the main menu.      
                                                                                
Use attribute files LOWE1 and LOWE2 and geographic file LOWE (both              
attribute files can be the same i.e. you only need one file).                   
                                                                                
Remember that you may have to type F3 to display the map.                       
                                                                                
 Note the form of the legend; the primary attribute (first file, top            
description) is the vertical part of the legend.                                
                                                                                
The main mapping menu will now appear:                                          
                                                                                
CHANGE ATTRIBUTES                                                               
DEFINE QUANTISATION                                                             
CHANGE DISPLAY FEATURES                                                         
DEFINE GEOGRAPHIC OVERLAYS                                                      
DEFINE MAP REGIONS                                                              
ANALYSE MAP DATA                                                                
SAVE DISPLAY FEATURES                                                           
                                                                                
These are the major groups of options and will be descibed in later             
chapters.                                                                       
                                                                                
Type F8 to return to the top menu.                                              

  9. 2. 2 Zones & sites Example                             
          ---------------------
 
This type of map is for applications such as deciding where to put shopping     
centres, where different symbols can be used for e.g. existing centres,         
centres owned by different retail chains and proposed new centres.              
                                                                                
This example shows that type of map and also how the geographic data displayed  
on a map can be extended and modified.                                          
                                                                                
Select DISPLAY ZONES AND SITES FOR TWO ATTRIBUTE FILES from the top menu.       
                                                                                
Use the LOWE1 and LOWE2 attribute files again, and the LOWE zones geographic    
file.                                                                           
                                                                                
Give the sites geographic file as LOWE-S1.                                      
                                                                                
This displayes a file with polygons coloured for one attribute and symbols      
sized for the other. Now we can add more sites.                                 
                                                                                
Choose DEFINE MAP REGIONS from the map menu, which shows a menu:                
                                                                                
CHANGE THE DISPLAYED ITEMS IN THE MAP                                           
CHANGE MAP REGION WINDOW (GEOGRAPHIC AREA)                                      


                                                                      38
ZOOM MAP REGION WINDOW ABOUT X-HAIR POINT                                       
CHANGE MAP REGION VIEWPORT (SCREEN AREA)                                        
DEFINE NEW REGION FOR QUANTISED ZONES                                           
DEFINE NEW REGION FOR QUANTISED SITES                                           
DISPLAY MORE QUANTISED ZONES ON A REGION                                        
DISPLAY MORE QUANTISED SITES ON A REGION                                        
                                                                                
and then DISPLAY MORE QUANTISED SITES ON A REGION. Give the next sites          
geographic file as LOWE-S2. Use symbol number 2 (number one is already used).   
                                                                                
Type F3 to regenerate the map.                                                  
                                                                                
You will have a coloured zones map with different sized symbols according to    
the attribute values and different symbols for the two files.                   
                                                                                
Use F8 (twice) to return to the top menu.                                       

  9. 2. 3 Geographic (GIS) maps Example                     
          -----------------------------
 
Maps can be displayed that show geographic data without attribute data i.e.     
polygons, lines, names at points and symbols at points.                         
                                                                                
Hence you can display roads, town locations, soil polygons etc.                 
                                                                                
Where the data are preclassified, feature codes can be used to subset the files 
for display.                                                                    
                                                                                
For example, display some of the Hawaii DLG files. These files came from the    
USGS, and after some cleaning up, were entered as DLG-3 data and the polygons   
formed using OzZone.                                                            
                                                                                
This example will display several of the files and show how feature codes       
can be used to subset the data displayed.                                       
                                                                                
Select DISPLAY GEOGRAPHIC FILES (NO ATTRIBUTES) from the top menu.              
                                                                                
The next menu allows you to define a map according to the main file of          
geographic data that you have. You can add other data to the map as overlays    
later:                                                                          
                                                                                
DISPLAY LINE SEGMENTS FROM A GEOGRAPHIC FILE                                    
DISPLAY MARKERS AT POINTS FROM A GEOGRAPHIC FILE                                
DISPLAY NAMES AT POINTS FROM A GEOGRAPHIC FILE                                  
DISPLAY POLYGONS FROM A GEOGRAPHIC FILE                                         
DISPLAY LINE SEGMENTS FOR FEATURE CODES                                         
DISPLAY MARKERS AT POINTS FOR FEATURE CODES                                     
DISPLAY NAMES AT POINTS FOR FEATURE CODES                                       
DISPLAY POLYGONS FOR FEATURE CODES                                              
                                                                                
                                                                                
Select DISPLAY POLYGONS FROM A GEOGRAPHIC FILE and use file HAWDLGWB, which is  
the outlines of the islands. Use any polygon number, give some text for the     
legend (e.g. "Islands") and use the no boundaries default.                      
                                                                                
Type F3 to regenerate if necessary.                                             
                                                                                
The main menu now appears for this type of map:                                 


                                                                      39
                                                                                
OVERLAY LINE SEGMENTS FROM GEOGRAPHIC FILE                                      
OVERLAY MARKERS FOR SITES IN GEOGRAPHIC FILE                                    
OVERLAY NAMES FOR SITES IN GEOGRAPHIC FILE                                      
UNDERLAY POLYGONS FROM GEOGRAPHIC FILE                                          
OVERLAY LINE SEGMENTS FOR FEATURE CODES                                         
OVERLAY MARKERS FOR SITES FOR FEATURE CODES                                     
OVERLAY NAMES FOR SITES FOR FEATURE CODES                                       
UNDERLAY POLYGONS FOR FEATURE CODES                                             
DEFINE MAP REGIONS#                                                             
CHANGE LEGEND                                                                   
DISPLAY TEXT                                                                    
SAVE DISPLAY AS A FILE                                                          
                                                                                
                                                                                
Select UNDERLAY POLYGONS FOR FEATURE CODES.                                     
Use file HAWDLGAB  which is administrative boundaries. The file has feature     
codes in the range 900103 to 900108. Give the range as 900103 to 900103 and use 
polygon number say 4.  Repeat for another feature code range and polygon        
number.                                                                         
                                                                                
You will notice that a new menu item REMOVE POLYGONS UNDERLAY appears. A        
feature of the OzGIS system is that menus are dynamic and reflect the current   
status.                                                                         
                                                                                
The administrative boundaries go outside the island coastlines so you may want  
to redraw the island outlines by overlaying line segments for file HAWDLGWB:    
                                                                                
Select OVERLAY LINE SEGMENTS FOR FEATURE CODES.                                 
Use file HAWDLGRD which is roads.  The file has feature codes in the range      
2905001 to 2905041.  Select a subset e.g. 2905000 to 2905020.                   
Give the legend text as "roads".                                                
                                                                                
Select OVERLAY LINE SEGMENTS FROM GEOGRAPHIC FILE.                              
Use file HAWDLGST which is streams. Give the legend text as streams.            
                                                                                
Select OVERLAY NAMES FOR SITES IN GEOGRAPHIC FILE. Give the file HAWDLGWB.  The 
polygon names will be displayed (the area numbers from the DLG file). Usually a 
points file would be used that has the actual names.                            
                                                                                
If necessary, type F3 to regenerate the map.                                    
                                                                                
Select DISPLAY TEXT, type in a title e.g. "HAWAII", and position it at          
the top of the map.                                                             
                                                                                
Note that if you regenerate the map the polygons are drawn first, and then line 
segments, symbols and finally names.  Within each type they are displayed in    
the order specified.  If a mistake is made overlays can be removed.             
                                                                                
If polygons overlap, "polygon overlay" operations can be simulated by           
displaying using hatching. e.g. select the hatch device file *HATCHSV1 from     
the main menu and then display polygons from the two files HAWDLGWB (the        
islands) and HAWDLGAB (administrative boundaries).                              
                                                                                
Type F8 to return to the top level geographic map menu and then F8 again.       
                                                                                
Be aware that you can type several menu selections without waiting for the      
menus to appear.                                                                


                                                                      40
                                                                                
A similar set of options are available for overlaying data on other types of    
maps. For example you may want to overlay roads or town names on a Census       
data map.                                                                       

  9. 2. 4 Diagrams Example                                  
          ----------------
 
Distributions, sorted values and quantisation results can be displayed as full  
screen diagrams for one or two attribute files. Scatter diagrams can be         
displayed for two files.                                                        
                                                                                
For example, to display two histograms for two attributes:                      
                                                                                
Choose DISPLAY ATTRIBUTE FILES (DIAGRAMS) from the top menu.                    
                                                                                
A menu appears that enables you to choose the type of diagram:                  
                                                                                
DISPLAY VALUES HISTOGRAM FOR AN ATTRIBUTE FILE                                  
DISPLAY QUANTISATION HISTOGRAM FOR AN ATTRIBUTE FILE                            
DISPLAY DISTRIBUTION HISTOGRAM FOR AN ATTRIBUTE FILE                            
DISPLAY VALUES HISTOGRAM FOR TWO ATTRIBUTE FILES                                
DISPLAY QUANTISATION HISTOGRAM FOR TWO ATTRIBUTE FILES                          
DISPLAY DISTRIBUTION HISTOGRAM FOR TWO ATTRIBUTE FILES                          
DISPLAY SCATTER DIAGRAM FOR TWO ATTRIBUTE FILES                                 
                                                                                
                                                                                
Choose DISPLAY DISTRIBUTION HISTOGRAM FOR TWO ATTRIBUTE FILES                   
                                                                                
Use LOWE1 and LOWE2 files.                                                      
                                                                                
Next choose CHANGE DISPLAY FEATURES from the main menu.                         
                                                                                
Now add some statistics lines:                                                  
                                                                                
Choose ADD STATISTICS TO DIAGRAM. A new menu appears:                           
                                                                                
DISPLAY MEAN & STD DEVIATION                                                    
DISPLAY MEDIAN                                                                  
DISPLAY REGRESSION POLYNOMIAL (for scatter diagrams)                            
REMOVE STATISTICS DISPLAY                                                       
                                                                                
Try the DISPLAY MEAN & STD DEVIATION option (and others if you like).           
                                                                                
Now use the Esc key to return to the main diagram menu.                         
                                                                                
You can change attributes and quantisation in the usual ways (and type F3 to    
show the results).                                                              
                                                                                
By now you will have realised that there are many options available down        
a multitude of menu paths. This can initially be confusing.                     
                                                                                
Always remember that if the current menu does not show an option for what       
you want to do, simply keep going up a level until you find a menu option       
that seems to offer what you want.                                              


                                                                      41

  9. 3 Presentations                                     
       -------------
 
This option enables a set of saved display files to be defined for              
demonstrations.                                                                 
                                                                                
An Ascii file is set up that gives the names of the saved display files and     
menu lines that are associated with them.                                       
                                                                                
The format of these files is explained in a later chapter.                      

  9. 4 Saved-display files                               
       -------------------
 
When you have prepared a map and have it displayed you can use the              
SAVE DISPLAY FEATURES option in the map display menu to store all information   
about the map in a file. There are two forms. One saves just the map definition 
while the other saves a screen image as well.                                   
                                                                                
Both forms enable a map to be restored for further mapping. This is the usual   
procedure if a map has taken a long time to design.                             
                                                                                
Saved maps are also used for hard-copy generation.                              

  9. 5 Time Lapse Display (not available)                
       ----------------------------------
 
                                                                                
This option was not ported from the PDP11 / DeANZA version.                     
Special options are available for the display of time lapse files.  The         
following parameters can be altered:                                            
                                                                                
      -  The time interval between successive attributes (given in units of     
         approximately seconds)                                                 
                                                                                
      -  The time interval between the end and beginning attributes of a        
         sequence (given in units of seconds); i.e. the pause between a         
         repeated sequence.                                                     
                                                                                
      -  The beginning and end attribute of the sequence being displayed.       
                                                                                
The zone legend format is not updated during a time lapse sequence, and by      
default the class description of the legend is set to the "HIGH" and "LOW"      
format.  Histograms and scatter plots cannot be displayed during a time lapse   
presentation.                                                                   
tribute values.                                                                 


                                                                      42
                   10. ATTRIBUTE SELECTION                               
                       ===================
 
                                                                                
                                                                                
Attribute data is held in attribute files. Each file can have many variables    
e.g. USA Census data STF1A files can have over 900 variables.                   
                                                                                
This chapter explains the options used to select which attribute is to be       
displayed on a map.                                                             
                                                                                
                                                                                
                                                                                

 10. 1 Introduction                                      
       ------------
 
Various attribute files can be nominated to generate a map display.             
                                                                                
Attribute may be selected for quantisation and display from attribute           
files in various ways:                                                          
                                                                                
To try these options, display a zones map using attribute file LOWE1 and        
geographic file LOWE as before and then select CHANGE ATTRIBUTES.               
                                                                                
The menu gives the following options:                                           
                                                                                
DISPLAY THE NEXT SEQUENTIAL ATTRIBUTE                                           
SELECT AN ATTRIBUTE FOR DISPLAY BY NUMBER                                       
SELECT AN ATTRIBUTE FOR DISPLAY BY DESCRIPTION                                  
                                                                                

 10. 2 Sequentially                                      
       ------------
 
This option will simply select the next attribute off the file. As usual F3 may 
have to be used to display the map.                                             

 10. 3 By number (position in file)                      
       ----------------------------
 
A particular attribute may be selected by the position within the file. Type    
zero to generate a list of the attributes on the current file.                  

 10. 4 By attribute description                          
       ------------------------
 
The attribute can also be selected by typing part of the description e.g.       
"FORC" to retrieve "ARMED FORCES". Typing L lists the attributes.               

 10. 5 By arithmetic operation                           
       -----------------------
 
This option is not available now due to the limited PC memory. See the data     
preparation option in the OzData program.                                       


                                                                      43

 10. 6 Zone/Site/Line names                              
       --------------------
 
It is your responsibility to ensure that the names referenced by the            
attributes match the names of the displayed zones, lines or sites in the        
map.  Obviously colours can be assigned only to the zone with names common      
to the attribute and zone files etc.                                            
                                                                                
Only some of the names have to agree; it is quite common to process attribute   
data for a larger area than is displayed.                                       


                                                                      44
                   11. QUANTISATION                                      
                       ============
 
                                                                                
                                                                                
Quantisation is the process of assigning map items to classes according to      
their attribute values.                                                         
                                                                                
The quantisation process is the most important aid for the analyst in           
understanding the features of the attribute data.  The quantisation method      
and parameters should be chosen logically according to the purpose of           
analysing the data.                                                             
                                                                                
The aim is to display the map that best shows the spatial features and          
distribution of the data.                                                       
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                

 11. 1 Introduction                                      
       ------------
 
Attributes are usually presented to OzGIS as values which have to               
be quantized into a number of classes for display.                              
                                                                                
A maximum of 10 classes can appear in single variate zone displays and          
9 classes (a maximum of 3 per variate) in a bivariate display.  A maximum       
of 4 classes is available for lines and 4 classes for sites.                    
                                                                                
The best maps usually have a small number of classes; manipulate the            
map to show the data according to requirements. This contrasts with the         
production of atlases, where large numbers of colours are used as the purpose   
to which the map will be put is not known.                                      
                                                                                
To try these options, display a zones map using attribute file LOWE1 and        
geographic file LOWE as before, and select DEFINE QUANTISATION.                 
                                                                                
The quantisation menu has the following form:                                   
                                                                                
CHANGE THE QUANTISATION METHOD                                                  
CHANGE THE NUMBER OF CLASSES                                                    
SELECT THE ZONES FOR QUANTISATION                                               
SELECT THE ATTRIBUTE VALUE RANGE FOR QUANTISATION                               
                                                                                
You will find that this menu is dynamic as usual. You will find other           
entries such as SELECT THE LINES FOR QUANTISATION or                            
CHANGE THE NUMBER OF SITE CLASSES for different types of maps.                  
                                                                                
Try changing the number of classes first and then work through                  
the various methods.                                                            
                                                                                
There are other options to change the list of zones to which quantisation is    
applied and to change the range of values over which the method operates.       


                                                                      45

 11. 2 Quantisation Methods                              
       --------------------
 
Selecting the menu option CHANGE THE QUANTISATION METHOD will display a new     
menu of the form:                                                               
                                                                                
USE EQUAL VALUE INTERVALS                                                       
USE QUANTILES                                                                   
USE SELECTED CLASS INTERVALS                                                    
USE SELECTED NUMBER OF ZONES PER CLASS                                          
USE REFINED EQUAL VALUE INTERVALS                                               
USE THE MEAN AND STD DEVIATION METHOD                                           
USE THE NESTED MEANS METHOD                                                     
USE THE NATURAL BREAKS METHOD                                                   
USE SELECTED PERCENTILES                                                        
USE SELECTED CLASS RANGE PERCENTILES                                            
USE INTERACTIVE SELECTION OF CLASS INTERVALS                                    
USE EQUIVALENCE CLASSES                                                         
USE CURRENT CLASS RANGES                                                        
USE CURRENT NO PER CLASS                                                        
                                                                                
If you have a 256 colour display the following item also appears:               
USE PSEUDO CONTINUOUS-COLOUR                                                    
                                                                                
You should try out these various methods e.g. with the attribute and            
geographic files OZ.                                                            
                                                                                
                                                                                
                                                                                
The following methods for quantization are available for determining            
the class intervals:                                                            
                                                                                
   (a)  Equivalence Classes:  numbers are assigned to the attribute values      
        (possibly with integer round-off).  The attribute values should lie     
        in the range of the maximum number of classes permitted but they        
        will be scaled for the selected number of classes.                      
                                                                                
        This method enables the quantisation to be carried out on another       
        system and the resulting class numbers entered instead of attribute     
        values.  A common use is for mapping discrete data e.g. political       
        parties on election maps.                                               
                                                                                
   (b)  Quantiles:  intervals are computed by assigning the same number of      
        zones to each class.                                                    
                                                                                
        This method has often been used to generate choropleth maps, e.g.       
        deciles.  The effect of equal numbers of zones is maps that have        
        approximate equal areas of each class colour.  Such maps are            
        pretty.  Unfortunately quantiles tend to obscure the distribution       
        of the attribute data.  (Conversely its a great method if your          
        data is of doubtful value)                                              
                                                                                
   (c)  Equal Value Intervals:  intervals are computed from equal               
        increments over the range of attribute values.                          
                                                                                
        The default quantisation method selected when a map is first            


                                                                      46
        generated is equal value intervals.  The advantage of this method       
        is that the number of zones assigned to each class indicate the         
        distribution of the data.  It is recommended for general purpose        
        maps and for initial investigations of attribute data.                  
                                                                                
   (d)  Refined Equal Value Intervals:  intervals are computed from equal       
        increments over the attribute value range, modified by a                
        "round-off" procedure (e.g. an increment of 10.12 would become          
        10.00).                                                                 
                                                                                
        Maps for publications usually have 'nice' values in the legend.         
                                                                                
   (e)  Continuous Colour:  121 intervals are computed from equal               
        increments over the range of attribute values.  Only 8 classes are      
        displayed in the legend, but the colours are assigned over the 121      
        quantized values to give a "continuous colour" appearance.              
        This option is only available with standard zone maps on 256            
        colour display systems.                                                 
                                                                                
   (f)  Interactive Selection of Class Intervals:  intervals are selected       
        by the user by placing crosshairs on a displayed histogram.             
        (256 colours interactive mode only!)                                    
                                                                                
   (g)  Mean and Standard Deviation:  intervals are determined by dividing      
        the range of attribute values at the mean value and at specified        
        offsets from the mean that are multiples of the standard deviation      
        of the data.  The number of classes must be even.                       
                                                                                
        This method has particular application for attribute data from          
        random populations where the data are expected to have a normal         
        distribution and hence statistical theorems govern percentages of       
        population within the classes.                                          
                                                                                
   (h)  Nested Means:  intervals are determined by iterative division of        
        the range of attribute values at the mean value of the subdivision.     
        The number of classes must be 2, 4 or 8.                                
                                                                                
   (i)  Natural Breaks:  intervals are determined by iterative division at      
        the largest difference between attribute values.  The number of         
        attribute values between differences is user-specified.  Hence          
        class intervals occur at "jumps" in the data.                           
                                                                                
   (j)  Specification of Class Intervals:  interval values (for a specified     
        number of classes) are typed in by the user.                            
                                                                                
        Hence data within certain value ranges can be isolated.   Suitable      
        class intervals for hard-copy maps can be selected.                     
                                                                                
   (k)  Specification of Numbers Per Class:  intervals are determined by        
        user-specification of the number of zones or sites in each class.       
        The numbers need only be given for some of the classes; the             
        remaining zones or sites will be distributed over the remaining         
        classes during each quantization.                                       
                                                                                
        An analyst can isolate data at the extremes of the attribute            
        distribution by using this method.                                      
                                                                                
   (l)  Class Number Percentiles:  intervals are determined from                


                                                                      47
        user-specified values giving the percentages of the number of zones     
        within each class.                                                      
                                                                                
   (m)  Class Range Percentiles:  intervals are determined from                 
        user-specified values giving the percentage of the total range of       
        attribute values in each class.                                         
                                                                                
   (n)  Current Class Intervals:  the intervals (and number of classes) are     
        used to quantize subsequent attributes.                                 
                                                                                
        Hence a series of maps can be produced with the same legend which       
        enables attributes to be compared.                                      
                                                                                
   (o)  Current Numbers:  the number of zones or sites per class (and           
        number of classes) are used to determine the intervals for              
        subsequent attributes.                                                  

 11. 3 Quantisation Ranges                               
       -------------------
 
The range of values over which the quantization is applied can be               
restricted in all methods.  The following options are available for             
limiting the range:                                                             
                                                                                
      -  the extremes of all values (default)                                   
      -  user-specified limits (the user enters the low and high values)        
      -  refined values (i.e., automatically rounded to "nice" values)          
      -  limits fixed at current values for subsequent quantisations            
                                                                                
Zones with values outside these limits are assigned the "excluded zone"         
value and colour, lines and sites are not displayed.                            
                                                                                
The menu is of the form:                                                        
                                                                                
QUANTISE FOR ATTRIBUTE VALUE RANGE                                              
TYPE IN ATTRIBUTE VALUE LIMITS FOR EVERY QUANTISATION                           
FIX LIMITS AT CURRENT VALUES                                                    
QUANTISE FOR AUTOMATICALLY SELECTED VALUE LIMITS                                
                                                                                
                                                                                
For example a standard legend for percentage data with value ranges             
0,25,50,75 and 100 could be generated by choosing extremes to be 0 and 100      
and fixing them, and by using 4 equal value classes.                            

 11. 4 Quantisation Lists                                
       ------------------
 
Each of the attribute processing streams has an associated list                 
that holds the names of the items being quantised i.e. zones or lines or        
sites.  There is one list for a single stream, one zones list for bivariate     
maps, and for two streams there is a list of zones and a list of lines or       
sites.                                                                          
                                                                                
Each list selects the items that are to be quantised from the                   
corresponding attribute file.  When a map is generated the lists are set to     
all the names if the attribute files (common names in the case of bivariate     
maps).                                                                          
                                                                                


                                                                      48
Zone lists can be reset to:                                                     
                                                                                
      -  all zones in current attribute file (single variate)                   
      -  all zones common to two attribute files (bivariate)                    
      -  the displayed zones                                                    
      -  zones in a names file                                                  
                                                                                
The menu is of the form:                                                        
                                                                                
QUANTISE FOR DISPLAYED SITES                                                    
QUANTISE FOR ALL SITES IN THE ATTRIBUTE FIL                                     
QUANTISE FOR SITES IN A NAME FILE                                               
EDIT SITES USED FOR QUANTISATION                                                
                                                                                
                                                                                
Zone lists can also be modified by adding or deleting zone names by             
typing in a name or selecting the zone with the cursor (256 colour mode)        
                                                                                
Site lists and line lists can be modified by giving the names.                  
                                                                                
Hence the quantisation can take place for a set of items that is                
independent of the displayed, zone lines and sites (although it is              
illogical for none to be the same).  It is common for the quantisation to       
be carried out over a larger geographic area than that being displayed.         
Sometimes zones are removed because the attribute data are doubtful e.g.        
Census districts with a low population.                                         
                                                                                
Changing attribute files does not change the items whose values are             
quantized.                                                                      


                                                                      49
                   12. GEOGRAPHIC OVERLAYS                               
                       ===================
 
                                                                                
This chapter describes how geographic data such as roads and town locations     
can be overlayed on top of displayed maps.                                      
                                                                                
                                                                                
                                                                                
                                                                                

 12. 1 Introduction                                      
       ------------
 
Geographic files can be displayed on zones, sites and lines maps to add extra   
information, usually for "navigation" purposes.                                 
                                                                                
Overlays are selected by choosing DEFINE GEOGRAPHIC OVERLAYS off the main       
map display menu.                                                               
                                                                                
A menu appears of the following form:                                           
                                                                                
OVERLAY LINE SEGMENTS FROM A GEOGRAPHIC FILE                                    
OVERLAY MARKERS FOR SITES IN GEOGRAPHIC FILE                                    
OVERLAY NAMES FOR SITES IN GEOGRAPHIC FILE                                      
UNDERLAY POLYGONS FROM GEOGRAPHIC FILE                                          
OVERLAY LINE SEGMENTS FOR FEATURE CODES                                         
OVERLAY MARKERS FOR SITES FOR FEATURE CODES                                     
OVERLAY NAMES FOR SITES FOR FEATURE CODES                                       
UNDERLAY POLYGONS FOR FEATURE CODES                                             
                                                                                
This menu is similar to the one used with geographic (no attributes) maps.      
                                                                                
Polygons can be displayed underneath, such as postal districts under a sites    
map.                                                                            
                                                                                
Lines are often displayed on top of a map e.g. roads, rivers.                   
                                                                                
Points can be displayed as symbols e.g. locations of shopping centres.          
                                                                                
Point labels can also be displayed e.g. names of towns.                         
                                                                                
Overlays etc are displayed in the order polygon underlays, then the standard    
map according to attribute values, then line overlays, then point symbols, and  
finally names.                                                                  
                                                                                
Within each type of overlay display takes place in the order the overlays are   
defined. In some cases order of definition is important as a later overlay can  
obscure an earlier one.                                                         
                                                                                
The basic geographic files contain  polygons,lines, points and names.           
e.g. a file of one level of census boundaries (e.g. blocks) could be displayed  
as a lines overlay. Files built with OzZone also contain approximate centroids  
of zones with labels being the zone names.                                      


                                                                      50

 12. 2 USA Census / TIGER Overlays Example               
       -----------------------------------
 
Some sample files are supplied with the system for Washington DC. These were    
supplied by the US Census Bureau, and would usually be obtained on CD-ROM.      
                                                                                
The attribute file is WASHTRACT and was created by entering the first file off  
the STF1A CD-ROM (the original file was called STF1A0DC.DBF). This file         
contains about 40 of the 1990 Census variables extracted for tract/BNAs.        
                                                                                
Three geographic files are supplied. These came from the CD-ROM files for       
Washington DC. The files for records type 1 (endpoints) and type 2 (shapes) were
processed. The files were simplified (thinned) to reduce the size.              
                                                                                
WASHTRACT was created by extracting census boundaries for the tract/BNAs with   
the OzEnter program, thinning with the OzData program, and finally building     
the zones with OzZone.                                                          
                                                                                
WASHRAIL is a lines file of railroads created by  extracting for feature codes  
200 to 252 in OzEnter.                                                          
                                                                                
WASHROAD is a lines file of all roads created by extracting for feature codes   
100 to 148 in OzEnter.                                                          
                                                                                
                                                                                
These files can be used to demonstrate the use of overlays:                     
                                                                                
First select DISPLAY ZONES FOR AN ATTRIBUTE FILE to display a zones map using   
attribute file WASHTRACT and geographic file WASHTRACT. This gives a standard   
choropleth map for 1990 Census data for Washington at tract/BNA level.          
                                                                                
Select DEFINE GEOGRAPHIC OVERLAYS from the map menu.                            
                                                                                
A menu appears that offers options for several types of overlays:               
                                                                                
OVERLAY LINE SEGMENTS FROM A GEOGRAPHIC FILE                                    
OVERLAY MARKERS FOR SITES IN GEOGRAPHIC FILE                                    
OVERLAY NAMES FOR SITES IN GEOGRAPHIC FILE                                      
UNDERLAY POLYGONS FROM GEOGRAPHIC FILE                                          
OVERLAY LINE SEGMENTS FOR FEATURE CODES                                         
OVERLAY MARKERS FOR SITES FOR FEATURE CODES                                     
OVERLAY NAMES FOR SITES FOR FEATURE CODES                                       
UNDERLAY POLYGONS FOR FEATURE CODES                                             
                                                                                
                                                                                
Now select OVERLAY MARKERS FOR SITES IN GEOGRAPHIC FILE,                        
use the same geographic file,                                                   
select marker 1, give the legend text as TRACTS.                                
                                                                                
A series of markers will be displayed. The locations are the points within      
the standard zones/polygon file built with OzZone so are the approximate        
centroids of the polygons.                                                      
                                                                                
Next select OVERLAY NAMES FOR SITES IN GEOGRAPHIC FILE, and use the same        
geographic file in a similar way to display the tract codes. The names here     
are the zone names. You could of course use any file with differnt locations and


                                                                      51
names e.g. town names.                                                          
                                                                                
Now add a line segments overlay. Select OVERLAY LINE SEGMENTS FROM A            
GEOGRAPHIC FILE. Use the file WASHRAIL to display railroads.                    
                                                                                
You could now do the same for the roads file. Try subsetting for feature codes  
as follows:                                                                     
                                                                                
Select OVERLAY LINE SEGMENTS FOR FEATURE CODES. Use a different                 
line number each time and try a range 110 to 138 first to display primary,      
secondary and country roads. Then try a range 140 to 148 to display             
neighbourhood roads. TIGER file feature codes are defined in the appendix.      
                                                                                
Finally hit F3 to regenerate the map in the default order.                      


                                                                      52
                   13.  DISPLAY CONTROL & MAP DESIGN                     
                       =============================
 
                                                                                
                                                                                
This chapter describes the options available for changing the general appearance
of a map.                                                                       
                                                                                
These options enable map features that are not geographically referenced to be  
defined.                                                                        
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                

 13. 1 Introduction                                      
       ------------
 
A series of options are available to control the general appearance of maps.    
                                                                                
These are chosen by selecting CHANGE DISPLAY FEATURES from the main map         
menu.                                                                           
                                                                                
The menu is of the form:                                                        
                                                                                
DISPLAY TEXT                                                                    
DEFINE ATTRIBUTE DIAGRAMS ON MAP                                                
ADD STATISTICS TO DIAGRAM                                                       
CHANGE ZONES LEGEND                                                             
CHANGE LINES LEGEND                                                             
CHANGE SITES LEGEND                                                             
CHANGE GEOGRAPHIC OVERLAYS (GIS) LEGEND                                         
DISPLAY SYMBOL LEGEND                                                           
DISPLAY REGION GRIDS                                                            
                                                                                
The actual options that appear depends on the type of map. The options are      
described in the following sections:                                            
                                                                                

 13. 2  Map Quantisation Legends                         
       -------------------------
 
                                                                                
A legend is always displayed on the monitor when an attribute is                
quantised for map display.  Similar legends are displayed for zones, lines      
and sites.                                                                      
                                                                                
The menu to change legends has the form:                                        
                                                                                
REMOVE/INCLUDE CLASS RANGES                                                     
ANNOTATE CLASS BOXES WITH 'HIGH' AND 'LOW'                                      
TYPE IN CLASS ANNOTATION (2 LINES PER CLASS)                                    
CHANGE ANNOTATION FOR A CLASS                                                   
TYPE IN CLASS ANNOTATION HEADER                                                 
REMOVE/INCLUDE CLASS ANNOTATION HEADER                                          
REMOVE/INCLUDE NO. ZONES IN CLASSES                                             


                                                                      53
REMOVE/INCLUDE MISSING DATA BOX                                                 
REMOVE/INCLUDE EXCLUDED ZONES BOX                                               
REMOVE/INCLUDE UNITS DESCRIPTION                                                
TYPE IN ZONES LEGEND TITLE                                                      
REMOVE/INCLUDE ZONES LEGEND TITLE                                               
SPECIFY CLASS RANGE DISPLAY PRECISION                                           
SELECT ZONES LEGEND VIEWPORT WITH THE BOX-CURSORS                               
                                                                                
                                                                                
The elements of a legend are:                                                   
                                                                                
      -  TITLE, a title for the legend (maximum of 3 lines and 16               
         characters per line).                                                  
                                                                                
      -  UNITS, description of the units of a legend (maximum of 10             
         characters).                                                           
                                                                                
      -  HEADER, a header for the class annotation (maximum of 8                
         characters).  The default is "RANGE".                                  
                                                                                
                                                                                
      -  CLASS ANNOTATION, either                                               
                                                                                
            -  the class intervals as numbers aligned between boxes             
               (maximum of 8 characters), or                                    
                                                                                
            -  class description aligned with the centre of boxes (maximum      
               of 2 lines, 8 characters per line), or                           
                                                                                
            -  "HIGH" and "LOW" at the top and bottom of the boxes              
               respectively.                                                    
                                                                                
      -  EXCLUDED ZONES, annotation for the "excluded zones" class              
                                                                                
      -  MISSING DATA ZONES, annotation for the "missing data" class            
                                                                                
      -  NUMBERS, the numbers of items in each class.                           
                                                                                
Zone legends have fixed size boxes that give the colours used for the           
classes.                                                                        
                                                                                
Site legends have variable sized symbols in a special colour that give          
the markers and their sizes used for the classes.                               
                                                                                
Line legends replace the boxes by sample lines in a special colour              
that give the line types used for the classes.                                  
                                                                                
All text in a legend is written with small fixed size characters.               
                                                                                
Display of the legend elements can be controlled by the user.  The              
boxes corresponding to attribute classes are always displayed but the           
elements (including "excluded zones" and "missing data " boxes) can be          
removed.                                                                        
                                                                                
Some of the legend text can be replaced by characters entered by the            
user on the keyboard, viz.,                                                     
                                                                                
         -  title                                                               


                                                                      54
         -  units                                                               
         -  header                                                              
and      -  class description                                                   
                                                                                
The default map layout sets the map image viewport as the left three            
quarters (approximately) of the monitor, and the legend viewpoints on the       
right side of the screen.  The zone legend is on the bottom, line or site       
legend above.                                                                   
                                                                                
New legend viewpoints can be selected with the box cursor.  A single            
variate legend may need more than one column to fit.                            
                                                                                

 13. 3 Overlays (GIS) legends                            
       ----------------------
 
When line overlays, markers, text at points or polygon underlays are displayed  
a legend appears that describes the overlays. The text must be specified by the 
user.                                                                           

 13. 4 Other Legends                                     
       -------------
 
When several line files are being displayed using different lines, or           
several site files are displayed using different markers, a legend can be       
added.                                                                          
                                                                                
      The line and marker legends have similar format:                          
                                                                                
      -  a header line of text                                                  
      -  legend entries                                                         
      -  marker or box in quantisation legend colour                            
      -  description                                                            

 13. 5 Text                                              
       ----
 
Lines of text can be typed in and displayed on the screen in one of             
the four available text types.  The text is positioned with the cursor.  Up     
to 20 lines of text can be displayed.                                           
                                                                                
Lines of text can be deleted and moved around the screen.                       
                                                                                
Text is usually added to a map to supply extra information e.g. the             
name of the geographic region and type of zones, organisation names,            
disclaimers.                                                                    

 13. 6 Attribute Diagrams                                
       ------------------
 
A menu is available to control diagrams added to an attribute map.              
                                                                                
Select DEFINE ATTRIBUTE DIAGRAMS ON MAP.                                        
                                                                                
                                                                                
DISPLAY THE SCATTER DIAGRAM                                                     
DISPLAY THE ATTRIBUTE DISTRIBUTION                                              
DISPLAY THE QUANTISATION RESULTS                                                


                                                                      55
DISPLAY THE SORTED ATTRIBUTE VALUES                                             
REMOVE/DISPLAY AXES                                                             
REMOVE DIAGRAM                                                                  
CHANGE DISPLAY VIEWPORT                                                         
                                                                                
                                                                                
      (a)  Histograms can be displayed in the map area.  The                    
           histograms show one of the following:                                
                                                                                
            -  the number of items (zones or sites) within equal intervals      
               of a single attribute                                            
            -  the number of items within class intervals of a single           
               attribute                                                        
            -  the attribute values corresponding to zones sorted in            
               ascending order of attribute value.                              
                                                                                
               The bars of a histogram are coloured according to the class      
               colours in the legend.  For two variate displays, two            
               histograms can be displayed one underneath the other.  The       
               histograms provide an overview of the statistical                
               distribution of the attribute values.                            
                                                                                
      (b)      Scatter plots can be displayed in the map area for               
               bivariate zone displays.  The plots show the distribution of     
               zones within the ranges of each attribute.  The elements of      
               the plot are coloured according to the class colours in the      
               legend.  The scatter plots provide an overview of the            
               statistical distribution of the attribute values.                
                                                                                
      (c)   Statistics can be added to the diagrams:                            
                                                                                
      -  mean and standard deviation lines                                      
      -  median                                                                 
                                                                                
      A regression polynomial of order 1,2 or 3 can be added to a scatter       
      diagram.                                                                  
                                                                                
      The diagram viewport is selected with the cursor.                         
                                                                                
Addition of a distribution histogram or scatter diagram (bivariate)             
add considerably to the information content of a map. They are displayed by     
default.                                                                        

 13. 7 Displayed Colours (removed)                       
       ---------------------------
 
                                                                                
Options to change colours are no longer available in the DOS version. They      
were removed when  DOS limits were exceeded.                                    
                                                                                
All colours within a map display can be changed by the user when a              
256 colour VGA display system is being used.  Individual colours can be         
selected in three ways:                                                         
                                                                                
      (a)  by reference to a colour palette.  The colour is selected with       
           the crosshairs (256 colour mode).                                    
                                                                                
      (b)  by a blue, green and red (B,G,R) triple.  Values for each of the     


                                                                      56
                                                                                
           elements in the triple range from 0 to 1.0;  a red colour would      
           therefore be 0.0,0.0,1.0.                                            
                                                                                
      (c)  by a name from a colour names file.  The name is a character         
           string typed on the keyboard.                                        
                                                                                
Any of these ways can be selected by the user.                                  
                                                                                
The set of colours is assigned to map classes and associated map                
elements by reference to the current device file.                               
                                                                                
This enables colours for all of  the classes to be assigned quickly, although   
individual colours in the set can be modified subsequently.                     
                                                                                
Displayed elements must be identified in order to change their                  
colour.                                                                         
                                                                                
Certain elements are explictly referenced in the menus associated               
with colour change, and can be identified by selecting the appropriate menu     
option.  These elements are:                                                    
                                                                                
     -  text                                                                    
     -  markers                                                                 
     -  lines                                                                   
     -  zone boundary                                                           
     -  map background                                                          
     -  excluded zones                                                          
     -  zones with missing data                                                 
     -  zone attribute classes                                                  
     -  background of attribute diagrams                                        
     -  site legend markers                                                     
     -  line legend                                                             
                                                                                
Specific attribute classes, text, markers and lines are identified by           
number.                                                                         


                                                                      57
                   14. MAP REGIONS                                       
                       ===========
 
                                                                                
                                                                                
This chapter describes the options that enable the geographic layout of a       
map to be defined.                                                              
                                                                                
                                                                                
                                                                                

 14. 1 Introduction                                      
       ------------
 
Map regions enable complex map layouts to be generated.  Maps often             
have only one region, typically zones from one geographic file displayed on     
the default viewpoint on the monitor.  Multiple regions, each with defined      
window and viewport provide many possibilities:                                 
                                                                                
For example:                                                                    
                                                                                
  . Display of different parts of a country (from different geographic          
    files) at the same time.                                                    
  . Display of a geographic area and a part extracted from it on the            
    same map.                                                                   
  . Display of overlays such as roads or retail sites on different parts of     
    a map.                                                                      
  . Changing the geographic areas that are currently displayed and moving       
    them on the screen.                                                         
  . Displaying adjacent geographic areas joined together.                       
                                                                                
These options are for the geographically referenced features of a map. There    
is a different set of options for defining other features on a map such as      
text and legends that are simply positioned on the screen.                      
                                                                                
                                                                                
Definition of map regions is requested by selecting DEFINE MAP REGIONS from     
the main map menu after a map has been displayed.                               
                                                                                
A menu then appears of the following form:                                      
                                                                                
CHANGE THE DISPLAYED ITEMS IN THE MAP                                           
CHANGE MAP REGION WINDOW (GEOGRAPHIC AREA)                                      
ZOOM MAP REGION WINDOW ABOUT X-HAIR POINT                                       
CHANGE MAP REGION VIEWPORT (SCREEN AREA)                                        
DEFINE NEW REGION FOR QUANTISED ZONES                                           
DISPLAY MORE QUANTISED ZONES ON A REGION                                        
DELETE QUANTISED ZONES FROM REGION                                              
                                                                                
These few options enable comples layouts to be defined (sometimes with a lot    
of playing around). If a map is complex it is recommended that the map be       
saved often so you will not have to start from the beginning if a               
mistake is made.                                                                


                                                                      58

 14. 2 Regions                                           
       -------
 
A new map region is established when a geographic file is displayed.  The       
region is defined by the geographic window (or subset) and its displayed        
area (or viewport) on the monitor.                                              
                                                                                
A standard map consists of one region. The window is the whole of the           
geographic file and the viewport is most of the screen.                         
                                                                                
Other regions can be added to a map. A maximum of 10 map regions can be         
defined in a map. The option DEFINE NEW REGION FOR QUANTISED ZONES enables      
other geographic files to be added to the map, each on their own part           
of the screen, and to be coloured according to the attribute file values.       
For example, you may want to display a map of 5 counties, where you have 5      
geographic files (one for each county) and one attribute file that has          
the values you want to display. You start by displaying just one                
geographic file and then use this option to add and position the other          
four files. You will find that it takes some time to finalise the layout        
in this type of map.                                                            
                                                                                
Regions are identified by number, being the order in which the regions are      
defined. A standard map has only region number one, and you do not have to      
specify the region number.                                                      
A geographic window is initially the total area of the geographic file          
(Files are subset as a data preparation process).  You can change the part      
of the geographic file that is displayed by selecting a new geographic          
extent via the options CHANGE MAP REGION WINDOW (GEOGRAPHIC AREA) or            
ZOOM MAP REGION WINDOW ABOUT X-HAIR POINT                                       
                                                                                
A new viewport is selected by positioning the cursor on the monitor with        
the mouse or arrows (i.e. it is a rectangular part of the screen) via           
the option CHANGE MAP REGION VIEWPORT (SCREEN AREA)                             
                                                                                
Polygon underlays, line, point and name overlays can be added to any map        
region. This process is the same as already described in the chapter on         
overlays except that the region number has to be given if there are more        
than one.                                                                       
                                                                                
More than one geographic file can be displayed on a region according to the     
attribute data with DISPLAY MORE QUANTISED ZONES ON A REGION. For example       
you may want to display maps of two adjoining states. You start by displaying   
one of the geographic files for the attribute file in the standard way.         
You then add the second file to the same region (and adjust the viewport and    
window). The two states will neatly fit together (if the projection &           
coordinate system is the same).                                                 
                                                                                
Geographic files are automatically windowed, scaled and clipped for             
display on map regions.                                                         
                                                                                
When multiple files are displayed on a region, the precedure order is           
polygons, quantised zones, lines, sites, line overlays, markers and finally     
text at points.                                                                 
                                                                                
Multiple regions can be defined anywhere on the map display area of             
the monitor.  However, if regions overlap the display procedure is              


                                                                      59
established by the order of definition.  Therefore the user should consider     
the order of display carefully in multiple region presentations.                
                                                                                
Geographic files can be displayed  in any order, and regions can be defined     
and changed as desired.                                                         
                                                                                
Many  of these operations destroy the data in the display system memory         
(the map display is corrupted) so F3 must be typed to completely regenerate     
the map display.                                                                
                                                                                

 14. 3 Map List                                          
       --------
 
A list of displayed items (zones, lines and sites) is maintained by             
the system.                                                                     
                                                                                
The list can be changed by selecting CHANGE THE DISPLAYED ITEMS IN THE MAP,     
which displays a menu of the form:                                              
                                                                                
USE THE ITEMS IN A NAMES FILE                                                   
USE ITEMS IN THE CURRENT ATTRIBUTE FILE                                         
USE DISPLAYED ITEMS FROM RANGE OF CLASSES                                       
USE THE ITEMS THAT ARE QUANTISED                                                
EDIT THE DISPLAYED MAP ITEMS                                                    
                                                                                
                                                                                
The list is sorted into alphabetical order, and the items are                   
displayed using pixels corresponding to the position in the table (256          
colour mode).  This enables items to be selected with the cursor and            
identified.                                                                     
                                                                                
A list of flags corresponding to the map list is also held.  The                
flags enable some of the displayed items to be dropped interactively.           
                                                                                
The flags are usually set to items in the attribute files:                      
                                                                                
The options are:                                                                
                                                                                
      -  names in attribute file (single variate)                               
      -  common to two attribute files (bivariate)                              
      -  names in two attribute files (zones and lines or sites)                
      -  names for ranges of classes                                            
      -  names in quantisation lists                                            
                                                                                
Items can be added or deleted by selecting them with the cursor or              
typing the name.                                                                
                                                                                
The DOS version of OzGIS can display up to 500 items.  When                     
the number of display items (plus standard features) is less than the           
length of the hardware LUT (number of simultaneous colours) the system can      
display the results of quantising zone attribute data extremely rapidly by      
changing the colours.  When the number of items is too large the system has     
to revert to displaying each zone by polygon fill.                              


                                                                      60

 14. 4 Quantised Zones                                   
       ---------------
 
Up to 10 sets of zones files can be displayed on defined regions.               
Adjacent files will automatically join.  GKS clips the polygons to the          
edges of the region viewports.  Where regions overlap, the zones of the         
last one to be displayed will overwrite the displayed data underneath.          
                                                                                
Zones that are not in the map list are not displayed.                           
                                                                                
When the system operates in fast interactive mode the zones are                 
displayed once and the colours changed for the quantisation results.  In        
polygon fill mode the zones are displayed every time attribute data are         
quantised using fill (colour, pattern or hatch) for the appropriate             
classes.                                                                        
                                                                                
Note that OzGIS expects overwriting to occur.  Hence display of                 
polygons on top of others is not successful using hatching on plotters,         
so OzGIS handles polygons in a special way for this case.                       

 14. 5 Quantised lines                                   
       ---------------
 
Up to 10 sets of lines can be displayed on regions.  GKS clips lines            
to region viewports.                                                            
                                                                                
Lines that are not in the map list are not displayed.                           
                                                                                
Each file is assigned to a different line, and is displayed in that             
line colour.  Four different lines are available.  The results of the           
quantisation are displayed by using different line types.                       
                                                                                
The attribute data can be quantised into up to four classes, so four            
line types are used.  The line files are assigned to the four available         
lines according to overall classification when they are defined (e.g.           
roads, railway tracks and rivers).                                              

 14. 6 Quantised sites                                   
       ---------------
 
Up to 10 files can be displayed on regions.                                     
                                                                                
Sites that are not in the map list or are outside the region window             
are not displayed.                                                              
                                                                                
Each file is assigned to a different marker and is displayed in that            
marker's colour and background colour.  Four different markers are              
available.  The results of the quantisation are displayed as different          
sized markers.  When operating in fast interactive mode, the markers are        
displayed in bit planes so they can be rapidly cleared.                         
                                                                                
The attribute data can be quantised into up to four classes so four             
different marker sizes are used.  The files are assigned to the four            
available markers according to overall classification (e.g. owners of banks     
at the sites).                                                                  


                                                                      61

 14. 7 Line Overlays                                     
       -------------
 
The segments from up to 10 geographic files can be displayed as                 
overlays on map regions.  Each file is assigned to a region and one of four     
available lines and is displayed as a solid line in that line's colour.         
GKS clips the lines to the region's viewport.                                   

 14. 8 Polygon underlays                                 
       -----------------
 
The polygons from up to 10 geographic files can be displayed as                 
underlays on map regions.  Each file is assigned to a region and one of eight   
available polygon colours.                                                      

 14. 9 Marker Overlays                                   
       ---------------
 
The points from up to 10 geographic files can be used to display                
markers at points in regions.  Each file is assigned to a region and to one     
of four available markers.  Markers are not displayed for points outside        
the region's window.                                                            

 14.10 Name Overlays                                     
       -------------
 
The  points from up to 10 geographic files can be used to display               
names at points in regions.  Each site file is assigned to a region and to      
one of four available types of text.  Names are not displayed for points        
outside the region's window.                                                    

 14.11 Map Modification                                  
       ----------------
 
The window and viewport of a map region can be modified by selecting            
a new one with the cursors.                                                     
                                                                                
Files displayed for quantisation can be deleted from regions, unless            
the only one of that type.                                                      


                                                                      62
                   15.  MAP ANALYSIS                                     
                       =============
 
                                                                                
                                                                                
This chapter describes how you can find out more about the attribute data       
displayed on a map.                                                             
                                                                                
                                                                                
                                                                                
                                                                                

 15. 1 Introduction                                      
       ------------
 
Selecting ANALYSE MAP DATA from the main map menu enables further analysis      
of a displayed map (with attribute data).                                       
                                                                                
The following menu appears:                                                     
                                                                                
INTERROGATE MAP DATA                                                            
GENERATE MAP REPORT ON FILE OZGIS.OUT                                           
DISPLAY ATTRIBUTE STATISTICS                                                    
                                                                                

 15. 2 Map Reports                                       
       -----------
 
                                                                                
An option is available to write a full map report (giving details of            
the displayed items, their attribute values and class numbers) on the file      
OZGIS.OUT                                                                       
                                                                                

 15. 3 Attribute Data Statistics                         
       -------------------------
 
                                                                                
The statistics of displayed attributes can be computed and displayed            
under user control.                                                             
                                                                                
The following statistics are computed for a simple attribute:                   
                                                                                
      -  minimum value                                                          
      -  maximum value                                                          
      -  mean value                                                             
      -  median value                                                           
      -  standard deviation                                                     
      -  skewness                                                               
      -  kurtosis                                                               
                                                                                
For pairs of attributes (bi-variate displays) the above statistics              
are computed for each attribute, as well as                                     
                                                                                
      -  correlation coefficient                                                
and   -  regression polynomial coefficients (to order 3).                       
                                                                                


                                                                      63

 15. 4 Map Interrogation                                 
       -----------------
 
                                                                                
When a map has been displayed, it is possible to interrogate the map            
data interactively.                                                             
                                                                                
The actual menu depends on the type of map, but is of the form:                 
                                                                                
LIST DATA FOR A CLASS RANGE                                                     
LIST DATA FOR NAMES TYPED AT TERMINAL                                           
LIST DATA FOR ITEMS IN A NAMES FILE                                             
LIST DISPLAYED SITES                                                            
LIST QUANTISATION SITES                                                         
LIST SITES WITHIN WINDOW SELECTED WITH BOX-CURSOR                               
LIST SITES WITHIN DIGITISED POLYGON                                             
LIST SITES WITHIN CIRCLE, TYPED IN RADIUS                                       
LIST SITES WITHIN CIRCLE, CURSOR SELECTED RADIUS                                
                                                                                
                                                                                
The details generated by interrogation are the names of the zones,              
lines or sites, the values of the displayed attributes (one value for           
single variate displays, and two for bivariate) and their assigned class        
number.  The options for interrogation are:                                     
                                                                                
                                                                                
   (a)  class number range                                                      
                                                                                
        -  items (zones, lines or sites) within a specified range of class      
           numbers.                                                             
                                                                                
   (b)  single item identification                                              
                                                                                
        -  zone line or site selected by entering its name at the keyboard.     
                                                                                
   (c)  set identification                                                      
                                                                                
        -  items selected by a names file, items in map, or items in            
           quantisation lists.                                                  
   (d)  Lists                                                                   
                                                                                
        -  The names of all the displayed items are held in one list.           
           Each attribute stream has an associated list of items that are       
           being quantised.                                                     
                                                                                
   (e)  Interactive selection                                                   
                                                                                
        -  The "box cursor" can be used to describe a rectangular region to     
           select items.  The selection of zones and lines is either by         
           all minimum bounding rectangles (MBR) of the items that fall         
           completely within the cursor window or MBRs that intersect           
           the window.  Sites (and zone centroids) are selected by points       
           that lie inside the window.                                          
                                                                                


                                                                      64
                   16. OzData DATA PREPARATION                           
                       =======================
 
                                                                                
                                                                                
                                                                                
This chapter describes options to prepare data for display and analysis.        
                                                                                
                                                                                
                                                                                
                                                                                

 16. 1 Introduction                                      
       ------------
 
The raw data are input to the system using the OzEnter program. However, the    
data often need further processing. Also, some data needed within the system    
cannot be specified as data files and need to be prepared.                      
                                                                                
These facilities are provided by the OzData program.                            
                                                                                
The main menu is of the form:                                                   
                                                                                
PROCESS ATTRIBUTE FILES                                                         
PROCESS GEOGRAPHIC FILES                                                        
PROCESS NAMES FILES                                                             
OUTPUT EXTERNAL DATA FILES                                                      
                                                                                

 16. 2 Attribute Files                                   
       ---------------
 
                                                                                
The PROCESS ATTRIBUTE FILES menu is:                                            
                                                                                
FORM ATTRIBUTES WITH ARITHMETIC EXPRESSIONS                                     
AMALGAMATE ATTRIBUTE DATA FOR AN COMBINE FILE                                   
                                                                                
                                                                                
A new attribute file can be generated from an attribute file and a              
combine file by selecting AMALGAMATE ATTRIBUTE DATA FOR AN COMBINE FILE.        
                                                                                
The combine file defines new zones (or site catchments)                         
in terms of the names referenced by the attribute file.                         
                                                                                
For example, you may define sales territories in terms of postal districts      
and put the definition in a combine file (manually or via OzTerr). You would    
then amalgamate both the geographic file of postal district boundaries and      
any attribute files based on postal boundaries to produce files for             
mapping.                                                                        
                                                                                
                                                                                
                                                                                
Attributes can also be derived from existing attributes by applying             
arithmetic operations to the attribute values via FORM ATTRIBUTES WITH ARITHMETI
                                                                                
A common application is preprocessing Census data before display to form        


                                                                      65
the desired attributes.                                                         
                                                                                
Attributes are identified by the character # followed by a number,              
indicating the sequential position of the attribute on the input file           
e.g. #10 represents the tenth attribute).  An example of an expression          
to form a composite attribute is:                                               
                                                                                
                 (#1+#2)/2 > 0 < 1000                                           
                                                                                
This creates a new attribute whose values are half the sum of the values        
from the first and second attributes on the input file.  Any valid              
arithmetic expression is acceptable.  The output values are limited to          
the given range.                                                                
                                                                                
Functions available are:-                                                       
                                                                                
      LOG10  :  common logarithm                                                
      SQRT   :  square root                                                     
      ABS    :  absolute value                                                  
      EXP    :  exponential                                                     
      SIN    :  sine                                                            
      COS    :  cosine                                                          
                                                                                
Functions removed from the PC version are:                                      
                                                                                
      LOG    :  natural logarithm                                               
      AINT   :  truncation                                                      
      TAN    :  tangent                                                         
      ATAN   :  arc tangent                                                     
      SINH   :  hyperbolic sine                                                 
      COSH   :  hyperbolic cosine                                               
                                                                                
Pi is referred to as PI.                                                        
                                                                                
Operators are:                                                                  
                                                                                
   +  addition                                                                  
   -  subtraction                                                               
   *  multiplication                                                            
   /  division                                                                  
   >  greater than or equal to                                                  
   <  less than or equal to                                                     
                                                                                
Expressions are evaluated left to right and have a limit of 70                  
characters.  Parentheses should be used to ensure there are no                  
ambiguities.                                                                    
                                                                                
The user must give a 30 character attribute description and 10 character        
units description for each new attribute that is generated.                     
                                                                                

 16. 3 Geographic Files                                  
       ----------------
 
The menu is of the following form:                                              
                                                                                
SUBSET FOR ZONES LIST                                                           
SUBSET FOR LINES LIST                                                           


                                                                      66
SUBSET FOR SITES LIST#                                                          
AMALGAMATE ZONES FOR A COMBINE FILE                                             
JOIN LINE SEGMENTS FOR POLYGONS                                                 
SIMPLIFY (THIN) LINE SEGMENTS                                                   
                                                                                
Often the geographic region covered by a geographic file will be much larger    
than is required. Geographic files can be subset (windowed) on the basis of     
a list of required display items (zones, sites, lines).                         
      - items in a names file                                                   
      - items in an attribute file                                              
      - items within a window selected with the cursor from a displayed file    
                                                                                
Line segments can be simplified to reduce the number of points that             
have to be processed.  This is used to speed up display where the               
resolution of the digitised data are higher that that needed for display        
terminals.                                                                      
                                                                                
Line segments that form polygons can be joined together into long segments.     
Where many short segments are used this process, in conjunction with            
simplification, can sustantially reduce the disk storage required and speed     
processing.                                                                     
                                                                                
The zones in a geographic file can be amalgamated according to a combine        
file to generate a new geographic file.  The new file contains the new          
zones.  The same combine file can be used to generate attribute data for        
the same new zones. For example, you may amalgamate basic Census zones into     
zones at a higher level or into sales territories.                              

 16. 4  Names Files                                      
       ------------
 
Names files give lists of items (zones, sites,lines) that are to be processed.  
These lists can be generated from other types of files. These options are       
particularly useful when the names files are to be modified.                    
                                                                                
The menu is of the form:                                                        
                                                                                
SAVE ATTRIBUTE FILE NAMES AS A NAMES FILE                                       
SAVE GEOGRAPHIC FILE ZONES AS A NAMES FILE                                      
SAVE GEOGRAPHIC FILE LINES AS A NAMES FILE                                      
SAVE GEOGRAPHIC FILE SITES AS A NAMES FILE                                      
EDIT A NAMES FILE                                                               
                                                                                
For example, you may output the names from a Census attribute file to a         
names file, edit it with a word processor and the use it to subset a            
census boundary (geographic) file to produce the desired map region.            
                                                                                

 16. 5  Output to Data Files                             
       ---------------------
 
Options are provided to output internal files as data files so they can be      
modified with word-processors for further processing.                           
                                                                                
The menu is of the following form:                                              
                                                                                
GENERATE ATTRIBUTE TEMPLATE DATA FILE                                           
OUTPUT NAMES DATA FILE                                                          


                                                                      67
OUTPUT ATTRIBUTE FILE IN SIMPLE (SAS) FORMAT                                    
OUTPUT COMBINE DATA FILE                                                        
                                                                                
Names files can be editted to change the lists of items used for processing.    
                                                                                
Attribute files can be output in simple database format.                        
                                                                                
Combine files can be modified as part of the definition of territories and      
sites.                                                                          
                                                                                
Attribute templates can be generated for preparation of attribute data with     
a word-processor. This is also useful for displaying new boundary data when     
you have no attribute file. The file can be input with OzEnter as a database    
format attribute file.                                                          

 16. 6 Palette Files (Removed from system)               
       -----------------------------------
 
Palette files have been removed from the system until display systems with more 
than 256 colours are available.                                                 
                                                                                
Palettes are generated by selecting colours for the elements of a               
palette shown on the screen.  The colours can be selected in the                
following ways:                                                                 
                                                                                
      -  by entering blue, green and red values.                                
                                                                                
      -  by reference to another palette                                        
                                                                                
      -  by reference to a colour names file                                    
                                                                                
      -  by reference to a colour cross-section displayed in the map area       
         of the screen.                                                         
                                                                                
After colour selection, the palette can be saved as a file.                     
                                                                                
   An existing palette file can be modified to produce a new file, by           
   displaying it and adding or deleting elements.                               

 16. 7 Colour Names Files  (Removed from system)         
       -----------------------------------------
 
   Colour names files are generated by typing in a name and then selecting      
   the corresponding colour in the ways described above for selecting           
   colours for palettes.  An existing colour names file can be modified.        


                                                                      68
                   17. OzZone BUILDING ZONES FROM SEGMENTS               
                       ===================================
 
                                                                                
                                                                                
                                                                                
Geographic data, such as Census boundaries, are often supplied as lines which   
have to be connected to form polygons.                                          
                                                                                
This chapter describes the OzZone program which carries out this zone building  
process and outlines common preprocessing of this type of data.                 
                                                                                
                                                                                
                                                                                

 17. 1 Use                                               
       ---
 
Zone boundary data can be supplied either as the complete set of points for the 
outsides of each polygon or as the line segments that make up the boundaries.   
Most segments will be common to two polygons so only about half the number of   
points are required. The segment form also allows zones to amalgamated into     
larger zones (by dropping internal segments) and to be thinned (by dropping     
excess points).                                                                 
                                                                                
The segments form of data is preferred to polygon formats.                      
                                                                                
The OzZone program takes line segments and joins the ends together to form      
polygons. The names of the zones on each side of the segments are used to       
derive the zone names.                                                          
                                                                                
Complex polygons are handled. Zones can be made up of many polygons, both       
disjoint polygons and polygons within polygons. The display order of the        
polygons are calculated so e.g islands within lakes within zones all appear.    
                                                                                
The OzZone program has been implemented as a separate program to provide        
maximum capacity on the PC.                                                     
                                                                                
It is usual to line simplify (thin) the segments before building as many        
digitised boundary files (e.g. census) are at a much higher resolution than     
require for the display. Joining of line segments and further thinning may      
follow.                                                                         
                                                                                
If the message"TOO MANY POINTS IN POLYGON" appears you will have to line        
simplify your data.                                                             

 17. 2 Faulty Digitised Data                             
       ---------------------
 
The algorithm assumes that the segments have been produced on a proper          
digitising system and are correct e.g. it is assumed that end-points meet and   
the segments do not cross. Problems such as repeated segments, missing segments 
etc may cause problems. Ensure you use the program with trace turned on. If     
necessary turn on debug and look at the OZGIS.OUT file.                         
                                                                                
Use the file interrogation option to find the statistics on the geographic file 
e.g. the number of zones.                                                       


                                                                      69
                                                                                
OzData can be used to generate a prototype attribute file (simple format) from  
the zones in the geographics file and hence get some test data that can be      
entered via OzEnter to form an attribute file. Displaying both files with       
OzCensus will allow the file to be checked.                                     
                                                                                

 17. 3 Example                                           
       -------
 
The procedure can be demonstrated with any of the geographic data files:        
                                                                                
First input the geographic data file and give it a temporary name:              
                                                                                
Run OzEnter, select INPUT GEOGRAPHIC FILES and then INPUT A STANDARD FORMAT     
GEOGRAPHIC FILE. Use the test data file LOWE-G and give the new file name as    
TEMP1.                                                                          
                                                                                
Next line simplify the line segments to drop points:                            
                                                                                
Start OzData, select PROCESS GEOGRAPHIC FILES and then SIMPLIFY (THIN) LINE     
SEGMENTS. The input file is the one just entered i.e. TEMP1 and output the new  
one as TEMP2. Simplify according to the size of the final map on the screen     
e.g. give a value of 100 to throw away a lot of the data points e.g. if you     
have a super VGA at 1024 X 768 you could use 750.                               
                                                                                
Now use OzZone to build the polygons structure from the lines.                  
                                                                                
The menu is:                                                                    
                                                                                
BUILD ZONES FROM LINE SEGMENTS INTO NEW GEOGRAPHIC FILE                         
BUILD ZONES FROM LINE SEGMENTS INTO NEW DATA FILE                               
                                                                                
The usual option is BUILD ZONES FROM LINE SEGMENTS INTO NEW GEOGRAPHIC FILE.    
                                                                                
Give the input geographic file as the simplified file TEMP2 and output it as    
TEMP3.                                                                          
                                                                                
Finally use OzGIS to display the result (using attribute file LOWE1 and         
geographic file TEMP3).                                                         


                                                                      70
                   18. MAP PROJECTIONS                                   
                       ===============
 
                                                                                
                                                                                
This chapter describes the options in the OzProj program for converting         
geographic files between coordinate systems.                                    
                                                                                
                                                                                
                                                                                
                                                                                

 18. 1 Introduction                                      
       ------------
 
OzProj is a program that will process a geographic file to form a new           
geographic file converting either from (Longitude,Latitude) to a projection     
or in the reverse direction.                                                    
                                                                                
Often projections will not be of concern, as map data will be used as supplied. 
However, if data comes from several sources in different projections, the files 
may have to be converted to a common coordinate system.                         
                                                                                
You will have to have a basic knowledge of the projection you want to use       
e.g. that AMG is UTM with the Australian Spheroid and a false origin            
(500000,10000000).                                                              
                                                                                
OzProj is based on public domain software from USGS.                            
                                                                                
The main menu is:                                                               
                                                                                
CHOOSE FROM PROJECTION SET 1                                                    
CHOOSE FROM PROJECTION SET 2                                                    
CHOOSE FROM SPHEROID SET 1                                                      
CHOOSE FROM SPHEROID SET 2                                                      
DEFINE NON-STANDARD UNIT                                                        
WRITE PROJECTION DEFINITION INTO GEOGRAPHIC FILE                                
TRANSFORM LAT / LONG FILE TO PROJECTION                                         
TRANSFORM PROJECTION FILE TO LAT / LONG                                         
DISPLAY PROJECTION PARAMETERS FOR GEOGRAPHIC FILE                               
                                                                                

 18. 2 Precision                                         
       ---------
 
Vertices are stored in single precision in OzGIS (there is not enough memory on 
the PC to do anything else). This means an accuracy of seven digits, so some    
values may not be accurate e.g. UTM may be a few metres out.                    

 18. 3 Latitude / longitude                              
       --------------------
 
Latitude / longitude data must be given with units degrees.                     
                                                                                
Latitudes are negative in the Southern hemisphere.                              
                                                                                
Usual value ranges are:                                                         


                                                                      71
Longitude -180 to +180                                                          
Latitude  -90  to +90                                                           
                                                                                
Note that the X value in data files is the longitude.                           
                                                                                
examples: (-100.0,50.0) i.e. longitude -100, latitude 50                        
          (145.0, -42.0) a point in Tasmania                                    

 18. 4 Projections                                       
       -----------
 
Several projections are supported:                                              
                                                                                
Albers Conical Egual Area                                                       
Azimuthal equidistant                                                           
Equidistant Conic                                                               
Equirectangular                                                                 
Gnomic                                                                          
Lambert Conformal Conic                                                         
Lambert Azimuthal Equal Area                                                    
Mercator                                                                        
Miller Cylindrical                                                              
Orthographic                                                                    
Polyconic                                                                       
Stereographic                                                                   
Transverse Mercator                                                             
Sinusoidal                                                                      
State Plane (USA) (NOT SUPPORTED YET)                                           
Universal Transverse Mercator                                                   
Van der Grinten                                                                 

 18. 5 Ellipsoids                                        
       ----------
 
Several spheroids are available. The default is either Clarke 1866 or the       
6370997 metre sphere where a radius is asked for.                               
                                                                                
MERIT 1983                                                                      
GRS 1980(IUGG, 1980)                                                            
IAU 1976                                                                        
Airy 1830                                                                       
Australian Natl, S. Amer., IAU 64                                               
GRS 67(IUGG 1967)                                                               
Bessel 1841                                                                     
Clarke 1866                                                                     
Clarke 1880 mod.                                                                
Everest 1830                                                                    
Hough                                                                           
International 1909 (Hayford)                                                    
Krassovsky, 1942                                                                
Mercury 1960                                                                    
Modified Airy                                                                   
Modified Everest                                                                
Modified Merc 1968                                                              
New International 1967                                                          
Southeast Asia                                                                  
Walbeck                                                                         
WGS 66                                                                          


                                                                      72
WGS 72                                                                          
Sphere of 6370997 m                                                             

 18. 6 Use                                               
       ---
 
The parameters of the projection are stored in the geographic file. When the    
data are first entered the projection is usually set to 'undefined', unless it  
is known e.g. Census boundary data are usually set to geographic (lat/long      
units degrees) by the OzEnter program.                                          
                                                                                
The first operation is often to define the projection of a new geographic file  
and store the parameters in the file header. Hence you have to                  
choose the projection, spheroid if non-standard, and then the option            
WRITE PROJECTION DEFINITION INTO GEOGRAPHIC FILE.                               
                                                                                
Transformation is to and from lat/long. Hence conversion from one projection to 
another has to take place in two steps.                                         
                                                                                

 18. 7 Example                                           
       -------
 
Suppose you have used OzEnter to input a file that you know is UTM for zone     
number 20 and you want to convert it to Lambert Conformal.                      
                                                                                
Select CHOOSE FROM PROJECTION SET 1 from the main menu, and then                
select U.T.M. and give the zone number.                                         
                                                                                
Then select WRITE PROJECTION DEFINITION INTO GEOGRAPHIC FILE and give           
the name of your file.                                                          
                                                                                
Your file will now be defined as UTM by having the file header updated.         
                                                                                
Now choose TRANSFORM PROJECTION FILE TO LAT / LONG and give the file names      
to generate a file in latitude / longitude from your original file.             
                                                                                
Then use CHOOSE FROM PROJECTION SET 1 again and choose LAMBERT CONFORMAL CONIC. 
                                                                                
Then using TRANSFORM LAT / LONG FILE TO PROJECTION will give you the            
desired file in Lambert Conformal from the lat/long file to a new file.         
                                                                                


                                                                      73
                   19. OzMap HARDCOPY MAP PRODUCTION                     
                       =============================
 
                                                                                
                                                                                
This chapter describes the OzMap program which allows maps to be output to      
printers, plotters and files.                                                   
                                                                                
                                                                                
                                                                                
                                                                                

 19. 1 Overview                                          
       --------
 
Maps are designed with the interactive OzGIS program and saved as Saved display 
files. These files are then read into the OzMap program and output on the       
desired device or file. Attributes and quantisation can be changed in the usual 
way to produce a series of maps.                                                
                                                                                
Often maps will be previewed on the screen and then output to a plotter,        
printer or file.                                                                
                                                                                
Hardcopy map production is limited by the capabilities of the SCIPLOT package.  
                                                                                
SciPlot produces many graphic file types:                                       
                                                                                
The Postscript file is an ASCII file that may be edited or sent directly to any 
Postscript printer.                                                             
                                                                                
The Encapsulated Postscript file (EPS) and the Computer Graphics Metafile (CGM),
an ANSI standard format file, are files that should not be edited for they      
contain binary information.  EPS and CGM files can be imported directly into    
wordprocessors or other graphical products.                                     
                                                                                
The HP pen plotter file (HPGL) is an ASCII file that can be edited or imported  
into wordprocessors or other graphical products.                                
                                                                                
The WordPerfect file (WPG) is a binary file in WordPerfect's internal graphics  
format.  WPG files are directly importable into the WordPerfect wordprocessor.  
                                                                                
The SciPlot Graphics file is a file in SciPlot's own internal format and is     
used solely as input to the VECTOR program.  This file is a binary file in very 
compact format.  It contains the stream of vectors which represent the figures, 
characters, etc. generated during the execution of the application program.     
VECTOR processes this graphic file and arranges raw vectors in a direction of   
paper motion order before display on dot matrix printers and laserjet printers. 
                                                                                
For Apple LaserWriters, HP pen plotters, and other graphics devices that        
support avector drawing commands directly, ordering is not required and VECTOR  
immediately displays the vectors.                                               
                                                                                
VECTOR's function is to provide a utility to register SciPlot's output on       
plotting devices (dot matrix and laserjet printers) which cannot be supported   
directly without requiring significant system resources.  VECTOR also provides  
interactive preview of graphics files on the screen or bath processing at some  
other time.                                                                     


                                                                      74

 19. 2 Procedure                                         
       ---------
 
The main menu is:                                                               
                                                                                
CHANGE ATTRIBUTES                                                               
DEFINE QUANTISATION (CLASSES)                                                   
DISPLAY DEVICE CHARACTERISTICS                                                  
CHANGE DEVICE FILE                                                              
SELECT ANOTHER SAVED DISPLAY FILE                                               
CHANGE DISPLAY DEVICE                                                           
                                                                                
You must provide the saved_display file name for a map that was prepared        
using OzGIS.                                                                    
                                                                                
You use the F3 key to display the map on the current device. Initially this     
is the screen, but you can use CHANGE DISPLAY DEVICE to send it e.g. to         
a printer. The available devices are selected from the menu:                    
                                                                                
SCREEN                                                                          
PLOTTER METAFILE (for VECTOR program)                                           
PRINTER METAFILE (for VECTOR program)                                           
POSTSCRIPT ASCII FILE                                                           
ENCAPSULATED POSTSCRIPT FILE                                                    
HPGL FILE                                                                       
CGM METAFILE                                                                    
WORDPERFECT FILE                                                                
ONLINE APPLE LASER WRITE,                                                       
ONLINE PLOTTER                                                                  
                                                                                
You can change attributes with CHANGE ATTRIBUTES option and can change the      
quantisation with DEFINE QUANTISATION (CLASSES). Thus you can work through      
a set of attributes in the usual way.                                           
                                                                                
The option SELECT ANOTHER SAVED DISPLAY FILE enables other maps to be displayed.

 19. 3 OzMap Device files                                
       ------------------
 
Several device files are provided to control the appearence of maps on output   
devices. These device files can also be used with OzGIS (they will need minor   
modification for use with EGAs).                                                
                                                                                
You have to use device files that use hatching for polygon fill. The            
configuration section explains the files available. Generally you need to use   
hatching device files that have the same resolution as that used in OzGIS or    
aspects and character sizes may not be suitable.                                
                                                                                
HATCHSV1   - provides polygon display using hatching.                           
HATCHBV1   - hatching for bivariate maps.                                       
CSIMSV* and CSIMBV* - a series of device files that use the red, green and blue 
plotter pens (or screen colours) to simulate the colour sequences; look at then 
on the screen first to decide which ones to try.                                
                                                                                
The hatching device files can of course be modified to define other hatching    
patterns.                                                                       


                                                                      75
                                                                                
The options DISPLAY DEVICE CHARACTERISTICS and CHANGE DEVICE FILE can be        
used to investigate the various device files.                                   
                                                                                

 19. 4 VECTOR Program                                    
       --------------
 
                                                                                
This program enables metafiles produced in the OzMap program to be output to a  
variety of devices and files with such options as rotation and scaling.         
                                                                                
Its easier to use than read about!!                                             
                                                                                
                                                                                
VECTOR has two modes of operation, an interactive mode and a batch mode.        
The batch mode processes command strings from a disk file.  The user can        
include the command filename with the VECTOR command (eg. VECTOR                
command.fil).  Alternatively, the user can wait until VECTOR issues a           
prompt for the type of interaction desired.  The format of the command          
file and a description of the VECTOR.CFG file follows:                          
                                                                                
VECTOR[d:][path][filename[.ext]] [/U]                                           
                                                                                
[d:][path][filename[.ext]] [/U] - Process file which contains                   
filenames of graphics files to be processed in batch mode.  These               
files will be processed one at a time and plotted on the designated             
printer, plotter, or graphics crt device.  As a default, the                    
VECTOR.CFG file will be searched for a process filename.  When a                
filename is specified on the VECTOR command line, the process                   
filename given in VECTOR.CFG file is totally ignored and replaced by            
this new filename.                                                              
                                                                                
/U - This update option is used to override all parameters specified            
in the VECTOR.CFG file. The option initiates an interactive dialog              
with the user to obtain a new set of parameters for VECTOR. The user            
is given the opportunity at the end of the dialog to update the                 
current VECTOR.CFG file with these new parameters.                              
                                                                                
VECTOR.CFG Configuration File.                                                  
                                                                                
The VECTOR.CFG configuration file contains a list of commands that              
define VECTOR processing parameters. Each time VECTOR executes, it              
reads and interprets this file. If the VECTOR.CFG file cannot be                
located, VECTOR will interact with the user from the terminal to set            
up these parameters.                                                            
                                                                                
Format of Configuration File Commands:                                          
                                                                                
Cmd    Option        Description                                                
                                                                                
FILE   =CONS         -Get graphics filenames from console.                      
       =[d:][path][filename[.ext]]- Use this file as a process file             
containing graphics filenames.                                                  
                                                                                
DEVICE =DOT          -Dot Matrix Printer                                        
       =PEN          -HP Pen Plotter                                            
       =JET          -HP LaserJet Printer                                       


                                                                      76
       =WRITER       -Apple LaserWriter Printer                                 
       =CGA          -CGA Color Screen                                          
       =EGA          -EGA Color Screen                                          
       =VGA          -VGA Color Screen                                          
       =HGA          -Hercules Monochrome Screen                                
                                                                                
PORT   =COM1         -Printer/Plotter on Primary Serial Port                    
       =COM2         -Printer/Plotter on Secondary Serial Port                  
       =LPT1         -Printer/Plotter on Primary Parallel Port                  
       =LPT2         -Printer/Plotter on Secondary Parallel Port                
                                                                                
ANGL   =XXX.XX       -Rotation Angle (degrees)                                  
XSCL   =XXX.XX       -X-Axis Scale Factor                                       
YSCL   =XXX.XX       -Y-Axis Scale Factor                                       
XOFS   =XXX.XX       -X-Axis Offset (inches)                                    
YOFS   =XXX.XX       -Y-Axis Offset (inches)                                    
                                                                                
WAIT   =ON           -Wait between Plot Frames                                  
       =OFF          -Do not wait between Plot Frames                           
                                                                                
[When serial port is used for printer/plotter device, following                 
commands are valid]:                                                            
                                                                                
HAND   =SOFT         -Software Handshake (XON/XOFF)                             
       =HARD         -Hardware flow control on DSR line                         
                                                                                
MODE   =195          -Serial Port Mode Set Code, specified in                   
decimal format. 195 = (9600 baud, no parity,                                    
1 stop bit, 8 bit characters)                                                   
                                                                                
- Mode Set Code Description -    [bits]                                         
                                                                                
7     6    5  4     3       2          1       0                                
--Baud Rate-- -Parity-   -Stop Bits-  -Char Length-                             
000 -  110   00 - None 0  -    1      10  - 7 Bits                              
001 -  300   01 - Odd  1  -    2      11  - 8 Bits                              
010 -  600   11 - Even                                                          
011 - 1200                                                                      
100 - 2400                                                                      
101 - 4800                                                                      
110 - 9600                                                                      
111 -19200                                                                      
                                                                                
[When dot matrix printer is used, following commands are valid]:                
                                                                                
PINS   =9           -EPSON (MX-80,FX-80,FX-85,FX-850...)                        
       =24          -RPDON (LQ-800)                                             
                                                                                
HRES   =HIGH        -High Horizontal Resolution                                 
       =LOW         -Low Horizontal                                             
                                                                                
VRES   =HIGH         -High Vertical Resolution                                  
       =LOW          -Low Vertical Resolution                                   
                                                                                
- Printer Resolution Table -                                                    
                                                                                
Printer  Resolution   Vertical  Horizontal                                      
9-Pin     LOW           72         120                                          


                                                                      77
9-Pin     HIGH          216         240*                                        
24-Pin     LOW          180         180                                         
24-Pin    HIGH          180         360                                         
* 240 dot per inch resolution is not available on MX-80.                        
                                                                                
[When HP Pen plotter is used, following plotter initialization                  
command is valid]:                                                              
                                                                                
INIT   =ON           -Send handshake init sequence before plotting              
       =OFF          -No handshake init sequence required                       
                                                                                
When a process file is specified, VECTOR will process multiple graphics         
files in a batch mode. For the individual graphics file, VECTOR processes       
one plot frame at a time, for each file may contain more than one plot          
frame.  For dot matrix and HP LaserJet printers, VECTOR first sorts all         
the vector records in a minimum Y order for one plot frame.  This sorting       
is accomplished by creating an in-memory linked list directory of the           
disk records for the frame.  VECTOR accesses the graphics file randomly,        
bringing in only those records that contain vectors in the current              
process window. These print devices restrict the processing to a paper          
movement order. For HP Pen Plotters, Apple LaserWriters, and crt                
displays, VECTOR can process the vectors directly without any sorting for       
these devices support vector drawing commands.                                  
                                                                                
An inherent difficulty in this sort of processing approach is the limit         
imposed by the processor's memory size. There is an upper bound on the          
size of the graphics plot that can be handled because the linked list           
directory as well as a limited set of the vectors must be memory                
resident.  The exact size limit is difficult to predict because it is a         
function of the number of records in the file, the density of vectors per       
processing window, and the amount of lengthy vectors that must be               
remembered over many processing windows.  The VECTOR.OBJ file on the            
distribution diskette supports 64KB of directory sort space.  If this is        
not enough, a VECTOR.LRG file is included which supports 256KB of               
directory sort space.  Please note that the use of the VECTOR.LRG object        
file will significantly increase the size of the VECTOR.EXE file.               
                                                                                
Features                                                                        
                                                                                
The features incorporated in VECTOR are numerous.  Multiple plot frame          
processing is automatic.  A graphics vector file may be accessed from any       
disk.  Normal FORTRAN I/O is used to read the 128 byte binary records by        
the direct access method.  The VECTOR program will respond to a                 
control-C/Break at any time during execution.  This will terminate the          
current processing task, reset the printer to the top of form, and              
request another task.  Statistics for each plot frame, as well as total         
run statistics are displayed during the execution of VECTOR. For the dot        
matrix type graphics printer, four basic resolutions are provided by            
VECTOR depending on the type of printer attached.  A low resolution mode        
is supported to quickly review the plot with very limited definition.           
This mode is useful for quick turn-around. The high resolution mode takes       
much more time because of hardware constraints, but gives very                  
satisfactory results.  VECTOR also has an on-screen preview capability          
which allows quick identification of graphics files.                            
                                                                                
Error Conditions:                                                               
                                                                                
During the execution of VECTOR, several error messages might be displayed       


                                                                      78
on the terminal.  The only message that is not serious has to do with a         
premature termination of the programs that produced the graphics output         
file. The message reads "Premature End-of-File at Record XXXX". It just         
means that the graphics file was not terminated properly, but all the           
graphics data is valid.                                                         
                                                                                
The second class of messages is serious and should not be ignored. The          
messages are listed along with reasons.                                         
                                                                                
"Error reading graphics file" - means that FORTRAN I/O was unable to read       
the graphics file. The file should be recreated on another disk to              
correct the error condition.                                                    
                                                                                
"File not in graphics format" - means that the speacified file is not in        
SciPlot graphics format. Check to see if the filename is correct or was         
produced by a current version of SciPlot.                                       
                                                                                
"Graphics file too large for memory" - means that the graphics file             
specified cannot be processed by VEACTOR due to inadequate memory sort          
space.                                                                          
                                                                                
"Too many vectors for memory" - means that number of vectors per                
processing window is too dense. Try using the VECTOR.LRG object deck to         
generate the VECTOR.EXE command file.                                           
                                                                                
                                                                                
The VECTOR program supports IBM Graphics, IBM ProPrinters, EPSON MX-80,         
FX-80 with GRAFTRAXPLUS, FX-85, FX-850, LQ-800 dot matrix printers              
connected on an 8-bit parallel I/O interface.  All 8 bits are necessary         
to register the full resolution of the graphics printers.  The resolution       
obtained is a plot frame of (960,1920,2880) pixels over 8 inches in the         
horizontal direction by (1800,2160) pixels over 10 inches in the vertical       
direction. The feature of positioning (1/216th, 1/180th) of an inch is          
used, giving a basic resolution of (120,240,360) by (180,216) pixels per        
inch over a unit square of one inch on a side.  The IBM                         
Graphics/ProPrinter, and the EPSON FX-80,85,850 printers have twice the         
resolution as that of the EPSON MX-80.  The hardware requires double            
passes to absolutely register two dots in adjacent columns for this high        
resolution mode.  This is the reason for the lengthy processing time in         
this mode.                                                                      
                                                                                
There is no paper positioning done by VECTOR. Therefore, the user must          
position the paper before executing the VECTOR program.  This is done           
purposefully to allow plots to be manually positioned.  It is possible to       
imbed plots in full text with a careful alignment of the paper.                 
                                                                                
The HP Pen Plotter, the HP LaserJet, and the Apple LaserWriter are all          
supported by VEACTOR to register the graphics files produced by SciPlot.        
                                                                                

 19. 5 OzMap Example                                     
       -------------
 
You can prepare and print a series of maps as follows:                          
                                                                                
You start by displaying a map with OzGIS and adding any text etc. When it is    
ready you save the map. There are two options for saved displays; either can be 
used but when saved for hardcopy output the screen is not saved so takes less   


                                                                      79
disk space.                                                                     
                                                                                
The OzMap program is then started.                                              
                                                                                
The name of the saved map file is given and a HARDCOPY! device file chosen.     
Use the default one initially.                                                  
                                                                                
Type F3 to display the map on the screen.                                       
                                                                                
Now select CHANGE DISPLAY DEVICE                                                
                                                                                
choose the printer metafile via PRINTER METAFILE (for VECTOR program)           
                                                                                
Type F3 to output the map to the file; give the file name e.g. phred.           
                                                                                
Type F10 to exit OzMap.                                                         
                                                                                
Type VECTOR to execute the program.                                             
                                                                                
Accept all default values (dot matrix printers) and give the Graphics file as   
phred.hrd (note the file extension).                                            
                                                                                
The map will be printed.                                                        

 19. 6 Fitting Maps on the Page                          
       ------------------------
 
If you find that maps printed on-line are not appearing neatly on the           
page you should output maps as meta-files and use the VECTOR program            
to print / plot them.                                                           
                                                                                
The developers, MicroGlyph Systems, have supplied the following:                
                                                                                
     The Apple LaserWriter and the HP Pen Plotters (7440,                       
7470,7475,7550) all require special attention. In order to                      
register a plot frame correctly, it is necessary to use proper                  
offsets and axes dimensions. The Apple LaserWriter must have at                 
least a .25 inch left margin and a .5 inch bottom margin                        
reserved. The HP Pen Plotters all have different basic plot                     
frame parameters.                                                               
                                                                                
     Two tables have been prepared which will allow the user to                 
have a portrait layout or a landscape layout for plot frames.                   
The ANGLE and XTRANS/YTRANS                                                     
arguments will be used from these two tables to obtain the                      
desired layout for plotting. The x-axis and y-axis lengths from                 
the tables serve as limits to the plot area. The DEMO.FOR program               
reflects the use of the PORTRAIT layout parameters from the tables.             
If VECTOR is used to register a graphics file (which has been                   
produced by using VECDEV=10) for any device other than an EPSON                 
dot matrix printer, then the correct layout parameters for that                 
destination device must be used to guarantee correct registration.              
The following tables contain the correct parameters for Portrait                
or Landscape layouts:                                                           
                                                                                
                                                                                
                                                                                
                    Portrait Layout Parameters                                  


                                                                      80
                                                                                
                                                                                
 -------------------------------------------------------------------            
| Device   Device      Paper  ANGLE X-Axis   Y-Axis XTRANS  YTRANS  |           
| Code     Type        Size   Degs  Length   Length Offset  Offset  |           
 -------------------------------------------------------------------            
    10     Epson,HPLJ 8.5x11   0.0   8.0     10.0     0.0     0.0               
    11,20  Apple LW   8.5x11   0.0   8.0     10.0     0.25    0.50              
    12     EPS File   8.5x11   0.0   8.0     10.0     0.0     0.0               
    13,21  HP-7470A    US/A   90.0   7.497   10.094  10.094   0.0               
    13,21  HP-7470A   MET/A4  90.0   7.497   10.682  10.682   0.0               
    13,21  HP-7475A    US/A   90.0   7.803   10.158  10.158   0.0               
    13,21  HP-7475A    US/B   90.0  10.158   16.306  16.306   0.0               
    13,21  HP-7475A   MET/A4  90.0   7.566   10.818  10.818   0.0               
    13,21  HP-7475A   MET/A3  90.0  10.818   15.834  15.834   0.0               
    13,21  HP-7550A    US/A   90.0   7.683    9.966   9.966   0.0               
    13,21  HP-7550A    US/B   90.0   9.966   16.121  16.121   0.0               
    13,21  HP-7550A   MET/A4  90.0   7.447   10.652  10.652   0.0               
    13,21  HP-7550A   MET/A3  90.0  10.652   15.649  15.649   0.0               
    14     CGM File   8.5x11   0.0   8.0     10.0     0.0     0.0               
    15     WPG File   8.5x11   0.0   8.0     10.0     0.0     0.0               
                                                                                
                                                                                
                    Landscape Layout Parameters                                 
                                                                                
                                                                                
 -------------------------------------------------------------------            
| Device   Device      Paper  ANGLE X-Axis   Y-Axis XTRANS  YTRANS  |           
| Code     Type        Size   Degs  Length   Length Offset  Offset  |           
 -------------------------------------------------------------------            
    10     Epson,HPLJ 8.5x11  90.0   10.0     8.0     8.0     0.0               
    11,20  Apple LW   8.5x11  90.0   10.0     8.0     8.25    0.50              
    12     EPS File   8.5x11  90.0   10.0     8.0     8.0     0.0               
    13,21  HP-7470A    US/A    0.0  10.094    7.497   0.0     0.0               
    13,21  HP-7470A   MET/A4   0.0  10.682    7.497   0.0     0.0               
    13,21  HP-7475A    US/A    0.0  10.158    7.803   0.0     0.0               
    13,21  HP-7475A    US/B    0.0  16.306   10.158   0.0     0.0               
    13,21  HP-7475A   MET/A4   0.0  10.818    7.566   0.0     0.0               
    13,21  HP-7475A   MET/A3   0.0  15.834   10.818   0.0     0.0               
    13,21  HP-7550A    US/A    0.0   9.966    7.683   0.0     0.0               
    13,21  HP-7550A    US/B    0.0  16.121    9.966   0.0     0.0               
    13,21  HP-7550A   MET/A4   0.0  10.652    7.447   0.0     0.0               
    13,21  HP-7550A   MET/A3   0.0  15.649   10.652   0.0     0.0               
    14     CGM File   8.5x11  90.0   10.0     8.0     8.0     0.0               
    15     WPG File   8.5x11  90.0   10.0     8.0     8.0     0.0               
                                                                                
                                                                                


                                                                      81
                   20. OzTerr TERRITORY DEFINITION                       
                       ===========================
 
                                                                                
                                                                                
This chapter describes the OzTerr program which can be used to define           
territories in terms of zones (polygons) in some displayed base map.            
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                
Usually territories are to be developed from base zones according to some       
criterion;  e.g. Sales territories should all have similar sales potential;     
e.g. School districts should have similar numbers of children.                  
                                                                                
The operations are as follows.                                                  
                                                                                
     A base map is displayed:  Usually this will be a standard geographic       
     file (e.g. Melbourne postcodes).  Basic OzGIS facilities are used          
     to subset files if non-standard regions are required.                      
                                                                                
     Specification of territories:  Each territory has a unique 10              
     character name.  Zones are assigned off the screen with the cursor.        
     Zones can be moved between territories and deleted.  Territories can       
     be defined or deleted at any time.                                         
                                                                                
     Specification of a base-map attribute file:  Territory attributes are      
     continually calculated by adding the values for the base zones in each     
     territory.  The derived values are quantised (usually sequential           
     colour 121 class method), the territories coloured, and a legend and       
     histogram of sorted values displayed. There can be no missing data.        
                                                                                
     Zones can be shuffled according to the displayed territories attribute     
     values to meet the assignment criteria  while watching the legend          
     and histogram.                                                             
                                                                                
     When territory assignment is complete, the definition is output as a       
     combine file.                                                              
                                                                                
The initial menu is:                                                            
                                                                                
START NEW SET OF TERRITORIES INTERACTIVELY                                      
START NEW SET OF TERRITORIES FROM COMBINE FILE                                  
                                                                                
This gives the choice of starting a new set of territories by selecting         
regions with the box-cursor, or reading in a pre-defined set of territories off 
a combine file that is probably the result of a previous run of OzTerr.         
                                                                                
the full menu now appears:                                                      
                                                                                
TUTORIALS & SYSTEM INFORMATION                                                  
START NEW SET OF TERRITORIES INTERACTIVELY#4001                                 
START NEW SET OF TERRITORIES FROM COMBINE FILE#4002                             
DISPLAY TERRITORY NAMES                                                         
DEFINE NEW TERRITORY                                                            
DELETE A TERRITORY                                                              


                                                                      82
ADD ZONES SELECTED WITH BOX-CURSOR TO A TERRITORY                               
ADD A ZONE SELECTED WITH CURSOR TO A TERRITORY                                  
DELETE ZONES SELECTED WITH BOX-CURSOR FROM A TERRITORY                          
DELETE A ZONE SELECTED WITH CURSOR FROM A TERRITORY                             
CHANGE BASE ZONE ATTRIBUTES                                                     
CHANGE THE QUANTISATION METHOD                                                  
OVERLAY MARKERS FOR SITES IN GEOGRAPHIC FILE                                    
OVERLAY NAMES FOR SITES IN GEOGRAPHIC FILE                                      
OVERLAY LINE SEGMENTS FROM A GEOGRAPHIC FILE                                    
OUTPUT TERRITORY NAMES AS GEOGRAPHIC FILE                                       
OUTPUT TERRITORIES AS COMBINE FILE                                              
                                                                                
You have to type F3 whenever you want to see the quantisation applied to the    
map.                                                                            
                                                                                
You define territories using the options:                                       
                                                                                
DISPLAY TERRITORY NAMES                                                         
DEFINE NEW TERRITORY                                                            
DELETE A TERRITORY                                                              
                                                                                
                                                                                
Usually you are trying to balance territories e.g. you may display an           
attribute that is number of customers and the try to give each salesman         
a territory with about the same number of customers. To  do this you            
define the correct number of territories making a guess at their size           
and then shuffle the zones between the territories while monitoring             
the results by typing F3 to display the map. The options relevant to            
modifying territories are:                                                      
                                                                                
ADD ZONES SELECTED WITH BOX-CURSOR TO A TERRITORY                               
ADD A ZONE SELECTED WITH CURSOR TO A TERRITORY                                  
DELETE ZONES SELECTED WITH BOX-CURSOR FROM A TERRITORY                          
DELETE A ZONE SELECTED WITH CURSOR FROM A TERRITORY                             
                                                                                
You can add overlays to the displayed map to provide "navigation" with:         
                                                                                
OVERLAY MARKERS FOR SITES IN GEOGRAPHIC FILE                                    
OVERLAY NAMES FOR SITES IN GEOGRAPHIC FILE                                      
OVERLAY LINE SEGMENTS FROM A GEOGRAPHIC FILE                                    
                                                                                
                                                                                
Finally the territory definitions can be output to a combine file that can      
be used in OzData to amalgamate the base zones and related attributes to        
get a geographic and attribute file for mapping by using the option             
OUTPUT TERRITORIES AS COMBINE FILE.                                             
                                                                                
                                                                                
You can also output a points geographic file that can be used as an overlay     
to label the territories on a map by using                                      
OUTPUT TERRITORY NAMES AS GEOGRAPHIC FILE.                                      
                                                                                


                                                                      83
                   21. ADDRESS MATCHING / GEOCODING                      
                       ============================
 
                                                                                
                                                                                
                                                                                
Address matching enables location data to be mapped where the locations are     
specified as addresses.                                                         
                                                                                
The address matching software is under development. The first version is        
available in this release.                                                      
                                                                                
                                                                                
                                                                                

 21. 1 Introduction                                      
       ------------
 
Many organisations have data which are spatially referenced by addresses, such  
as customer databases.                                                          
                                                                                
These data can be shown on a zones map by accumulating the data within each     
postal district and displaying the results using digitised postal district      
boundaries. Examples are total number of customers and average sales amount.    
                                                                                
Digital data are now becoming available that contain address information e.g.   
the US Census TIGER data. These data enable the locations of the attribute data 
to be extracted as points and maps produced with or without related attribute   
data.                                                                           
                                                                                
The OzGIS system allows digitised road data and their associated addresses to   
be processed. Sets of addresses can be processed to produce geographic files of 
point locations. These point files can then be displayed in the usual ways,     
either as symbols or names as map overlays or as sites sized according to       
some attribute data.                                                            
                                                                                
For example, a bank may want to extract points using the addresses of           
some customers and then map the average monthly account balances.               

 21. 2 Addresses                                         
       ---------
 
An address is made up of three parts, a number, a name and a postal code.       
Examples are:                                                                   
                                                                                
123 Main Street 654321                                                          
Hyde Park                                                                       
12 Funny Farm Drive, Hicksville 2601                                            
                                                                                
1. The number is a simple integer. Common variations such as 22A, 5-6, 5/66 etc 
are not supported. If a number is not given the point will be placed in the     
centre of the geographic feature.                                               
                                                                                
2. The name must be given, and is the main part of the address for matching.    
                                                                                
3. The postal district is an integer number that helps processing in cases      
where the same address name is used in different districts. It need not be      


                                                                      84
given.                                                                          
                                                                                

 21. 3 Data entry                                        
       ----------
 
Lines data can be entered with the OzEnter program. Addresses are supported for 
TIGER data and data in standard form. Other formats will be supported according 
to availability of data and demand.                                             
                                                                                
Only line data is supported as that is what is currently available. Typically   
the data will be roads.                                                         
                                                                                
Two ranges of street numbers will usually be associated with a road, a set of   
odd numbers down one side and even numbers down the other e.g. a digitised line 
segment may have road name "Hollywood Boulevarde" and number ranges 111 to 179  
and 120 to 220.                                                                 
                                                                                
A road may also have one range (e.g. 1 to 200) or no range may be given.        
                                                                                
The order of the road numbers defines the direction of the road. The direction  
does not have to be the same for the odd and even numbers. If two ranges are    
given and one is not odd and the other even, a single range is derived from the 
limits, but the direction must be the same as defined by the two ranges.        
                                                                                

 21. 4 Address Matching                                  
       ----------------
 
An option is provided in the OzData program to match addresses in a data file   
with those in the digitised line data in a geographic file.                     
                                                                                
The major difficulty is the matching of the road names allowing for differences 
in spelling.                                                                    
                                                                                
After a match is found, the number in the given address is used to find the     
distance along the road (using the ranges) and hence a location is calculated.  
                                                                                
The set of addresses are given on a data file that has the following:           
                                                                                
1. An identifier that can be used to attach attribute data to the point and     
which can be used as a label on maps. If no identifier is given the road name   
will be used. This identifier would often be a database primary key.            
                                                                                
2. The road number. If not given the generated point will be the centre of the  
road.                                                                           
                                                                                
3. The road name. Mandatory.                                                    
                                                                                
4. The post (zip) code. Optional.                                               
                                                                                
A geographic file of points is generated. Any addresses that cannot be matched  
are listed on the OZGIS.OUT file.                                               
                                                                                


                                                                      85

 21. 5 Matching Addresses                                
       ------------------
 
                                                                                
Matching takes place on upper case characters i.e. case is not significant e.g. 
"Main St" and MAIN st" match.                                                   
                                                                                
Multiple blanks are removed e.g. "Grand Parade" matches "Grand      Parade".    
                                                                                
A parameter file is used to convert parts of the names. This is commonly used   
to handle abbreviations e.g. ROAD and RD.                                       
                                                                                
Matching is controlled by a level:                                              
                                                                                
Level 1. Every character in the names in the geographic and data files must be  
the same e.g. "PHREDS ROAD" and PHRED ROAD" are not the same.                   
                                                                                
Level 2. Every character of the shorter name must match the other e.g. "phred"  
would match the above two strings.                                              
                                                                                
Level 3. The first word in each name must match e.g.  "Bloggs Street" and       
"Bloggs Ave" match.                                                             
                                                                                
Level 4. Matching is carried out by using derived names e.g. vowels are all     
treated the same, repeated letters are removed, non alphabetic characters are   
all the same.                                                                   
                                                                                
Level 5. Matching uses the "soundex" algorithm                                  
                                                                                
                                                                                

 21. 6 Procedure                                         
       ---------
 
Address matching is an option in the OzData program.                            
                                                                                
                                                                                
When the OzData program is executed the main menu is:                           
                                                                                
TUTORIALS & SYSTEM INFORMATION                                                  
PROCESS GEOGRAPHIC FILES                                                        
PROCESS ATTRIBUTES FILES                                                        
PROCESS NAMES FILES                                                             
OUTPUT EXTERNAL DATA FILES                                                      
ADDRESS MATCHING                                                                
CHANGE DEVICE FILE                                                              
                                                                                
So you choose ADDRESS MATCHING, which displays the menu:                        
                                                                                
EXACT MATCHING FOR POINTS OVERLAYS                                              
MATCH FOR START OF ADDRESS FOR POINTS OVERLAYS                                  
MATCH FOR FIRST WORD OF ADDRESS FOR POINTS OVERLAYS                             
DESPERATION MATCHING FOR POINTS OVERLAYS                                        
EXACT MATCHING FOR SITE MAPPING                                                 
MATCH FOR START OF ADDRESS FOR SITES MAPPING                                    
MATCH FOR FIRST WORD OF ADDRESS FOR SITES MAPPING                               


                                                                      86
DESPERATION MATCHING FOR SITES MAPPING                                          
                                                                                
These options correspond to the 4 matching levels for either point overlays     
or site mapping.                                                                
                                                                                
You have to specify a number of files:                                          
                                                                                
1. the geographic file that contains the roads and the road names and address   
limits                                                                          
                                                                                
2. Your data file containing the addresses to be matched                        
                                                                                
3. A parameter file of abbreviations to help the matching process e.g. AVE is   
defined as the abbreviation for Avenue                                          
                                                                                
4. the name of the geographic file to be generated with the points location     
                                                                                
After you have generated the points geographic file you should check the        
file OZGIS.OUT to see how well the addresses were matched. You may then want    
to change some of the addresses in the data file to improve the hit rate.       
                                                                                
You can now map the data with the OzGIS program. This is covered in other       
chapters, but briefly:                                                          
                                                                                
DISPLAY GEOGRAPHIC FILES (NO ATTRIBUTES) is used to display the points as       
symbols.                                                                        
                                                                                
You would probably then use DEFINE GEOGRAPHIC OVERLAYS and add your roads file  
as a lines overlay and also overlay the names of the points.                    
                                                                                
DISPLAY SITES FOR AN ATTRIBUTE FILE would be used if you have attribute data    
for the points. You would probably add the roads as a lines overlay and the     
identifiers as a names overlay.                                                 
                                                                                
DISPLAY ZONES AND SITES FOR TWO ATTRIBUTE FILES could also be used if you       
want to display other data such as Census data as a zones map underneath        
the points with their attribute data.                                           
                                                                                
The points could of course be added as overlays to any map.                     

 21. 7 Data                                              
       ----
 
You specify the addresses you want to match in a data files with fixed format   
records:                                                                        
                                                                                
10 bytes  Identifier. If blank the road name is used (first 10 bytes)           
                                                                                
10 digits street number (optional)                                              
                                                                                
30 bytes  street name                                                           
                                                                                
10 digits postal (zip) code                                                     
                                                                                
For example, the demonstration file DEMOMTCH.DAT looks like:                    
                                                                                
EXAMPLE ADDRESSES FOR MATCHING - DEMOMTCH.DAT                                   
ADDRESS001         1     GReat north road                    2600               


                                                                      87
                 666     GReat north road                    2600               
JOE BLOGGS       333     GReat north road                    2600               
ADDRESS004               GReat north road                    2600               
                 333     GReat north road                                       
PIZZA KING               GReat north road                                       
ADDRESS007       333     GReat                               2600               
HARRY S          333     GReat north rd                      2600               
ADDRESS009       333     GReet narth read                    2600               
ADDRESS011       666     GReat    north     road             2600               
ADDRESS012       666     Molonglo Gorge                      2600               
ADDRESS013               Molonglo Gorge                                         
                  11     Northbourne Ave                     2602               
ADDRESS015        44     Northbourne Ave                     2600               
ADDRESS016        10     Northbourne Ave                     2600               
ADDRESS017        68     Northbourne Ave                     2600               
ADDRESS018        57     Northbourne Ave                     2600               
ADDRESS019        40     EPPING HWY                                             
ADDRESS020        33     EPPING HWY                                             
                                                                                

 21. 8 Abbreviations parameter file                      
       ----------------------------
 
A parameter file must be given to allow for abbreviations such as ST, AVE, RD   
                                                                                
A sample file from the USA Census TIGER documentaion is provided \OZGIS\USA.PRM 
                                                                                
You should set up your own abbreviation file. The shorter it is the faster will 
be the matching process.                                                        
                                                                                
The first record of the file is a comment, and each following record is:        
                                                                                
30 bytes text                                                                   
10 bytes  abbreviation                                                          
                                                                                
                                                                                
The file must be in upper case, and the abbreviation must be shorter than the   
text string.                                                                    
                                                                                
The demonstration file is DEMOMTCH.PRM:                                         
                                                                                
Address matching parameter file DEMOMTCH.PRM                                    
AVENUE                        AVE                                               
BOULEVARD                     BLVD                                              
CIRCLE                        CIR                                               
DRIVE                         DR                                                
FREEWAY                       FWY                                               
HIGHWAY                       HWY                                               
MOTORWAY                      MTWY                                              
PARKWAY                       PKY                                               
PLACE                         PL                                                
ROAD                          RD                                                
STREET                        ST                                                
                                                                                
                                                                                
                                                                                


                                                                      88

 21. 9 Handling Errors                                   
       ---------------
 
The results of the matching process are written to the log file OZGIS.OUT       
                                                                                
Each data record is listed with either "MATCHED", "DUPLICATE" or "REJECTED".    
When the names match both the data and geographic file  addresses are listed as 
well as the level of the match.                                                 
                                                                                
The output will be of the form:                                                 
                                                                                
                                                                                
 ======= ADDRESS MATCHING AT LEVEL 4 ======                                     
                                                                                
                                                                                
GEOGRAPHIC FILE demoaddr                                                        
ADDRESSES  FILE demomtch                                                        
PARAMETER  FILE demomtch                                                        
                                                                                
MATCHED          333     GReat north road                    2600               
MATCHED          666     GReat    north     road             2600               
NO MATCH         666     Molonglo Gorge                      2600               
NO MATCH          68     Northbourne Ave                     2600               
MATCHED           11      EPPING HWY                            0               
MATCHED           33            EPPING HWY                      0               
NO MATCH          33     EPXXING HWY                            0               
                                                                                


                                                                      89
                   22. OzSpat SPATIAL OPERATIONS (being tested)          
                       ========================================
 
                                                                                
                                                                                
                                                                                
This chapter describes the OzSpatial program that enables a new geographic      
file to be generated that is the result of spatial operations such as union     
and intersection between the spatial objects in two input geographic files.     
                                                                                
                                                                                
                                                                                

 22. 1 Operations                                        
       ----------
 
                                                                                
The operations take place between the objects in two input geographic files,    
with the resultant objects being output to a new geographic file.               
                                                                                
The following operations are supported:                                         
                                                                                
. Intersection of points with polygons                                          
                                                                                
  For example, extract all sightings (points) of the wedgetail eagle within     
  vegetation type 100 (polygons)                                                
                                                                                
  For example extract all retail sites within competitor's store catchments     
  (polygons).                                                                   
                                                                                
  This is a point-in-polygon operation i.e. the points in one file that lie     
  inside any of the polygons in the second file are selected.                   
                                                                                
. Intersection of lines with polygons                                           
                                                                                
  For example, select all roads that are within the franchise area. (then match 
  addresses)                                                                    
                                                                                
  This is a crossing operation i.e. the parts of any lines that cross (are      
  inside of) the polygons in the other file are output.                         
                                                                                
. Intersection of polygons with polygons                                        
                                                                                
  For example, Extract polygons that have soil types (feature codes) 500 to 600 
  and forest trees feature codes 77 to 88                                       
                                                                                
  For example, Extract Census districts within the digitised areas covered by   
  all hospitals.                                                                
                                                                                
  The polygons that are the overlapped parts of any pairs of polygons from      
  the two files are output (an AND operation)                                   
                                                                                
. Union of polygons with polygons.                                              
                                                                                
  For example, Extract polygons that have soil types  500 to 600  or            
  forest trees feature codes 77 to 88                                           
                                                                                


                                                                      90
  Pairs of polygons from the two input files that overlap are merged to         
  form new polygons. Those that do not overlay are output as is.                
                                                                                
. Buffer generation                                                             
                                                                                
  Generation of buffers at a given distance around spatial objects may be       
supported in future releases.                                                   
                                                                                
                                                                                
                                                                                
                                                                                
Two levels of polygons will be supported:                                       
                                                                                
1. Simple polygons                                                              
                                                                                
Single polygons are processed. There is no regard for polygons inside other     
polygons. Polygons with the names OUTSIDE or INSIDE are ignored.                
                                                                                
This will often be all that is required.                                        
                                                                                
These data can have been entered into the system using OzEnter as one           
of the polygonal formats supported (SAS, Atlas etc).                            
                                                                                
2. Complex polygons NOT IMPLEMENTED YET                                         
                                                                                
This handles zones which are made up of any mixture of polygons, some of        
which can be inside others to a considerable depth.                             
                                                                                
The zones will have been formed from line segments by using the OzZone program. 
                                                                                
The results of the polygon processing is a file of line segments that can be    
built into polygons with the OzZone program.                                    
                                                                                

 22. 2 Feature codes                                     
       -------------
 
Processing can take place for a range of feature codes or the whole of the      
files can be processed.                                                         
                                                                                
A new feature code must be specified for the generated objects. Optionally the  
existing feature codes for both files of objects can be added as well.          
                                                                                

 22. 3 Procedure                                         
       ---------
 
When the OzSpat program is executed the menu appears:                           
                                                                                
INTERSECT POINTS (SECONDARY) WITH SIMPLE POLYGONS (PRIMARY)                     
INTERSECT LINES (SECONDARY) WITH SIMPLE POLYGONS (PRIMARY)                      
INTERSECT SIMPLE POLYGONS  WITH SIMPLE POLYGONS                                 
UNION OF SIMPLE POLYGONS  WITH SIMPLE POLYGONS                                  
INTERSECT POINTS  WITH SIMPLE POLYGONS FOR FEATURE CODES                        
INTERSECT LINES  WITH SIMPLE POLYGONS FOR FEATURE CODES                         
INTERSECT POLYGONS  WITH SIMPLE POLYGONS FOR FEATURE CODES                      
UNION OF POLYGONS  WITH SIMPLE POLYGONS FOR FEATURE CODES                       
                                                                                


                                                                      91
You select the appropriate option. You can either process all the geographic    
data or subset it for a feature code range.                                     
                                                                                
Then you have to give the names of the two input geographic files. As indicated 
by the menu items, the primary geographic file is always a file of polygons     
while the secodary geographic file is the points or line segments or polygons.  
                                                                                
You also have to give a name for the geographic file that will be generated.    
                                                                                
You always have to provide a feature code (a positive number) for the           
generated objects, and can optionally have the feature codes from the           
intersected (or unioned) pairs of objects included in the new objects.          
                                                                                
Polygons are not directly generated. If you intersect or form the union of      
polygons with polygons the output is line segments which then have to be        
built into polygons with the OzZone program.                                    
                                                                                


                                                                      92
                   23. OzDigit DIGITISING (being ported from VAX)        
                       ==========================================
 
                                                                                
                                                                                
This chapter desribes the OzDigit program for digitising paper maps to obtain   
data for input into the OzGIS system.                                           
                                                                                
                                                                                
                  DRAFT DOCUMENTATION                                           
                                                                                
                                                                                
                                                                                

 23. 1 Introduction                                      
       ------------
 
Digitising is a tedious, soul-destrying job. If you can, obtain your data       
from commercial or other sources. If you cant, try and get someone else to      
do it for you (but not someone you love!) If all else fails, this program       
will allow you to produce accurately digitised and topologically correct        
geographic data files.                                                          
                                                                                
One IMPORTANT point:                                                            
                                                                                
It is easy to rapidly digitise a map, but it can take a long time to fix        
any digitising errors such as digitising a line twice.                          
                                                                                
Hence......                                                                     
                                                                                
Digitise in a logical, precise way. Do a small amount at a time, process        
the data to check it, and then do some more.                                    
                                                                                
In particular, the first time you try digitising, draw yourself a trivial       
map on a piece of paper and digitise that to work out the procedure.            

 23. 2 Configuration                                     
       -------------
 
Summagraphics compatible digitisers are supported. These plug directly into     
a port in the PC and work by generating Ascii messages to the PC that look      
like keyboard input.                                                            
                                                                                
Configuration involves editing a line in the \ozgis\ozgis.ini file to           
specify the port that is being used.                                            
                                                                                

 23. 3 Files                                             
       -----
 
You specify three files to the OzDigit program:                                 
                                                                                
.  The menu file describes the menu being used and where it is located on the   
    board.                                                                      
                                                                                
.  The digitiser file contains all the current digitised data (see below)       
                                                                                


                                                                      93
.  An output data files is generated that is in standard geographic file        
format and is read into the system with OzEnter.                                
                                                                                
The digitiser file actually contains the names of several other files, which    
you dont usually worry about, but some of which can be modified directly once   
you understand how the digitising process works.                                
                                                                                
These other files all have the same name as the digitiser file. but with        
different extensions. for example:                                              
                                                                                
PHRED.DIG the digitiser file                                                    
PHRED.CPS the control point file                                                
PHRED.FIT the parameters for the transformation                                 
PHRED.DGV the digitised data file                                               
PHRED.ZON the zone/poly names and feature codes file                            
PHRED.LIN the line segment names and feature codes file                         
PHRED.PNT the point names and feature codes file                                
                                                                                

 23. 4 Preparation for Digitising                        
       --------------------------
 
First of all make sure that the paper map to be digitised is in good condition. 
If necessary iron it to make it flat and tape any rips.                         
                                                                                
Fix the map to the digitiser board with tape. Remember that the very edge of the
board may not be "active", so put it away from the edge. If the map is too big  
it can be moved later to do the rest of the digitising i.e. you can digitise it 
in pieces.                                                                      
                                                                                
The map should be close to horizontal on the board.                             
                                                                                

 23. 5 Setting up the Menu                               
       -------------------
 
You control much of the digitising process from a paper menu that you stick     
on the digitiser board.                                                         
                                                                                
If you have a big board you may find that you leave the menu stuck in the       
same place all the time. However, you may find that you often need to           
stick the menu on a corner of the map you are digitising, and may have to       
move it to digitise what is underneath.                                         
                                                                                
You can have different sizes and shapes of menus to allow for fitting it        
on the board according to the shape of the map being digitised.                 
                                                                                
You start by drawing yourself a menu on some paper.                             
                                                                                
The menu has 17 entries:                                                        
                                                                                
the digits 0 to 9                                                               
"POLY" for zone / polygon internal points                                       
"PNT"  for intersection points (or points or nodes)                             
"LINE" for line segments                                                        
"DELP" for delete point                                                         
"DELS" for delete line segment                                                  
"END"  end-of-job, end of number                                                


                                                                      94
                                                                                
You draw the menus on rectangular pieces of paper on a grid:                    
                                                                                
e.g. you may set up a menu of 3 columns and 6 rows as follows:                  
                                                                                
                                                                                
      ----------------------                                                    
      |      |      |      |                                                    
      |  0   |      | END  |                                                    
      |      |      |      |                                                    
      ----------------------                                                    
      |      |      |      |                                                    
      |  1   |  2   |  3   |                                                    
      |      |      |      |                                                    
      ----------------------                                                    
      |      |      |      |                                                    
      |  4   |  5   |  6   |                                                    
      |      |      |      |                                                    
      ----------------------                                                    
      |      |      |      |                                                    
      |  7   |  8   |  9   |                                                    
      |      |      |      |                                                    
      ----------------------                                                    
      |      |      |      |                                                    
      | ZONE | PNT  | LINE |                                                    
      |      |      |      |                                                    
      ----------------------                                                    
      |      |      |      |                                                    
      | DELP | DELS |      |                                                    
      |      |      |      |                                                    
      ----------------------                                                    
                                                                                
The menu boxes should all be the same size.                                     
                                                                                
If you are doing a lot of digitising you will probably draw up several menus    
such as a vertical 1 column, 17 rows menu, a horizontal 1 row 17 columns        
menu and perhaps both 3X6 and 6X3 rectangular menus or a 5x4 menu.              
                                                                                
                                                                                
Before you start digitising you have to stick the menu on the board,            
select the DEFINE DIGITISING MENU option from the main OzDigit menu, and        
digitise the four corners of the menu so the program knows where you have put   
it. You also have to give the number of rows and columns in the menu.           
Finally you give symbol that goes into each each menu location where row        
1 is the top, and column 1 is the left. The symbols are those above, with       
blank being a menu location that is not used.                                   
                                                                                
The menu definition is written on a file and remains current until changed.     
                                                                                
You can move the menu on the board during the digitising process, but you       
then have to redefine the corners. So you usually dont move it if you can       
help it - ever!                                                                 
                                                                                
You use the menu by digitising a point within the square of the item you        
want to select. Numbers, which are identifiers, are selected by digitising      
the digits followed by EOJ.                                                     
                                                                                


                                                                      95

 23. 6 Control points                                    
       --------------
 
When you digitise a point the OzDigit program reads it in digitiser board       
coordinates. These are usually in a range like 0 to 10,000                      
                                                                                
The program has to be able to convert these coordinates to the map coordinates  
such as latitude/longitude or UTM.                                              
                                                                                
This is done by digitising "control points".                                    
                                                                                
These are several points on the map at known map coordinates that are           
digitised at the start of data capture. The program knows both the board and    
map coordinates of each of the points, so can generate a function to transform  
any digitised point to map coordinates.                                         
                                                                                
                                                                                
First of all you select some suitable points on the map where you know the      
actual map coordinates - usually on the map grid. You should use at least four  
points near the corners of the part of the map being digitised and preferably   
at least one near the centre of the map too. You usually mark the points        
on the map with a coloured pen so you can remember which ones you used, and     
number them 1,2,3...                                                            
                                                                                
                                                                                
Next select DEFINE CONTROL POINTS from the menu and define the points in turn   
giving an identifying number and the point in map coordinates (remember that    
for latitude longitude the X value is the longitude). The coordinates are       
given as decimals, and appropriate signs should be used e.g. latitude is        
negative below the equator like -35.0.                                          
                                                                                
The results are stored on a control points file and you can read in an          
existing file and overwrite the values in it.                                   
                                                                                
The digitising software does not use map projections. You can use the OzProj    
program for that purpose.                                                       
                                                                                
                                                                                
Finally you have to digitise the points. You define the numbers by selecting    
from the menu digits followed by EOJ for the control point identifier, and      
then digitise the actual point. The first time you will have to digitise        
all the points, but after that only any that you might have changed.            
                                                                                
The program generates the transformation equation table -> map coordinates      
and prints out a goodness-of-fit. You can accept that or can modify the         
control point definitions.                                                      
                                                                                

 23. 7 Digitising the Map                                
       ------------------
 
The OzDigit program is designed for digitising maps and producing data in       
a correct topological structure of zone-polygon-line where boundary lines       
occur once only (usually) and are shared between the adjacent polygons.         
                                                                                
This requires careful, logical digitising.                                      


                                                                      96
                                                                                
These types of maps are for choropleth mapping e.g. Census maps.                
                                                                                
However, the system can also be used to produce a subset such as just points,   
lines or simple polygons for production of map overlays (e.g. town locations,   
roads) or environmental applications e.g. vegetation type polygons where the    
polygons may not be adjacent.                                                   
                                                                                
You start the digitising process by selecting DIGITISE NEW MAP DATA.            
                                                                                
The procedure for digitising Census type maps is:                               
                                                                                
First of all digitise "nodes" which are the intersection points of all          
the boundary lines. Every node has a number (identifier) which can be           
generated sequentially by the system, but it is recommended that you            
assign your own numbers. You should prepare the map before digitising by        
writing the numbers against every place lines join/cross (some people use       
coloured stickers). Alternatively label each point as you digitise it.          
Ensure that you mark the points so you dont digitise them twice or miss         
any.                                                                            
                                                                                
Next you digitise the boundary lines. All lines start and end on a node.        
While digitising you can keep going along the map lines, but everytime you      
pass through a node you have to be sure that you digitise the node point        
so the program can connect to it. You usually find that you have missed         
labelling a few nodes.  Lines also have numeric identifiers. As before they     
can be automatically assigned but it is recommended that you choose a range of  
numbers that is different to those used for the points and label the map        
either before you start or as you go.  Ensure that you mark lines in some       
way as you go so you dont digitise lines twice and you dont miss any.           
                                                                                
If you have a large map you should digitise complete polygons in a small        
part of the map, ensure it is correct, and then do a bit more, until            
finished.                                                                       
                                                                                
Next you have to digitise internal points in each of the polygons that make     
up the zones. Once again you should label these points carefully, using         
a different range of numbers.                                                   
                                                                                
In all cases you start digitising a map object by choosing the type from        
the digitiser menu i.e. ZONE, INT or LINE, and then the identifying             
number from the digits on the digitiser menu. You then start digitising         
the map data. You can digitise a sequence of objects without returning          
to the menu, in which case the identifying number is incremented for each       
object.                                                                         
                                                                                
The PC display will show the data as it is digitised.                           
                                                                                
When EOJ is selected you are presented with several options for displaying      
and modifying the data.                                                         
                                                                                
                                                                                
While you are digitising, the transformation is used to convert the locations   
to map coordinates.                                                             
                                                                                
The digitised data is usually saved at the end of digitising and can be read    
back in next time.                                                              
                                                                                


                                                                      97
If you are digitising data for overlays you may take a more casual approach     
as you are not concerned that lines can be joined into polygons. You may        
then digitise and allow nodes to be automatically generated. Polygons are       
then likely to be generated as closed lines, with the same node at each end.    
                                                                                
                                                                                

 23. 8 Examining digitised data                          
       ------------------------
 
You can choose the option EXAMINE DIGITISED DATA to plot points, lines          
or zones for ranges of identifying numbers.                                     
                                                                                

 23. 9 Giving Names and Feature codes                    
       ------------------------------
 
Zones (polygons), lines and points are identified by numbers during the         
digitising process.                                                             
                                                                                
If you want to assign attribute data to them when mapping with OzGIS            
program, you have to provide the names that correspond to the object            
identifying numbers.                                                            
                                                                                
You do this by choosing one of:                                                 
                                                                                
DEFINE ZONE NAMES AND FEATURE CODES                                             
DEFINE LINE NAMES AND FEATURE CODES                                             
DEFINE POINT NAMES AND FEATURE CODES                                            
                                                                                
The identifying numbers are written to files, and can be read back in           
and changed.                                                                    
                                                                                
You can also assign one feature code to each polygon, line or point by          
either specifying them individually or assigning a default code.                
                                                                                

 23.10 Forming Polygons / checking                       
       ---------------------------
 
                                                                                
The final product is a data file in standard OzGIS geographic format.           
                                                                                
This is produced by choosing GENERATE GEOGRAPHIC DATA FILE                      
                                                                                
This process involves joining lines into polygons, if required, and             
outputting the topological structure to a file.                                 
                                                                                
Any names defined for zones, lines or points will be used.                      
                                                                                
Errors are detected at this stage and messages are output to the OZGIS.OUT      
file. You need to use display and editing programs to fix any mistakes.         
                                                                                
You  will find that careful analysis is sometimes required to discover          
digitising errors.                                                              
                                                                                


                                                                      98

 23.11 Editing Digitised Data                            
       ----------------------
 
You can choose EDIT DIGITISED DATA to display and modify the data.              
                                                                                
Options are:                                                                    
                                                                                
delete lines, points or zones                                                   
                                                                                
plot lines, points or zones                                                     
                                                                                
renumber intersections or zones                                                 
                                                                                
split lines                                                                     
                                                                                
Change region displayed.                                                        
                                                                                

 23.12 Variations                                        
       ----------
 
                                                                                
Two extra digitising environments are available:                                
                                                                                
1. The table can be simulated by the PC screen and mouse/cursor. This           
can be used for very simple digitising, where your map has to be drawn on       
some clear medium. This also supports digitising boards that simulate a mouse.  
                                                                                
2. Map overlays can be digitised by displaying a geographic file on the         
PC screen as the map to be digitised. Control points are not required           
as the transformation is known and a standard digitiser menu will               
be provided on the screen.                                                      
                                                                                
                                                                                


                                                                      99
                   24. OzCatch RETAIL SITE CATCHMENTS (NOT AVAILABLE YET)
                       ==================================================
 
                                                                                
                                                                                
The OzCatch program enables catchments to be defined as contours around         
retail sites and the attribute data to be extracted from base zones.            
                                                                                
                                                                                
                                                                                
                                                                                

 24. 1 Introduction                                      
       ------------
 
Modules have been developed for site selection on a VAX using RAMTEK display    
systems.                                                                        
                                                                                
This software has to be completely rewritten for the limited PC displays.       
                                                                                
It is uncertain when or if the software will be made available on the PC        

 24. 2  SITE CATCHMENTS                                  
       ----------------
 
The system aims to provide facilities for analysis of sites for the             
 definition of site locations and catchments, the                               
retrieval of data, development of models and display of results.                
                                                                                
The base of the process is the catchment file.                                  
A catchment file holds the definition of several sites.  The sites have         
some common grouping (e.g. all part of the same retail chain) and all fit       
on the same base map.                                                           
                                                                                
A typical analysis would involve several catchment files, e.g. several sets     
of sites each for a different organisations( e.g. several sets, each            
defined on different base maps to increase resolution. )                        
                                                                                
Site definition is carried out for a current set of sites.  These               
sites can be modified and new sites defined.  A base map is always              
displayed and all the current sites must fit on the displayed map.              
                                                                                
Also defined for assistance are any other catchment files relevant to the analys
Site symbols, names and catchments are displayed if they fit on the             
map.  These sites cannot be modified.                                           
                                                                                
A catchment file contains the following information for each site.              
                                                                                
-    site name (10 characters)                                                  
-    site location                                                              
-    site symbol display location                                               
-    site name display location                                                 
-    catchment contours (up to 5)                                               
-    base zones and weights within catchment                                    
-    type of zones.                                                             
                                                                                
A site analysis could be carried out as follows.                                


                                                                     100
                                                                                
Phase 1 - Definition                                                            
                                                                                
Each catchment file has to be defined.                                          
                                                                                
-    A base-map geographic file of suitable size is displayed.                  
                                                                                
-    An old catchment file may be read in for modification.                     
                                                                                
-    Sites are defined by giving a name and location (cursor or typing lat      
     long).  Initial catchment contours are given as circles.                   
                                                                                
-    The results are stored as a catchment file.                                
                                                                                
The zones list in the catchment file can now be output as anames file.          
                                                                                
The names file is passed to OzData, attribute data are retrieved for the site   
catchments, and some basic statistics calculated.  On the basis of              
correlation coefficient and error levels for particular sites, the              
modifications for site catchments are decided.                                  
                                                                                
e.g.   there may be 2 or 3 base maps for Melbourne and                          
others for the country areas, each with different sites on them.                
                                                                                
Phase II - Modification of Catchments                                           
                                                                                
The site catchments (or positions) now have to be modified to obtain better     
agreement with known results.                                                   
                                                                                
-    The base map is displayed again.  Other site catchment files and           
     geographic overlays (e.g. roads) may also be displayed.  Note that the     
     base map could be changed.                                                 
                                                                                
-    the sites are modified.  More contours may be added.  Contours may be      
     replaced with circles of different radii or a replacement digitised.       
                                                                                
-    Zones lists are re-calculated.                                             
                                                                                
-    The new sites are processed by OzData again, and the process repeated      
     if necessary.                                                              
                                                                                
For example,  the base maps could change, say to go from                        
postcodes to collection districts.  Contours would change to get a better       
fit to the client's data.                                                       
                                                                                
Phase III - Zones                                                               
                                                                                
A base map is displayed and the contours overlayed.                             
The pixels within each contour polygon are counted and from the                 
total zone pixel counts and contour weights                                     
a list of zones and weights for each site is generated                          
and stored in the catchment file.                                               
                                                                                
The user has to make sure that the base map extends past the                    
catchment.                                                                      
Note that any type of zones can be used as the contours are                     
stored as lat-long points.                                                      
                                                                                


                                                                     101
Phase IV - Display Preparation                                                  
                                                                                
A base map is displayed that is to be used for the final maps, and current      
catchment file displayed.  All the catchment files are displayed -              
contours, symbols and site names.                                               
                                                                                
Symbols and names in the current catchment file are repositioned with the       
cursor if they conflict with those from other files.                            
Lines are displayed between the symbol and true positions.                      
                                                                                
A new catchment file is generated.                                              
                                                                                
An combine file is generated for retrieval of attribute data for all site       
names.                                                                          
                                                                                
A base map is displayed and the catchment files displayed that are to have      
the same symbol on the maps.                                                    
                                                                                
A geographic file is generated for site symbol display.                         
                                                                                
A geographic file to display the lines between the offset                       
symbol locations and site locations is generated.                               
This file also contains points for site name display.                           
                                                                                
For example,  a base map for the part of Victoria required                      
would be subset from a Victorian postcode map.  All the catchment files are     
displayed and names and symbols moved for the locations where there are two     
close sites.                                                                    
                                                                                
Phase V - Map Production                                                        
                                                                                
A names file is generated from the combine file for                             
all sites that are to be displayed.                                             
                                                                                
-    Data are retrieved from OzData for the names file.                         
                                                                                
-    A map is displayed for either just sites, or sites on quantised map        
     zones.                                                                     
                                                                                
     If there are several sets of sites each file                               
 is added and possibly assigned                                                 
     to a different symbol.                                                     
Note that symbol 1 is the top bit plane, symbol 2 the                           
next down etc.                                                                  
                                                                                
Standard geographic overlays can be added from the geographic                   
files that were generated; sites names, symbols, lines                          
between symbol and true locations.                                              
                                                                                
-    Other geographic overlays, diagrams etc are added.                         
                                                                                
For example,  a map could be displayed by using the Victorian                   
postcode map as a base with postcode attributes, and displaying symbols at      
sites using attributes calculated by OzData.  If potential sites are being      
evaluated, they would be in different geographic files and different            
symbols would be used.                                                          
                                                                                


                                                                     102
                     A. DATA SOURCES                                      
                       ============
 
                                                                                
                                                                                
This appendix lists some of the major suppliers of map data which can be used   
with the OzGIS system.                                                          
                                                                                
                                                                                

  A. 1 General                                           
      -------
 
Data are often available in different formats and at different prices. You      
need to be sure exactly what you want before ordering.                          
                                                                                
If you are ordering Census boundary data you need to consider if you want       
to be able to amalgamate the polygons into bigger regions such as sales         
districts; if so you have to have segments. If you are ordering polygon         
formats (e.g. SAS) you will probably have to get them in a thinned form         
as otherwise the polygons may have too many vertices for the capacity of        
the OzGIS system under DOS. Thinned polygons are often cheaper. Generally,      
segments are preferable as they offer more capabilities, but they must not      
have too many vertices. Generally the system expects to be operating on         
geographic files that have the full zone-polygon-segments structure. Some       
operations are not available on files that were entered as polygons.            

  A. 2 Australia                                         
      ---------
 

  A. 2. 1 Australian Bureau of Statistics                   
          -------------------------------
 
The ABS collects and disseminates enormous volumes of statistics, some of which 
is available on floppy disk and CD ROM for mapping.                             
                                                                                
The major data source is the Census of Population and Housing - by far the most 
extensive source of demographic data available in Australia.                    
                                                                                
The ABS will supply data on floppy disk. Data output from the GeoStats product  
in LAMM format is supported.                                                    
                                                                                
The ABS will supply boundary data for the 1991 Census.                          
                                                                                
Arrangements have been made to obtain test data from the ABS so 1991 Census     
and boundary data will be supported when they become available in               
late 1992.                                                                      
                                                                                
Many publications describing the data are available.                            
                                                                                
Contact:                                                                        
                                                                                
Information Services,                                                           
Australian Bureau of Statistics,                                                
PO Box 10, Belconnen, ACT 2616.                                                 
Phone (06) 252 5402, 252 6627, or 252 6007.                                     


                                                                     103
                                                                                
or any ABS state office.                                                        

  A. 2. 2 AUSLIG data                                       
          -----------
 
The Australian Land Information Group in Canberra can supply                    
the boundaries of the Collection Districts for the 1986 Census.                 
                                                                                
Data are available for each state for:-                                         
      - collection districts                                                    
      - postcodes                                                               
      - Local Government Areas                                                  
      - Statistical divisions                                                   
      - etc                                                                     
                                                                                
Ozenter can process the AUSLIG segments data to produce the OzGIS segments,     
which can then be formed into polygons with OzZone (to reflect                  
the structure of the data e.g. which polygons are inside others).               
                                                                                
The data are extremely detailed, so large files are involved. Hence subsetting, 
segment joining and line simplification are usually used.                       
                                                                                
All data are projection code 0 = latitude-longitude, units degrees.             
                                                                                
Make sure you get census boundaries in SEGMENTS format on floppy disk.          
                                                                                
Other map data are available, but need reformatting for use with OzGIS e.g.     
names file.                                                                     
                                                                                
AUSLIG is also selling postcode boundaries developed in collaboration with      
Telecom.                                                                        
                                                                                
Unfortunately, government policy of cost recovery means that AUSLIG data are    
expensive.                                                                      
                                                                                
Several publications are available.                                             
                                                                                
Contact:                                                                        
                                                                                
AUSLIG SALES (Digital Data), PO Box 2, Belconnen ACT 2616.                      
Phone (06) 252 6389  Fax (06) 251 5446                                          

  A. 3 New Zealand                                       
      -----------
 
The Department of Statistics have a product SAM (Socio-economic Area Mapping)   
and will supply data suitable for mapping on floppy disk.                       
                                                                                
Contact their Information Consultancy Group first.                              
                                                                                
Offices are in Auckland, Wellington, Christcurch and Dunedin.                   
                                                                                
You should be able to obtain boundary data in a format supported within         
OzEnter (e.g. SAS, Gina).                                                       
                                                                                
Population Census data and other attribute data are available in comma          
delimited formats.                                                              


                                                                     104

  A. 4 United Kingdom                                    
      --------------
 
The various agencies are in the process of generating digitised boundary data,  
and there are some private efforts.                                             
                                                                                
Contact:                                                                        
The Office of Population Censuses and Surveys (OPCS),                           
St Catherines House,                                                            
10 Kingsway London                                                              
Phone 071 242 0262                                                              
                                                                                
or:                                                                             
                                                                                
Customer Services,                                                              
General Register Office,                                                        
Ladywell House,                                                                 
Edinburgh.                                                                      
Phone 031 334 0380                                                              
                                                                                

  A. 5 USA Census Data                                   
      ---------------
 
The Census Bureau is the primary source of map data in the USA.                 
                                                                                
They distribute boundary data as TIGER files and Census data as STF1A files.    
                                                                                
The data are distributed on CD-ROM so you need a drive or access to one.        
                                                                                
The Census Bureau has several offices throughout the USA.                       
                                                                                
The 1990 Census TIGER/Line files are available on magnetic tape or tape         
cartridges (IBM 3480 compatible) from Customer Services Branch, Data User       
Services Division, Washington, DC  20233; (301) 763-4100.  FAX:  (301)          
763-4794.  The price is $200 for the first county in a state, plus $25 for      
each additional county in the same state ordered at the same time.  The         
files also are available on CD-ROM disks.  The price per disk is $250; most     
states fit on one disk.                                                         
                                                                                
See the appendix for information on how to use TIGER and STF1A files.           
                                                                                

  A. 6 Canada                                            
      ------
 
Statistics Canada has not answered our letters or FAXes.                        

  A. 7 Others                                            
      ------
 
Attemps to obtain other data from other suppliers has so far failed. The best   
we get is a heap of glossies. Questions we ask in our letters are ignored.      
Requests for test data are either greeted with paranoia or are ignored.         
                                                                                
Most suppliers also sell mapping software, so it is not in their interest       


                                                                     105
to encourage a competitor selling at a fraction of the price. It also does      
not look good when they are selling data at many times the price of the         
software.                                                                       
                                                                                
You will find that you can usually buy map data in one of the formats           
supported by OzGIS.                                                             


                                                                     106
                     B. MAP DATA FORMATS                                  
                       ================
 
                                                                                
                                                                                
This appendix describes the data formats supported by the OzEnter program.      
                                                                                
                                                                                
You obtain your data on a file in a format supported by the OzEnter program,    
and use the appropriate option to read that file and create an OzGIS file       
that can be used for mapping.                                                   
                                                                                
                                                                                
                                                                                
                                                                                

  B. 1 Introduction                                      
      ------------
 
The OzGIS system was designed to accept data from external sources.             
                                                                                
These data may be supplied in standard formats that are supported by the        
OzEnter program.                                                                
                                                                                
If not, data will  have to be reformatted into one of the system formats        
before use.                                                                     

  B. 2 OzGIS Data Formats                                
      ------------------
 
Every type of file has a standard format within OzGIS.                          
                                                                                
The data files have been designed with a simple format which can be easily      
generated on computer systems.                                                  
                                                                                
Most data are held as character files so that they can be generated by          
programs with, for example, database system export procedures, formatted        
FORTRAN write statements, or by a text editor.  The record lengths are up to    
80 bytes long.                                                                  
                                                                                
Each file starts with a comment record of up to 80 characters, which should     
be used to hold a meaningful description of the file.  The OzGIS system         
will display this comment when data files are interrogated, so it is in         
your interest to make the comments meaningful.  This record must contain        
at least one non-blank character.                                               
                                                                                
Data values are entered in record fields that are multiples of 10 bytes.        
The following computer restrictions apply:                                      
                                                                                
     -  Character data (e.g. zone names) are usually left justified and         
        blank filled.  Sorted character strings must conform to the ASCII       
        collating sequence.                                                     
                                                                                
     -  All real values (i.e. with decimal points) can be placed anywhere       
        in the 10 byte fields, but the decimal points must be included.         
                                                                                
     -  All integer values must be right justified in the 10 byte fields.       


                                                                     107
        Their values must be within the range the computer is capable of        
        handling.                                                               
                                                                                
While the file formats are defined as fixed size fields, variable formats can   
be used, but numbers must be delimitted by commas and text fields must          
be enclosed in """" pairs.                                                      
                                                                                
The maximum numbers of some data items that can be handled                      
are system parameters. Refer to the Appendix.                                   

  B. 3 Description of File Formats                       
      ---------------------------
 
The formats for describing the data files in the following sections are         
similar.                                                                        
                                                                                
The number of bytes in the field is given at the start of the line.  If         
there are several values in a format, this condition is indicated               
differently (e.g. 8 x 10 implies eight fields of 10 bytes).                     
                                                                                
The information on the next line is the type of data in a field:                
                                                                                
     byte     = character                                                       
     real     = number containing a decimal point                               
     integer  = number without a decimal point                                  


                                                                     108

  B. 4 Format of attribute files                         
      -------------------------
 

  B. 4. 1 Preprocessing                                     
          -------------
 
Attribute data are often obtained from Census Bureaux. These data are seldom    
what is required, so will need processing by OzData before use.                 
                                                                                
Data often need normalising to allow for the differences in zone sizes. This is 
done by arithmetic operations where new attributes are derived by dividing by   
total population, area etc.                                                     
                                                                                
Also, data often need amalgamation e.g. census age groups to get the required   
group.                                                                          

  B. 4. 2 OzGIS Standard Format                             
          ---------------------
 
Attribute files contain the attribute value of each zone or line or site        
for a number of attributes.  The names must correspond to those defined in      
a geographic file.                                                              
                                                                                
The attribute description is used by OzGIS as a heading in a map                
displaying the attribute.  The units description is used by OzGIS as a          
heading to the class values in the map legend.                                  
                                                                                
For efficient use of the system and to facilitate disc file management,         
files should contain as many attributes as possible (to avoid having            
separate files for each attribute).                                             
                                                                                
Attribute files will usually be prepared by special programs which extract      
data from a data-base and convert attribute values into the OzGIS               
format.                                                                         
                                                                                
     Comment Record:                                                            
     80       byte      comment describing the data                             
                                                                                
     Header Record:                                                             
     10       integer   number of attributes                                    
     10       integer   number of names                                         
     10       real      value used to indicate missing data                     
                                                                                
     Name Records:                                                              
     8 x 10   byte      names, sorted into ascending order                      
                                                                                
Sets of records follow to define the attributes:-                               
                                                                                
     Definition Record:                                                         
     30       byte      attribute description                                   
     10       byte      units description                                       
                                                                                
     Values Records:                                                            
     8 x 10   real      attribute values for zones, lines or sites in name      
                        order                                                   


                                                                     109
                                                                                

  B. 4. 3 Sample attribute file DEMOATTR.DAT                
          ----------------------------------
 
DEMOATTR.DAT   - ATTRIBUTES FOR SIMPLE 3 ZONE TEST MAP                          
         5         6     -9.9                                                   
ABCDEFGHIJZONE 1    ZONE 2    ZONE 3    ZONE 4    ZONE Z                        
FIRST STATISTIC               FIRST UNITS                                       
       1.0       2.0       3.0       4.0       5.0       6.0                    
SECOND STAT                   SECOND UNITS                                      
     100.0     200.0      -9.9     400.0     500.0     600.0                    
THIRD STAT                    3RD UNITS                                         
       0.1       0.9       0.3       0.7       0.1       0.8                    
FOURTH STATS                  4TH UNIT                                          
       1.0       2.0       3.0       3.0       2.5       1.5                    
FIFTH STAT                    5TH UNIT                                          
       9.0       6.0       3.0       2.0       6.0       8.0                    

  B. 4. 4 Simple Attribute format (tabular database format) 
          -------------------------------------------------
 
                                                                                
Many data retrieval systems (e.g. ORACLE,SAS) produce attribute data in a form  
where for each attribute the names and their values are given.                  
                                                                                
This tabular format is supported in OzGIS although there are some restrictions  
on its use.  The list of names is obtained from the first attribute; hence      
no new names can occur in following attributes (although names may be           
missing).  A set of data records for an attribute is assumed to finish (and     
the next set start) when the attribute description & units changes.             
                                                                                
     Comment record:                                                            
     80      byte       Comment describing the data                             
                                                                                
     Data records:                                                              
     10      byte       name                                                    
     10      real       value                                                   
     30      byte       attribute description                                   
     10      byte       attribute units                                         
                                                                                

  B. 4. 5 Sample simple attribute file DEMOSASA.DAT         
          -----------------------------------------
 
SIMPLE FORMAT ATTRIBUTE FILE - DEMOSASA.DAT                                     
TOP            1.0   DESCRIPTION A                 UNITS A                      
SQUARE         2.0   DESCRIPTION A                 UNITS A                      
DIAMOND        3.0   DESCRIPTION A                 UNITS A                      
TRIANGLE       4.0   DESCRIPTION A                 UNITS A                      
TOP            1.0   DESCRIPTION B                 UNITS B                      
DIAMOND        3.0   DESCRIPTION B                 UNITS B                      
SQUARE         2.0   DESCRIPTION B                 UNITS B                      
TRIANGLE       4.0   DESCRIPTION B                 UNITS B                      
TOP            1.0   DESCRIPTION C                 UNITS C                      
SQUARE         2.0   DESCRIPTION C                 UNITS C                      
DIAMOND        3.0   DESCRIPTION C                 UNITS C                      
TRIANGLE       4.0   DESCRIPTION C                 UNITS C                      


                                                                     110
TOP            1.0   DESCRIPTION D                 UNITS D                      
TRIANGLE       4.0   DESCRIPTION D                 UNITS D                      
DIAMOND        3.0   DESCRIPTION D                 UNITS D                      
DIAMOND        3.0   DESCRIPTION E                 UNITS E                      
TRIANGLE       4.0   DESCRIPTION E                 UNITS E                      
                                                                                

  B. 4. 6 Spreadsheet data formats                          
          ------------------------
 
                                                                                
Data from spreadsheets can be input in Lotus 1-2-3 format (WK1).                
                                                                                
The spreadsheet must be set up in a fixed format:                               
                                                                                
The data values are in a matrix with the values for the zones (or sites or      
lines) in columns and the different attributes across in the rows.              
Values can be missing and can be integer or floating point.                     
                                                                                
The first column must contain labels which are the 10 character zone (site etc) 
names, beginning at row 3. These must be SORTED in ascending order.             
                                                                                
The top row contains labels that are the (up to) 30 character attribute         
descriptions starting at column 2.                                              
                                                                                
The second row is the 10 character attribute descriptions.                      
                                                                                
e.g. the file DEMO123.dat can be read into the spreadsheet. It should look      
like:                                                                           
                                                                                
                 POPULATION GROWTH   SALES                                      
                 NUMBER              $                                          
ABBOTSFORD                 7418      237                                        
BURWOOD E                  9925      955                                        
CONCORD                    8984      202                                        
CROYDON N                  9369      298                                        
CROYDON W                   735                                                 
FIVE DOCK                  9903      716                                        
HABERFIELD                           727                                        
HOMEBUSH                   6631      704                                        
HUDSONPARK                 4668       71                                        
MORTLAKE                   1725      198                                        
STRATHFIELD                6285      663                                        
YARALLA                    9875      516                                        

  B. 4. 7 ATLAS Data files                                  
          ----------------
 
Attribute data files for the Atlas mapping system come as pairs of files, a     
format file and a data file.                                                    
                                                                                
The first record of the format file is a map name, which is ignored.            
There follows a a set of records, each of which gives the name of an            
attribute. For example, the following file specifies two attributes:            
                                                                                
"      Bundesland$"                                                             
"Population 1984        Totale Population in Tausend"                           
"Ausdehnung in qkm      Ausdehnung in Quadratkilometer"                         


                                                                     111
                                                                                
                                                                                
The data files have one record for each map item. Each record starts with the   
item name, and is followed by the values. The values are in the same order as   
the attribute names and there is one per attribute (2 here). Values can be in   
integer, decimal point or exponential formats. A value of 1.0E36 is missing     
data. For example:                                                              
                                                                                
"SCHLES.-HOLSTEIN", 2615 , 157.21                                               
"HAMBURG", 1.23E21 , 1.0E36                                                     
"BREMEN", 671 , 404                                                             
"NIEDERSACHSEN", 7230 , 47.447                                                  
"NORDR.-WESTFALEN", 16.777 , 34061                                              
"HESSEN", 5548 , 21114                                                          
"RHEINLAND-PFALZ", 3627 , 198.48                                                
"SAARLAND", 1052 , 25.71                                                        
"B.-WUERTTEMBERG", 9240 , 35751                                                 
"BAYERN", 10964 , 70552                                                         
"BERLIN", 1850 , 480                                                            
                                                                                
Names and attribute descriptions must be delimited by apostrophes as shown,     
and values must be comma delimited. Only the first 10 characters of a zone etc  
name is used and only the first 30 characters of a description.                 
                                                                                
Two data files have to be specified to OzEnter. The first is the format file,   
the second the Atlas data file. The format file is handled as a parameter file  
within the OzEnter program so can be present on disk as a file named with       
extension .PRM. In practise your two files will probably have the Atlas standard
file names with extensions FMT and DAT and you give the full file names when    
asked for them.                                                                 
                                                                                
For example, you might have a pair of files named EUROPE.FMT and EUROPE.DAT     
so you give the parameter file as EUROPE.FMT and the data file as either EUROPE 
or EUROPE.DAT (as DAT is the default extension).                                

  B. 4. 8 LAMM format                                       
          -----------
 
The LAMM package was developed at the CSIRO Division of Building Research. The  
format is supported as it is the only suitable format for mapping available in  
the Australian Bureau of Statistics GEOSTATS system.                            
                                                                                
The first record gives the number of map items and the number of attributes     
respectively.                                                                   
                                                                                
The attribute names follow, one per record                                      
                                                                                
Finally the value records are given, being the name followed by the values.     
The records are sorted into ascending name order. Values are separated by       
blanks or commas.                                                               
                                                                                
An example file is DEMOLAMM:                                                    
                                                                                
12,8                                                                            
MALES 35 - 44 (81)                                                              
MALES 35 - 44 (86)                                                              
MALES - UNEMPLOYED (76)                                                         
MALES - UNEMPLOYED (81)                                                         


                                                                     112
MALES - UNEMPLOYED (86)                                                         
INCOME MALES $18001-$26000 (76)                                                 
INCOME MALES $18001-$26000 (81)                                                 
INCOME MALES $18001-$26000 (86)                                                 
'ABBOTSFORD'   69 0 14 27 48 0 51 55                                            
'BURWOOD E'    223 0 48 134 89 0 218 397                                        
'CONCORD'      102 0 5 12 29 0 109 197                                          
'CROYDON N'    161 0 27 50 53 0 156 284                                         
'CROYDON W'    180 0 24 36 76 0 307 241                                         
'FIVE DOCK'    50 0 20 2 0 0 19 11                                              
'HABERFIELD'   126 0 28 20 20 0 208 185                                         
'HOMEBUSH'     114 0 26 51 37 0 165 212                                         
'HUDSONPARK'   243 0 65 99 65 0 231 385                                         
'MORTLAKE'     0 0 0 0 2 0 0 113                                                
'STRATHFIELD'  100 0 4 7 10 0 74 70                                             
'YARALLA'      7 0 16 2 0 0 4 3                                                 
                                                                                

  B. 4. 9 Comma delimited format                            
          ----------------------
 
The comma delimited format consists of a set of records:                        
                                                                                
Each record has a series of values separated by commas.                         
                                                                                
The first value is the item (zone,line or site) name and there follows one      
number for each attribute.                                                      
                                                                                
                                                                                
The comma delimited form is seriously deficient in that it contains no          
attribute descriptions.                                                         
                                                                                
Processing this format would require asking the user to type in the description 
for each attribute which is time consuming and there is always the danger that  
an attribute could be incorrectly labelled.                                     
                                                                                
Either:                                                                         
                                                                                
read the data into a spreadsheet                                                
                                                                                
Or:                                                                             
                                                                                
convert into LAMM or ATLAS format with a word processor.                        
                                                                                
The file DEMOCOMD.DAT looks like:                                               
                                                                                
2727400,115,114,105,6                                                           
2727800,77,75,63,29                                                             
PHRED,85,81,66,36                                                               
NEW YORK,5,6,3,3                                                                
2728200,27,27,21,12                                                             
2728300,74,72,63,34                                                             
.                                                                               
.                                                                               
.                                                                               
.                                                                               
2739100,13,12,12,5                                                              
2739200,2,0,3,1                                                                 


                                                                     113
                                                                                

  B. 4.10 Other attribute data formats                      
          ----------------------------
 
Other formats will be supported as required.                                    
                                                                                
We will support any formats for major data suppliers, but you must send sample  
data and documentation.                                                         
                                                                                
We will also attempt to support file formats from other packages.               


                                                                     114

  B. 5 Standard OzGIS formats for geographic files       
      -------------------------------------------
 

  B. 5. 1 General Information                               
          -------------------
 
The standard data format reflects the internal topological file structure.      
                                                                                
In practice, a complete data file is seldom available. It is more common to     
bring in just points (as a map and points partition) or lines (as a map and     
segments partition). Zones are usually formed from the segments by using the    
OzZone program.                                                                 
                                                                                
Coordinates are usually given either in degrees (for lat,long) or in metres /   
feet for UTM.                                                                   

  B. 5. 2 Structure of data                                 
          -----------------
 
Geographic files contain several partitions.  The first must be the map         
partition, and can be followed by at most one of each of zones, polygons,       
lines, segments and points partitions.                                          
                                                                                
Each partition is preceded by a type record, which is one of MAP, ZONES,        
POLYGONS, LINES or POINTS; for example, a zones file must  have the             
following structure:                                                            
                                                                                
     Comment record                                                             
     MAP                                                                        
     map records                                                                
     POLYGONS                                                                   
     polygon records                                                            
     ZONES                                                                      
     zone records                                                               
     SEGMENTS                                                                   
     segment records                                                            
                                                                                
Different partitions are present (the MAP partition is always first)            
 according to the type of data:-                                                
                                                                                
Files which describe zones have a ZONES partition to define                     
the zones, a POLYGONS partion to give the polygons that                         
bound each zone (including lakes and islands), and a SEGMENTS partition         
to define the coordinate points that draw the segments along the                
polygon boundaries.                                                             
                                                                                
Sites files have a POINTS partition to give the site names                      
and locations.                                                                  
                                                                                
Lines files have a LINES partition to define the line names                     
and a SEGMENTS partion to define the coordinate points in the                   
segments that make up the lines.                                                
                                                                                
Line overlays are defined by SEGMENTS partitions.                               
                                                                                


                                                                     115
Marker and name overlays are defined by POINTS partitions.                      
                                                                                
Coordinate data should be entered in standard units.  Coordinate pairs are      
always in the order (X,Y) (e.g. (Longitude, Latitude)).  Note that latitude     
must be entered as a negative number in the Southern Hemisphere.                
                                                                                
Data entered in latitude-longitude projection can be converted to other         
projections.                                                                    
Feature codes may be included to give a classification of geographic items.     
e.g. segments may be classified as different types of roads.                    
                                                                                
All geographic regions (windows) are given in actual coordinate values in       
the order:  X-minimum, X-maximum, Y-minimum, Y-maximum.                         

  B. 5. 3 Internal Data                                     
          -------------
 
The geographic data are held internally as a word-addressable                   
random access disk file.                                                        
The file structure reflects the data structure with the necessary               
indexing etc for processing.                                                    
Additional data are also generated for efficient processing:-                   
                                                                                
Polygons are held in display order so the map zones can be                      
rapidly displayed.                                                              
                                                                                
 A POINTS partition is generated internally by OzGIS                            
for the centroids of the zone polygons.                                         
This enables markers or zone names to be overlayed over                         
a zones map, and for the points to be displayed as sites                        
where the site names are the zone names.                                        
                                                                                
Lists of names are also generated for zones, lines or sites                     
for rapid retrieval.                                                            

  B. 5. 4 Comment Record                                    
          --------------
 
     80      byte       comment describing the data                             
                                                                                

  B. 5. 5 Map Partition                                     
          -------------
 
This partition contains general information about the file (map) and must       
be the first partition.                                                         
                                                                                
     Type Record:                                                               
     3        byte      partition header = MAP                                  
                                                                                
     Window Record:                                                             
     4 x 10  real       the region covered by the file                          
                                                                                
     Projection Record: (now redundant)                                         
     10 integer         Map projection code                                     
                        0=none, 1=lat-long degrees                              
     10       integer   type of zones (optional)                                
                                                                                


                                                                     116

  B. 5. 6 Zones Partition                                   
          ---------------
 
This partition defines the zones in the geographic region.                      
                                                                                
Each zone is defined by one or more polygons.  A zone may consist of a          
polygon, several separated polygons, polygons with interior polygons of         
other zones, etc.                                                               
                                                                                
If a zones partition is present, a polygons partition with the referenced       
must be given.                                                                  
                                                                                
The partition may be used as a polygon underlay and feature codes may be used   
to give a classification e.g. the polygons may be different soil types.         
                                                                                
     Type Record:                                                               
     5        byte      partition header = ZONES                                
                                                                                
     Definition Record:                                                         
     10       integer   number of zones                                         
     10       integer   number of feature codes                                 
                                                                                
     Feature code Records (if required):                                        
     8 x 10  integer    feature codes                                           
                                                                                
     Zone Records:                                                              
     10       byte      zone name, usually left justified, blank filled         
     10       integer   number of polygons in the zone                          
                                                                                
     Polygon Records:                                                           
     8 x 10  integer    identifying numbers of the polygons                     

  B. 5. 7 Line Partition                                    
          --------------
 
The partition defines networks of lines (e.g. roads, rivers).  Each network     
has a name and is specified in terms of line segments.The name can be used      
to apply quantised attribute data.                                              
                                                                                
Type record:                                                                    
     5       byte       partition Leader = LINES                                
                                                                                
Header record:                                                                  
     10      integer    number of lines                                         
                                                                                
                                                                                
Line record:                                                                    
     10      byte       line name, usually left justified, blank                
                        filled                                                  
     10      integer    number of segments forming the line                     
                                                                                
                                                                                
Region Record:                                                                  
     4x10    real       line limits (window)                                    
                        X minimum, X-maximum, Y-minimum, Y-maximum)             
                                                                                


                                                                     117
Segments Records:                                                               
     8x10    integer    the identifying numbers of the line segments.           

  B. 5. 8 Polygons Partition                                
          ------------------
 
A polygon defines an enclosed geographic area.  Each polygon is specified       
in terms of the line segments which constitute its boundary.  If a zones        
partition is given, every polygon referenced by the zones must be defined.      
                                                                                
The centroid or internal point of a polygon is be used by OzGIS to              
locate text (zone names) or graphic symbols;                                    
a points partition is generated.                                                
                                                                                
Type Record:                                                                    
     8        byte      partition header = POLYGONS                             
                                                                                
     Header Record:                                                             
     10       integer   number of polygons                                      
                                                                                
A set of records follow for each polygon:-                                      
                                                                                
     Definition Record:                                                         
     10       integer   polygon identification number                           
     10       byte      name of zone enclosed by polygon                        
     10       integer   number of lines forming the polygon boundary            
     10       integer   level of polygon for display using                      
                        polygon fill 0=standard, 1=lakes, 2=islands in          
                        lakes etc. (range 0-5)                                  
                                                                                
     Region Record:                                                             
     4 x 10   real      polygon limits (window)                                 
                        (X-minimum, X-maximum, Y-minimum, Y-maximum)            
                                                                                
     2 x 10   real      centroid or labelling point (X,Y) in the polygon        
                        (set to centre of window if not given)                  
     10       real      area of polygon                                         
                        (calculated if not given)                               
                                                                                
     Segments Records:                                                          
     8 x 10   integer   the identifying numbers of the segments + ve if         
                        segment is clockwise, -ve if anticlockwise.             

  B. 5. 9 Segments Partition                                
          ------------------
 
Line segments are defined by a set of points connected by straight lines.       
                                                                                
Segments may define the boundaries of zones, define line                        
networks, or line overlays.                                                     
                                                                                
When a segment is a boundary segment of a polygon, it can be the boundary       
of at most two polygons.                                                        
  In other words, the polygons must be a unique tessellation of the geographic r
                                                                                
When the segments define polygon boundaries, the partition should contain       
only the segments of the polygons, and the records must contain the names       
of the zones on each side.  Left and right zones are defined by the             


                                                                     118
direction implied by the sequence of points in the line.  The zone names        
must correspond to those defined in the zones partition.  The special zone      
name OUTSIDE (left aligned)                                                     
should be used when the line is at the edge of the map, or on                   
the boundary of void areas.                                                     
                                                                                
Line segments (of polygons)                                                     
 must be closed (i.e., the last point in a segment must be the                  
first point of another segment), and segments must not cross or have loops.     
Further, segment must not be repeated.                                          
                                                                                
Segments that are to be used as geographic overlays may have feature codes to   
give a classification e.g. different types of rivers.                           
                                                                                
Address information can be present. This consists of the name of the street     
followed by 0, 1 or 2 sets of entries for street number ranges and postal codes.
These zip codes are optional as are the number ranges. If 2 ranges are given    
one is odd and the other even numbers. The start and end values are given       
according to the direction of the numbers and the digitising direction.         
                                                                                
     Type Record:                                                               
     8        byte      partition header = SEGMENTS                             
                                                                                
     Header Record:                                                             
     10       integer   number of segments                                      
                                                                                
A set of records follows for each segment.                                      
                                                                                
     Definition Record:                                                         
     10       integer   identifying number                                      
     10       byte      name of left zone (if line is part of a zone            
                        boundary)                                               
     10       byte      name of right zone (if line is part of a zone           
                        boundary)                                               
     10       integer   number of points in segment                             
     10       integer   number of feature codes                                 
     10       byte      non blank indicates that address info follows           
                                                                                
     Feature code Records (if required):                                        
     8 x 10  integer    feature codes                                           
                                                                                
     Address Records (if required):                                             
     10       byte      name of street, park etc                                
     6 x 10  integer    start number, end number, postal (ZIP) code, followed   
                        by optional second set                                  
                                                                                
     Point Records:                                                             
     8 x 10   real      (X,Y) coordinate pairs (4 per record)                   

  B. 5.10 Points Partitions                                 
          -----------------
 
The partition contains a set of points or sites at which symbols can be         
overlayed on the map.  The site name can be used to apply quantised             
attribute data or used to annotate the points.                                  
                                                                                
Feature codes can define a classification for display as sites.                 
                                                                                


                                                                     119
Type Record:                                                                    
     6        byte      partition header = POINTS                               
                                                                                
     Header Record:                                                             
     10       integer   number of points                                        
                                                                                
     Point Records:                                                             
     10       real      X-coordinate value                                      
     10       real      Y-coordinate value                                      
     40       byte      site name or annotation                                 
     10       integer   number of feature codes                                 
                                                                                
     Feature code Records (if required):                                        
     8 x 10  integer    feature codes                                           
                                                                                
Note that only the first 10 characters are used for the site name.              

  B. 5.11 Sample boundaries geographic file DEMOZSEG.DAT    
          ----------------------------------------------
 
Geographic data for zones (e.g. Census districts) are usually brought in as the 
line segments that form the boundaries of the zones.                            
                                                                                
The boundary segments contain the (X,Y) vertices that make up the line and the  
names of the zones on each side of the line.                                    
                                                                                
These data are usually entered using OzEnter, then excessive vertices discarded 
(thinned) using OzData, and then the full zone / polygon/ line segment /        
centroids structure built using OzZone to prepare for display.                  
                                                                                
For example, to extract ZIP code boundaries from USA TIGER files, the left and  
right ZIP codes are extracted from the records and formed into left aligned     
zone names, and the latitude / longitude vertices are also extracted. If the    
left and right zone names are the same the segments are internal to the zone    
and can be ignored.                                                             
                                                                                
The following illustrates the standard format used to enter such data. Note     
that the MAP partition is required but that the extent need not be given.       
                                                                                
EXAMPLE ZONE BOUNDARY SEGMENTS THAT CAN BE BUILT INTO ZONES - DEMOZSEG.DAT      
MAP                                                                             
  0.0       0.0       0.0       0.0                                             
         0                                                                      
SEGMENTS                                                                        
        10                                                                      
       107ZONE 1    OUTSIDE            2                                        
102.00    503.00    114.00    503.00                                            
       125ZONE 2    ZONE 1             2                                        
102.00    503.00    110.00    513.00                                            
       143ZONE 1    ZONE 3             2                                        
114.00    503.00    110.00    513.00                                            
       161ZONE 3    OUTSIDE            6                                        
114.00    503.00    115.00    505.00    116.00    507.00    117.00    509.00    
118.00    511.00    119.00    513.00                                            
       187ZONE 2    ZONE 3             2                                        
110.00    513.00    119.00    513.00                                            
       205ZONE 2    OUTSIDE            4                                        
119.00    513.00    114.00    518.00    109.00    517.00    104.00    516.00    


                                                                     120
       227ZONE 2    OUTSIDE            2                                        
104.00    516.00    110.00    513.00                                            
       245SURPLUS   SURPLUS            2                                        
119.00    513.00    122.00    506.00                                            
       263OUTSIDE   ZONE 2             2                                        
103.00    509.00    110.00    513.00                                            
       281OUTSIDE   ZONE 2             2                                        
102.00    503.00    103.00    509.00                                            

  B. 5.12 Sample segments file with adddresses DEMOADDR.DAT 
          -------------------------------------------------
 
Address information can be added to line segments. Note the non-blank flag.     
                                                                                
EXAMPLE  SEGMENTS (ROADS) WITH ADDRESSES - DEMOADDR.DAT                         
MAP                                                                             
  0.0       0.0       0.0       0.0                                             
         0                                                                      
SEGMENTS                                                                        
        10                                                                      
       107ZONE 1    OUTSIDE            2            ADDRESS                     
Great North Road                                                                
         1       666      2600                                                  
102.00    503.00    114.00    503.00                                            
       12            ZONE 1             2          ADDRHERE                     
Molonglo Gorge                                                                  
                                                                                
102.00    503.00    110.00    513.00                                            
       143ZONE 1    ZONE 3             2            address                     
Burra Street                                                                    
         1        99         6        140                                       
114.00    503.00    110.00    513.00                                            
       161                             6            address                     
Northbourne Ave                                                                 
         1        55      2602        20         66      2600                   
114.00    503.00    115.00    505.00    116.00    507.00    117.00    509.00    
118.00    511.00    119.00    513.00                                            
       187ZONE 2    ZONE 3             2                                        
110.00    513.00    119.00    513.00                                            
       205                             4            address                     
Yass rd                                                                         
         1        99      2600                                                  
119.00    513.00    114.00    518.00    109.00    517.00    104.00    516.00    
       227ZONE 2    OUTSIDE            2                                        
EPPING HWY                                                                      
        44        22                  77         11                             
104.00    516.00    110.00    513.00                                            
       245SURPLUS   SURPLUS            2            address                     
Hume Highway                                                                    
         1        99      2301        88         44      2304                   
119.00    513.00    122.00    506.00                                            
       263OUTSIDE   ZONE 2             2            address                     
Mains Avenue                                                                    
         1        99      2600         6        140      2600                   
103.00    509.00    110.00    513.00                                            
       281OUTSIDE   ZONE 2             2            address                     
Lover's Lane                                                                    
        33        11                                                            


                                                                     121
102.00    503.00    103.00    509.00                                            
                                                                                
66 >> <SS>Sample geographic file DEMOZONES.DAT                                  
The full topological geographic structure can be entered (although in practise  
this is seldom available).                                                      
                                                                                
COMMENT LINE FOR TEST DATA     - DEMOZONE.DAT                                   
MAP                                                                             
102.00    122.00    502.00    518.00                                            
         0                                                                      
ZONES                                                                           
         3                                                                      
ZONE 1             1                                                            
       352                                                                      
ZONE 2             2                                                            
       377       402                                                            
ZONE 3             1                                                            
       327                                                                      
POLYGONS                                                                        
         4                                                                      
       327ZONE 3             3         0                                        
110.00    119.00    503.00    513.00    114.00    510.00                        
       187      -161       143                                                  
       352ZONE 1             3         0                                        
102.00    114.00    503.00    513.00    108.00    506.00                        
      -125       107       143                                                  
       377ZONE 2             3         0                                        
102.00    110.00    503.00    513.00    104.00    508.00                        
      -263      -281       125                                                  
       402ZONE 2             3         0                                        
104.00    119.00    513.00    518.00    110.00    515.00                        
       205       227       187                                                  
SEGMENTS                                                                        
        10                                                                      
       107ZONE 1    OUTSIDE            2                                        
102.00    503.00    114.00    503.00                                            
       125ZONE 2    ZONE 1             2                                        
102.00    503.00    110.00    513.00                                            
       143ZONE 1    ZONE 3             2                                        
114.00    503.00    110.00    513.00                                            
       161ZONE 3    OUTSIDE            6                                        
114.00    503.00    115.00    505.00    116.00    507.00    117.00    509.00    
118.00    511.00    119.00    513.00                                            
       187ZONE 2    ZONE 3             2                                        
110.00    513.00    119.00    513.00                                            
       205ZONE 2    OUTSIDE            4                                        
119.00    513.00    114.00    518.00    109.00    517.00    104.00    516.00    
       227ZONE 2    OUTSIDE            2                                        
104.00    516.00    110.00    513.00                                            
       245SURPLUS   SURPLUS            2                                        
119.00    513.00    122.00    506.00                                            
       263OUTSIDE   ZONE 2             2                                        
103.00    509.00    110.00    513.00                                            
       281OUTSIDE   ZONE 2             2                                        
102.00    503.00    103.00    509.00                                            
                                                                                


                                                                     122

  B. 5.13 Sample lines geographic file DEMOLINES.DAT        
          ------------------------------------------
 
A lines structure is used for line data that is to be displayed for attribute   
data:                                                                           
                                                                                
COMMENT LINE FOR TEST DATA       DEMOLINES.DAT                                  
MAP                                                                             
103.50    121.50    503.50    517.50                                            
         0                                                                      
LINES                                                                           
         4                                                                      
ROAD 3             3                                                            
110.50    119.50    503.50    513.50                                            
       187       161       143                                                  
ROAD 1             3                                                            
103.50    114.50    503.50    513.50                                            
       125       107       143                                                  
ROAD 2             3                                                            
103.50    110.50    503.50    513.50                                            
       263       281       125                                                  
ROAD 4             3                                                            
104.50    119.50    513.50    517.50                                            
       205       227       187                                                  
SEGMENTS                                                                        
        10                                                                      
       107ROAD 1    OUTSIDE            2                                        
103.50    503.50    114.50    503.50                                            
       125ROAD 2    ROAD 1             2                                        
103.50    503.50    110.50    513.50                                            
       143ROAD 1    ROAD 3             2                                        
114.50    503.50    110.50    513.50                                            
       161ROAD 3    OUTSIDE            6                                        
114.50    503.50    115.50    505.50    116.50    507.50    117.50    509.50    
118.50    511.50    119.50    513.50                                            
       187ROAD 2    ROAD 3             2                                        
110.50    513.50    119.50    513.50                                            
       205ROAD 2    OUTSIDE            4                                        
119.50    513.50    114.50    517.50    109.50    517.50    104.50    516.50    
       227ROAD 2    OUTSIDE            2                                        
104.50    516.50    110.50    513.50                                            
       245SURPLUS   SURPLUS            2                                        
119.50    513.50    121.50    506.50                                            
       263OUTSIDE   ROAD 2             2                                        
103.50    509.50    110.50    513.50                                            
       281OUTSIDE   ROAD 2             2                                        
103.50    503.50    103.50    509.50                                            

  B. 5.14 Sample points geographic file DEMOPOINT.DAT       
          -------------------------------------------
 
Points files just give the (X,Y) locations and a site name / label.             
                                                                                
These files can be used with an attribute file for mapping site data or can be  
used to place sysmols or labels at locations (overlays).                        
                                                                                


                                                                     123
COMMENT LINE FOR TEST DATA     - DEMOPOINT.DAT                                  
MAP                                                                             
102.00    122.00    502.00    518.00                                            
         0                                                                      
POINTS                                                                          
         3                                                                      
114.0     503.0     PNT1                                                        
104.0     516.0     PNT2                                                        
114.0     518.0     PNT3                                                        
                                                                                


                                                                     124

  B. 6 Format of polygon geographic files                
      ----------------------------------
 

  B. 6. 1 Standard (not implemented)                        
          --------------------------
 
Geographic data are often available in polygon format, and this data            
definition enables it to be used used with OzGIS.                               
                                                                                
The common line segments on the boundaries of adjacement polygons are           
effectively defined twice in polygon data; OzGIS assumes that they are          
exactly the same.  The polygon boundary must not cross itself.                  
                                                                                
Each polygon has a name, which is the name of the zone to which it belongs.     
                                                                                
Polygons may occur inside other polygons.  Where the polygon is not part of     
a zone (e.g. a lake) it may be given the name OUTSIDE.  The level field         
defines lakes, islands within lakes etc.  When maps are generated on            
devices using polygon fill the level gives the order of display so the          
polygons will overwrite correctly.                                              
                                                                                
                                                                                
Comment record:                                                                 
                                                                                
     80      byte       comment describing the data                             
                                                                                
Definition Record:                                                              
     10      integer    map projection code                                     
     10      integer    zone type (optional)                                    
                                                                                
Each polygon is defined by a set of records:                                    
                                                                                
Polygon header:                                                                 
     10      byte       zone name, usually left justified, blank filled         
                        or OUTSIDE if an internal polygon.                      
     10      integer    number of points in the line                            
     10      real       level of polygon for hardcopy generation using          
                        polygon fill 0=standard, 1=lakes, etc.                  
                                                                                
Centroid record:                                                                
     2x10    real       centroid or labelling point (X,Y) in polygon            
                                                                                
Point records:                                                                  
     8x10    real       (X,Y) coordinate pairs (4 per record) The last          
                        point must be the same as the first.                    
                                                                                

  B. 6. 2 SAS Format Zone Files                             
          ---------------------
 
The SAS system provides a crude polygon format for map data. The old format has 
been updated to allow for multiple polygons in zones and for data at several    
levels of resolution.                                                           
                                                                                
The polygons must be given in the correct order for display when there are      


                                                                     125
polygons within other polygons.                                                 
                                                                                
The data consists of variable length records with the following fields:         
                                                                                
field1: the zone name                                                           
field2: the polygon number within the zone (usually 1)                          
field3: the X value                                                             
field4: the Y value                                                             
                                                                                
For example, part of a file might be as follows, where zone 19 has 2 polygons   
                                                                                
  17   1 135.0198593289   -45.006152242                                         
  17   1 135.0214474499   -45.008039698                                         
  17   1 135.0234586746   -45.011447966                                         
  17   1 135.0232417881   -45.011781529                                         
  17   1 135.0146185011   -45.012796119                                         
  17   1 135.0149845481   -45.012392245                                         
  17   1 135.0148004219   -45.011233956                                         
  17   1 135.0155192316   -45.009236805                                         
  17   1 135.0140719935   -45.006661419                                         
  19   1 135.0200279355   -45.018230647                                         
  19   1 135.0211774409   -45.018684313                                         
  19   1 135.0218305141   -45.017554402                                         
  19   1 135.023555249    -45.017326832                                         
  19   1 135.024860993    -45.014845043                                         
  19   1 135.0251943022   -45.014588848                                         
  19   1 135.0192894787   -45.023670658                                         
  19   1 135.0179009587   -45.022158593                                         
  19   1 135.0182676911   -45.021624267                                         
  19   1 135.0180351585   -45.020997345                                         
  19   1 135.0192095339   -45.020121485                                         
  19   1 135.0194375813   -45.01857923                                          
  19   2 135.0279172212   -45.023049563                                         
  19   2 135.0281361789   -45.022784472                                         
  19   2 135.0283748209   -45.0230802                                           
  19   2 135.0285159498   -45.022607252                                         
  19   2 135.0283438861   -45.023600549                                         
  21   1 135.041364044   -45.0087376237                                         
  21   1 135.039871216   -45.0095451251                                         
  21   1 135.039485425   -45.0093839765                                         
  21   1 135.037185282   -45.0106722265                                         
            .                                                                   
            .                                                                   
            .                                                                   
            .                                                                   
            .                                                                   

  B. 6. 3 Simple Format (old SAS) Zone Files                
          ----------------------------------
 
Simple format files are in common use by the SAS system and other packages      
providing SAS interfaces.  Polygon for lakes etc. should follow standard        
polygons to provide the correct display order for overwriting.                  
                                                                                
This format has now been updated in the SAS system.                             
                                                                                
                                                                                
Each data record has the form                                                   


                                                                     126
     10      byte       zone name                                               
     10      real       X coordinate                                            
     10      real       Y coordinate                                            
     10      integer    Polygon number within zone                              

  B. 6. 4 Sample simple zones data file DEMOSASG.DAT        
          ------------------------------------------
 
SQUARE        3.0       5.0                                                     
SQUARE        7.0       5.0                                                     
SQUARE        7.0       10.0                                                    
SQUARE        3.0       10.0                                                    
DIAMOND       8.0       8.0                                                     
DIAMOND       10.0      5.0                                                     
DIAMOND       12.0      8.0                                                     
DIAMOND       10.0      11.0                                                    
TRIANGLE      13.0      5.0                                                     
TRIANGLE      16.0      10.0                                                    
TRIANGLE      19.0      5.0                                                     
TRIANGLE      13.0      2.0            2                                        
TRIANGLE      15.0      2.0            2                                        
TRIANGLE      14.0      4.0            2                                        
SQUARE        4.0       0.0            2                                        
SQUARE        8.0       0.0            2                                        
SQUARE        8.0       4.0            2                                        
SQUARE        4.0       4.0            2                                        
SQUARE        0.0       0.0            2                                        
SQUARE        5.0       1.0            2                                        
SQUARE        5.0       3.0            2                                        
SQUARE        7.0       3.0            2                                        
SQUARE        7.0       1.0            2                                        
OUTSIDE       15.0      6.0            2                                        
OUTSIDE       15.0      7.0            2                                        
OUTSIDE       17.0      7.0            2                                        
OUTSIDE       17.0      6.0            2                                        
TOP           4.0       8.0                                                     
TOP           19.0      8.0                                                     
TOP           19.0      9.0                                                     
TOP           4.0       9.0                                                     


                                                                     127

  B. 7 GIS / common geographic file formats              
      ------------------------------------
 

  B. 7. 1 DIME format                                       
          -----------
 
This format is supported, but has not had much use. The data are primarily 2    
point segments, so is inefficient on storage.                                   
                                                                                
Note that only 499 2 point segments can be handled.                             
                                                                                
The data are usually passed through OzZone to build polygons and then through   
OzData to join up the segments into ones of decent length.                      
                                                                                
The data are long Ascii records, and look something like:                       
                                                                                
XX91609160012583                       1                                        
  MANUEL              ST                       8    8      201   299   200      
   29891600000011 14502 1450219711197119160       38  440195019510003016     234
  10003016     213   1818                        396750 757476396740            
7574760610215040685606098370406849                                              
  MANUEL              ST                       8    8      301   359   300      
  35891600000029 14502 1450219711197119160       44  480195019510003016     233 
  10003016     212   1818                        396740 757476396730            
7574760609837040684906095020406848                                              
  MANUEL              ST                       8    8      361   399   360      
  39891600000037 14502 1450219711197119160       48  540195019510003016     233 
  10003016     233   1818                        396730 757476396718            
7574760609502040684806090470406846                                              
  SCHOOL              ST                       9    9      900   998   901      
   99991600000045 162   162  19720197209160       37  220200020010003031     107
  10003031     108   1818                        396611 755737396619            
7557430605026045580006053140455632                                              
  SCHOOL              ST                       9    9     1000  1098  1001      
  109991600000052 162   162  19720197209160       22  140200020010003031     115
  10003031     115   1818                        396619 755743396624            
7557460605314045563206054910455542                                              

  B. 7. 2 DLG optional 3 format                             
          ---------------------
 
The DLG-3 format is the major interchange format in use, and data can be        
obtained from many mapping agencies e.g. from USGS.                             
                                                                                
The data differs in concept from the usual data displayed by OzGIS in that it   
is preclassified by the assignment of numeric "feature codes".                  
                                                                                
All identifiers are numbers. These are converted to names by adding prefixes.   
Point names are POINT + 5 digit number, zone names are AREA + 6 digit zero      
filled number e.g.                                                              
                                                                                
AREA000001                                                                      
AREA000630                                                                      
POINT00004                                                                      
POINT00234                                                                      


                                                                     128
                                                                                
The data entry process processed the lines only. Any line with one vertice or   
two vertices and the same node numbers is taken as a point.                     
                                                                                
Other lines are output with the left and right names set to the area names.     
Left and right area numbers of zero or one are taken to be outside the map.     
                                                                                
Feature codes are stored as numbers (combined input pairs) for lines, points    
and zones e.g. '291  22' becomes 2910022.                                       
                                                                                
The first area is ignored as it should be the boundary of the map.              
                                                                                
Polygons are generated by passing the geographic file through the OzZone        
program.  This carries the area feature codes through to the polygons, retains  
the line segments, and forms a points segment that contains the centroids of    
the polygons.                                                                   
                                                                                
Note that file should have 80 character fixed length records. In practise files 
often have no end-of-records (e.g. USGS CD-ROM files) or records may be         
truncated. Records with end-of-line markers must no be more than 80             
characters long.                                                                
                                                                                
You will find that DLG-3 files off ARC-INFO systems often have extraneous       
background polygons that "zap" the map when displayed.                          
                                                                                
Some test files are supplied for Hawaii.  These were read off the USGS GeoDATA  
CD ROM on a SUN system, and 'newline' characters inserted to form 80 character  
records.  The files had to be edited as an arbitrary polygon was given as       
outside the map as the left and right areas on the line (this could also be     
handled during display by specifying feature codes).                            
                                                                                
The test files are:                                                             
                                                                                
HAWDLGWB - water boundaries i.e. the islands                                    
HAWDLGWB - administrative boundaries                                            
HAWDLGRD - roads                                                                
HAWDLGST - streams                                                              
                                                                                
The data format is described in the US Geological Survey Circular 895-c         
"USGS Digital Cartographic Data Standards, Digital Line Graphs"                 
                                                                                
The files look like:                                                            
                                                                                
USGS-NMD  DLG DATA - CHARACTER FORMAT - 09-29-82 VERSION s21_wb.dlg             
HAWAIIAN ISLANDS POLY 10 DROPPED        1967, 1980  2000000.                    
                                                                                
     3     3  9999     2 0.50800000000D+02     4     0     4     1              
   0.637820640000000D+07   0.676865799729109D-02   0.800000000000000D+07        
   0.180000000000000D+08  -0.157000000000000D+09   0.300000000000000D+07        
   0.0                     0.0                     0.0                          
   0.0                     0.0                     0.0                          
   0.0                     0.0                     0.0                          
 0.10000000000D+01 0.0               0.0               0.0                      
SW       19.000000 -160.000000        -316386.41  1771715.66                    
NW       22.000000 -160.000000        -312489.03  2102112.53                    
NE       22.000000 -155.000000         208312.61  2101093.98                    
SE       19.000000 -155.000000         210917.63  1770684.40                    
WATER BODIES           0    74    74 010    12    12 010    70    70   1        


                                                                     129
N    1  -316386.41  1771715.66           0           0     0                    
N    2  -312489.03  2102112.53           0           0     0                    
N    3   208312.61  2101093.98           0           0     0                    
N    4   210917.63  1770684.40           0           0     0                    
.                                                                               
.                                                                               
.                                                                               
.                                                                               
N   74  -320966.08  2105481.92           2           0     0                    
   -69    70                                                                    
A    1   -68438.87  1949336.24           3     0     1     0     0              
     8     9     7                                                              
     0     0                                                                    
A    2  -327997.34  2094827.63           3     0     1     0     0              
   -10    -2    -1                                                              
    40   150                                                                    
.                                                                               
.                                                                               
.                                                                               
.                                                                               
A   13   -91708.84  2025480.45           3     0     1     0     0              
   -66   -65   -67                                                              
    40   150                                                                    
L    1     7     6     2     0                24     1     0                    
  -332906.23  2078428.77  -332805.62  2077920.57  -331991.53  2078579.38        
  -332446.45  2079748.67  -331479.96  2080407.19  -331224.96  2080914.69        
  -331578.38  2082032.98  -331221.19  2082845.09  -330100.11  2084620.90        
  -329235.22  2085279.61  -328573.03  2086192.72  -328571.24  2087107.12        
  -327247.56  2088577.74  -325977.26  2088727.66  -325164.16  2088878.47        
  -324909.37  2089284.37  -324503.57  2088978.78  -323182.17  2089280.99        
  -322319.07  2089025.30  -321707.68  2089938.51  -321250.68  2089836.02        
  -320995.88  2090241.92  -319775.79  2090696.74  -318961.20  2091609.55        
   290  4000                                                                    
.                                                                               
.                                                                               
.                                                                               
.                                                                               
L   70    74    66    11     0                 2     1     0                    
  -320966.08  2105481.92  -321422.78  2105736.82                                
   290  4002                                                                    

  B. 7. 3 Gina format                                       
          -----------
 
The standard interchange format for GeoVision GIS is Gina.                      
                                                                                
OzEnter processes some of the file. Feature codes must be numeric. Zone names   
generated are of the form ZONE12345 and site names are of the form POINT12345.  
                                                                                
Only boundary lines and points are output - OzZone has to be used to generate   
the zones / polygons.                                                           
                                                                                
The sample file DEMOGINA.DAT is as follows:                                     
                                                                                
udb-start b v 8192                                                              
                                                                                
udb-header 0.5 fred-db "Fred's test database"                                   
descr      29oct85 14:32:10 example GINA files                                  


                                                                     130
coord-sys  rect  feet                                                           
extent -12000, -8000,  12000, 8000                                              
layer 1 base        "base information layer"                                    
layer 2 roads       "roads and streets layer"                                   
layer 3 hydro       "hydrographic layer (rivers, streams etc)"                  
layer 4 telephone   "telephone plant layer"                                     
layer 5 lots        "property lots layer"                                       
                                                                                
network 1 emergency l 2 "emergency routes"                                      
network 2 property  p 5 "property polygon network"                              
                                                                                
udb-primary                                                                     
table road free                                                                 
field name        char 40   i n   "road name"                                   
field r_type      char 12   i n   "type of road, arterial, highway etc"         
field lanes       num  2,0        "maximum number of lanes"                     
field surface     char 10   n     "type of surface"                             
fc   1000, 1099                                                                 
table house free                                                                
field h_type      char 10   n     "house type: bungalow;""test quotes""  etc"   
field lot_no      num 10    i     "lot number"                                  
fc   1130,  1139                                                                
table lots free                                                                 
field lot_no      num  10   i u n "lot number"                                  
field address_no  num  6,0  i n                                                 
field street      char 40   n     "street name"                                 
fc   1100                                                                       
                                                                                
                                                                                
udb-feature                                                                     
feat 1  1002 2 0 l xy 0 0 0 1 0                                                 
coor 1805 1120 1805 1143                                                        
coor 2018 1143 2018 1204 2508 1204                                              
text "Elm Street"                                                               
attr Elm suburban 2 "asphalt"                                                   
feat 2  1004 2 0 l xy 0 0 0 1 0                                                 
coor 2508 1204 2508 820                                                         
text "Oak Street"                                                               
attr Oak arterial 4 "concrete"                                                  
feat 3  1400 5 2 l xy                                                           
coor 2508 903 2508 933                                                          
feat 4  1400 5 2 l xy                                                           
coor 2508 933 2568 933                                                          
feat 5  1400 5 2 l xy                                                           
coor 2568 933 2568 903                                                          
feat 6  1400 5 2 l xy                                                           
coor 2508 903 2568 903                                                          
feat 7  1400 5 2 l xy                                                           
coor 2508 873 2508 903                                                          
feat 8  1400 5 2 l xy                                                           
coor 2568 903 2568 873                                                          
feat 9  1400 5 2 l xy                                                           
coor 2508 873 2568 873                                                          
feat 20  1100 5 2 p xy                                                          
coor 2520 920                                                                   
attr  10875,  104 Oak                                                           
feat 21  1133 5 0 l xy                                                          
coor 2530  920                                                                  


                                                                     131
attr 2-story  10875                                                             
feat 22  1100 5 2 p xy                                                          
coor 2520  890                                                                  
attr 10874,  106 Oak                                                            
feat 23  1133 5 0 l xy                                                          
coor  2530 890                                                                  
attr bungalow 10874                                                             
                                                                                
udb-polygon                                                                     
poly 3 20 r e                                                                   
poly 4 20 r e                                                                   
poly 6 20 l e                                                                   
poly 5 20 r e                                                                   
poly 6 22 r e                                                                   
poly 8 22 r e                                                                   
poly 9 22 l e                                                                   
poly 7 22 r e                                                                   
                                                                                
udb-indirect                                                                    
table road_types free                                                           
field r_type    char 12 i u n  "road type"                                      
field maint     char 2         "maintenance class"                              
field resp_code char 3  n      "responsibility code"                            
attr highway    m3  A-4                                                         
attr aterial    m6  B-3                                                         
attr secondary  n2  B-1                                                         
attr suburban   s4  B-8                                                         
                                                                                
                                                                                
udb-indirect                                                                    
table house_types  free                                                         
field h_type    char 10  i u n "house  types"                                   
field tax_code  char 4   n     "taxation code"                                  
attr bungalow  10-5                                                             
attr 2-story   12-2                                                             
attr split     11-5                                                             
                                                                                
udb-end                                                                         

  B. 7. 4 ANSII standard                                    
          --------------
 
The new standard format for interchange will be supported when test data become 
available.                                                                      

  B. 7. 5 SIF format (not available)                        
          --------------------------
 
SIF format will be supported if there is a demand.                              
Data files appear to be 80 character ascii files.                               
                                                                                
The files contain a series of commands that define how the coordinates are to be
displayed.                                                                      
                                                                                
Most of the commands are ignored.                                               
                                                                                
The commands of value seem to be:                                               
                                                                                


                                                                     132
DID/ is the first record in the file, and gives some basic information. The     
parameter MO=2 or MO=3 gives the number of dimensions (compulsory?). Any Z value
is ignored.                                                                     
                                                                                
OVR/   defines the active level. This is stored in the relations as a number    
column 'ovr' as it seems to  be  effectively a layer.                           
                                                                                
ASC/ggnum defines the graphic group number, and is used to  form the entid of   
form SIFggnum.                                                                  
                                                                                
If ggnum is 0 the item is ignored (not appended).                               
                                                                                
If ggnum is <0 a number is assigned to it (sequentially starting at 10001).     
                                                                                
LST/xx, defines a line. There are 2-101 vertices in a record. If a record has   
101 values and the next record starts with the same point as the end point it is
taken to be a continuation. (actually found some records with more than 101)    
                                                                                
LST/ and LST/OP are line strings.                                               
                                                                                
LST/HO and LST/SO are polygons (solid & holes)                                  
                                                                                
Vertices are (x,y) or (x,y,z) according to the DID/ header.                     
                                                                                
New records that are not continuations are taken to be new components.          
                                                                                
                                                                                

  B. 7. 6 DXF format                                        
          ----------
 
Digitised map data can be entered into OzGIS in the AutoCAD Drawing Interchange 
and File format as lines, points and polygons.                                  
                                                                                
The format is described in the AutoCAD manuals.                                 
                                                                                
If the data are to be used for choropleth mapping (with attribute data)         
the entities must have been digitised  with handles to give the entities        
names. The hexadecimal handle values will become the zone (or point) names      
that will also have to be used in the attribute files. You can rename the       
entities with a combine file by using OzData, but the the easiest method is to  
edit the names with a word-processor. The names are treated as text.            
The handles are given in type 5 groups.                                         
                                                                                
The entities are processed as follows:                                          
                                                                                
LINEs are stored as line segments, and can only be used for line overlays       
as there is no left & right zone names to enable polygons to be built.          
                                                                                
POINTs are stored as points. Any handle will be used as the name.               
                                                                                
POLYLINE & VERTEXes give a series of points that are either lines for line      
overlays, or polygons if a bit flag values defines it as closed. If a           
handle value is given it becomes the name and attribute values can be linked    
to it (polygons).                                                               
                                                                                
TEXT entities are stored as points with the text group used as the name         
or for assigning attribute values (first 10 characters).                        


                                                                     133
                                                                                

  B. 7. 7 ATLAS Export Format                               
          -------------------
 
Digitised boundary data can often be purchased in a format supported by the     
Atlas PC mapping system.                                                        
                                                                                
The files are Ascii, and records are of the form:                               
                                                                                
"name",n,x1,y1,...........Xn,Yn                                                 
                                                                                
where                                                                           
                                                                                
n=1 => a point                                                                  
n=2 => a circle                                                                 
n>2 => a polygon                                                                
n<0 => a line                                                                   
                                                                                
These data can be entered via the OzGIS system with some restrictions:          
                                                                                
. circles are not supported                                                     
                                                                                
. only the first 10 characters of the name can be used to assign attribute      
  values.                                                                       
                                                                                
. there cannot be more than one spatial object in a record                      
                                                                                
. The name of a polygon that is internal e.g. a lake, should be "OUTSIDE".      
                                                                                
                                                                                
An example file for africa AFRICA.DAT may be included with your system.         
                                                                                
Example file records from the africa files are:                                 
                                                                                
"Morocco",141                                                                   
13.92683,60.72203                                                               
13.92685,60.67901                                                               
13.99129,60.48547                                                               
14.1201,60.33495                                                                
14.24891,60.18444                       A POLYGON                               
14.3777,60.07695                                                                
14.48501,60.05548                                                               
14.61376,60.07703                                                               
14.72104,60.09858                                                               
14.80687,60.14163                                                               
    .                                                                           
    .                                                                           
"Tunisia",113                          A ZONE with 2 polygons                   
24.03397,61.15581                                                               
   .          .    polygon 1                                                    
   .          .                                                                 
24.03397,61.15581                                                               
25.49409,58.66141                                                               
   .          .    polygon 2                                                    
   .          .                                                                 
25.49409,58.66141                                                               
24.03397,61.15581   < - first point repeated after every polygon                


                                                                     134
                                                                                
                                                                                
    .                                                                           
    .                                                                           
"Mbabane",1                                                                     
41.41317,7.313157                                                               
"Maseru",1                                                                      
38.45704,4.957369                       POINTS                                  
"Pretoria",1                                                                    
39.15494,8.036585                                                               
    .                                                                           
    .                                                                           
    .                                                                           
"euro3",-41                                                                     
33.15051,61.9                                                                   
33.10709,61.72918                                                               
33.14988,61.68601                       A LINE                                  
33.21407,61.62125                                                               
33.34267,61.55629                                                               
    .                                                                           
    .                                                                           
    .                                                                           
Atlas seems to handle multiple polygons within a zone by simply putting them    
all together in the record following the name i.e. if the first vertex is       
found to be equal to another in the following list, then that is the end of     
that polygon and the next vertex is the start of the next polygon etc. For      
some strange reason the first point of the region is repeated after each        
of the polygons.                                                                
                                                                                
Atlas does not support topologically structured polygons, so ensure that        
internal polygons are given after the containing polygons so they are not       
overwritten on the screen. Also, internal polygons that are to have the         
background colour should have names "OUTSIDE".                                  
                                                                                
Apparently there are two possibilities for regions with multiple polygons:      
                                                                                
The polygons can be kept together, which results in the format which you        
see in the africa-files (see below). This is the default! The other             
possibility is to split the the region into separate polygons. This results     
in an export format where each polygon starts with the boundary name, number    
of vertices and then the vertices. (The easiest way to do this in ATLAS is      
to SELECT ALL, and then BOUNDARY, SPLIT, ISLANDS.)                              
                                                                                
The following is supposed to be from the ATLAS EXPORT/IMPORT MANUAL:            
                                                                                
ISLANDS AND LAKES                                                               
                                                                                
The Island/Lake Rule                                                            
--------------------                                                            
                                                                                
If you return to the firs coordinate pair in the description of a region,       
you have closed the main polygon. The line to the next coordinate pair          
will not be drawn, but will instead signal the start of an island or lake.      
The last coordinate pair in the island or lake must be the same as the first    
one; this must also be followed by the first coordinate pair of the main        
polygon - this line again will not be drawn. This rule may be applied as        
many times in succession as necessary, one time for each island or lake.        
                                                                                


                                                                     135
Curves created with Atlas*Draw can also have islands, but ASCII boundary        
files do not support this.                                                      
                                                                                
General Region Structure With Island/Lake                                       
------------------------------------------                                      
                                                                                
The format for a region containing an island and/or lake is:                    
                                                                                
"Pname","Sname",numxy                                                           
x1,y1                                                                           
..                                                                              
xn,yn                                                                           
x1,y1                                                                           
xx1,yy1,                                                                        
..                                                                              
xx1,yy1                                                                         
x1,y1                                                                           
                                                                                
The second xx1,yy1 pair closes the island or lake and is immediately            
followed by an x1,y1 pair, which closes back to the main polygon.               
Additional islands or lakes can follow, as long as each closes on itself        
and then closes back to the main polygon.                                       
                                                                                
The illustrations below show examples of a region with an island, and of a      
region with a lake containing an embedded region.                               
                                                                                
The region with an island is listed as:                                         
                                                                                
"Region w/Island",11                                                            
1,1 first coordinate pair                                                       
1,0                                                                             
0,0                                                                             
0,1                                                                             
1,1 end of main polygon                                                         
2,1 start of island                                                             
3,1                                                                             
3,0                                                                             
2,0                                                                             
2,1 end of island                                                               
1,1 end of main polygon                                                         
                                                                                
An entry for a region with a lake containing an embedded region:                
                                                                                
"Region w/lake",11                                                              
0,3 first coordinate pair                                                       
3,3                                                                             
3,0                                                                             
0,0                                                                             
0,3 end of main polygon                                                         
1,2 start of lake                                                               
1,1                                                                             
2,1                                                                             
2,2                                                                             
1,2 end of lake                                                                 
0,3 end of main polygon                                                         
"Embedded Region", 5                                                            
1,2                                                                             
2,2                                                                             


                                                                     136
2,1                                                                             
1,1                                                                             
1,2                                                                             
                                                                                
According to the documentation, regions with multiple polygons can name         
them all with a record of the form e.g. "poly1","poly2","poly3",num             
The data we have seen does not seem to do this, but just gives one name.        
                                                                                
                                                                                

  B. 7. 8 MapInfo Data Interchange Format                   
          -------------------------------
 
Many data suppliers can provide geographic data in a format suitable for use    
with the MapInfo mapping system.                                                
                                                                                
This format is partially supported, primarily for Census boundaries.            
The main restriction is that the more contrived spatial types are not supported.
                                                                                
The data is supplied usually as two files. The MapInfo Interchange File (MIF)   
contains the coordinates. The other file, the MID file, contains data, of which 
the only part of interest is the names of the spatial objects. Hence the MID    
file has to be given if you want to display attribute data, such as Census      
data, according to the names. Optionally the MID file need not be given, in     
which case the lines, points and polygons can only be used as overlays.         
                                                                                
                                                                                
The MIF file starts with a header of the form:                                  
                                                                                
             Version 2                                                          
             Delimiter ","                                                      
             CoordSys Earth Projection 1, 0                                     
             Columns 2                                                          
               Name Char(40)                                                    
               ID Integer                                                       
             Data                                                               
                                                                                
The only parts of the header used are:                                          
                                                                                
"Delimiter" defines the seperator used in the MID file, default <tab>           
                                                                                
"Columns" gives the number of values in the MID file for each object            
                                                                                
"Data" indicates the end of the header and start of the coordinates etc         
                                                                                
The data part of the file describes several types of objects. Only real         
geographic types are processed:                                                 
                                                                                
POINT and CENTER describe points (sites)                                        
LINE and PLINE describe line segments                                           
REGION describes zones (polygons)                                               
                                                                                
Entries such as PEN are ignored.                                                
                                                                                
A typical Census boundary file will have region entries with coordinates that   
will be output as polygons and centre's output as points. The polygons and the  
points will both have the same names from the MID file, so Census data can be   
mapped as either zones or sites, and the polygons and points can also be used   


                                                                     137
for overlays e.g. to put names on the polygons.                                 
                                                                                
                                                                                
For example, the data part of a MID file could look like:                       
                                                                                
Region 1                                                                        
  41                                                                            
147.30982 -42.851953                                                            
147.309298 -42.851559                                                           
147.309174 -42.851233                                                           
147.309033 -42.851096                                                           
147.308207 -42.851211                                                           
       .       .                                                                
       .       .                                                                
       .       .                                                                
       .       .                                                                
       .       .                                                                
       .       .                                                                
147.312079 -42.850697                                                           
147.310575 -42.851964                                                           
147.30982 -42.851953                                                            
    Pen (1,2,12582912)                                                          
    Brush (2,16777215,16777215)                                                 
    Center 147.308418 -42.848512                                                
Region 1                                                                        
  13                                                                            
147.286268 -42.838088                                                           
147.282985 -42.841294                                                           
147.283788 -42.842113                                                           
147.285434 -42.843622                                                           
147.286394 -42.844522                                                           
147.28709 -42.845175                                                            
147.289192 -42.847147                                                           
147.290486 -42.84662                                                            
       .       .                                                                
       .       .                                                                
       .       .                                                                
       .       .                                                                
                                                                                
The MID file provides the names of the objects as "columns". You will have      
to provide the number of the column that is the names (usually 1)               
                                                                                
If a polygon  is inside another it should have the name "OUTSIDE" so it         
will be displayed with the background colour.                                   
                                                                                
A MID file with the name in column 1 looks like:                                
                                                                                
Canberra,637                                                                    
Burra Creek,639                                                                 
Phred,640                                                                       
London,641                                                                      
Wagga Wagga,642                                                                 
1230807,644                                                                     
  .                                                                             
  .                                                                             
  .                                                                             
                                                                                


                                                                     138

  B. 8 Format of names files                             
      ---------------------
 
                                                                                
Names files give lists of zones, lines or sites which are to be used to         
restrict certain kinds of processing in OzGIS.                                  
                                                                                
The file would usually be prepared with a text editor, possibly operating       
on a file output from OzGIS.                                                    
                                                                                
     Comment Record:                                                            
     80       byte      comment describing the data                             
                                                                                
     Name Records (one per zone or line or site)                                
     10       byte      name                                                    
                                                                                

  B. 8. 1 Sample names file DEMOATTR.DAT                    
          ------------------------------
 
DEMONAMES.DAT - NAMES FILE                                                      
ZONE 1                                                                          
ZONE 2                                                                          
ZONE 4                                                                          
                                                                                

  B. 9 Format of colour names files (Removed from system)
      --------------------------------------------------
 
                                                                                
Colour names files are usually generated within OzGIS, but they may be          
entered as data files. The file X11-BGR is supplied.                            
                                                                                
Comment record:                                                                 
     80      byte       comment describing the file                             
                                                                                
Colour records:                                                                 
     40      byte       colour name (in ascending order)                        
     10      real       blue value, range 0.0 to 1.0                            
     10      real       green value, range 0.0. to 1.0                          
     10      real       red value, range 0.0 to 1.0                             
                                                                                
The demonstration file DEMOCOLNM.DAT looks like:                                
                                                                                
DEMO COLOUR NAMES FILE                                                          
aquamarine                                   .8314    1.0000     .4980          
blue                                        1.0000     .0000     .0000          
brown                                        .1647     .1647     .6471          
darkseagreen                                 .5608     .7373     .5608          
hotpink                                      .7059     .4118    1.0000          
lemonchiffon                                 .8039     .9804    1.0000          
lightskyblue                                 .9804     .8078     .5294          
mintcream                                    .9804    1.0000     .9608          
pink                                         .7961     .7529    1.0000          
purple                                       .9412     .1255     .6275          
royalblue                                    .8824     .4118     .2549          


                                                                     139
salmon                                       .4471     .5020     .9804          
steelblue                                    .7059     .5098     .2745          
turquoise                                    .8157     .8784     .2510          
yellowgreen                                  .1961     .8039     .6039          
                                                                                

  B.10 Format of combine files                           
      -----------------------
 
                                                                                
Combine files define new map zones in terms of zones in a base map, or site     
catchments in terms of percentages of base zones.                               
                                                                                
Comment record:                                                                 
     80      byte       comment describing the file                             
                                                                                
Header record:                                                                  
     10      integer    number of items defined                                 
                                                                                
                                                                                
Sets of records follow for the items:                                           
                                                                                
Item definition record:                                                         
     10      byte       name (ascending order)                                  
     10      integer    number of zones                                         
                                                                                
Zone records:                                                                   
     10      byte       zone name (ascending order)                             
     10      real       proportion of zone in area (0 to 1.0)                   
                                                                                
                                                                                

  B.10. 1 Sample combine file DEMOCOMB.DAT                  
          --------------------------------
 
This file defines three territories AREA1, AREA2, AREA3 in terms of base zones  
A, B, ......                                                                    
                                                                                
3 AREAS                                                                         
         3TEST AREAS                                                            
AREA1              1                                                            
H             1.0                                                               
AREA2              3                                                            
N             1.0                                                               
O             1.0                                                               
R             1.0                                                               
AREA3              5                                                            
A             1.0                                                               
B             1.0                                                               
C             1.0                                                               
D             1.0                                                               
E             1.0                                                               

  B.11 Format of presentation files                      
      ----------------------------
 
                                                                                
Presentation files give a set of saved map files that are to be referenced      


                                                                     140
by menu items so the maps can be easily displayed when giving demonstrations.   
                                                                                
Presentation files must have names with extension prs e.g. DEMO.PRS             
                                                                                
     First record:                                                              
                                                                                
     60      byte       menu header                                             
                                                                                
A pair of records is given for each saved display file                          
     60      byte       menu item text                                          
     50      byte       saved map file in full form                             
                                                                                

  B.11. 1 Sample presentation file                          
          ------------------------
 
AURISA Exhibition                                                               
Far East Asia zone map                                                          
DEMOFEA.SAV                                                                     
Lowe Electorate bivariate zone map                                              
BIVLOWE.SAV                                                                     
Diagram map                                                                     
DIAG1.SAV                                                                       
Zones & Sites map                                                               
ZONESITE.SAV                                                                    
Australia Statistical Division zones map                                        
DEMOOZ.SAV                                                                      
Canberra LGAs zone map with overlays                                            
ACT.SAV                                                                         

  B.12 Format of marker files                            
      ----------------------
 
                                                                                
Markers are displayed in OzGIS as single polygons using polygon fill.           
                                                                                
OzGIS has standard files available (star, triangle etc.) but a you can          
define your own.                                                                
                                                                                
A marker is a single closed polygon.  OzGIS requires that the points that       
define the polygon lie within a circle of unit diameter.                        
                                                                                
The data points are usually prepared by drawing the marker on graph paper,      
centred on the origin, and lying within a circle of radius 0.5.                 
                                                                                
     Comment record:                                                            
                                                                                
     80      byte       marker name, comments                                   
                                                                                
     Header record:                                                             
                                                                                
     10      integer    number of points (3-100)                                
                                                                                
     Boundary record:                                                           
                                                                                
     8x10    real       Polygon points (X,Y) 4 per record                       
                        Values are in the range (-0.5 to +0.5)  The last        
                        point must be the same as the first                     


                                                                     141
                                                                                

  B.12. 1 Sample marker file SQUARE.DAT                     
          -----------------------------
 
SQUARE.DAT - MARKER                                                             
         5                                                                      
-0.35     -0.35     -0.35     0.35      0.35      0.35      0.35      -0.35     
-0.35     -0.35                                                                 

  B.13 Format of device files                            
      ----------------------
 
                                                                                
Device files describe the characteristics of graphics display devices and set   
colours etc.                                                                    
                                                                                
Standard files are usually held on the system for all devices available. Users  
would not usually define their own.                                             
                                                                                
 OzGIS was designed to operate as a highly interactive colour mapping system    
where speed of display was obtained by the use of an  advanced raster display   
system.                                                                         
                                                                                
 The software can operate on most graphics devices, but there could be loss of  
speed and capabilities depending on the characteristics of the devices being    
used.                                                                           
                                                                                
 OzGIS is based on graphics packages with the functionality of the GKS graphic  
standard. These graphic packages provide graphic primitives such as lines,      
text, and filled polygons. An important feature of GKS is that it is device     
independent so the package allows OzGIS to produce maps on a large range of     
devices.                                                                        
                                                                                
 Every device available for use with OzGIS has at least one file associated with
it.                                                                             
                                                                                
All devices within OzGIS have the same characteristics so e.g. a map previewed  
on a display device can be output directly to a hard-copy device. The files     
ensure that a device with limited capabilities can  simulate the required       
capabilities in the best way.                                                   
                                                                                
 The device files also set GKS primitive attributes such as colours and zone    
fill types. A colour display system has several files available that provide    
standard sets of colours for maps. Files with similar colours are usually       
available for different devices for hard-copy generation.                       
                                                                                
The easiest way to generate device data files is to edit standard ones.         
                                                                                
The device files require colours to be specified in blue,green,red. One way to  
decide on these values is to look at the definitions in the colour names data   
file \ozgis\x11-bgr.dat.                                                        
                                                                                
Hardcopy device files are based on the SCIPLOT package which has a fixed set of 
colours. Of course plotter colours depend on the pens. SCIPLOT colours are:     
     Black                                                                      
     Blue                                                                       
     Green                                                                      


                                                                     142
     Cyan                                                                       
     Red                                                                        
     Magenta                                                                    
     Brown                                                                      
     Light Gray                                                                 
     Dark Gray                                                                  
     Light Blue                                                                 
     Light Green                                                                
     Light Cyan                                                                 
     Light Red                                                                  
     Light Magenta                                                              
     Yellow                                                                     
     White                                                                      
                                                                                
                                                                                
                                                                                
     Comment record:                                                            
                                                                                
     80      byte       Device description                                      
                                                                                
                                                                                
     Size record:                                                               
                                                                                
     10      real       Extent of device surface                                
     Note: defines units used for all sizes in data i.e. divide by this         
     10      real       width of device in device units (now set from OZGIS.INI)
     10      real       max address height of device    (now set from OZGIS.INI)
                                                                                
     Type record:                                                               
                                                                                
     10      integer    GKS workstation number                                  
     10      integer    Display type, 1 = raster display, pixel addressed       
                                      2 = continuous coordinates                
     10      integer    Fill type, 1 = solid colour                             
                                   2 = pattern                                  
                                   3 = hatch                                    
     10      integer    Locator device number, 0 = none, 1 = default            
                                               2 = crosshairs                   
                                                                                
     Advanced Raster Record  (now set fromOZGIS.IN)                             
                                                                                
     10      integer    number of bit planes (1-24)                             
     10      integer    length of LUT (1-4096)                                  
     10      integer    number of pixels across screen (256-4096)               
     10      integer    number of lines on screen (256-4096)                    
     10      integer    run-length encoding/decoding, 0 = not available         
                                                                                
     Colour definition record:                                                  
                                                                                
     10      integer    number of colours defined                               
                                                                                
     Colour table records:                                                      
                                                                                
     10      real       blue value (0.0 - 1.0) for colour table                 
     10      real       green                                                   
     10      real       red                                                     
                                                                                
     Hatch definition record:                                                   


                                                                     143
                                                                                
     10      integer    number of hatch patterns (0 - 256)                      
                                                                                
     Hatch records (if required):                                               
                                                                                
     10      integer    line number (1 - 8)                                     
                        (from overlay and quant. lines)                         
     10      real       line angles (0.0 - 180.0)                               
     10      real       line separation  (<0.1)                                 
     10      integer    line number (0 - 4) , 0 = not used                      
     10      real       second line angle (if reqd)                             
     10      real       second line separation (if reqd)                        
                                                                                
The rest of the data records set internal tables for GKS primitive              
attributes.  Most records reference the colour table; the index has range 1     
to length of table.                                                             
                                                                                
                                                                                
A style table is used with the colour table for polygon fill according to       
the fill type.                                                                  
                                                                                
-  SOLID - the colour is used, style not relevant                               
-  HATCH - the pen colour is obtained from the colour table, the hatch          
           pattern number from the style table                                  
-  PATTERN - the colour table is not used, the style table gives the device     
             dependent pattern number                                           
                                                                                
Area Fill records:                                                              
                                                                                
10   integer            colour index                                            
10   integer            fill or style index                                     
                                                                                
Several fill records are required, in following order:                          
                                                                                
-  background. NOTE also the menu / messages/ everything colour                 
-  zone missing data                                                            
-  excluded zones                                                               
-  diagram background                                                           
-  line or site quantisation legend and diagram                                 
-  8 polygon underlay records                                                   
                                                                                
Text records:                                                                   
                                                                                
10   integer            colour index                                            
10   integer            font number  (1-9)                                      
10   integer            text precision 0=STRING, 1=CHAR, 2=STROKE               
10   real               height of character space (pixels)                      
10   real               width of character space  (pixels)                      
                                                                                
Note:  on display devices hardware text of known size will be used.             
Fonts are available for use on the screen, but are more usually used for output 
on plotters.                                                                    
                                                                                
The following fonts are available:                                              
                                                                                
1 VGA/EGA hardware font or default hardcopy font                                
2 Simplex Roman, the most basic                                                 
3 Duplex Roman, more detailed than the simplex with about twice as many strokes 


                                                                     144
4 Complex Roman, similar but with more tapered segments                         
5 Triplex Roman, heavier version                                                
6 Simplex script, based on handwriting                                          
7 Complex script                                                                
8 Complex italic italic version of complex roman                                
9 Triplex italic                                                                
                                                                                
The text records are:                                                           
                                                                                
4 records to define the text available for name overlays at sites or typed      
in text.                                                                        
The text is usually defined in increasing size order.                           
                                                                                
Legend text record:  This is fixed size text used for generation of all the     
legends.  The size is very important as it governs the overall size of the      
legend e.g. the zone legend boxes are 3 times the text height in height, 2      
times the text width in width.                                                  
                                                                                
Attribute description text record:  This is normally large text.  The           
interactive system has to be able to clear it off for each attribute so it      
should be fixed size hardware text in that case.  When two variates are         
displayed the two descriptions are separated by                                 
 a 'VS' or 'AND' generated using the                                            
legend text.                                                                    
                                                                                
                                                                                
Line records:                                                                   
                                                                                
10   integer            colour index                                            
10   integer            GKS type (1-4)                                          
                        1 = solid, 2 = dashed, 3 = dotted, 4 = dash dot         
                                                                                
The actual records are as follows:                                              
                                                                                
4 records for lines to be used for line overlays.                               
                                                                                
4 records for lines to be used for quantised lines (line-type has no            
meaning here as types are assigned according to quantisation).                  
                                                                                
Note that these first 8 records also define the hatching                        
plotter 'pens' if applicable.                                                   
                                                                                
A record to define zone boundaries line.                                        
                                                                                
A record to define the line used to draw axes on diagrams (should be            
solid).                                                                         
                                                                                
A record to define the line used to draw statistical values on diagrams.        
                                                                                
Marker records:                                                                 
                                                                                
10     integer     colour index                                                 
10     integer     fill style index                                             
10     real        marker height (and width)                                    
40     byte        marker file name, left aligned, system format                
                                                                                
The records are as follows:                                                     
                                                                                


                                                                     145
4 records for markers to be used as overlays at sites.                          
                                                                                
4 records for markers used for sites with quantised attribute data (marker      
size has no meaning, is set for class).                                         
                                                                                
1 record for site marker background  (currently not used)                       
                                                                                
1 record for scatter diagram (GKS marker no 1)                                  
                                                                                
Colour Sequence records (170 records):                                          
                                                                                
10     integer  colour index                                                    
10     integer  style index                                                     
                                                                                
These records give sequences of colours (or patterns) or hatching for           
colouring zones after quantisation.                                             
                                                                                
There are two types of sequence:                                                
                                                                                
-  a 121 value array for single variate zones followed by                       
-  a 7x7 array for bivariate                                                    
                                                                                
                                                                                
The class fill is found by sampling out of the sequence for the number of       
classes, e.g. for bivariate                                                     
                                                                                
2 classes         1        7                                                    
3 classes         1   4    7                                                    
4 classes         1  3  5  7                                                    
                                                                                
Similarly, the single variate 121 value array allows exact sampling for         
number of classes 2-7; a best choice is made for 8,9 or 10 classes.  In the     
special case of pseudo-continuous colour maps the whole 121 values are          
used.                                                                           
                                                                                
Menu colour records (graphics mode, fixed for text mode)                        
                                                                                
10 integer background text number (1-8)                                         
10 integer foreground text number (1-8)                                         
                                                                                
The menu colours are:                                                           
                                                                                
1 main menus                                                                    
2 lists                                                                         
3 help messages                                                                 
4 input of values                                                               
5 error messages                                                                
                                                                                
The 5 menu records use internal text numbers                                    
                                                                                
Note:  Files for advanced raster display systems with long LUT's should be      
set up as follows:                                                              
                                                                                
-  Display type = 1                                                             
-  Fill type = 1                                                                
-  LUT length 256 or greater                                                    
-  One LUT colour for each record in the data file i.e. all colour index        
   values unique                                                                


                                                                     146
                                                                                
The system by passes the colour index and style index when operating in         
fast interactive code and accesses the LUT directly.                            


                                                                     147
                     C. USA Census data                                   
                       ===============
 
                                                                                
                                                                                
                                                                                
                                                                                
This appendix describes the procedure for entering US Census Bureau CD-ROM      
files into the OzGIS system, and gives examples of the procedures to            
prepare data and display maps.                                                  
                                                                                
                                                                                
                                                                                
                                                                                
                                                                                

  C. 1 Overview                                          
      --------
 
The Census Bureau supplies data on CD-ROM. There are two types supported:       
                                                                                
1. the population and housing Census data (STF1A files), one State              
   per CD-ROM                                                                   
                                                                                
2. the digitised map data (TIGER format) supplied as one County per             
   CD-ROM                                                                       
                                                                                
The OzEnter program provides the facilities to input these data, BUT...         
                                                                                
THE FILES MUST BE NAMED IN THE CORRECT WAY as described later.                  
                                                                                
The CD-ROM files can be very large, but the internal OzGIS files are much       
smaller. Hence the  usual procedure will be to read the raw data files          
directly off CD-ROM. Processing can take some time.                             
                                                                                
The basic facility provided in the OzGIS system is to map tract/BNA or          
block group level data on a County basis. Census data can be extracted          
into one attribute file for one or more Counties. Census boundaries can         
be extracted into separate files for each county. Multiple county maps          
are generated by mapping the single attribute file with multiple geographic     
files.                                                                          
                                                                                
Data for map overlays (e.g. roads) can also be extracted from TIGER data.       
These data can be displayed without Census data.                                
                                                                                
Other data could be extracted from the CD-ROMs (e.g. blocks, places) and        
will be supported if there is demand.                                           
                                                                                
The capacity of the OzGIS system can be exceeded by these data. This should be  
corrected when the WINDOWS3.1 version becomes available as it will use          
extended memory. The capacity should be sufficient to produce tract/BNA maps    
with overlays for single counties in all cases.                                 
                                                                                
Generally the procedure for producing tract/BNA maps is to enter the TIGER      
data for the county of interest and all the STF1A files for the same county     
by selecting the appropriate options from the OzEnter menus.                    
                                                                                


                                                                     148
Usually a new DOS directory will be set up for each map area. It must be on     
the same disk as the \OZGIS directory.                                          
                                                                                
Census data is often not exactly what is required, so OzData program will       
probably be used to produce derived attributes. Common processing is to         
amalgamate age ranges and to normalise by dividing by total population.         
                                                                                
The boundary line segments will probably be thinned with OzData to reduce       
their size and speed up display.                                                
                                                                                
The polygons have to be built with OzZone to produce the final geographic       
file.                                                                           
                                                                                
Finally the data are mapped with OzCensus (simple maps) or OzGIS.               
                                                                                
Note that the number of tract/BNAs will often be under the magic 240 zone       
limit, so fast interacive mapping will be available on 256 colour super VGA     
systems if 16 colour device files are used. Otherwise you will have to keep     
redrawing the maps every time something changes.                                
                                                                                
The most important sections in this appendix are:                               
                                                                                
Processing STF1A data  and                                                      
OzGIS Processing of TIGER data                                                  
                                                                                
These sections follow, with an example and further more general information     
after that.                                                                     

  C. 2 Documentation                                     
      -------------
 
Extensive documentation is available from the Census Bureau and on the          
CD-ROMs.                                                                        
                                                                                
Some of that documentation is reproduced here.                                  

  C. 3 OzGIS Processing of TIGER data                    
      ------------------------------
 
You enter TIGER data into OzGIS with the OzEnter program.                       
                                                                                
Select INPUT GEOGRAPHIC FILES from the top menu and then                        
INPUT A TIGER FORMAT GEOGRAPHIC FILE                                            
                                                                                
The next menu is:                                                               
                                                                                
TRACTS / BNA                                                                    
BLOCK GROUPS                                                                    
BLOCKS                                                                          
ZIP CODES (IF PRESENT)                                                          
VOTING DISTRICTS                                                                
SELECT LANDMARKS BY FEATURE CODES                                               
SELECT LINES BY FEATURE CODES                                                   
SELECT POINTS BY FEATURE CODES                                                  
                                                                                
You will probably use options TRACTS / BNA and BLOCK GROUPS to extract          
boundaries for mapping with STF1A data. The OzZone program has to be used       
to build the polygons.                                                          


                                                                     149
                                                                                
The option SELECT LINES BY FEATURE CODES will also be used often to extract     
line overlay data such as roads.                                                
                                                                                
The Feature codes are described later in this appendix.                         
                                                                                
The TIGER files must be present on hard disk or CD-ROM  with file names in a    
restricted form.                                                                
                                                                                
It seems that each state is on at least one CD-ROM (some states like California 
are on two or more, but most are either on one by themselves or share           
a disk with one or two small states). The structure of the CD-ROM appears       
to be: general documentation and full state FIPS listing files at               
the top  (GRF_N_xx, where xx is the state's FIPS code); a subdirectory          
for each state named by its FIPS code (e.g. Indiana's subdirectory is 18); in   
each state's subdir are subdirectories for each county, again by FIPS codes     
(e.g. Allen County, Indiana is 003) using 3 digits; in each of these reside the 
(finally!) Tiger files of the form TGRXXYYY.F4n, where XX is the STATE code and 
YYY is the county code and n is the record format code.                         
                                                                                
You usually read data directly off CD-ROM by giving the full file name.         
The files will probably already be named correctly on CD-ROM, where they usually
to have extensions of the form ".F4n". e.g. e:/36/121/tgr36121.f41              
You give the name of any one of the files and that name is used as a            
template for the rest of the files.                                             
                                                                                
There are two forms of file name:                                               
                                                                                
Firstly, as files are often on CD-ROM with file names of the form, for          
example boondocks.f41, boondocks.f42, boondocks.f43 etc, the OzEnter            
process will look for sets of files with names of the form ????.f4n             
                                                                                
If no files are present of this form it will look for a second form, where      
the file names must contain the string "TGRn" where n is 1,2,3 or 7. This       
ensures that related files are named as a set. Files on hard disk are usually   
given names with extension ".DAT".                                              
                                                                                
Name examples on hard disk are WASHTGR1.DAT, WASHTGR2.DAT, WASHTGR3.DAT,        
WASHTGR7.DAT and  TGR1NY.DAT and TGR2NY.DAT                                     
                                                                                
Only the files of the required types are required:                              
                                                                                
Extracting Census boundaries usually requires types 1 and 2, but in some        
cases the zone names (e.g. voting districts or 1980 regions) require that       
the record type 3 file is also processed.                                       
                                                                                
Extracting lines by feature code requires types 1 and 2.                        
                                                                                
Extracting points by feature codes requires type 1.                             
Extracting landmark features by feature code requires type 7.                   
                                                                                
Address extraction by feature code requires types 1 and 2. Type 6 records       
are not processed.                                                              


                                                                     150

  C. 4 Processing STF1A data                             
      ---------------------
 
US Census data STF1A files can be entered into the system with the OzEnter      
program by choosing INPUT ATTRIBUTE FILES from the top menu and then            
one of:                                                                         
INPUT USA CENSUS STF 1A FILES FOR TRACT/BNA                                     
INPUT USA CENSUS STF 1A FILES FOR BLOCK GROUPS                                  
                                                                                
The data files must be present with names of the form *1An* where n is in       
the range 0 to 9. The supplied files on CD-ROM will probably have extensions    
DBF and file names in the correct form. Data files on hard disk are usually     
given the extension .DAT                                                        
                                                                                
Example file names are e:/xyz/stf1a0dc.dbf, stf1a0in.dat, wash1a3.dat           
You do not need to give the file extension if it is the default .DAT            
                                                                                
All files present will be processed, so anywhere between 1 and 10 files         
will be read. It takes a long time to read all the data, but it will be         
usual to load it all in once.                                                   
                                                                                
You give the name of any one of the files and that name is used as a            
template for the rest of the file names.                                        
                                                                                
If you only want to process one or two files you will have to copy them to hard 
disk. It will be usual to input files directly from CD-ROM as they can be very  
big. The internal files are much smaller as only a small part of the data is    
required.                                                                       
                                                                                
THE FIRST STF1A FILE (number zero) MUST ALWAYS BE PRESENT as it contains the    
level codes necessary to avoid multiple records being extracted.                
                                                                                
A parameter file must be given. These are described in the next section.        
You can use the supplied parameter file by giving the name as *STF1A, as        
described in the following section.                                             
                                                                                
You can also set up your own parameter file, probably by modifying the example  
provided.                                                                       
                                                                                
Attributes (table variables) that are not on the parameter file will not be     
processed, so a subset can be extracted by including just the appropriate       
entries in the file.                                                            
                                                                                
You give a list of numbers for the counties you want to process e.g.            
001, 005,...                                                                    
                                                                                
If all the values for an attribute are zero nothing is written to the output    
file for that attribute.                                                        
                                                                                
A log file is output to OZGIS.OUT which lists the attributes output and the     
position on the file. The positions are of value when generating new            
attributes as arithmetic expressions and for selecting attributes for display.  


                                                                     151

  C. 5 The STF1A parameter file                          
      ------------------------
 
A parameter file must be used to define the description, units and number of    
decimal places for each variable (field).                                       
                                                                                
A sample parameter file is provided:   \OZGIS\STF1A.PRM (i.e. called *STF1A)    
                                                                                
This file was generated by editing the STF1A data dictionary, and there is no   
guarantee that it is correct. (We would be pleased to accept a better version). 
                                                                                
The format is fixed, so ensure any file has data in the correct columns if you  
modify the file. The first line of the file is a comment, then there is one     
line for each Census table variable that is to be processed in the following    
format:                                                                         
                                                                                
 8 characters table name                                                        
 2 characters filler                                                            
30 characters variable description                                              
 2 characters filler                                                            
10 characters units description                                                 
 2 characters filler                                                            
 1 digit number of decimal places (0 or 2)                                      
                                                                                
                                                                                
The example parameter file is as follows:                                       
                                                                                
Sample STF1A parameter file                                                     
P0010001  TOTAL  PERSONS                  PERSONS     0                         
P0020001  TOTAL  FAMILIES                 FAMILIES    0                         
P0030001  TOTAL HOUSEHOLDS                HOUSEHOLDS  0                         
P0040001  PERSONS INSIDE URBANIZED AREA   PERSONS     0                         
P0040002  PERSONS OUTSIDE URBANIZED AREA  PERSONS     0                         
             .                                                                  
             .                                                                  
             .                                                                  
             .                                                                  
             .                                                                  

  C. 6 Example                                           
      -------
 
You should have looked at the early chapters on using OzCensus and OzEnter      
before you look at this example.                                                
                                                                                
                                                                                
Suppose you want to produce a map of 1990 Census data for three counties in     
Texas for tract/BNA zones.                                                      
                                                                                
First you look up the county FIPS codes in the documentation:                   
                                                                                
48         Texas                                                                
     .                                                                          
     .                                                                          
48   047   Brooks County                                                        
     .                                                                          


                                                                     152
     .                                                                          
48   117   Deaf Smith County                                                    
     .                                                                          
     .                                                                          
48   301   Loving County                                                        
                                                                                
So the codes are 047, 117 and 301.                                              
                                                                                
                                                                                
Now set up a directory to work in on the SAME disk as the \OZGIS directory.     
                                                                                
e.g.                                                                            
CD \                                                                            
MKDIR TEXAS                                                                     
CD TEXAS                                                                        
                                                                                
                                                                                
Now get the CD-ROM with the STF1A file for Texas and the TIGER CD-ROMs for      
the three counties.                                                             
                                                                                
What you need to do is to prepare an attribute file with Census data for        
the three counties and three geographic files, one for each county.             
                                                                                
                                                                                
You will probably find it most profitable to work through this example          
using your own CD-ROM files.                                                    
                                                                                
                                                                                
                                                                                
Step1: input the Census data                                                    
----------------------------                                                    
                                                                                
Mount the STF1A CD-ROM in the drive. Suppose the files are called               
TEXAS1A0.DBF ......... TEXAS1A9.DBF.                                            
                                                                                
Type OZENTER to start the program                                               
                                                                                
A menu appears:                                                                 
                                                                                
TUTORIALS & SYSTEM INFORMATION                                                  
INPUT GEOGRAPHIC FILES                                                          
INPUT ATTRIBUTE FILES                                                           
INPUT A NAMES FILE                                                              
INPUT A COMBINE FILE                                                            
INPUT A DEVICE FILE                                                             
INPUT A MARKER FILE                                                             
                                                                                
select the option to INPUT ATTRIBUTE FILES                                      
                                                                                
A new menu appears:                                                             
                                                                                
INPUT A STANDARD FORMAT ATTRIBUTE FILE                                          
INPUT A LOTUS 1-2-3 FORMAT ATTRIBUTE FILE                                       
INPUT A DATABASE (SIMPLE) FORMAT ATTRIBUTE FILE                                 
INPUT A LAMM FORMAT ATTRIBUTE FILE                                              
INPUT USA CENSUS STF 1A FILES FOR TRACT/BNA                                     
INPUT USA CENSUS STF 1A FILES FOR BLOCK GROUPS                                  
INPUT ATLAS DATA FILES                                                          


                                                                     153
                                                                                
Obviously you now select:                                                       
                                                                                
INPUT USA CENSUS STF 1A FILES FOR TRACT/BNA                                     
                                                                                
Give the input data file as E:/xxx/TEXAS1A0.DBF (using the correct drive)       
                                                                                
Give the output attribute file as TEXAS1 (no extension!!)                       
                                                                                
Give the parameter file as *STF1A                                               
                                                                                
Give the numbers for the counties i.e. 047, 117 and 301.                        
                                                                                
All the files will be processed. Trace messages will say what is going on.      
                                                                                
Type F10 to exit from the program.                                              
                                                                                
Either print the file OZGIS.OUT or copy it to a file. This is a list of         
the census variables and their positions in the attribute file.                 
                                                                                
                                                                                
Some comments ....... the file name given (TEXAS1A0.DBF) is used as a template  
to generate the other file names (TEXAS1A1.DBF etc) and all files in the set    
on the CD-ROM are processed.                                                    
                                                                                
If the file name is not of the standard form you have to copy the files to      
hard disk and rename them.                                                      
                                                                                
You can process just some of the files by copying them to hard disk (the first  
file, number zero, must always be there). i.e. all the files present are        
processed.                                                                      
                                                                                
                                                                                
Step2: derive census variables (optional)                                       
-----------------------------------------                                       
                                                                                
You now have an attribute file called TEXAS1 ready for mapping. However,        
raw Census variables are often not exactly what you want.                       
                                                                                
Suppose you actually want to map teenagers in the age group 12 to 15 years old. 
                                                                                
Also, if you are interested in the way the data are spatially distributed you   
have to normalise the data to allow for differences in the total number of      
people in the different tract/BNAs.                                             
                                                                                
This can be done as follows:                                                    
                                                                                
First look at the file OZGIS.OUT from the OzEnter run to find the variable      
numbers. Suppose it looks like:                                                 
                                                                                
  1  TOTAL  PERSONS                                                             
    .                                                                           
    .                                                                           
    .                                                                           
108  12 AND 13 YEARS                                                            
109  14 YEARS                                                                   
110  15 YEARS                                                                   
    .                                                                           


                                                                     154
    .                                                                           
    .                                                                           
                                                                                
The new variable is the sum of the three age variables, divided by the total.   
                                                                                
                                                                                
Now type OZDATA to execute the data preparation program.                        
                                                                                
The menu looks like:                                                            
                                                                                
PROCESS ATTRIBUTE FILES                                                         
PROCESS GEOGRAPHIC FILES                                                        
PROCESS NAMES FILES                                                             
OUTPUT EXTERNAL DATA FILES                                                      
                                                                                
                                                                                
Select PROCESS ATTRIBUTE FILES, which gives another menu:                       
                                                                                
FORM ATTRIBUTES WITH ARITHMETIC EXPRESSIONS                                     
AMALGAMATE ATTRIBUTE DATA FOR AN COMBINE FILE                                   
                                                                                
                                                                                
Select FORM ATTRIBUTES WITH ARITHMETIC EXPRESSIONS                              
                                                                                
                                                                                
Now you have to specify an input attribute file, which is here TEXAS1, and a    
new output file, say TEXAS2                                                     
                                                                                
You can then define a series of arithmetic operations (type H for help)         
                                                                                
So you give the arithmetic expression as:                                       
                                                                                
(#108+#109+#110) / #1 * 100.0                                                   
                                                                                
You also have to give a description, say "12 TO 15 YEAR OLDS" and a             
units description, say "%POP".                                                  
                                                                                
Type an expression "E" to exit, and then type F10 to quit the program.          
                                                                                
                                                                                
                                                                                
Step 3: Enter the TIGER data                                                    
----------------------------                                                    
                                                                                
You will have a CD-ROM for each County. Put the first in the drive.             
                                                                                
Suppose the files for Brooks County have names tgr48047.d41, tgr48047.f42 etc   
                                                                                
Type OZENTER to start the program.                                              
                                                                                
select INPUT GEOGRAPHIC FILES and then INPUT A TIGER FORMAT GEOGRAPHIC FILE.    
                                                                                
The TIGER menu is:                                                              
                                                                                
TRACTS / BNA                                                                    
BLOCK GROUPS                                                                    
BLOCKS                                                                          
ZIP CODES (IF PRESENT)                                                          


                                                                     155
VOTING DISTRICTS                                                                
SELECT LANDMARKS BY FEATURE CODES                                               
SELECT LINES BY FEATURE CODES                                                   
SELECT POINTS BY FEATURE CODES                                                  
                                                                                
Obviously, you need to select TRACTS / BNA as that is what you extracted        
Census data for.                                                                
                                                                                
As before, give the input data as the name of one of the CD-ROM files, say      
D:/48/047/TGR48047.F42, and the new geographic file as say BROOKS1              
                                                                                
If there are problems reading the files you may have to copy the ones required  
to hard disk and rename them, as described in previous sections.                
                                                                                
The file BROOKS1 contains the lines that form the boundaries of the tract/BNAs. 
                                                                                
Suppose you also would like to display a lines overlay on your map of important 
roads.                                                                          
                                                                                
Looking at the section on feature codes you find that a range of 110 to 128     
covers primary and secondary roads.                                             
                                                                                
So, select SELECT LINES BY FEATURE CODES                                        
                                                                                
Give the input data file as before, and the output geographic file as           
say BROOKRD                                                                     
                                                                                
Give the feature code range as found: 110 to 128                                
                                                                                
                                                                                
Repeat the process for the TIGER files for each of the counties so you          
end up with a geographic file of boundaries for tract/BNAs for each county,     
and line overlay files for the roads.                                           
                                                                                
type F10 to exit.                                                               
                                                                                
                                                                                
                                                                                
Step4: Simplify lines                                                           
---------------------                                                           
                                                                                
Often you will want to thin the lines data i.e. throw away a lot of the points. 
                                                                                
You do this for several reasons:                                                
                                                                                
.  The less the number of vertices the faster map display is.                   
                                                                                
.  You often dont care if the map is particularly accurate, its the attribute   
data you are interested in.                                                     
                                                                                
.  Your screen is low resolution, there is no advantage in having many vertices 
for each pixel on the monitor.                                                  
                                                                                
.  When you form polygons from the lines the number of vertices in some         
polygons may exceed system limits.                                              
                                                                                
.  Geographic files take less disk space after thinning.                        
                                                                                


                                                                     156
                                                                                
Simplification is an option in the OzData program which reads a geographic      
file and outputs a new one where the line segments have less points.            
                                                                                
So, type OZDATA to execute the program.                                         
                                                                                
Select PROCESS GEOGRAPHIC FILES and then select SIMPLIFY (THIN) LINE SEGMENTS   
                                                                                
                                                                                
Give the input file as BROOKS1 and the new output file as BROOKS2.              
                                                                                
The resolution for thinning is given as the number of pixels. For example,      
if you are displaying maps on a standard VGA at 640 X 480 you might give        
the resolution as 450 pixels. If you are more interested in speed of            
display than appearance give a value of 100.                                    
                                                                                
Repeat for the other files.                                                     
                                                                                
type F10 to exit.                                                               
                                                                                
                                                                                
                                                                                
Step5: Form polygons from lines                                                 
-------------------------------                                                 
                                                                                
The geographic files of tract/BNAs contain the line segments that form the      
boundaries of the Census regions.                                               
                                                                                
You have to form the zone / polygon / line structure by joining the ends of     
the lines to form polygons, finding which polygons form the zones and           
working out which polygons are inside others.                                   
                                                                                
                                                                                
Type OZZONE to run the program.                                                 
                                                                                
Select BUILD ZONES FROM LINE SEGMENTS INTO NEW GEOGRAPHIC FILE                  
                                                                                
Give the input geographic file as BROOKS2                                       
                                                                                
Give the output geographic file as BROOKS                                       
                                                                                
The program will now build the polygons etc.                                    
                                                                                
Repeat for the other tract/BNA boundary files (not the roads!)                  
                                                                                
type F10 to quit.                                                               
                                                                                
If you type "DIR BROO*.GEO" you will find that you have the three geographic    
files created during processing:                                                
                                                                                
BROOKS.GEO                                                                      
BROOKS1.GEO                                                                     
BROOKS2.GEO                                                                     
                                                                                
You only need the final one, so you can delete BROOKS1.GEO and BROOKS2.GEO      
                                                                                
                                                                                
                                                                                


                                                                     157
                                                                                
Step6: Display simple maps                                                      
--------------------------                                                      
                                                                                
You can start by displaying some simple maps with the OzCensus program.         
                                                                                
Type OZCENSUS to execute the mapping program.                                   
                                                                                
The first menu appears:                                                         
                                                                                
1 TUTORIALS & SYSTEM INFORMATION                                                
2 DISPLAY A NEW MAP                                                             
                                                                                
                                                                                
choose the option to "DISPLAY A NEW MAP".                                       
                                                                                
give your attribute file name i.e. TEXAS1                                       
                                                                                
and give your final geographic file name i.e. BROOKS                            
                                                                                
The data are now processed, the map is displayed, and the next menu appears.    
                                                                                
You now have a default map with legend and distribution diagram. The legend     
has the numbers of zones in each class on the left and the class value ranges   
to the right of the coloured boxes.                                             
                                                                                
If you use an option such as changing the displayed attribute you may have      
to type F3 to cause the new map to be displayed.                                
                                                                                
Refer to the chapter at the front of the manual on using OzCensus if you  have  
not already looked at the example there.                                        
                                                                                
type F10 to exit.                                                               
                                                                                
                                                                                
                                                                                
                                                                                
Step7: Display complex maps                                                     
---------------------------                                                     
                                                                                
Lets display a map with the three counties tract/BNA geographic files, called   
say BROOKS, DEAF and LOVING. The raw attribute file TEXAS1 will be used and     
the three road overlay files BROOKSRD, DEAFRD and LOVINGRD will be used.        
                                                                                
Type OZGIS to execute the main mapping program.                                 
                                                                                
the first menu enables you to select the type of map or diagram that is         
required:                                                                       
                                                                                
DISPLAY ZONES FOR AN ATTRIBUTE FILE                                             
DISPLAY LINES FOR AN ATTRIBUTE FILE                                             
DISPLAY SITES FOR AN ATTRIBUTE FILE                                             
DISPLAY BIVARIATE ZONES FOR TWO ATTRIBUTE FILES                                 
DISPLAY ZONES & LINES FOR TWO ATTRIBUTE FILES                                   
DISPLAY ZONES AND SITES FOR TWO ATTRIBUTE FILES                                 
DISPLAY GEOGRAPHIC FILES (NO ATTRIBUTES)                                        
DISPLAY ATTRIBUTE FILES (DIAGRAMS)                                              
DISPLAY A SAVED-DISPLAY FILE                                                    


                                                                     158
DISPLAY A PRESENTATION FILE                                                     
                                                                                
Select DISPLAY ZONES FOR AN ATTRIBUTE FILE for a straight forward               
choropleth map.                                                                 
                                                                                
Give the attribute file as TEXAS1 and give one of the geographic boundary       
files, say BROOKS.                                                              
                                                                                
A map will be displayed that will be the same as that with OzCensus. The        
difference is that you now have many more options for mapping.                  
                                                                                
The main menu is:                                                               
                                                                                
CHANGE ATTRIBUTES                                                               
DEFINE QUANTISATION                                                             
CHANGE DISPLAY FEATURES                                                         
DEFINE GEOGRAPHIC OVERLAYS                                                      
DEFINE MAP REGIONS                                                              
ANALYSE MAP DATA                                                                
SAVE DISPLAY FEATURES                                                           
                                                                                
                                                                                
                                                                                
First we will add the other two tract/BNA files to the map. This requires       
an understanding of map regions which are defined by both a geographic          
window and the part of the screen it is to appear on.                           
                                                                                
select DEFINE MAP REGIONS.                                                      
                                                                                
A menu then appears of the following form:                                      
                                                                                
CHANGE THE DISPLAYED ITEMS IN THE MAP                                           
CHANGE MAP REGION WINDOW (GEOGRAPHIC AREA)                                      
ZOOM MAP REGION WINDOW ABOUT X-HAIR POINT                                       
CHANGE MAP REGION VIEWPORT (SCREEN AREA)                                        
DEFINE NEW REGION FOR QUANTISED ZONES                                           
DISPLAY MORE QUANTISED ZONES ON A REGION                                        
DELETE QUANTISED ZONES FROM REGION                                              
                                                                                
What you do next depends on whether the counties are adjacent or not.           
                                                                                
If counties are adjacent, add the files to the existing map region as           
follows:                                                                        
                                                                                
select ZOOM MAP REGION WINDOW ABOUT X-HAIR POINT, choose a location with        
the cursor and mouse or arrows (select with left button or Enter). Give         
a zoom factor, say 4. Type F3 to regenerate the map in necessary.               
                                                                                
You now have space for the other counties. Select DISPLAY MORE QUANTISED ZONES  
ON A REGION and give the next boundary geographic file DEAF. Repeat for LOVING. 
                                                                                
If the counties are not adjacent you probably want to display the files in      
different parts of the screen in their own regions. Use the option              
DEFINE NEW REGION FOR QUANTISED ZONES to do this.                               
                                                                                
You probably end up with a mess. Use CHANGE MAP REGION WINDOW (GEOGRAPHIC AREA) 
and CHANGE MAP REGION VIEWPORT (SCREEN AREA) to clean up the map layout.        
                                                                                


                                                                     159
You often find that Census maps have very small polygons in the centres of      
cities. You can add "blow-ups" of the CBDs by using DEFINE NEW REGION FOR       
QUANTISED ZONES to add a geographic file a second time to the map and then      
use CHANGE MAP REGION WINDOW (GEOGRAPHIC AREA) to display just the desired      
area. (you can also use OzData to subset for complete polygons).                
                                                                                
Finally add the roads. Type ESC to go back to the main map menu and             
select DEFINE GEOGRAPHIC OVERLAYS                                               
                                                                                
A menu appears that offers options for several types of overlays:               
                                                                                
OVERLAY LINE SEGMENTS FROM A GEOGRAPHIC FILE                                    
OVERLAY MARKERS FOR SITES IN GEOGRAPHIC FILE                                    
OVERLAY NAMES FOR SITES IN GEOGRAPHIC FILE                                      
UNDERLAY POLYGONS FROM GEOGRAPHIC FILE                                          
OVERLAY LINE SEGMENTS FOR FEATURE CODES                                         
OVERLAY MARKERS FOR SITES FOR FEATURE CODES                                     
OVERLAY NAMES FOR SITES FOR FEATURE CODES                                       
UNDERLAY POLYGONS FOR FEATURE CODES                                             
                                                                                
Use OVERLAY LINE SEGMENTS FROM A GEOGRAPHIC FILE to overlay the road geographic 
files BROOKSRD, DEAFRD and LOVINGRD one at a time. If you have more than one    
region you will have to give the region number - the number is defined by the   
order the regions were defined. You could also use OVERLAY LINE SEGMENTS FOR    
FEATURE CODES and give a feature code range to subset the lines further.        
                                                                                
You may have to type F3 to regenerate the map i.e. to cause the changes to      
appear.                                                                         
                                                                                
You can add the names of the tract/BNAs to the map by using OVERLAY NAMES FOR   
SITES IN GEOGRAPHIC FILE and adding each of the boundary files.                 
                                                                                
Having spent all this time you dont want to lose the map, so save it with the   
option SAVE DISPLAY FEATURES from the main map menu.                            
                                                                                
                                                                                
The other options are all described fully elsewhere in the manual.              
                                                                                
                                                                                
type F10 to exit.                                                               
                                                                                


                                                                     160

  C. 7 OzGIS Census Zone Names                           
      -----------------------
 
Federal Information Processing Standards (FIPS) codes are assigned              
for a variety of geographic entities, including American Indian and             
Alaska Native area, congressional district, county, county subdivision,         
metropolitan area, place, and State. The structure, format, and meaning         
of FIPS codes used in the census are shown in the 1990 census                   
Geographic Identification Code Scheme; in the data dictionary portion of        
the technical documentation for summary tape files, CD-ROM's, and               
microfiche.                                                                     
                                                                                
The names assigned to Census polygons in OzGIS are generated from the           
standard codes.                                                                 
                                                                                
Tract / BNA name = 3digit county + 5 digit tract FIPS code                      
                                                                                
Block group name = 3digit county + 5 digit tract FIPS code + first block digit  
                                                                                
If you want to input your own data try generating a template attribute data     
file with OzData.                                                               
                                                                                
These names are unique only within a state.                                     

  C. 8 STF1A Census data                                 
      -----------------
 
Summary Tape File 1 (STF 1) contains 100-percent data.  Population items        
include age, race, sex, marital status, Hispanic origin, household type,        
and household relationship.  Population items are cross tabulated by age,       
race, Hispanic origin, or sex.  Housing items include occupancy/vacancy         
status, tenure, units in structure, contract rent, meals included in            
rent, value, and number of rooms in housing unit.  Housing data are cross       
tabulated by race or Hispanic origin of householder or by tenure.               
                                                                                
Selected aggregates and medians also are provided.  Data are presented in       
37 population tables (matrices) and 63 housing tables (matrices).               

  C. 9 STF1A Geographic areas                            
      ----------------------
 

  C. 9. 1 Blocks                                            
          ------
 
Census blocks are small areas bounded on all sides by visible features such     
as streets, roads, streams, and railroad tracks, and by invisible               
boundaries such as city, town, township, and county limits, property lines,     
and short, imaginary extensions of streets and roads.                           
                                                                                
  Tabulation blocks, used in census data products, are in most cases the        
same as collection blocks, used in the census enumeration. In some              
cases, collection blocks have been "split" into two or more parts               
required for data tabulations. Tabulation blocks do not cross the               
boundaries of counties, county subdivisions, places, census tracts or           
block numbering areas, American Indian and Alaska Native areas,                 


                                                                     161
congressional districts, voting districts, urban or rural areas, or             
urbanized areas. The 1990 census is the first for which the entire              
United States and its possessions are block-numbered.                           
                                                                                
  Blocks are numbered uniquely within each census tract or BNA. A block         
is identified by a three-digit number, sometimes with a single                  
alphabetical suffix. Block numbers with suffixes generally represent            
collection blocks that were "split" in order to identify separate               
geographic entities that divide the original block. For example, when a         
city limit runs through data collection block 101, the data for the             
portion inside the city is tabulated in block 101A and the portion              
outside, in block 101B. A block number with the suffix "Z"                      
represents a "crews-of-vessels" entity for which the Census                     
Bureau tabulates data, but that does not represent a true geographic            
area; such a block is shown on census maps associated with an anchor            
symbol and a census tract or block numbering area with a .99 suffix.            

  C. 9. 2 Block Groups                                      
          ------------
 
A geographic block group (BG) is a cluster of blocks having the same            
first digit of their three-digit identifying numbers within a census            
tract or block numbering area (BNA). For example, BG 3 within a census          
tract or BNA includes all blocks numbered between 301 and 397. In most          
cases, the numbering involves substantially fewer than 97 blocks.               
Geographic BG's never cross census tract or BNA boundaries, but may             
cross the boundaries of county subdivisions, places, American Indian            
and Alaska Native areas, urbanized areas, voting districts, and                 
congressional districts. BG's generally contain between 250 and 550             
housing units, with the ideal size being 400 housing units.                     

  C. 9. 3 Census tract and block numbering area             
          -------------------------------------
 
Block Numbering Area (BNA)                                                      
                                                                                
Block numbering areas (BNA's) are small statistical subdivisions of             
a county for grouping and numbering blocks in nonmetropolitan counties          
where local census statistical areas committees have not established            
census tracts. State agencies and the Census Bureau delineated BNA's            
for the 1990 census, using guidelines similar to those for the                  
delineation of census tracts. BNA's do not cross county boundaries.             
                                                                                
  BNA's are identified by a four-digit basic number and may have a              
two-digit suffix; for example, 9901.07. The decimal point separating            
the four-digit basic BNA number from the two-digit suffix is shown in           
printed reports, in microfiche, and on census maps; in machine-readable         
files, the decimal point is implied. Many BNA's do not have a suffix;           
in such cases, the suffix field is left blank in all data products. BNA         
numbers range from 9501 through 9989.99, and are unique within a county         
(numbers in the range of 0001 through 9499.99 denote a census tract).           
The suffix .99 identifies a BNA that was populated entirely by persons          
aboard one or more civilian or military ships. A "crews-of-vessels" BNA         
appears on census maps only as an anchor symbol with its BNA number (and        
block numbers on maps showing block numbers); the BNA relates to the ships      
associated with the onshore BNA's having the same four-digit basic number.      
Suffixes in the range .80 through .98 usually identify BNA's that either        
were revised or were created during the 1990 census data collection             


                                                                     162
activities. Some of these revisions produced BNA's that have extremely          
small land area and ay have little or no population or housing. For data        
analysis, such a BNA can be summarized with an adjacent BNA.                    

  C. 9. 4 Census Tract                                      
          ------------
 
Census tracts are small, relatively permanent statistical subdivisions of a     
county. Census tracts are delineated for all metropolitan areas (MA's) and      
other densely populated counties by local census statistical areas              
committees following Census Bureau guidelines (more than 3,000 census           
tracts have been established in 221 counties outside MA's). Six States          
(California, Connecticut, Delaware, Hawaii, New Jersey, and Rhode Island)       
and the District of Columbia are covered entirely by census tracts. Census      
tracts usually have between 2,500 and 8,000 persons and, when first             
delineated, are designed to be homogeneous with respect to population           
characteristics, economic status, and living conditions. Census tracts do       
not cross county boundaries. The spatial size of census tracts varies           
widely depending on the density of settlement. Census tract boundaries are      
delineated with the intention of being maintained over a long time so that      
statistical comparisons can be made from census to census. However,             
physical changes in street patterns caused by highway construction, new         
development, etc., may require occasional revisions; census tracts              
occasionally are split due to large population growth, or combined as a         
result of substantial population decline. Census tracts are referred to         
as "tracts" in all 1990 data products.                                          
                                                                                
  Census tracts are identified by a four-digit basic number and may have        
a two-digit suffix; for example, 6059.02. The decimal point separating          
the four-digit basic tract number from the two-digit suffix is shown in         
printed reports, in microfiche, and on census maps; in machine-readable         
files, the decimal point is implied. Many census tracts do not have a           
suffix; in such cases, the suffix field is left blank in all data               
products. Leading zeros in a census tract number (for example, 002502)          
are shown only on machine-readable files.                                       
                                                                                
  Census tract numbers range from 0001 through 9499.99 and are unique           
within a county (numbers in the range of 9501 through 9989.99 denote a          
block numbering area). The suffix .99 identifies a census tract that            
was populated entirely by persons aboard one or more civilian or                
military ships. A "crews-of-vessels" census tract appears on                    
census maps only as an anchor symbol with its census tract number (and          
block numbers on maps showing block numbers). These census tracts               
relate to the ships associated with the on-shore census tract having            
the same four-digit basic number. Suffixes in the range .80 through .98         
usually identify census tracts that either were revised or were created         
during the 1990 census data collection activities. Some of these                
revisions may have resulted in census tracts that have extremely small          
land area and may have little or no population or housing. For data             
analysis, such a census tract can be summarized with an adjacent census         
tract.                                                                          

  C. 9. 5 County                                            
          ------
 
The primary political divisions of most States are termed "counties." In        
Louisiana, these divisions are known as "parishes." In Alaska, which has no     
counties, the county equivalents are the organized "boroughs" and the           


                                                                     163
"census areas" that are delineated for statistical purposes by the State of     
Alaska and the Census Bureau. In four States (Maryland, Missouri, Nevada,       
and Virginia), there are one or more cities that are independent of any         
county organization and thus constitute primary divisions of their States.      
These cities are known as "independent cities" and are treated as               
equivalent to counties for statistical purposes. That part of Yellowstone       
National Park in Montana is treated as a county equivalent. The District of     
Columbia has no primary divisions, and the entire area is considered            
equivalent to a county for statistical purposes.                                
                                                                                
  Each county and county equivalent is assigned a three-digit FIPS code         
that is unique within State. These codes are assigned in alphabetical           
order of county or county equivalent within State, except for the               
independent cities, which follow the listing of counties.                       

  C. 9. 6 Hierarchical Presentation                         
          -------------------------
 
A hierarchical geographic presentation shows the geographic entities            
in a superior/subordinate structure in census products. This structure          
is derived from the legal, administrative, or areal relationships of            
the entities. The hierarchical structure is depicted in report tables           
by means of indentation, and is explained for machine-readable media in         
the discussion of file structure in the geographic coverage portion of          
the abstract in the technical documentation. An example of hierarchical         
presentation is the "standard census geographic hierarchy":  block, within      
block group, within census tract or block numbering area, within place,         
within county subdivision, within county, within State, within division,        
within region, within the United States. Graphically, this is shown as:         
                                                                                
 United States                                                                  
   Region                                                                       
     Division                                                                   
      State                                                                     
         County                                                                 
           County subdivision                                                   
            Place (or part)                                                     
               Census tract/block numbering area (or part)                      
                Block group (or part)                                           
                   Block                                                        

  C. 9. 7 Zip codes                                         
          ---------
 
ZIP Codes are administrative units established by the United States             
Postal Service (USPS) for the distribution of mail. ZIP Codes serve             
addresses for the most efficient delivery of mail, and therefore                
generally do not respect political or census statistical area                   
boundaries. ZIP Codes usually do not have clearly identifiable                  
boundaries, often serve a continually changing area, are changed                
periodically to meet postal requirements, and do not cover all the land         
area of the United States. ZIP Codes are identified by five-digit codes         
assigned by the USPS. The first three digits identify a major city or           
sectional distribution center, and the last two digits generally                
signify a specific post office's delivery area or point. For the 1990           
census, ZIP Code data are tabulated for the five-digit codes in STF 3B.         


                                                                     164

  C.10 The STF1A file                                    
      --------------
 

  C.10. 1 File Segments                                     
          -------------
 
The file is segmented into 10 dBase III (.DBF) files, designated                
STF1A0ss.DBF through STF1A9ss.DBF where ss is the two-character State           
abbreviation.  The STF1A0 segment contains the full 67 field identification     
section.  The identification field names are shown in the Data Dictionary       
chapter of the technical documentation.  Segments STF1A1 through STF1A9         
each contain seven identification fields repeated from the STF1A0 segment.      
They are shown below.                                                           
                                                                                
Identification Fields Common To All Segments                                    
                                                                                
         SUMLEV                    Summary Level                                
         STATEFP                   State (FIPS)                                 
         CNTY                      County (FIPS)                                
         COUSUBFP                  County Subdivision (FIPS)                    
         PLACEFP                   Place (FIPS)                                 
         TRACTBNA                  Census Tract/Block Numbering Area            
         BLCKGR                    Block Group                                  
         LOGRECNU                  Logical Record Number                        
                                                                                
The segments are divided as shown below.  Tables 12 and 13 go across            
segments.                                                                       
                                                                                
Data Tables In Each Segment                                                     
                                                                                
         STF1A0                    P1 - P10                                     
         STF1A1                    P11 - P12(pt.2)                              
         STF1A2                    P12(pt. 3) - P12(pt. 5)                      
         STF1A3                    P12(pt. 6) - P12(pt. 8)                      
         STF1A4                    P12(pt. 9) - P13(pt. 1)                      
         STF1A5                    P13(pt. 2) - P19                             
         STF1A6                    P20 - P35                                    
         STF1A7                    P36, H1 - H20                                
         STF1A8                    H21 - H40                                    
         STF1A9                    H41 - H55                                    
                                                                                
Parts of Table P12                                                              
                                                                                
(Each part contains 31 categories of age)                                       
                                                                                
         Part 1                    White males                                  
         Part 2                    White females                                
         Part 3                    Black males                                  
         Part 4                    Black females                                
         Part 5                    American Indian, Eskimo or Aleut males       
         Part 6                    American Indian, Eskimo or Aleut females     
         Part 7                    Asian or Pacific Islander males              
         Part 8                    Asian or Pacific Islander females            
         Part 9                    Other race males                             
         Part 10                    Other race females                          


                                                                     165
                                                                                
Parts of Table P13                                                              
                                                                                
(Each part contains 31 categories of age)                                       
                                                                                
         Part 1                    Hispanic origin males                        
         Part 2                    Hispanic origin females                      
                                                                                
You can process all or some of the files.                                       

  C.10. 2 Field Names In Numeric Data Tables                
          ----------------------------------
 
Fields in numeric data tables are named according to a convention which         
identifies the tables and the sequence of the data item within the table.       
The 310 data items in P12, for example, are identified as P0120001 through      
P0120310.  The one data item in table H23A is identified as H023A001.           
                                                                                
Components Of The Field Name                                                    
                                                                                
Character 1                    P or H                                           
Character 2-4                  Table number; right justified with               
                               leading zeroes                                   
Character 5                    Sub-table letter; zero if not applicable         
Character 6-8                  Item number; right justified with                
                               leading zeroes                                   

  C.11  TIGER US Census Digital Map Data                 
      ---------------------------------
 
The 1990 Census TIGER/Line file provides digital data for all 1990 census       
map features and boundaries, the associated 1990 census final tabulation        
geographic area codes (such as 1990 census block numbers), and the codes        
for the January 1, 1990 legal and statistical areas on both sides of each       
line segment of every mapped feature.  This version also contains the final     
voting district codes and the 1990 census designated place codes.               
                                                                                
The 1990 Census TIGER/Line files cover the entire United States, Puerto         
Rico, the Virgin Islands of the United States, American Samoa, Guam, the        
Northern Mariana Islands, Palau, the other Pacific entities that were part      
of the Trust Territory of the United States for the 1980 census (the            
Marshall Islands and the Federated States of Micronesia), and the Midway        
Islands (to provide complete mapping within the boundaries of the State of      
Hawaii).                                                                        

  C.12  TIGER files                                      
      ------------
 
The normal geographic coverage for a 1990 Census TIGER/Line file is a           
county.  The files can be combined to cover the whole Nation and its            
possessions.  Each 1990 Census TIGER/Line file consists of 12 record types      
that collectively contain geographic information (attributes) such as           
address ranges and ZIP codes for street segments (only in areas covered by      
the 1980 GBF/DIME-Files), names and codes of feature types, codes for legal     
and statistical entities, selected 1980 census geographic area codes,           
latitude/longitude coordinates of linear and point features, landmark           
features, area landmarks, and area and polygon boundaries.  The 12 record       
types are on the tape as 12 separate files.                                     


                                                                     166
                                                                                
                                                                                
The 1990 Census TIGER/Line file contains basic information for 1990 census      
geographic area codes, basic map features and their names, and address          
ranges in the form of 12 "Record Types."  The record types are as follows:      
                                                                                
     1.     Basic Data Records (Individual Feature Segment Records)             
     2.     Shape Coordinate Points (Feature Shape Records)                     
     3.     Additional Decennial Census Geographic Area Codes                   
     4.     Index to Alternate Feature Names                                    
     5.     Feature Name List                                                   
     6.     Additional Address Range and ZIP Code(2) Information                
     7.     Landmark Features                                                   
     8.     Area Landmarks                                                      
     A.     Additional Polygon Geographic Area Codes                            
     I.     Area Boundaries                                                     
     P.     Polygon Location                                                    
     R.     Record Number Range                                                 
                                                                                
Each segment record contains appropriate decennial census and, when             
appropriate, FIPS(1) geographic area codes, latitude/longitude coordinates      
for all line segments and point features, the name of the feature               
(including the relevant census feature class code identifying the segment       
by category), and, for areas formerly covered by the GBF/DIME-Files, the        
address ranges and the ZIP Code associated with those address ranges for        
each side of street segments.  For other areas, the TIGER/Line files do not     
contain address ranges or ZIP Codes.  The shape records provide coordinate      
values that describe the shape of those feature segments that are not           
straight.                                                                       
                                                                                
Record types 1,2,3 and 7 are processed by OzGIS. The types used depend on       
the options chosen:                                                             
                                                                                
Record Type 1:    Basic Data Record                                             
                                                                                
Record Type 1 provides a single record for each unique line segment in the      
1990 Census TIGER/Line file.  The end points of the line segments are           
expressed in latitude/longitude coordinate values in degrees and decimal        
fractions of a degree to six decimal places.  This record also contains         
address ranges and ZIP codes (in selected areas) and geographic area codes      
for each side of the line segment.  By convention, if one is standing at        
the "from" coordinate position facing the "to" coordinate position,             
data listed in the fields carrying a right qualifier would indeed be found      
to the right of the line segment.  Data users can collect the necessary         
segments to construct polygons and features that intersect from the             
information contained in this basic record.                                     
                                                                                
Record Type 2:   Shape Coordinate Points                                        
                                                                                
Record Type 2 provides an additional series of latitude and longitude           
coordinate values that describe the shape of each line segment that is not      
straight for the associated Record Type 1.  All coordinate values are           
expressed in degrees and decimal fractions of a degree of latitude and          
longitude.  The decimals are carried to six places to permit the                
representation of lines that are very close to one another.  If the segment     
in Record Type 1 is a straight line, there will not be a Record Type 2.         
                                                                                
Record Type 3:   Additional Decennial Census Geographic Area Codes              


                                                                     167
                                                                                
Record Type 3 includes the 1990 voting district codes provided to the           
Census Bureau for the 1990 Census Redistricting Data Program.  Record Type      
3 also includes some 1980 census geographic area codes and 1990 census          
geographic area codes not included on Record Type 1.  The 1980 census block     
numbers are available only for areas covered by the 1980 GBF/DIME-Files.        
During the conversion of the 1980 GBF/DIME-Files to the TIGER data base         
format, some 1980 census block numbers may have been deleted or changed.        
Users are advised to check all 1980 census geographic area codes,               
especially any 1980 block numbers, before using them in a planned               
application.  The Census Bureau has not verified any of the 1980 census         
geographic area codes in these files.  There will be discrepancies between      
the geographic area boundaries and codes in these files and the 1980 census     
maps, which are the basis for the 1980 census tabulations.                      
                                                                                
The TIGER/Line files may contain 1980 block numbers for portions of the         
country where the Census Bureau did not tabulate 1980 census data by block      
or block group.  These situations occur because these portions of the TIGER     
file originated from the 1980 GBF/DIME-Files that extended beyond the 1980      
block-numbered area.  Data users concerned about the validity of 1980 block     
numbers are advised to discard all 1980 block numbers that do not               
correspond to block numbers in the 1980 MARF or 1980 STF files.                 
                                                                                
Record Type 6:   Additional Address Range and ZIP Code Data                     
                                                                                
Record Type 6 provides additional address range information for a street        
segment when the information cannot be presented as a single address range      
(e.g., the house/building numbers are not uniformly arranged to form an         
address range).  Additional ZIP Codes, if any, also appear in Record Type 6     
for corresponding address ranges.  Record Type 6 appears only for those         
counties that have address ranges and ZIP Code information in the TIGER         
data base.  There is no assurance that the address ranges provided on           
Record Type 6 will be "shorter" than those appearing on Record Type 1.          
Data users must use Record Type 6 to obtain the complete picture of the         
potential address ranges along a segment.                                       
                                                                                
                                                                                
Record Type 7:   Landmark Features                                              
                                                                                
Record Type 7 contains the area and point landmarks in the Census Bureau's      
TIGER data base.  During the extraction of this data, we assigned a             
temporary Landmark Identification Number that we use to link the landmark       
attributes to the polygons that comprise the landmark.  If there is no          
landmark in a county file, there will be no Record Type 7 or Record Type 8      
for that county file.                                                           

  C.13 TIGER Geographic Area Definitions                 
      ---------------------------------
 
United States - The 50 States and the District of Columbia.                     
                                                                                
States and Statistically Equivalent Areas - The 50 States; in addition, we      
treat the District of Columbia, Puerto Rico, and each of the outlying           
areas-American Samoa, Guam, the Northern Mariana Islands, Palau, and the        
Virgin Islands of the United States-as statistical equivalents to States        
for presentation.  We also have TIGER/Line files for the Marshall Islands,      
the Federated States of Micronesia, and the Midway Islands.                     
                                                                                


                                                                     168
Counties, Parishes, Statistically Equivalent Areas - The first-order            
divisions of each State, the District of Columbia, Puerto Rico, and the         
outlying areas:  counties for 48 States; parishes for Louisiana; boroughs       
and census areas for Alaska; independent cities in Maryland, Missouri,          
Nevada, and Virginia; Yellowstone National Park in Montana, "District of        
Columbia" for the District of Columbia, municipios in Puerto Rico; other        
entities in the outlying areas.                                                 
                                                                                
Minor Civil Divisions (MCDs) - Legally defined subcounty areas such as          
towns and townships.  For the 1990 census, these are found in 28 States,        
Puerto Rico, and the outlying areas.                                            
                                                                                
Sub-MCDs - Legally defined subdivisions of a minor civil division;              
specifically,  subbarrios in Puerto Rico, and municipal districts in the        
Federated States of Micronesia.                                                 
                                                                                
Incorporated Places - Legal units incorporated as a city, town (excluding       
the New England States, New York, and Wisconsin), borough (excluding Alaska     
and New York), or village.                                                      
                                                                                
American Indian Reservations - American Indian areas with boundaries            
established by treaty, statute, and/or executive or court order.                
                                                                                
Alaska Native Regional Corporations (ANRCs) - Corporate entities                
established by the Alaska Native Claims Settlement Act (P.L. 92-203) to         
carry out the business and non-profit operations established by and for         
Native Alaskans under the Act.  Twelve ANRCs have specific boundaries and       
cover the State of Alaska except for the Annette Islands Reserve.               
                                                                                
Statistical Areas                                                               
                                                                                
Alaska Native Village Statistical Areas (ANVSAs) - 1990 census statistical      
areas that delineate the settled area of each Alaska Native village (ANV).      
Officials of Alaska Native Regional Corporations (ANRCs) and other              
appropriate State officials delineated the ANVSAs for the Census Bureau for     
the sole purpose of presenting census data.                                     
                                                                                
Tribal Designated Statistical Areas (TDSAs) - Geographic areas delineated       
for 1990 census data tabulation purposes by tribal officials of Federally       
and State-recognized tribes outside of Oklahoma that do not have a legally      
defined reservation.                                                            
                                                                                
Tribal Jurisdiction Statistical Areas (TJSAs) - Geographic areas delineated     
for 1990 census data tabulation purposes by tribal officials in Oklahoma        
for Federally recognized tribes that do not have a legally defined              
reservation.                                                                    
                                                                                
Census County Divisions (CCDs) - Areas delineated by the Census Bureau in       
cooperation with State and local officials in States where MCDs are not         
adequate for reporting subcounty statistics.                                    
                                                                                
Unorganized Territories (UTs) - Areas delineated by the Census Bureau for       
those portions of a State with MCDs where MCDs do not exist or are not          
adequate for reporting subcounty statistics.                                    
                                                                                
Census Designated Places (CDPs) - Densely settled population centers            
without legally defined corporate limits or corporate powers, defined in        
cooperation with State officials and local data users.                          


                                                                     169
                                                                                
Census Tracts - Small, locally delineated statistical areas within selected     
counties, generally having stable boundaries and, when first established by     
local committees, designed to have relatively homogeneous demographic           
characteristics.                                                                
                                                                                
Block Numbering Areas (BNAs) - Areas delineated by State governments or the     
Census Bureau for the purpose of grouping and numbering blocks in counties      
without census tracts.                                                          
                                                                                
Census Blocks - Small, usually compact areas, usually bounded by streets        
and other prominent physical features as well as boundaries of legal areas      
for which the Census Bureau tabulates data.  Blocks do not cross county,        
census tract, or BNA boundaries.                                                
                                                                                
Voting Districts (VTDs) - For the 1990 census, the term "voting district"       
replaces the 1980 census term "election precinct."  A voting district is        
any of a variety of areas (for example, election districts, precincts,          
legislative districts, wards) defined by State and local governments for        
purposes of elections.  The 1990 voting district codes that appear in the       
1990 census version of the TIGER/Line files were supplied by the State          
under the 1990 Census Redistricting Data Program.  The boundaries of the        
voting districts recorded in the TIGER/Line files may represent pseudo-         
voting districts; the States were required to have voting districts follow      
1990 census block boundaries, and therefore they may have had to relocate       
the boundaries of actual voting districts to a nearby feature used as a         
block boundary.  States had the option of participating in the program on a     
county-by-county basis.  Voting districts do not appear in all TIGER/Line       
files.                                                                          

  C.14 TIGER feature codes                               
      -------------------
 
Data can be extracted from the TIGER files and subset for display by            
feature codes.                                                                  
                                                                                
Feature codes are derived from the Census Feature Class Codes (CFCC)            
by changing the leading alphabetic character by its position in the             
alphabet.                                                                       
                                                                                
This is a series of codes that provides more detailed information on the        
classification of the line segment, such as class of road, class of stream,     
and so forth.                                                                   
                                                                                
A list of these codes follows.                                                  
                                                                                
CFCC    CLASSIFICATION A = ROAD FEATURES                                        
                                                                                
100     Road, Classification Unknown or Not Elsewhere Classified                
101     Road, undivided                                                         
102     Road, undivided, in tunnel                                              
103     Road, undivided, underpassing                                           
104     Road, undivided, rail line in center                                    
105     Road, divided                                                           
106     Road, divided, in tunnel                                                
107     Road, divided, underpassing                                             
108     Road, divided, rail line in center                                      
                                                                                


                                                                     170
110     Primary road, interstate highway and limited access road                
111     Primary road, interstate highway and limited access road, undivided     
112     Primary road, interstate highway and limited access road,               
         undivided, in tunnel                                                   
113     Primary road, interstate highway and limited access road,               
         undivided, underpassing                                                
114     Primary road, interstate highway and limited  access road,              
         undivided, rail line in center                                         
115     Primary road, interstate highway and limited access road, divided       
116     Primary road, interstate highway and limited access road, divided,      
         in tunnel                                                              
117     Primary road, interstate highway and limited access road, divided,      
         underpassing                                                           
118     Primary road, interstate highway and limited access road, divided,      
         rail line in center                                                    
                                                                                
120     Secondary road, U.S. highway not classified 110, and state roads        
121     Secondary road, U.S. highway not classified 110, and state roads,       
         undivided                                                              
122     Secondary road, U.S. highway not classified 110, and state roads,       
         undivided, in tunnel                                                   
123     Secondary road, U.S. highway not classified 110, and state roads,       
         undivided, underpassing                                                
124     Secondary road, U.S. highway not classified 110, and state roads,       
         undivided, rail line in center                                         
125     Secondary road, U.S. highway not classified 110, and state roads,       
         divided                                                                
126     Secondary road, U.S. highway not classified 110, and state roads,       
         divided, in tunnel                                                     
127     Secondary road, U.S. highway not classified 110, and state roads,       
         divided, underpassing                                                  
128     Secondary road, U.S. highway not classified 110, and state roads,       
         divided, rail line in center                                           
                                                                                
130     Connecting road, county roads, and roads not classified as 110 or       
         120                                                                    
131     Connecting road, county roads, and roads not classified as 110 or       
         120, undivided                                                         
132     Connecting road, county roads, and roads not classified as 110 or       
         120, undivided, in tunnel                                              
133     Connecting road, county roads, and roads not classified as 110 or       
         120, undivided, underpassing                                           
134     Connecting road, county roads, and roads not classified as 110 or       
         120, undivided, rail line in center                                    
135     Connecting road, county roads, and roads not classified as 110 or       
         120, divided                                                           
136     Connecting road, county roads, and roads not classified as 110 or       
         120, divided, in tunnel                                                
137     Connecting road, county roads, and roads not classified as 110 or       
         120, divided, underpassing                                             
138     Connecting road, county roads, and roads not classified as 110 or       
         120, divided, rail line in center                                      
                                                                                
140     Neighborhood roads, city streets and unimproved roads                   
141     Neighborhood roads, city streets and unimproved roads, undivided        
142     Neighborhood roads, city streets and unimproved roads, undivided,       
         in tunnel                                                              
143     Neighborhood roads, city streets and unimproved roads, undivided,       


                                                                     171
         underpassing                                                           
144     Neighborhood roads, city streets and unimproved roads, undivided,       
         rail line in center                                                    
145     Neighborhood roads, city streets and unimproved roads, divided          
146     Neighborhood roads, city streets and unimproved roads, divided, in      
         tunnel                                                                 
147     Neighborhood roads, city streets and unimproved roads, divided,         
         underpassing                                                           
148     Neighborhood roads, city streets and unimproved roads, divided,         
         rail line in center                                                    
                                                                                
150     Jeep trail, passable only by four-wheel drive (4WD) vehicle             
151     Jeep trail, passable only by four-wheel drive (4WD) vehicle,            
         undivided                                                              
152     Jeep trail, passable only by four-wheel drive (4WD) vehicle,            
         undivided, in tunnel                                                   
153     Jeep trail, passable only by four-wheel drive (4WD) vehicle,            
         undivided, underpassing                                                
                                                                                
160     Special Road Feature                                                    
161     Cul-de-sac                                                              
162     Traffic circle                                                          
163     Cloverleaf or interchange                                               
164     Service drive                                                           
165     Ferry crossing                                                          
                                                                                
170     Other Thoroughfare                                                      
171     Walkway                                                                 
172     Stairway                                                                
173     Alley                                                                   
                                                                                
NOTE:  In the portion of the TIGER/Line file prepared from the GBF/DIME-        
Files, the roads are classified as Class 4 roads with a few exceptions.         
The interstate highways that were identified by name as such in the             
GBF/DIME-File, are classified as Class 1 roads.  Also, in the GBF/DIME-File     
coverage areas, users may not find many roads with alternate names; if an       
alternate name is provided, it usually represents another local name and        
not a Route Number.                                                             
                                                                                
CFCC    CLASSIFICATION B = RAIL FEATURES                                        
                                                                                
200     Railroad, Classification Unknown or Not Elsewhere Classified            
201     Railroad track                                                          
202     Railroad track, in tunnel                                               
203     Railroad track, underpassing                                            
                                                                                
210     Railroad Main Track                                                     
211     Railroad main track                                                     
212     Railroad main track, in tunnel                                          
213     Railroad main track, underpassing                                       
                                                                                
220     Railroad Spur Track                                                     
221     Railroad spur track                                                     
222     Railroad spur track, in tunnel                                          
223     Railroad spur track, underpassing                                       
                                                                                
230     Railroad Yard                                                           
231     Railroad yard                                                           


                                                                     172
232     Railroad yard, in tunnel                                                
233     Railroad yard, underpassing                                             
                                                                                
240     Railroad Ferry Crossing                                                 
                                                                                
250     Other Rail Feature                                                      
251     Carline                                                                 
252     Cog railroad, incline railway, or logging tram                          
                                                                                
CFCC    CLASSIFICATION C = PIPELINES, POWER TRANSMISSION LINES, AND             
              MISCELLANEOUS TRANSPORTATION FEATURES                             
                                                                                
300     Special Transportation Feature, Classification Unknown or Not           
         Elsewhere Classified                                                   
                                                                                
310     Pipeline                                                                
                                                                                
320     Power Transmission Line                                                 
                                                                                
330     Other Special Transportation Feature                                    
331     Aerial tramway, monorail, or ski lift                                   
                                                                                
CFCC    CLASSIFICATION D = LANDMARK FEATURES                                    
                                                                                
400     Landmark Feature, Classification Unknown or Not Elsewhere               
         Classified                                                             
                                                                                
410     Military installation                                                   
                                                                                
420     Multihousehold and transient quarters                                   
421     Apartment building or complex                                           
422     Rooming or boarding house                                               
423     Trailer court or mobile home park                                       
424     Marina                                                                  
425     Crew of vessel                                                          
426     Housing facility for workers                                            
427     Hotel, motel, resort, spa, YMCA, or YWCA                                
428     Campground                                                              
429     Shelter or mission                                                      
                                                                                
430     Custodial facility                                                      
431     Hospital                                                                
432     Halfway house                                                           
433     Nursing home, retirement home, or home for the aged                     
434     County home or poor farm                                                
435     Orphanage                                                               
436     Jail or detention center                                                
437     Federal penitentiary, state prison, or prison farm                      
                                                                                
440     Educational or religious institution                                    
441     Sorority or fraternity                                                  
442     Convent or monastery                                                    
443     Educational institution                                                 
444     Religious institution                                                   
                                                                                
450     Transportation terminal                                                 
451     Airport or airfield                                                     
452     Train station                                                           


                                                                     173
453     Bus terminal                                                            
454     Marine terminal                                                         
455     Seaplane anchorage                                                      
                                                                                
460     Employment center                                                       
461     Shopping center or major retail center                                  
462     Industrial building or industrial park                                  
463     Office building or office park                                          
464     Amusement center                                                        
465     Government center                                                       
466     Other employment center                                                 
                                                                                
470     Tower                                                                   
471     Lookout tower                                                           
                                                                                
480     Open space                                                              
481     Golf course                                                             
482     Cemetery                                                                
483     National park or forest                                                 
484     Other federal land                                                      
485     State or local park or forest                                           
                                                                                
490     Special purpose landmark                                                
491     Post office box ZIP code                                                
                                                                                
CFCC    CLASSIFICATION E = OTHER PHYSICAL FEATURES                              
                                                                                
500     Physical Feature, Classification Unknown or Not Elsewhere               
         Classified                                                             
                                                                                
510     Fence line                                                              
520     Topographic feature                                                     
521     Ridge line                                                              
522     Mountain peak                                                           
                                                                                
CFCC    CLASSIFICATION F = NONVISIBLE BOUNDARIES                                
                                                                                
600     Nonvisible Boundary, Classification unknown or not Elsewhere            
         Classified                                                             
                                                                                
610     Nonvisible Political Boundary                                           
611     Offset corporate boundary                                               
612     Corporate Corridor                                                      
613     Nonvisible interpolated boundary, polygon definition line for           
         hydrological areas                                                     
                                                                                
620     Feature Extension, Not Otherwise Classified                             
621     Automated extension                                                     
622     Irregular block extension                                               
623     Closure extension                                                       
624     Nonvisible separation line                                              
625     Nonvisible corporate corridor centerline                                
                                                                                
630     Point-to-Point Line                                                     
                                                                                
640     Property Line                                                           
                                                                                
650     ZIP Code Boundary                                                       


                                                                     174
                                                                                
660     Map Edge                                                                
                                                                                
670     Statistical Boundary                                                    
671     1980 Statistical Boundary                                               
672     1990 Block Boundary                                                     
673     1990 Statistical Boundary                                               
674     1990 Statistical Boundary, Tabulation Areas Only                        
                                                                                
CFCC    CLASSIFICATION H = HYDROGRAPHIC FEATURES                                
                                                                                
800     Water Feature, Classification Unknown or Not Elsewhere Classified       
                                                                                
801     Shoreline of perennial water feature                                    
802     Shoreline of intermittent water feature                                 
                                                                                
810     Stream                                                                  
811     Perennial stream                                                        
812     Intermittent stream or wash                                             
813     Braided stream                                                          
                                                                                
820     Canal, Ditch, or Aqueduct                                               
821     Perennial canal, ditch, or aqueduct                                     
822     Intermittent canal, ditch, or aqueduct                                  
                                                                                
830     Lake or pond                                                            
831     Perennial lake or pond                                                  
832     Intermittent lake or pond                                               
                                                                                
840     Reservoir                                                               
841     Perennial reservoir                                                     
842     Intermittent reservoir                                                  
                                                                                
850     Bay, Estuary, Gulf, Sound, Sea, or Ocean                                
851     Bay, estuary, gulf, or sound                                            
853     Sea or ocean                                                            
                                                                                
860     Gravel Pit or Quarry Filled With Water                                  
                                                                                
870     Nonvisible Water Area Definition Boundary                               
871     USGS closure line                                                       
872     Census computed center line                                             
873     Census international water boundary, 10-mile limit, area                
         measurement line                                                       
874     Census water boundary, inland or coastal or Great Lakes                 
875     3-mile limit water boundary                                             
                                                                                
880     Special Water Feature                                                   
881     Glacier                                                                 
                                                                                


                                                                     175
                     D. CONFIGURING OZGIS                                 
                       =================
 
                                                                                
                                                                                
This appendix provides additional information about configuring OzGIS.          
                                                                                
You should read the the information in the early chapter first as that provides 
most of the information you need.                                               
                                                                                
                                                                                

  D. 1 Configuring for a Super VGA                       
      ---------------------------
 
INTERACTER supports 5 non-standard screen modes numbered 9 to 13 which          
can be activated by inserting suitable 'MODEnn' keywords in the INTERACTER      
initialisation file. The INTERACT.INI file contains some examples which         
contain suitable initialisation file MODEnn entries for various combinations    
of video board and display monitor.                                             
                                                                                
                                                                                
The supported non-standard screen modes are as follows                          
                                                                                
   INTERACTER      Mode Type                                                    
   Mode Number                                                                  
   -----------     ---------                                                    
       9            640x400 'Olivetti' monochrome graphics                      
      10            132x25   16 colour text                                     
      11            800x600  16 colour 'Super VGA' graphics                     
      12            256 colour 'Super VGA' graphics                             
      13            256 colour 'Super VGA' graphics                             
                                                                                
Notes :                                                                         
(1) The dimensions of mode numbers 12 and 13 are definable as part of           
    the MODEnn keyword. By default they are 640x480 and 800x600 modes.          
(2) 800x600 and 1024x768 modes will require a multisync or Super-VGA type       
    monitor. On certain boards, 132 column mode also requires such a monitor.   
    Be sure to use a suitable monitor/adapter combination.                      
(3) The precise mode numbers used by particular video board manufacturers       
    can vary. Users should check the documentation supplied with their          
    video board before including the supplied example MODEnn entries            
    in their INTERACTER initialisation file.                                    
                                                                                
Initialisation entries can be found for following:                              
                                                                                
  Ahead B chipset                                                               
  ATI VGA Wonder chipset                                                        
  Chips & Technology chipset                                                    
  Everex chipset                                                                
  Oak Technology chipset                                                        
  Olivetti M24/M28/M300, AT&T 6300, Compaq Portable                             
  Paradise chipset (inc. Compaq, Dell, HP D1180A, AST VGA's))                   
  Toshiba 3100 + Gas plasma screen                                              
  Trident chipset                                                               
  TsengLabs ET3000 chipset                                                      
  TsengLabs ET4000 chipset                                                      


                                                                     176
  VAXmate II                                                                    
  Video 7 chipset                                                               
                                                                                
  By default, mode numbers 12 & 13 are 640x480 and 800x600 256 colour Super     
  VGA modes using the TsengLabs ET3000 chipset.                                 
  However the precise dimensions of these modes can now be specified using the  
  MODE12 and MODE13 initialisation keywords which now take up to 7 parameters : 
                                                                                
      MODE12 = ax bx cx dx chipset width height                                 
      MODE13 = ax bx cx dx chipset width height                                 
                                                                                
      ax bx cx dx = Interrupt 10h mode selection register values, as before     
                                                                                
      chipset     = VGA chipset number :                                        
                    0 = Tseng Labs ET3000 (default)  5 = ATI                    
                    1 = Tseng Labs ET4000            6 = Trident                
                    2 = Paradise                     7 = Chips & Technology     
                    3 = Video 7                      8 = Ahead B                
                    4 = Everex                       9 = Oak Technology         
                                                                                
      width       = screen mode width in pixels                                 
                    (default = 640 in mode 12 or 800 in mode 13)                
                                                                                
      height      = screen mode height in pixels                                
                    (default = 480 in mode 12 or 600 in mode 13)                
                                                                                
  Any trailing values which are omitted take the default values indicated.      
  Available modes on the supported chipsets include :                           
                                                                                
    Chipset     Chipset   640x350   640x400   640x480   800x600  1024x768       
                Number                                                          
    Tseng 3000    0          y                   y         y                    
    Tseng 4000    1          y         y         y         y         y          
    Paradise      2                    y         y                              
    Video 7       3                    y         y         y                    
    Everex        4          y         y         y         y                    
    ATI           5                    y         y         y                    
    Trident       6                    y         y         y         y          
    Chips & Tech  7                    y         y         y                    
    Ahead B       8                    y         y         y                    
    Oak           9                              y         y                    
                                                                                
  The precise combination of modes available on any given board varies          
  according to the manufacturer and the amount of video RAM available.          
  The 640x480 and 800x600 modes require 512k and the 1024x768 mode requires     
  1 megabyte. Here are some examples of suitable initialisation file keywords   
                                                                                
  VGA board based on the Tseng Labs ET3000 chipset :                            
    MODE12 = 46                                                                 
    MODE13 = 48                                                                 
                                                                                
  VGA board based on the Paradise chipset :                                     
    MODE12 = 94 0 0 0 2 640 400                                                 
    MODE13 = 95 0 0 0 2 640 480                                                 
                                                                                
  VGA board based on the Video 7 chipset :                                      
    MODE12 = 28421 103 0 0 3                                                    
    MODE13 = 28421 105 0 0 3                                                    


                                                                     177
                                                                                
  VGA board based on the Everex chipset :                                       
    MODE12 = 112 19 0 0 4 640 350                                               
    MODE13 = 112 20 0 0 4 640 400                                               
                                                                                
  The number of text columns and rows available in modes 12 and 13 varies       
  according to the pixel dimensions :                                           
                                                                                
    Columns = mode_width/8                                                      
    Rows    = mode_height/14 (if mode_height < 480)                             
           or mode_height/16 (if mode_height >=480)                             
                                                                                
  This gives the following text dimensions :                                    
                                                                                
     640x350 mode :  80 columns x 25 rows                                       
     640x400 mode :  80 columns x 28 rows                                       
     640x480 mode :  80 columns x 30 rows                                       
     800x600 mode : 100 columns x 37 rows                                       
    1024x768 mode : 128 columns x 48 rows                                       
                                                                                
- Since most Microsoft compatible mouse drivers do not support a mouse          
  cursor in non-standard PC graphics modes, an option has been added to         
  the MODEnn initialisation file keyword which tells INTERACTER to display      
  it's own cross-hair cursor in such modes. Simply place a single letter        
  'C' (upper or lower case) at the very end of the record containing the        
  MODEnn keyword to cause INTERACTER to provide a mouse cursor in that mode.    
                                                                                
      MODE9  = 64 C                                                             
      MODE11 = 88 C                                                             
      MODE12 = 94 0 0 0 2 640 400 c                                             
      MODE13 = 95 0 0 0 2 640 480 c                                             
                                                                                
                                                                                
EXAMPLE................                                                         
                                                                                
                                                                                
Here is the configuration file for a 1Mbyte Trident board (1024 x 768 x 256)    
using a mouse and saving screens on disk.                                       
                                                                                
                                                                                
DISPLAY    = 10                                                                 
CHARSET    = c:\ozgis\standard.chr                                              
COLUMNS    = 80                                                                 
TEMPMENU   = \ozgis\menu.tmp                                                    
TEMPWINDOW = \ozgis\window.tmp                                                  
mode13  = 98 0 0 0 6 1024 768 C                                                 

  D. 2 Hardcopy configuration for  OzMap                 
      ---------------------------------
 
This section is applicable if you want to output maps to printers or            
plotters with the OzMap and Vector programs.                                    
                                                                                
The configuration file \ozgis\sciplot.ini has to be set up if OzMap is going to 
be used to produce hardcopy maps. The file looks like:                          
                                                                                
VGA                                  VGA or EGA                                 
40.0      0                          HP Plotter metafile                        


                                                                     178
18.0      1                          Dot-matrix printer metafile                
18.0      1                          Postscript Ascii metafile                  
18.0      1                          Encapsulated Postscript file               
18.0      0                          HPGL file                                  
18.0      1                          CGM file                                   
18.0      0                          WordPerfect graphics file                  
18.0      1 COM1                     On-line Apple Laser Writer                 
40.0      0 LPT1                     On-line HP plotter                         
00C3                                 device mode & serial modes HEXIDECIMAL     
                                                                                
The first column is the width of the drawing surface in cm. Values will need to 
be set for your plotter or printer.                                             
                                                                                
The second column is the drawing line width for Postscript, Encapsulated        
Postscript, Apple LaserWriter, Computer Graphics Metafile, dot matrix, and HP   
LaserJet printers.                                                              
0  = Ignore parameter                                                           
1  = 1 device space units (1-10 Valid)                                          
                                                                                
The third column is the port used for printers and plotters:                    
'COM' - Primary Serial Port                                                     
'COM2'- Secondary Serial Port                                                   
'LPT1'- Primary Parallel Port                                                   
'LPT2'- Secondary Parallel Port                                                 
                                                                                
The value at the bottom is a hexidecimal set of flags for setting the port for  
on-line printers or plotters.                                                   
                                                                                
The packed coded device mode word with the device mode byte in the most         
significant part of the integer, and the serial modest byte in the least        
significant part of the integer.                                                
                                                                                
Format of the integer = [device mode | serial modeset].                         
                                                                                
Device mode byte description:  [bits]                                           
76543210                                                                        
_______0  = XON/XOFF flow control                                               
_______1  = Hardware flow control on DSR line                                   
______0_  = Bell with FRAME or PLTEND                                           
______1_  = No bell with FRAME or PLTEND                                        
_____0__  = Cr with FRAME or PLTEND                                             
_____1__  = No cr with FRAME or PLTEND                                          
____0___  = Check for break in PLOT                                             
____1___  = No check for break in PLOT                                          
___0____  = HP pen plotter handshake init                                       
___1____  = No HP pen plotter handshake init                                    
                                                                                
Serial modeset byte description:  [bits]                                        
7      6   5  4    3        2        1    0                                     
--Baud Rate-- -Parity-  -Stop Bits- -Char Length-                               
000 -   110  00 - None  0  - 1   10  - 7 Bits                                   
001 -   300  01 - Odd   1  - 2   11  - 8 Bits                                   
010 -   600  11 - Even                                                          
011 -  1200                                                                     
100 -  2400                                                                     
101 -  4800                                                                     
110 -  9600                                                                     
111 - 19200                                                                     


                                                                     179
                                                                                
For example, 9600 baud, no parity, 1 stop bit, 8 bits is                        
                                                                                
110 00 0 11 = C3 hex = 195 decimal                                              
                                                                                

  D. 3 Plotter setup                                     
      -------------
 
                                                                                
Plotter pens should agree with those defined in device files. The standard      
order is:                                                                       
BLACK        PEN 1                                                              
BLUE         PEN 2                                                              
GREEN        PEN 3                                                              
RED          PEN 4                                                              
YELLOW       PEN 5  The last four dont matter that much!                        
MAGENTA      PEN 6                                                              
CYAN         PEN 7                                                              
GREY         PEN 8                                                              
                                                                                
If this order conflicts with other packages in use the device files can be      
modified. The order of the first four pens is particularly important for colour 
simulation, although as long as all pens have different colours the final maps  
will probably be acceptable.                                                    
                                                                                
                                                                                
Plotters will usually use software handshaking.                                 
                                                                                
HP pen plotters require a serial interface between the  Personal Computer and   
the HP pen plotter. On the PC side, a cable with a D9 or D25 connector should be
connected to a  serial port or asynchronous adapter port. On the HP pen plotter,
a cable with a D25 connector should be connected to the computer/modem port. A  
detailed specification of the way the  cable should be wired follows:           
                                                                                
Serial cable wiring for HP pen plotters: 7440A, 7470A, 7475A, 7550A             
                                                                                
 ----------------------------             -----------------------               
| Personal Computer          |           | HP Pen Plotter        |              
| [Serial I/O Port or        |           | [Computer/modem port] |              
| Asynchronous Adapter Port] |           |                       |              
 ----------------------------              ----------------------               
                                                                                
      Transmit Data     *-------------------*   Receive Data                    
       [D9/Pin-3, or                             [D25/Pin-3]                    
        D25/Pin-2]                                                              
                                                                                
      Receive Data      *-------------------*   Transmit Data                   
       [D9/Pin-2, or                             [D25/Pin-2]                    
        D25/Pin-3]                                                              
                                                                                
      Signal Ground     *-------------------*   Signal Ground                   
       [D9/Pin-5, or                             [D25/Pin-7]                    
        D25/Pin-7]                                                              
                                                                                
      Data Set Ready    *-----*-------------*   Data Terminal Ready             
       [D9/Pin-6, or          |                  [D25/Pin-20]                   
        D25/Pin-6]            |                                                 


                                                                     180
                              |                                                 
      Clear-To-Send     *-----*                                                 
       [D9/Pin-8, or                                                            
        D25/Pin-5]                                                              
                                                                                
      Data Terminal Rdy *--------------*-----*  Data Set Ready                  
       [D9/Pin-4, or                   |         [D25/Pin-6]                    
        D25/Pin-20]                    |                                        
                                       |                                        
                                       *-----*  Clear-To-Send                   
                                                 [D25/Pin-5]                    
                                                                                
Please note that the previous wiring diagram is necessary if full hardware      
handshake is desired. If the user intends to  use only software handshake       
(XON/XOFF), then only three wires  are required. For software handshake the only
connections  required are: signal ground, receive data, and transmit data.      
                                                                                
     There are certain restrictions when an HP pen plotter is used as the plot  
device. Not all HP pen plotters possess equal capability! SciPlot only supports 
the 7470A, the 7475A, and the 7550A HP Pen Plotter. There are enough control    
mechanisms in SciPlot to allow the use of others though.  Please note the       
following:                                                                      
                                                                                
 The "INIT=ON" command in the VECTOR.CFG file will send initialization commands 
in the I/O stream to the  plotter when VECTOR is executed. Older HP plotters    
will  produce errors on receipt of these handshake mode commands.  If this      
happens, set "INIT=OFF" in the VECTOR.CFG file, and the offending commands will 
be deleted from the stream.                                                     
                                                                                
                                                                                


                                                                     181
                     E. GLOSSARY OF TERMS                                 
                       =================
 
The purpose of this Appendix is to provide definitions for a number of          
terms used within this Guide.  Most of these terms are commonly used words      
or phrases which have taken on a more precise technical meaning in one of       
the areas spanned by the OzGIS system.  Technical terms have been               
borrowed from the jargon of statistics, data processing, computer software      
and hardware, cartography, and graphic arts.  Because of the diversity of       
these disciplines, it is unlikely that a potential OzGIS user will have         
developed a level of expertise in each.  This glossary should provide most      
of the information necessary for communicating the basic concepts of            
OzGIS.                                                                          
                                                                                
The glossary is available on-line, and is accessed by typing 'G' to a menu      
selection request.                                                              
                                                                                
Area - 1) A measurement of the size of a geographical region whose shape is     
   displayed on the OzGIS monitor.  2) An arbitrary portion of the face         
   of the monitor.                                                              
                                                                                
Attribute - A general term for the variable associated with a set of            
   geographic zones, lines or sites to be processed by OzGIS.                   
   Attributes may be variates, statistics or simply data collected for each     
   item.  Note that the modes of display for an attribute are usually           
   referred to as "single variate" or "bi-variate".  See also Variate and       
   Statistic.                                                                   
                                                                                
Background - The informationless area displayed on the monitor around a map     
   and its associated components.  Usually given a user selected, neutral       
   colour such as black or white.                                               
                                                                                
Bit - A unit of information representing the value (either 1 or 0) of a         
   single binary digit.                                                         
                                                                                
Bivariate - A display of the relative distribution of two different sets        
   of statistics on the same map.  It must be noted that no relationship        
   between the two statistics is implied by the display.  For example, if       
   the distribution of little old ladies is displayed simultaneously with       
   the distribution of cricket players, the result is not a display of the      
   distribution of little old ladies who play cricket.  See also Variate.       
                                                                                
Boundary - A set of lines displayed on the monitor to represent the edges       
   of polygons defined to the system.  Often the same as zone edges.            
                                                                                
Byte - A group of eight bits.  See also Bit.                                    
                                                                                
Catchment - The region of influence around a site e.g. suburbs around a         
   shopping centre where most of the customers live.                            
                                                                                
                                                                                
Character - A single symbolic pattern which may be displayed on either the      
   monitor or terminal.  It may be alphabetic, numeric, or punctuational,       
   as the normal symbols encountered on a typical typewriter keyboard, or a     
   special symbol generated for display as an entity, such as a square root     
   symbol.                                                                      
                                                                                


                                                                     182
Choropleth Map - A map portraying the values of an attribute averaged over      
   data collection units (or zones) and represented by a symbol covering        
   the entire unit.  A map displayed by OzGIS represents the zones by a         
   uniform colour.                                                              
                                                                                
Class - A convenient subdivision of the total range of values of a              
   particular statistical variate.  Classes are usually chosen to make          
   computations or analyses less labourious, or to make the results of such     
   analyses more obvious or meaningful.  For example, the range of a set of     
   values might be divided into ten equal classes in order to highlight         
   items in the top ten percent.  See also Variate, Class Boundary, Class       
   Interval and Class Number.                                                   
                                                                                
Class Boundary - The special values of variates which determine the upper       
   and lower limits of the range of a class.  See also Class.                   
                                                                                
Class Interval - The range of variate values between the upper and lower        
   limits of the class.  See also Class.                                        
                                                                                
Class Number - A cardinal number assigned to each class into which a            
   particular statistical range has been divided.  Conventionally, the          
   class whose members have the lowest magnitude is assigned number 1, with     
   class numbers increasing uniformly as the magnitude of class values          
   increases.  See also Class.                                                  
                                                                                
Colour - One of the combinations of blue, green, and red which may be           
   specified for display on the monitor.  The total number of colours           
   available depends on the display system.                                     
                                                                                
Colour Space - The range of colours which may be specified for display on       
   the colour monitor.  Since the colours are specified as values of blue,      
   green, and red, it is convenient to think of the colour space as a cube      
   located on a standard three dimensional coordinate system.  Black is         
   placed at the origin, with each of the x, y and z axes representing          
   blue, green, and red, respectively.  The range of possible values is 0.0     
   to 1.0 on each axis of the cube.                                             
                                                                                
Continuous Colour - A method of representating statistical values               
   associated with map zones by graduating zone colours to correspond with      
   changes in statistical value.  From a user defined, or default, sequence     
   of colours, OzGIS generates the intermediate colours to provide a            
   12 colour graduated path through the colour space.  The statistic to be      
   represented is quantized into 12 equal value classes, and the classes        
   are assigned colours from the generated colour sequence.  This allows        
   small changes in statistical value to be represented by subtle changes       
   in colour, while large changes in value may be visually observed as          
   significant colour differences.                                              
                                                                                
                                                                                
Controller - A general term applied to a piece of intermediate equipment in     
   the data path between the electrical signals of a processor and their        
   physical realization in a peripheral device.  Within OzGIS, the term         
   will most often be used for the Color Display Controller.                    
   It will be used to a lesser extent to describe interface controllers for     
   the various disc and tape drives.                                            
                                                                                
Coordinate - One of a pair of numbers which designates the location of a        
   geographic point with respect to another known point.  Geographic files      


                                                                     183
   for entry into the system under OzGIS must have their points                 
   specified in appropriately scaled and formatted coordinates.  The            
   coordinates specified by the user are converted by OzGIS for display         
   on the monitor.  On the monitor screen, the origin is in the lower left      
   hand corner of the viewing area.  The coordinates of a point on the          
   monitor screen are specified by their distance right and up from the         
   origin                                                                       
                                                                                
Crosshair Cursor - A pair of lines at right angles to each other which is       
   displayed on the monitor to designate the location of a certain point of     
   interest.  Under most circumstances, the location of the crosshair           
   cursor may be controlled by movements of the mouse.  See also Box            
   Cursor, and Joystick.                                                        
                                                                                
Data - Numerical values associated with certain physical phenomena, such as     
   128 cm long, 14 years old, or 43 kangaroos.  As a generality,                
   OzGIS was not designed to handle data, but rather the statistics             
   derived from data, such as average length, medium age, or number of          
   kangaroos per hectare.  See also Statistics.                                 
                                                                                
Decile - One of the nine data values which divide the range of a variate        
   into ten equal sized classes.  See also Quantile and Percentile.             
                                                                                
Default - A set of parameters automatically selected by OzGIS in the            
   absence of any stated preference by the user.  The actual default            
   parameters may be defined by the user in the users default file.  For        
   example, OzGIS may initially display a map by arbitrarily selecting          
   zone colours from a palette of possible shades which the user selected       
   previously.  After this default colouring, the user may wish to change       
   some particular zone colour to improve the appearance of the display.        
                                                                                
Disc - An electronic device for storing digital data on a rotating plate        
   coated with magnetic material.  See also Controller.                         
                                                                                
Display - As a verb, the act of presenting information on the monitor or        
   terminal for the purpose of visually communicating that information to       
   the user.  This includes all the procedures necessary to correctly           
   present the information in a format suitable for both the equipment and      
   the viewer.  Example:  "A map is displayed on the monitor, while a menu      
   is displayed on the terminal".                                               
                                                                                
                                                                                
   As a noun, the presentation which is visually perceived when a user          
   looks at the screen of the monitor or terminal;  the total information       
   content on the screen.  Examples:  "The terminal display indicates the       
   options possible now";  "This map display is too red".  See also Monitor     
   and Terminal.                                                                
                                                                                
Display Elements - The components or items of a display on the OzGIS            
   monitor;  for example, legend, title, image map, boundaries, image           
   symbols, histograms.                                                         
                                                                                
Distribution - The manner in which a number of samples of data are spread       
   across the range of possible values.  May be a subjective statement,         
   such as:  "These data appear to have an even distribution".  More often,     
   some quantifiable measure will be given such as:  "These data have a         
   normal distribution with a mean of 40 and standard deviation of 3".          
   Sometimes, distribution information will be presented in graphical form,     


                                                                     184
   such as a histogram or scatter diagram.                                      
                                                                                
Equal Value Quantization - A method of dividing the range of values of a        
   statistical variate into a number of classes where the magnitude of the      
   range of each class is the same.  See also Class.                            
                                                                                
Excluded Zone - A zone displayed on the map and coloured with a special         
   shade indicating that it has not been used for quantization or has been      
   omitted from the area of interest.                                           
                                                                                
File - A number of data items grouped together and considered as a unit for     
   convenience of storage and retrieval by a computer.  Within OzGIS,           
   such files are stored as distinct entities on disk.  Files are               
   identified by media designation, name, and type.  The OzGIS user             
   normally supplies only the file name, but the storage media may also be      
   specified.  The file type is supplied by the system.  The same name may      
   be used for files of different types, but within a particular type, no       
   two files may have the same name.                                            
                                                                                
Frequency - A statistical term referring to the number of members of a          
   population falling into a specified class.  See also Class.                  
                                                                                
Geographic Data - Digitized map data which are referenced to a geographic       
   (or spatial) coordinate system, usually a map projection.                    
                                                                                
Graphics - Data which can be displayed on the monitor in terms of lines         
   points and text, as opposed to colouring and filling regions of the          
   screen.  Used to refer to geographic and symbol data.                        
                                                                                
Histogram - A type of bar graph in which vertical rectangles are erected on     
   the horizontal axis with the height of each bar representing the             
   frequency, and the width representing the corresponding class interval,      
   for each of the classes of a particular variate.  OzGIS can display          
   such statistical information on the monitor.  See also Scatter Diagram,      
   and Class.                                                                   
                                                                                
                                                                                
Information - The subjective knowledge which may be associated with an          
   objective set of data.  The ages and locations of children are data;         
   the distribution of school age children is statistic;  where the schools     
   should be built is information.  See also Data and Statistics.               
                                                                                
Interval - The numerical distance between the upper and lower limits of a       
   class.                                                                       
                                                                                
Joystick - An electro-mechanical device which converts the positions of a       
   small lever into electrical voltages.  The voltages are further              
   converted into digital signals which are used by the PDP11 to                
   position various cursor patterns on the monitor screen.  See also Box        
   Cursor, and Crosshair Cursor.                                                
                                                                                
Legend - A display on the monitor which indicates the correspondence            
   between the statistical values and their associated colours or symbols       
   as defined for a particular map.  The legend usually occupies                
   approximately the rightmost one fifth of the viewing area of the monitor     
   and has two general forms, single variate and bivariate.  One type of        
   single variate legend consists of a column of coloured rectangles beside     
   which are numbers indicating the corresponding class boundaries for          


                                                                     185
   those colours.  The other is a rectangular column with colours gradually     
   changing from top to bottom, and an upper and lower number indicating        
   the range across which the "Continous Colour" varies.  The bivariate         
   legend consists of a 45 degree parallelogram divided left to right and       
   up and down into coloured smaller parallelograms.  A set of numbers          
   along the left side indicates the class boundaries of the primary            
   variate, while similar numbers across the upper side indicate the            
   secondary variate class boundaries.                                          
                                                                                
Line - This term has three special meanings within OzGIS in addition to         
   its normal English usage.  (1) Any set of contiguous segments comprising     
   the section of a zone boundary which has one zone on its right and a         
   second zone on its left as part of a map.  (2) Any contiguous set of         
   segments as part of a graphics display.  (3) A set of alpha-numeric          
   characters meant to be displayed as one row on either the monitor or the     
   terminal.                                                                    
                                                                                
Location - The position of a datum point, or pixel, on the monitor screen.      
   This is given by its x and y coordinates, with the origin in the lower       
   left hand corner.  The range of values depends on the display system.        
                                                                                
Lookup Table (LUT) - A table in the display system which can modify the         
   value in memory for display purposes.                                        
                                                                                
Map - Geographic data which can be displayed on the monitor by colouring        
   and filling regions of the screen or as lines or symbols.                    
                                                                                
Map Projection - Refers to the coordinate system used for processing the        
   display of a map.                                                            
                                                                                
                                                                                
Markers - Special characters or symbols which may be displayed on the           
   monitor to identify locations of points.  For example, aircraft              
   symbols to indicate the location of airports.  Different sized markers       
   are used to show the classification of site attribute data.                  
                                                                                
Mean - The arithmetic average of a set of data values.                          
                                                                                
Memory - A portion of the OzGIS hardware used for the storage of data           
   by the altering of the electrical state of the appropriate circuitry.        
                                                                                
Menu - An itemized list of alternative actions which might be selected          
   within OzGIS.  Menus are displayed on the terminal.  The terminal            
   keyboard is used to enter selections from the options listed on the          
   menu.  The sequence of menu items which is selected controls the "flow"      
   of the OzGIS program through its various tasks.                              
                                                                                
Monitor - The electronic equipment, resembling a colour television              
   receiver, on which maps and graphics are displayed.                          
                                                                                
Nested Means - A quantization method in which classes are generated by          
   dividing each variate range into two classes about the mean for that         
   range.  For example, the central class limit is set at the overall mean,     
   then the upper and lower classes are each divided at the means of the        
   two parts, giving four classes.  This process may be repeated, giving        
   eight classes.                                                               
                                                                                
Operating System - Computer software provided to facilitate usage of the        


                                                                     186
   various computer resources available within the OzGIS system.                
                                                                                
Overlay - As a noun, overlay refers to graphic data written on top of the       
   existing display.  This is displayed on the monitor as though placed         
   between the previous display and the viewer.  Overlays generally are         
   entered in the refresh memory in single bit planes.                          
   As a verb, overlay refers to the act of adding graphics data to a            
   display by putting it "on top of" the previous display.                      
                                                                                
Palette - An array of coloured rectangles which is displayed on the monitor     
   at certain stages of OzGIS.  The palette shows a range of colours            
   which are available for selection by the user.  Palettes are held as         
   files within OzGIS.  Several palette files are provided as part of           
   the software package.                                                        
                                                                                
Parameter - A general term referring to a physical characteristic which may     
   be measured or quantified in some way, even though the precise value of      
   that measurement may be unknown in specific instances.  For example, age     
   is a parameter of human beings.                                              
                                                                                
Percentile - One of the set of 99 values which divide the range of a            
   statistic into 100 equal sized classes.                                      
                                                                                
Peripherals - Items of auxillary equipment added to a computer to enhance       
   its performance.  These include such items as disc drives, tape drives,      
   and printers.                                                                
                                                                                
                                                                                
Pixel - The smallest, individually controllable, element (or cell)              
   displayed as dots of colour on the monitor's screen.  The monitor area       
   is made up of lines of pixels.  For each pixel, there is a corresponding     
   location in the refresh memory for storing the data value associated         
   with that pixel.  This location is the smallest datum area which can be      
   individually controlled by the software.  See also Image and Location.       
                                                                                
Point - A geographic feature which, for display purposes, may be described      
   by only indicating its location as an x and y coordinate.                    
                                                                                
Polygon - A geographic area described by the line segments forming its          
   boundary and the zone name which forms its surface.  One or more             
   polygons may be combined to form a zone.                                     
                                                                                
Presentation Maps - A set of maps prepared for rapid display on the             
   monitor.                                                                     
                                                                                
Primary Variate - The set of statistical values characterized by a common       
   name which is displayed on any given single variate map.  Two such sets      
   of values are displayed on a bivariate map.  The primary variate is          
   named at the top of the title, and its colour values are indicated in        
   the rows of the legend.  See also Variate.                                   
                                                                                
Processor - The hardware which executes the procedural and computational        
   tasks specified by OzGIS.  The standard OzGIS processor is a                 
   Digital Equipment Corporation minicomputer, the VAX.                         
                                                                                
 Projection - The representation of a physical shape on the screen of the       
   monitor according to a fixed mathematical coordinate system.  Normally,      
   a projection in OzGIS terms will refer to a method for presenting            


                                                                     187
   maps of geographic areas.  See also Map Projection.                          
                                                                                
Quantile - Any of the specific values which divide the range of a statistic     
   into equal sized classes.  Some values have other special terms, i.e.,       
   if the range is divided into four classes, the boundary values are           
   called quartiles.  See also Percentile.                                      
                                                                                
Quantify - To assign a number or quantity to an otherwise unnumbered            
   entity.  In particular, to assign a class number to a statistical value      
   or zone name.                                                                
                                                                                
Quantization - The process of assigning class numbers to zones according to     
   the value of the statistic for that zone.  Viewed the other way,             
   quantization is the process of putting zones into classes.                   
                                                                                
Quartile - One of the three data values which divide the range of a variate     
   into four equal sized classes.  See also Quantile and Percentile.            
                                                                                
Raster - a term applied to image data.  In particular data handled on a         
   line basis.                                                                  
                                                                                
                                                                                
Refresh Memory - The portion of the hardware (within the display                
   controller) which holds the digital data necessary to continuously           
   regenerate the colour monitor display.  The cathode ray tube (CRT) of        
   the monitor produces its display by electrically stimulating various         
   phosphorus based compounds deposited on its face.  The colours thus          
   produced fade rapidly with time and must be continually "refreshed".         
   The data necessary to perform this refresh correctly is stored in the        
   refresh memory.                                                              
                                                                                
Region - A designated portion of a map displayed on the monitor.  A region      
   consists of one or more zones or parts of zones defined in some way          
   (e.g. a circular region centered at a point on the map).  The concept of     
   a region is important when the displayed map consists of several             
   geographic areas.  In this context, a region consists of a window            
   (geographic area) and its displayed viewport on the screen (screen           
   area).  See also Area.                                                       
                                                                                
Save - To store on disc (or magnetic tape) all the pertinent data regarding     
   a map displayed on the monitor.  The maps which are "saved" can later be     
   fully regenerated with all details preserved.                                
                                                                                
Scatter Diagram - A two dimensional plot of points whose x and y                
   coordinates are the values of the individual variates associated with        
   those points.  Scatter diagrams are displayed on the monitor in              
   conjunction with bivariate maps.  In this instance, each map zone is         
   assigned a point on the diagram.  The y-coordinate of the point              
   corresponds to the value of the primary variate for that zone as             
   displayed on the map.  The x-coordinate of the point has a similar           
   relationship to the secondary variate.  In addition, the point will be       
   coloured the same as its associated map zone.  Scatter diagrams provide      
   a visual method of assessing the correlation between the two variates        
   displayed on the map.                                                        
                                                                                
Secondary Variate - The second set of statistical values which are              
   displayed (along with a primary variate) on the map.  The                    
   secondary variate is named at the bottom of the title.  See also Primary     


                                                                     188
   Variate.                                                                     
                                                                                
Segment - A set of connected straight lines defined to OzGIS by                 
   specifying the coordinates of their starting, intermediate, and end          
   points, along with the names of the two zones on either side of the          
   lines.  Consequently, segments must represent a portion, or all, of the      
   boundary between two zones.  See also Line and Boundary.                     
                                                                                
Site - A geographic location that has associated attribute data.  A site is     
   defined by a name and fixed location e.g. a site could be a city or a        
   retail store.                                                                
                                                                                
Standard Deviation - A statistical measure of the dispersion amongst a set      
   of measured values.  The standard deviation is mathematically equivalent     
   to the positive square root of the variance of the sample on which the       
   statistic is based.                                                          
                                                                                
                                                                                
Statistics - A general term referring to:  1) The branch of mathematics         
   involved with performing certain analytical calculations regarding           
   various relationships among sets of numerical data, and 2) The numerical     
   results of such calculations.  The height of an individual is data;  the     
   average height of a group is a statistic.                                    
                                                                                
Status - The present condition of the software and hardware system,             
   especially as to its progress toward the completion of the tasks at          
   hand.  The status messages are displayed as a response to                    
   typing interpretation of various abbreviated messages displayed on the       
   terminal.  The status messages are displayed as a response to typing an      
   "S" command.                                                                 
                                                                                
Terminal - An item of hardware comprising a keyboard for entering commands      
   to the processor, and some means for the processor to return                 
   alpha-numeric messages to the user.  The standard OzGIS terminal is          
   the Digital Equipment Corporation VT100.  This contains the necessary        
   keyboard, and a cathode ray tube for displaying processor generated          
   messages.  Some OzGIS installations may also have a printer terminal         
   for providing a permanent copy of the messages on paper.                     
                                                                                
Territory - a zone which has been formed by amalgamating bas zones e.g. sales   
   territories formed from postcodes.                                           
                                                                                
Text - Combinations of characters which may be specified by typing at the       
   terminal.  Lines of text may be displayed on either the terminal or the      
   monitor in various fonts.  See also Character, and Line.                     
                                                                                
Time Lapse Maps - A formatted set of maps concerning a geographic area and      
   certain statistics associated with it as they have been collected over       
   time.  Time lapse files are used to display the time related changes in      
   the statistical data by rapid and periodic changes in map colours            
   corresponding to the statistics.  For example, variations in population      
   density, as recorded by the 1971, 1976, and 1981 census data, could be       
   shown by changing the colours of the displayed map at one second             
   intervals corresponding to the 3 sets of data.                               
                                                                                
User - The person who is interactively controlling the OzGIS system at          
   the terminal.                                                                
                                                                                


                                                                     189
Value - The number associated with a particular statistical item, as            
   opposed to the colour associated with that item.  For example, the zone      
   might be coloured red to indicate four to ten beer drinkers per pub in       
   that zone.  The actual value of the statistic might be 9.4 beer drinkers     
   per pub.                                                                     
                                                                                
Variate - A measurable quantity which may take on any of the values within      
   a given range, and which has associated with it a specified probability      
   function describing the manner in which the permissible values are           
   likely to occur.  See also Bivariate, Primary Variate, and Secondary         
   Variate.                                                                     
                                                                                
Viewport - The rectangular area of the colour monitor face selected for         
   displaying a specified item.                                                 
                                                                                
Window - The rectangular portion of a geographic map which is selected for      
   display on the colour monitor.                                               
                                                                                
                                                                                
Zone - A geographic area which is to be considered as a spatial unit.  A        
   zone is defined in terms of one or more polygons which form it.              
   Statistically, a zone is defined in terms of a single value for each         
   variate in question.  This relationship of one variate value per defined     
   geographic zone allows zones to be completely and uniformly coloured in      
   a map display.  See also Polygon and Variate.                                
                                                                                
Zone Name - An alphanumeric designation attached to the various                 
   computerized data associated with a zone.  The zone name facilitates for     
   the processor the task of relating various data items to the proper          
   zones.                                                                       


                                                                     190
                     F. SYSTEM LIMITS                                     
                       =============
 
The OzGIS system has a standard set of limits to various maximum counts. These  
correspond to array sizes.                                                      
                                                                                
The limited memory on the PC makes these limits quite small under DOS. When     
the WINDOWS version is available these limits should be much larger.            
                                                                                
                                                                                
The standard limits are:-                                                       
                                                                                
500   max no displayed zones+sites+lines                                        
500   max no values in attribute file (zones,sites,lines)                       
10    max no map regions                                                        
10    max no quantised zone geog files                                          
10    max no quantised site geog files                                          
10    max no quantised line geog files                                          
10    max no line overlays                                                      
10    max no polygon underlays                                                  
10    max no marker overlays                                                    
10    max no name overlays                                                      
20    max no test strings displayed                                             
50    max no polygons in a zone                                                 
499   max no segments in a polygon                                              
100   max no segments in a line                                                 
256   max no vertices in a segment                                              
500   max no points in a fast display polygon                                   
1000  max no zones per item in a combine file                                   
256   max length of display system LUT                                          
2000  max no vertices in foreign segments data file                             
5000  max no zones that can be built from line segments                         


                                                                     191
                     G. TROUBLE-SHOOTING                                  
                       ================
 
Many of the Oz programs use most of available memory in the 640K. If you have   
other programs loaded they man not run. This will often show up as errors when  
opening files.                                                                  
                                                                                
IO errors can be caused initially by not having buffers=20, files=20 set        
in config.sys. Another common cause is lack of disk space. Some processing      
uses a lot of disk space as scratch files.                                      
                                                                                
If you have trouble displaying maps then you probably have not configured the   
system properly. If you are using a super VGA get the system working in standard
VGA mode first. Generally check the \ozgis\interact.ini file for the DISPLAY    
parameter for the monitor type (usually 10). Super VGA modes need the correct   
startup register values to be set. Edit the interact.ini file and throw away    
irrelevant parts.                                                               
                                                                                
If you have trouble with the mouse in super VGA mode you may need the C         
parameter on the end of the mode command in the interact.ini file. Ensure that  
there are no comments following the C parameter. There have also been problems  
with incompatible mouse drivers; microsoft and Genius drivers are known to work.
The mouse driver must be called MOUSE.COM.                                      
                                                                                
If you have trouble with menus reload the \ozgis\ozgis.men file. This file      
defines all the menus and actions and is constantly rewritten. A hardware error 
could corrupt the file.                                                         
                                                                                
Check the osgis.out file after problems to see if there are any error messages. 
                                                                                
GIS data (digitised data) are often incorrect. This can cause problems with     
polygon display e.g. if zone boundaries cross themselves, and during zone       
building. Your data supplier probably wont be of much help. Try windowing into  
the part of the map with problems to isolate it and use the debug option to     
print values. You will have to patch the data files with a word processor.      
                                                                                
Rebooting the system while the OzGIS programs are running can cause "loss" of   
disk space. This can be recovered using CHKDSK.                                 


                                                                     192
                     H. REFERENCES                                        
                       ==========
 
                                                                                
O'CALLAGHAN, J.F., SIMONS, L. and PALMER, J.A.B. (1980).  A prototype           
system for interactive colour mapping.  Proc. URPIS-8 (k. Davies (ed.)),        
Surfers Paradise, pp. 9.1-9.5.                                                  
                                                                                
SIMONS, L., O'CALLAGHAN, J.F. and PAINE, T. (1982).  COLOURMAP - an             
interactive colour mapping workstation.  Proc. DECUS (Digital Equipment         
Computer Users Society), Melbourne, Vol. 10, pp.1501-1504.                      
                                                                                
O'CALLAGHAN J.F., and SIMONS, L.W.J. (1983) COLOURMAP: An Interactive           
Colour Mapping System. Proc. First Australasian Conference on Computer          
Graphics, Sydney.                                                               
                                                                                
O'CALLAGHAN J.F., and SIMONS, L.W.J. (1984).   Map Display Techniques for       
Interactive Colour Mapping.                                                     
                                                                                
Henzell, O'Callaghan. A Sequential Line Simplification Algorithm based on       
Equivalent Height. CSIRONET Technical Report, May 1980                          
                                                                                
Robertson, O'Callaghan. The Generation of Colour Sequences for Univariate and   
Bivariate Mapping. IEEE Computer Graphics and Applications, February 1986.      
                                                                                
Gerald Evenden. Cartographic Projection Procedures for the UNIX Environment - A 
User's Manual. USGS open-file report 90-284.                                    
                                                                                
TIGER/Line Census Files, 1990 Technical Documentation / prepared                
by the Bureau of the Census. Washington:  The Bureau, 1991.                     
                                                                                
Atef A Elassal. General Cartographic Transformation Package (GCTP), Version ii  
NOAA Technical Report NOS 124 CGS 9                                             
                                                                                
J Sibert, 'Continuous-colour Choropleth Maps', Geo-Processing, (1980)           
207-216.                                                                        
                                                                                
'The Harvard Library of Computer Graphics Mapping Collection', Harvard          
University.                                                                     
                                                                                
E Giamottic and P Puliafits, 'An Interactive Spatial Information System: A      
Tool for Regional Planning'; Proc IFIP 79.                                      
                                                                                
J Dalton et al, 'Interactive Colour Map Displays of Domestic Information',      
Proc SIGGRAPH 79, Computer Graphics, Vol 13 No 2 ACM/SiGGRAPH.                  
                                                                                
A Robinson et al, 'Elements of Cartography', Wiley 1978.                        
                                                                                
                                                                                
D Des Jardins, 'Multi-Level Statistical Maps in Graphic Communication',         
Proc NCGA, Anaheim 1982.                                                        
                                                                                


                                                                     193
                     I. FUTURE PLANS                                      
                       ============
 
The OzGIS system is undergoing constant development.                            
                                                                                
Current plans are for:                                                          
                                                                                
Support for 1991 Australian Census data (the first data should be available in  
August 92)                                                                      
                                                                                
Support for more data formats e.g. UK Census                                    
                                                                                
Support for formats of other PC mapping systems.                                
                                                                                
Development of a WINDOWS 3.1 version. The primary reason is to enable the       
system to use extended memory to overcome some of the limitations in the DOS    
version e.g. it may be possible to display maps of 20,000 zones and handle      
polygons of up to (say) 10,000 vertices.                                        
                                                                                
                                                                                
Various minor enhancements.                                                     
                                                                                
Spatial operations (polygon overlay)                                            
                                                                                
Digitising                                                                      
                                                                                


                    CONTENTS

  1. OzGIS INTRODUCTION                                              4          
  1. 1 Programs                                                      4          
  1. 2 Concepts                                                      4          
  1. 3 Environment                                                   5          
  2. SUMMARY                                                         7          
  3. SYSTEM CONFIGURATION                                           10          
  3. 1 Introduction                                                 10          
  3. 2  DOS system files                                            10          
  3. 3  Standard EGA and VGA boards                                 11          
  3. 4  Super VGA boards                                            12          
  3. 5 Maths Coprocessor                                            13          
  3. 6 Extra RAM                                                    14          
  3. 7 Mouse                                                        14          
  3. 8 Hardcopy configuration                                       14          
  3. 9 Digitiser                                                    14          
  4. OzEnter DATA ENTRY                                             15          
  4. 1 Introduction                                                 15          
  4. 2 Example of data entry                                        16          
  4. 3 Demonstration Files                                          18          
  4. 4 Example geographic and attribute data                        18          
  4. 5 Example device files                                         19          
  4. 6 Marker data files                                            19          
  4. 7 Colour names data (no longer used)                           19          
  5. BASIC CHOROPLETH MAPPING EXAMPLE                               20          
  5. 1 OzCensus                                                     20          
  5. 2 Example Choropleth Map                                       20          
  5. 3 Summary                                                      23          
  6. INTERACTIVE USER INTERFACE TO OzGIS                            24          
  6. 1 Menus                                                        24          
  6. 1. 1 Menu format                                               24          
  6. 1. 2 Function keys                                             24          
  6. 1. 3 Stacking selections                                       25          
  6. 2 Questions                                                    25          
  6. 3 Commands                                                     26          
  6. 4 Graphic interaction                                          27          
  6. 5 Pop-up                                                       27          
  6. 6  Print file                                                  27          
  7. OzGIS FILES                                                    28          
  7. 1 File Origins                                                 28          
  7. 2 File types                                                   29          
  7. 3 File Names                                                   31          
  7. 4 Directories                                                  31          
  8. DEVICE FILES                                                   33          
  9. OzGIS MAP TYPES                                                36          
  9. 1 Map Types                                                    36          
  9. 2 Attribute maps                                               36          
  9. 2. 1 Bivariate zones map Example                               37          
  9. 2. 2 Zones & sites Example                                     37          
  9. 2. 3 Geographic (GIS) maps Example                             38          
  9. 2. 4 Diagrams Example                                          40          
  9. 3 Presentations                                                41          
  9. 4 Saved-display files                                          41          
  9. 5 Time Lapse Display (not available)                           41          
 10. ATTRIBUTE SELECTION                                            42          
 10. 1 Introduction                                                 42          
 10. 2 Sequentially                                                 42          


 10. 3 By number (position in file)                                 42          
 10. 4 By attribute description                                     42          
 10. 5 By arithmetic operation                                      42          
 10. 6 Zone/Site/Line names                                         43          
 11. QUANTISATION                                                   44          
 11. 1 Introduction                                                 44          
 11. 2 Quantisation Methods                                         45          
 11. 3 Quantisation Ranges                                          47          
 11. 4 Quantisation Lists                                           47          
 12. GEOGRAPHIC OVERLAYS                                            49          
 12. 1 Introduction                                                 49          
 12. 2 USA Census / TIGER Overlays Example                          50          
 13.  DISPLAY CONTROL & MAP DESIGN                                  52          
 13. 1 Introduction                                                 52          
 13. 2  Map Quantisation Legends                                    52          
 13. 3 Overlays (GIS) legends                                       54          
 13. 4 Other Legends                                                54          
 13. 5 Text                                                         54          
 13. 6 Attribute Diagrams                                           54          
 13. 7 Displayed Colours (removed)                                  55          
 14. MAP REGIONS                                                    57          
 14. 1 Introduction                                                 57          
 14. 2 Regions                                                      58          
 14. 3 Map List                                                     59          
 14. 4 Quantised Zones                                              60          
 14. 5 Quantised lines                                              60          
 14. 6 Quantised sites                                              60          
 14. 7 Line Overlays                                                61          
 14. 8 Polygon underlays                                            61          
 14. 9 Marker Overlays                                              61          
 14.10 Name Overlays                                                61          
 14.11 Map Modification                                             61          
 15.  MAP ANALYSIS                                                  62          
 15. 1 Introduction                                                 62          
 15. 2 Map Reports                                                  62          
 15. 3 Attribute Data Statistics                                    62          
 15. 4 Map Interrogation                                            63          
 16. OzData DATA PREPARATION                                        64          
 16. 1 Introduction                                                 64          
 16. 2 Attribute Files                                              64          
 16. 3 Geographic Files                                             65          
 16. 4  Names Files                                                 66          
 16. 5  Output to Data Files                                        66          
 16. 6 Palette Files (Removed from system)                          67          
 16. 7 Colour Names Files  (Removed from system)                    67          
 17. OzZone BUILDING ZONES FROM SEGMENTS                            68          
 17. 1 Use                                                          68          
 17. 2 Faulty Digitised Data                                        68          
 17. 3 Example                                                      69          
 18. MAP PROJECTIONS                                                70          
 18. 1 Introduction                                                 70          
 18. 2 Precision                                                    70          
 18. 3 Latitude / longitude                                         70          
 18. 4 Projections                                                  71          
 18. 5 Ellipsoids                                                   71          
 18. 6 Use                                                          72          
 18. 7 Example                                                      72          
 19. OzMap HARDCOPY MAP PRODUCTION                                  73          


 19. 1 Overview                                                     73          
 19. 2 Procedure                                                    74          
 19. 3 OzMap Device files                                           74          
 19. 4 VECTOR Program                                               75          
 19. 5 OzMap Example                                                78          
 19. 6 Fitting Maps on the Page                                     79          
 20. OzTerr TERRITORY DEFINITION                                    81          
 21. ADDRESS MATCHING / GEOCODING                                   83          
 21. 1 Introduction                                                 83          
 21. 2 Addresses                                                    83          
 21. 3 Data entry                                                   84          
 21. 4 Address Matching                                             84          
 21. 5 Matching Addresses                                           85          
 21. 6 Procedure                                                    85          
 21. 7 Data                                                         86          
 21. 8 Abbreviations parameter file                                 87          
 21. 9 Handling Errors                                              88          
 22. OzSpat SPATIAL OPERATIONS (being tested)                       89          
 22. 1 Operations                                                   89          
 22. 2 Feature codes                                                90          
 22. 3 Procedure                                                    90          
 23. OzDigit DIGITISING (being ported from VAX)                     92          
 23. 1 Introduction                                                 92          
 23. 2 Configuration                                                92          
 23. 3 Files                                                        92          
 23. 4 Preparation for Digitising                                   93          
 23. 5 Setting up the Menu                                          93          
 23. 6 Control points                                               95          
 23. 7 Digitising the Map                                           95          
 23. 8 Examining digitised data                                     97          
 23. 9 Giving Names and Feature codes                               97          
 23.10 Forming Polygons / checking                                  97          
 23.11 Editing Digitised Data                                       98          
 23.12 Variations                                                   98          
 24. OzCatch RETAIL SITE CATCHMENTS (NOT AVAILABLE YET)             99          
 24. 1 Introduction                                                 99          
 24. 2  SITE CATCHMENTS                                             99          
  A. DATA SOURCES                                                  102          
  A. 1 General                                                     102          
  A. 2 Australia                                                   102          
  A. 2. 1 Australian Bureau of Statistics                          102          
  A. 2. 2 AUSLIG data                                              103          
  A. 3 New Zealand                                                 103          
  A. 4 United Kingdom                                              104          
  A. 5 USA Census Data                                             104          
  A. 6 Canada                                                      104          
  A. 7 Others                                                      104          
  B. MAP DATA FORMATS                                              106          
  B. 1 Introduction                                                106          
  B. 2 OzGIS Data Formats                                          106          
  B. 3 Description of File Formats                                 107          
  B. 4 Format of attribute files                                   108          
  B. 4. 1 Preprocessing                                            108          
  B. 4. 2 OzGIS Standard Format                                    108          
  B. 4. 3 Sample attribute file DEMOATTR.DAT                       109          
  B. 4. 4 Simple Attribute format (tabular database format)        109          
  B. 4. 5 Sample simple attribute file DEMOSASA.DAT                109          
  B. 4. 6 Spreadsheet data formats                                 110          


  B. 4. 7 ATLAS Data files                                         110          
  B. 4. 8 LAMM format                                              111          
  B. 4. 9 Comma delimited format                                   112          
  B. 4.10 Other attribute data formats                             113          
  B. 5 Standard OzGIS formats for geographic files                 114          
  B. 5. 1 General Information                                      114          
  B. 5. 2 Structure of data                                        114          
  B. 5. 3 Internal Data                                            115          
  B. 5. 4 Comment Record                                           115          
  B. 5. 5 Map Partition                                            115          
  B. 5. 6 Zones Partition                                          116          
  B. 5. 7 Line Partition                                           116          
  B. 5. 8 Polygons Partition                                       117          
  B. 5. 9 Segments Partition                                       117          
  B. 5.10 Points Partitions                                        118          
  B. 5.11 Sample boundaries geographic file DEMOZSEG.DAT           119          
  B. 5.12 Sample segments file with adddresses DEMOADDR.DAT        120          
  B. 5.13 Sample lines geographic file DEMOLINES.DAT               122          
  B. 5.14 Sample points geographic file DEMOPOINT.DAT              122          
  B. 6 Format of polygon geographic files                          124          
  B. 6. 1 Standard (not implemented)                               124          
  B. 6. 2 SAS Format Zone Files                                    124          
  B. 6. 3 Simple Format (old SAS) Zone Files                       125          
  B. 6. 4 Sample simple zones data file DEMOSASG.DAT               126          
  B. 7 GIS / common geographic file formats                        127          
  B. 7. 1 DIME format                                              127          
  B. 7. 2 DLG optional 3 format                                    127          
  B. 7. 3 Gina format                                              129          
  B. 7. 4 ANSII standard                                           131          
  B. 7. 5 SIF format (not available)                               131          
  B. 7. 6 DXF format                                               132          
  B. 7. 7 ATLAS Export Format                                      133          
  B. 7. 8 MapInfo Data Interchange Format                          136          
  B. 8 Format of names files                                       138          
  B. 8. 1 Sample names file DEMOATTR.DAT                           138          
  B. 9 Format of colour names files (Removed from system)          138          
  B.10 Format of combine files                                     139          
  B.10. 1 Sample combine file DEMOCOMB.DAT                         139          
  B.11 Format of presentation files                                139          
  B.11. 1 Sample presentation file                                 140          
  B.12 Format of marker files                                      140          
  B.12. 1 Sample marker file SQUARE.DAT                            141          
  B.13 Format of device files                                      141          
  C. USA Census data                                               147          
  C. 1 Overview                                                    147          
  C. 2 Documentation                                               148          
  C. 3 OzGIS Processing of TIGER data                              148          
  C. 4 Processing STF1A data                                       150          
  C. 5 The STF1A parameter file                                    151          
  C. 6 Example                                                     151          
  C. 7 OzGIS Census Zone Names                                     160          
  C. 8 STF1A Census data                                           160          
  C. 9 STF1A Geographic areas                                      160          
  C. 9. 1 Blocks                                                   160          
  C. 9. 2 Block Groups                                             161          
  C. 9. 3 Census tract and block numbering area                    161          
  C. 9. 4 Census Tract                                             162          
  C. 9. 5 County                                                   162          


  C. 9. 6 Hierarchical Presentation                                163          
  C. 9. 7 Zip codes                                                163          
  C.10 The STF1A file                                              164          
  C.10. 1 File Segments                                            164          
  C.10. 2 Field Names In Numeric Data Tables                       165          
  C.11  TIGER US Census Digital Map Data                           165          
  C.12  TIGER files                                                165          
  C.13 TIGER Geographic Area Definitions                           167          
  C.14 TIGER feature codes                                         169          
  D. CONFIGURING OZGIS                                             175          
  D. 1 Configuring for a Super VGA                                 175          
  D. 2 Hardcopy configuration for  OzMap                           177          
  D. 3 Plotter setup                                               179          
  E. GLOSSARY OF TERMS                                             181          
  F. SYSTEM LIMITS                                                 190          
  G. TROUBLE-SHOOTING                                              191          
  H. REFERENCES                                                    192          
  I. FUTURE PLANS                                                  193