___________________________________________________________________________
STAC FAX                                                           STAC FAX

Title: Configuring a CD-ROM on a Stacked System  

STACKER NOTE TEC036 - 6/18/92                          STAC FAX Index #2507
___________________________________________________________________________

Background.

   During system startup, Stacker drives are assigned a drive letter by DOS 
   as they are "mounted" by the Stacker device driver in Config.sys.  CD-ROM 
   drives are not assigned a drive letter until MSCDEX.exe loads in the
   Autoexec.bat file.  Because Stacker drive letters are assigned first, 
   the CD-ROM will have to take the next available letter.  This means that 
   if your CD-ROM existed before Stacker, you will probably have to 
   re-configure it to use a new drive letter. 

Configuring the CD-ROM.

1.  CONFIG.SYS
    Here are is a sample Config.sys.  It is recommended that the CD-ROM 
    device be loaded after SSWAP.COM as shown.

    DEVICE=C:\DOS\SETVER.EXE  (this is required if running under DOS 5.0)
    DEVICE=C:\STACKER\STACKER.COM  C:\STACVOL.DSK .....etc.
    DEVICE=C:\STACKER\SSWAP.COM C:\STACVOL.DSK /SYNC

    DEVICE=SONYCDU.SYS or DEVICE=PCD650S.SYS   [/D:name /B:xxx /M:mode]

2.  AUTOEXEC.BAT:
    The CD-ROM letter is assigned here with the /L: parameter on the 
    MSCDEX command line.  Take note of the Stacker drive letter  assignments 
    at boot time.  For example, to determine which drive letters Stacker has 
    been given, type:

    C:\STACKER\STACKER      <ENTER>
	
    The output will look similar to: 
    
    STACKER - 2.00, (c) 1990-91, Stac Electronics, Carlsbad, CA
    Drive C: was drive D: at boot time   [ D:\STACVOL.DSK ]
    Drive D: was drive C: at boot time  
   
    Set the CD-ROM to the next available drive letter. In this example, 
    drive E: is available for the CD-ROM.  In Autoexec.bat you would assign 
    drive E: on the MSCDEX command line.  
      
    MSCDEX /D:name /M:x /V /L:letter /E 

    Change /L:Letter to /L:E
    
    MSCDEX /D:name /M:x /V  /L:E  /E    

    After changing the CD-ROM drive letter, it may be necessary to re-setup 
    applications or programs to recognize the new drive letter designation.

___________________________________________________________________________
Copyright 1992, Stac Electronics                    STAC FAX (619) 431-6712