Documentation for StackMan Stack Manager.


What can StackMan do for you?

    Have you ever experienced your machine hanging unexpectedly? Have
    you ever experienced programs dumping beeping garbage on the screen?
    Ever found your overnight working machine hanging when you return
    to work even though the same programs work well during the day? Ever
    seen the message "Stack overflow"? Found some resident or background
    software to hang the machine as soon as you want to activate them?
    Does your system run unreliably when you put the statement
    "Stacks=0,0" in your Config.Sys file? Do some programs crash when
    using them in combination with some TSR's?

    If you can answer all these questions with "No" the Stack Manager
    will not be useful for you.

    If some of these events frequently happen to you, these problems are
    likely caused by stack overflows. Mostly these problems can be
    solved by using the Config.Sys statement "Stacks 9,256". Sometimes
    not. Anyway, the "Stacks" statement consumes precious memory and it
    is hard to guess the correct values. The "Stacks" statement is not
    explained very well in most documentations. Only a few users seem
    to understand its purpose.


What is a stack and how does it fail?

    A stack is a memory buffer used by software and the processor itself
    to store temporary data. All programs establish a stack when they
    are executed, but background or resident software have to use the
    stack of the foreground program. As soon as you press a key the
    processor is interrupted by the keyboard processor to fetch the
    pressed key. Every timer tick the processor is interrupted to
    increase the system timer. All these background processes consume
    some stack space. Sometimes there is a timer tick, a keyboard
    interrupt and another interrupt at the same time. It will not happen
    often, but when it happens, all these processes need some stack
    space at the same time. If it is not available the system will
    simply hang... And as you might expect, these random events are hard
    to reproduce...

    Although it is recommended to supply plenty of stack space in a
    program, many programmers keep the stack very small to save memory,
    especially if the program is intended to remain resident in memory.
    Of course resident programs can set up their own temporary stack as
    soon as they are activated, but before they are able to do that they
    need to use some of the foreground stack space, and the resident
    stack is often also very small for obvious reasons. If you have a lot 
    of resident software and/or background software the stack might be too
    small in some cases.

    To avoid these problems DOS is able to maintain a stack pool and it
    switches to a dedicated stack if a hardware interrupt occurs. The
    "Stacks" statement in the Config.Sys can be used to control this
    stack pool.

    However, the DOS stack switching has some drawbacks and this is one
    of the reasons why StackMan has been developed.


Features of StackMan

    StackMan offers the same functionality as the DOS "Stacks" command,
    but in addition to this:

    -   If you use DOS 5.00, StackMan can be loaded high and/or into the
        HMA. DOS instead always maintains the stack pool in conventional 
        memory. When using StackMan you free up about 1.5Kb of memory.

    -   The parameters of StackMan are more flexible. You can define just
        one stack frame if it is sufficient. The minimum of DOS is 8.

    -   StackMan can be loaded AFTER your TSR's become resident. This
        causes the TSR's to use the stackspace provided by StackMan. The
        DOS stacks pool however is only available for the DOS and BIOS
        code. TSR's still use the foreground program's stack, and if this
        causes problems the DOS stacks command will not solve this.

    -   The DOS stacks command offers the user a type of roulette: the
        only way to find the correct values is by trial and error. StackMan
        can print a report and it is easy to find out the stack requirements
        of your system configuration. It is easy to fine-tune the StackMan
        parameters to suit your system configuration perfectly.

    -   Sometimes DOS stacks seem to disappear. Although this can be
        considered as a bug from one of the TSR's or foreground programs
        it is hard to deal with the resulting DOS message "Stack
        overflow. System halted". This never happens immediately but a while
        after the offending program corrupted a stack. StackMan however
        recognizes this situation and it will automatically recover the lost
        stack without interrupting the program.

    Although StackMan can be used to replace the DOS stacks command it has
    additional features:

    -   In some cases the total stack requirements of all resident int 21h
        handlers may exceed the available stack space, especially if using
        a program that maintains a tiny stack (like some popular swap
        utilities). Although these programs may perform well at the machine
        of the developer, many other users may experience problems.
        StackMan can be used to force a normal stack space for DOS at all
        times.

    -   To be safe TSR's should maintain their own stack, but that means
        that the TSR program would occupy some extra memory to hold the
        stack. If only 1% of the users need that stack and the other
        systems can run without it, it is not very convenient to install 
        a dedicated stack in all cases. Being the author of TbScanX and
        Thunderbyte this dilemma applies to me. In 99.9% of the
        configurations my products perform very well, but a few systems
        hang when these products are used in combination with some other
        software. Should I convert my products to consume extra memory
        only to solve the problems of the unhappy few? There should be a
        better way. And now there is a better way... StackMan is able to
        handle stack requests, and TSR programs may ask StackMan to
        setup a temporary stack. Many TSR programs can share a few
        of the stacks provided by StackMan. The stack is available
        when the TSR activates, and gone as soon as the TSR resumes
        system control. It just saves memory...


Usage

    Before using StackMan it is recommended to put the statement
    "Stacks=0,0" into the Config.Sys file. Using any other (or the
    default values) just causes DOS to waste memory.

    The syntax of StackMan is:
        StackMan [[=] <num of stacks),<stack size>] [<options...>]

    The best place to invoke StackMan is at the end of your Autoexec.Bat
    file. This way resident software will use the stacks provided by
    StackMan automatically.

    You can highload StackMan if you want to.

    As a first test it is recommended to use large values like:
        StackMan = 18,384

    Now use the system as you do normally and test if some of the
    problems are solved. Invoke all TSR's you have and try also to
    activate multiple TSR's at the same time. Use your modem, mouse,
    etc. It is not necessary to execute large programs since they have
    their own stack and they will not affect the results of StackMan.

    Now run StackMan again. You should see something like this:

    ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
    ³                                                             ³
    ³   StackMan already installed, with 18 stacks of 384 bytes.  ³
    ³   Maximum stacks/space ever used:  6 stacks of 112 bytes.   ³
    ³                                                             ³
    ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

    You can now reduce the parameter values of StackMan.
    It is highly recommended to maintain some extra overhead. "Special
    events" are very hard to reproduce. Reliable values for this example
    are: "StackMan = 8,192".

    If the first value of the StackMan report is below or equal to 3 and
    the second does not exceed 48 you can use your system without
    StackMan. In other cases unlikely events are able to crash the
    machine and you should use StackMan to avoid random problems.

    It is recommended to check the output of StackMan once in a while
    to fine-tune the system and anticipate on increasing stack requirements
    of your configuration.


    If still some of the problems occur you can test if the -dos parameter
    solves it. Specify this on the command line after a reboot:
        StackMan = 18,384 -dos -noirq

    The report of StackMan should now be treated differently: the first
    value will always show the maximum stacks amount available, only
    the stackspace used is reliable. If this value exceeds 48 you should
    consider use of the -dos option of StackMan.

    If the first test shows that you have to use StackMan anyway you should
    remove the -noirq option. If only DOS needs StackMan you can keep this
    parameter. If you use the -dos option you should allocate two extra
    stack frames in addition to the values achieved by the first test.


Options available

    The following options are available:

    -help
        This option shows a little help screen.

    -dos
        This option causes StackMan to force a fresh stack before
        entering DOS. This may solve some problems, especially if they
        occur at program startup or termination or in combination with
        swapping shell programs.

    -noirq
        If you specify this option StackMan will not switch the stack
        after an interrupt occurs. The only functionality left in this
        case is the -dos option and the stack sharing of StackMan-
        supporting TSR programs.

    -hma
        This option can only be specified if you are using DOS 5+ when
        DOS is loaded into the HMA (with the dos=high statement). You
        can not use this option in combination with the -dos option.
        The -hma option causes StackMan to keep the stacks in the HMA
        space left by DOS. Although this saves memory you should test
        very thoroughly if your system allows the use of the HMA by
        StackMan.


StackMan API

    If you are software developer and wish to make use of StackMan this
    chapter will be useful for you.

    Your TSR program should check the segment pointed to by int B4h.
    If you find the string "STACKXXX' at offset 0Ah the stack manager
    is installed. The next byte (at offset 12h) contains the version
    number of StackMan in BCD form. The word at offset 14h contains the
    number of stacks available, and the word at offset 16h specifies the
    size of each stack.

    To request a new stack execute "Int B4h". All registers and flags are
    preserved. The interrupt returns with a new private stack.

    To restore the original stack execute "Int B5h". Of course all
    registers and flags are preserved. Register SP should have the value
    provided by "Int B4h" before executing "Int B5h". This will normally
    automatically be the case.

    StackMan will issue an install-broadcast when it goes resident. The
    broadcast is issued by invoking int 2Fh with the value C9FFh in
    register AX, the BCD version number in register BL, the number of
    stacks in register CX and the stacksize in register DX.

    Hint: If StackMan is not installed make Int B4h and Int B5h point to
    an "iret" instruction. If you do this you don't have to make decisions
    in the resident part of your program. Just execute Int B4h/B5h whether
    StackMan is installed or not.


License agreement

    StackMan is FreeWare. As long as you meet these requirements/restrictions
    you are entitled to use and distribute it:

    -   StackMan.Exe and StackMan.Doc are copyrighted by Thunderbyte B.V.

    -   It is not allowed to spread modified parts of the StackMan package.

    -   Thunderbyte B.V. nor Frans Veldman accepts any responsibilities for
        the use or results of the use of StackMan. Being the user of
        StackMan you are fully responsible for the results of StackMan.

    -   You are allowed to distribute StackMan with your products as long
        as credit is given to Thunderbyte B.V. AND Frans Veldman.


    StackMan is written by Frans Veldman, chief executive of Thunderbyte
    B.V. in The Netherlands.