The Great Outdoor BBS
                              Binghamton, NY
                            BBS: (607) 722-1689
                             HST to 38400 24 Hr's
 
 
                          LOADS FOR THE M1 GARAND
 
 
          The following information was written by Ed Harris and
     relates to suggested loads for the M1 Garand. You can direct
     question to Ed through the Firearms Echo.
 
                           -=-=-=-=-=-=-=-=-=-=-
 
          I have had good luck with the following .30-'06 loads, using
     LC Match cases and either Fed. 210M or Winchester WLR primers.
     These charges are not quite max., but there is no need to exceed
     them. Main thing you must realize is that current IMR powders are
     somewhat faster than those made prior to 1976, and great old
     loads you may have heard need to be cut at least 5% across the
     board with current powders.
 
     150-gr. MK to simulate M2 Ball velocity - 49 grs. IMR4895
                                          or   50 grs. IMR4064
                                          or   48 grs. IMR3031
                                          or   50 grs. W748
 
     168-gr. MK for 300 rapid and calm 600     46 grs. IMR4895
                                               48 grs. IMR4064
                                           or  48 grs. W748
 
     LC 173-175 pulls or Sierra 180MK          45 grs. IMR4895
 
                      USE THESE FOR 600        47 grs. IMR4064
 
          I don't recommend slower powders than 4064 or W748 in the
     Garand.
 
          Of the Accurate Arms powders, 2520 is probably the best
     choice, but I don't have specific .30-'06 data for it. AAC's
     recommended charges should be OK.  If your Garand is 7.62 NATO
     let me know and I will post you some appropriate data - have
     pressure tested a lot in that caliber.
 
 
                           -= END OF ARTICLE =-