P C   F l t   P l a n   1.1

                   Computer Flight Planning for DOS

                 Copyright 1990-1992 Geir A. Granviken


                       D O C U M E N T A T I O N

------------------------------------------------------------------------
                            C O N T E N T S

     Part I - General Information
          1.   GENERAL
               1.1  Disclaimer
               1.2  Registration
               1.3  Distribution
          2.   INTRODUCTION
               2.1  About the program
               2.2  Documentation
               2.3  Hardware requirements

     Part II - Quick Start
          3.   QUICK START GUIDE
               3.1  Installing
               3.2  Starting the program
               3.3  Configuring and Preparing the program
               3.4  Making a flight plan
               3.5  Ending and Restarting PC Flt Plan
               3.6  Nav Computer

     Part III - Detailed Guide
          4.   INSTALLING
          5.   STARTING PC FLT PLAN
          6.   PREPARING THE PROGRAM FOR USE
               6.1  Configuring
               6.2  Aircraft Data
               6.3  Nav-Database
          7.   HOW TO MAKE A FLIGHT PLAN
               7.1  Data
               7.2  Create/Edit a Route
          8.   ROUTE EDITOR
               8.1  Legs
               8.2  To / From Fields
               8.3  Automatic or Manual Calculation of
                    course/dist:
               8.4  Flight Data
               8.5  Map View
          9.   PRINT/VIEW A FLIGHT PLAN
               9.1  Flight Plan Data
               9.2  Print or Show the flight plan
          10.  ABOUT THE FLIGHT PLAN
               10.1 Leg Times
               10.2 Fuel
               10.3 Corrections
               10.4 How to use the ETO/RTO/ATO fields
          11.  NAV COMPUTER
          12.  TERMS & ABBREVIATIONS USED IN THE PROGRAM
------------------------------------------------------------------------


                      Part I - General Information


1.   GENERAL

1.1  Disclaimer

     THIS PROGRAM MAY ONLY BE USED IF THE USER AGREES TO THE FOLLOWING
     TERMS:

     There is no warranty of any kind. In no event shall the author be
     liable for any damages, including any lost profits or other
     incidental or consequential damages arising out of the use of or
     inability to use this program, even if the author has been advised
     of the possibility of such damages. The author shall not be liable
     for any possible wrong calculations made by the program.

1.2  Registration

     IMPORTANT: The demo program package (NOT the registered disk
     version) may freely be distributed in it's unmodified form and
     tested, like shareware. BUT in it's unregistered state, saving a
     route to disk is disabled.

     If you find the program useful, it may be registered for USD 25,-.
     You will receive a registration number as soon as possible to be
     inserted under the configuration option. A valid reg. number will
     enable saving routes to disk. Registration will also be valid for
     the next version.

     This program must NOT be used by COMMERCIAL-, MILITARY- or
     GOVERNMENTAL operators without a special licence agreement with the
     author.

     Also for general use in a flying club or similar, a special agree-
     ment is required.

     For registration, comments or questions, contact:
     -------------------------------------------------------------------
     Geir A. Granviken                        Tel: (Intl+47) 3-285565
     Godheimvn. 85                 After 3 Jun 93: (Intl+47) 31 28 55 65
     N-3440 Roeyken
     Norway
     -------------------------------------------------------------------

1.3  Distribution

     The demo program package (NOT the registered disk version) can be
     freely distributed, but all files must be included and they must
     not be altered in any way. The configuration file FPL.CFG (created
     by the program) or the file FPL.REG (if you have that), shall NOT
     be included. No fees must be charged, except for diskette costs.

     The demo/sw package consists of the following files:

     - README       - General info
     - MAILER       - Registration form
     - FPL11.DOC    - Documentation (This file)
     - FPL.EXE      - Main program file
     - FPLSETUP.EXE - Program file (normally called from main program)
     - FPL.DTA      - Data file (will be made by program if not present)
     - FPL2.DTA     - Data file ( "   "   "   "     "    "   "     "   )
     - FPLFLY.DTA   - Data file, aircraft data
     - FPLFAC.DTA   - Data file, nav database
     - FPLFAC.IDX   - Data file, nav database
     - FPLFAC.TXT   - Nav database in ASCII text format
     - FPLFIL.DIR   - Route file remarks (used by the program)
     - ********.RT* - Examples, saved routes.


2.   INTRODUCTION

2.1  About the program

     The program is used to make operational flight plans for VFR or IFR
     flights, - fixed wings or helicopters. (VFR = Visual Flight Rules,
     IFR = Instrument Flight Rules.)

     A flight can be defined to the destination and to one or two
     alternates. In addition, a list of other diversion fields may be
     created.

     The program has a nav-database with lat/long coordinates, magnetic
     variation and frequencies for airfields, navigational aids, inter-
     sections or other frequently used waypoints. The facilities
     included are examples (they are correct though), but the user can
     enter his own waypoints into the database as he creates or edits a
     route, and in that way build up a database.

     The program also provides a small register where some key data for
     the different aircraft used may be stored.

     The routes created may be saved on disk.

     There are 4 different flight plan printouts to be selected from.
     One of these is a knee-board size flight plan.

2.2  Documentation

     This file makes up the documentation. If you find that some topics
     are covered to lightly (or it's just pure lousy all together...),
     the program should hopefully be fairly easy to use, and if you take
     a close look at the sample routes, it should be possible to make
     some sense of it. And there are no hidden features not shown in the
     menus or input options.

     Chapter 3 gives a quick introduction to get started, while the
     following chapters goes more in detail.

2.3  Hardware requirements

     - IBM PC/XT/AT/PS2 or compatible.

     - Minimum 512 KB RAM.

     - Any display type, but to use the map view function, a VGA display
       is required.

     - Hard-disk not required, but the program will work much faster. On
       a floppy disk system, the drive should be at least 720 KB.

     - A disk cache program is recommended but not required.
       SMARTDRV.SYS (or .EXE) which is included with DOS 5.0 and Windows
       is such a cache program, and works very well.

     - To be able to print out all four flight plan variants, the
       printer should be able to print IBM's graphic characters (line
       drawing characters).


                          Part II - Quick Start


3.   QUICK START GUIDE

     This part is for those who want to get started right away, and
     prefer to just go ahead and try a program instead of reading a pile
     of documentation. If you want details on a topic, it may be looked
     up in part III.

3.1  Installing

     Note: The disk version is supplied with an install program. If this
     is used, the instructions below may be disregarded.

     Make a directory on your hard-disk, name it what you like (sugges-
     tion: FPL), and put all necessary files in it. To be able to look
     at the sample routes, all files except README, MAILER and FPL11.DOC
     are required.

3.2  Starting the program

     Go to the directory you have made, type FPL <Return>. The first
     time, before you have configured the program, you may enter a
     switch for display type: M for mono display, B for black & white
     display connected to a colour adapter, and C for colour display.

3.3  Configuring and Preparing the program

     The first time you use the program, you should select SET-UP from
     the Main menu, and then CONFIGURE. Enter the data asked for, or
     just press <Enter> to leave the item unchanged. After you have gone
     through this, a file called FPL.CFG is created.

     The next thing you should do, is to select AIRCRAFT from the Set-up
     menu, and define your aircraft.

     If the nav database is not prepared in your copy of the program
     (you will see this by the files FPLFAC.DTA and FPLFAC.IDX missing,
     and that the program warns you about it), a file called FPLFAC.TXT
     will be included. In that case you will need to build the nav-
     database from FPLFAC.TXT, - unless you want to make your own
     database. This is done by selecting IMPORT in the Nav-Database
     editor.

     IMPORTANT: The program will find an existing record in the nav-
     database dramatically faster when the database is sorted in
     alphabetical order. If you append new records, or change any of the
     idents, you should select SORT/COMPRESS DATABASE in the Nav-Data-
     base menu afterwards.

3.4  Making a flight plan

     From the Main menu, select FLIGHT PLAN. At the Flight Plan menu,
     you may see an example route already there. A route in the work
     area is retained until you delete it or load another one.

     CREATING LEGS IN THE ROUTE EDITOR:
     When you want to make a new route from scratch, select NEW ROUTE,
     answer YES to erase the present route, and enter the ROUTE EDITOR.
     Select ADD LEG, and start entering data. Airfields and other nav-
     points are entered by it's identifier. If it is not found in the
     nav-database, you may enter the data manually, and, if desired,
     save it in the database. Leg #0 contains the departure field and
     nothing else. For the other legs, you will also be asked for true
     airspeed, wind etc.

     AUTOMATIC/MANUAL COURSE/DISTANCE:
     Usually you will enter "A", and let the program calculate the
     course & distance. But if you are planning a VFR flight for
     example, and pick out landmarks on the map, you may want to measure
     course & distance with a ruler instead of finding the coordinates.
     If so, select "M", and enter these data manually. (In that case,
     the Lat/Long and magnetic variation fields may be left open.)

     SID'S, APPROACHES (Mostly IFR-related):
     Since a normal leg is calculated as a straight line between the two
     waypoints, it will be incorrect if a SID or approach involves extra
     turns and manoeuvring (which they usually do). There is a feature
     which allows you to reserve a certain distance or time for such
     cases.

     If you want to start out on a Standard Instrument Departure (SID),
     you put the departure field in leg #0 as usual. In leg #1 you enter
     *SID in the FROM field, and in the TO field you enter where the SID
     ends. After typing in TAS etc., you will be asked for GS, DIST and
     TIME for the SID. You need only enter two of these items. What you
     enter here will not be affected by the TAS and Wind given for the
     leg. But the program uses these data, if given, to tell you time
     and GS if the leg was flown direct. You can then adjust the GS
     and/or time figures as appropriate.

     Similarly, for an instrument approach, you enter *APP in the FROM
     field (or *ILS or what you like, just make sure it starts with the
     "*") and in the TO field enter where the approach terminates
     (usually the airfield...). The leg before this one, should end
     where the approach starts (well, where else?).

     Note: If a SID or approach is just a straight leg (for example a
     straight in approach from a beacon), you may enter the data as for
     any other normal leg, without using the procedure described above.

     ALTERNATES:
     When you have reached your destination, you may add legs to an
     alternate (or two), if needed. First you create a leg that only
     contains *ALT (or *ALT1 or *ALTN etc., just make sure it starts
     with "*ALT") in the FROM field. In the following legs, the route to
     the alternate is described. If you need two alternates, you enter
     *ALT2 in the FROM field after you have reached the first alternate,
     and then go on to the second.

     DIVERSION FIELDS (IFR and VFR):
     In the real world, you sometimes have to change alternate right
     before departure, and you do not have the time to make a new flight
     plan. But this may be prepared for by having a list giving the time
     and fuel burn from the destination to various diversion fields on
     your flight plan. Even if you are flying VFR, such a list may
     become handy. It is created by entering *DIV in the FROM field in
     the leg after the last one of the main (and alternate) route. Each
     of the following legs contains only your DESTINATION in the FROM
     field, and a DIVERSION AIRFIELD in the TO field. You enter fuel
     flow etc. as normal, but note that these values should be an
     average for the entire flight from destination to the diversion
     field. But there is an additional item asked for, which is extra
     time in minutes for approach etc. This item may also be used for
     adding some extra minutes if the flight cannot be expected to be a
     straight line.

     When this feature is used, the list will appear in the flight plan,
     with time and fuel burn from the destination field to each of the
     optional diversion fields. Also, it will show the total fuel
     required if the airfield is used as the alternate instead of the
     planned alternate(s).

     MAP VIEW:
     A VGA display is required for this feature. It may be selected from
     the Flight Plan menu or from the Route Editor. It is not very
     sophisticated, but it will show you the route, and optionally all
     other points from the nav-database in the area covered. If you want
     a printout, you will need to use GRAPHICS.COM and the <Prt Scrn>
     key. But at least you may select black & white colours (will remove
     the menu also) to avoid a totally cluttered printout.

     PRINT/SHOW FLIGHT PLAN:
     Exit the Route Editor, and select Print/Show flight plan from the
     Flight Plan Menu. You will first be taken to a screen where you
     enter type of aircraft, what reserves you want and some weight and
     fuel data. When completed, a screen with a bunch of data about the
     flight will be shown. From here, you may view the flight plan on
     screen, print it out or write it to a text file.

3.5  Ending and Restarting PC Flt Plan

     The program may be exited from the Main Menu, or directly from the
     info screen where you select printing. In both cases, the route and
     the other flight plan data will be retained.

3.6  Nav Computer

     Selected from the Main menu. This does nothing to your flight plan,
     but is used if you want to look up quickly how far it is between
     two points, and optionally how long it will take with various
     airspeeds and winds. It also gives some more details than the route
     editor, like rhumb line distance versus great circle distance, and
     initial and final courses for great circles.


                        Part III - Detailed Guide


4.   INSTALLING

     Note: The disk version is supplied with an install program. If this
     is used, the instructions below may be disregarded.

     If you have a hard-disk, make a directory and copy the required
     files into this. The program may also be installed on a floppy
     disk. Even if you have a hard-disk, it might be convenient to also
     have the program on a floppy which you can bring with you.

     The files required to run the program are:

             - FPL.EXE              - FPLFAC.DTA
             - FPLSETUP.EXE         - FPLFAC.IDX
             - FPLFLY.DTA

     The following files should also be copied into the directory if you
     want to see an example of data making up a flight plan:

             - FPL.DTA              - FPL2.DTA

     If these files are not present, they will be made by PC Flt Plan
     during program run. They contain the route and flight plan data
     from the last run.

     If you want to be able to load the sample route files, you should
     also copy the following files:

             - Files ending with .RTx, where x is a number
             - FPLFIL.DIR

     The two EXE-files work fine if compressed with PKLite(tm), a
     shareware program that makes EXE- and COM files significantly
     smaller.


5.   STARTING PC FLT PLAN

     Make the disk and directory where the program was installed the
     current directory (i.e. CD C:\FPL), then type FPL <Return>. The
     first time, before you have gone through the configure option, you
     may enter a switch for display type. (If you don't, you will be
     asked for it anyway.) The switches are:

     - M = Mono display connected to a mono adapter (MDA, Hercules)
     - B = Black & White display connected to a colour adapter
     - C = Colour display and colour adapter.

     To use a switch, type FPL, a space, the switch and then <Return>.
     Example, which starts PC Flt Plan with mono colour settings:

             fpl m<Return>

     FPLSETUP.EXE may be run directly, but is normally called from the
     PC Flt Plan Main menu. If you go through the CONFIGURE option in
     the Set-up menu, a configuration file, FPL.CFG, will be created. Do
     not delete this. After you have configured the program, you no
     longer need to use any of the switches, nor will you be asked what
     display type you have on start-up.


6.   PREPARING THE PROGRAM FOR USE

6.1  Configuring

     The first time the program is run, you should go through the
     CONFIGURE option in the Set-up menu. When you press <Return>, you
     store the data in the input field and proceed to the next item. If
     you press <Esc>, configuring is terminated and all items are
     restored to their original settings. The various items are
     explained as you work your way through, but if you find any of them
     hard to understand, just leave the item unchanged and press
     <Enter>. None of the items are required, except the colour
     settings, and maybe the printer codes, if you have problems getting
     the flight plan printed out.

6.2  Aircraft Data

     The next thing you should do, is to enter data for the aircraft you
     will use. This is done with the option AIRCRAFT DATA in the Set-up
     menu. You may also specify aircraft data when making a flight plan,
     but it is much more convenient to have it in this little database.

     The aircraft data that can be stored are:

     - AIRCRAFT:  You may do this two ways: You can store the AIRCRAFT
       TYPE, i.e. Cessna 172. Or, if you will operate several different
       aircraft of the same type, but with slightly different Dry
       Operating Weights for example, you may have one entry for each
       aircraft and instead enter the AIRCRAFT REGISTRATION here.

     - REMARKS:  The data here are not used in the flight plans so far,
       but the entry will be shown when you select an aircraft when
       making a flight plan. If you have stored the aircraft by
       registration, you may put the type and configuration here.

     - ICAO FLIGHT PLAN NAME:  Not used by the program so far, but the
       entry is reserved for the aircraft code used in ICAO flight
       plans. Example: Cessna 172 is "C172".

     - WEIGHT UNIT:  K=Kg/L=Lbs. All weight data for an aircraft must be
       in the unit you enter here.

     - DRY OPERATING WT:  Aircraft weight, with full oil tanks,
       equipment, catering and crew. Includes everything except Payload
       and Fuel.

     - MAX ZERO FUEL WT:  If applicable. If not, enter 0.

     - MAX TAKE-OFF WT:  Yes, just that.

     - MAX LANDING WT:  If applicable. If not, enter 0.

     - START/TAXI FUEL:  Fuel normally used for start-up and taxi before
       take-off.

     - RESERVE FUEL FLOW:  Fuel consumption rate normally used when
       calculating the reserve required by the flight rules you operate
       under.

     - HOLDING FUEL FLOW:  Fuel consumption rate normally used when
       calculating extra holding, extra reserves, company fuel etc.

     - MAX FUEL CAPACITY:  Max tank capacity. Not mandatory.

     - UNUSABLE FUEL:  On some aircraft, a certain amount of the fuel in
       the tanks are considered not usable, and can therefore not be
       counted as available fuel when planning a flight.

     - ACTUAL FUEL LOAD:  Typical Fuel Load in the same unit as the
       fuel-data above . If Fuel Load varies, you may enter 0, and enter
       the number when making the flight plan.

     - ACTUAL FUEL WT:  The WEIGHT of ACTUAL FUEL LOAD above. Must be in
       the same unit as the other weight data. If ACTUAL FUEL LOAD and
       ACTUAL FUEL WT are in the same unit, i.e. lbs, you may enter 0.

     If FUEL FLOW-data and WEIGHT-data are in different units, i.e.
     gallons and pounds, PC Flt Plan must know the relationship between
     these to be able to calculate landing weights etc. This relation is
     found when the program is given ACTUAL FUEL LOAD and ACTUAL FUEL
     WEIGHT in their respective units.

6.3  Nav-Database

     GENERAL:
     The Nav-Database is accessed from the Set-up menu. This is where
     airfields, navigational aids, intersections and other facilities or
     waypoints are stored. Any frequently used point may be stored here,
     like special check-points, landmarks, oil-rigs - you name it...
     When preparing the program for use, it is a good idea to enter the
     facilities in your local area. You can later add points as you
     create routes, since the route editor allows you to enter data for
     a facility not found in the nav-database, and save it.

     When in the route editor, searches are made on the facility's
     identifier. The program will find an existing facility in the nav-
     database dramatically faster when the database is sorted in
     alphabetical order. The reason is that the program first executes a
     fast alphabetical search, and, if the facility is not found, a
     sequential search from top to bottom is initiated. The database is
     not maintained in a sorted order automatically however. It is
     therefore recommended to use the SORT/COMPRESS function (explained
     below) after having added new facilities, or changed any of the
     identifiers. This function also removes empty records, which will
     appear when facilities are deleted.

     DATABASE STRUCTURE:
     The database consists of the files FPLFAC.DTA and FPLFAC.IDX. It is
     strongly recommended to maintain backup copies of these files on a
     separate disk!

     Each facility makes up a record. Each record consists of the
     following fields:

     - Ident (For example airport code)
     - Name  (Name of the facility)
     - Latitude (North/South geographical coordinates)
     - Longitude (East/West geographical coordinates)
     - Magnetic Variation 
     - Frequency

     IMPORTANT: Commas should not be used in any of the fields, as these
     are used for separating the fields when exporting to- or importing
     from an ASCII file!

     Note that in most countries, the three letter and four letter
     airfield codes are totally different. The 3 letter codes are those
     used by airlines and their international SITA network, while in
     most countries the 4 letter ICAO codes are used in ATC flight
     plans, notams, weather forecasts etc. USA is a bit special though,
     if you take a 3 letter US airfield code and put a "K" in front of
     it, you have the 4 letter ICAO code. In PC Flt Plan, it is
     recommended to use the four letter codes for airfields, to
     distinguish them from the airport VOR's (In the US, the idents are
     often the same). Also, the Map View function will then be able to
     distinguish between airfields and other facilities (nav-aids and
     fixes never have a 4 letter code).

     Examples:
                                3 letter code    ICAO code
             London/Heathrow        LHR            EGLL
             New York/Kennedy       JFK            KJFK

     For those who want some more technical info: The file (fplfac.dta)
     is a random access file. Searches are done in a separate, parallel
     file (fplfac.idx), which contains only idents, to speed up the
     sequential search somewhat. As mentioned, the alphabetical search
     is very fast, even on large databases, but the sequential search is
     not that bad either; - on a 386sx/25 with a cache program
     installed, PC Flt Plan uses a little over 2 seconds to search
     through a database with 3000 records.

     CREATING/EDITING FACILITIES:
     From the Main menu, select SET-UP, then select NAV-DATABASE. Here,
     facilities may be viewed, edited, added, listed or written to a
     text file in ASCII format. Note that if you delete a facility, a
     blank record will appear, as the record itself is not removed. When
     you add a new facility, the data will be stored in the first empty
     record found, or appended to the end. The SORT/COMPRESS function
     will remove any blank records and sort the database in alphabetical
     order.

     An alternate way to edit the database, is to use the EXPORT
     function (in the Nav-Database menu) to export it to an ASCII file.
     The file is comma delimited, which means that it may be imported
     into most database- or spreadsheet systems, or you may edit it in
     your favourite text editor. After external editing, use the IMPORT
     function to rebuild the database from the ASCII file. If you have
     specified a text editor in the configuration, you may call this
     from the function EXPORT/IMPORT/EDITOR. Otherwise, you have to
     leave PC FLT Plan, run your editor, then restart PC Flt Plan. The
     format of the ASCII file, necessary to import records correctly, is
     explained in detail in the program.

     FUNCTIONS IN THE NAV-DATABASE EDITOR:

     - NEW RECORD:  To add a new facility. The program first asks for
       the identifier, and checks for no others records with the same
       ident.

       If the database covers several countries, you may run into
       duplicate identifiers. A way to handle that is to add the two
       letter ICAO country code. An example: Midhurst VOR in England has
       the identifier "MID". The country code for Great Britain is "EG",
       so the ident may be entered as "MID EG". This will never be
       necessary for airfields however, as long as their 4 letter ICAO
       codes are used.

     - FIND RECORD:  Searches for a facility with a given identifier.

     - SEARCH ON NAME:  Searches for all records containing the name, or
       part of a name, you specify. For example "okman" will find
       "Brookmans Park". Note that the search is made on the NAME fields
       only, not the idents.

     - EDIT RECORD:  Change any item in a record. If you change the
       ident, a search for duplicates will be performed.

     - DELETE RECORD:  Deletes the facility presently shown, and
       replaces it with a blank record.

     - LIST RECORDS:  Lists out facilities on screen. If anything is
       entered in the input field which appears, only records with
       identifiers starting with the letters you type will be listed.

     - SORT & COMPRESS:  Sorts the database in alphabetical order, and
       removes any blank/empty records. It first writes the records to a
       temporary text file. This file is sorted using the DOS sort, or
       any other sort program specified in CONFIGURE. If the ASCII file
       becomes larger than 64 Kilobytes, the DOS sort will not handle it
       however, requiring an external sort program. Many good and small
       shareware programs that sort text files are available for this
       purpose. After this process, the database is rebuilt from the
       resulting sorted file.

     - EXPORT/IMP./EDITOR:  From here, you may export the database to a
       comma delimited ASCII file, or import from the same. When
       importing, the records may be appended to the existing database,
       or replace the existing database. If an external editor is
       specified in CONFIGURE, this is also accessed from here

     - HELP:  A brief help screen.

     - QUIT:  Returns to the Set-up menu.


7.   HOW TO MAKE A FLIGHT PLAN

7.1  Data

     The flight plan is made from two sets of information:

     - ROUTE DESCRIPTION:  The route to be flown from point of depar-
       ture, through several waypoints to the destination, and if
       required, to one or two alternates and/or a list of diversion
       fields. Altitude/flight level, winds, true airspeed and fuel flow
       are entered for each leg. For IFR flights, special legs like
       SID's, approaches etc. may be entered.

       This is the information that is stored when you save a route.
       When you load a route; winds, TAS etc. may be changed quickly for
       the entire flight without having to edit each leg.

     - FLIGHT PLAN DATA: Aircraft (and it's data), reserves, fuel load
       and payload. These data are not saved together with the route,
       but are contained between program sessions.

     Normally, you will first create the route to be flown, or load a
     previously saved route and make the necessary changes, - and then
     enter the flight plan data. The program takes you through an input
     screen for these data when you select PRINT/VIEW FLIGHT PLAN from
     the Flight Plan menu.

7.2  Create/Edit a Route

     Select FLIGHT PLAN from the Main menu. To clear the route in the
     work area, if any, and start from scratch; select NEW ROUTE and
     answer Yes to erase.

     If you want to use a route saved on disk, select LOAD ROUTE, and
     select from the routes shown. Any route present in the work area
     will be deleted when loading a new one. You may edit the loaded
     route in the Route Editor, or you may change FL/Alt, TAS, Wind or
     Fuel Flow globally for all or several legs by selecting GLOBAL
     CHANGE from the Flight Plan menu.


8.   ROUTE EDITOR

8.1  Legs

     Enter the Route Editor by selecting FLIGHT PLAN from the Main menu,
     then ROUTE EDITOR from the Flight Plan Menu.

     Select ADD LEG to create new legs.

     When some legs have been created, the <Left> and <Right> keys can
     be used to move between the legs. <PgDn> or <PgUp> will advance/go
     back 10 legs respectively. Select EDIT LEG if you want to make
     changes. The <Up> and <Down> keys are used for moving between menu
     items.

     If you delete or insert a leg, be aware that the TO and FROM fields
     will not match between the legs before and after, you must there-
     fore edit these as necessary after such an operation!

     Leg #0 holds the point of departure only. No further data are
     entered for this leg.

8.2  To / From Fields

     In the TO and FROM fields, you enter the facility's identifier. The
     program then searches the nav-database. If the facility is not
     found, you may enter lat/long coordinates, name, magnetic variation
     and frequency manually. You will then also be asked if you want to
     save the waypoint in the nav-database.

     You do not have to enter lat/long coordinates if you want to enter
     course and distance manually instead of letting the program
     calculate these (See 8.3). This may be useful if you plan a trip
     where you just pick landmarks on the map as waypoints and measure
     course/ distance with a ruler.

     A star (*) as the first character in the FROM-field denotes a
     special leg, which is used for SID's, STAR's, approaches etc. They
     are also used together with codes to separate the route to
     destination, to the alternate(s), and the diversion list:

     *xxxx - A "*" and up to 4 characters is used when you want to enter
             a SID, STAR, or approach instead of a straight leg. "xxxx"
             can be anything (i.e. "SID", "ILS", "APPR" etc.) except for
             the codes below. In the TO field enter the point where the
             leg ends. For these legs you will be asked for estimated
             average ground speed, time or distance. You only have to
             enter 2 of the values. For example if you want to reserve
             10 minutes of fuel for an approach at the destination, you
             can enter 10 minutes and the average GS for the approach.
             The program will then calculate the distance this
             represents and add it to the total trip distance.

     *ALTx - Means that the route after this leg describes flight to the
             ALTERNATE(s). No further data are entered in a leg with
             this mark, it is used as a separation line. "x" may be
             anything, for example "1" or "2". This code may be used
             twice in a route description. If used, the route will be
             divided into the following sections:

             - Before any *ALTx  :  From DEP.FIELD to DESTINATION
             - After first *ALTx :  From DESTINATION to ALTERNATE 1
             - After second *ALTx:  From ALTERNATE 1 to ALTERNATE 2

             (The reason you can have two alternates is that under some
             regulations, you can file a flight plan to an airfield
             which is below weather minimums, - provided that you have
             two alternates. The first alternate must then have landing
             minimums, the second must be above alternate minimums.)

     *DIV -  Means that the following legs make up a DIVERSION list.
             These legs are shown on the flight plan as a list of
             optional alternates. They show time and fuel used for
             direct flight from DESTINATION to the various DIVERSION
             fields, plus extra time for approach or extra route
             distance, which may be entered for these legs.

8.3  Automatic or Manual Calculation of course/dist:

     For straight legs you enter "A" or "M" for Auto or Manual course &
     distance. If you select "A", course & dist will be calculated from
     the lat/long coordinates and magnetic variation for the waypoints. 

     If for example you find that the course differs a degree or so from
     what is found on your IFR-chart, and you want it to be the same, -
     you may select "M" and enter the magnetic course manually. When
     using the "M" option, no lat/long coordinates or magnetic variation
     are required.

8.4  Flight Data

     When FROM and TO for a leg are defined, you enter the following
     data:

     - FL/ALT:  Flight Level or Altitude. These data are not used by any
       calculations, but are shown as information about planned- or
       minimum altitudes on the flight plan. It is recommended to enter
       the values as in ATC flight plans; for example "F090" for Flight
       Level 90, "A050" for 5000 feet. Or you may use "CLMB", "DESC",
       "VFR" or whatever you like.

     - TAS:  True AirSpeed in knots.

     - WIND:  Wind Direction (what direction the wind comes FROM), and
       Wind Speed in knots.

     - F.FLOW:  Fuel consumption per hour.

8.5  Map View

     (Selected from the Flight Plan menu or in the Route editor)

     This function only works with a VGA display or better. When you
     select MAP VIEW, you will see a graphical representation of the
     route and waypoints. From the Route Editor, the map will be centred
     around the current waypoint, while from the Flight Plan menu, the
     map will fit the entire route.

     The program does not have graphical printing capability, but if you
     load the DOS program GRAPHICS.COM (which is a resident program)
     before starting PC Flt Plan, you can print out the display by
     pressing <Prt Scrn> (if your printer supports graphics that is!).
     Before you press <Prt Scrn>, press P to change all the colours to
     black & white. This also removes the menu from the display. To get
     the colours and menu back, press P again, or simply press <ESC> to
     quit the map display. This is somewhat crude of course, but it does
     work.


9.   PRINT/VIEW A FLIGHT PLAN

9.1  Flight Plan Data

     When the route has been defined, you select PRINT/SHOW FLIGHT PLAN
     from the Flight Plan menu. You will then be taken to an input
     screen, where the Flight Plan Data are entered. The following data
     may be entered or changed here:

     - DATE:  Date of flight.

     - FLTNO/CS:  Flight Number or Call-sign.

     - AIRCRAFT:  The aircraft picked from the aircraft database, or one
       that you specify here.

     - SKED DEP:  Scheduled time of departure (block).

     - SKED ARR:  Scheduled time of arrival.

     - FINAL RESERVE:  Reserve required by the flight regulations you
       operate under. Enter minutes and fuel flow.

     - ROUTE RESERVE:  Additional reserve in PERCENT. If used, the
       amount will be calculated as the specified percent of fuel
       required to destination and to the alternate(s), if any.

     - EXTRA HOLDING:  May be used for expected holding, company fuel or
       similar. Enter minutes and fuel flow.

     - START/TAXI:  Fuel used for start-up and taxi, before take-off.
       The minutes are estimated time from off block to airborne. Will
       be counted when ETA is calculated.

     - UNUSABLE FUEL:  On some aircraft, the last rest of fuel in the
       tanks is considered not usable, and can therefore not be counted
       as available fuel.

     - ACTUAL RAMP FUEL:  Planned fuel load. AMOUNT must be in the same
       unit as the fuel flow figures above. WEIGHT must be in the same
       unit as the other weight data. If Fuel LOAD and WEIGHT are in the
       same unit, just enter 0 in the weight field.

     - DRY OPERATING WT:  Aircraft weight, with full oil tanks,
       equipment, catering and crew. Includes everything except payload
       and fuel.

     - ACTUAL PAYLOAD:  Planned payload.

9.2  Print or Show the flight plan

     When you have entered the Flight Plan Data, a screen with a summary
     of the flight will be shown. From here you may print out the flight
     plan or view it on the screen. Explanation of some of the items
     showed:

     - TIME:  Airborne time (hr:mins) to destination.

     - BURN:  Start/Taxi-fuel + trip-fuel to destination.

     - DIST:  Distance (NM) to destination. Includes approaches.

     - AVG.WC:  Average wind component to destination (plus=tail-wind,
       minus=head-wind).

     - DEP:  Scheduled Time of Departure.

     - ETA:  Estimated Time of Arrival at destination. Taxi time at the
       departure field is counted in.

     - NO WIND:  Burn/Time to destination if there had been no winds.

     - REQUIRED FUEL:  Total fuel required, considering flight to
       destination, alternates(s) (if any), winds, reserves and
       start/taxi.

     - EXTRA FUEL:  The difference between Required fuel and Actual fuel
       load. The time shown is the approximate flight time this represe-
       nts, calculated from the average consumption to destination and
       alternate(s).


     If you have trouble printing out the flight plan, try to find the
     proper printer codes and enter them under the configuration option
     in the Set-up menu.

     If this doesn't work, you may try another solution: Select PRINT
     FLIGHT PLAN TO FILE. The file written is in plain ASCII, and may be
     imported into a word processor and printed from here. For the
     "knee-board size", select a font with a pitch of around 17
     characters/inch and normal line height.

     The two A4-variants send only plain ASCII-text to the printer, and
     should therefore be usable on most printers.


10.  ABOUT THE FLIGHT PLAN

10.1 Leg Times

     In the flight plan produced, the time for each leg is rounded up or
     down to the nearest whole minute. But the small difference between
     the accurate leg time and the whole minute is added or subtracted
     to the next leg time. This is the same method used in professional
     flight planning systems used by airlines. The reason for this is
     that on a trip with many legs, the total time may become several
     minutes wrong if for example most of the legs happen to be rounded
     down.

10.2 Fuel

     The fuel amount shown in the last column of the flight plan is the
     remaining fuel you would have over the checkpoint if you departed
     with the TOTAL FUEL REQUIRED. This way you can see if you have all
     your specified reserves intact along the flight. If you have less
     fuel, you have started to consume your reserve, route reserve or
     extra holding fuel.

10.3 Corrections

     The correction factors shown on the flight plan are fuel and time
     to destination, and total fuel required if the conditions were:

     - NO WIND:  No winds at all.

     - +20KT:  20 knots more TAIL-WIND than the average wind component
       you get from the winds you have planned for.

     - -20KT:  20 knots more HEAD-WIND than the average wind component
       you get from the winds you have planned for.

     Example: If you get an average wind component of +7 knots (tail-
     wind), the "+20" will be the figures for 27 knots tail-wind, while
     the "-20" will be the figures for 13 knots head-wind. The "no wind"
     will be for no winds, no matter what the planned winds are.

10.4 How to use the ETO/RTO/ATO fields

     After take-off, you start filling out all the Estimated Time Over-
     head (ETO) fields all the way down to destination, using the leg
     times given. Usually, you will only put down the minutes, except
     when starting on a new hour.

     When you pass a waypoint, you write down the time in the Actual
     Time Overhead (ATO) column, then calculate the new estimated time
     for the next waypoint, and put this in the Revised Time Overhead
     (RTO) column for that point. This way, you will have a fresh
     estimate for the next reporting point for ATC (and yourself).

     As you now pass the waypoints, it will be very easy to see if you
     are ahead or behind the flight plan by comparing ATO and the
     original ETO (the latter was calculated in relation to the take-off
     time).


11.  NAV COMPUTER

     This function is entered from the Main menu. It does nothing to
     your flight plan, but is used if you want to look up quickly how
     far it is between two points, and optionally how long it will take
     with various airspeeds and winds. It also gives some more details
     than the route editor. The following data are calculated:

     GREAT CIRCLE: - Initial course, in true & magnetic
                   - Final course,    "   "  "    "
                   - Average course,  "   "  "    "
                   - Distance.

     RHUMB LINE:   - Course, in true & magnetic
                   - Distance.

     (Great circles and rhumb lines are explained in chapter 12.)


12. TERMS & ABBREVIATIONS USED IN THE PROGRAM

Acc    - Accumulated time
AMT    - Average Magnetic Track
ATC    - Air Traffic Control
ATO    - Actual Time Overhead (when passing a waypoint)
ATT    - Average True Track
Alt    - Altitude
Arr    - Arrival
Burn   - Fuel Burn
CS     - Call Sign
Dist   - Distance in nautical miles
DOW    - Dry Operating Weight. Weight of everything except payload
         (cargo/passengers) and fuel
Dep    - Departure
Dest   - Destination
ETA    - Estimated Time of Arrival
ETD    - Estimated Time of Departure
ETO    - Estimated Time Overhead
FF     - Fuel Flow (Fuel consumption per hour)
FL     - Flight Level
Flt No - Flight Number
GS     - Ground Speed. Speed in relation to the ground after wind
         effect is taken into account
Kts    - Knots ( = speed in nautical miles per hour)
LWT    - Landing Weight
MH     - Magnetic Heading
MLWT   - Max Landing Weight
MT     - Magnetic Track
MTOW   - Max Take-Off Weight
MZFW   - Max Zero Fuel Weight
NM     - Nautical Miles (1 NM = 1.852 meters)
RTO    - Revised estimated Time Overhead. (You may also encounter
         RTO used as an abbreviation for Rejected Take-Off.)
Rte Res- Route Reserve. In percent of fuel used to destination and
         alternate(s)
TAS    - True AirSpeed
TOW    - Take-Off Weight
WC     - Wind Component (Headwind or tailwind)
ZFW    - Zero (wing) Fuel Weight. Weight of everything except fuel.
         Larger aircraft usually have a max limit on this, because if
         the aircraft body is loaded up while the wings remain light
         (little fuel in the wing tanks), the bending loads on the wings
         will be excessive.

Great Circle - The shortest line between two points on the earth. Over a
               large distance, or at high latitudes, the course may
               change considerably trough the flight.
Rhumb Line   - (Also called loxodrome track) A line between two points
               on the earth which crosses all meridians at the same
               angle. This means that the course will remain the same
               all along the route. Over a large distance, or at high
               latitudes, a rhumb line will be significantly longer than
               the great circle.

         Note: In the route editor, all legs are calculated as great
               circles. The course is the average course.