PSP™ (PlayStation®Portable) Basic Specifications and Features (10.08.05)

| Product Name | PlayStation®Portable |
| --- | --- |
| Colour | Black |
| Product Code | PSP-1002K |
| Dimensions | Approximately 6.7 in (W) x .9 in (H) x 2.9 in (D) |
| Weight | Approximately 280g / .62 lbs (including battery) |
| CPU | PlayStation Portable CPU (System clock frequency 1 - 333MHz) |
| Main Memory | 32MB |
| Embedded DRAM | 4MB |
| Display | 4.3 inch, 16:9 widescreen TFT LCD 480 x 272 pixel, 16.77 million colours Maximum luminance 180 / 130 / 80cd/m2 (when using Battery Pack) Maximum luminance 200 / 180 / 130 / 80cd/m2 (when using AC Adaptor) |
| Sound | Built-in stereo speakers |
| Main Input/Output | IEEE 802.11b High Speed USB (USB 2.0) Memory Stick Duo™ IrDA |
| Main Connectors | Memory Stick Duo™ slot USB connector DC OUT connector DC IN 5V connector Headset connector |
| Power | Lithium-ion Battery AC Adaptor |
| Disc Drive | UMD Drive (Read only) |
| Profile | PlayStation Portable Game UMD Audio UMD Video |
| Codec | [Video]: “UMD”: H.264/MPEG-4 AVC Main Profile Level 3 [Video]:“Memory Stick”: MPEG-4 SP, AAC [Music]: “UMD”: linear PCM, ATRAC3plus™ [Music]:“Memory Stick”: ATRAC3plus™, MP3(MPEG1/2 Layer3) [Photo]: JPEG (DCF2.0/Exif2.21) |
| Security | (Encryption) 128bit AES (Copyright protection technology) MagicGate™ |
| Access control | Region, Parental Control |
| Wireless communications IEEE802.11b | Infrastructure Mode Ad Hoc Mode (connects up to 16 PlayStation Portable systems) |
| PLAYSTATION PORTABLE Value Pack supplied accessories | AC Adaptor Battery Pack Memory Stick Duo™ (32MB) Pouch (Black) Headphones with Remote Control (White) UMD In-pack Sampler Wrist Strap (White) Cloth (Light Grey) |