CHANGES AND UPDATES TO MS-DOS KERMIT 3.15

This file lists the changes and corrections in each Beta pre-release of
MS-DOS Kermit 3.15, in reverse chronological order.

The following Appendices are included at the end of this file:

APPENDIX I:   LATIN-2 COMPOSE SEQUENCES
APPENDIX II:  MS-DOS KERMIT AND PPP
APPENDIX III: MEMORY MANAGEMENT

____________________________________________
Preliminary Final Release, 15 September 1997

Beta 25 with Beta notice removed and new date, code freezed.  IBM PC and
compatibles only.  Accompanying text files still need to be updated.

FILENAME       SIZE   DESCRIPTION       

MSK315.EXE   251768   Full-featured version
MSR315.PCH      325   Initial patch for full-featured version
MSK315M.EXE  199356   Medium version: no networks, serial connections only
MSRM315.PCH     317   Patch for medium version
MSK315N.EXE  164312   Lite version I: networks included, no terminal emulator 
MSRN315.PCH     327   Initial patch for Lite version I
MSK315L.EXE  113414   Lite version II: no terminal emulator or networks
MSRL315.PCH     310   Initial patch for Lite version II

_________________________
Beta 25, 6 September 1997

New commands:

SET INPUT FILTER-ECHO { ON, OFF }
   When ON (which is the default), only printable characters and controls
   are sent to the screen when INPUT ECHO is ON.  When OFF, all incoming
   characters (except NUL and DEL, which are discarded) are passed to the
   screen, the idea being that a console driver (such as ANSI.SYS) will
   process them and format the screen nicely -- this only works if the
   escape and control sequences coming from the host are recognized by the
   console driver; remember, MS-DOS Kermit's terminal emulator is NOT
   active during INPUT commands.

Bugs fixed:

 . IF NUMERIC did not work for unsigned numbers longer than one digit.

 . \frpad() and flpad() ignored a blank third argument and used the closing
   paren instead.

 . Array elements could not be assigned, e.g. by READ.

 . Writing an empty array element into a file could cause MSK or DOS to crash.

 . Assigning \%x variables inside SWITCH statement didn't work.

 . SERVER <time> was broken; if a timeout value was given, it did not work
   until and unless some packets were exchanged.

 . S, I, and A packets and/or their ACKs could be sent that were longer than
   the requested size; conversely, incoming packets that were longer than the
   requested size could be rejected even when the actual buffer was long
   enough to accommodate them.  Both conditions have been corrected.  This
   problem was evident only when very short packet lengths were requested.

____________________
Beta 24, 15 Aug 1997

The following bugs were fixed:

 . Host-directed printing would not stop if the stop-printing sequence
   was <ESC><CSI>4i, rather than simply <ESC>[4i or <CSI>4i.

 . Under certain conditions, an overlong Kermit data packet could be sent.

___________________
Beta 23, 3 Aug 1997

ANSI terminal emulation modified to allow use of the 25th line by
direct cursor addressing and by scrolling.

DG 217 emulation added.  Does not support UNIX mode.

____________________
Beta 21, 19 May 1997

The status-line clock now can show elapsed time for the current connection
via SET TERMINAL CLOCK { ON, OFF, ELAPSED-TIME }.  ON shows time of day,
ELAPSED-TIME shows elapsed time.  Also the clock sampling and display
mechanism were adjusted to prevent flickering in Windows, and so now
is ON by default for both DOS and Windows 3.x.  The elapsed-time clock can
also be set back to 0 with the new RESET CLOCK command.

New \Kdebug Kverb added, to toggle SET DEBUG SESSION while in CONNECT
mode, and assigned to Alt-d by default.  This removes the necessity to
escape back, SET DEBUG SESSION, and reconnect to get terminal-screen
debugging, and then escape back, SET DEBUG OFF, and reconnect to turn it
off again.

\Kreset (reset the terminal emulator) assigned to Alt-r for compatibility with
Kermit 95.  It is also still on Alt-=, as before.

Additional TCP/IP stack monitoring and debugging facilities (refer to Beta 10
description below).  SET TCP/IP DEBUG ON now adds a performance meter to the
CONNECT-mode status line.  Regular TCP/IP debugging material is displayed on
the terminal screen by default, or if you have a transaction log active, it is
written to the log instead.  But in both cases, the new fields are shown in
the status line:

  nnnnR = Number of microseconds to Receive an IP packet.
  nnnnT = Number of microseconds to Transmit an IP packet.

The packet times are displayed when a packet is transmitted, so the R field
represents the most recent reception.  Smaller numbers mean fewer cpu cycles
devoted to packet movement between Kermit and the LAN adapter; small is good.

The most precise numbers occur when using Novell ODI drivers.  Packet drivers
produce spuriously tiny reception values, because most of the board work
occurs before Kermit is notified (and hence before Kermit can time the
reception process).  In the case of reception Kermit measures the time between
being first asked for a buffer and when the LAN driver finally reports the
buffer is filled.  For transmission, Kermit initiates events and the time is
between Kermit's initial command to the LAN driver to transmit a buffer and
the LAN driver's final reply that it has done so.  The important point is the
times measure Kermit to/from LAN driver events.

______________________
Beta 20, 23 April 1997

Another adjustment to DHCP material to make sure the server ident field is not
created spontaneously.  And to stop any misunderstandings about "time since
boot" the client secs field is forced to 0 in all packets.  Plus protection
against endless retries on rejected IP lease renewals; needs testing.

______________________
Beta 19, 13 April 1997

Changes to DHCP client operation.  Xander Jansen pointed out that some new
small-office routers, such as the 700 series from Cisco, have changed their
expectation of what a DHCP client must say to gain service.  The prevailing
formal rules were in RFC1541 and nearby documents.  Brand-new RFCs 2131 and
2132 (April 1997) describe a method which is in direct contradiction to RFCs
1541 1533.  When testing MS-DOS Kermit 3.15 Beta 18 against the small router,
Xander found the router rejected the client.  In Beta 19, the DHCP support was
changed to be compatible with both ways of being a DHCP client, trying first
the RFC2132/2133 method and if that is rejected then the RFC1541 method.

SHOW COMMUNICATIONS now distinguishes DHCP from BOOTP.

_________________________
Beta 18, 14 February 1997

Corrections:

 . Long-standing bug of being unable to delete characters via CSI P which are
   within four columns of the left margin while in 132 column video mode.

 . Bug introduced into beta 17 while adding \f(filespec). This forced the
   requested filename pattern to be prepended as a path to individual
   filenames of an incoming GET request, resulting in failure to find the
   files.

Changes:

 . Modify the VT100 terminal ident from very long standing vanilla ESC ? 1 c
   to be ESC ? 1; 0 c to satisfy some string matching style remote
   programs.  Similarly use ESC ? 6; 0 c for VT102.

________________________
Beta 17, 9 February 1997

Beta 17 fixes the following bugs:

 . A TAKE file once opened was never closed.

 . Macro argument variables, \%0..\%9, were not removed after the last nested
   macro exited and thus collided with possible non-macro use of the same
   variable names.

 . A harmless message occurred if a macro expected several arguments and fewer
   were provided on the invocation line.

 . A correction for Data General terminal emulation to clear video attributes
   adversely affected VTxxx emulations, leading to unwanted underlining, etc,
   after an erasure operation. This occurred only in Beta 16.

 . SET KEY definitions involving a macro name were not parsed properly in a
   few annoying cases.

And adds the following new feature:

 . New variable \v(filespec) shows the filename pattern most recently used for
   sending or receiving files. It may contain wild cards and paths, depending
   on what the user typed.

________________________
Beta 16, 6 February 1997

In this issue we try to resolve known problems with the INPUT
command.  Some coding errors were discovered and fixed.

The length of SET KEY definitions is down to 150 bytes maximum, because
borrowing a longer buffer causes internal interference (MSK 3.15 Beta 15
introduced the much longer buffer (borrowed)).  A consequence of that
interference was loss of ability to invoke macros within key definitions

Finally, an undiscovered omission in Data General terminal emulation
was pointed out by Jeff Altman: underlining was not turned off when a Form
Feed command arrived.

________________________
Beta 15, 3 February 1997

Key definitions can now be up to 1K in length.  The previous maximum length
was 127 bytes.

Some glitches fixed in the INTRO screen.

There is now a new SET PARITY option.  It is mostly untested, so testing is
needed by those in a position to test it:

  SET PARITY { EVEN, ODD, MARK, SPACE, NONE }

behave as before: SET PARITY none establishes 8 data bits, no parity; the
others 7 data bits and 1 parity bit.  The new option is:

  SET PARITY HARDWARE { EVEN, ODD, MARK, SPACE }

When this command is given, MS-DOS Kermit uses 8 data bits and 1 parity bit,
and parity is handled by the hardware (i.e. the UART).  This feature is added
for the benefit of certain devices that can only communicate with 8 data bits
and one parity bit, and should not be used except when absolutely necessary,
since hardware checking of parity is a great deal less intelligent and
tolerant than the normal software handling done by MS-DOS Kermit itself.
SET PARITY HARDWARE works only on real serial ports; not on BIOS ports,
FOSSIL ports, or network connections.

_______________________
Beta 14, 27 January 1997

New REGET command.  REGET is to GET as RESEND is to SEND: file transfer
recovery of interrupted binary-mode transfers, in this case when downloading
from a Kermit server.  Works only when Kermit's FILE TYPE is BINARY.

\v(date) format changed to "27 Jan 1997" for compatibility with C-Kermit.
Language-independent numeric (Julian) dates are available as \v(ndate), as
always.

The new CONNECT-mode status-line clock (with blinking colon) is turned off
when running under Windows, even in a full-screen DOS box), to stop flickering
of the display caused by Windows recovering from a polling DOS call to get the
time of day.

The CONNECT-mode status line is now refreshed to show the proper printing
status if a printer is unavailable, rather than leaving a ghost "PRN"
indication if printing has been terminated.

_______________________
Beta 13, 4 January 1997

SET KEY syntax simplified; curly braces no longer required when mixing
Kverbs, Kmacros, and text strings except to resolve ambiguities or to
preserve leading and/or trailing whitespace.  Thus:

  set key \315 \kkp4\kkp5 foo \kkp6

is now a legal definition, resulting in those three verbs being seen at
keypress time, and the embedded string is sent in the middle of them.  The
old, more complicated syntax, is still accepted.

_________________________
Beta 12, 26 December 1996

A timer-related problem was fixed that could cause MS-DOS Kermit to block
(hang) on a TCP/IP connection for up to a minute or more if a sent packet
were lost while slowly sending tiny packets. This problem was most
frequently observed in Telnet terminal sessions, while typing.

IF commands containing variables were being overevaluated; e.g.:

  if = \%i 4 decrement \%i

Such statements now work again.

The following command-related changes were made for compatibility with
C-Kermit 6.0:

 . The LOCAL command now works with macro names as well as \%x variable 
   names.  So, for example:

     LOCAL FOO BAR \%A

   declares three local variables, foo, bar, and \%a.  FOO and BAR are macro
   names, which can be used either as "local subroutines" or as long-named
   variables accessible via the \m(name) construction.

 . The LOCAL command can now be used not only in macro definitions, but also
   in command files.  This allows construction of portable command procedures
   with private data, without danger of conflict with variable names already
   in use by other procedures.

 . MSLEEP added as a synonym for MPAUSE (millisecond sleep).

(There was no open Beta 11)

_________________________
Beta 10, 18 December 1996

New items:

 . Add built-in Cyrillic support for the terminal emulator:
   SET TERMINAL CHARACTER-SET { CYRILLIC-ISO, KOI8, SHORT-KOI },
   SET TERMINAL CODE-PAGE CP866.  Previously this was done with command
   files (lots of SET TRANSLATE INPUT and SET KEY commands), but that did
   not work well with ISO 2022 character-set designation and invocation
   (G0, G1, G2, G3 switching, VT220 line-drawing characters, etc).

 . Modify commands ASSIGN, DEFINE, UNDEFINE, _ASSIGN, and _DEFINE for the
   syntax expressing array names.  Each permits expressions and variables
   within the [index] field.  Assign, define, and undefine do not permit
   substitution in the spelling of the array name of \&<character>; _assign
   and _define do permit it.

 . Add keyword IF to the list for command CHECK.  CHECK IF reports that
   extended IF statements are present.

 . Add UNDEFINE variable/macro to undefine an item. This is the same as the
   DEFINE command with no definition text.

 . Add XECHO string to display the string without the leading CR/LF.

 . Add variable \v(connection) which always returns string "local".

 . Add function \fbasename(filename) which returns the filename without
   its drive letter and path prefix.

 . Keyboard definitions to invoke named macros had used definitions of the
   form {\kmacro-name}. The surrounding curly braces are no longer required,
   but they may be used with older material.  This also means the syntax for
   specifying keyboard "verbs" and macros is now the same.

Corrections:

 . SET KEY \xxx {\Kmacroname} was broken in earlier betas.

 . DEC User Defined Keys returned illegally and crashed the program.

 . Correct a small bug with processing DEC Sixel graphics.

 . SET PRINTER to a file which could not be opened crashed the program.

 . LOCAL list of \%<char> variables failed to skip items in the list which
   were not of the form \%<char>.

 . Revise the TCP/IP protocol stack code to be less agressive in sending long
   groups of packets but more agressive in responding to network
   congestion.  The result should be fast transfers with fewer packets lost
   from too many packets per second on the wire.

 . Add code to catch errors of delivering TCP/IP packets from the LAN adapter
   driver to Kermit. The error of interest is when a packet buffer is
   allocated from Kermit but the LAN driver fails to signal that the buffer
   has been filled with a new packet.  Failures are visible when command SET
   TCP DEBUG ON is given, and they may be made invisible but recorded in the
   Transaction log if command LOG TRANSACTION filename is stated.
 
 . Included in the TCP debug information are arriving ARP broadcasts (good for
   testing if the LAN adapter is still receiving) and IP packet transit time
   details. For specialists, the timing details appear as lines like this
   example, where fields are:

     time=2093 rtt=1 avg=0 std_dev=1 s->rto=5

   time since the TCP stack started, current IP packet round trip time (rtt),
   smoothed average rtt, standard deviation of the difference, and the round
   trip timeout, all in units of Bios clock ticks (18.2 of them per
   second). Message "Failed to put packet on wire" is written if the lan
   adapter is unable to perform a transmission requests; Kermit retries the
   attempt.

 . Add a test for Control-C or Control-BREAK being typed while waiting for a
   TCP byte stream to be delivered to the remote host.  This is an attempt to
   break free of waiting while Kermit file transfer packets are held back
   because TCP is waiting for an ACK to previously sent material.  Such waits
   can be several minutes in bad cases.  This test is of limited usefulness.

 . Fill in a Reverse ARP request field which is normally empty and ignored but
   might be looked at anyway.

 . Fixed a problem which crashes the program when going between text and
   graphics screens when neither extended nor expanded memory is used to
   preserve the graphics screen.
   
 . Time-of-day clock added to status line, with blinking colon.  If this
   produces any unwanted effects, use "set term clock off" to disable it.

(Beta 9 was skipped)
_________________________
Beta 8, 10 September 1996

New items:

 . Add keyboard verbs \Ksession1 through \Ksession6 to select 
   a particular Telnet session of the six available (versus the 
   \Knextsession toggle). These new verbs are not preassigned
   to keys.

Fixes:

 . Current directory, as shown in prompt, was over-evaluated.

 . Bug with UDKs fixed.

 . \v(drive) value had a spurious null character on the end.

 . SET PRINTER problems displayed gibberish rather than a proper 
   error message.   

 . No Ping response was generated for SLIP connections.

 . SHOW SESSIONS did not wait for a confirming Enter key.

 . \v(input) lost its text.

 . Invoking macros within macros which used END to leave had
   confused the END command.

------------------------
Beta 7, 7 September 1996

New items:

Modify assign/define/undefine/_assign/_define for array name syntax.  All
permit expressions and variables within the [index] field.  Assign, define,
and undefine do not permit substitution in the array name of \&<character>;
_assign and _define do permit it.

Add keyword IF to the list for CHECK.  CHECK IF always succeeds, indicating
the script programming language is present.

Add UNDEFINE variable/macro to undefine an item.  This is the same as the
DEFINE command with no definition text.

Add XECHO <string> to display the <string> without adding CR/LF.

Add variable \v(connection) which always returns string "local".

Add function \fbasename(filename) which returns the filename without is drive
letter and path prefix.

Corrections:

DEC User Defined Keys returned illegally, could crash program.

SET PRINTER to a file which could not be opened crashed the program.

LOCAL list of \%<char> variables failed to skip non-\%<char> items in the list.

------------------------
Beta 6, 2 September 1996:

Bug fixes:

 . END/POP statement acted too strongly and exited all macros rather
   than just the current macro.

 . Consecutive spaces in strings were collapsed to single spaces,
   such as ECHO 1 2   3   showed 1 2 3, and INPUT 10 {WORD   WORD}
   expected only a single space.

 . Declaration of arrays of size 14 eventually led to memory corruption.

 . INPUT ignored bytes read during preceeding script commands, such
   as PAUSE or OUTPUT.

-----------------------
Beta 5, 27 August 1996:

New commands:

NOPUSH
  Hidden, one-way command, prevents PUSH/RUN

SET TERMINAL ESCAPE-CHARACTER {ENABLED, DISABLED}
  Determines whether the Connect mode escape character, normally Control-],
  is an escape or is sent to the host as an ordinary character.

Added TCP keepalive probes when using a TCP passive open (Listen).  Times out
a session after about 100 seconds of no response to a series of five probes.

Fixed bugs with arrays having more than 14 elements.

-----------------------
Beta 4, 19 August 1996:

 o Correct bug of losing the first two characters of the first argument
   word in the DIAL command.
 o Add new command SET TERMINAL CR-DISPLAY {Normal, CR-LF}, default is
   normal.  The alternative adds a Line Feed after each received Carriage
   return.
 o Correct bugs in INPUT and MINPUT.
 o Adds three new commands: SWITCH, MOVE, and RETRIEVE.

   SWITCH <variable-name> {
     :label1, command, command, ... BREAK
     :label2, command, command, ... BREAK
     :label3, command, command, ... BREAK
     ...
     :DEFAULT, command, command, ...
   }

This is similar to the C-language switch statement, and identical to the
switch statement in C-Kermit 6.0 Beta.  Like both, it can be nested.  Example:

SWITCH \v(nday) {
  :0, echo Sunday, break
  :1, echo Monday, break
  :2, echo Tuesday, break
  :3, echo Wednesday, break
  :4, echo Thursday, break
  :5, echo Friday, break
  :6, echo Saturday, break
  :default, echo When did the week get more than 7 days?
}

The MOVE command is just like SEND, except that after sending the file
succesfully, MS-DOS Kermit deletes its copy.  Thus the file is actually moved
from your PC to the other computer, rather than copied.

The RETRIEVE command, to be sent by a client to a server, is just like GET
except that it tells the server to delete each file after -- and if and only
if -- it has been sent successfully.  Thus it is like MOVE, but in the other
direction.  Requires a server on the other end that understands this command.
As of yet, only MS-DOS Kermit qualifies.  The next beta edit of C-Kermit will
have this feature too (both ends, server and client).

-----------------------
Beta 3, 11 August 1996:

Correction to DHCP lease renewal procedure.

-------------------------------------------------
Second (unnumbered) test version, 11 August 1996:

Corrections to reported bugs:
 o STOP <digit> string now properly displays the string.  The DIAL command
   uses this syntax when the dialing script is not found.
 o SET PROMPT allows \numbers again.
 o INPUT <timeout> single-byte no longer hangs in an infinite loop.
 o MINPUT <timeout> {string} {another string} ... 
   now properly recognizes each string.
 o \v(minput) now properly reports the index of the string matched by MINPUT.
 o Loss of modem Carrier Detect may now be recognized promptly during file 
   transfers, but the changes are untested.  Probably more work is needed.
 o \$(DOS Environment variable) now finds both uppercase and lower case
   variables, but not mixed case variables.  Windows 3.1x creates variable
   "windir" in lower case, as can be observed within the DOS box, so this is
   a way for MS-DOS Kermit to check whether it is running under Windows 3.x.

Additional features:
 o \fchecksum(string) yields the decimal value of the 32-bit unsigned sum
   of the code values of each byte in string, e.g. \fcheck(ABCD) = 266.
 o SET TCP ADDRESS has new option, DHCP, as a synomym for BOOTP.
 o SET TCP ADDRESS DHCP or BOOTP  both try DHCP negotiation and accept
   the first response of possibly many, whether DHCP or Bootp responses.
   Special note for users of Novell's DHCPSRVR.NLM server v2.0: 
   use  SET TCP BROADCAST 255.255.255.255  to avoid a bug in that server
   which is triggered by using a directed broadcast address.

Question on a requested enhancement:
   TCP/IP SOCKS support requires a choice of authentication mechanism.
   People asking for SOCKS support need to tell us which mechanism they 
   require since one needs to be written into the code. The two choices are
   no authentication and plaintext username/password, neither of which
   provides any security, and the latter is a big security hole.

--------------------------------
First (unnumbered) test version, 18 July 1996:

ERROR CORRECTIONS

1. All patches issued for MS-DOS Kermit version 3.14 are incorporated into
   version 3.15

2. Unpatchable problem with ARP affecting some remote hosts is fixed in
   version 3.15

3. Unpatchable bug which prevented communications between LAN adapters from
   the same vendor (the first three octets of the hardware address were the
   same), fixed in version 3.15

4. Correction of a fatal bug when using internal TCP/IP over ARCnet ODI
   drivers.

5. Failure to act upon 8-bit control codes SS2 and SS3 in VT220/320 terminal
   emulation, even though their 7-bit equivalents were implemented.

FILE TRANSFER IMPROVEMENTS

Kermit file transfer protocol and TCP/IP internal protocol stack:

1. Dynamic Kermit packet retry timing, based on measured round trip times.
   This should provide faster recovery from lost packets.

2. Congestion avoidance strategy during packet transmission.  Both (1) and
   (2) are directly from TCP/IP rules and procedures by Van Jacobson.  This
   should improve performance on busy comms lines of all kinds.

3. Improved timing of IP packets within the internal TCP/IP stack, to deal
   with today's steadily deteriorating Internet performance.

4. Improvement of TCP keepalive probe detection techniques, to keep Telnet
   connections alive forever even if no user activity occurs.

5. Optional announcement in Kermit packets of the kind of operating system
   so that two alike systems would exchange files in BINARY mode
   automatically, and without filename conversion.  The new command:

     SET TRANSFER MODE { AUTOMATIC, MANUAL }

   controls this feature, with the default being MANUAL for no announcement.
   If the "sysid" mode is used it overrides user choice of binary or text
   mode file transfers when like systems converse.  Works with C-Kermit
   16.0.192 (in Beta), Kermit 95 1.1.5 or later, IBM Mainframe Kermit 4.3.2
   (soon to be announced), and of course MS-DOS Kermit 3.15 itself.

6. Automatic recognition of Kermit packets while in terminal emulation
   mode.  See next section.

TERMINAL EMULATION IMPROVEMENTS

1. Kermit can now use extended memory (raw memory above 1MB) in place of
   expanded memory for screen rollback space. The command below has been
   enhanced to include choices EXTENDED and EXPANDED.

     SET TERMINAL EXPANDED-MEMORY { OFF, EXPANDED, EXTENDED, ON }

   The default is ON, which means try expanded memory first, and if that
   fails then try extended.  With Extended in use Kermit does not need an
   expanded memory page frame (located in UMB memory).  The default ON
   results in operation the same as for version 3.14 of MS-DOS Kermit.

2. Automatic recognition of incoming Kermit packets while in terminal
   emulation mode.  The new command:

     SET TERMINAL AUTODOWNLOAD { ON, OFF } 

   controls this feature, with the default being ON.  When the remote host
   sends a Kermit "I" or "S" packet to initiate a file transfer in either
   direction (via a SEND or GET command) then MS-DOS Kermit switches to file
   transfer mode, performs the file transfer, then returns to CONNECT mode.
 
   To download a file, just tell the remote Kermit to send it, e.g. (for
   C-Kermit on the remote end):

     kermit -s <filespec>          ; To download in text mode
     kermit -is <filespec>         ; To download in binary mode

   or (at the Kermit prompt):

     C-Kermit> set file type text  ; (or "binary")
     C-Kermit> send <filespec>

   To upload a file, tell the remote Kermit to GET it, e.g.:

     kermit -g <pc-filespec>       ; To upload in text mode 
     kermit -ig <pc-filespec>      ; To upload in binary mode 

   or:

     C-Kermit> set file type text  ; (or "binary")
     C-Kermit> get <pc-filespec>

3. The Compose Key (verb \Kcompose, assigned by default to Alt-c) now
   works not only for Latin-1 (Western European) character sets, but also
   Latin-1 (Eastern European) character sets.  Latin-2 compose sequences
   are accepted when your local code page is CP852 and your terminal
   character-set is Latin-2; otherwise, Latin-1 sequences are used, as
   before.  See Appendix I.

SCRIPT PROGRAMMING IMPROVEMENTS

1. New command functions, \fname(arguments):

   \frindex(pattern,string,position)
     Right Index.  Returns 1-based position of first occurrence of pattern in
     string, looking from right to left, starting "position" bytes from from
     the right (default position is 0).  Returns 0 if pattern not found.

   \feval(math expression)
     Returns numerical result of a math expression.
     Numbers are 32-bit signed integers in calculations.
     Math operators are:

       +, -, *, /  Add, subtract, multiply, divide
       + and - are also unary operators

       %  modulo, remainder
       ^  exponent, to power of 
       !  factorial
       ~  logical bit-wise NOT, one's complement
       &  bit-wise AND 
       |  bit-wise OR
       #  bit-wise Exclusive-OR 
       @  Greatest Common Divisor 
      ( ) Clustering symbols, to 8 deep.

   \fipaddr(string)
     Returns IP address in dotted decimal form found within string.  Can
     be used with \v(input) to obtain IP address during SLIP login.

   \ftod2secs(hh:mm:ss)
     Converts hours:minutes:seconds to seconds.

   \fverify(pattern, string, offset)
     Checks that all characters in string are in pattern, starting search at
     offset of string.  Returns 0 if all match, else 1-based position of first
     mismatch in string.

   Function names may be abbreviated to uniqueness, such as \fmin().

2. Mathmatical expressions, such as (1992+3*3-5), can be used almost
   everywhere to represent a single numercial value.  The rules of what 
   is an expression are the same as for \feval() and follow common usage.
   If spaces occur then use ( ) around the entire expression.

   Numbers can be expressed as implicit decimal, 1996, or have a base
   associated with them such as \x1b for hexadecimal (27 dec).  Numbers 
   may be signed and results are retained to 32-bits.

   Single byte numerical values, \x1b, are permitted in text strings and
   represent one byte.  To use backslash as itself double it, \\.  Note 
   that a number may terminate from its value filling a byte.  For example:

     ECHO testing \12345   

   produces:

     testing {45  

   because \123 makes a full byte (visually a left curly brace).

3. To assist the CD, DIR, and RUN commands single byte \number conversion no
   longer occurs.  Thus one may now safely say CD \4DOS.

4. Command word spelling may be composed on the fly from substitution
   variables, such as 

	define \%a minal
	set ter\%a type vt320

   This concept is extended to spelling of \function names, labels,
   and even the names of substitution variables themselves.

5. Substitution variables now support the notion of arrays of strings:

   DECLARE \&<char>[size]
     Allocates space for "size" number of strings. If size is 0 then the
     structure becomes undefined.

   \&<char>[index]
     Is member index of the array <char>.  Use DEFINE or ASSIGN to create the
     array member.  Index starts at 1 and should not exceed the declared
     "size."  Strings are limited in length to 1KB which is the limit of a
     Kermit command. Not all members need be created, only the ones you
     wish. An empty definition removes that member.

6. Multiple match patterns for script INPUT statements, via new command

   	MINPUT <optional timeout> pattern1 patttern2 pattern3...

   This behaves the same as INPUT except each of the patterns is examined
   and the first match terminates the command.  Patterns containing spaces
   should be placed within curly braces, e.g. {three word pattern}.  The
   pattern which is matched is revealed in new variable \v(minput): 1
   if the first one was matched, two if the second, and so on, or 0 if
   none were matched.

     NOTE: For compatibility with C-Kermit, the optional timeout in the
     MINPUT, INPUT, and REINPUT commands, should always be included.

7. New variables:

   \v(instatus)
     Status of most recent INPUT or MINPUT command:
      -1 for not initialized yet
       0 for success
       1 for timed out
       2 for user level Control-C interrupt
       4 for connection lost

   \v(minput)
     Shows which search pattern was matched by the MINPUT command, which
     is a script INPUT command with one or more match patterns.  The 
     variable is 0 if no match was obtained.

    \v(return)
     The text string given by a "RETURN string" command. See RETURN below.

    \v(input)
     This is the contents of the INPUT command buffer, but with two changes
     from version 3.14.  Now \v(input) is the entire buffer rather than up to
     the first Carriage Return, and control codes are retained intact (and
     thus are invisble). To see the control codes visually use command
     SHOW SCRIPT where controls are displayed in "caret-character" notation
     such that null is ^@, 1 is ^A, 2 is ^B and so on.

8. Program control functions FOR, WHILE, XIF, ELSE.  They are:

     FOR <variable-name> <start> <end> <increment> { <command>, ... }

     WHILE <logical-test> { <command>, ... }

     XIF <logical-test> { <command>, ... } ELSE { <command>, ... }

     IF <logical-test> <command>
     ELSE <command>

   where:

   <variable-name> 
     Is a substitution variable, \%<character>, which holds the loop index;
     <start>, <end>, and <increment> are numbers, and yes, loops can run
     backward by using negative increments.

   <command>
     Is any MS-DOS Kermit command.

   { <command>, ... }
     Is curly braces surrounding one or more Kermit commands, with commands
     separated by commas to represent end of line, or multiple lines of Kermit
     commands where the physical end of line acts automatically as a command
     terminator.  A side effect of this is commands using { will be continued
     automatically by the next line until a closing } is encountered; each
     input line will have a comma prepended.

   <logical-test> is any of the IF statement tests.

   XIF may have the ELSE word in the middle of a command line, but ELSE must
   not be a separate command line. Only the IF statement uses ELSE as a
   separate command line (see below).

   The IF statement has been extended to allow an optional second line of ELSE
   Kermit command.  ELSE must be at the start of the next line rather than on
   the same line as the IF main body.

   BREAK terminates a FOR or WHILE loop. Control resumes at the next outer
   statement, if any.

   CONTINUE continues FOR and WHILE statements the at the bottom, skipping
   statements between itself and the bottom of the loop.

   These statements may be nested.

9. RETURN string

    Used by macros to return "string" to new variable \v(return) and then
    terminate the macro. Termination is otherwise the same as by POP or END.

10. SETENV name=string

    Puts NAME=string into the DOS master environment.
    Example script sequence:
	input 10 Your IP number today is
	input 10 Please record it now.
	setenv myip=\fipaddr(\v(input))

    where the remote machine sends "Your IP number today is 123.111.222.123.
    Please record it now." The DOS master enviroment would have the new
    line "MYIP=123.111.222.123" at the end.

    Note that changing the master environment does not affect the copy
    existing within Kermit nor any processes launched while in Kermit.

11. Local variables

In macros, you can declare any \%x (x = any letter) variable to be local to
the macro.  Syntax:

  LOCAL <variable-name> [ <variable-name> [ ... ] ]

APPENDIX I: LATIN-2 COMPOSE SEQUENCES

Accented Letters.
Enter in the desired case (upper or lower).
Key 1 (K1) and Key 2 (K2) can be entered in either order.

Character Name          K1   K2

A acute                 A    '
A breve                 A    %
A circumflex            A    ^
A diaeresis             A    "
A ogonek                A    =
C acute                 C    '
C caron                 C    &
C cedilla               C    ,
D caron                 D    &
D stroke                D    -
E acute                 E    '
E caron                 E    &
E diaeresis             E    "
E ogonek                E    =
I acute                 I    '
I circumflex            I    ^
L acute                 L    '
L caron                 L    &
L with stroke           L    /
N acute                 N    '
N caron                 N    &
O acute                 O    '
O circumflex            O    ^
O diaeresis             O    "
O double acute          O    #
R acute                 R    '
R caron                 R    &
S acute                 S    '
S caron                 S    &
S cedilla               S    ,
T caron                 T    &
T cedilla               T    ,
U acute                 U    '
U diaeresis             U    "
U double acute          U    #
U ring                  U    *
Y acute                 Y    '
Z acute                 Z    '
Z caron                 Z    &
Z dot above             Z    .

ss (German sharp s)     s    s  (lowercase only)

Accents and special characters; enter K1 and K2 in the order shown:

Character Name          K1   K2

Acute accent            '    '   (two apostrophes)
Breve                   %    %   (two percent signs)
Caron                   &    &   (two ampersands)
Cedilla                 ,    ,   (two commas)
Currency sign           X    0   (or X O, or x 0, or x o)
Degree sign             0    ^   (zero and circumflex)
Diaeresis               :    :   (two colons)
Division sign           -    :   (hyphen and colon)
Dot above               .    .   (two periods)
Double acute            #    #   (two number or pound signs)
Multiplication sign     X    X   (or x x)
Ogonek                  =    =   (two equal signs)
Paragraph sign          S    !   (or S 0 or S O, upper or lower case)
Soft hyphen             -    -   (two hyphens)

APPENDIX II: MS-DOS KERMIT AND PPP

Here is a brief description of how to set up and use MERIT's PPP driver
PPP.EXE (available in the Crynwr Collection of Packet Drivers).  The
documentation available for PPP.EXE is not very clear, hence this note.

  NOTE: We have not tested every variety and version of DOS PPP software.
  The version discussed here is University of Michigan Merit Network PPP
  1.9.49 Beta, which seems to work satisfactorily, and which can be obtained
  with anonymous from kermit.columbia.edu, directory packet-drivers/ppp.
  Other versions might be available from the master site:

    ftp://merit.edu/pub/ppp/pc/etherppp.zip

  We do not necessarily recommend any version besides the 1.9.49 one, which
  has been tested successfully.

Note that the term "EtherPPP" is often used to refer to the Merit PPP driver,
because that is the name of ZIP file in which is it is packaged.

First, install PPP on your PC.

Step 1: Download the SLIP files IN BINARY MODE to your PC's KERMIT
        directory (wherever you keep MS-DOS Kermit).

Step 2: In AUTOEXEC.BAT or elsewhere add a line like the following, which
        specifies the path of the Merit PPP configuration file, CONFIG.PPP.

          SET CONFIG.PPP=C:\PPP

Step 3: Edit the sample CONFIG.PPP file, which looks like this:

	  ppp trace 0
	  ppp pap user myusername mypassword
	  ppp pap timeout 20
	  ppp quick
	  ppp lcp open

        Replace "myusername" and "mypassword" with your own PPP username and
        password.

Step 4: Create a STARTPPP.BAT file in your KERMIT directory.

STARTPPP.BAT starts PPP.EXE and it contains one line that looks like this:

ppp /c 1 /s 57600 /d none /k 6 /v 1

When we run it MERIT's PPP driver starts up on the existing telphone
connection.  The parameters are as follows; replace them by parameters that
are appropriate to your setup:

  /d none
     No dialing by the driver; use the connection that's already there.

  /k 6
     Present a SLIP interface to the TCP/IP stack (rather than an Ethernet
     interface).  NOTE: "/k 6" is important.  The driver must be configured
     as a SLIP driver, not an Ethernet driver, or else the TCP/IP stack will
     falsely believe that it should be doing broadcasts such as ARP.

  /v 1       
     Be verbose (so you can see error messages)

  /c 1
     Use COM1.  Replace this by "/c 2" if you are using COM2, etc.

  /s 57600
     Set the speed of the given COM port to 57600 bps.  Replace this by
     the highest speed that can be used with your modem.

Once PPP is installed, you won't need to repeat the steps above.

Now to make a PPP connection, there are three major steps:

 1. Use Kermit to dial up your Internet Service Provider (ISP).
 2. Start PPP on the connection from Step 1.
 3. Have Kermit make TCP/IP connections over the PPP connection from Step 2.

Begin by using MS-DOS Kermit ot dial up the terminal server at your Internet
Service Provider and tell it who you are and what protocol you wish to use
over the line.  A Kermit script works well for this, but the example below is
typed by hand (MS-Kermit> is Kermit's prompt, you don't type it):

  MS-Kermit> set port 1
  MS-Kermit> set speed 57600
  MS-Kermit> set flow rts/cts
  MS-Kermit> connect

If you are using port 2 or other port, then specify that instead of port 1.
You can use other speeds too, but obviously the higher the better -- use the
highest one that works with your modem.  Use the same port and speed as you
have specified in STARTPPP.BAT.

Now make the phone call.  In this example we type "ATDT" followed by the phone
number, and then press the Enter key (of course there are also other ways to
make Kermit dial the phone, but all that is covered elsewhere):

  atdt73456

A few seconds later you should get back a message from the modem:

  CONNECT 57600/LAPM

If instead it says BUSY or NO CARRIER, etc, then try again later.

Now you should see a message from your ISP.  If you don't see anything, try
pressing the Enter key one or more times.  Here is an example showing the
dialog at Utah State University:

  Welcome to the USU modem pools.

  Enter: vms, library, telnet, or your PPP (or SLIP) username.
  nb1 login: jrd-ppp
  Password: xxxxxxx

  Enabled IPCP address negotiation for jrd-ppp-ppp
  Added interface jrd-ppp-ppp for IPX
  Packet mode enabled
  ~}#A!}!} } }8}!}$}%}"}&} } } } }%}&}$U}$}'}"}(}"3¢~

NOTE: Other service providers will have different dialogs.  Some services
are "PPP-only" and you will not get any kind of recognizable greeting or
prompt -- instead you will get either garbage (similar to the last line in
the example above), or nothing at all -- just a blank screen.  In that case,
there is no way to log in "by hand"; instead the user ID and password will
be sent by PPP.EXE itself (after you start it), from your CONFIG.PPP file.

Now return to the MS-Kermit> prompt by pressing ALT-x, and EXIT from
MS-DOS Kermit.

Now that the PPP connection is running on the remote side we need to perform
step two: start PPP on our client machine and tell Kermit the current IP
address.  After the driver finishes negotiating with the remote side it
displays the current IP number for us; we write it down and then tell Kermit
to use it.

Step 1: Start Kermit again.

Step 2: At the MS-Kermit> prompt, type "run startppp.bat" (and press Enter).
        You should see something like this:

  C>ppp /c 1 /s 57600 /d none /k 6 /v 1
  PPP: version 1.9.49 beta
  PPP command line parameters:
	  --class=6 --int=0x60
	  --com=1 --irq=4 --base=0x3F8
	  --speed=57600 --hard=0 --fifo=1 --quit=0
	  --dial='none'
  16650A detected

  IP address set to 129.123.246.5

Step 3: Now you see what your IP address is.  Tell Kermit what it is:

  MS-Kermit> set tcp add 129.123.246.5

Step 4: Now you can make a Telnet connection to any host on the Internet:

  MS-Kermit> set port tcp xyzcorp.com
  MS-Kermit> connect

When the session has completed the phone line might be disconnected by the
remote end.  If it isn't then you can make another Telnet connection, or you
can just exit from Kermit but in this case you should use the Packet Driver
support program TERMIN to terminate the connection.  After Kermit puts you
back at the DOS prompt, just type:

  termin 0x60

APPENDIX III: MEMORY MANAGEMENT

  (*** Reconcile this with section 19 of KERMIT.BWR ***)

MS-DOS Kermit can use large amounts of memory to store the terminal emulator
screen rollback buffer, Telnet session controls, and graphics mode screens.
Where these items are stored is up to you and thus you need to be aware of the
selection process.  There are three choices:

 1. Conventional memory (lower 640K).  Advantages: easy, no extra work
    needed, can work everywhere.  Disadvantages: Conventional memory is
    limited and precious; the amount of rollback screens is limited by
    available conventional memory; ability to run DOS commands or programs
    under Kermit is limited, etc.

 2. Expanded memory (EMS).  Any or all memory you might have installed
    beyond 1MB, accessed through a 64KB chunk (Upper Memory Blocks, UMB) in
    Conventional memory.  This is the fastest "extra-memory" option, but
    requires Requires a memory manager and configuration thereof by the
    user, which can be confusing and risky.  dedicating 64KB of conventional
    memory.

 3. Extended memory (XMS).  Any or all memory you might have installed
    beyond 1MB, accessed "directly".  Slower than EMS but does not require
    the 64K UMB in Conventional Memory.

OVERVIEW

If the computer is running just DOS (by itself) and has no memory management
facility loaded, then Kermit stores its large buffers in conventional memory
Today almost all PCs use some form of memory management software, including
that provided by Microsoft Windows 3.1, 95 and NT.  EMM386.EXE is a familiar
manager from Microsoft; QEMM/386 is one from Quarterdeck.  With a memory
manager Kermit can use memory above 1MB to hold these buffers.
Memory above 1MB is commonly either extended or expanded memory.

EXTENDED MEMORY

Extended is provided by memory managers but can be slower to access than
expanded memory (which can be deselected by the user).

EXPANDED MEMORY

Expanded memory is in two pieces, one large piece above 1MB and a 64KB piece
in Upper Memory Blocks (UMB, between 640KB and 1MB).  Expanded memory needs
to be controlled by the user.  For example, EMM386.EXE provides expanded
memory unless the phrase NOEMS is used on its command line.  Windows
provides both automatically.  QEMM provides expanded memory upon request
when configuring the machine; its "stealth" mode requires it.  Expanded
memory provides faster access than extended memory, but it costs that 64KB
area in UMB.

Placement of the expanded memory 64KB working area can be left to the memory
manager or more wisely it can be located by the user in a safe UMB location.
Please see the instructions of your memory manager about details of placement,
but the common control is phrase FRAME=d000 or similar keyword.  Do not
located it below C000 (video space) nor on an existing BIOS nor on shared
memory clients (often network adapters).  In the end configuring memory is a
responsiblity of the user.

MEMORY MANAGEMENT IN WINDOWS

(this needs to be filled in -- presumably users do not -- and most should
not -- mess with memory configuation in Windows, esp Win95 and NT -- and so
which kind of ex****ed memory do they get and what should they tell Kermit?)

MEMORY MANAGEMENT AND MS-DOS KERMIT

Kermit's choices of memory are decided by finding if a memory manager is
active.  If there is none then conventional memory is used.  With a memory
manager MS-DOS Kermit relies upon command SET TERMINAL EXPANDED-MEMORY
<setting> to make a selection.  We may review the choice by giving command
SHOW TERMINAL and viewing the setting of the EXPANDED-MEMORY line.

The SET TERMINAL EXPANDED-MEMORY command has four choices: OFF, EXPANDED,
EXTENDED, ON.  These correspond to use conventional memory, use expanded, use
extended, or ON to try first expanded and if not successful then use extended
memory.  The default is OFF, and a better choice for many people today is ON.
The choice may be changed at any time but existing buffers will be lost by the
change.

Please be aware that locating the largest buffer, the screen rollback area, in
conventional memory very quickly exhausts that memory.  Each screen consumes
about 4KB, so saving say 100 screens uses 400KB and that's not enough to let
Kermit use command.com for some commands.  The default number of saved screens
is 10, and the number can be changed by DOS Environment command SET
KERMIT=ROLL number-of-screens.

Our recommendation is use a memory manager and enable expanded or extended
memory usage by Kermit, by adding line

  SET TERMINAL EXPANDED-MEMORY ON

to your MSCUSTOM.INI file.

(End)