/* C:\DOC\PKTMUX.DOC **** 12 NOV 92 ** 12:36 ******; G W Robinson


                   R A L   I B M   P C   U S E R   G U I D E
                   -----------------------------------------

                       PKTMUX Packet Driver Multiplexor
                       --------------------------------

      Contents
      ========

      1.    Introduction and Disclaimer

      2.    Installation

      3.    Overview

      4.    Usage Guidelines

      5.    Program Description
      5.1     PKTMUX.EXE
      5.2     PKTDRV.EXE
      5.3     PKTSTATS.EXE
      5.4     WINPKT.COM

      6.    Examples
      6.1     Packet Driver, PCTCP and PC-NFS Applications under DOS
      6.2     MOS2 under DOS
      6.3     Packet Driver and IEEE 802.3 (ISO 8802/3) applications
      6.4     Packet Driver and Rainbow Applications
      6.5     Packet Driver Applications under Windows 3
      6.6     Packet Driver, PCTCP and PC-NFS Applications under Windows
      6 7     Windows 3 Applications
      6.8     Novell Netware
      6.9     Packet Driver/PKTMUX/PKTDRV BAT files

      7.    Technical Description
      7.1     Basic Methodology
      7.2     Buffer Strategy
      7.3     Channel Management
      7.4     Control Programs
      7.5     Listeners and /l Options
      7.6     Port Duplication
      7.7     IP Fragmentation
      7.8     Other IP Protocols
      7.9     IEEE802.3 (ISO 8802/3) Protocol Support
      7.10    Use of Packet Driver Internal Buffer
      7.11    Novell Protocol Support
      7.12    Packet Driver Protocol Filtering

      8.    Problem Solving

      9.    Bugs/Features and Problem Programs

      10.   Differences in PKTMUX versions

      11.   Support

      12.   References




      1. Introduction and Disclaimer
      ==============================

      The author and his employers accept no responsibilty for any damage
      done by this software.  It is run strictly at the user's risk and
      all necessary precautions, such as backing up of discs, should be
      taken before hand.

      Similarily the vendors/authors of applications and Packet Drivers
      accept no responsibility for problems and malfunctions, and will
      give no support, when their software is used with PKTMUX.

      This document describes PKTMUX which is a program that provides a
      multiplexing interface to a Packet Driver. It thus allows several
      IP protocol stacks to be run in parallel either under DOS or a
      control program such as Windows 3 or DESQview.

      Multiplexing IP protocol stacks is a non trivial problem and this
      program is only likely to meet about 90% of user requirements.
      There will always be 10% who need a more sophisticated product.
      Because PKTMUX makes certain probability assumptions it is also
      highly likely that it will make a mistake every now and then when
      they are not valid.  At best an application will recover from this
      situation and at worse something, possibly even the whole PC, will
      fail.  It is therefore likely that PKTMUX will never be 100%
      reliable and in some situations it may be so flakey as to be
      unusable.

      This documents version 1.2a and differences from previous versions
      are detailed in Section 10.  The programs from this version must
      not be mixed with those from previous versions as they are
      incompatible.  Many thanks to those around the world who have
      reported problems and helped with their solution.


      2. Installation
      ===============

      The system comes as a single program named PKTMUXxx.EXE where xx is
      the version number, currently 12.  When this program is run it
      expands into several files.  These are:

        PKTMUX.EXE      The packet multiplexor
        PKTDRV.EXE      The pseudo Packet Driver interface to PKTMUX
        PKTSTATS.EXE    A program state and statistics display program
        PKTMUX.DOC      This documentation

      In addition a free program WINPKT.COM and a source listing
      WINPKT.ASM is supplied since this provides some of PKTMUX's
      functionality and is rather smaller.

      The programs should be copied into a directory in the Path such as
      C:\BIN on RAL machines.  PKTMUX.DOC should be put in a
      documentation directory such as C:\DOC on RAL machines.  The BAT
      file INSTALL.BAT does this.




      3. Overview
      ===========

      The Packet Driver interface was developed by FTP Software Inc as a
      standardised way of accessing different makes of communications
      cards.  It is widely used especially over ethernets and a large
      amount of communications software is available for it.  The
      ethernet implementation makes use of the fact that two bytes in the
      header define the packet type and this is used to provide a
      multiplexing mechanism between several packet types.  However it
      looks no further into the protocol stack and thus this feature is
      of limited use when protocols of the same type, such as those from
      the TCP/IP family, are used.

      PKTMUX attempts to remove this limitation by providing a
      multiplexing facility for Internet Protocols (IP).  This is done by
      not only switching on the packet type (which denotes IP) but also
      the IP protocol type (which can denote IP protocols TCP, UDP, ICMP
      and others).  In the case of TCP and UDP it can also switch on the
      Port number being used.  It is therefore possible to run more than
      one IP protocol stack at the same time.  It is not possible to
      multiplex other protocol stacks or more than one of each IP
      protocol type other than TCP, UDP or ICMP.  One protocol stack can
      be IEEE 802.3 (ISO 8802/3) protocol.

      PKTMUX was originally written to meet the needs of the RAL MOS2
      system which is a TSR (Terminate and Stay Resident) program that
      provides IBM 3270 emulation over asynchronous and ethernet
      communications.  In this context it provides two functions for the
      TCP/IP version of MOS2.  On is that it allows additional
      communications applications to run alongside MOS2.  This is useful
      because, since MOS2 is a TSR, you can hot key back to DOS and run
      other commands.  Thus an LPR or FTP can be run alongside the MOS2
      3270 session.

      A second requirement was to allow MOS2 to run under a control
      program such as Windows 3 or DESQview.  This is an instance of a
      more general problem in running an application which uses a Packet
      Driver under a control program.  It arises because the Packet
      Driver, which is loaded before Windows, calls the application when
      it has received a packet.  This is quite satisfactory under DOS but
      under Windows there is no certainty that the application is
      currently running and there is therefore the risk of jumping into
      the middle of another program with dire consequences.  A Packet
      Driver option -w gets over this by checking that part of the
      application program code is present and throwing away the packet if
      not.  This leads to a rather slow data rate as the protocol timeout
      and retry mechanisms have to be brought into play to recover from
      the situation.  A better solution is provided by the free software
      WINPKT which only works under Windows 3 Enhanced mode and uses
      Windows 3 facilities to make sure the application is running.  A
      copy of WINPKT is provided in this package.  WINPKT has the
      drawback that it does not work with other control programs such as
      DESQview and also with certain ethernet cards such as the BICC 16
      bit varient.  PKTMUX meets this requirement and gives the
      additional feature of being able to run communications applications
      in more than one window.




      Given the widespread use of Packet Driver it is surprising that
      nobody has written a PKTMUX before.  It is probably because a
      general purpose multiplexor is impossible to implement.  PKTMUX
      only attempts to meet the needs of IP protocols and is therefore
      likely to be of little use in other situations.  It must however be
      emphasised that PKTMUX will only work when the probability of
      various identifying values being duplicated is low and that when
      duplication does occur then the various retry mechanisms can
      recover from the mess.  If this is not the case the PKTMUX is of
      little use.

      PKTMUX has so far been tested satisfactorily with PCTCP, PC-NFS,
      NCSA, CUTCP, B&W TCP, Waterloo TCP and Novell Netware.  It has also
      been tested with shims that interface onto a Packet Driver such as
      PDETHER for ODI and RAL LLCPKT for BICC MPS.  It also runs on top
      of the RAL LLCPK2 program that provides a Packet Driver and BICC
      MPS interface.

      Further technical details are given in the Program and
      Technical Description sections.




      4. Usage Guidelines
      ===================

      The following give basic usage guidelines.  For more detail consult
      the Program Descriptions and Examples sections. All programs except
      WINPKT give help when run with the /h option.

      The normal procedure for running a communications application is to
      load a Packet Driver and then run the application. To introduce
      multiplexing into this PKTMUX and PKTDRV must be loaded after the
      Packet Driver and before the application.

      Thus under DOS type the following after you have loaded the Packet
      Driver:

        PKTMUX n                ; n is the maximum number of packet
                                ; driver channels to support - default 2
        PKTDRV                  ; repeated n times - displays Interrupt
                                ; used

      Then run the applications as required.  Note the first ones must
      usually be TSRs otherwise you cannot get back to DOS to load
      subsequent applications.  Applications which search for a Packet
      Driver will find the first free PKTDRV.  Once an application
      starts using PKTDRV it becomes busy and is no longer recognised as
      a Packet Driver.  Note that this only happens once the application
      has started communicating over the network so each application
      must be got to this state before further applications are loaded.
      If not then two applications will link into the same PKTDRV and
      fail. Applications for which you have to specify the Packet Driver
      Interrupt should be set for the highest PKTDRV Interrupt to avoid
      conflicts.

      For usage under a control program such as Windows 3 run PKTMUX as
      above but dont run PKTDRV until after the control program is
      active.  Then run one copy of PKTDRV in any DOS session from which
      you wish to use a communications application that runs over a
      Packet Driver. All sessions must continue to run when in the
      Background and for Windows 3 the Background Priority should be
      at least 50 and it must be in Enhanced mode.

      For applications that run directly under Windows 3 (eg WINQVT)
      either use WINPKT or, if further packet driver channels are
      required, then run PKTMUX as above and then one PKTDRV before
      Windows 3 is loaded.  Then start up the Windows application which
      will use this PKTDRV.  Further applications running in DOS sessions
      must have their PKTDRV loaded in their DOS session before they are
      run.

      The program PKTSTATS gives details of program states and various
      statistics.




      5. Program Descriptions
      =======================


      5.1 PKTMUX.EXE
      --------------

      This is a TSR that provides, in conjunction with PKTDRV, multiple
      IP protocol channels to a Packet Driver. Its format is:

        PKTMUX  chan_cnt pkt_drv_int chan_time_out /options

      which installs the multiplexor on the first packet driver it finds
      or hex interrupt "pkt_drv_int" is this is specified (note 1).
      "Chan_cnt" channels are supported - default is 2 (note 2).
      "chan_time_out" is the time in seconds a timed out channel waits
      before being reset (note 6).  Any failure during loading will cause
      PKTMUX to abort and set the DOS ERRORLEVEL to 1.  PKTMUX memory
      usage ranges from 15K for one channel to 34K for eight channels.

      The following options modify the action taken:

        a  display additional information on loading.
        b  look for and use buffer in Packet Driver (note 12).
        d  drop packets if application has no buffers (note 5).
        o  override use of specified interrupt (note 1).
        h  display this help information.
        i  support one IEEE 802.3 channel (note 9).
        p  pause if error found (note 13).
        q  query state of a PKTMUX (note 11).
        r  reset timed out channels; rr resets internal flags as well and
           should be used with care (note 6).
        s  silence output except warnings (unless /ss) or errors
           (unless /sss) (note 10).
        t  terminate PKTMUX and Packet Driver (note 3).
        u  unload PKTMUX if not being used by a PKTDRV (note 3).
        v  set DOS Environment variable PKT_INT to interrupt used or
           found (notes 1 & 11).
        x  multiplex all received packets - testing only (note 7).
        1 to 9  allocate buffers for this channel count (note 4).

      Examples are:

        pktmux               ; normal use - 2 channels
        pktmux 4             ; install to multiplex four applications
        pktmux 2 62          ; install on Packet Driver at Int 62
        pktmux 4 /b          ; try using Packet Driver buffer
        pktmux 4 /bi         ; support IEEE 802.3 and also try and use
                             ; Packet Driver buffer
        pktmux /u            ; unload PKTMUX (dont forget to unload
                             ; PKTDRVs first)
        pktmux 8 /4          ; install to multiplex eight applications
                             ; but only allocate enough buffers for four
        pktmux /r            ; reset timed out channels




      Notes:

      1.  By default PKTMUX searches for a Packet Driver and, on finding
      one, takes over its interrupt effectively hiding it so it cannot be
      found by any other application.  There is then no confusion between
      the real Packet Driver and the pseudo ones provided by PKTDRV.  If
      the /v option is given then the interrupt used is recorded in the
      Environment variable PKT_INT.  Note that PKTMUX will refuse to load
      if during its search for a Packet Driver either another PKTMUX or a
      PKTDRV is found or if one of these is the specified pkt_drv_int.
      This latter restriction can be overcome by the /o (override)
      option.

      2.  By default PKTMUX supports two Packet Driver channels.  This
      means it will communicate with up to two copies of PKTDRV and
      provide two pseudo Packet Driver interfaces.  Each PKTDRV acts,
      within limits, as if it were a Packet Driver with its own ethernet
      card albiet with the same MAC address as any others.  PKTMUX
      supports up to eight busy copies of PKTDRV.  Note that supporting
      only one channel achieves the same effect as a normal Packet Driver
      and is only useful where PKTMUX provides additional functionality
      such as allowing an application to run under Windows 3.

      3.  The /u option causes PKTMUX to unload unless a PKTDRV is still
      busy.  The /t option does the same thing but also sends a terminate
      request to the Packet Driver, which will also unload if it supports
      this facility.

      4.  By default PKTMUX allocates a basic set of buffers and then
      adds an additional one to each size group for each channel.  Tests
      suggest this is adequate for most cases.  However this can be
      overridden by giving /n where n is a decimal number in the range 0
      to 9.  PKTMUX will then allocate buffers as if this number of
      channels were to be used.  This can be used to either save memory
      by reducing the buffer allocation or increasing the number of
      buffers when experience suggests it is needed.  The memory overhead
      per channel is a little over 2K.

      The buffer allocation is shown by PKTMUX when it is loaded and in
      detail by running PKTSTATS /a after PKTMUX has been loaded.

      5. PKTMUX does its best to avoid losing data by holding packets in
      its buffers when an application is unable to accept them. In some
      cases this can cause a shortage of buffers. The /d (drop) option
      causes PKTMUX to behave exactly as a Packet Driver and to drop any
      packet that is refused by an application because it has
      insufficient buffer space. This option acts on all channels and
      overrides a similar option on PKTDRV which works on a per channel
      basis.




      6.  When running under Windows 3 or DESQview with a PKTDRV and the
      application in a DOS session then, if the session is terminated
      without closing down the application, PKTMUX is left with the
      channel marked as Busy.  It will either be freed after
      "Chan_time_out" seconds (default infinity) or the option /r (reset)
      can be used on a call to PKTMUX to reset all such channels.  If /rr
      is given then the busy flags in PKTMUX are also reset which could
      cause it to fail.  See also the PKTDRV /r option and the section on
      Channel Management in the Technical Description below for further
      details.

      7.  By default PKTMUX sends data direct to the application when
      only one channel is in use.  If the /x option is given then packets
      are copied to a buffer and multiplexed by the normal mechanisms as
      if several channels were operational.  This is therefore a test
      facility to check if PKTMUX is able to support an application
      irrespective of any other application that is running. Note that
      if /x is used with Novell and Windows 3 it can crash Windows.

      8.  PKTMUX only supports Accesses for Packet Driver Class 1
      (DEC/Intel/Xerox "Bluebook" Ethernet).  It will not refuse other
      Classes but the result is undefined and a failure is likely if
      the same Class is used over more than one channel.

      9.  If the /i option is given then PKTMUX opens the Packet Driver
      for all types and does its own filtering on the Type field in order
      to decide to which handle a packet is destined.  This is order to
      allow one channel to Access as Packet Driver Class 1 and to accept
      IEEE 802.3 type packets where the Type field is the data length and
      is a value of 1500 bytes or less.  This dramatically reduces the
      efficiency of PKTMUX so should only be used when IEEE 802.3 packets
      are to be used.  Unfortunately the overhead remains irrespective of
      whether such packets are being used but this can be mitigated by
      the /b option.

      Note this is a new facility to evaluate feasibility and may not be
      very satisfactory. In particular if used with Novell and Windows 3
      it can crash Windows.

      10.  If the /s option is given then PKTMUX does not give out any
      messages unless an error or warning occurs. The option /ss prevents
      any warning messages as well and /sss prevents errors as well.

      11. The /q option causes PKTMUX to return the state of
      "pkt_drvr_int" in both text form and also via the ERRORLEVEL as
      follows:

                0    No PKTMUX found
                1    PKTMUX found

      If the "pkt_drvr_int" is not specified then a search is made from
      Interrupts 60 to 7F looking for PKTMUX. If the /v option is given
      then the interrupt used is recorded in the Environment variable
      PKT_INT.



      12.  The /b option causes PKTMUX to try and locate the data buffer
      within the Packet Driver so that it can look at the data before
      taking a copy of the packet.  This option is specific to the Packet
      Drivers of certain ethernet cards and has been tested successfully
      on the following:

                Card                     Buffer Size Found in Bytes

        BICC 16 bit ISA and MCA versions            64
        NE2000                                      23
        WD8003                                      64

      Note that if PKTMUX is unable to find the data buffer the option is
      disabled so it can be used safely in any situation.  However if the
      card you are using is not in the above list then it would be
      prudent to check that all is well just in case the algorithm fails
      to locate the correct buffer.  If the /x option is given then
      PKTMUX goes through the motions of trying to locate the buffer but
      does not use it.  Note that PKTSTATS displays the current state of
      the algorithm and with the /a option gives more details.

      This is a new facility to evaluate feasibility and may not be very
      satisfactory in some cases.  It is further explained in the
      Technical Description section below.

      13.  One of the problems in running PKTMUX from a batch file is
      that if an error occurs then the message often disappears off the
      screen before it can be noted. The /p option causes output to pause
      if an error is detected when PKTMUX is first loaded and wait for
      input from the user before proceeding.





      5.2 PKTDRV.EXE
      --------------

      This is a TSR which provides the pseudo Packet Driver interface in
      conjunction with PKTMUX.  Its format is:

        PKTDRV pkt_drvr_int mux_int all_type /options

      which uses the multiplexor on hex interrupt "mux_int" or by default
      searches for it.  It installs itself as a Packet Driver on hex
      interrupt "pkt_drvr_int" or, by default, the first free interrupt
      after the multiplexor (note 1).  The "all_type" parameter
      (repeatable) defines the packet Type values used when an
      application asks for all types (eg PC-NFS v3.0).  The
      default setting is 0800, 0806 and 8035 (note 2).  Any failure
      during loading will cause PKTMUX to abort and set the DOS
      ERRORLEVEL to 1.  PKTDRV memory usage is a little over 1K.

      The following options modify the action taken:

        c   copy send buffers (note 3).
        d   drop packets if application has no buffers (note 5).
        e   extend search area under a control program (note 11).
        f   force PKTDRV to be Free; !f forces to Busy (note 1)
        h   display this help information.
        i   asking for all types gives IEEE 802.3 channel (note 7).
        l   act as listener for any protocol type (note 4).
       !l   dont act as listener for any protocol type.
        lf  act as listener for TCP FTP; !lf negates.
        li  act as listener for IP; !li negates.
        lt  act as listener for TCP; !lt negates.
        lt# act as listener for TCP port # (decimal); !lt# negates.
        lu  act as listener for UDP only; !lu negates.
        lu# act as listener for UDP port # (decimal); !lu# negates.
        n   only load PKTDRV if needed ie. there is no free PKTDRV
            already (note 8).
        o   override use of specified interrupt (note 1).
        p  pause if error found (note 12).
        q   query state of a PKTDRV (note 10).
        r   reset a PKTDRV that is busy (note 1).
        s   silence output except warnings (unless /ss) or errors
            (unless /sss) (note 9).
        t   terminate PKTDRV, PKTMUX and Packet Driver (note 6).
        u   unload last loaded PKTDRV if Busy (note 6).
        uu  unload last loaded PKTDRV even if Busy.
        ur  repeatedly unload last loaded PKTDRV if not Busy.
        v   set DOS Environment variable PKT_INT to interrupt used or
            found (notes 1 & 11).



      Examples are:

        pktdrv               ; normal use
        pktdrv /c            ; copy send buffers
        pktdrv 66 62         ; multiplexor on 62, put Packet Driver on 66
        pktdrv /t            ; terminate PKTDRV, PKTMUX and Packet Driver
        pktdrv /u            ; unload last PKTDRV to be loaded
        pktdrv /uu           ; unload last PKTDRV to be loaded even if Busy
        pktdrv 63 /u         ; unload PKTDRV on Int 63
        pktdrv 0 0 800 806 1000 ; Application wanting all packet types will
                                ; just get 0800, 0806 and 1000
        pktdrv /!l /lf       ; not a listener for any service except FTP
        pktdrv /lt21         ; listener for TCP port 21

      Notes:

      1.  PKTDRV by default uses the next free Interrupt after that used
      by PKTMUX.  It avoids Interrupts 61, 62 and 64, as these are used
      by PCTCP, Vista eXceed and Novell respectively, and also 67 as this
      is the EMS entry point.  Interrupts 70 - 76 are normally in use on
      all but the XT type PCs.  If the /v option is given then the
      interrupt used is recorded in the Environment variable PKT_INT.  If
      the Interrupt is specified it is checked to see if it already in
      use by PKTDRV, PKTMUX or a Packet Driver and if so PKTDRV will
      refuse to load unless the /o option is given.

      Note that under a control program, such as Windows 3, PKTDRV will,
      by default, use the same Interrupt in each DOS session it is loaded
      in.  This is because each DOS session has its own version of the
      Interrupts.  For the same reason PKTSTATS will only see the PKTDRV,
      if any, in its DOS session yet will display the correct total that
      are busy.

      Part of the Packet Driver definition is the use of the string PKT
      DRVR just after the interrupt entry point in order to identify it.
      A communications application which does not require the explicit
      definition of the Packet Driver interrupt searches from Interrupt
      60 up to 7f until it finds one.  PKTDRV uses the same mechanism and
      so appears to be a genuine Packet Driver.  However once a
      communications application has accessed PKTDRV the identification
      is changed and only reverts back when the application has given a
      release command.  Thus several copies of PKTDRV can provide the
      impression that multiple Packet Drivers are present.  The state of
      each PKTDRV is shown by calling PKTSTATS - Free means it can be
      used by an application and Busy means its identification has been
      changed and it is in use.

      One problem with this mechanism is when two applications can use
      the same Packet Driver - for example PCTCP running alongside a
      Novell Packet Driver using TYPE 8137 protocol - then doing this
      over one PKTDRV will fail.  One solution is to use separate PKTDRV
      for each.  Alternatively once the first application has been
      started and the PKTDRV is now Busy then a command of the form:

        pktdrv pkt_drvr_int /f

      forces the state back to Free. A second application can then be
      loaded which finds PKTDRV and can use it.




      The opposite problem is when an application is loaded, locates a
      Free PKTDRV but does not issue any commands and thus change the
      PKTDRV state to Busy.  The call:

        pktdrv pkt_drvr_int /!f

      forces the PKTDRV to be Busy thus subsequent applications will not
      find it.

      If a PKTDRV is marked as Busy and the application has terminated
      (or crashed!) then calling PKTDRV with /r option will reset the
      specified "pkt_drvr_int" PKTDRV.  Note that /r resets the channel
      whereas /f simply resets the program identification and leaves all
      the call details intact.  If the PKTDRV was also terminated at the
      same time as the application, such as when a Windows DOS session is
      terminated, then the channel is Busy but there is no PKTDRV to send
      a Reset to.  In this case PKTMUX will have registered that the
      PKTDRV has gone and giving the command:

        pktmux /r

      will reset any Busy channel for which there is no PKTDRV.

      Note that in the PKTDRV calls above if the "pkt_drvr_int" is
      not specified then a search is made from the last possible PKTDRV
      Interrupt number (7f) back to the first (60).  Thus a generalised
      use of the feature is possible provided the PKTDRV being used is
      the last one that was loaded and/or the highest Interrupt number.
      See also note 11.

      The /f, /!f and /r requests are refused if they are directed at a
      PKTDRV which was loaded under DOS and the PKTDRV issuing them is
      running under Windows or DESQview.  This can be overriden by
      repeating the option for example /ff, /!f!f or /rr.

      A copy of PKTDRV can be loaded at any time.  If it is required to
      unload the system at some later time it is perhaps wise to load all
      the PKTDRV copies that are required under DOS just after PKTMUX.
      This minimises the chance of problems with interrupt chains but
      means that any use of the /f or /r options need the "pkt_drvr_int"
      specifying.

      2.  Instead of requesting certain packet types some applications,
      notably PC-NFS v3.0, ask for all packet types.  PKTMUX
      does not allow this since it makes its job extremely difficult so
      PKTDRV intercepts such a request and replaces it by specific packet
      types.  By default these are 0800 (IP Protocols), 0806 (ARP -
      Address Resolution Protocols) and 8035 (RAPR - Reverse ARP) and
      these are all PC-NFS really needs for its own use.  Where further
      packet types are required these can be overridden and alternatives
      supplied.

      One limitation of this implementation is that an application with a
      genuine requirement for all packet types cannot be supported.  An
      exception is IEEE 802.3 (ISO 8802/3) over a Packet Driver Class
      1 as used by the RAL LLCPKT product and this can be supported by
      via the /i option.



      Note that a single PKTDRV will only support a single application
      when implementing all packet types (such as PC-NFS) or IEEE802.3.
      If another application is required, such as Novell, then it must
      use another PKTDRV.


      3.  Under Windows 3 (and possibly DESQview) some communications
      cards which use DMA (direct memory access) for sending data don't
      work properly.  The same thing can happen when the application is
      located in upper memory (ie above 640K).  The solution is to copy
      the data from the application's buffer into one in PKTMUX and send
      it from there.  This is done by the /c option and it only applies
      to data sent via that PKTDRV.  The only card so far found to
      require this is the BICC 16bit ethernet card though this may be
      dependent on the PC hardware and the EMM in use.

      4.  The /l and /!l options indicate whether or not the application
      using this PKTDRV should act as a listener for well known services.
      See Technical Description below for further details.

      5.  The /d (drop) option makes this PKTDRV channel behave as a
      normal Packet Driver and drop any packet for which the application
      has no buffer rather than holding it in a buffer which is the
      default.  The PKTMUX option /d implements the same feature for all
      channels and overrides the PKTDRV setting.

      6.  The /u option causes PKTDRV to unload unless it is still busy
      with an application.  Adding an /r requests all PKTDRVs be
      unloaded.  Note this may not be possible if other TSRs where loaded
      between PKTDRVs.  If it is known that an application is not Busy,
      such as when it has crashed, then the /uu option will force the
      unload.  The /t option does the same thing but also sends a
      terminate request to PKTMUX which, if it is acceptable, will also
      send a terminate request to the Packet Driver. These requests are
      refused if the PKTDRV they are directed at was loaded under DOS
      and the PKTDRV issuing them is running under Windows or DESQview.

      If the "pkt_drvr_int" is not specified then a search is made from
      the last possible PKTDRV Interrupt number (7f) back to the first
      (60).  Thus a generalised use of this feature is only possible
      provided the PKTDRV being unloaded is the last one that was loaded
      and also the highest Interrupt number. See also note 11.

      7.  If the /i option is given then a request for all types will
      result in IEEE 802.3 (ISO 8802/3) type packets (ie those 1500 bytes
      long or less) being routed up this channel.  The PKTMUX /i option
      must also be given for this to work.

      Thus implementations of ISO CONS (Pinkbook in the UK academic
      community) can run over PKTMUX where Access is done using Packet
      Driver Class 1.  UK Academic users of the RAINBOW software who wish
      to use a Packet Driver alongside to run say PC-NFS or any other
      TCP/IP stack thus have two options.  They can either run the RAL
      LLCPKT2 product which provides a packet driver interface.  This
      interface can then be either used directly by an application or via
      PKTMUX for several applications.



      Alternatively they can run LLCPKT direct to a PKTDRV with the /i
      option.  Note however that the overheads of both methods are
      significant. However if the /b option is successfully used on
      PKTMUX then the latter is dramatically more efficient.

      Note this is a new facility to evaluate feasibility and may not be
      very satisfactory. Depending on feedback a better implementation
      may be included in the next version.

      8.  The /n option instructs PKTDRV to check either the specified
      "pkt_drvr_int" or, if this is not given, then Interrupts between 60
      to 7f to see if a PKTDRV is already running and whether it is Free.
      If this is true it does not load and returns an ERRORLEVEL
      similar to the /q option as follows:

                0    No Free PKTDRV found - PKTDRV loaded ok
                2    Free PKTDRV found - PKTDRV not loaded
                3    As 2 but Free PKTDRV loaded before Control Program
                4    No Free PKTDRV found - PKTDRV load failed for
                     another reason such as no PKTMUX present.

      The parameter settings of the free PKTDRV are also set to those of
      the PKTDRV call.

      This option allows a BAT file to only load a PKTDRV if it is
      required. See also note 11. Note that the ERRORLEVEL denoting a
      failure is now 4 instead of 1 as it is when the /n option is not
      present.

      9.  If the /s option is given then PKTDRV does not give out any
      messages unless an error or warning occurs. The option /ss prevents
      any warning messages and /sss prevents error messages as well.

      10. The /q option causes PKTDRV to return the state of
      "pkt_drvr_int" in both text form and also via the ERRORLEVEL as
      follows:

                0    No PKTDRV found
                1    Busy PKTDRV found
                2    Free PKTDRV found
                3    As 2 but Free PKTDRV loaded before Control Program

      If the "pkt_drvr_int" is not specified then a search is made from
      Interrupts 60 to 7F looking for any PKTDRVs.  Reporting a Free
      PKTDRV takes precedence over a Busy one. See also note 11.

      11.  The rules for searching for a PKTDRV are modified when
      running in the DOS session of a control program such as Windows or
      DESQview.  In this case, even if the "pkt_drvr_int" is specified,
      only the PKTDRV programs loaded in this DOS session are checked.
      To expand the search to all PKTDRVs, that is to include those
      loaded before the control program was run, the option /e must be
      given.  Thus it is possible to target the effect of any option to
      either the current DOS session or all the PKTDRVs in the machine
      excluding those in other DOS sessions.  If the /v option is given
      then the PKTDRV interrupt is recorded in the Environment variable
      PKT_INT.  These search rules affect options /f, /!f, /n, /q, /r,
      /t and /u.



      12.  One of the problems in running PKTDRV from a batch file is
      that if an error occurs then the message often disappears off the
      screen before it can be noted. The /p option causes output to pause
      if an error is detected when PKTDRV is first loaded and wait for
      input from the user before proceeding.



      5.3 PKTSTATS.EXE
      ----------------

      This program displays program details and statistics from PKTMUX.
      Its format is:

        PKTSTATS /options

      The following options modify the action taken:

        a  display further information - can be repeated (note 1).
        e  extend PKTDRV search area under a control program (note 5).
        h  display this help information.
        q  query state of a Packet Driver, PKTMUX and PKTDRV (note 4).
        s  silence output from /q option.
        v  set DOS Environment variable PKT_INT to interrupt found by
           /q option (note 5).

      Examples are:

        pktstats             ; normal use
        pktstats /a          ; show further information
        pktstats /q          ; query state
        pktstats /qe         ; query state under Windows including
                             ; PKTDRV copies loaded under DOS

      Notes:

      1.  The option /a can be repeated up to 3 times to give increasing
      levels of information.  This is mainly intended for debugging
      purposes.  Repeating /a 3 times can get the program in a loop or
      give misleading information since it scans queues which may be
      changing.  This is intended only for cases when PKTMUX has stopped
      with a system error.

      2.  The counts given by PKTSTATS are 16 bit integers so will
      overflow over a period of time.  The counts are not read at the
      same time but are obtained as they are required by PKTSTATS.  As
      PKTMUX is processing data at the same time there may be some
      inconsistencies in fast moving values such as Broadcast and Ignored
      counts.

      3.  In the output from PKTSTATS where the name before a count value
      is in CAPITAL letters then this indicates that data is being lost
      or discarded for some reason.  Further details are given in the
      section on Problem Solving.




      Each PKTDRV channel may have one or more of the following
      qualifiers againsts it:

        /Drop_buff      PKTDRV /d option given
        /DV             PKTDRV running under DESQview
        /DOS_to_Window  PKTDRV running under DOS but application under
                        Windows so application may loose packets.
        /TIMED_OUT      PKTDRV appears to be no longer active.
        /TX_Copy        PKTDRV /c option given
        /Win            PKTDRV running under Windows
        /Zero_type      All Packet Types requested so mapped onto
                        specified Types - usually 0806 and 0800.
        /802.3          PKTDRV /i option given

      4. The /q option causes PKTSTATS to search Interrupts 60 to 7f
      for the state of a Packet Driver, PKTMUX and PKTDRV and report
      back in both text form (unless /s option given) and also via the
      ERRORLEVEL as follows:

                0    No Packet Driver found
                1    Packet Driver found
                2    PKTMUX and Packet Driver found
                3    Busy PKTDRV, PKTMUX and Packet Driver found
                4    Free PKTDRV, PKTMUX and Packet Driver found
                5    As 4 but Free PKTDRV loaded before Control Program

      Reporting a Free PKTDRV takes precedence over a Busy one.  See also
      note 5.

      5.  The rules for searching for a PKTDRV with the /q option are
      modified when running in the DOS session of a control program such
      as Windows or DESQview.  In this case only the PKTDRV programs
      loaded in this DOS session are checked.  To expand the search to
      all PKTDRVs, that is to include those loaded before the control
      program was run, the option /e must be given.  Thus it is possible
      to target the effect of the /q option to either the current DOS
      session or all the PKTDRVs in the machine excluding those in other
      DOS sessions.  If the /v option is given then the interrupt of
      whatever is found is recorded in the Environment variable PKT_INT.




      5.4 WINPKT.COM
      --------------

      This program is not part of the PKTMUX system but since it provides
      a subset of the facilities for a smaller memory requirement it is
      included.  In is not supported by RAL.  In accordance with the
      distribution licence the source is also supplied in WINPKT.ASM.
      The program COPYING mentioned at start up is not supplied as I dont
      have a copy.  WINPKT is also part of the Crynwr (ex Clarkson)
      Packet Driver collection v10 and may be a later version.

      WINPKT acts as an interface between an application running under
      Windows 3 in Enhanced mode and a Packet Driver.  It uses Windows 3
      calls so is specific to this case.  Its format is:

        WINPKT new_pkt_drvr_int old_pkt_drvr_int

      where "old_pkt_drvr_int" is the interrupt of the Packet Driver in
      either decimal or hex preceeded by 0x.  "new_pkt_drvr_int" is the
      new interrupt to use and cannot be the same as "old_pkt_drvr_int".
      There are no documented options.


      Examples are:

        winpkt 0x63 0x64        ; Packet driver on Interrupt 64, WINPKT
                                ; accessed via Interrupt 63
        winpkt                  ; provide help information


      Notes:

      1.  WINPKT should be loaded after the Packet Driver and before
      Windows 3 is loaded.  It is recommended that "new_pkt_drvr_int" is
      before "old_pkt_drvr_int" since applications that search for a
      packet driver will find the driver and not WINPKT.

      2.  WINPKT has no unloading mechanism so if unloading is required
      the RAL LOADSYS system or similar must be used.

      3. WINPKT may not work with certain ethernet cards. The BICC 16 bit
      card is the only know example so far found. PKTMUX should be used
      in these cases along with the /c option on PKTDRV.




      6.  Examples
      ============

      The following examples illustrate the use of PKTMUX and attempt to
      show the various possible uses of the system. It assumes a degree
      of familiarity with setting up and use of the various systems
      exampled. Examples include the RAL MOS2 IBM 3270 emulator since
      this system was one of the reasons for writing PKTMUX. The RAL
      LOADSYS program to load and unload TSRs and Device Drivers can also
      be useful in running multiple protocol stacks. Details of both are
      given in the Reference Section.

      It is usually the case that a sequence of commands is put into a
      BAT file and one section below gives examples of techniques that
      facilitate this.

      In general there are two classes of communications applications.
      The simplest are those that just need a Packet Driver in order to
      work, for example the CUTCP programs PING, LPR and FTPBIN.  A more
      complicated type are those applications which require their own TSR
      to be loaded first.  The applications then communicate via this
      instead of directly to the Packet Driver.  Examples are
      applications that run over PCTCP and PC-NFS.

      Another twist are those applications that either are, or can
      become, TSRs and thus allow you to return to DOS.  Thus further
      applications can be run.  Examples are MOS2 which is a TSR and FTP
      which via the command !  becomes a TSR and starts up a DOS session.


      6.1 Packet Driver, PCTCP and PC-NFS Applications under DOS
      ----------------------------------------------------------

      The following illustrates how to run a Packet Driver application
      alongside those requiring their own TSR to be loaded.  The first is
      for PCTCP and assumes IPCUST.SYS and IFCUST.SYS are loaded in
      CONFIG.SYS.

        ne2000 0x63 0x5 0x320    ; Load Packet Driver for NE2000 card
        pktmux                   ; Support 2 channels
        pktdrv                   ; PKTDRV for PCTCP to use
        pktdrv                   ; PKTDRV for Packet Driver application
                                 ; to use
        ethdrv                   ; PCTCP Packet Driver interface

      You can now run applications from the PCTCP program suite, such as
      FTP, PING or LPR. Programs that just require a Packet Driver can
      also be run such as FTPBIN from the CUTCP program suite.




      The following illustrates how to run a Packet Driver application
      alongside the PC-NFS TSR.  It is assumed that SOCKDRV.SYS, PKTD.SYS
      and ANSI.SYS are loaded in CONFIG.SYS.

        pcnfs.sys /b1            ; loaded in CONFIG.SYS

        mbdndpd 0x63 /I10 /D3    ; Load Packet Driver for BICC 16 bit
                                 ; card
        pktmux                   ; Support 2 channels
        pktdrv                   ; PKTDRV for PC-NFS to use
        pktdrv                   ; PKTDRV for Packet Driver application
        cd \nfs
        prt *                    ; Normal PC-NFS loading
        net init

      PC-NFS applications such as NFSPING can now be run as well as those
      just requiring a Packet Driver such as FTPBIN from CUTCP.


      6.2 MOS2 under DOS
      ------------------

      The RAL MOS2 IBM 3270 Emulator v2.3 is a TSR.  It supports the
      Waterloo TCP/IP protocol stack and is normally run by loading the
      Packet Driver and then running the file MOS2T.BAT.  To achieve this
      using PKTMUX type:

        ne2000 0x63 0x5 0x320    ; Load Packet Driver
        pktmux                   ; Support 2 channels
        pktdrv                   ; PKTDRV for MOS2 to use
        pktdrv                   ; PKTDRV for applications to use
        mos2t                    ; Run MOS2

      Once MOS2 is running you can then hot key (Alt-Esc) back to DOS and
      then any other communications application which runs over a Packet
      Driver can be used. For example PING from the Waterloo TCP/IP
      suite or FTPBIN or LPR from the CUTCP suite. For example:

        ftpbin ib                ; establish FTP communications with IB


      To run MOS2 alongside applications from the PCTCP applications
      suite the following is suggested:

        ne2000 0x63 0x5 0x320    ; Load Packet Driver
        pktmux                   ; Support 2 channels
        pktdrv                   ; PKTDRV for PCTCP to use
        pktdrv                   ; PKTDRV for MOS2 to use
        ethdrv                   ; PCTCP Packet Driver interface
        mos2t                    ; Run MOS2

      Once MOS2 is running the PCTCP applications can be used.

      A combination of the two cases, that is the ability to run
      applications from the PCTCP program suite or any other application
      that runs directly over a Packet Driver can be achieved by the
      following:




        ne2000 0x63 0x5 0x320    ; Load Packet Driver
        pktmux 3                 ; Support 3 channels
        pktdrv                   ; PKTDRV for PCTCP to use
        pktdrv                   ; PKTDRV for MOS2 to use
        pktdrv                   ; PKTDRV for applications to use
        ethdrv                   ; PCTCP Packet Driver interface
        mos2t                    ; Run MOS2

      Once MOS2 is running either the PCTCP applications or those
      requiring a Packet Driver can be used.

      Note that it is possible to run MOS2 before loading PCTCP but this
      is not recommended.  Loading PCTCP first removes any problems
      with the provision of well known services such as an FTP listener.
      If MOS2 must be loaded first then its PKTDRV should have the /!l
      option so that any incoming calls for well known services are
      routed to the next PKTDRV which should be the one for PCTCP.


      6.3 Packet Driver and IEEE 802.3 (ISO 8802/3) applications
      ----------------------------------------------------------

      The following illustrates how to run an IEEE 802.3 application
      using a Class 1 access alongside one or more Packet Driver
      applications.  One obviously must be a TSR in order to allow a
      return to DOS in order to run the other.  If the Packet Driver
      application was a TSR (eg PC-NFS) then the sequence could be:

        ne2000 0x63 0x5 0x320    ; Load Packet Driver
        pktmux /ib               ; Support 2 channels
        pktdrv                   ; PKTDRV for application to use
        pktdrv /i                ; PKTDRV for IEEE 802.3 use

      You then load the Packet Driver application TSR then on returning
      to DOS run the IEEE 802.3 application. Note that PKTMUX and the
      PKTDRV used by the IEEE 802.3 application must have a /i option. In
      fact all PKTDRVs could have the /i option so that the IEEE 802.3
      application could use any one. However the exception to this is an
      application, such as PC-NFS v3.0, which asks for all packet types.
      Its PKTDRV must not have a /i option.

      The /b option on PKTMUX is very strongly recommended for IEEE 802.3
      work since, if it works, it should dramatically reduce the
      overheads.




      6.4 Packet Driver and Rainbow Applications
      ------------------------------------------

      UK academic users of the Rainbow product can run Packet Driver
      applications alongside by use of a similar sequence to the previous
      section. The Rainbow software (eg PINKBOOK) must be run over the
      IEEE 802.3 PKTDRV via the LLCPKT interface provided by RAL. Thus to
      run it alongside PC-NFS could be done as follows:

        pcnfs.sys /b1            ; loaded in CONFIG.SYS

        mbdndpd 0x63 /I10 /D3    ; Load Packet Driver for BICC 16 bit
                                 ; card
        pktmux /ib               ; Support 2 channels
        pktdrv                   ; PKTDRV for PC-NFS to use
        pktdrv /i                ; PKTDRV for PINKBOOK to use
        cd \nfs
        prt *                    ; Normal PC-NFS loading
        net init

        llcpkt                   ; LLCPKT Packet Driver to BICC MPS
                                 ; interface
        pinkbook                 ; PINKBOOK TSR
        rainbow                  ; Rainbow application


      6.5 Packet Driver Applications under Windows 3
      ----------------------------------------------

      The following illustrates how to run Packet Driver applications
      under Windows 3 in Enhanced mode. Use under DESQview is very
      similar.

        ne2000 0x63 0x5 0x320    ; Load Packet Driver
        pktmux 8 /4              ; Support 8 channels but only 4 will
                                 ; will be active at once
        win                      ; Run Windows 3

      To run an application open a DOS session and type:

        pktdrv                   ; PKTDRV for application to use

      followed by the application. The application could be the MOS2
      emulator BAT file for example:

        mos2t

      To run further applications just open more DOS sessions and run
      PKTDRV then the application. For IEEE 802.3 applications the PKTMUX
      call must have the option /i added (and /b is also recommended) and
      the PKTDRV run under the DOS session should have a /i. Thus to run
      the Rainbow application in their Windows DOS session would type:



        pktdrv /i
        llcpkt                   ; LLCPKT Packet Driver to BICC MPS
                                 ; interface
        pinkbook                 ; PINKBOOK TSR
        rainbow                  ; Rainbow application

      Where a PIF file is used then the associated BAT file could
      contains commands similar to above. A little care is needed with
      error conditions since if there is no free channel then the PKTDRV
      load will fail. For example:

        pktdrv /p
        IF ERRORLEVEL 1 GOTO EXIT          ; Jump if failed
        .
        run application
        .
        :EXIT

      If the loading of PKTDRV fails for any reason the /p option holds
      up processing allowing the user to see the error message generated.
      The complete BAT file for the MOS2 emulator would therefore be:

        pktdrv /p
        IF ERRORLEVEL 1 GOTO FAIL          ; Jump if failed
        call mos2t
        command
        :EXIT

      Be warned that Windows, especially 3.0, can become unstable if you
      have insufficient memory and opening too many DOS sessions may
      result in a Unrecoverable Application Error.  This usually does no
      damage and other sessions are unaffected.  Note also that, unless
      the PC is quite powerful, applications may fail as they will not
      get enough CPU to process their communications in time and
      protocols may time out. This is especially so if IEEE 802.3
      protocols are used.




      6.6 Packet Driver, PCTCP and PC-NFS Applications under Windows 3
      ----------------------------------------------------------------

      This is essentially the same as under DOS but with the PKTDRV for
      the Packet Driver application run under a DOS session. For example
      to run both PCTCP and Packet Driver applications the following
      would suffice.

        ne2000 0x63 0x5 0x320    ; Load Packet Driver
        pktmux 8 /4              ; Support 8 channels but only 4 will
                                 ; will be active at once
        pktdrv                   ; PKTDRV for PCTCP to use
        ethdrv                   ; PCTCP Packet Driver interface
        win                      ; Run Windows 3

      To run a Packet Driver application open a DOS session and type:

        pktdrv                   ; PKTDRV for application to use

      followed by the application. For PCTCP applications just run the
      application.


      6.7  Windows 3 Applications
      ---------------------------

      Windows 3 applications are slightly different in that they do not
      run in a DOS session so it is not possible to run PKTDRV after
      Windows has been loaded.  For those that run over PCTCP or PC-NFS
      then the appropriate TSR is loaded under DOS after PKTMUX and one
      PKTDRV as illustrated above.  The application is then run under
      Windows as normal.

      For those that run over a Packet Driver, for example WINQVT, then
      the procedure is very similar to running them under DOS, that is
      the PKTDRV is loaded before Windows 3. For example to run WINQVT
      and also other applications that use a Packet Driver the following
      would suffice:

        ne2000 0x63 0x5 0x320    ; Load Packet Driver
        pktmux 8 /4              ; Support 8 channels but only 4 will
                                 ; will be active at once
        pktdrv                   ; PKTDRV for WINQVT to use
        pktint                   ; WINQVT Packet Driver interface
        win                      ; Run Windows 3

      Then run WINQVT as normal with QVT_TCP.RC edited to contain the
      line:

      packet_vector=65

      This is done because WINQVT has to have its Packet Driver interrupt
      specified and PKTDRV will use 65 by default in the above example.
      If there is any doubt then PKTDRV could have its interrupt number
      specified as the first parameter for example:

        pktdrv 65




      If WINQVT is not going to be loaded immediately then there is a
      problem that another application may use the PKTDRV intended for
      WINQVT since it would the the first one found when searching down
      the Interrupts.  To combat this it is recommended that
      WINQVT is given a high interrupt number (eg 7F) to guarantee it
      will be free. For example:

        ne2000 0x63 0x5 0x320    ; Load Packet Driver
        pktmux 8 /4              ; Support 8 channels but only 4 will
                                 ; will be active at once
        pktdrv 7f                ; PKTDRV for WINQVT to use
        pktint                   ; WINQVT Packet Driver interface
        win                      ; Run Windows 3

      Then run WINQVT as normal with QVT_TCP.RC edited to contain the
      line:

      packet_vector=7f

      To run further Packet Driver applications open a DOS session and
      run PKTDRV and the application as before.  To run PCTCP or PC-NFS
      applications then modify the above to include the TSR before
      loading Windows.  Alternatively for PCTCP the TSR can be run under
      Windows 3 inside a DOS session since it is effectively a Packet
      Driver application.  IPCUST.SYS and IFCUST.SYS must have previously
      been loaded in CONFIG.SYS or could be loaded by the RAL LOADSYS
      system.




      6.8  Novell Netware
      -------------------

      Novell using a Type 8137 packet can be run in a variety of ways.
      Note that because PKTMUX hides the real Packet Driver by taking
      over its interrupt then the Novell Packet Driver interface IPX must
      use a PKTDRV.  For example:

        ne2000 0x63 0x5 0x320    ; Load Packet Driver
        pktmux 2                 ; Support 2 channels
        pktdrv                   ; PKTDRV for Novell to use
        pktdrv                   ; PKTDRV for application to use
        ipx                      ; Load Novell 8137 Packet Driver
                                 ; interface
        etc

      An improvement on this is to note that PKTDRV, like a normal Packet
      Driver, can support several protocol types so it is possible for
      one PKTDRV to support both Novell and an application. However the
      difference is that PKTDRV sets itself busy when it is Accessed so
      it must be made Free again before it can be Accessed again. For
      example:

        ne2000 0x63 0x5 0x320    ; Load Packet Driver
        pktmux 2                 ; Support 2 channels
        pktdrv                   ; PKTDRV for Novell and one
                                 ; application to use
        ipx                      ; Load Novell 8137 Packet Driver
                                 ; interface
        pktdrv /f                ; make PKTDRV free again
        pktdrv                   ; PKTDRV for second application to use
        etc

      Note that in this case the second application must not be one that
      uses all packet types (eg PC-NFS v3.0) or IEEE802.3.  Further note
      that if the application does any form of filestore redirection such
      as PC-NFS or IDRIVE from PC/TCP then this must be loaded before IPX
      is run.  This is because although at Packet Driver level there are
      no problems it appears that only the Netware filestore redirector
      can cope with another redirector following it in the chain. It must
      therefore be loaded last.

      If the Novell service is using the Standard Netware protocol, that
      is using in a standard IEEE802.3 packet, then the Packet Driver
      will map this to Type 8137 if the -n option is given. Thus the
      first line in examples above would become:

        ne2000 -n 0x63 0x5 0x320 ; Load Packet Driver





      6.9 Packet Driver/PKTMUX/PKTDRV BAT files
      -----------------------------------------

      It is frequently the case that a general purpose BAT file has to be
      written to load communications software.  PKTMUX provides various
      tools to assist in this as are illustrated in the following
      examples.  Note that the /s option can be added to all the calls to
      avoid confusing the user with the messages that are generated. It
      is also recommended that the /p option is added to all calls to
      load PKTMUX and PKTDRV so that the BAT file pauses if an error is
      found thus allowing the user to read the message.

      The following example checks if a Packet Driver or PKTMUX has
      already been loaded before loading both along with a PKTDRV ready
      to run a communications application.

        pktstats /qp                       ; Query state
        IF ERRORLEVEL 4 GOTO GOT_FREE      ; Jump if got a Free PKTDRV
        IF ERRORLEVEL 2 GOTO GOT_PKTMUX    ; Jump if got a PKTMUX
        IF ERRORLEVEL 1 GOTO GOT_PACKET    ; Jump if got a Packet Driver
        ne2000 0x63 0x5 0x320              ; Load Packet Driver

        :GOT_PACKET
        pktmux                             ; Load PKTMUX
        IF ERRORLEVEL 1 GOTO FAIL          ; Jump if failed

        :GOT_PKTMUX
        pktdrv                             ; PKTDRV busy so load new one
        IF ERRORLEVEL 1 GOTO FAIL          ; Jump if failed

        :GOT_FREE                          ; All loaded and a Free PKTDRV
        etc                                ; available


      Alternatively the PKTDRV call could have the /n option which would
      remove the need for the second line jump to GOT_FREE and is a
      general purpose way of loading a PKTDRV only if one is not already
      Free.  Such use does require a different testing of the ERRORLEVEL
      since a value is returned if the PKTDRV is not loaded because a
      Free one already exists.  For example:

        pktdrv /n
        IF ERRORLEVEL 4 GOTO FAIL          ; Jump if failed

      Note that ERRORLEVEL values of 2 and 3 mean not loaded due to a
      Free PKTDRV being present.




      If the application was one that terminated and then released the
      Packet Driver, for example LPR or TRUMPET, then the line:

        pktdrv /u

      could be added after the application had been run to unload the
      PKTDRV, if this is possible.  This would reduce the memory
      occupancy and increase the possibility of being able to unload any
      other TSRs.

      Note that in all the above cases the /v option could have been
      added thus causing the interrupt used to be recorded in the DOS
      Environment variable PKT_INT. Thus in the above case the call:

        pktdrv /nv

      would set PKT_INT to either the Free interrupt it found or the
      Interrupt used by the new PKTDRV. Hence an application requiring to
      know the Interrupt value in its call could be passed this detail.

      However if such an application held the interrupt number in a file
      so that it could not be easily changed in a BAT file then checks
      for a PKTDRV on this fixed interrupt number, 7f in the
      example, could be done as follows:

        pktdrv /q 7f
        IF ERRORLEVEL 3 GOTO GOT_FREE      ; Jump if got a Free PKTDRV
        IF ERRORLEVEL 2 GOTO FAIL          ; Jump if got a Busy PKTDRV
        pktdrv 7f                          ; Load PKTDRV on 7f
        IF ERRORLEVEL 4 GOTO FAIL          ; Jump if failed

        :GOT_FREE
        run application

        pktdrv 7f /u                       ; Unload PKTDRV if possible

      If there was already a Busy PKTDRV on Interrupt 7F then it would
      not be possible to run the application.

      All the above cases would also work under a control program such as
      Windows or DESQview provided certain conditions are met concerning
      any PKTDRV programs loaded under DOS, that is before the control
      program was loaded.  They must all be busy when the control program
      was loaded, for example being used by PCTCP or PC-NFS.  If they are
      still free then they must either be made busy as soon as the
      control program is loaded by the application, such as WINQVT, being
      loaded at startup, or they must use a high interrupt such as 7F.
      The reason behind all this is to avoid an application in a DOS
      session searching from Interrupt 60 and finding a free PKTDRV
      running under DOS rather than in the DOS session itself.  Whilst an
      application will work in this case the response will be a lot
      slower and the likelyhood of failure much higher.  If it can be
      guaranteed that any Free PKTDRV loaded under DOS has an Interrupt
      at the end of the range, eg 7F, then the examples above will work.





      If not then any Free PKTDRV under DOS must be made Busy to avoid
      any problems.  The following suggests how and uses the /e option to
      widen the search outside the DOS session and the /v option to note
      the PKTDRV interrupt number:

        pktdrv /nv                         ; Load PKTDRV unless one Free
                                           ; in this DOS session
        IF ERRORLEVEL 4 GOTO FAIL          ; Jump if failed

        :TEST_AGAIN                        ; Have a Free PKTDRV in the
                                           ; DOS session
        pktdrv /qve                        ; Check entire machine
        IF ERRORLEVEL 3 GOTO GOT_DOS       ; Jump if Free PKTDRV under DOS
        run application                    ; All ok so run application
        GOTO EXIT

        :FAIL                              ; Failure to load PKTDRV
        Echo Cannot load PKTDRV
        GOTO EXIT

        :GOT_DOS                           ; Free PKTDRV under DOS
        pktdrv /e!f!f %PKT_INT%            ; Busy it
        GOTO TEST_AGAIN                    ; Test again in case another

        :EXIT

      This BAT file forces to Busy any Free PKTDRV running under DOS with
      a lower Interrupt number than any in the DOS session so that an
      application does not use it.  Note that this BAT file will run
      equally happily under DOS provided a PKTDRV at a high interrupt
      number is not Free.




      7.  Technical Description
      =========================

      This section describes how PKTMUX goes about its task and is
      intended for those who wish to understand how the system works and
      why it has the limitations it has.  An understanding of the Packet
      Driver interface is assumed.  The various PKTMUX counts and states
      detailed below are shown the command:

        pktstats /a

      Additional states are given by the option /aa.


      7.1 Basic Methodology
      ---------------------

      In essence the system is very simple.  PKTMUX talks to the Packet
      Driver and receives data from it.  Each PKTDRV passes all commands
      onto PKTMUX with the addition of the channel number.  PKTDRV also
      sits on a timer interrupt and asks PKTMUX once per system tick if
      there are any packets for this channel and if so then gets them
      passed over.  A PKTDRV is only Busy from when it has been
      asked by an application to Access a packet Type to when that is
      Released.  In between it remains Free.


      Whilst PKTMUX makes every attempt to be efficient it does create a
      significant overhead when multiplexing between several
      applications.  This is because the Packet Driver interface only
      tells you it has a packet and does not give a pointer so that you
      can see if you are interested in its contents.  Where only one
      application is using this packet type then the packet is sent
      direct to the application.  Otherwise it is necessary for PKTMUX to
      read the packet into its own storage, analyse its contents and then
      send it when asked by a PKTDRV to the appropriate application(s).
      Thus every packet received in this manner has to be copied once
      more than necessary unless devious cunning is employed via the
      /b option.


      7.2 Buffer Strategy
      -------------------

      When an application is unable to accept a packet, usually because
      it has no free buffer space, then PKTMUX keeps the packet in its
      buffers and every timer tick keeps asking the application to accept
      it.  It does this even when it normally sends data direct to the
      application, thus those applications which operate on a small
      buffer pool may lose less data when under PKTMUX especially when
      they receive less CPU cycles when running under Windows 3.  The
      decision whether to keep a packet when an application is unable to
      accept it is a difficult one and depends on the available buffer
      pool and activity on other channels.  The ultimate criterion is the
      age of the buffer and after between 2 and 3 seconds it is dropped.
      Whilst this mechanism is satisfactory for most applications there
      are some that give problems.  One that has been noted is TRUMPET




      which, when an interaction has been completed and it is waiting for
      user input, refuses to accept any more packets.  Whilst
      PKTMUX's buffer strategy will cope in normal circumstances, under
      heavy loading this could give problems.  The /d option is therefore
      available on PKTDRV which causes a packet to be always dropped when
      an application is unable to accept it.  Thus it behaves exactly as
      a Packet Driver.  The /d option is also available on PKTMUX to
      provide this feature on all channels and could be used in cases of
      extreme loading.


      7.3 Channel Management
      ----------------------

      Normally a channel is freed when the application Releases all the
      packet TYPEs is has Accessed.  If this does not occur, usually
      because the application has crashed, then there are two possible
      cases.

      The first, and most normal, is where the PKTDRV being used by the
      application is still running and a call the PKTSTATS shows it to be
      Busy.  The command:

        pktdrv /r

      will reset the PKTDRV and free the channel.

      The second case is when the PKTDRV is not running.  PKTMUX detects
      this by the absense of any timer interrupts and frees the channel
      after about two seconds.  However this technique fails under a
      control program such as Windows 3 or DESQview since the DOS session
      can be locked thus preventing the PKTDRV from sending its timer
      interrupts.  An example is when an area is Selected under
      Windows 3.0 for such actions as cut and paste.

      To overcome this PKTMUX does not immediately free such channels
      when running under a control program but this gives the new problem
      that it now has no means of knowing the channel can be freed.  Such
      channels are marked as having Timed Out and this is displayed by
      PKTSTATS.  To reset such a channel use the following command:

        pktmux /r

      in a DOS session and this will make all such channels free again.

      An automatic means of recovery from this situation is provided by
      the third PKTMUX parameter, Chan_time_out.  This is the time in
      seconds the call stays in a timed out state before being freed
      automatically.  However this should be set with care since if you
      spend too long on your cut and paste the channel may be freed and
      your application will fail.



      One side effect of an application crashing is that it may leave
      PKTMUX in one of its internal busy states. This is shown by the
      PKTSTATS /aa output in the line "Busy Flags". If this occurs then
      PKTMUX will effectively go to sleep. When this is the case then the
      call:

        pktmux /rr

      will also reset these flags and PKTMUX may resume working. It may
      also crash!

      The maximum number of Busy channels supported by PKTMUX is 8 but
      realistically a rather lower number is recommended.  This value is
      permitted in order to mitigate the problems detailed above by
      preventing timed out channels from blocking other applications.  If
      say only 4 channels are actually going to be required but 8 are
      specified then to save memory the number of buffers should be
      reduced by a call such as:

        pktmux 8 /4


      7.4 Control Programs
      --------------------

      One of the problems with the Packet Driver interface is that when
      it receives a packet it then calls a routine in the application.
      This will not fail under DOS but if the application is running
      under a control program such as Windows 3 or DESQview, where the
      application can be swopped in and out of the current virtual
      memory, then there is a need to establish that the current
      application is the correct one.  PKTMUX does this by noting the
      code it is to jump to when a packet is received and checking if
      that is present.  This works satisfactorily unless two copies of
      the same application are running and in this case the application
      has to be tagged in a unique way.

      Note that there are two ways of using PKTDRV under a control
      program.  The preferred way is to load it in a DOS session after
      the control program has been started and then run the application.
      In this way when PKTDRV asks PKTMUX if it has received a buffer it
      can be sure the application is in memory and so minimises any
      delay.  Alternatively when an application runs directly under the
      control program it is therefore not possible to load PKTDRV in the
      same virtual memory so it has to be loaded under DOS before the
      control program.  It therefore has no certainty that the
      application is running when it asks PKTMUX if any data has been
      received so sometimes has to wait until its timer interrupt
      coincides with the time slice of the application.  This can slow
      things down considerably and may require PKTMUX to have a larger
      buffer pool in order to cope.




      7.5 Listeners and /l Options
      ----------------------------

      One of the problems PKTMUX has to solve is to which application to
      route packets for which it has no previous knowledge.  Examples are
      ARP requests and calls to previously unused TCP or UDP ports.
      Experience has shown it is best to send ARP requests to all
      applications.  For TCP and UDP ports the requests can be either for
      well know services (such as TELNET or FTP) in which case the
      default is to send it to the first application to sign up for that
      packet type in the hope that it has a listener for this service.
      This avoids more than one response to such a request.

      Alternatively it may be to a port previously notified by the
      application (an example is FTP) and in this case it is sent to all
      applications who use that packet type.  This latter technique works
      provided the application is tolerant of such unsolicited messages.
      Tests so far indicate that PC-NFS and CUTCP dont mind.  However
      PCTCP, Waterloo TCP and WINQVT are more strict and send back an
      error message.  For TCP this is a RST (reset) and for UDP it is an
      ICMP Port Undefined message.  Since this upsets the service being
      used such cases are trapped and the error message filtered out.
      Note that the WINQVT log may report "Packet received for invalid
      port - reset sent".  In the PKTSTATS output such packets are
      counted under "Ignored:  err Resp" and under "Ign" in the "PKTDRV
      channels:" tables.  There is currently no way of preventing such
      unsolicited messages being sent to an application and the /l
      options only apply to packets for well known ports.

      The definition of a well known port is a little vague these days.
      Originally it was 0-255 but the Unix fraternity officially extended
      this to 1024 for Unix Standard Services and the current RFC 1106
      list goes way beyond this value.  As some applications assume this
      rule in their port usage so PKTMUX designates ports 0-255 as well
      known and routes them to only one channel.  Any other services
      outside this range are likely to be provided by a specialist server
      so sending to all should locate it.  This may be revised in the
      light of experience.

      The various /l options on PKTDRV override the default setting for
      well know services and indicate where such a request should be
      sent or not.  Options of the form /l indicate this application has
      servers of this type and /!l indicates it does not.  The absence
      of an /l or /!l option means the application provides all servers
      but it is used only when no other application has an /l option.

      The /l option types are implemented as an hierarchy with the
      specific protocol ports for TCP and UDP taking precedence over the
      protocols themselves which in turn take precedence over the
      protocol family (IP).  Last in precedence is a general listener.
      The applications are also searched in reverse order of loading so
      that a later application can take precedence over an earlier one.



      The simplest method of making sure the main services such as FTP
      are found is to load that application first.  Where this is not
      possible then the PKTDRVs for applications that do not support
      servers over a protocol should be marked as such by an /!l (ie not
      a listener) type option so that it is avoided when looking for the
      default.  And any application that wants to take over from the
      default can be marked by an /l (ie I am a listener) type option.
      Note that requests will be discarded if no listener is found.

      PKTSTATS will display the listener settings for each channel.


      7.6 Port Duplication
      --------------------

      When an application makes a call to a service it specifies the port
      to which replies should be sent.  How this port number is generated
      is dependent on the application.  There is therefore a possibility
      that two applications could generate the same reply port number.
      To combat this PKTMUX inspects all reply port numbers in outgoing
      packets for TCP and UDP and replaces any new and duplicated number
      by the next one higher, if that is not in use.  It also resets the
      packet header sumcheck if this is being used.  Port numbers on
      incoming packets are similarily mapped along with ICMP packets
      containing TCP and UDP.  Thus it is possible to run two copies of
      the same application without any problems of port duplication.

      However there are two areas that cannot be fixed.  One is where the
      application specifies the reply port via the protocol.  For example
      FTP usually specifies the port to be used for the file transfer via
      the PORT command in its controlling data stream.  Since PKTMUX does
      not analyse the data going through it this is not noted.  There is
      therefore the possibility that such a port number may be duplicated
      if two copies of the same application are run.  Fortunately tests
      with the FTP implementations from PCTCP and CUTCP have not shown
      this to be a problem.

      The second is where the reply port is a well known port and an
      example of this is BOOTP. In this case it assumed that any
      duplicate use of this port is by an application taking over the
      function this well known port supports. Thus a BOOTP exchange on
      one channel will be assumed complete when a second channel uses
      BOOTP. If this is not the case, as it would be if two applications
      started up at the same time, then hopefully the BOOTP retry
      mechanisms will recover the situation.




      7.7 IP Fragmentation
      --------------------

      IP Fragmentation is a means whereby a large packet is carried
      through a network whose packet size limit is too small. It is done
      by simply putting the extra data into the data part of one or more
      IP packets ie. where you would normally expect the TCP or UDP
      header to be. The constituent packets of the fragment are linked by
      having the same IP Identification.

      PKTMUX notes the channel that the first fragment is sent to and
      then routes all further fragments with the same Identifier to that
      channel. This works satisfactorily for most cases but has some
      potential problems.

      The first is when the fragments arrive out of order.  As PKTMUX
      needs the first packet in order to get the TCP or UDP header out
      then any fragment that arrives before this packet will be
      discarded. Such cases are recorded in the NO FRAGMENT count of
      PKTSTATS output. The protocol retry mechanisms should retransmit
      the packet and hopefully the first packet of the fragment will
      arrive first and everything will be ok.

      The second is a more difficult problem in that if the same IP
      Identification is used by two fragmentation sources then PKTMUX has
      no way of distinquishing between the two.  Hopefully this will be
      very rare and the receiving application(s) should spot that they
      have the wrong fragments and their retry mechanisms should recover
      the situation.

      Note that when fragmentation is occurring then the number of
      received and copied fragments (excluding the first) is displayed by
      PKTSTATS.


      7.8 Other IP Protocols
      ----------------------

      PKTMUX is only able to multiplex on IP protocols it knows about.
      These currently are TCP, UDP and ICMP. Any other IP protocol type
      will be handled correctly provided there is only one channel using
      it. Multiple usage of another IP protocol will therefore fail.
      Provided any such protocol has a port mechanism of some form it
      would be possible add to support to PKTMUX if required.




      7.9 IEEE802.3 (ISO 8802/3) Protocol Support
      -------------------------------------------

      Since this protocol changes the meaning of the Type field to be the
      length, PKTMUX has to ask the Packet Driver to send it all packets
      and not just those of a certain TYPE.  This dramatically increases
      the number of packets copied into PKTMUX and hence the overhead on
      the PC.  It also increases the response time, especially under
      control programs such as Windows 3, so can give protocol problems
      as well. Use of the /b option (see next section) can improve this.

      This option is for those IEEE802.3 implementations that Access the
      Packet Driver as a Class 1.  The correct way to support IEEE802.3
      is via Class 11 but this is only available on recent Packet
      Drivers and gives problems as detailed in section 7.12 below.

      Users of the RAL LLCPKT2 product which allows the Rainbow software
      to run alongside a Packet Driver interface should note that PKTMUX
      now supports the simpler LLCPKT product which, if used with the /b
      option, can give a more efficient system.


      7.10 Use of Packet Driver Internal Buffer
      -----------------------------------------

      One of the limitations of the Packet Driver interface is that when
      it receives a packet it then calls a routine in the application
      asking for a buffer of a certain size.  Thus PKTMUX only knows how
      big the data is but has no idea of the contents other than that
      provided via the handle used in the call.  The generic Packet
      Driver code is actually provided with a pointer to the Type field
      which is also used to access the next byte but unfortunately the
      registers pointing to this are overwritten before PKTMUX is called.

      It is therefore reasonable to assume that somewhere within the
      Packet Driver program are held the first few bytes of the incoming
      packet and that they are valid at the point when PKTMUX is asked to
      provide a buffer in order to read this packet.  The /b option
      instructs PKTMUX to search the Packet Driver for this buffer, to
      copy it and then to test it against the data it actually obtains
      from the Packet Driver.  Should a consistent match be found then
      the Packet Driver buffer is used to filter out those packets that
      are of no interest and to send those packets for which there is in
      only one channel direct to the application.  This should therefore
      reduce the copying of data and in the case of IEEE802.3 support can
      dramatically reduce the overhead.  The gain in other cases is
      dependent on how much of the packet is found and hence how much of
      the protocol headers is available for analysis.



      How you locate the buffer is an interesting problem.  So far two
      types of Packet Driver implementations have been found.  One,
      exampled by NE2000, uses a fixed buffer every time so this is
      fairly easy to locate.  A second type uses a buffer pool and this
      is rather more difficult to track.  The BICC 16 bit card uses this
      technique and experimentation has shown that a segment register
      always points to the correct area of memory.  An algorithm that
      copes with both these cases has been implemented.  Testing with
      other cards will no doubt require it to be modified.  PKTSTATS
      gives an indication of where the algorithm is and the eventual
      outcome of the testing.

      Please note that this is a test implementation to evaluate the
      technique.  Once again PKTMUX is breaking all the rules.  How
      effective this option is depends on the size of buffer available.
      When the available buffer is 64 bytes you get the full benefit and
      for all cases there should be a significant improvement in
      performance.  Where the buffer is smaller then below 48 bytes the
      benefits tail off considerably. However if you are using IEEE802.3
      then the /b option avoids the copying of all packets not for
      this address so gives a significant reduction in overheads.


      7.11 Novell Protocol Support
      ----------------------------

      PKTMUX has been tested satisfactorily with Novell Netware using
      their Type 8137 protocol.  It has not been tested with the 802.3
      varient but this protocol will probably work provided the -n option
      is given to the Packet Driver as shown in the examples section.
      Further details are given in the next section.


      7.12 Packet Driver Protocol Filtering
      -------------------------------------

      An area fraught with problems is the use of a Packet Driver in a
      mixed protocol environment.  An example would be TCP/IP and Novell
      Netware using its 802.3 protocol.  The following gives details of
      the filtering algorithm used by the Packet Driver and applies to
      Versions 9 and 10 of the collection.  It has been gleaned by
      examining the code (mostly HEAD.ASM) provided to standardise the
      implementation of the Packet Driver and will only apply to drivers
      that use this code. Drivers from earlier versions of the collection
      may work differently.

      On receipt of a packet the Packet Driver examines the Packet Type
      field, which is the length field in IEEE 802.3, and checks if it is
      greater than 1500 bytes.  If so it is marked as Class 1 (Bluebook
      Ethernet) otherwise as Class 11 (IEEE802.3).



      If the -n (Novell) option has been given then Class 11 packets are
      checked to see if the DSAP/NSAP (the two bytes after the Packet
      Type/Length) is 0xFFFF.  If so then this is assumed to be a Novell
      802.3 packet and the Class is changed to 1 and the Packet Type is
      changed to 8137.  Class 1 packets are also checked and if a Packet
      Type of 8137 is found this is changed to 8138.  Similarily any
      packet sent by the Packet Driver that has a Type of 8137 is
      modified if the the -n option is given by replacing the Packet Type
      by the length thus making it IEEE802.3 conformant.  Thus the -n
      option dictates the protocol being sent to and expected from the
      Novell server and in both cases the Novell application is using
      8137.

      The next test if to search the list of Packet Types that have been
      Accessed by the application.  When such an Access is made the
      application specifies the Class and which Packet Type it wishes to
      receive.  The Packet Type is either a specific one such as 0800 for
      IP, 0806 for ARP or 8137 for Novell or it can be for All Types
      implying that the application wishes to receive all packets of the
      given Class - whether it actually does so is dependent on whether
      it was the first Access or not as indicated in the rules below.

      1. When an Access is made its Class and Packet Type are added as
      the next entry in the list unless it is a request for All Types.

      2. If a request for All Types is the first Access for that Class
      it is added as the next entry in the list.

      3. If the request for All Types is the second or subsequent Access
      for a Class then it is put at the end of the list and all
      subsequent Access entries added before it.

      4.  When the Packet Type list is searched to match an incoming
      packet the Class and Packet Type are checked against each entry
      until either a match is found or an All Types entry for any Class
      is found. Thus an All Types entry blocks any further entries in the
      table irrespective of their Class.

      The rules have been slightly simplified in that they describe
      the Class 1 case where the Packet Type is fixed at two bytes.
      For Class 11 there is the likelyhood of longer Packet Types since
      this now selects on the DSAP/NSAP and following bytes so
      complications arise when different lengths are specified. Should
      the shorter be a subset of a longer Type then the former takes
      precedence and the latter Access is rejected.

      These rules have several interesting consequences for programs,
      such as PC-NFS v3.0 (actually is the PKTD.SYS v3.0.2 program) and
      LLCPKT, which ask for All Types, and these are best illustrated by
      examples.  Consider the case of PC-NFS 3.0 loaded first.  As it
      asks for All Types of Class 1 then no other application
      irrespective of its Class will work alongside it.

      The second case is where PC-NFS is not the first application to
      be loaded.  If any Access was for the IP or ARP Packet Types then
      PC-NFS would not work since it needs to receive these Types.
      However if the first Access was for the Novell Packet Type 8137
      then PC-NFS would run alongside it.



      Note that the version of PKTD.SYS for PC-NFS v3.5 and later stopped
      asking for All Types so the problem effectively goes away and it
      can be run alongside Novell. But note that PC-NFS must be loaded
      before Novell for other reasons.

      Tests have also been carried out on Version 5 Packet Drivers and
      suggest that they will accept just one All Types Access or several
      specific Accesses but will not accept any combination of the two.
      The official BICC card driver, MBDNDPD, is based on this version.
      This card's Version 10 driver, named ISOLINK, is probably a much
      better bet.





      8. Problem Solving
      ==================

      This section attempts to suggest how problems with PKTMUX should be
      tackled. It is worthwhile reading the meaning of the various
      options and also the Technical Description above in order to
      ascertain if your problem and its solution is documented therein.
      Also the section on Bugs/Features and Problem Programs should be
      consulted.

      One of the biggest difficulties with PKTMUX is sorting out why
      something is not working properly.  To assist in this the utility
      PKTSTATS is provided which, when used with the /a option, gives
      details of what PKTMUX is up to and its various counts.  Any count
      whose name is in CAPITAL letters indicates data being lost or
      discarded because there is a problem and the following attempts to
      explain what they mean.  Note that such counts are usually only
      displayed when they have a value so their absence indicates all
      should be well.

      The first class of problems is where PKTMUX simply does not work
      with an application.  The first test is to run the application on
      its own having loaded PKTMUX with the /x option.  Normally in this
      situation PKTMUX would pass data direct to the application but with
      the /x option (multiplex) it copies data to its buffers and uses
      its multiplexing facilities thus checking if they can cope with the
      application.  If this fails then the application probably has some
      quirk that confuses PKTMUX.  If it is a standard application that
      works elsewhere then you may have a networking set up that PKTMUX
      cannot cope with.

      A second test is to add the /c (copy) option to each PKTDRV -
      PKTSTATS will show /TX_Copy for that channel.  This causes it to
      copy the data sent to the network into its own buffers and this has
      been known to cure problems related to the use of upper and/or
      EMS/XMS memory.

      Where an application works with PKTMUX as above but not in
      conjunction with other applications then it is worth trying
      different combinations and seeing what does and does not work.
      This may isolate one application as being the problem or show a
      certain loading order to be the cause.  Possible reasons are that a
      listener for a well known port is being usurped by another
      application (see PKTDRV /l option) or that one application simply
      prevents any other from running.  Check the Bugs/Features and
      Problem Programs section for any indication of problems.  It is
      also worthwhile checking if anyone else has a similar problem.

      Another class of problems is where PKTDRV is marked Busy when it
      should be Free or there are no Free PKTMUX channels.  This is
      usually due to applications failing in some manner and the means of
      recovery are described in the Channel Management part of the
      Technical Description section.



      The final, and probably the largest, class of problems is where
      everything works for a while then things start going wrong. Using
      PKTSTATS can give an indication of the cause but in general it is
      only those cases where the problem can be reproduced that a
      solution can be found with any degree of certainty. Note that
      PKTMUX depends on probability for its successfull working and when
      the odds are wrong it will fail for no apparent reason. However for
      regular failures the suggestions below may help.

      If the /b option is in use on PKTMUX it should be removed to see if
      this is the cause.

      If you are running under a control program such as Windows 3 or
      DESQview then check that the application is getting a sufficient
      percentage of the processor especially if the application starts
      failing when running in the background.  For Windows 3 a Background
      Priority of anything less than 50 can lead to problems and check
      that Execution in the Background is enabled. Also check that
      applications running in a DOS box have their own PKTDRV and are not
      using one loaded before the control program. This is shown by
      PKTSTATS and the PKTDRV entry at the start should have a /Win or
      /DV against it. If it has /DOS_to_Window then you are using a
      PKTDRV loaded before the control program and this should only be
      the case for applications that run under the control program such
      as WINQVT under Windows 3.

      A general technique is to run PKTSTATS /a and note the various
      counts.  Then run the application(s) that cause the failure and
      subsequently run PKTSTATS /a again and note which counts have
      increased.  This could give a clue about whats going wrong as
      detailed below.

      A possible reason for an application not working properly is that
      it, or PKTMUX, has run out of buffers with which to receive data.
      This is especially prevalent under a control program such as
      Windows where applications do not get enough CPU time to process
      their data.  Details of buffer usage are given in the "Buffers:"
      table and for the case of PKTMUX running out of buffers the count
      "PKTMUX NO BUFFER" is given in the "Recv ignored reasons" line.
      Increasing the number of buffers used via the /1 to /9 options on
      PKTMUX should solve this one.

      Detecting that the application is running out of buffers is more
      difficult since PKTMUX may not be able to deliver the data for a
      variety of reasons.  This can be isolated by running the
      application on its own over PKTMUX (without the /x option).  As it
      has only one channel operative PKTMUX just passes all calls
      directly to the application.  Any refusal by an application to
      supply a buffer causes PKTMUX to copy the data into its own
      buffers.  This is shown in the Copied count on the "Recv total"
      line and and in the "Recv copy reasons" line.  The PKTDRV channel
      counts also show the copied count for each channel.  The only
      solution is to increase the applications buffers if this is
      possible.



      When PKTMUX has more than one channel Busy, and has to wait to pass
      received data to an application, this is also recorded in the
      PKTDRV table.  The wait reason is either no buffer available from
      application (Buff) or, under Windows 3 or DESQview only, the
      application was not in memory (App).  For the Buff case if the /d
      option is given then the data is discarded and the "Dropped" counts
      increamented.  The App case is especially prevalent for background
      processes paticularily when a foreground process requires a lot of
      CPU.  When it has to wait PKTMUX has to decide whether to try again
      later or discard the buffer.  The latter is only done when PKTMUX
      has several channels that are actually moving data at the same time
      and it has insufficient buffers to meet all their demands.  The
      "LOST" count in the "PKTDRV channels:" table would be incremented
      in this instance and again increasing the number of PKTMUX and/or
      application buffers is a possible solution.  The count in the
      "Queues" section "LOST DUE TO APPLICATION ....." sums this total
      for all channels.  It may be that, especially under Windows 3 or
      DESQview, the PC has simply not enough horsepower to cope with the
      communications load as well as any processing in progress at the
      same time.  Thus the application(s) are not processing the received
      data fast enough to cope with the incoming rate.  Alternatively it
      may be an application, such as TRUMPET, that refuses to accept
      packets when it knows it is not expecting data.  Note that the /d
      option can significantly increase this count since packets are
      throw away at the first refusal.

      Another reason that data may be discarded is when there is no
      listener for the service that is being requested.  The count "NO
      LISTENER" is incremented in the "Recv ignored reasons" list.  There
      are several possible reasons for this but in general it is because
      the /l and /!l options on PKTDRV calls dont leave a suitable
      listener.  Note that this count will not be incremented if there is
      a listener available but it does not support the service requested.
      In this case an application that supports the service must be run
      with a PKTDRV that routes requests for the service to it by using
      the /l or /!l options.

      A final reason for discarding data is when an IP Fragment arrives
      out of order.  If it arrives before the first fragment then PKTMUX
      has no way of knowing to which channel it belongs and so discards
      it and increments the count "NO FRAGMENT" in the "Recv ignored
      reasons" list. The subsequent retry should overcome this problem
      provided that this time the first fragment arrives first.





      9. Bugs/Features and Problem Programs
      =====================================

      The following list of situations that need special action.  It is
      based upon limited experience so only covers a few cases at
      present.

      The 16 bit BICC ethernet cards require the /c option on PKTDRV
      when running under a control program and dont work with WINPKT.
      The /c is not required when under DOS but is needed when a
      protocol stack such as PCTCP is run under DOS for a Windows 3
      application such as Vista eXceed X Windows.

      When the X Window server Vista eXceed is running over PCTCP it
      must have enough buffers allocated via the ETHDRV command otherwise
      the call will be reset at intervals and thus fail. An ETHDRV call
      similar to the following is recommended:

         ethdrv -t 10 -p 20

      Further details are given the Vista eXceed and PCTCP manuals.  It
      may also be necessary to increase the PKTMUX buffer allocation when
      using this or other X Windows servers.

      PKTMUX will not work with the packet driver version of Novell IPX
      if the PKTDRV is using Interrupt 64. This is because Interrupt 64
      is a Novell API and so from v1.1 onwards it is not allocated by
      default.

      IEEE802.3 support can give problems with other protocols due to the
      overheads it imposes. In particular Novell running over Type 8137
      protocol has been found to crash in this mode.

      PKTMUX tends to operate a lot with interrupts disabled. This may
      cause problems with time critical communications methods such as
      asynchronous links using SLIP.

      TRUMPET refuses to accept packets when it is waiting for user input
      and expects no more data.  This can cause PKTMUX to run out of
      buffers under heavy loading.  It is recommended that the /d option
      be added to the PKTDRV used by TRUMPET.

      When PC-NFS is in use alongside PCTCP then a TSR, such as the MOS2
      3270 emulator, is unable to run when the PCTCP FTP program is
      waiting for a command. The problem does not occur with the CUTCP
      FTP so it appears to be related to the wait loop used by the PCTCP
      FTP when waiting for a command.





      10. Differences in PKTMUX versions
      ==================================


      10.1 Version 1.0
      ----------------

      First release to prove that the techniques worked.  Note this
      version does not support IP Fragmentation.


      10.2 Version 1.0a
      -----------------

      PKTMUX now checks that it is loading on top of a real Packet Driver
      and aborts if it finds its actually a PKTDRV.


      10.3 Version 1.1
      ----------------

      The programs from this version must not be mixed with those from
      version 1.0 as they are incompatible.

      In searching for a Packet Driver PKTMUX now checks the interrupts
      to see if PKTMUX or PKTDRV is already loaded and aborts if one is.
      Similarily if the Packet Driver interrupt is specified this is
      checked to see if it is a real Packet Driver.  This is to prevent
      multiple loadings of the system.  The option /o (override) has
      been added to PKTMUX to override this restriction.

      PKTMUX now starts by default with 2 channels.

      PKTDRV options /f and /!f have been added to force a PKTDRV to the
      Free or Busy state.  The PKTSTATS output has been changed to
      reflect this.

      PKTDRV no longer uses Interrupt 64 by default as this clashes with
      a Novell API.

      IP Fragmentation was not supported in previous versions.  It is now
      supported within limitations (see Technical Description).

      The buffer management system has been improved especially with
      regard to discarding unwanted packets. The option /d (drop) has
      been added to tell PKTMUX to drop all packets for which the
      application has no buffer rather than keeping them until the
      application has space. The same option is available on PKTDRV which
      works on a per channel basis. The number base of buffers has been
      also been increased in some cases.

      A bug in the Packet Driver handle mapping when PC-NFS was in use
      has been fixed as has one in the area of duplicate handles.

      A bug in the mapping of ICMP packets onto channels has been fixed.
      The bug caused ICMP packets containing IP data to be sent all
      channels.




      PKTMUX v1.0 used a time out mechanism to determine whether a PKTDRV
      and its application had been forcably terminated under a Windows or
      DESQview environment.  Unfortunately this mechanism was also
      triggered when the window was Selected under Windows 3.0 for
      actions such as cut and paste and caused the channel to be closed
      down.  This has been changed in v1.1 so that in these circumstances
      a channel will not be closed down.  The option /r has been added to
      PKTMUX to reset such channels otherwise they are permanently busy
      and there is no PKTDRV to reset them.  A third parameter has also
      been added to PKTMUX to reset such channels after a given time.

      ARP Request Broadcasts are now sent to all channels.  The /la
      option is therefore no longer needed.  The handling of Broadcast
      packets has also been improved so that only those ARP requests that
      are not for this address are discarded.

      BOOTP did not work for second and subsequent channels because it
      replies on a well known port and this only went to the first
      listener. This has now been changed and the response is sent to
      originator of the BOOTP provided no other channel has done a BOOTP
      in between. If this occurs then the timeout and retry mechanisms
      should recover the situation.

      The problem solving section has been improved and the /x option
      (multiplex) added to PKTMUX to assist this process.


      10.4 Version 1.2
      ----------------

      The maximum number of channels has been increased to 8 in order to
      improve the flexibility under Windows 3. If a Channel is in a timed
      out state then further channels can still be opened without
      reaching the maximum.

      The /q, /v, /e and PKTDRV /n options have been added and should
      enable a BAT file to work out the current state and load programs
      as required and this is illustrated by examples. Details of the
      options follows.

      The option /n on PKTDRV only loads PKTDRV if it is needed, that is
      if there is not already a Free one available, and reports the
      result via the DOS ERRORLEVEL.

      The option /q has been introduced on PKTDRV, PKTMUX and PKTSTATS in
      order to query the current state and returns the reply in text and
      the DOS ERRORLEVEL.  PKTSTATS indicates the presence of a Packet
      Driver, PKTMUX and PKTDRV (Free or Busy).  PKTDRV and PKTMUX return
      the state of their own program.

      The /v option causes the DOS Environment variable PKT_INT to be set
      to the hexadecimal value of the interrupt used or found by PKTDRV,
      PKTMUX or PKTSTATS when executing a command.




      The /e option extends the search under a control program to outside
      the DOS session and helps in determining whether a PKTDRV is
      running within the DOS session or not.

      The repeatable /s (silent) option has been introduced to reduce the
      output from PKTMUX, PKTDRV and PKTSTATS.  /sss inhibits all output,
      /ss all but errors and /s lets through warnings as well.

      The /b option to reduce packet copying by trying to locate the data
      in the Packet Driver has been added.  This can may give improved
      performance which in the case of IEEE 802.3 can be dramatic.  This
      is a test implementation for evaluation purposes.

      Support for a channel using IEEE 802.3 over Packet Driver Class 1
      is now included via the /i option on both PKTMUX and PKTDRV.  This
      feature allows PKTMUX to support the RAL LLCPKT product instead of
      using LLCPKT2 and with the /b option can be very much more
      efficient.  This is a test implementation for evaluation purposes
      and, depending on feedback, a better implementation may be
      incorporated in a future release.

      A bug in PKTDRV whereby the /d option did not work has been fixed.

      A bug in PKTDRV and PKTMUX whereby they could not be run by
      LOADHIGH when there was a limited amount of upper memory has been
      fixed. A bug in correct allocation allocation of buffer memory in
      such circumstances has also been fixed.

      PKTDRV and PKTMUX now release all their file handles so frequent
      unloading does not cause you to run out.

      A bug which caused WINQVT to crash the PC if it was run twice has
      been cured. This fix should cure problems with any Windows
      application which uses a DOS TSR (PKTINT in the case of WINQVT) to
      interface it to a Packet Driver.

      The decision criteria for sending a packet direct to an application
      rather than copying it has been improved.

      The algorithm whereby packets held in the buffer queue were dropped
      after a certain time has been improved.  Packets are now held until
      the application requests them provided there are sufficient free
      buffers left. The numbers and sizes of buffers has also been
      revised in the light of experience.

      The filtering of broadcasts and especially ARP requests has been
      improved.

      Bugs in the handling of ICMP messages have been fixed.

      PKTMUX now copes with features in both NCSA and B&W software
      where unusual Access commands are made.

      PKTDRV actions on another PKTDRV such as /r, /u and /t are now
      checked under Windows and DESQview to see if they are being done on
      a PKTDRV that was loaded under DOS and refused if so.




      PKTSTATS output now gives more information especially that relevent
      to the effect of the /b option.


      10.5 Version 1.2a
      -----------------

      This fixes a bug in the /i (IEEE802.3) code which caused it to
      crash the PC.



      11. Support
      ===========

      PKTMUX is supplied free and is supported, within the limits of its
      specification, for all users at RAL on IBM PC and PS/2 computers
      and near clones.  Note that support is confined to bugs in the
      programs and clarification in the documentation of the systems
      limitations.

      Users outside RAL are requested in the first instance to obtain
      copies and help from their normal support sources.

      Academic user support organisations may seek help from RAL but the
      latter will only be given on a 'best endeavours' basis.

      There is no support for other organisations other than by private
      arrangement with the author.

      Updates of the software may be file transferred from the binary
      file PKTMUXxx EXE (xx being version number without a point -
      currently 12) on the RAL IBM mainframe (UK.AC.RL.IB on JANET,
      IB.RL.AC.UK on the Internet) disc PCSOFT 192.  Be warned that the
      IBM file and disc naming format uses a space between the parts of a
      name (eg PKTMUX12 EXE and PCSOFT 192) when they are accessed by a
      user logged into the machine and this is replaced by another
      character, usually a full stop (.), for external access such as FTP
      (eg PKTMUX12.EXE and PCSOFT.192).  Thus from the Internet an
      Anonymous FTP user should CD to PCSOFT.192 and binary GET
      PKTMUX12.EXE.  Executing the file will produce the program and
      documentation.

      Bug reports or problems should be reported, ideally by email, to
      Graham Robinson:

      Via JANET    : GWR@UK.AC.RL.IB         G W Robinson
      Via Internet : GWR@IB.RL.AC.UK         Atlas Centre
      UK Telephone : 0235 44 5636 or 6391    Rutherford Appleton Laboratory
      International: +44 235 44 5636         Chilton, Didcot
                                             Oxon,OX11 0QX,UK

      12. References
      ==============

      The RAL LOADSYS system version 1.4 is held in file LOAD14 EXE on
      PCSOFT 192 as detailed above. It is a loader/unloader for both
      programs and device drivers.

      The RAL LLCPKT and LLCPKT2 systems are held together in file
      LLCPKTS EXE on PCSOFT 192.  They map the BICC MPS ethernet
      interface onto a Packet Driver and are only of use to users of the
      Rainbow software.

      The RAL MOS2 IBM 3270 emulator version 2.3 is held in files MOS23
      EXE, MOS23X EXE and MOS23Y EXE on PCSOFT 192.  This TSR provides
      IBM 3270 emulation, EEHLLAPI and GDDM-PCLK support over
      asynchronous and ethernet communications.