**************************************************
               *                                                *
               *                    S F G R                     *
               *                    -------                     *
               *                                                *
               *         SCREEN FORMAT GENERATOR PROGRAM        *
               *                  FOR CP/M-80                   *
               *                                                *
               *                 VERSION  1.00                  *
               *                                                *
               *       Copyright (c) 1986  Harris Landsberg     *
               *                                                *
               *                Harris Landsberg                *
               *              1350 East 5th Street              *
               *                   Suite 1-J                    *
               *            Brooklyn, New York 11230            *
               *                                                *
               *                 1-718-951-7075                 *
               *                                                *
               **************************************************


                                   COPYRIGHT
                                   =========

          No part of this  documentation, software system, source  code  or
     technical information used in  this system may be sold,  either  stand
     alone or as part of another package, without the written permission of
     the author. Object produced through the program source code written by
     the user  may be distributed  as the writer pleases,  but  the  author
     requests a copy as a thankful gesture for program use.
          It is presently intended that software may be shared freely,  but
     the author requests a modest donation of $10.00 if you  find it useful
     in any way. Those who make a contribution will be  entitled to support
     and software updates if any should arise.
          The author reserves the  right to later repackage  this  software
     system for  sale with  other software. Any  alterations  made  to  the
     software, source code or  documentation should be sent to  the  author
     for final approval. This is done to keep the integrity  and quality of
     the software at the standard the author deems fit.

                                LIMITED WARRANTY
                                ================

          The author  warrants this product  to run under CP/M  2.2  on  an
     Epson QX-10/16 with Televideo  920 terminal emulation.  Every  attempt
     will be made  to isolate terminal specific  instruction,  and  provide
     either an installation program or  patch instructions. See  applicable
     documentation and technical information for further reference.
          No other warranties are expressed or implied including warranties
     of merchantibility, fitness for a particular purpose. Nothing in  this
     statement shall be  construed as a written  statement  guarantee.  You
     have specific legal rights, but that is only if you make the requested
     contribution of $10.00. All rights reserved.














     Table of Contents                                            Page

       1.  Introduction . . . . . . . . . . . . . . . . . . . . .    3
       2.  Screen Specifications. . . . . . . . . . . . . . . . .    4
       3.  Display Specifications . . . . . . . . . . . . . . . .    6
       4.  Running SFGR from CP/M-80. . . . . . . . . . . . . . .   11
       5.  Error Messages . . . . . . . . . . . . . . . . . . . .   12
       6.  Technical Information. . . . . . . . . . . . . . . . .   14
       7.  The User Support Concept . . . . . . . . . . . . . . .   16
       8.  Registration Form. . . . . . . . . . . . . . . . . . .   17













































                                       2








                                  Introduction
                                  ------------

          The SFGR Compiler is  intended to process  user-generated  screen
     format specifications and produce a display screen format object  file
     that can be loaded at  run-time by a program. SFGR is a utlity on  the
     IBM System 34/36 mini-computer systems and used primarily with the RPG
     language. It is also interfaced with Cobol and Basic on  those systems
     running under SSP, System Support Program.
          This version  is intended to  run under CP/M-80  version  2.2  or
     higher. It can  be interfaced with any  language to drive  the  screen
     displays, user  response,  and  input/output.  This  implimentaion  is
     System  34/36 compatible, with all examples provided tested under  the
     System 36 environment. Some restriction  apply and not all  attributes
     have been implimented. This document will point out such discrepencies
     where it is deemed appropiate.
          In addition  to generating  a  screen  object  format,  SFGR  can
     generate a listing, either to the screen, printer or file, listing the
     source specifications and diagnostic or informational messages for use
     with implimenting the screen format. These are:

          a) Output buffer description.
          b) Input buffer description.
          c) Indicators used.

          A utility program is provided called FVIEW that will page through
     a screen format file and display output constants with output variable
     as "*". The proper syntax  is FVIEW [d:]filename, with  file-extension
     assumed as ".FMT".




























                                       3








                             Screen Specifications
                             ----------------------

          The first record in  a display format specification is  a  screen
     format specification statement. This  control statement  provides  the
     necessary information to the support  program that is relavent to  the
     entire display screen. It sets up where the display screen  will start
     and for how may lines should be cleared prior to  its display. Also it
     identifies the allowable command key response allowed by the user, and
     the name to call this format screen.
          The following are the valid screen specification fields that  are
     implimented and their meaning.

     Sequence Number (Columns 1-5)

          Columns 1 through 5 may  contain record sequence information.  It
     is ignored by the SFGR  Compiler, but is listed when listing has  been
     requested. This field is not required.

     Form Type (Column 6)

          Column 6 must contain the character "S" to identify that  this is
     a screen specification. This is required field.

     Format Name (Coumns 7-14)

          This entry gives a unique name to the screen format that is being
     defined. Duplicate names in  the same source program are  invalid  and
     will be flagged by the SFGR Compiler. The first character  must not be
     blank, and blanks cannot be embedded within the name. The  format name
     can be  a combination  of any character  except ","  (comma)  and  "'"
     (quote). The format name must be 8 characters or less.  If there is an
     "*" in column 7 then that record is considered a comment.

     Start Line Number (Columns 17-18)

          The start line number  where the display will begin.  The  actual
     start line number  on which a field  begins is calcuated  through  the
     following equation:

                Actual Line # = Start Line # + Display Row # -1

          Entried allowed for start line number:

          Blank     Line 1 of the display screen is assumed as start.
          1-24      Specifies the line where the display is to begin.
          V         Variable start line defined by within program.

     Lines to Clear (Columns 19-20)

          Specifies the number of  lines to clear prior to  displaying  the
     screen format. Valid entries are between 0 and 24, with  blank assumed
     as entire screen (24 lines)




                                       4








     Lowercase (Column 21)

          Specifies whether all alphabetic characters will be displayed and
     sent to the user program in lowercase or uppercase. Allowable  entries
     are N (or blank)  for all alphabetic characters are  uppercase, and  Y
     for alphabetic letters can be sent in lowercase.

     Sound Alarm (Columns 25-26)

          Allow the bell to  sound prior to screen display.  Valid  entries
     are N (or blank) for the bell not to sound and Y for the bell cast its
     lovely sound. Also allowed are indicators (an internal switch that can
     be turned on  or off by the  user program) 01 through 99.  If a  valid
     indicator is on, the the bell will sound.

     Enable Function Keys (Column 28)

          Allow operator to use command keys to control program  operation.
     You use enable function keys  to allow command keys to be allowed.  If
     functions are not  enabled then all function  keys are  disabled.  The
     specific command keys to be enabled are defined in the key mask.

          Valid entries for enable function keys:

          Blank     All command keys are disabled. Key mask is ignored.
          Y         Command keys identified in key mask are enabled.
          N         Same as blank.
          R         Retain previous mask. Not implimented.

     Key Mask (Columns 64-79)

          The key mask  is a string of  letters that identify  the  command
     keys that  are enabled for  this screen. The key  mask must  begin  in
     column 64 and cannot  contain embedded blanks. Letters may  be put  in
     any order, though alphabetically would be easier to read.
          This SFGR  Compiler has  only  implimented  10  command  keys.  A
     command key is the ESC  character followed by a number from 1  through
     10. On System  34/36 machines there are  24 allowable  indicators.  An
     implimentation of SFGR in MS-DOS  by Lattice impliments only 10.  This
     version impliments only 10,  because in most applications  written  on
     System 34/36 only use the first 10 indicators.
          The alphabetic letters A through  J correspond to command keys  1
     through 10, respectively.

          Note: No  provision has  been  made  to  impliment  blink  cursor
     function, return input, erase  input fields and function  keys.  These
     were either deemed inappropriate for  CP/M-80 or lack of use by  users
     of the System 34/36 environment.









                                       5








                             Display Specifications
                             ----------------------

          The records that follow the screen specification are known as the
     display specifications. They define a  field on the display, and  each
     field must have its own record. A field can be  either constant output
     or variable input/output depending on how it is defined.

     Sequence Number (Columns 1-5)

          Columns 1 through 5 may  contain record sequence information.  It
     is ignored by the SFGR  Compiler, but is listed when listing has  been
     requested. This field is not required.

     Form Type (Column 6)

          Column 6 must contain the character "D" to identify that  this is
     a display specification. This is required field.

     Field Name (Columns 7-14)

          This entry specifies the name of the field being defined  and can
     have a maximum of 8 characters. It is used for  reference only and not
     included in  the screen object  format. There need not  be  any  match
     between the name given and  the actual name used in your program,  but
     it is  suggested, for debugging  purposes, that  they  are  identical.
          An asterisk in column 7 identified this record as comment record,
     except when this is a  continuation record. If the previous record  is
     an output constant and requires a continuation, and has the letter "X"
     in column 80, then the continuation line starts in column 7.

     Field Length (Column 15-18)

          Specifies the length of  the field. The field number  may be  any
     number from 1 to 1840. The value must be right-justified  with leading
     zeros allowed, but not required.
          This implimentation limits the length for output variables to 250
     positions. For input fields the maximum is 80 and cannot  cross screen
     line boundries. For output constant the maximum is 96 characters, with
     only one continuation line allowed  per field. This is sufficient  for
     most applications. Also  a maximum of 250  variable input  fields  are
     allowed per screen format.

     Line Number (Column 19-20)

          Specifies the number of  the line relative to the  start line  as
     defined in the screen specification statement. The actual  calculation
     was given by the start line definition. The actual line  number cannot
     exceed the  maximum lines for  the entire screen. The  value  must  be
     right-justified with leading zeros allowed, but not required.







                                       6








     Column Position (Column 21-22)

          Specifies the column number of  the first position in the  field.
     Valid numbers are  between 1 through 80.  It must  be  right-justified
     with leading zeros allowed, but not required.

     Output Data (Columns 23-24)

          If a "Y" is specified in column 23 and a "C" appears in column 56
     then the data  specified in columns 57  through 79,  and  continuation
     line if it applies, is  displayed. If a "C" does not appear in  column
     56 then the data to be displayed is taken from the output buffer.
          If a "N" is  specified in column 23 then  no output is  performed
     for this specification statement.
          If an indicator (from 01 through 99) is specified, then when that
     indicator is  set on,  then information  from  the  output  buffer  is
     displayed. If the indicator has not been set on, then  the data within
     the buffer for the field  length of position is not displayed but  the
     buffer pointer is advanced.
          If an output field  is also defined as an  input field, then  the
     data is moved into the  input buffer and displayed and can be  changed
     by the program user.

     Input Allowed (Column 26)

          This allowes whether this field is an input field. The  allowable
     type of data is defined in the data type entry.  Valid entries are "Y"
     or "N". The input buffer is allocated only for "Y" entries.

     Data Type (Column 27)

          This entry defines the  type of data that can  be entered for  an
     input field. This SFGR Compiler limits it to the following:

          B (or blank)   Can contain any valid typing character.
          N              Numeric data only. (0-9,.,-)

          All other types are  not implimented and will be  flagged by  the
     SFGR Compiler. We hope in  the future to impliment more data types  if
     there is a request for them. Here is a quick  list of extra data types
     available on a System  36: A - alphabetic only.  S - signed  numerical
     data. R - data from magnetic tape reader. Z -  cursor moves from right
     to left. D -  decimal data. K - Katakana   characters. E - mixture  of
     different characters.

     Adjust Fill (Column 31)

          If Z is specified then  information entered into this field  will
     be right-justified  and unused positions  will be  filled  with  zeros
     before exiting field. If B is specified then information entered  into
     this field will be right-justified and unused positions will be filled
     with blanks before exiting field. A field exit key must  be pressed to
     exit the field for it to take affect.




                                       7








     Position Cursor (Columns 32-33)

          This field is used to explicitly position the cursor. Usually the
     cursor is positioned at the first input field defined after the screen
     specifications, but with this entry you can change all that.  If there
     is more than one position cursor enabled at time of  display, then the
     cursor is positioned at the first field that has enable indicator.
          If a "Y" is specified in column 32, the cursor appears will start
     at this filed, unless other fields have prior have cursor  positioning
     enabled. A "N" (or blank), the cursor is not positioned in this field,
     unless it is the first input field defined after the "S" specification
     and no other fields have cursor positioning enabled.
          If an indicator (from 01 through 99) is specified, then when that
     indicator is set on, then the cursor will be positioned unless a prior
     field has cursor positioning  enabled. If the indicator has  not  been
     set on, then the cursor  won't be positioned unless this is the  first
     input field specified for that screen format.

     Controlled Field Exit (Column 35)

          If you specify "Y" for this field, then a field  exit key must be
     pressed to exit field. A  "+" will be used for  delete-to-end-of-field
     and justifying. TAB will be used for simple exit of field. The regular
     cursor keys will not be allowed, and once you come  to the end of this
     field, the cursor will not advance to the next field. A "N" (or blank)
     means a  field exit  can be  used (should be  used when  you  want  to
     justify input, especially numeric data) but is not required. Also, the
     cursor will advance to  next field when the position  of the  previous
     field has been entered.


     Auto Record Advance (Column 36)

          If you specify  "Y" for this field,  the entire screen  of  input
     will be returned when the  operator has either: a) completed the  last
     position of  the field  that does not  require a field  exit.  b)  has
     pressed the "+" key as field exit whether field requires field exit or
     not. A "N" (or blank) means after entering field the  cursor will then
     go to next field. Normally, a program requires the ENTER key key to be
     depressed for  input data  to be  returned to  a  program.  With  auto
     advance enabled the screen will  be returned without the need for  the
     ENTER key. Note: you can  bypass field with TAB to exit field and  not
     return input to program. The cursor keys can be used  too if the field
     is not control field exit enabled.

     Protect field (Column 37-38)

          If you  specify "Y" in  column 37, this field  will  be  bypassed
     whenever input is requested. If "N" (or blank) then normal  processing
     will take place for this field, meaning input allowed.
          If an indicator (from 01 through 99) is specified, then when that
     indicator is set on, then  the cursor bypass this field for input.  If
     the indicator has not been set on, then the field will not be bypassed
     when input is requsted for display format.



                                       8








     High Intensity (Columns 39-40)

          If you specify "Y" in column 39, this field will  be displayed in
     high intensity. If "N"  (or blank) then this field  will be  displayed
     with normal  intensity. If  an  indicator  (from  01  through  99)  is
     specified, then when that indicator is set on, then the  field will be
     displayed in high intensity. Otherwise, if the indicator has not  been
     set, then the field will be displayed in normal intensity.

     Blink Field (Columns 41-42)

          If you specify  "Y" in column 41,  this field will  be  displayed
     with blink attributes. If "N"  (or blank) the field will be  displayed
     in normal non-blink attributes. When an indicator (from 01 through 99)
     is specified, then when that indicator is set on, then  the field will
     be displayed blinking. Otherwise, if  the indicator has not been  set,
     then the field will not be blinking.

     Nondisplay Field (Columns 43-44)

          If you specify "Y" in column 43, this field will not be displayed
     on the screen. If an input field, characters will not  echo. If "N" or
     blank the field will be displayed in normal non-blink attributes. When
     an indicator  (from 01  through  99)  is  specified,  then  when  that
     indicator is  set on,  then the  field  will  be  displayed  blinking.
     Otherwise, if the indicator has not been set, then the  field will not
     be blinking.
          A note on mixing  screen attributes: If nondisplay  is  specified
     together with high intensity,  reverse image, or underline,  then  the
     field will be assumed as nondisplay.

     Reverse Image (Colum 45-46)

          If you specify "Y" in column 45, this field will  be displayed in
     reverse image. If "N" (or blank) the field will be displayed in normal
     attributes. When an indicator (from 01 through 99) is specified,  then
     when that indicator  is set on, then  the field will be  displayed  in
     reverse image. Otherwise, if the indicator has not been set,  then the
     field will not be in reverse image.

     Underline (Columns 47-48)

          If you specify  "Y" in column 47,  this field will  be  displayed
     with the underline atttribute. If "N" (or blank) then this  field will
     be displayed without underline. When an indicator (from 01 through 99)
     is specified, then when that indicator is set on, then  the field will
     be underlined. Otherwise, if the indicator has not been set,  then the
     field will not be without an underline.

     Column Separator (Column 49)

          Most computers cannot display column separators, so an  underline
     is usually substituted. If "Y" is specified then the column  separator
     attribute is used. If "N" (or blank) then it is not used.



                                       9








     Constant Type (Column 56)

          This field specifies whether  constant information is  output  or
     data is to be taken from the output buffer. If  "C" is specified, then
     constant data is assumed. An indicator cannot be used for  output data
     field if constant data  is used. (Nondisplay field should  be used  if
     you do not want to display on an indicator.)
          If column 56 is blank, the display record is an  output variable,
     even if constant data is specified in columns 57 through 79. This last
     statement makes this SFGR not entirely in conformity with SFGR  on the
     System 34/36. In most situations, you specify a "C" for  constant data
     even if columns 57-79 are not blank.

     Constant Data (Columns 57-79)

          This specifies the data  constant that is to be  displayed in  an
     output or input/output field. This is the actual constant data  and if
     longer than 23 characters it is continued on the next  record starting
     in column 7 and continues until column 79 of that record. If the field
     consists of all blanks, then all blanks should be typed in, especially
     when a continuation record is needed.

     Continuation (Column 80)

          If more than 23 characters of constant data is needed,  an "X" is
     placed in column 80 to indicate that the record is continued. Only one
     continuation record per field is allowed in this version. Positions  7
     through 79 of the next record contain the continuation data. And to be
     compatible with System 4/36 SFGR, comments should not follow a  record
     with an "X" in column 80.

     General Note:

          Unused columns within a record should be left blank, but will not
     be flagged  by this SFGR  Compiler. Also, try to  limit all  types  of
     lines to 80 characters. (132  character lines can be used safely,  but
     is not recommended.) For all  comments, please use an "*" in column  7
     for any record type  except a continuation record. The  SFGR  Compiler
     ignores such lines. Also, put comments after the screen  specification
     that are relevant to the screen format.

















                                       10








                           Running SFGR from CP/M-80
                           -------------------------

          Running the SFGR from command line is easy. All that is needed is
     compiler (SFGR.COM) and error  message file (SFGR.ERR). If  the  error
     message file is not on  the current disk, then errors will be  flagged
     without a display message. No  space is saved in not having the  error
     message file. There are three options that can be used for listing the
     source member. The listing includes the source with error flagging  at
     the line, output buffer description, input buffer description, and the
     indicators used. The switches are:

          no switch      no listing except for error to console.
          /S             listing to screen with everything.
          /P             same as above, but to the printer.
          /F             listing to file with ".LST" extension.

          The file extension of a screen format source is ".SCR".  The SFGR
     Compiler requires this  extension and cannot be  changed.  The  output
     format object file has a ".FMT" extension. The temporary file  has the
     standard ".$$$" extension, and will be renamed ".FMT" if no errors are
     found in the source  member. If an unsuccessful compile  occured,  the
     previous format object file is not deleted or changed in any way. This
     is nice when you blunder something so bad, and forgot to make a backup
     of the original source.
          Input source member,  Output object file, and  listing  file  are
     placed or found on the same drive. Current drive will  be used, unless
     you specify a diffent drive. User areas are not directly  supported in
     this compiler. Here is the proper syntax:

          SFGR [d:]filename [/x]

          Where d: is the drive  where the source is found and object  will
     be created. It is optional, defaulting to current drive. For  filename
     is a valid CP/M filename with an extension of ".EXT" (Must be left off
     or switches will be  ignored.). The /x is a  valid switch as  pictured
     above. Must be uppercase (CP/M  changes it to uppercase) and if it  is
     not valid it will be ignored. Usually use /S.
          After the compilation, a message of how many format screens  that
     are within the compiled member are displayed. A maximum of 250 screens
     are allowed for each source member. Also, the exact count  of how many
     bytes generated is displayed. On  disk, it will be written in  records
     of 128 bytes, the CP/M standard.
          The ".FMT" object file can be quickly viewed, paged by screen, to
     find it compiled normally by  using the FVIEW utility. It is a  simple
     program that will display constant output without extra attributes and
     variable output as a series  of "*". To run type: FVIEW  [d:]filename,
     and press ENTER to view next screen and ESC to end program.









                                       11








                              SFGR Error Messages
                              -------------------

          The following are the 15 error message that are used for the SFGR
     Compiler Version  1.00. These may  be edited to your  taste  with  the
     provided utility EDITERR. To run  this program type: EDITERR  [d:]SFGR
     where d: is optional  drive. Format of each record  is 64 byte  random
     record with zero  hex fill at end.  This error message editor  is  the
     same one provided with the SPL compiler package. If the  file SFGR.ERR
     is not found it will be created on the specified or current drive.
          This program can edit any  other file with ".ERR" extension  with
     the substitution of SFGR for a different file name. Entering 9999 will
     exit from this program.  See technical section for  possible  terminal
     specific code such as clear screen and cursor positioning.

          1) NO S SPECIFICATION PRIOR TO D SPECIFICATIONS

          You have forgotten to specify a screen specification record prior
     to the display specification. The SFGR Compiler must know what  screen
     format will receive the  display. The screen specification  names  the
     screen format, so it can be called by a program.

          2) INVALID SPECIFICATION, MUST BE EITHER S OR D

          You have specified in column  7 something other than a "S" for  a
     screen specification or "D" for a display specification. It must  also
     be in uppercase. Help specifications are not supported in this release
     of the SFGR Compiler.

          3) MUST SPECIFY INPUT/OUTPUT IN D SPECIFICATION

          You forgot to put a "Y" for input/output data or  did not specify
     an indicator for output. It must be uppercase. How is  SFGR suppose to
     know what you want to do if you don't tell it?

          4) FIELD OVERLAPS WITH A PREVIOUSLY DEFINED FIELD

          The current field overlaps with another field that was previously
     defined for the same  screen format. You may have  expanded the  field
     and did not realise  it overlapped or you forgot  to place the  screen
     specification statement properly.

          5) INVALID LINE NUMBER SPECIFIED IN COLUMN 19-20

          There are a maximum  of 24 lines on the  entire screen. You  must
     take into account the starting line number. So if you  display on line
     18 when starting line number is 10, then it will be invalid.

          6) INVALID COLUMN NUMBER SPECIFIED IN COLUMN 21-22

          Only supports columns 1 through  80. If columns 21-22 are  blank,
     then this error will occur. If greater than 80, too. Terminal that can
     display 132 characters are only supported to 80 column width.




                                       12








          7) INVALID FIELD LENGTH SPECIFIED IN COLUMN 15-18

          The usual cause is when columns 15 through 18 are left blank. The
     other cause if you  have an input field that  crosses from one  screen
     line to another. The final cause is if you specified  a number greater
     than 250 for output field.

          8) INVALID KEY MASK STRING SPECIFIED IN COLUMN 64-79

          Letters greater than "J" (command key 10) are not supported. Also
     they must be in uppercase.  Numbers 1 through 5 are function keys  and
     are not implimented in this version.

          9) EMBEDDED BLANKS OR BLANK FORMAT NAME IN COLUMN 7-14

          The format name must be one word without any blank preceeding it.
     If all blank  or blanks embedded then  you will see this  nasty.  Name
     must be blank padded on the right if less than 8 letters.

          10) INVALID START LINE NUMBER SPECIFIED IN COLUMN 17-18

          Either 0 entered, number greater than 24, or invalid letter.

          11) INVALID LINES TO CLEAR SPECIFIED IN COLUMN 19-20

          Can only clear up to:  (24 - start line + 1). Probable cause  was
     clearing of more than available lines.

          12) DUPLICATE FORMAT NAME SPECIFIED IN COLUMN 7-14

          The format name has appeared in a screen specification of a prior
     record. The format name must be unique within a member.

          13) UNIMPLIMENTED DATA TYPE, MUST BE EITHER N OR BLANK

          This version of SFGR limits you to only two types of data. You've
     specified a data type  which was not implimented or  is invalid.  Also
     the "N" or "B" must be in uppercase if specified.

          14) EXCEEDED THE MAXIMUM OF 250 INPUT FIELDS PER SCREEN

          SFGR cannot  handle more than  this without  overflow.  Also  the
     driver program is  index with a maximum  of 250 input field.  This  is
     only per format screen not  per format member. A theorectical  maximum
     of 62,500  input fields are  allowed per format member.  There  is  no
     limit for output specifications, however.

          15) INDICATOR CANNOT CONDITION OUTPUT FOR A CONSTANT

          Provided to keep System 34/36 compabibility.







                                       13








                             Technical Information
                             ---------------------

          The following information is provided for users to impliment SFGR
     format object code in any  language. It is preferable to impliment  it
     for RPG II (Report Program Generator), but I am not about to write one
     on the spur of the  moment. An implimentation of the driver will  soon
     be written in SPL (one of my other lanaguages) and  Modula-2. They may
     provided an easy way to modify for your own type  of screen. My screen
     responds to something close to Televideo 920. This is for  Epson QX-10
     and QX-16 machines and very close to a Kaypro.
          There are two commercially  known SFGR Compilers for the  IBM  PC
     family. One by Lattice,  and is packaged with their  RPG II  Compiler.
     The other  is by California  Software, which is  packaged  with  their
     development system of Baby/36.  Both generate SFGR code  that  appears
     quite different and are more System 34/36 compatible. Baby/36 will run
     nearly everything that runs  on an IBM System 34/36  (in color if  you
     have a color monitor, of course). Lattice to a lesser degree.
          For the FVIEW and EDITERR utilities the following is the possible
     terminal specific instructions: Clear screen  puts a 1AH character  to
     the screen. Cursor positioning puts an ESC "=" row+31 col+31. There is
     little or no space for  patch, since data area begins right after  the
     code area after loaded. Check with DDT.
          Some sample screen  members are provided to  provide a  means  of
     simple understanding the capabilities of  SFGR. Using FVIEW, you  will
     be able to see  what these screens would look  like in a program.  All
     will compile on a System 36 (some were downloaded) and, of course, can
     be compiled with the SFGR Compiler.
          The Object specification records may  change with version, so  if
     you write a driver, make it easily fixable to include  the changes. It
     will usually be additional bytes in the screen and/or display records,
     and possibly an attribute attatched to a pre-existing attribute  byte.
     It may seem hard  to write a driver, but  once written display  screen
     can be created by just calling an object file.
          If you are really  interested in SFGR, then I  must refer you  to
     the IBM manuals for the System 36 such as Screen  Display Manual using
     Screen Design Aid. There  may be other books on  the market that  deal
     with RPG II that also deal with the workstation file definitions. Such
     a book may presumably be more readable.


















                                       14








                       Screen Specification Object Record

          Bytes     Description of object byte
          -----     -------------------------------------------------------
              1     Always 0FFH to signify start of format record
            2-9     Format Screen Name, left justified blank-fill
                    If byte = 0FFH then no more screen formats.
             10     Start Line Number (00 = Variable Start Line)
             11     Lines to Clear (0-24 valid entry)
             12     Most Significant Bit - Lowercase (1=yes,0=no)
                    Others - Alarm (01-99 indic) (0=no,100=yes)
             13     Command keys 1-5 in the 5 Least Signif. Bits
             14     Command keys 6-10 in the 5 Least Signif. Bits

                      Display Specification Object Record

          Bytes     Description of object byte
          -----     -------------------------------------------------------
              1     Type (bit 0=output var,bit 1=input var,bit 2=constant)
              2     Row, actual row except if variable start line.
              3     Column on the Screen Line to start field.
              4     Length of field.
              5     Output indicator (0=no,01-99=indicator,1=yes)
              6     If alphabetic - (bit 0=0,bit 1=lowercase)
                    If numeric - (bit 0=1,bit 1=fill type)
                    (bit 2=control exit,bit 3=auto advance)
              7     High intensity (0=no,01-99=indicator,1=yes)
              8     Blink field (0=no,01-99=indicator,1=yes)
              9     Reverse image (0=no,01-99=indicator,1=yes)
             10     Most Significant Bit - Underline (1=yes,0=no)
                    Others - Column separators (01-99 indic) (0=no,100=yes)
             11     Nondisplay (0=no,01-99=indicator,1=yes)
             12     Position cursor (0=no,01-99=indicator,1=yes)
             13     Protect field (0=no,01-99=indicator,1=yes)
             14+    Data if output constant (upto 96 characters)






















                                       15








                     A word about user supported software:

          The user supported  software concept (sometimes  referred  to  as
     cheapware or freeware or shareware) is an attempt to provide  software
     at low cost. The cost of offering a new product  by conventional means
     is quite staggering, and hence dissuades many new sotware authors from
     developing and promoting their ideas and products. The User  supported
     software is an attempt to develop a somewhat new marketing channel and
     technique, where products can be introduced at low cost.
           If user supported software works,  then everyone who is part  of
     it will benefit from it. The user will benefit by  receiving a quality
     product at low cost,  and by being able to  "see what it really  does"
     before purchasing it. The author  benefits by being able to enter  the
     commercial software market without first needing large sum of cash  to
     pay all the overhead that is involved otherwise.
          But it can  only work with your  "USER" support. It is  not  just
     program package, but  about all user supported  software. If  you  are
     still using a program after a couple of weeks, then  it is means it is
     worth something to you, and you should send in a  contribution. A mere
     $10.00 is requested for this  programs use. If you register, you  will
     be entitled to "USER" support from the author.




































                                       16









                                   ORDER FORM



          Check which items you wish to support:

              (_) Noncommercial license for the use of SFGR.

              (_) Payment of $_____ is enclosed (checks please)





              _______________________________________________
              Name

              _______________________________________________


              _______________________________________________
              Address

              ______________________   ________  ____________
              City                     State     Zip


              Telephone Number

          Send this completed form to:

                                Harris Landsberg
                              1350 East 5th Street
                                   Suite 1-J
                            Brooklyn, New York 11230


          For a commercial  site license, please write  to the  author  for
     further arrangements.

















                                       17