MAKING ZCNFG OVERLAY FILES
                              Al Hawley


ZCNFG needs a configuration overlay file for each target program
that will be configured. The overlay files are by default recognized
by ZCNFG when the file extension is '.CFG' and the filname is the
same as that of the target program. If the name of the overlay is
included in the target program at offset 0DH from the start of the
program, then ZCNFG will use that name directly without mention on
the invoking command line. The structure of configuration overlays
is described in detail in ZCNFG.HLP. You should have it available
for reference when using this implementation note.

This memo describes a procedure by which configuration overlays
can be made with minimum effort and confusion. Carson Wilson has
contributed a file (ZCNFGMDL.ZZ0) which is an excellent description
of configuration overlays. You should study that file along with
this one; you may wish to use IT to make your first configuration
overlay. For multiple screens and a complex configuration, use of
the following techniques will save time and aggravation, however.
It is assumed that the target program contains configurable data 
within the first 256 bytes of the program (for ZCNFG13 and earlier
the limit is the first 128 bytes). 
You will need the following programming tools:

1. A text editor which can produce straight ASCII files. I use PMATE
or WordStar in non-document mode. Many others are satisfactory. Use
it to produce MENU and HELP SCREEEN images (.TXT files) and for
assembler source files.

2. A Relocating Macro Assembler and associated Linker. I used ZMAC
and ZML for the procedures given below. The SLR and Microsoft will
work with very few changes. Others can be used, but may require
some changes to pseudo-op names.

3. The TEXT2DB program, available from ZNODEs and other bulletin
boards. This program converts a .txt file to an assembler source
file of DB statements. MENU images require labels on some of these
DB statements where fields in the image are to be programatically
updated; TEXT2DB generates such labels according to your desires.

4. An alias, MCFG.COM, is provided in this library to generate
the final .CFG file. A similar alias can be written for use by
an assembler/linker other than ZMAC/ZML.

5. CNFGDEF.LIB which contains the Function and Macro definitions
required for the code in ZCCFG.

The file names given as examples are part of ZCNFGCFG.LBR, the
complete configuration overlay source for ZCNFG itself.

To make the overlay file, the following command is used:

	>MCFG ZCCFG ZCNFG

ZCCFG.SRC is the source file for the overlay and ZCNFG.CFG is
the file produced. The MCFG alias invokes ZMAC to assemble the
source file and then (if there are no errors) ZML to link the 
resulting REL file to make the final .CFG file. The structure of
ZCCFG is:

	<Program offset definitions>
	INCLUDE CNFGDEF		;ZCNFG related definitions
	rst	0		;first byte of code in the overlay
	dw	menu1		;required reference for relocation
menu1:	dw	menu1,menu1,........(etc. see ZCCFG.SRC)
case11:	<The CASE TABLE for the first menu screen>
scrn1:	INCLUDE ZCSCR1
help1:	INCLUDE ZCHLP1
	...
	<DATA structures used by CASE tables>
	end

If the configuration options are numerous enough to require
several menu screens, then menu1:, case11:, scrn1:, and help1:
are simply repeated for each screen with appropriate changes in
labels, of course. (See ZCNFG.HLP)

To make a configuration overlay, start with the Screen Image(s),
then make the CASE table(s), then the HELP files.

SCREEN Images

Use your editor to make the screen exactly as you want it to appear.
Fields in the image that change during operation of ZCNFG such as
'YES'/' NO' or a place for numbers should be filled in with some
visible character. I use 'zzz...' or the ASCII string that just fills
the field. These are fields destined to be marked for labeling by
TEXT2DB. There will be one such field for each configurable item
in the target program configuration block.

The last five lines of a menu screen are reserved for use by ZCNFG.
Thus, for a 24 line screen the menu itself must be 18 lines or less,
including blank lines at the top of the screen.

After you are satisfied with the screen layout, INSERT an accent 
character (`) before each such field. Then replace the dummy 
characters in each field with spaces. The accent character is the 
que that TEXT2DB uses to generate a label for that field. The
label generated is of the form AAAnnn, where AAA is alphabetic and
'nnn' is a decimal number. You specify the first label for TEXT2DB
to use; subsequent labels have the numeric part incremented so that
each generated label is unique. The command

	TEXT2DB ZCSCR1 .LIB /SSCR100

generates ZCSCR1.LIB from ZCSCR1.TXT. The labels in the output file
are SCR100:, SCR101:, etc. You will be using these labels when you
generate the CASE table in the next step. If there are many of them,
you may wish to make a printed copy of the .LIB file for reference.

CASE table

In this example, the Case Table is part of ZCCFG.SRC. If it is very
large or if there are several such tables (for multiple screens),
then you might wish to make an INCLUDE file of this one, too.

The case table is assembly source code prepared with a text editor.
The details of its structure are described in ZCNFG.HLP. You will be
filling in the argument list for one of the macros in CNFGDEF.LIB for
each entry in the case table. These arguments are mostly symbols which
are labels in the SCREEN (ZCSCR1.LIB), labels in the DATA area, 
symbolic offsets in the target program, and parameters that tell ZCNFG
what to do with the configuration data and screen field for each
configuration item. The symbols used for ZCNFG parameters are defined
in CNFGDEF.LIB. Detailed information for each field is in ZCNFG.HLP.

Two macros are provided which you can use to make Case Table records,
BITMAP and VECTOR. The only difference between them is the treatment
of the 6th bye of the record, 'bdata'. For function 0, this byte
specifies the bit to be toggled in a configuration byte. The bit to
be toggled corresponds to the bit that is set in bdata. The BITMAP
macro simply translates an easier-to-enter number from 0 to 7 into
a byte with exactly one bit set in the correct location. So, it is
best to use the BITMAP macro for function 0, and the VECTOR macro
for other functions. The use of tabs and spaces in the macro argument
list is useful to keep the Case Table entries formatted so you can
easily keep track of the identity of each argument; each argument type
has its own column. 

Construction of the Case Table(s) is the most exacting task you will
perform. Once you 'get the hang of it', it goes pretty fast.

The HELP screens

The files ZCHLP1.TXT and ZCHLP1.LIB are examples of the help screens
you include in the .CFG file for the user to reference during a
configuration session. There must be a help screen for each Menu,
even if it only contains a 'HELP not available' message.

A help file may be as long as you wish. ZCNFG displays the help text
with paging and a prompt on the bottom line of the screen. Each page
is 22 lines long (2 lines are reserved for the prompt). A colon (':')
as the first character on a line will force a new page. The colon is
not displayed by ZCNFG versions after v1.8, but will be displayed by
earlier versions (and ignored as a pageing signal). You can use this
function to avoid having paragraphs split between screens, and you 
can provide a space at the top of each screen. 

To generate the .lib file from the .txt file, use TEXT2DB. Since there
are no labels in the help file, the /S option is not needed. Here's
the command that generated ZCHLP1.LIB

	TEXT2DB ZCHLP1   .LIB

That's it. Now assemble and link!

-A tip about .TXT files-
Don't throw them away! When you want to make changes to the .CFG
file, you will save a lot of time by just modifying the old .TXT
file and regenerating the .LIB file!