***************************************************************************
** COPYRIGHT (C) MASSACHUSETTS INSTITUTE OF TECHNOLOGY AND HARVARD       **
** UNIVERSITY, BIOMEDICAL ENGINEERING CENTER 1977.  ALL RIGHTS RESERVED. **
***************************************************************************

FLOATING POINT
J. SACHS 2/2/77

FLOATING POINT IN ADDED TO STOIC BY LOADING THE FILE "FP".
SUBSEQUENT TO LOADING "FP", FLOATING POINT LITERALS ARE
RECOGNIZED BY STOIC, AND A SET OF FLOATING POINT WORDS ARE
DEFINED.  THE FORMAT OF FLOATING POINT NUMBERS IS AS
FOLLOWS:

	BYTE	CONTENTS	FORMAT

	0	SIGN		=0 FOR POSITIVE
				=80 HEX FOR NEGATIVE

	1	EXPONENT 	8-BIT 2'S COMPLEMENT

	2,3	FRACTION	UNSIGNED BINARY
				BINARY POINT IS JUST LEFT OF THE MSB

	WHEN A FLOATING POINT NUMBER IS ON THE STACK, THE SIGN/EXPONENT
WORD IS ON TOP, THE FRACTION IS AT TOP - 1.  PRECISION IS BETTER THAN 4 1/2
DECIMAL PLACES.  WHEN A FLOATING POINT NUMBER IS STORED IN MEMORY, THE
SIGN/EXPONENT WORD IS AT (ADDRESS), THE FRACTION IS AT (ADDRESS+2).

FLOATING POINT LITERALS ARE THE SAME AS INTEGER LITERALS EXCEPT THAT THEY
MAY INCLUDE A DECIMAL POINT AND MAY OPTIONALLY BE FOLLOWED BY AN "E"
FOLLOWED BY AN EXPONENT.  EMBEDDED SPACES WITHIN THE LITERAL ARE NOT ALLOWED.
FLOATING POINT LITERALS ARE ALWAYS DECIMAL.

EXAMPLES:

1.
2.0E-1
+12.345
-5.0E-3

THE FOLLOWING WORDS MAKE UP THE FLOATING POINT PACKAGE:

FCONSTANT	DEFINES A FLOATING POINT CONSTANT
FVARAIBLE	DEFINES A FLOATING POINT VARIABLE

EXAMPLES:

	2.71828 'E FCONSTANT
	0.0 'X FVARAIBLE

PI	A FLOATING POINT CONSTANT EQUAL TO 3.1416

F@	PUSHES THE FLOATING POINT NUMBER ADDRESSED BY THE TOP
	OF THE STACK.

F!	STORES THE FLOATING POINT NUMBER AT TOP - 1 AND TOP - 2
	AT THE ADDRESS AT TOP.

D2OVER	PUSH A COPY OF TOP-3,TOP-2

D3OVER	PUSH A COPY OF TOP-5,TOP-4

D2UNDER	STORE TOP-1,TOP AT TOP-5,TOP-4

D3UNDER	STORE TOP-1,TOP AT TOP-7,TOP-6

FMINUS	FLOATING POINT NEGATE

FABS	FLOATING POINT ABSOLUTE VALUE

F+	FLOATING POINT ADD

F-	FLOATING POINT SUBTRACT

F*	FLOATING POINT MULTIPLY

F/	FLOATING POINT DIVIDE

F+!	FLOATING POINT ADD TO MEMORY

FLOAT	CONVERT THE INTEGER AT TOP TO FLOATING POINT

INTEGER	TRUNCATE THE FLOATING POINT NUMBER AT TOP-1,TOP TO
	AN INTEGER.

FRAC	PUSH THE FRACTION PART OF THE FLOATING POINT NUMBER
	ON THE TOP OF THE STACK

FMOD	FLOATING POINT MOD FUNCTION.
	COMPUTED AT ARG2*FRAC(ARG1/ARG2)

FLTZ	FLOATING POINT LESS THAN ZERO
FLEZ	FLOATING POINT LESS THAN OR EQUAL TO ZERO
FGTZ	FLOATING POINT GREATER THAN ZERO
FGEZ	FLOATING POINT GREATER THAN OR EQUAL TO ZERO
FEQZ	FLOATING POINT EQUAL TO ZERO
FNEZ	FLOATING POINT NOT EQUAL TO ZERO

FLT	FLOATING POINT LESS THAN
FLE	FLOATING POINT LESS THAN OR EQUAL TO
FGT	FLOATING POINT GREATER THAN
FGE	FLOATING POINT GREATER THAN OR EQUAL TO
FEQ	FLOATING POINT EQUAL TO
FNE	FLOATING POINT NOT EQUAL TO

FSQRT	FLOATING POINT SQUARE ROOT
FSIN	FLOATING POINT SINE (ARGUMENT IN RADIANS)
FCOS	FLOATING POINT COSINE (ARGUMENT IN RADIANS)
FATAN	FLOATING POINT ARCTANGENT (SINGLE ARGUMENT, RESULT IN RADIANS)
FLN	FLOATING POINT LOG BASE E
FLOG2	FLOATING POINT LOG BASE 2
FLOG10	FLOATING POINT LOG BASE 10
FEXP	FLOATING POINT EXPONENTIAL BASE E
2.0**	FLOATING POINT EXPONENTIAL BASE 2
10.0**	FLOATING POINT EXPONENTIAL BASE 10

F=	FLOATING POINT E-FORMAT PRINT
F?	PRINT FLOATING POINT NUMBER ADDRESSED BY TOP OF STACK

FLITERAL
	ACCEPTS A STRING ARGUMENT AT TOP AND ATTEMPTS
	TO CONVERT THE STRING TO A FLOATING POINT NUMBER.
	IF SUCCESSFUL, A -1 IS LEFT AT TOP, AND THE VALUE IS
	RETURNED AT TOP - 1 AND TOP - 2.  IF NOT SUCCESSFUL,
	A ZERO IS RETURNED AT TOP.

<LSQ	INITIATE A LINEAR LEAST SQUARES FIT.

LSQ	ACCEPTS TWO FLOATING POINT NUMBERS, A Y COORDINATE AT TOP
	AND AN X COORDINATE BENEATH.  THIS POINT (X,Y) IS PROCESSED.

LSQ>	WHEN "LSQ" HAS BEEN CALLED FOR ALL INPUT POINTS, "LSQ>" IS
	CALLED, RETURNING THE SLOPE AND INTERCEPT OF THE LINEAR LEAST
	SQUARES FIT TO THE GIVEN POINTS.  (SLOPE RETURNED AT TOP,
	Y-INTERCEPT AT TOP - 1)

FRAND	RETURNS A RANDOM FLOATING POINT NUMBER UNIFORMLY DISTRIBUTED
	BETWEEN 0.0 AND 1.0.



***EOF***