TABLE OF CONTENTS

disassembler.library/--Background--
disassembler.library/FindStartPosition
disassembler.library/Disassemble


disassembler.library/--Background--	disassembler.library/--Background--

    PURPOSE

	The purpose of this library is to provide an easy to use and 
	powerful disassembler. It knows all MC68K processors starting with 
	the 68000 up to the 68060, FPU and MMU instructions.

	The code is MMU aware, i.e. won't try to access invalid or 
	non-available memory, and makes use of the mmu.library if it is 
	available. It will even work without the library, but it won't be 
	able to validate its accesses and might, therefore, access invalid 
	memory if the addresses passed in are incorrect.

	The library functions are interrupt and supervisor callable, 
	provided your functions - and the PutProc function passed in - is.


disassembler.library/Disassemble       disassembler.library/Disassemble

    NAME
	Disassemble     -   disassemble MC68K object code to assembler

    SYNOPSIS
	nextpc = Disassemble ( disdata );
	d0			a0

	APTR Disassemble ( struct DisData * );

    FUNCTION
	Disassembles the memory between the ds_From and ds_Upto fields
	writing the disassembled data out using the ds_PutProc function.
	The PC position is marked by a "*".

    INPUTS
	disdata     -   A structure specifying the details of the request.
			It has to be filled out like the following:

	struct DisData {
	    APTR	    ds_From;	
	    APTR	    ds_UpTo;    
	    APTR	    ds_PC;      
	    void	   *ds_PutProc; 
	    APTR	    ds_UserData;
	    APTR	    ds_UserBase;   
	    UWORD	   ds_Truncate;    
	    UWORD	   ds_reserved;   
	};

	ds_From is the memory location to start the disassembly from. This 
	*MUST* be an even address.
	ds_UpTo is the (exclusive) end of the memroy region to disassemble.

	ds_PC is a special address which is marked by an asterisk ("*") on
	disassembly. This feature can be used to mark the position of the
	PC.

	void *PutProc is actually a function pointer. It is not declared as
	such to avoid unnecessary casting between compilers. Your code is
	called like this:

	register d0 -   the ASCII code to print. Line ends are marked with a
			single line feed LF = 0x0a.
	register a1 -   the contents of the ds_UserData field of the structure
			above.
	register a3 -   ditto.
	register a4 -   the contents of ds_UserBase. This is most useful for
			passing the pointer to the data space when using C or
			other high level languages.

	On exit, the routine may pass an updated a3 register back to the 
	library which will be passed in a1 and a3 next time, similar to
	the exec RawDoFmt() function.

	ds_UserData is the contents of registers a1 and a3 upon calling your
	routine. They are for your private use.

	ds_UserBase is loaded to register a4 before calling the put procedure.
	Should be setup to be the _LinkerDB if the near data model is used.

	ds_Truncate is the maximal line length to output. If this field is,
	for example, set to 80, longer lines will be truncated by the library
	to fit on the screen. If set to zero, no truncation takes place.

	ds_reserved must be set to zero to support future extensions.


    RESULTS
	an updated pointer where the disassembly stopped. If you pass this
	pointer back in as "ds_From", the disassembler will automatically
	continue at the right place.

    NOTES
	this call will make use of the mmu.libary if available. It won't
	access illegal memory or I/O space, provided the mmu table is
	setup correctly.

	This routine is interrupt and supervisor callable, provided your
	provided bs_PutProc is. This makes this library function ideal for
	debugging tools and monitors.

    BUGS

    SEE ALSO
	exec.library/RawDoFmt(), libraries/disassembler.h


disassembler.library/FindStartPosition disassembler.library/FindStartPosition

    NAME
	FindStartPosition   -   find an anchor point for disassembly

    SYNOPSIS
	start = FindStartPosition ( pc , min , max );
	d0			    a0   d0    d1

	APTR FindStartPosition ( APTR , UWORD min , UWORD max );

    FUNCTION
	Given a PC address, this routine tries to find a useable address
	to start the disassembly from, in a way that the PC address is
	correctly included in the disassembly and that no, or as few illegal
	instructions as possible show up. The code in front of the PC is
	investigated, and a location between pc-min and pc-max is
	returned, with min<max. If no suitable address was found, the pc
	passed in is returned.

	This makes this function an "go backwards" disassembly tool. This 
	is usually problematic due to the CISC design of the MC68K, namely
	having instructions of various lengths.

    INPUTS
	pc      -   the anchor point. This is supposed to be known to be a
		    valid address with a valid instruction. This instruction
		    is guaranteed to show up in a disassembly started at the
		    resulting address.
	min     -   the minimum distance from the PC to start the search.
		    Note that this must be postive, it will be subtracted
		    from the "pc".
	max     -   the maximal distance where the search will stop. This is
		    again a positive number.

    RESULTS
	An address between pc-max and pc-min which, when used as start
	address for Disassemble(), will make the requested "pc" instruction
	part of the output stream.

    NOTES
	The purpose of this function is to find an anchor point for 
	disassembling code "around" a given location. Use, as first step,
	the desired location to this procedure, then start disassembling
	at the result, using about max*2 bytes.

    BUGS

    SEE ALSO
	Disassemble(), libraries/disassembler.h