TABLE OF CONTENTS

fpsp.resource/--Background--
fpsp.resource/FPSPMonadic
fpsp.resource/FPSPDyadic


fpsp.resource/--Background--		   fpsp.resource/--Background--

    PURPOSE

	This resource contains the emulation routines for FPU instructions
	which are non-native for the 68040 or the 68060 processor.
	This resource is - as all resources - not disk based. Instead, it
	is build by the 68040 or 68060.library on startup. The CPU driver
	libraries install the "FPSP" code as part of their initialization
	process, such that every non-impelemented FPU instruction will be
	emulated properly. However, this means that for every such 
	instruction, the CPU has to go thru exception processing, and will
	therefore stop multitasking when emulating a non-implemented in-
	struction. Calling the fpsp routines directly thru the new
	fpsp.resource will prevent this overhead and will gain some speed.
	
	A separate patch - the FastIEEE program - will patch the system
	math libraries to make use of this resource.	

	The fpsp.resource is re-entrant, interrupt-callable code. The
	resource offers only two functions which emulate monadic resp.
	dyadic functions of the 68881/68882 FPU on a 68040 FPU.

	Currently, only the V40 68040.library builds and provides this
	resource, future versions of the 68060.library might offer this
	as well.

	These functions are designed to be stub functions for assembly
	language, they are not designed to be callable from C or any
	other high-level language. Typical applications would call these
	routines indirectly thru a link library which provides all
	requires parameters. Direct calling from within application
	programs is not desired.

	Moreover, the FPSP routines *do not* generate FPU exceptions them-
	selves for speed reasons. If this is desired, the calling routine 
	has to check the fpcr and the fpsr FPU registers manually and
	has to generate the exceptions itself.


fpsp.resource/FPSPMonadic		      fpsp.resource/FPSPMonadic

    NAME
	FPSPMonadic     -   emulate a monadic 68881/68882 instruction

    SYNOPSIS
	storeflag = FPSPMonadic ( opword, operand );
	d0			   d0      fp0

	BYTE FPUControl ( UWORD , IEEEExtended );

    FUNCTION
	This function emulates the 68881/68882 monadic instruction 
	passed in in register d0, and performs the desired mathematical
	operation on FP0. It returns the result in the FPU register FP0 
	and FP1.

    INPUTS
	opword      -   The extension word of a valid 68881/68882 
			instruction. Valid extension words are found in
			the motorola family guide or the 68881/68882
			manual.
			Note that this is actually the SECOND (!) opword
			of the 68881/68882 instruction.
			The bits of the opword have to be specified as
			follows:

			Bits 15 and 13 must be cleared. The fpsp.resource
			does not emulate FPU control instructions.
			It emulates all transcendential math instructions,
			and "fint" and "fintrz". Even though these two
			instructions are "native" for the 68060, calling
			the resource with these opwords works correctly.


			R/M:    Source operand mode,    bit 14.
				Must be set to zero.
			Source: Source specifier,       bits 12 to 10.
				Must be set to zero.
			Dest:   Destination specifier,  bits 9 to 7.
				Must be set to zero.
			Inst:   Instruction field,      bits 5 to 0.
				Must be filled with the opcode of the
				desired instruction, see the motorola
				documents for the list. For the special
				case of FPSINCOS, the FPC field, bits
				2 to 0, has to be set to 001 to encode
				FP1 as secondary result register.

	operand     -   A valid IEEE extended precision number as argument
			to the function to be performed.

	Secondary inputs are delivered in the FPU registers FPCR and FPSR,
	namely to select the rounding precision and the behaiviour in case
	of invalid arguments or infinite results.

    RESULTS
	storeflag   -   This is set to 0 in case the FPSP routine could
			generate a result. THIS DOES NOT MEAN that the
			arguments are valid. In case all exceptions are
			disabled, the storeflag will always be returned as
			zero, but the result might be infinite or a NAN.

	Secondary results are delivered in the FPU registers FP0, FP1 and
	FPSR.

	FP0 contains the (primary) result of the 68881/68882 instruction
	in case the storeflag is 0. *IT MIGHT WELL BE A NAN OR AN INF*

	In case the storeflag is non-zero, FP0 is undefined and the FPSP
	routines indicate that an exception should be generated by the
	caller. This happens only if an exception condition was detected
	and the corresponding exception has been enabled in the FPCR 
	passed in. In all other cases a NAN or a INF will be returned
	and the storeflag will indicate a valid result.

	FP1 contains a secondary result, if any. The only case were FP1
	is used is the FSINCOS instruction where the sine is returned in
	FP0 and the cosine in FP1. Otherwise undefined.

	FPSR contains the FPU status similar to what a real 68881/68882 
	would have returned. 

    NOTES
	This function should not be called directly. It should either be
	called by the system math libraries, or by compiler link libaries.

	Note that a non-zero store flag indicates that an exception 
	condition was detected. NOTE THAT THE FPSP CODE DOES NOT CAUSE
	AN EXCEPTION ITSELF. It is the responsibility of the caller to
	check the FPSR, the FPCR and the storeflag to generate this
	exception itself, if desireable. In case the storeflag is non-
	zero, no useful result is returned in FP0 or FP1.

	Useful instruction opwords can be found in the motorola 
	documentation, either the MC68K family guide, or in the 68881/
	68882 manual.

	This function does not require a6 to be loaded with the FPSP 
	resource base. It is interrupt-callable.

    BUGS

    SEE ALSO
	libraries/68040.h, FPSPDyadic,
	the Motorola 68881/68882 manual, the MC68K family guide.


fpsp.resource/FPSPDyadic		       fpsp.resource/FPSPDyadic

    NAME
	FPSPDyadic      -   emulate a dyadic 68881/68882 instruction

    SYNOPSIS
	storeflag = FPSPMonadic ( opword, operand1, operand2 );
	d0			   d0      fp0     fp1

	BYTE FPUControl ( UWORD , IEEEExtended , IEEEExtended );

    FUNCTION
	This function emulates the 68881/68882 dyadic instruction 
	passed in in register d0, and performs the desired mathematical
	operation on FP0 and FP1. It returns the result in the FPU 
	register FP0.

    INPUTS
	opword      -   The extension word of a valid 68881/68882 
			instruction. Valid extension words are found in
			the motorola family guide or the 68881/68882
			manual.
			Note that this is actually the SECOND (!) opword
			of the 68881/68882 instruction.
			The bits of the opword have to be specified as
			follows:

			Bits 15 and 13 must be cleared. The fpsp.resource
			does not emulate FPU control instructions.
			It emulates all transcendential math instructions,
			and "fint" and "fintrz". Even though these two
			instructions are "native" for the 68060, calling
			the resource with these opwords works correctly.

			R/M:    Source operand mode,    bit 14.
				Must be set to zero.
			Source: Source specifier,       bits 12 to 10.
				Must be set to zero.
			Dest:   Destination specifier,  bits 9 to 7.
				Must be set to zero.
			Inst:   Instruction field,      bits 5 to 0.
				Must be filled with the opcode of the
				desired instruction, see the motorola
				documents for the list. For the special
				case of FPSINCOS, the FPC field, bits
				2 to 0, has to be set to 001 to encode
				FP1 as secondary result register.

	operand1    -   A valid IEEE extended precision number as argument
			to the function to be performed. This is the source
			operand of dyadic instructions.

	operand2    -   The destination operand of the dyadic 68881/68882
			instructions.

	Secondary inputs are delivered in the FPU registers FPCR and FPSR,
	namely to select the rounding precision and the behaiviour in case
	of invalid arguments or infinite results.

    RESULTS
	storeflag   -   This is set to 0 in case the FPSP routine could
			generate a result. THIS DOES NOT MEAN that the
			arguments are valid. In case all exceptions are
			disabled, the storeflag will always be returned as
			zero, but the result might be infinite or a NAN.

	Secondary results are delivered in the FPU registers FP0, FP1 and
	FPSR.

	FP0 contains the (primary) result of the 68881/68882 instruction
	in case the storeflag is 0. *IT MIGHT WELL BE A NAN OR AN INF*

	In case the storeflag is non-zero, FP0 is undefined and the FPSP
	routines indicate that an exception should be generated by the
	caller. This happens only if an exception condition was detected
	and the corresponding exception has been enabled in the FPCR 
	passed in. In all other cases a NAN or a INF will be returned
	and the storeflag will indicate a valid result.

	FP1 contains a secondary result, if any. As there is currently no
	dyadic opcode with a secondary result, this register should be
	ignored.

	FPSR contains the FPU status similar to what a real 68881/68882 
	would have returned. 

    NOTES
	This function should not be called directly. It should either be
	called by the system math libraries, or by compiler link libaries.

	Note that a non-zero store flag indicates that an exception 
	condition was detected. NOTE THAT THE FPSP CODE DOES NOT CAUSE
	AN EXCEPTION ITSELF. It is the responsibility of the caller to
	check the FPSR, the FPCR and the storeflag to generate this
	exception itself, if desireable. In case the storeflag is non-
	zero, no useful result is returned in FP0 or FP1.

	Useful instruction opwords can be found in the motorola 
	documentation, either the MC68K family guide, or in the 68881/
	68882 manual.

	This function does not require a6 to be loaded with the FPSP 
	resource base. It is interrupt-callable.

    BUGS

    SEE ALSO
	libraries/68040.h, FPSPMonadic,
	the Motorola 68881/68882 manual, the MC68K family guide.