TABLE OF CONTENTS

pronet.device/--Overview--
pronet.device/CloseDevice
pronet.device/CMD_WRITE
pronet.device/OpenDevice
pronet.device/ReceivedData

pronet.device/--Overview--                         pronet.device/--Overview--

 >> GENERAL INFORMATION <<

 The device is able to handle several Units, which are defined in the
 `devs:pronet/.config' file. Each Unit corresponds to a certain driver
 and interface. The Units are subdivided into Ports, which are channels
 between two sides of one Unit. This way two application systems may work
 through the same connection without interfering each other.

 pronet.device is *not* a SANA-II compliant networking device, and it is not
 compatible to any other exec device, because it's got some very strange
 behaviour regarding incoming data.  Sometimes it is useful, sometimes it is
 not, but I will not change this anyway:  CMD_READ is not supported, instead
 of that, when opening the device, you specify a MsgPort to which all
 incoming data will be sent automatically, if you want it or not!

 pronet.device v37 is incompatible to ProNET applications written
 earlier, see below. I'm sorry for that, but I've not heard from people
 using this device anyway ;-)

 >> ERROR CODES <<

 pronet.device v37 can return one of the following error codes after
 OpenDevice():

 PNDERR_PORTEXISTS
	You've tried to open up a Port which is already in use.

 PNDERR_DRIVERTROUBLE
	The driver of the Unit you requested can not be started.
	You can request a more detailed error message by setting the
	according bit in OpenDevice()/Flags. pnr_Data must then point to
	a buffer provided by you. The string will not exceed 63 characters
	plus the terminating zero. If no error occurs, the buffer will
	not be changed!

 PNDERR_UNIT_NOT_DEFINED
	The Unit you requested is missing a definition in the config file.

 >> CHANGES SINCE V3 <<

 v37: Write doesn't support two chunks anymore, Write can fail
    with PNDERR_DESTINATION_GONE now, no more #?ConfigString() in order
    to keep the configuration file tidy. Structure of received data
    has changed. PNB_ERRORSTRING.

 >> WRITING DRIVERS <<

 You find information on this subject in the other autodoc file supplied
 with the ProNET distribution.


pronet.device/CloseDevice                           pronet.device/CloseDevice

   NAME   
	CloseDevice -- Close a port of a certain ProNET Unit.

   SYNOPSIS
	CloseDevice(PNRequest);
                   A1

   FUNCTION
	This is an exec.library call.

	This function terminates access to the corresponding ProNET Unit.
	Since the Unit is not shut down automatically, even if you were
	the last user of it, a RemDevice() would be the right thing to
	do after closing pronet.device.

   INPUTS
	PNRequest - A pointer to a previously opened ProNET IO Request.

   EXAMPLE
	This code can force a specified device to try and expunge.
	Of course, if the device is in use nothing will happen:

	void FlushDevice(name)
	char  *name;
	{
	struct Device *result;

	    Forbid();
	    if(result=(struct Device *)FindName(&SysBase->DeviceList,name))
		RemDevice(result);
	    Permit();
	}

   SEE ALSO
	exec.library/CloseDevice(), exec.library/RemDevice()


pronet.device/CMD_WRITE                               pronet.device/CMD_WRITE

   NAME   
	Write -- send output to ProNET Port.

   FUNCTION
	This command causes a packet of data to be written out the ProNET
	Port/Unit. The number of characters is specified in pnr_Length.

   IO REQUEST
	io_Command - CMD_WRITE
	pnr_Data - pointer to block of data to transmit
	pnr_Length - number of characters to transmit. MUST BE EVEN AND MUST
	    NOT BE GREATER THAN 0x4000!

   RESULTS
	io_Error - if the Write succeeded, then io_Error will be zero.
	    The only other possible error code is PNDERR_DESTINATION_GONE.


pronet.device/OpenDevice                             pronet.device/OpenDevice

   NAME   
	OpenDevice -- Open up a new port of a certain ProNET Unit.

   SYNOPSIS
	error = OpenDevice("pronet.device", unit, ioRequest, flags);
       D0                  A0              D0    A1         D1

	BYTE OpenDevice(STRPTR, ULONG, struct PNRequest*, ULONG);

   FUNCTION
	This is an exec.library call.

	Hey, what do you think it does?!??

   INPUTS
	unit - This number must be defined in the `DEVS:ProNET/.config' file,
	    otherwise OpenDevice() will return PNDERR_UNIT_NOT_DEFINED.
	ioRequest - A pointer to an initialized (see below) PNRequest block.
	flags - As described in the overview page, you have the option
	    to get extensive error messages when setting a bit here.
	    The bit is defined as PNB_ERRORSTRING (the PNF_ definition also
	    exists).

	Two components of the PNRequest must be initialized before calling
	OpenDevice():

	pnr_MsgPort - pointer to a MsgPort where incoming data is sent to.
	pnr_NetSourcePort - The port number you want to open.

   RESULT
	error - zero if everything went o.k., otherwise an error code
	    as defined in exec/errors.h or devices/pronet.h.

   NOTES
	The *one and only* valid port numbers are 0x0001 to 0x7fff. If you
	want a special number above 0x7fff reserved for your application,
	please contact me!

	If you don't have any special preferences for your port number,
	you can use PNP_NEXTFREE to let pronet.device assign you the next
	free one (it will be put into pnr_NetSourcePort then).


pronet.device/ReceivedData                         pronet.device/ReceivedData

 Received data will be sent to the MsgPort you specified in pnr_MsgPort
 when opening the device. You can not change it after opening.
 mn_Length, as opposed to pre-v37, contains the length of the whole Message
 structure. The first word of mn_Node.ln_Name contains the source ProNET
 Port, the second word contains the destination port. The data comes behind
 the Message structure.

 This Message must be replied as soon as there is no use for it any more.

 If there is incoming data but pronet.device can't allocate the Message
 structure, the packet is lost!