TABLE OF CONTENTS

miamibpf.library/--general information--
miamibpf.library/--packet format--
miamibpf.library/MiamiBPFClose
miamibpf.library/MiamiBPFFilter
miamibpf.library/MiamiBPFInit
miamibpf.library/MiamiBPFIoctl
miamibpf.library/MiamiBPFOpen
miamibpf.library/MiamiBPFRead
miamibpf.library/MiamiBPFSetAbortmask
miamibpf.library/MiamiBPFSignalmask

miamibpf.library/--general information--

	Miami:libs/miamibpf.library is an implementation of the
	Berkeley Packet Filter, an efficient, portable packet filtering
	mechansim for BSD-derived protocol stack.

	MiamiBPF is implemented on top of the packet monitoring callback
	mechanism in Miami 1.9.3 and above, and because of that only works
	with the registered version of Miami.

	The main advantages of MiamiBPF over the standard packet monitoring
	callback are:

	- MiamiBPF provides a socket-like API for monitoring that may be
	  easier to use in some situations than a callback hook.

	- MiamiBPF takes care of the necessary buffering, task switching and
	  signalling, so you can run all your packet analysis/debugging code
	  on your own task schedule.

	- MiamiBPF supports BPF programs, i.e.	virtual machine code allowing
	  you to very efficiently pre-filter packets.  BPF virtual machine
	  code is executed within the callback hook, so packets filtered out
	  by the virtual machine code do not create task switching overhead.

	- MiamiBPF adjusts itself to the speed of Miami and your program.  If
	  your program gets behind in analyzing packets then MiamiBPF
	  automatically drops packets so Miami does not get slowed down by
	  your program.

	A detailed description of the BPF virtual machine language is beyond
	the scope of this document.  If you want to write your own BPF
	programs then you should get the standard BPF documentation (for BSD)
	from the Internet or from other sources.


miamibpf.library/--packet format--	   miamibpf.library/--packet format--

	The BPF standard by itself does not define the format of packets
	(e.g.  the size and type of link-layer headers) BPF programs operate
	on.  This can be a problem for the BPF programmer because a BPF
	program has to be adjusted to each interface individually.

	With MiamiBPF this is a bit different: MiamiBPF only operates on the
	packet payload, not on the link-layer header, so all packets
	processed by MiamiBPF have an identical format, regardless of which
	interface they came from.

	Before MiamiBPF passes a packet to a BPF program it prepends the
	following (virtual) header:

	- 1 byte: packet type (MIAMIPFBPT_...)

	- 1 byte: link type (always DLT_MIAMI)

	- 14 bytes: reserved: currently padded with zero.

	This means that your BPF program can identify the packet type (Arp,
	IP etc.) by reading byte zero.	The actual packet contents are
	located starting at offset 16.

	The virtual packet header is automatically added by MiamiBPF to any
	packet arriving at MiamiBPF.  This includes packets arriving from
	Miami and packets passed in through MiamiBPFFilter.

	Packets read by MiamiBPFRead include the virtual packet header.


miamibpf.library/MiamiBPFClose		       miamibpf.library/MiamiBPFClose

   NAME
	MiamiBPFClose -- Closes a BPF channel

   SYNOPSIS
	MiamiBPFClose( channel );
		       D0

	void MiamiBPFClose( ULONG channel );

   FUNCTION
	Closes the specified BPF channel, detaches it from its current
	interface, and frees all related resources.

   INPUTS
	channel - BPF channel


miamibpf.library/MiamiBPFFilter 	      miamibpf.library/MiamiBPFFilter

   NAME
	MiamiBPFFilter -- Executes a BPF virtual machine program for a packet

   SYNOPSIS
	retval = MiamiBPFFilter( program, packet, length, ptype );
	D0			 A0	  A1	  D0	  D1

	unsigned long MiamiBPFFilter( struct bpf_insn *program, unsigned char
	    *packet, unsigned long length, char ptype );

   FUNCTION
	Executes a BPF virtual machine program on a packet.  Both the BPF
	program and the packet have to be specified in the function call.

	The program is specified by a pointer to an array of (compiled) BPF
	instructions.

	The packet is specified by a pointer to the first byte in the packet
	and by the packet length.

	The value returned by MiamiBPFFilter is the value returned by a RET
	instruction in your program.  The return value is undefined if your
	program is malformed.

   INPUTS
	program - First instruction of BPF program

	packet - Packet to filter

	length - Packet length

	ptype - Packet type (MIAMIPFBPT_...)

   RESULT
	retval (D0) - Return value

   NOTE
	The packet MAY NOT contain any link-layer header.  The first byte of
	the packet has to be the first byte visible to the protocol stack.

	This function is NOT needed if you just want to listen for packets on
	one of Miami's interfaces.  It can be useful though if you want a BPF
	filter to execute on packets arriving from some OTHER source, e.g.
	when reading packets from a file.


miamibpf.library/MiamiBPFInit			miamibpf.library/MiamiBPFInit

   NAME
	MiamiBPFInit -- initialize MiamiBPF

   SYNOPSIS
	MiamiBPFInit( MiamiBase, SocketBase );
		      A0	 A0

	void MiamiBPFInit( struct Library *MiamiBase, struct Library
	    *SocketBase );

   FUNCTION
	Initializes MiamiBPF for use.  You MUST call this function before
	calling any other function in miamibpf.library.

   INPUTS
	MiamiBase - Library base of miami.library

	SocketBase - Library base of bsdsocket.library

   NOTE
	You need to open miami.library V6 or higher and bsdsocket.library V4
	or higher before calling this function.  Mind the version numbers !
	Using miamimpf.library with older library versions will cause
	crashes.


miamibpf.library/MiamiBPFIoctl		       miamibpf.library/MiamiBPFIoctl

   NAME
	MiamiBPFIoctl -- Reads or writes control information for a BPF
	channel

   SYNOPSIS
	error = MiamiBPFIoctl( channel, command, data );
	D0		       D0	D1	 A0

	LONG MiamiBPFIoctl( ULONG channel, ULONG command, UBYTE *data );

   FUNCTION
	Reads or writes control or state information associated with a
	previously opened BPF channel.	The following commands are valid:

	- FIONREAD: 'data' needs to point to a longword (at least
	  word-aligned).  When the call returns that longword contains the
	  number of bytes ready for reading from this BPF channel.

	- SIOCGIFADDR: 'data' needs to point to a 'struct ifreq', with
	  ifr_name initialized to a valid interface name.  When the call
	  returns the 'struct ifreq' has been filled with address information
	  for AF_INET for the specified interface.

	- BIOCGBLEN: 'data' needs to point to a longword (at least
	  word-aligned).  When the call returns that longword contains the
	  current size of a BPF packet buffer.

	- BIOCSBLEN: 'data' needs to point to a longword (at least
	  word-aligned), that contains the desired size of the BPF packet
	  buffer.

	- BIOCSETF: 'data' needs to point to a 'struct bpf_program' that
	  contains a valid, compiled BPF virtual machine code program.	When
	  the call returns MiamiBPF has attached that program to the BPF
	  channel, so all subsequent packets will be filtered using the new
	  program.

	- BIOCFLUSH: all current read buffers are emptied.

	- BIOCGETIF: 'data' needs to point to a 'struct ifreq'.  When the
	  call returns ifr_name has been initialized with the name of the
	  interface the BPF channel is currently attached to.

	- BIOCSETIF: 'data' needs to point to a 'struct ifreq', with ifr_name
	  initialized to a valid interface name.  When the call returns the
	  BPF channel has been attached to the specified interface, i.e.
	  packets arriving at that interface or sent through that interface
	  are directed to the BPF channel.

	- BIOCSRTIMEOUT: 'data' needs to point to a 'struct timeval' that
	  contains the new timeout for a call to MiamiBPFRead.

	- BIOCGRTIMEOUT: 'data' needs to point to a 'struct timeval'.  When
	  the call returns that 'struct timeval' contains the current timeout
	  for a call to MiamiBPFRead.

	- BIOCGSTATS: 'data' needs to point to a 'struct bpf_stat'.  When the
	  call returns that 'struct bpf_stat' contains the current packet
	  statistics for this BPF channel.

	- BIOCIMMEDIATE: 'data' needs to point to a 'unsigned int' defining
	  the state of the 'immediate' flag (TRUE/FALSE).  Usually MiamiBPF
	  only completes a MiamiBPFRead call when a read buffer is full or
	  when the read timeout is expired.  However if the 'immediate' flag
	  is set to TRUE then MiamiBPFRead completes after EACH packet
	  received.

	- BIOCVERSION: 'data' needs to point to a 'struct bpf_version'.  When
	  the call returns that 'struct bpf_version' contains the major and
	  minor version numbers for this implementation of the BPF code
	  engine.

	The returned 'error' value is negative if an error has occured, and
	zero if the function completed successfully.

   INPUTS
	channel - BPF channel

	command - command (usually BIOC...)

	data - data for the command

   RESULT
	error (D0) - error condition


miamibpf.library/MiamiBPFOpen			miamibpf.library/MiamiBPFOpen

   NAME
	MiamiBPFOpen -- Opens a new BPF channel

   SYNOPSIS
	channel = MiamiBPFOpen( tags );
	D0			A0

	ULONG MiamiBPFOpen( struct TagList *tags );

   FUNCTION
	Opens a new BPF channel.  The channel is set to default settings, and
	not attached to any interface.

	The returned value is either 0 if the function has failed, or a valid
	BPF channel (a value different from 0).

	The taglist should be NULL for compatibility to future versions.

	All open BPF channels are automatically closed when miamibpf.library
	is closed.

	Note that BPF channels are quite different from socket numbers.  You
	CANNOT use BPF channel numbers in an FD_SET (e.g.  in a WaitSelect
	call).

   INPUTS
	tags - taglist (not used)

   RESULT
	channel (D0) - BPF channel


miamibpf.library/MiamiBPFRead			miamibpf.library/MiamiBPFRead

   NAME
	MiamiBPFRead -- Reads packets from a BPF channel

   SYNOPSIS
	length = MiamiBPFRead( channel, buffer, maxlen );
	D0		       D0	A0	D1

	LONG MiamiBPFRead( ULONG channel, UBYTE *buffer, ULONG maxlen );

   FUNCTION
	Reads one or more packets from a BPF channel.  This function blocks
	until data is available for reading.  Whether the function returns
	for EACH packet or only after several packets have been read depends
	on the state of the 'immediate' flag for this BPF channel (see
	MiamiBPFIoctl).

	'maxlen' has to be EXACTLY IDENTICAL to the current buffer size for
	this channel, or MiamiBPFRead immediately returns -1.  You can
	set/get the current buffer size through MiamiBPFIoctl.

	A 'length' value greater than zero indicates the number of bytes read
	(one or more packets).	A value of zero indicates that a timeout has
	occured.  A value less than zero indicates that an error has occured
	or that one or more signals in the current abort mask have arrived.
	In the latter case use SetSignal to find out which signal has
	arrived.

   INPUTS
	channel - BPF channel

	buffer - packet buffer

	maxlen - size of the packet buffer

   RESULT
	length (D0) - number of bytes returned


miamibpf.library/MiamiBPFSetAbortmask	miamibpf.library/MiamiBPFSetAbortmask

   NAME
	MiamiBPFSetAbortmask -- Defines the abort mask for a BPF channel

   SYNOPSIS
	MiamiBPFSetAbortmask( channel, signals );
			      D0       D0

	void MiamiBPFSetAbortmask( ULONG channel, ULONG signals );

   FUNCTION
	Usually a MiamiBPFRead command only returns when data is available
	for reading or when the read timeout (if any) has expired.

	This function allows you define an additional condition when you want
	MiamiBPFRead to return, e.g.  when the user hits Ctrl-C.

   INPUTS
	channel - BPF channel

	signals - abort mask

   EXAMPLE
	MiamiBPFSetAbortmask(channel,SIGBREAKF_CTRL_C);


miamibpf.library/MiamiBPFSignalmask	  miamibpf.library/MiamiBPFSignalmask

   NAME
	MiamiBPFSignalmask -- Returns the signal mask for a BPF channel

   SYNOPSIS
	signals = MiamiBPFSignalmask( channel );
	D0			      D0

	ULONG MiamiBPFSignalmask( ULONG channel );

   FUNCTION
	Each open BPF channel has an associated signal mask that is set
	whenever a MiamiBPFRead function would complete.  That signal mask is
	returned by this function.

	If you want to ensure that MiamiBPFRead does not block then you need
	to first check if data is available for reading (FIONREAD).  If not
	then wait for the signal(s) returned by MiamiBPFSignalmask to be set
	for your task, and check again (FIONREAD).  Call MiamiBPFRead only if
	FIONREAD returns a non-zero number of bytes.

   INPUTS
	channel - BPF channel

   RESULT
	signals (D0) - signal mask