`term' - A terminal program for Amiga computers

   Copyright © 1990-1996 Olaf Barthel

   You may make and distribute verbatim copies of this documentation if
the contents are unchanged or the author has agreed to any changes made.

   No guarantee of any kind is given that the program described in this
document are 100% reliable. You are using this material on your own
risk.

   The program `term' and the data received/sent by it must not be used
for the following purposes:

  1. The construction, development, production or testing of weapons or
     weapon systems of any kind.

  2. The construction, development, production or use of
     plants/installations which include the processing of
     radioactive/fissionable material.

  3. The training of persons to deal with the abovesaid actions.


   Listen to your conscience.

Changes
*******

   Previous `term' releases would use a different ARexx host interface
implementation.  In order to conform to Commodore-endorsed user
interface style guidelines it was redesigned from scratch for version
3.0. The design and implementation of the ARexx host interface was
suggested by the `Amiga User Interface Style Guide' and strongly
influenced by Martin Taillefer's `TurboText' ARexx host interface.

   Not a simple command has `survived' the revision, the new
implementation is no longer compatible with its predecessors, so
existing ARexx scripts will have to be adapted or even entirely
rewritten.

   `term' no longer distinguishes explicitely between asynchronous and
synchronous commands (i.e. commands which force the main program to
wait and commands which need not bother the main program as the ARexx
handler process is able to execute them). As of this writing it is safe
to assume that almost any command will be processed by the main
program, exceptions are noted.

term and ARexx
**************

   This document describes the ARexx(tm) (1) commands supported by
`term'.  This is not intended to be an introduction to the language
itself.  Rexx was developed by Mike F.  Cowlishaw on an IBM/SP system
and ported to the Amiga by William S.  Hawes.

   ARexx (or Amiga Rexx) is a commercial product which is included with
the AmigaDOS 2.0 Enhancer Package.  If you need a good introduction and
description of the language, try to get a hold of the book `The REXX
Language A Practical Approach to Programming' by M.F.  Cowlishaw,
available from Prentice-Hall International, Inc.

   The section entitled Command execution gives a brief introduction
how to write and run ARexx commands. For more information refer to the
Release 2 Users Manual `Using the System Software'.

   By default `term' opens an ARexx host by the name of `TERM'
(accessable via `address term').  If more than a single `term' process
is running on your machine, the name of the host will be adapted to the
number of the program (i.e.  the first programm will use `TERM', the
second one will use `TERM.1', the third one `TERM.2', etc.). The
default name can be overridden by invoking the program with certain
parameters (see main program documentation). The name of the host is
displayed in the status window (see main program documentation).

   ---------- Footnotes ----------

   (1)  ARexx is a registered trademark of Wishful Thinking Development
Corp.

Command execution
=================

   In order to invoke any command supported by `term' one usually has
to address the host explicitely:

     /* Address the `term' host. */

     ADDRESS term

     /* Invoke the `beepscreen' commmand. */

     BEEPSCREEN

   However, if an ARexx script is invoked directly by the `term' main
program, the script will by default address the main program it was
invoked by.

   Most commands will return results or error codes on failure. To
enable result codes, one has to use the `options results' command. The
results returned by commands will be placed in the `result' variable:

     /* We assume that the script will address the host it was invoked from.
      *
      * Enable command results.
      */

     OPTIONS RESULTS

     /* Request a string from the user. */

     REQUESTSTRING DEFAULT 'anything' PROMPT 'Enter anything'

     /* Did the user cancel the requester? */

     IF rc ~= 0 THEN
        SAY 'user cancelled requester'
     ELSE
        SAY result /* Output the result . */

   Failure codes will always be returned in the `rc' variable (see
previous example).

   In case of failure (variable `rc' >= 10), `term' will leave an error
code in the `term.lasterror' variable:

     /* Enable command results. */

     OPTIONS RESULTS

     /* Produce an error by not supplying any arguments. */

     STOPBITS

     /* Display the error code. */

     SAY term.lasterror

   Rexx tries to tokenize any command parameters, this process involves
promoting them to all upper case letters and checking for illegal
characters. This feature inhibits the use of the `:' (colon) and blank
space characters in parameter names unless the corresponding arguments
are enclosed in quotes. To make things even more complicated, the
parser will not always accept parameters to contain blank spaces. If a
command template accepts the entire command line (such as `TEXT/K/F') a
parameter can include any number of blank spaces. A command template to
accept just a single parameter (such as `TEXT/K') requires double
quotes if blank spaces are included. Text such as `tea or coffee?' thus
becomes `'"tea or coffee?"''.

     /* The following command will fail to send the file `ram:foobar' as the colon
      * in the path name will cause an error:
      */

     SENDFILE ram:foobar

     /* Here is how to do it correctly: */

     SENDFILE 'ram:foobar'

     /* The following command will fail to send the file `foo bar' as the
      * file name is treated as two single files:
      */

     SENDFILE foo bar

     /* The next line will still fail to send the file `foo bar'
      * as the ARexx parser will split the argument into two
      * parameters.
      */

     SENDFILE 'foo bar'

     /* Here is how to do it correctly: */

     SENDFILE '"foo bar"'

     /* The following command will not transmit the string `Hello sailor'
      * across the serial line as the single words will be capitalized,
      * they will be transmitted as `HELLO SAILOR':
      */

     SEND Hello sailor

     /* Here is how to do it correctly: */

     SEND 'Hello sailor'

Stopping a command
******************

   Programs and commands sometimes fail to do what the user is expecting
them to do which makes it necessary to bring program/command execution
to a stop. A common ARexx script to call no external functions or host
commands one can be halted in the following ways:

  1. Executing the `HI' command (located in the `SYS:rexxc' drawer)
     from Shell. This command will attempt stop *all* currently running
     ARexx scripts.

  2. If the ARexx script to be executed runs in an environment to sport
     an output window, activate the window and press the `Control + C'
     keys.  A break signal will be sent to the ARexx script, causing it
     to stop as soon as possible.


   With host environments such as `term' it may not always be possible
to abort a command using the simple measures described above. As for
`term' any command to wait (such as the READ, DELAY or WAIT commands)
can be aborted by sending `term' itself a break signal in the following
fashion:

  1. If the `term' program is still attached to a Shell output window,
     activate the window and press the `Control + D' keys.

  2. If the `term' program was invoked from a Shell but is no longer
     attached to it, enter `status command term' from Shell, remember
     the number printed, then enter `break <number>' with `<number>'
     being the number returned by the `status' command.

  3. Press the hotkey combination configured in the program hotkey
     settings (see main program documentation). The default is `Right
     Shift + Left Shift + Escape'. This will cause a break signal to be
     sent to the `term' program.


Commands
********

   The commands supported by `term' are listed in a table of the
following form:

`Format:'
     The command name with its possible calling parameters. In this
     table parameters are enclosed in brackets and braces, separated by
     commas and vertical bars; *do not type these special characters
     along with the parameters!*:

    `< > (Angle brackets)'
          Angle brackets enclose parameters whose contents *must not*
          be omitted in order to make the command work properly.

    `[ ] (Square brackets)'
          Square brackets enclose optional parameters.

    `{ } (Curly braces)'
          Curly braces enclose items which can be repeated a number of
          times, such as file name lists.

    `| (Vertical bar)'
          Vertical bars separate alternative, mutually exclusive
          options.

    `, (Comma)'
          Commas separate multiple applicable options.

`Template:'
     The command template, similar to the command templates employed by
     AmigaDOS Shell commands.  Possible templates are:

    `<Parameter>/A'
          The parameter must always be included in order to get
          accepted.

    `<Option>/K'
          The option's keyword must be given.

    `<Option>/S'
          This option works as a switch. If this option keyword is
          included the switch is on, else it is off.

    `<Option>/N'
          A numeric parameter is expected.

    `<Option>/M'
          Multiple parameters are accepted.

    `<Text>/F'
          The text must be the final parameter on the command line.

    `, (Comma)'
          Indicates that the command takes no parameters.

`Purpose:'
     Briefly describes what the command will do.

`Specifications:'
     Describes the command and its possible uses in more detail.

`Result:'
     The type of the command result code if any.

`Warning:'
     If the command can return with a warning and when.

`Example:'
     An example code fragment to illustrate how to use the command.
     Commands and keywords are given in upper case, the names of
     variables and command arguments are given in lower case. Where a
     single command line would not fit into a single line on the
     screen, an ellipsis ('...') is meant to join the broken line.

   Table of commands in alphabetical order:

   Table of commands in functional groups:

   Commands dealing with text buffer and capturing

   Commands dealing with serial I/O

   Commands dealing with lists

   Commands dealing with the clipboard

   Commands dealing with file transfers

   Commands dealing with terminal I/O

   Commands dealing with windows and requesters

   Commands dealing with program attributes

   Commands dealing with program execution

   Commands dealing with file I/O

   Miscellaneous commands

The ACTIVATE command
====================

`Format:'
     ACTIVATE

`Template:'
     ,

`Purpose:'
     De-iconifies the program, brings the main window to the front and
     makes it active.

`Specifications:'
     The program can be put to sleep using the DEACTIVATE command, to
     bring it back to proper operation, use the `ACTIVATE' command. If
     this command is invoked while the program is not asleep, it will
     cause the main window to be brought to the front and activated.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* This is how the main programm can be (re-)activated: */

          ACTIVATE

The ADDITEM command
===================

`Format:'
     ADDITEM [To] <Upload|Download|Dial|Wait> [Before|After] [Command
     <Command for trap list>] [Response <Response text>] [Phone <Entry
     number, name or wildcard pattern>] [Name <Name>]

`Template:'
     TO/A,BEFORE/S,AFTER/S,RESPONSE/K,COMMAND/K,PHONE/K/F,NAME/K/F

`Purpose:'
     Inserts an item (a name, a phone number, text, etc.) before or
     after the currently selected list item.

`Specifications:'
     `term' maintains a number of lists, these are:
    `Upload list'
          The list of files to be uploaded.

    `Download list'
          The list of files the program has downloaded.

    `Dial list'
          The list of phone numbers or phone book entries to be dialed.

    `Wait list'
          The list of texts the WAIT command is to wait for.

     New items can be added to the list with the `ADDITEM' command. The
     upload list expects the names of files the SENDFILE command is to
     transfer. It makes little sense to add files names to the download
     list as the `term' main program maintains it and adds the names of
     files received to it, but it is still possible. The wait list
     expects text lines the WAIT command will look for in the terminal
     input stream.  A wait list entry added using the `RESPONSE'
     keyword will if found in the input data stream cause the response
     text to be immediately sent to the remote.  *Note: a wait list
     entry to make use of the `RESPONSE' keyword will be handled by the
     WAIT command, the ARexx script will not notice if this list entry
     was found or not.*

     The dial list accepts a number of different parameters:
    `Phonebook entry numbers'
          These are passed using the `Phone' parameter which should be
          a numeric value as it is used as an index to pick the
          corresponding entry from the phone book.

    `Phonebook entry names'
          These are also passed using the `Phone' parameter which can
          be a proper name or a wildcard pattern.

    `Phone numbers'
          These are passed using the `Name' parameter.

     List item can be inserted before or after the currently selected
     list item (see SELECTITEM command). The default is to insert them
     after the currently selected list item.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Enable result codes. */

          OPTIONS RESULTS

          /* Get a file name from the user. */

          REQUESTFILE TITLE '"Select a file to upload"'

          /* Add the file name to the upload list. */

          IF rc = 0 THEN ADDITEM TO upload NAME result

          /* Add phonebook entry #2 to the dial list. */

          ADDITEM TO dial PHONE 2

          /* Add all phonebook entries whose names start
           * with an `a' to the dial list.
           */

          ADDITEM TO dial PHONE a#?

          /* Add a plain phone number to the dial list. */

          ADDITEM TO dial NAME 424242

The BAUD command
================

`Format:'
     BAUD [Rate] <Transfer speed in bits per second>

`Template:'
     RATE/A/N

`Purpose:'
     Sets the serial line transfer speed

`Specifications:'
     Sets the serial line transfers speed to some defined value. The
     rate parameter passed in will be matched against all valid BPS
     rates supported by `term', the closest value will be used.

`Result:'
     Returns the old baud value.

`Warning:'
     -

`Example:'
          /* Change the serial transfer speed to 2400 bps. */

          BAUD 2400

The BEEPSCREEN command
======================

`Format:'
     BEEPSCREEN

`Template:'
     ,

`Purpose:'
     `Beeps' the terminal screen.

`Specifications:'
     Invokes a bell signal, as configured in the program settings.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Invoke a bell signal. */

          BEEPSCREEN

The CALLMENU command
====================

`Format:'
     CALLMENU [Title] <Title text or wildcard pattern>

`Template:'
     TITLE/A/F

`Purpose:'
     Invokes the function associated with a menu item.

`Specifications:'
     Calls a pull-down menu function just as if the user had selected it
     using the mouse. The `Title' parameter can be any valid menu item
     name or a wildcard pattern. In the latter case, only the first
     menu item to match the pattern will be called.

`Result:'
     -

`Warning:'
     If no matching menu item was to be found.

`Example:'
          /* Invoke the `About...' menu item. */

          CALLMENU abou#?

The CAPTURE command
===================

`Format:'
     CAPTURE [To] <Printer|File> [Append|Overwrite|Skip] [Name <File
     name>]

`Template:'
     TO/A,APPEND/S,OVERWRITE/S,SKIP/S,NAME/K

`Purpose:'
     Starts a file or printer capture.

`Specifications:'
     If a capture is not already in progress will open a capture file
     or start capturing incoming terminal text to the printer. If the
     `File' argument is given and the `Name' parameter is omitted, will
     prompt for the name of a file to capture to.

     If to capture to a given file, will append the captured text. If
     user is to select a file to capture to, will ask whether to append
     the text to the file or to overwrite it.

     The command will not prompt the user to confirm whether an
     existing file should be overwritten, etc. if one of the following
     options are in effect:

    `APPEND'
          If the named file exists, append the new capture data to it.

    `OVERWRITE'
          If the named file exists, delete it before adding new capture
          data to it.

    `SKIP'
          If the named file exists, don't overwrite it. Do not open the
          capture file.

`Result:'
     -

`Warning:'
     In case user was to select a file and aborted the selection.

`Example:'
          /* Open a named capture file. */

          CAPTURE TO file NAME 'ram:capture file'

          /* Close the capture file, ask the user for a file name. */

          CLOSE FILE
          CAPTURE TO file

          /* Capture to the printer. */

          CAPTURE TO printer

The CLEAR command
=================

`Format:'
     CLEAR [From] <Upload|Download|Dial|Wait|Buffer> [Force]

`Template:'
     FROM/A,FORCE/S

`Purpose:'
     Clears the contents of a global list or the text buffer.

`Specifications:'
     This command serves to clear the contents of the lists to be
     maintained using the ADDITEM, REMITEM, SELECTITEM, etc. commands
     and to purge the contents of the text buffer. In the latter case
     the program will prompt for confirmation in case the buffer still
     holds any lines. This confirmation can be suppressed by using the
     `Force' parameter.

`Result:'
     -

`Warning:'
     In case the user did not confirm to clear the buffer.

`Example:'
          /* Clear the wait list. */

          CLEAR FROM wait

          /* Clear the buffer, ask for a confirmation. */

          CLEAR FROM buffer

          /* If no confirmation was given, clear it by force. */

          IF rc ~= 0 THEN CLEAR FROM buffer FORCE

The CLEARSCREEN command
=======================

`Format:'
     CLEARSCREEN

`Template:'
     ,

`Purpose:'
     Clears the terminal screen

`Specifications:'
     Clears the terminal screen and positions the cursor in the top
     left corner.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Clear the terminal screen. */

          CLEARSCREEN

The CLOSE command
=================

`Format:'
     CLOSE [From] <Printer|File|All>

`Template:'
     FROM/A

`Purpose:'
     Terminates file and/or printer capture.

`Specifications:'
     Terminates a capture process as started with the CAPTURE command.
     Will terminate printer capture, file capture or both.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Terminate both file and printer capture. */

          CLOSE ALL

The CLOSEDEVICE command
=======================

`Format:'
     CLOSEDEVICE

`Template:'
     ,

`Purpose:'
     Release the current serial device driver

`Specifications:'
     Frees the serial device driver for use with other applications.
     The driver can be reopened (or a different device driver can be
     selected) using the OPENDEVICE command.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Release the serial device driver, all serial I/O
           * will be halted.
           */

          CLOSEDEVICE

The CLOSEREQUESTER command
==========================

`Format:'
     CLOSEREQUESTER

`Template:'
     ,

`Purpose:'
     Closes the currently open requester window

`Specifications:'
     Will close any currently open requester window, such as the
     dialing window, the phone book, the serial settings window, etc.
     Will not close windows such as the file transfer window or the
     text/numeric input windows.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Close the currently open requester window,
           * whatever it may be.
           */

          CLOSEREQUESTER

The DEACTIVATE command
======================

`Format:'
     DEACTIVATE

`Template:'
     ,

`Purpose:'
     Iconifies the program.

`Specifications:'
     Puts the application to sleep. Requires Workbench to be running,
     so an AppIcon can be put on the Workbench backdrop. This command
     will be ignored if the application has already been put to sleep.
     To wake the application up, use the ACTIVATE command.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Iconify the program. */

          DEACTIVATE

The DELAY command
=================

`Format:'
     DELAY [MIC|MICROSECONDS <Number>] [[SEC|SECONDS] <Number>]
     [MIN|MINUTES <Number>] [QUIET]

`Template:'
     MIC=MICROSECONDS/K/N,SEC=SECONDS/N,MIN=MINUTES/K/N,QUIET/S

`Purpose:'
     Delays program execution for a couple of microseconds, seconds and
     minutes.

`Specifications:'
     Will cause both the program to make the call and the application
     to wait for a certain period of time. Unless the `QUIET' option is
     in effect will process and display data received from the serial
     line.

`Result:'
     -

`Warning:'
     If command was aborted before the timeout had elapsed.

`Example:'
          /* Wait for five seconds. */

          DELAY 5

          /* Wait for one second and seven microseconds. */

          DELAY MIC 7 SEC 5

The DIAL command
================

`Format:'
     DIAL [WAIT|SYNC] [[Num] <Phone number>]

`Template:'
     WAIT=SYNC/S,NUM/F

`Purpose:'
     Dials the provided phone number. If no phone number was given,
     will dial the numbers and phone book entries stored in the dial
     list.

`Specifications:'
     This command will build a dialing list from the available sources
     and pass it to the dialing function which is to schedule the
     dialing process and perform any login-actions. Available sources
     are the `Num' parameter which will cause the command to dial only
     this single number or the dial list whose contents will be used if
     the `Num' parameter is omitted.

     If the `WAIT' parameter is used the command will wait until a
     connection is made. If the parameter is not use this command will
     return as soon as the dialing process has been initiated.

`Result:'
     -

`Warning:'
     If no connection was to be made.

`Example:'
          /* Dial a single phone number. */

          DIAL 424242

          /* Wait a bit and abort the dialing process. */

          DELAY 5
          CLOSEREQUESTER

          /* Clear the dialing list, then add all the phonebook entries
           * to the list.
           */

          CLEAR FROM dial
          ADDITEM TO dial PHONE #?

          /* Dial the dial list. */

          DIAL WAIT

          /* Did we get a connection? */

          IF RC == 0 THEN SEND TEXT "Ack!\r"

The DUPLEX command
==================

`Format:'
     DUPLEX [Full|Half|Echo]

`Template:'
     FULL/S,HALF=ECHO/S

`Purpose:'
     Sets the serial line duplex mode.

`Specifications:'
     Sets the serial line duplex mode, this can be either full duplex
     or half duplex (local echo).

`Result:'
     Returns the old duplex value.

`Warning:'
     -

`Example:'
          /* Enable local terminal echo. */

          DUPLEX ECHO

The EXECTOOL command
====================

`Format:'
     EXECTOOL [Console] [Async] [Port] [Command] <File name>

`Template:'
     CONSOLE/S,ASYNC/S,PORT/S,COMMAND/A/F

`Purpose:'
     Executes a program.

`Specifications:'
     Will load and execute an AmigaDOS program. The `Console' parameter
     will cause an output file or window to be opened, the `Async'
     parameter will cause the command to return as soon as the
     execution process has been launched. The `Port' parameter will
     cause the current ARexx host port name to be passed to the tool on
     the command line.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Launch the `Dir' command. */

          EXECTOOL CONSOLE COMMAND 'dir c:'

The FAULT command
=================

`Format:'
     FAULT [Code] <Error code>

`Template:'
     CODE/A/N

`Purpose:'
     Returns the descriptive text associated with an error code as
     returned by `term'.

`Specifications:'
     `term' will return error codes in the `term.lasterror' variable.
     In order to get the descriptive text associated with an error
     code, use this command.  All internal Rexx and AmigaDOS errors
     codes are supported as well as the error codes special to `term'.

`Result:'
     The error description associated with the error code.

`Warning:'
     -

`Example:'
          /* Enable command results. */

          OPTIONS RESULTS

          /* Get the text associated with error #1001. */

          FAULT 1001

          /* Output the result. */

          SAY result

The GETATTR command
===================

`Format:'
     GETATTR [Object] <Name> [Field] <Name> [Stem <Name>] [Var <Name>]

`Template:'
     OBJECT/A,FIELD,STEM/K,VAR/K

`Purpose:'
     Obtains information on an application attribute.

`Specifications:'
     Obtains information on an object, if possible will store it in the
     `result' variable. If a stem or simple variable name is given
     using the `Stem' or `Var' parameters will store the information in
     this variable.  If no `Field' parameter is given, will store the
     entire object contents which requires that the `Stem' parameter is
     given. For a list of valid attributes see the section entitled
     Attributes.

`Result:'
     Returns information either in `result' variable or in the supplied
     `Stem' or `Var' variable.

`Warning:'
     -

`Example:'
          /* Enable command results. */

          OPTIONS RESULTS

          /* Query the name of the ARexx host we are communicating with. */

          GETATTR OBJECT term FIELD arexx

          /* Output the result. */

          SAY result

          /* Same as above, but using a different syntax. */

          GETATTR term.arexx
          SAY result

          /* Store the entire contents of the phone book in a
           * stem variable.
           */

          GETATTR phonebook STEM book

          /* Output the phonebook contents. */

          SAY 'phone book contains' book.count 'entries'

          DO i = 0 TO book.count - 1
             SAY 'entry #' i

             SAY 'name    :' book.i.name
             SAY 'number  :' book.i.number
             SAY 'comment :' book.i.commenttext
             SAY 'username:' book.i.username
          END i

The GETCLIP command
===================

`Format:'
     GETCLIP [Unit <Number>]

`Template:'
     UNIT/K/N

`Purpose:'
     Retrieves the contents of the clipboard.

`Specifications:'
     Obtains the contents of the clipboard and returns it in the
     `result' variable. Will optionally read from the given clipboard
     unit, but uses the unit number selected in the application
     settings by default. *Note that a string returned can be up to
     65,536 characters long!*

`Result:'
     Contents of the clipboard if it contains any text.

`Warning:'
     If clipboard does not contain any text.

`Example:'
          /* Enable command results. */

          OPTIONS RESULTS

          /* Get the primary clipboard contents. */

          GETCLIP

          /* Output the contents. */

          IF rc ~= 0 THEN
             SAY 'clipboard does not contain any text'
          ELSE
             SAY result

The GOONLINE command
====================

`Format:'
     GOONLINE

`Template:'
     ,

`Purpose:'
     Cause `term' to go into online state.

`Specifications:'
     After this command is processed `term' will immediately go into
     online state. If the carrier signal is to be checked and no signal
     is present `term' will drop into offline state right away.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Go into online state. */

          GOONLINE

The HANGUP command
==================

`Format:'
     HANGUP

`Template:'
     ,

`Purpose:'
     Hang up the serial line.

`Specifications:'
     Hangs up the serial line, executes logoff and cleanup operations.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Hang up the line, whether the program is online or not. */

          HANGUP

The HELP command
================

`Format:'
     HELP [[Command] <Name>] [Prompt]

`Template:'
     COMMAND,PROMPT/S

`Purpose:'
     Returns the template of a command or invokes the online help
     system.

`Specifications:'
     This command will either return the template associated with a
     `term' ARexx command specified using the `Command' parameter or
     invoke the AmigaGuide(tm) help system.

`Result:'
     Command template if requested.

`Warning:'
     -

`Example:'
          /* Enable command results. */

          OPTIONS RESULTS

          /* Query the template associated with the `selectitem' command. */

          HELP selectitem

          /* Output the result. */

          SAY result

          /* Invoke the online help. */

          HELP PROMPT

The OPEN command
================

`Format:'
     OPEN [Name <File name>] [TO] <Translations|Functionkeys|Cursorkeys|
     Fastmacros|Hotkeys|Speech|Sound|Buffer|Configuration|Phone>

`Template:'
     NAME/K,TO/A

`Purpose:'
     Reads data from a disk file.

`Specifications:'
     This command reads the contents of a disk file and stores the
     information either in the configuration, the phone book or the
     text buffer. If text is read into the text buffer it will be
     appended to the existing text. If no file name is given will
     prompt the user to select a file.

`Result:'
     -

`Warning:'
     If user was requested to select a file and cancelled the selection.

`Example:'
          /* Load the configuration from a file. */

          OPEN NAME 'ram:term.prefs' TO configuration

          /* Add text to the text buffer. */

          OPEN TO buffer

The OPENDEVICE command
======================

`Format:'
     OPENDEVICE [Name <Device name>] [Unit <Number>]

`Template:'
     NAME/K,UNIT/K/N

`Purpose:'
     (Re-)Opens the serial device driver.

`Specifications:'
     (Re-)Opens the previously released (see CLOSEDEVICE command) device
     driver or a different device driver/unit if the corresponding
     `Device' and `Unit' parameters are given.

`Result:'
     Returns the old device name and unit number.

`Warning:'
     -

`Example:'
          /* Request command results. */
          options results

          /* Release the serial device driver. */

          CLOSEDEVICE

          /* Open a different device driver. */

          OPENDEVICE DEVICE 'duart.device' UNIT 5

          /* Tell the name of the old device driver,
           * and unit number, e.g. "serial.device/0"
           */

          say RESULT

The OPENREQUESTER command
=========================

`Format:'
     OPENREQUESTER [REQUESTER]
     <Serial|Modem|Screen|Terminal|Emulation|Clipboard|






     Capture|Commands|Misc|Path|Transfer|Translations|Functionkeys|Cursorkeys|
     Fastmacros|Hotkeys|Speech|Sound|Phone>

`Template:'
     REQUESTER/A

`Purpose:'
     Opens a requester window.

`Specifications:'
     Opens a requester window. Only a single window can be open at a
     time.  The window opened can be closed using the CLOSEREQUESTER
     command.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Open the phonebook window. */

          OPENREQUESTER phone

The PARITY command
==================

`Format:'
     PARITY [Even|Odd|None|Mark|Space]

`Template:'
     EVEN/S,ODD/S,NONE/S,MARK/S,SPACE/S

`Purpose:'
     Sets the serial line parity mode.

`Specifications:'
     Sets the serial line parity mode.

`Result:'
     Returns the old parity mode.

`Warning:'
     -

`Example:'
          /* Set the parity mode. */

          PARITY NONE

The PASTECLIP command
=====================

`Format:'
     PASTECLIP [Unit <Number>]

`Template:'
     UNIT/K/N

`Purpose:'
     Feed the contents of the clipboard into the input stream.

`Specifications:'
     Feeds the contents of the clipboard into the input stream. Obtains
     the data either from the given clipboard unit or from the default
     unit configured in the program settings.

`Result:'
     -

`Warning:'
     If clipboard does not contain any text.

`Example:'
          /* Paste the contents of clipboard #2. */

          PASTECLIP UNIT 2

The PRINT command
=================

`Format:'
     PRINT [From]
     <Screentext|Clipboard|Buffer|Dial|Wait|Upload|Download> [TO <File
     name>] [Serial|Modem|Screen|Terminal|User|Comment| Size|Date|Attr]

`Template:'
     FROM/A,TO/K,SERIAL/S,MODEM/S,SCREEN/S,TERMINAL/S,USER/S,
     COMMENT/S,SIZE/S,DATE/S,ATTR/S

`Purpose:'
     Prints the contents of the screen, the clipboard, the textbuffer
     or one of the lists.

`Specifications:'
     Outputs the contents of the screen, the clipboard, the textbuffer
     or one of the lists (see ADDITEM command) to a file or the
     printer. If the `To' parameter is omitted, will output the data to
     the printer. The parameters `Serial' through `Attr' control what
     will be printed:
    `Screentext, Clipboard, Buffer, Wait list'
          Options have no effect on the output.

    `Dial list'
          Responds to the `Serial', `Modem', `Screen', `Terminal',
          `User' and `Comment' parameters. The printout will contain
          information on the corresponding settings.

    `Upload list, Download list'
          Responds to the `Comment', `Size', `Date' and `Attr'
          parameters. The printout will contain information on the
          corresponding file attributes. *Note: if any of these
          parameters are given, only the base file names will be
          printed along with the corresponding information.*

`Result:'
     -

`Warning:'
     If user cancelled print operation.

`Example:'
          /* Clear the dialing list, then add the entire phone book to it. */

          CLEAR dial
          additem to dial phone #?

          /* Send the contents of the dial list to a disk file. */

          PRINT FROM dial TO 'ram:phonebook' SERIAL MODEM SCREEN...
          ...TERMINAL USER COMMENT

The PROCESSIO command
=====================

`Format:'
     PROCESSIO <On|Off>

`Template:'
     ON/S,OFF/S

`Purpose:'
     Turns serial I/O processing on or off.

`Specifications:'
     Usually, the `term' main program processes incoming data from the
     serial line, i.e. text is displayed in the terminal window or data
     transfers are started. This can interfere with custom I/O
     processing, such as done by an ARexx program which wants to
     receive and process all incoming serial data, without getting
     interrupted by the main program. For an application example see
     WAIT.

`Result:'
     Returns the old PROCESSIO value.

`Warning:'
     -

`Example:'
          /* Turn off I/O processing. */

          PROCESSIO OFF

The PROTOCOL command
====================

`Format:'
     PROTOCOL [None|RTSCTS|RTSCTSDTR]

`Template:'
     NONE/S,RTSCTS/S,RTSCTSDTR/S

`Purpose:'
     Sets the serial line handshaking protocol.

`Specifications:'
     Sets the serial line handshaking protocol. See the main program
     documentation for details.

`Result:'
     Returns the old protocol mode.

`Warning:'
     -

`Example:'
          /* Set the handshaking protocol. */

          PROTOCOL NONE

The PUTCLIP command
===================

`Format:'
     PUTCLIP [Unit <Unit>] [TEXT] <Text to store>

`Template:'
     UNIT/K/N,TEXT/A/F

`Purpose:'
     Stores text in the clipboard.

`Specifications:'
     Stores the provided text in the clipboard. Will store it in the
     given clipboard unit if the `Unit' parameter is given. Will use
     the unit number configured in the program settings otherwise.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Store a short string in the clipboard. Note: can
           * only be up to 65,536 characters long.
           */

          PUTCLIP 'hello sailor!'

The QUIT command
================

`Format:'
     QUIT [Force]

`Template:'
     FORCE/S

`Purpose:'
     Terminates the application.

`Specifications:'
     Terminates program execution, will ask for a confirmation to leave
     unless the `Force' parameter is used. *Caution: this command may
     fail if there are still output windows open on the `term' screen.*

`Result:'
     -

`Warning:'
     If user did not confirm termination.

`Example:'
          /* Try to terminate the program, ask for confirmation. */

          QUIT

          /* If no confirmation was given terminate by force. */

          IF rc ~= 0 THEN QUIT FORCE

The READ command
================

`Format:'
     READ [Num <Number of bytes>] [CR] [Noecho] [Verbatim] [Timeout
     <Seconds>] [Terminator <Character>] [[Prompt] <Prompt text>]

`Template:'

     NUM/K/N,CR/S,NOECHO/S,VERBATIM/S,TIMEOUT/K/N,TERMINATOR/K,PROMPT/K/F

`Purpose:'
     Reads a number of bytes or a string from the serial line.

`Specifications:'
     If `Num' parameter is given will read a number of bytes from the
     serial line (*note: only a maximum of 65,536 bytes can be read*).
     The command will return when the read request has been satisfied,
     the timeout (settable using the TIMEOUT command) has elapsed or
     the command was aborted.

     If the `CR' parameter is given will handle simple line editing
     functions (`Backspace', `Control-X') and return a string as soon
     as the `Carriage return' key is pressed, the timeout (settable
     using the TIMEOUT command) has elapsed or the command is aborted.

     The `Noecho' parameter will cause `term' not to echo typed
     characters back to the remote. *Note that in order to see any
     input on the local side the remote is to echo the characters typed
     back.*

     With the `Timeout' parameter you can override the global timeout
     value (settable using the TIMEOUT command) for this command.

     The `Terminator' parameter tells the command to stop when finding
     the given character in the input stream. For example, `TERMINATOR
     "\n"' would tell the command to stop when finding the line feed
     character in the input stream.

     If present, the `Prompt' text will be sent across the serial line,
     much the same as if it had been sent using the SEND command.

     This command pays attention to the current character translation
     table for incoming characters. If the characters are to be read
     without any changes made one has to use the `Verbatim' parameter.

`Result:'
     The string read.

`Warning:'
     If command was cancelled, no input was made or, if the `CR'
     parameter is used, the timeout elapsed.

`Example:'
          /* Enable command results. */

          OPTIONS RESULTS

          /* Set the read timeout to five seconds. */

          TIMEOUT 5

          /* Read seven bytes. */

          READ NUM 7

          /* Output the result. */

          IF rc ~= 0 THEN
             SAY 'no data was read'
          ELSE
             SAY result

          /* Wait up to eight seconds to eight bytes to arrive. */

          READ TIMEOUT 8 NUM 8

          /* Turn the timeout off. */

          TIMEOUT OFF

          /* Prompt for input. */

          READ CR PROMPT 'Enter a line of text:'

          /* Output the result. */

          IF rc ~= 0 THEN
             SAY 'no input was made'
          ELSE
             SAY result

The RECEIVEFILE command
=======================

`Format:'
     RECEIVEFILE [Mode <ASCII|Text|Binary>] [Name <File name>]

`Template:'
     MODE/K,NAME/K

`Purpose:'
     Receive one or more files using the XPR protocol.

`Specifications:'
     Receives one or more files using the currently configured XPR
     protocol.  The `Mode' parameter determines the file transfer mode
     (either plain ASCII, Text mode or binary file mode), if omitted
     the file(s) will be received in binary mode. Some file transfer
     protocols do not require any file names to be given as they have
     their own means to determine the names of the files to be
     received. However, a file name parameter can be given. If omitted
     the file transfer protocol will prompt the user for a file name if
     necessary.

     The names of all files received are placed on the download list
     for processing. The list will be cleared before the transfer is
     started.

`Result:'
     -

`Warning:'
     If user cancelled file selection.

`Example:'
          /* Start to receive a file in text mode. */

          RECEIVEFILE MODE text

The REDIAL command
==================

`Format:'
     REDIAL

`Template:'
     ,

`Purpose:'
     Redials the numbers remaining in the currently configured dialing
     list.

`Specifications:'
     Redials the numbers which still remain in the dialing list built
     either by the phone book or by the DIAL command. *Note that this
     command will return as soon as the dialing process is initiated.*

`Result:'
     -

`Warning:'
     If dialing list is empty.

`Example:'
          /* Redial the list. */

          REDIAL

          /* Successful? */

          IF rc ~= 0 THEN SAY 'dialing list is empty'

The REMITEM command
===================

`Format:'
     REMITEM [From] <Upload|Download|Dial|Wait> [Name <Name or
     wildcard>]

`Template:'
     FROM/A,NAME/K/F

`Purpose:'
     Removes one or more items from a list.

`Specifications:'
     Removes one or more items from a list. If no `Name' parameter is
     given will remove the currently selected list item (selectable
     using the SELECTITEM command). The `Name' parameter can be a
     proper name or a wildcard pattern.

     *Note: Cannot remove named items from the dial list.*

`Result:'
     -

`Warning:'
     If no list item would match the name pattern.

`Example:'
          /* Remove the currently selected item from the wait list. */

          REMITEM FROM wait

          /* Remove all items from the wait list which end with `z'. */

          REMITEM FROM wait NAME '#?z'

The REQUESTFILE command
=======================

`Format:'
     REQUESTFILE [Title <Title text>] [Path <Path name>] [File <File
     name>] [Pattern <Wildcard pattern>] [Multi] [Stem|Name <Variable
     name>]

`Template:'
     TITLE/K,PATH/K,FILE/K,PATTERN/K,MULTI/S,STEM=NAME/K

`Purpose:'
     Requests one or more file names from the user.

`Specifications:'
     Requests one or more file names from the user. Will present a file
     requester with given title text and preset path, file name and
     pattern values. If only a single file name is to be requested will
     place the result in the `result' variable. The `Multi' parameter
     allows multiple files to be selected, the number of files selected
     and the file names will be placed in the variable specified using
     the `Stem' parameter.

`Result:'
     The name of the file selected will be placed in the `result'
     variable. If multiple file were selected, will place the following
     information in the supplied stem variable:
    `<Variable name>.COUNT'
          The number of files selected.

    `<Variable name>.0 through <Variable name>.n-1'
          The file names selected.

`Warning:'
     If user cancelled selection.

`Example:'
          /* Enable command results. */

          OPTIONS RESULTS

          /* Request a single file name from the user. */

          REQUESTFILE TITLE '"select a file"'

          /* Output the result. */

          IF rc ~= 0 THEN
             SAY 'no file was selected'
          ELSE
             SAY result

          /* Request several files. */

          REQUESTFILE TITLE 'select several files' MULTI STEM names

          /* Output the result. */

          IF rc ~= 0 THEN
             SAY 'no files were selected'
          ELSE DO
             SAY 'files selected:' names.count

             DO i = 0 TO names.count - 1
                SAY names.i
             END
          END

The REQUESTNOTIFY command
=========================

`Format:'
     REQUESTNOTIFY [Title <Title text>] [Prompt] <Prompt text>

`Template:'
     TITLE/K,PROMPT/A/F

`Purpose:'
     Notify the user with a message.

`Specifications:'
     Opens a requester to notify the user, the prompt text can include
     line feed characters (`'0A'X'), the user will be able to answer
     the requester by clicking on a `Continue' button.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Notify the user. */

          REQUESTNOTIFY TITLE '"Important information"' ...
          ...PROMPT 'This message is important'

The REQUESTNUMBER command
=========================

`Format:'
     REQUESTNUMBER [Default <Default number>] [Prompt <Prompt text>]

`Template:'
     DEFAULT/K/N,PROMPT/K/F

`Purpose:'
     Requests a numeric value from the user

`Specifications:'
     Requests a numeric value from the user, will display the provided
     prompt text or a default text and present the provided default
     number, so user can simply hit return to accept the defaults.

`Result:'
     The number the has entered.

`Warning:'
     If user cancelled requester.

`Example:'
          /* Enable command results. */

          OPTIONS RESULTS

          /* Requester a single number. */

          REQUESTNUMBER DEFAULT 42 PROMPT 'Enter the answer'

          /* Output the result. */

          IF rc ~= 0 THEN
             SAY 'no number was entered'
          ELSE
             SAY result

The REQUESTRESPONSE command
===========================

`Format:'
     REQUESTRESPONSE [Title <Title text>] [Options <Options string>]
     [Prompt] <Prompt text>

`Template:'
     TITLE/K,OPTIONS/K,PROMPT/A/F

`Purpose:'
     Request a response from user.

`Specifications:'
     Requests a response from the user, uses provided title and prompt
     text and a number of options. If no options are specified will use
     `Yes|No' as the defaults.

`Result:'
     For `Options' passed as `Yes|Perhaps|No' will return 1 for `Yes',
     2 for `Perhaps' and return a warning for `No'.

`Warning:'
     If user selected negative choice.

`Example:'
          /* Enable command results. */

          OPTIONS RESULTS

          /* Request a response. */

          REQUESTRESPONSE PROMPT 'Are you indecisive?' ...
          ...OPTIONS '"Yes|Don't know|No"'

          /* Look at the response. */

          IF rc ~= 0 THEN
             SAY 'Not indecisive'
          ELSE DO
             IF result = 0 THEN
                SAY 'Indecisive'
             ELSE
                SAY 'Probably indecisive'
          END

The REQUESTSTRING command
=========================

`Format:'
     REQUESTSTRING [Secret] [Default <String>] [Prompt <Text>]

`Template:'
     SECRET/S,DEFAULT/K,PROMPT/K/F

`Purpose:'
     Requests a string from the user.

`Specifications:'
     Requests a string from the user, will display the provided prompt
     text or a default text and present the provided default string, so
     user can simply hit return to accept the defaults.

     If the `Secret' parameter is provided, will not display the
     characters typed.

`Result:'
     The text the user entered.

`Warning:'
     If user cancelled the requester.

`Example:'
          /* Enable command results. */

          OPTIONS RESULTS

          /* Request a secret string. */

          REQUESTSTRING SECRET DEFAULT '"hello sailor!"' ...
          ...PROMPT 'Enter secret message'

          /* Output the result. */

          IF rc ~= 0 THEN
             SAY 'no text was entered'
          ELSE
             SAY result

The RESET command
=================

`Format:'
     RESET [Clear][Styles][Text][Timer]

`Template:'
     CLEAR/S,STYLES/S,TEXT/S,TIMER/S

`Purpose:'
     This is a superset of all the RESET commands.

`Specifications:'
     See RESETSTYLES, RESETTEXT, RESETSCREEN, RESETTIMER.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Reset the terminal screen. */

          RESET CLEAR

The RESETSCREEN command
=======================

`Format:'
     RESETSCREEN

`Template:'
     ,

`Purpose:'
     Resets the terminal screen to defaults.

`Specifications:'
     Resets the terminal screen to defaults, this includes clearing the
     screen, moving the cursor to the home position and resetting text,
     text rendering styles and colours.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Reset the terminal screen. */

          RESETSCREEN

The RESETSTYLES command
=======================

`Format:'
     RESETSTYLES

`Template:'
     ,

`Purpose:'
     Resets the text rendering styles to defaults.

`Specifications:'
     Resets the text rendering styles to defaults, turning off inverse
     video, boldface, italics, etc. modes.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Reset the text rendering styles. */

          RESETSTYLES

The RESETTEXT command
=====================

`Format:'
     RESETTEXT

`Template:'
     ,

`Purpose:'
     Reset the terminal text to defaults.

`Specifications:'
     Reset the terminal text to defaults, this includes switching back
     from graphics text or G1 mode.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Reset the terminal text. */

          RESETTEXT

The RESETTIMER command
======================

`Format:'
     RESETTIMER

`Template:'
     ,

`Purpose:'
     Reset the online timer.

`Specifications:'
     The online timer is reset to 00:00:00, regardless whether `term'
     is currently online or not.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Reset the online timer. */

          RESETTIMER

The RX command
==============

`Format:'
     RX [Console] [Async] [Command] <Command name>

`Template:'
     CONSOLE/S,ASYNC/S,COMMAND/A/F

`Purpose:'
     Invokes an ARexx macro file.

`Specifications:'
     Invokes an ARexx macro file, if `Console' argument specified opens
     a console output window, else uses `NIL:', if `Async' argument
     specified executes the macro asynchronously.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Launch the `term' command shell. */

          RX CONSOLE ASYNC 'term:cmdshell.term'

The SAVE command
================

`Format:'
     SAVE [From] <Translations|Functionkeys|
     Cursorkeys|Fastmacros|Hotkeys|Speech|
     Sound|Buffer|Configuration|Phone| Screentext|Screenimage>

`Template:'
     FROM/A

`Purpose:'
     Saves data to a disk file.

`Specifications:'
     Saves data to a disk file, will prompt for a file name to save to.
     See SAVEAS command for more information.

`Result:'
     -

`Warning:'
     If user cancels save operation.

`Example:'
          /* Save the terminal screen contents to an
           * IFF-ILBM file.
           */

          SAVE FROM screenimage

The SAVEAS command
==================

`Format:'
     SAVEAS [Name <File name>] [From]
     <Translations|Functionkeys|Cursorkeys|
     Fastmacros|Hotkeys|Speech|Sound|Buffer|
     Configuration|Phone|Screentext| Screenimage>

`Template:'
     NAME/K,FROM/A

`Purpose:'
     Saves data to a disk file.

`Specifications:'
     Saves data to a disk file, will prompt for a filename to save to
     if none is provided. Will save either parts of the program
     configuration or the phone book contents (`Phonebook' parameter),
     the contents of the terminal screen as plain ASCII text
     (`Screentext' parameter) or the contents of the terminal screen as
     an IFF-ILBM-file (`Screenimage' parameter).

`Result:'
     -

`Warning:'
     If user cancels save operation.

`Example:'
          /* Save the program configuration to a file. */

          SAVEAS NAME 'ram:term.prefs' FROM configuration

The SELECTITEM command
======================

`Format:'
     SELECTITEM [Name <Name>] [From] <Upload|Download|Dial|Wait>
     [Next|Prev|Previous|Top|Bottom]

`Template:'
     NAME/K,FROM/A,NEXT/S,PREV=PREVIOUS/S,TOP/S,BOTTOM/S

`Purpose:'
     Select an item from a list.

`Specifications:'
     Selects an item from a list, returns the item name in the `result'
     variable. The `Top' parameter will select the first list item,
     `Bottom' the last item. The `Previous' parameter will select the
     previous list item, `Next' the next successive item. Instead of
     using a positioning parameter, it is also possible to use a
     wildcard pattern or name with the `Name' parameter. The first list
     item to match the name will be selected.

     *Note: cannot be used with the dial list.*

`Result:'
     Returns the list item in the `result' variable.

`Warning:'
     If end of list reached.

`Example:'
          /* Enable command results. */

          OPTIONS RESULTS

          /* Output the contents of the download list. */

          SELECTITEM FROM download TOP

          DO WHILE rc = 0
             SAY result
             SELECTITEM FROM download NEXT
          END

The SEND command
================

`Format:'
     SEND [Noecho] [Local] [Literal] [Byte <ASCII code>] [Text] <Text>

`Template:'
     NOECHO/S,LOCAL/S,LITERAL/S,BYTE/K/N,TEXT/A/F

`Purpose:'
     Sends the provided text to the serial line, executes embedded
     command sequences.

`Specifications:'
     Sends the provided text to the serial line, executes embedded
     command sequences (see main program documentation). To send a
     single byte, use the `Byte' parameter. The `Noecho' parameter will
     suppress terminal output. The `Local' parameter will cause the
     text to be output only locally in the terminal window, it will not
     be sent across the serial line. The `Literal' parameter keeps
     `term' from interpreting any special characters, such as `\r', in
     the text to send and just transmits the text you passed in.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Send some text to the serial line. */

          SEND 'This is some text.\r\n'

          /* Send a single byte (a null) to the serial line. */

          SEND BYTE 0

          /* Execute an embedded command (send a break signal). */

          SEND '\x'

The SENDBREAK command
=====================

`Format:'
     SENDBREAK

`Template:'
     ,

`Purpose:'
     Send a break signal across the serial line.

`Specifications:'
     Send a break signal across the serial line.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Send a break signal. */

          SENDBREAK

The SENDFILE command
====================

`Format:'
     SENDFILE [Mode <ASCII|Text|Binary>] [Names] {File names}

`Template:'
     MODE/K,NAMES/M

`Purpose:'
     Transfers files using the currently selected file transfer
     protocol.

`Specifications:'
     Transfers one or more files using the currently configured XPR
     protocol.  The `Mode' parameter determines the file transfer mode
     (either plain ASCII, Text mode or binary file mode), if omitted
     the file(s) will be sent in binary mode. Some file transfer
     protocols do not require any file names to be given as they have
     their own means to determine the names of the files to be sent.
     However, a file name parameter can be given. If omitted the file
     transfer protocol will prompt the user for a file name if
     necessary. Several file names can be given if necessary, they will
     be transferred along with the file names stored in the upload
     list. The file transfer process will remove any files successfully
     transferred from the upload list, leaving only those behing which
     were not to be transferred correctly.

     Files whose names do not include a fully qualified path name are
     expected to reside in the default upload directory as specified in
     the main program paths settings.

`Result:'
     -

`Warning:'
     If user cancels file selection.

`Example:'
          /* Prompt for files to be uploaded. */

          SENDFILE

          /* Send a single file. */

          SENDFILE 'c:list'

          /* Clear the upload list, add a single file name. */

          CLEAR upload
          ADDITEM TO upload NAME 'c:dir'

          /* Transfer the file. */

          SENDFILE

The SETATTR command
===================

`Format:'
     SETATTR [Object] <Name> [Field] <Name> [Stem <Name>] [Var <Name>]

`Template:'
     OBJECT/A,FIELD,STEM/K,VAR

`Purpose:'
     Sets a certain application attribute.

`Specifications:'
     Sets a certain application attribute, retrieves the information
     from the supplied stem or simple variable. For a list of valid
     attributes, see the section entitled Attributes.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Set the transfer speed. */

          SETATTR serialprefs baudrate 2400

The SPEAK command
=================

`Format:'
     SPEAK [Text] <Text>

`Template:'
     TEXT/A/F

`Purpose:'
     Speaks the provided text using the Amiga speech synthesizer.

`Specifications:'
     Speaks the provided text using the Amiga speech synthesizer,
     requires that speech support is enabled.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Say something sensible. */

          SPEAK 'something sensible'

The STOPBITS command
====================

`Format:'
     STOPBITS [0|1]

`Template:'
     0/S,1/S

`Purpose:'
     Sets the serial line stop bits.

`Specifications:'
     Sets the serial line stop bits.

`Result:'
     Returns the old number of stop bits.

`Warning:'
     -

`Example:'
          /* Set the serial line stop bits. */

          STOPBITS 1

The TEXTBUFFER command
======================

`Format:'
     TEXTBUFFER [Lock|Unlock]

`Template:'
     LOCK/S,UNLOCK/S

`Purpose:'
     Locks or unlocks the text buffer contents.

`Specifications:'
     Locks or unlocks the text buffer contents, similar to the effect
     of the corresponding main menu entry.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Lock the text buffer. */

          TEXTBUFFER LOCK

The TIMEOUT command
===================

`Format:'
     TIMEOUT [[Sec|Seconds] <Number>] [Off]

`Template:'
     SEC=SECONDS/N,OFF/S

`Purpose:'
     Sets the serial read timeout.

`Specifications:'
     Sets the timeout the WAIT and READ commands will wait until they
     exit.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Set the read timeout. */

          TIMEOUT SEC 5

The TRAP command
================

`Format:'
     TRAP <On|Off>

`Template:'
     ON/S,OFF/S

`Purpose:'
     Turns the trap list processing on or off.

`Specifications:'
     This command tells the main program whether it should process
     entries of the trap list when filtering input or not.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Ignore the trap list. */

          TRAP OFF

The WAIT command
================

`Format:'
     WAIT [Noecho] [Timeout <Seconds>] [[Text] <Text>]

`Template:'
     NOECHO/S,TIMEOUT/K/N,TEXT/F

`Purpose:'
     Waits for a certain sequence of characters to be received from the
     serial line.

`Specifications:'
     Wait for text to be received from the serial line. If no text to
     wait for is provided wait for either item of the wait list to
     appear. The `Noecho' parameter suppresses terminal output. *Note
     that text comparison does not consider the case of characters (in
     respect to the ECMA Latin 1 character set).* As `term' has control
     over the incoming data stream before and after the `WAIT' command
     is executed, it may `eat' and process data the `WAIT' command
     ought to receive. In order to avoid this effect you can use the
     `PROCESSIO' command (see PROCESSIO). For example, at the beginning
     of a program you could tell `term' to leave the incoming data
     stream alone with the `PROCESSIO OFF' command, then invoke the
     `WAIT' command as needed, and eventually when your program exits
     allow `term' to process incoming data with the `PROCESSIO ON'
     command.

     With the `Timeout' parameter you can override the global timeout
     value (settable using the TIMEOUT command) for this command.

`Result:'
     Returns the string found.

`Warning:'
     If timeout has elapsed before any matching text was received.

`Example:'
          /* Enable command results. */

          OPTIONS RESULTS

          /* Set the read timeout. */

          TIMEOUT SEC 30

          /* Wait for a single line of text. */

          WAIT 'some text'

          /* Wait up to ten seconds for a single line of text. */

          WAIT TIMEOUT 10 'some more text'

          /* Clear the wait list, add a few items. */

          CLEAR wait
          ADDITEM TO wait NAME 'foo'
          ADDITEM TO wait NAME 'bar'

          /* Wait for the text to appear. */

          WAIT

          /* Output the result. */

          IF rc ~= 0 THEN
             SAY 'no text was received'
          ELSE
             SAY result

The WINDOW command
==================

`Format:'
     WINDOW [Names] {<Buffer|Review|Packet|Fastmacros|
     Status|Main|UploadQueue>} [Open|Close] [Activate] [Min|Max]
     [Front|Back] [Top|Bottom|Up|Down]

`Template:'
     NAMES/A/M,OPEN/S,CLOSE/S,ACTIVATE/S,MIN/S,MAX/S,FRONT/S,BACK/S,
     TOP/S,BOTTOM/S,UP/S,DOWN/S

`Purpose:'
     Manipulates the aspects of a window.

`Specifications:'
     Manipulates the aspects of a window. Not all windows will support
     all available commands. The windows supported are:
    `Buffer'
          The text buffer window and screen. Supports the `Open',
          `Close', `Activate' and `Front' commands.

    `Review'
          The review window. Supports the `Open', `Close', `Activate',
          `Min', `Max', `Front', `Back', `Top', `Bottom', `Up', and
          `Down' commands.

    `Packet'
          The packet window. Supports the `Open', `Close', `Activate',
          `Min', `Max', `Front' and `Back' commands.

    `Fastmacros'
          The fast! macro window. Supports the `Open', `Close',
          `Activate', `Min', `Max', `Front' and `Back' commands.

    `Status'
          The status window. Supports the `Open', `Close', `Activate',
          `Front' and `Back' commands.

    `Main'
          The main program window. Supports the `Open', `Close',
          `Activate', `Front' and `Back' commands.

`Result:'
     -

`Warning:'
     -

`Example:'
          /* Open all available windows. */

          WINDOW buffer review packet fastmacros status main OPEN

Attributes
**********

   Several of the application's internal variables are can be accessed
and modified using the GETATTR and SETATTR commands. Information is
available on the objects and their associated fields explained below.
Each line consists of the object and field name and the type of the
available data:
`Numeric data'
    `<Object>.<Field>'
          Numeric

     The information is a numeric value.

`Text data'
    `<Object>.<Field>'
          Text

     The information is a text string.

`Boolean data'
    `<Object>.<Field>'
          Boolean

     The information is a boolean value and can be `ON' or `OFF'.

`Mapped codes'
    `<Object>.<Field>'
          <Value 1> ... <Value n>

     The information can be one of the given values.

The TERM object (read-only)
===========================

`TERM.VERSION'
     Text

     The `term' program revision.

`TERM.SCREEN'
     Text

     The name of the public screen the `term' main window has been
     opened on.

`TERM.SESSION.ONLINE'
     Boolean

     Whether the program is currently online or not.

`TERM.SESSION.SESSIONSTART'
     Text

     Time and date when the `term' program was started.

`TERM.SESSION.BYTESSENT'
     Numeric

`TERM.SESSION.BYTESRECEIVED'
     Numeric

`TERM.SESSION.CONNECTMESSAGE'
     Text

     The message issued by the modem when the connection was
     established.

`TERM.SESSION.BBSNAME'
     Text

`TERM.SESSION.BBSNUMBER'
     Text

`TERM.SESSION.BBSCOMMENT'
     Text

`TERM.SESSION.USERNAME'
     Text

`TERM.SESSION.ONLINEMINUTES'
     Numeric

     The number of minutes the program is currently connected to a BBS.

`TERM.SESSION.ONLINECOST'
     Numeric

     The cost of the connection to the BBS.

`TERM.AREXX'
     Text

     The name of the ARexx host port the program is communicating with.

`TERM.LASTERROR'
     Numeric

     The code corresponding to the error the last command has caused.

`TERM.TERMINAL.ROWS'
     Numeric

     The number of available terminal screen rows.

`TERM.TERMINAL.COLUMNS'
     Numeric

     The number of available terminal screen columns.

`TERM.BUFFER.SIZE'
     Numeric

     The size of the text buffer.

The PHONEBOOK object (read-only)
================================

   Available fields are:
`PHONEBOOK.COUNT'
     Numeric

     The number of entries in the phonebook. The single phonebook
     entries can be accessed as `PHONEBOOK.0...' through
     `PHONEBOOK.n-1...'.

`PHONEBOOK.n.NAME'
     Text

`PHONEBOOK.n.NUMBER'
     Text

`PHONEBOOK.n.COMMENTTEXT'
     Text

`PHONEBOOK.n.USERNAME'
     Text

`PHONEBOOK.n.PASSWORDTEXT'
     Text

The SERIALPREFS object
======================

   Available fields are:
`SERIALPREFS.BAUDRATE'
     Numeric

`SERIALPREFS.BREAKLENGTH'
     Numeric

     The break signal length in microseconds.

`SERIALPREFS.BUFFERSIZE'
     Numeric

`SERIALPREFS.DEVICENAME'
     Text

`SERIALPREFS.UNIT'
     Numeric

`SERIALPREFS.BITSPERCHAR'
     Numeric

     The number of bits per transferred char. This can be either seven
     or eight.

`SERIALPREFS.PARITYMODE'
     `NONE' `EVEN' `ODD' `MARK' `SPACE'.

`SERIALPREFS.STOPBITS'
     Numeric

     The number of stop bits to be used. This can be either 0 or 1.

`SERIALPREFS.HANDSHAKINGMODE'
     `NONE' `RTSCTS' `RTSCTSDSR'

`SERIALPREFS.DUPLEXMODE'
     `HALF' `FULL'

`SERIALPREFS.LOCALECHO'
     Boolean

`SERIALPREFS.INTERNALXONXOFF'
     Boolean

`SERIALPREFS.HIGHSPEED'
     Boolean

`SERIALPREFS.SHARED'
     Boolean

`SERIALPREFS.STRIPBIT8'
     Boolean

`SERIALPREFS.CARRIERCHECK'
     Boolean

`SERIALPREFS.PASSXONXOFFTHROUGH'
     Boolean

`SERIALPREFS.DIRECTCONNECTION'
     Boolean

`SERIALPREFS.QUANTUM'
     Numeric

`SERIALPREFS.USEOWNDEVUNIT'
     Boolean

`SERIALPREFS.OWNDEVUNITREQUEST'
     `RELEASE' `RELEASERETRY' `IGNORE'

The MODEMPREFS object
=====================

   Available fields are:
`MODEMPREFS.MODEMINITTEXT'
     Text

`MODEMPREFS.MODEMEXITTEXT'
     Text

`MODEMPREFS.MODEMHANGUPTEXT'
     Text

`MODEMPREFS.DIALPREFIXTEXT'
     Text

`MODEMPREFS.DIALSUFFIXTEXT'
     Text

`MODEMPREFS.CHARSENDDELAY'
     Numeric

`MODEMPREFS.DIALMODE'
     `PULSE' `TONE'

`MODEMPREFS.NOCARRIERTEXT'
     Text

`MODEMPREFS.NODIALTONETEXT'
     Text

`MODEMPREFS.CONNECTTEXT'
     Text

`MODEMPREFS.VOICETEXT'
     Text

`MODEMPREFS.RINGTEXT'
     Text

`MODEMPREFS.BUSYTEXT'
     Text

`MODEMPREFS.OKTEXT'
     Text

`MODEMPREFS.ERRORTEXT'
     Text

`MODEMPREFS.REDIALDELAY'
     Numeric

     The redial delay in seconds

`MODEMPREFS.DIALRETRIES'
     Numeric

`MODEMPREFS.DIALTIMEOUT'
     Numeric

     The dial timeout in seconds

`MODEMPREFS.VERBOSEDIALING'
     Boolean

`MODEMPREFS.CONNECTAUTOBAUD'
     Boolean

`MODEMPREFS.HANGUPDROPSDTR'
     Boolean

`MODEMPREFS.REDIALAFTERHANGUP'
     Boolean

`MODEMPREFS.NOCARRIERISBUSY'
     Boolean

`MODEMPREFS.CONNECTLIMIT'
     Numeric

     Time limit in minutes.

`MODEMPREFS.CONNECTLIMITMACRO'
     Text

`MODEMPREFS.TIMETOCONNECT'
     Numeric

`MODEMPREFS.INTERDIALDELAY'
     Numeric

The SCREENPREFS object
======================

   Available fields are:
`SCREENPREFS.COLOURMODE'
     `TWO' `FOUR' `EIGHT' `SIXTEEN'

`SCREENPREFS.FONTNAME'
     Text

`SCREENPREFS.FONTSIZE'
     Numeric

`SCREENPREFS.MAKESCREENPUBLIC'
     Boolean

`SCREENPREFS.SHANGHAIWINDOWS'
     Boolean

`SCREENPREFS.BLINKING'
     Boolean

`SCREENPREFS.FASTERLAYOUT'
     Boolean

`SCREENPREFS.TITLEBAR'
     Boolean

`SCREENPREFS.STATUSLINEMODE'
     `DISABLED' `STANDARD' `COMPRESSED'

`SCREENPREFS.USEPUBSCREEN'
     Boolean

`SCREENPREFS.PUBSCREENNAME'
     Text

`SCREENPREFS.USEPENS'
     Boolean

`SCREENPREFS.WINDOWBORDER'
     Boolean

`SCREENPREFS.SPLITSTATUS'
     Boolean

`SCREENPREFS.ONLINEDISPLAY'
     `TIME' `COST' `BOTH'

The TERMINALPREFS object
========================

   Available fields are:
`TERMINALPREFS.BELLMODE'
     `NONE' `VISIBLE' `AUDIBLE' `BOTH' `SYSTEM'

`TERMINALPREFS.ALERTMODE'
     `NONE' `BELL' `SCREEN' `BOTH'

`TERMINALPREFS.EMULATIONMODE'
     `INTERNAL' `ATOMIC' `TTY' `EXTERNAL' `HEX'

`TERMINALPREFS.FONTMODE'
     `STANDARD' `IBM' `IBMRAW'

`TERMINALPREFS.SENDCRMODE'
     `IGNORE' `CR' `CRLF'

`TERMINALPREFS.SENDLFMODE'
     `IGNORE' `LF' `LFCR'

`TERMINALPREFS.RECEIVECRMODE'
     `IGNORE' `CR' `CRLF'

`TERMINALPREFS.RECEIVELFMODE'
     `IGNORE' `LF' `LFCR'

`TERMINALPREFS.NUMCOLUMNS'
     Numeric

`TERMINALPREFS.NUMLINES'
     Numeric

`TERMINALPREFS.KEYMAPNAME'
     Text

`TERMINALPREFS.EMULATIONNAME'
     Text

`TERMINALPREFS.FONTNAME'
     Text

`TERMINALPREFS.FONTSIZE'
     Numeric

`TERMINALPREFS.USETERMINALPROCESS'
     Boolean

`TERMINALPREFS.AUTOSIZE'
     Boolean

The EMULATIONPREFS object
=========================

   Available fields are:
`EMULATIONPREFS.IDENTIFICATION'
     `VT200' `VT102' `VT101' `VT100'

`EMULATIONPREFS.CURSORMODE'
     `STANDARD' `APPLICATION'

`EMULATIONPREFS.NUMERICMODE'
     `STANDARD' `APPLICATION'

`EMULATIONPREFS.CURSORWRAP'
     Boolean

`EMULATIONPREFS.LINEWRAP'
     Boolean

`EMULATIONPREFS.INSERTMODE'
     Boolean

`EMULATIONPREFS.NEWLINEMODE'
     Boolean

`EMULATIONPREFS.SCROLLMODE'
     `JUMP' `SMOOTH'

`EMULATIONPREFS.DESTRUCTIVEBACKSPACE'
     `OFF' `OVERSTRIKE' `OVERSTRIKESHIFT'

`EMULATIONPREFS.SWAPBSDELETE'
     Boolean

`EMULATIONPREFS.PRINTERENABLED'
     Boolean

`EMULATIONPREFS.ANSWERBACKTEXT'
     Text

`EMULATIONPREFS.CLSRESETSCURSOR'
     Boolean

`EMULATIONPREFS.NUMPADLOCKED'
     Boolean

`EMULATIONPREFS.CURSORLOCKED'
     Boolean

`EMULATIONPREFS.FONTLOCKED'
     Boolean

`EMULATIONPREFS.WRAPLOCKED'
     Boolean

`EMULATIONPREFS.STYLELOCKED'
     Boolean

`EMULATIONPREFS.COLOURLOCKED'
     Boolean

`EMULATIONPREFS.MAXPRESCROLL'
     Numeric

`EMULATIONPREFS.MAXJUMP'
     Numeric

`EMULATIONPREFS.USEPENS'
     Boolean

The CLIPBOARDPREFS object
=========================

   Available fields are:
`CLIPBOARDPREFS.UNIT'
     Numeric

`CLIPBOARDPREFS.CONVERTLF'
     Wahrheitswert

`CLIPBOARDPREFS.LINEDELAY'
     Numeric

     Paste line delay in 1/100 seconds.

`CLIPBOARDPREFS.CHARDELAY'
     Numeric

     Paste character delay in 1/100 seconds.

`CLIPBOARDPREFS.LINEPROMPTTEXT'
     Text

`CLIPBOARDPREFS.SENDTIMEOUT'
     Numeric

     Timeout in 1/100 seconds.

`CLIPBOARDPREFS.TEXTPACING'
     `DIRECT' `ECHO' `ANYECHO' `PROMPT' `DELAY' `KEYBOARD'

`CLIPBOARDPREFS.INSERTPREFIXTEXT'
     Text

`CLIPBOARDPREFS.INSERTSUFFIXTEXT'
     Text

The CAPTUREPREFS object
=======================

   Available fields are:
`CAPTUREPREFS.LOGACTIONS'
     Boolean

`CAPTUREPREFS.LOGFILENAME'
     Text

`CAPTUREPREFS.LOGCALLS'
     Boolean

`CAPTUREPREFS.CALLLOGFILENAME'
     Text

`CAPTUREPREFS.MAXBUFFERSIZE'
     Numeric

`CAPTUREPREFS.BUFFER'
     Boolean

`CAPTUREPREFS.BUFFERSAVEPATH'
     Text

`CAPTUREPREFS.CONNECTAUTOCAPTURE'
     Boolean

`CAPTUREPREFS.AUTOCAPTUREDATE'
     `NAME', `INCLUDE'

`CAPTUREPREFS.CAPTUREFILTER'
     Boolean

`CAPTUREPREFS.CONVERTCHARACTERS'
     Boolean

`CAPTUREPREFS.CAPTUREPATH'
     Text

`CAPTUREPREFS.OPENBUFFERWINDOW'
     `TOP', `END'

`CAPTUREPREFS.REMEMBERBUFFERWINDOW'
     Boolean

`CAPTUREPREFS.OPENBUFFERSCREEN'
     `TOP', `END'

`CAPTUREPREFS.REMEMBERBUFFERSCREEN'
     Boolean

`CAPTUREPREFS.BUFFERSCREENPOSITION'
     `LEFT', `MID', `RIGHT'

`CAPTUREPREFS.BUFFERWIDTH'
     Numeric

`CAPTUREPREFS.SEARCHHISTORY'
     Numeric

`CAPTUREPREFS.BUFFERSAFETYMEMORY'
     Numeric

The COMMANDPREFS object
=======================

   Available fields are:
`COMMANDPREFS.STARTUPMACROTEXT'
     Text

`COMMANDPREFS.LOGINMACROTEXT'
     Text

`COMMANDPREFS.LOGOFFMACROTEXT'
     Text

`COMMANDPREFS.UPLOADMACROTEXT'
     Text

`COMMANDPREFS.DOWNLOADMACROTEXT'
     Text

The MISCPREFS object
====================

   Available fields are:
`MISCPREFS.PRIORITY'
     Numeric

`MISCPREFS.BACKUPCONFIG'
     Boolean

`MISCPREFS.OPENFASTMACROPANEL'
     Boolean

`MISCPREFS.RELEASEDEVICE'
     Boolean

`MISCPREFS.CREATEICONS'
     Boolean

`MISCPREFS.SIMPLEIO'
     Boolean

`MISCPREFS.PROTECTIVEMODE'
     Boolean

`MISCPREFS.IOBUFFERSIZE'
     Numeric

`MISCPREFS.ALERTMODE'
     `NONE' `BELL' `SCREEN' `BOTH'

`MISCPREFS.REQUESTERMODE'
     `IGNORE' `CENTRE' `RELATIVE'

`MISCPREFS.REQUESTERLEFT'
     Numeric

`MISCPREFS.REQUESTERTOP'
     Numeric

`MISCPREFS.REQUESTERWIDTH'
     Numeric

`MISCPREFS.REQUESTERHEIGHT'
     Numeric

`MISCPREFS.CONSOLEWINDOW'
     Text

`MISCPREFS.SUPPRESSOUTPUT'
     Boolean

The PATHPREFS object
====================

   Available fields are:
`PATHPREFS.ASCIIUPLOADPATH'
     Text

`PATHPREFS.ASCIIDOWNLOADPATH'
     Text

`PATHPREFS.TEXTUPLOADPATH'
     Text

`PATHPREFS.TEXTDOWNLOADPATH'
     Text

`PATHPREFS.BINARYUPLOADPATH'
     Text

`PATHPREFS.BINARYDOWNLOADPATH'
     Text

`PATHPREFS.CONFIGPATH'
     Text

`PATHPREFS.EDITORNAME'
     Text

`PATHPREFS.HELPFILENAME'
     Text

The TRANSFERPREFS object
========================

   Available fields are:
`TRANSFERPREFS.DEFAULTPROTOCOL'
     Text

`TRANSFERPREFS.ERRORNOTIFYCOUNT'
     Numeric

`TRANSFERPREFS.ERRORNOTIFYWHEN'
     `NEVER' `ALWAYS' `START' `END'

`TRANSFERPREFS.ASCIIUPLOADPROTOCOL'
     Text

`TRANSFERPREFS.ASCIIDOWNLOADPROTOCOL'
     Text

`TRANSFERPREFS.QUIETTRANSFER'
     Boolean

`TRANSFERPREFS.MANGLEFILENAMES'
     Boolean

`TRANSFERPREFS.LINEDELAY'
     Numeric

`TRANSFERPREFS.CHARDELAY'
     Numeric

`TRANSFERPREFS.LINEPROMPTTEXT'
     Text

`TRANSFERPREFS.TEXTPACING'
     `DIRECT' `ECHO' `ANYECHO' `PROMPT' `DELAY' `KEYBOARD'

`TRANSFERPREFS.SENDTIMEOUT'
     Numeric

`TRANSFERPREFS.STRIPBIT8'
     Boolean

`TRANSFERPREFS.IGNOREDATAPASTTERMINATOR'
     Boolean

`TRANSFERPREFS.TERMINATORCHAR'
     Numeric

`TRANSFERPREFS.IDENTIFYCOMMAND'
     Text

`TRANSFERPREFS.EXPANDBLANKLINES'
     Boolean

`TRANSFERPREFS.TEXTUPLOADPROTOCOL'
     Text

`TRANSFERPREFS.TEXTDOWNLOADPROTOCOL'
     Text

`TRANSFERPREFS.BINARYUPLOADPROTOCOL'
     Text

`TRANSFERPREFS.BINARYDOWNLOADPROTOCOL'
     Text

`TRANSFERPREFS.OVERRIDEPATH'
     Boolean

`TRANSFERPREFS.SETARCHIVEDBIT'
     Boolean

`TRANSFERPREFS.COMMENTMODE'
     `IGNORE' `FILETYPE' `SOURCE'

`TRANSFERPREFS.TRANSFERICONS'
     Boolean

`TRANSFERPREFS.HIDEUPLOADICON'
     Boolean

`TRANSFERPREFS.TRANSFERPERFMETER'
     Boolean

`TRANSFERPREFS.DEFAULTTYPE'
     `XPR' or `PROGRAM'

`TRANSFERPREFS.DEFAULTSENDSIGNATURE'
     Text

`TRANSFERPREFS.DEFAULTRECEIVESIGNATURE'
     Text

`TRANSFERPREFS.ASCIIUPLOADTYPE'
     `XPR', `PROGRAM', `DEFAULT' or `INTERNAL'

`TRANSFERPREFS.ASCIIUPLOADSIGNATURE'
     Text

`TRANSFERPREFS.ASCIIDOWNLOADSIGNATURE'
     Text

`TRANSFERPREFS.ASCIIDOWNLOADTYPE'
     `XPR', `PROGRAM', `DEFAULT' or `INTERNAL'

`TRANSFERPREFS.ASCIIDOWNLOADSIGNATURE'
     Text

`TRANSFERPREFS.ASCIIDOWNLOADSIGNATURE'
     Text

`TRANSFERPREFS.TEXTUPLOADTYPE'
     `XPR', `PROGRAM' or `DEFAULT'

`TRANSFERPREFS.TEXTUPLOADSIGNATURE'
     Text

`TRANSFERPREFS.TEXTDOWNLOADSIGNATURE'
     Text

`TRANSFERPREFS.TEXTDOWNLOADTYPE'
     `XPR', `PROGRAM' or `DEFAULT'

`TRANSFERPREFS.TEXTDOWNLOADSIGNATURE'
     Text

`TRANSFERPREFS.TEXTDOWNLOADSIGNATURE'
     Text

`TRANSFERPREFS.BINARYUPLOADTYPE'
     `XPR', `PROGRAM' or `DEFAULT'

`TRANSFERPREFS.BINARYUPLOADSIGNATURE'
     Text

`TRANSFERPREFS.BINARYDOWNLOADSIGNATURE'
     Text

`TRANSFERPREFS.BINARYDOWNLOADTYPE'
     `XPR', `PROGRAM' or `DEFAULT'

`TRANSFERPREFS.BINARYDOWNLOADSIGNATURE'
     Text

`TRANSFERPREFS.BINARYDOWNLOADSIGNATURE'
     Text

The PROTOCOLPREFS object
========================

   This object features no fields, it contains a single line of text:
the XPR protocol options.

The TRANSLATIONPREFS object
===========================

   Indices referring to the ascii codes range from 0 to 255, available
fields are:
`TRANSLATIONPREFS.n.SEND'
     Text

`TRANSLATIONPREFS.n.RECEIVE'
     Text

The FUNCTIONKEYPREFS object
===========================

   Key indices range from 1 to 10 (representing F1 through F10),
available fields are:
`FUNCTIONKEYPREFS.n'
     Text

`FUNCTIONKEYPREFS.SHIFT.n'
     Text

`FUNCTIONKEYPREFS.ALT.n'
     Text

`FUNCTIONKEYPREFS.CONTROL.n'
     Text

The CURSORKEYPREFS object
=========================

   Available fields are:
`CURSORKEYPREFS.UPTEXT'
     Text

`CURSORKEYPREFS.RIGHTTEXT'
     Text

`CURSORKEYPREFS.DOWNTEXT'
     Text

`CURSORKEYPREFS.LEFTTEXT'
     Text

`CURSORKEYPREFS.SHIFT.UPTEXT'
     Text

`CURSORKEYPREFS.SHIFT.RIGHTTEXT'
     Text

`CURSORKEYPREFS.SHIFT.DOWNTEXT'
     Text

`CURSORKEYPREFS.SHIFT.LEFTTEXT'
     Text

`CURSORKEYPREFS.ALT.UPTEXT'
     Text

`CURSORKEYPREFS.ALT.RIGHTTEXT'
     Text

`CURSORKEYPREFS.ALT.DOWNTEXT'
     Text

`CURSORKEYPREFS.ALT.LEFTTEXT'
     Text

`CURSORKEYPREFS.CONTROL.UPTEXT'
     Text

`CURSORKEYPREFS.CONTROL.RIGHTTEXT'
     Text

`CURSORKEYPREFS.CONTROL.DOWNTEXT'
     Text

`CURSORKEYPREFS.CONTROL.LEFTTEXT'
     Text

The FASTMACROPREFS object
=========================

`FASTMACROPREFS.COUNT'
     Numeric

     The number of fast macros available, entries range from
     `FASTMACROPREFS.0...' to `FASTMACROPREFS.n-1...'

`FASTMACROPREFS.n.NAME'
     Text

`FASTMACROPREFS.n.CODE'
     Text

The HOTKEYPREFS object
======================

   Available fields are:
`HOTKEYPREFS.TERMSCREENTOFRONTTEXT'
     Text

`HOTKEYPREFS.BUFFERSCREENTOFRONTTEXT'
     Text

`HOTKEYPREFS.SKIPDIALENTRYTEXT'
     Text

`HOTKEYPREFS.ABORTAREXX'
     Text

`HOTKEYPREFS.COMMODITYPRIORITY'
     Numeric

`HOTKEYPREFS.HOTKEYSENABLED'
     Boolean

The SPEECHPREFS object
======================

   Available fields are:
`SPEECHPREFS.RATE'
     Numeric

`SPEECHPREFS.PITCH'
     Numeric

`SPEECHPREFS.FREQUENCY'
     Numeric

`SPEECHPREFS.SEXMODE'
     `MALE' `FEMALE'

`SPEECHPREFS.VOLUME'
     Numeric

`SPEECHPREFS.SPEECH'
     Boolean

The SOUNDPREFS object
=====================

   Available fields are:
`SOUNDPREFS.BELLNAME'
     Text

`SOUNDPREFS.CONNECTNAME'
     Text

`SOUNDPREFS.DISCONNECTNAME'
     Text

`SOUNDPREFS.GOODTRANSFERNAME'
     Text

`SOUNDPREFS.BADTRANSFERNAME'
     Text

`SOUNDPREFS.RINGNAME'
     Text

`SOUNDPREFS.VOICENAME'
     Text

`SOUNDPREFS.ERRORNAME'
     Text

`SOUNDPREFS.PRELOAD'
     Boolean

The CONSOLEPREFS object
=======================

   This object features no fields, it contains a single line of text:
the console output window specification.

The FILEPREFS object
====================

   Available fields are:
`FILEPREFS.TRANSFERPROTOCOLNAME'
     Text

`FILEPREFS.TRANSLATIONFILENAME'
     Text

`FILEPREFS.MACROFILENAME'
     Text

`FILEPREFS.CURSORFILENAME'
     Text

`FILEPREFS.FASTMACROFILENAME'
     Text

Wanted!
*******

   As of this writing only a single example ARexx script is included in
the `term' distribution (see the `Rexx' drawer). However, it is
desirable to include more sample scripts so more users will be able to
take advantage of the ARexx interface.

   If you wish to share your scripts with the `term' user community,
send them (including documentation) to:

                             Olaf Barthel

                           Brabeckstrasse 35

                           D-30559 Hannover

                      Federal Republic of Germany

                    Internet: olsen@sourcery.han.de