TEL (1)                   BDS C Users' Group                   TEL (1)



     NAME        NAME 
          tel - dumb terminal emulator with file transfer 

     SYNOPSIS        SYNOPSIS 
          tel             tel 

     DESCRIPTION        DESCRIPTION 
          Tel is a considerably modified version of Telnet v2.3, as 
          distributed with v1.46 of the BDS C compiler.  The following 
          features have been added: 
          (1) multiple files may be sent/received by one command 
          (2) directories may be listed 
          (3) the quit command hangs up a hayes smartmodem.  
          To accommodate these changes, some of the command names have 
          been changed.  
          This program uses a modem to emulate a dumb terminal.  
          Incoming data may be buffered in memory and written to disk, 
          data may be transmitted from disk to the modem, or files may 
          be formally transferred in a "checksum" mode with automatic 
          handshaking and buffering.  

     CAVEATS        CAVEATS 
          This program was tested with v1.50 of the BDS C compiler 
          under CP/M 2.2.  It should work with other versions of BDS C 
          and CP/M, but has not been tested.  

     SEE ALSO        SEE ALSO 
          telnet(1),tl370(1) 

     WARNINGS        WARNINGS 
          The checksum file transfer does not follow the XMODEM 
          protocol.  
          Variable baud rate support is present, but commented out.  
          Hardware-specific coding would be required to implement it.  

     BUGS        BUGS 
          Tel assumes that the CP/M console is much faster than the 
          modem (e.g. a 1200+ baud console with a 300 baud modem).  

     NOTES        NOTES 
          Requires local.c and files.c for link.  


















                                      -1-

d from disk to the modem, or files may 
          be formally transferred in a "checksum" mode with automatic