XRPzedzap.doc by Robert Williamson

   XPRzedzap.library is an enhanced version of xprzmodem.library for use in
FTN   sessions.    The  xprzedzap.library  uses  the  3.1  version  of  the
xprzmodem.library   as   its   base   and   uses   the   0.85   version  of
xprzedzap.library  by  Yves  Konigshofer  for FTN-related extensions.  This
version  was  audited  by  Yves and released with his approval of myself as
KOTS for zedzap.

      Since  the  version  0.55  sources  were written for lattice C, I had
decided  to  forget  about them AND the .85 and .90 sources and build a new
one  from xprzmodem v3.1 source.  This source is compilable with SASc v6.51
and  uses  the  libent  and  libinit  modules instead of the old latticelib
assembly stubs.

  The  new  version has virtually all the useful xprzedzap v1.0 options and
features  DirectZap  as  well  and ZedZap, ZedZip, SZmodem and Zmodem.  The
protocol currently active is displayed in the xpr status window.

Mailers and XPR Protocols 

    Many  Mailers  make  use  of  XPR  protocols  to  provide file transfer
capabilities  and  to  gain the advantage of easy addition of new protocols
when they become available.  Those known to use XPP protocols include:

    POP, JAZ, RAP, UMBRELLA, GAZEBO, PORTICUS, ROOF, NORM and JAMMAIL.

   Since  Mailers  perform  a  fast  turaround  from  send  to  receive and
vise-versa,  the XPR design must insure that both echoed characters and any
left  unread  from  the previous transfer do not cause detrimental effects.
While the changes to avoid these problems will not affect term programs and
BBS's   using   xprzedzap.library,   the   lack   of   these   'fixes'   in
xprzmodem.library make it near useless in mailers.

    Mailers  require that a session can be accomplished without reporting a
failure  if  there were no files sent and/or received.  The enhancements in
XPRzedzap.library address this problem.

    Mailers  also  require notification of the status of each file transfer
in a batch.  This is provided by the XPR 3 function upd_status().

    Calculation  of CPS and expected transfer times are based upon the baud
rate.  If the mailer does not set this to the linked rate, the calculations
will  be  based  either  upon  the  Locked  rate or the prefs setting.  The
C<baud> option allows passing the LINK rate for more accurate and realistic
results.

    The maximum packet size can be set with a maximum/default at 8192 and a
mimimum  of  64.   This  will  vary  when  sending  and will be static when
receiving.   When  receiving, it should be 8192 but the maximum packet size
can be set to less than if the local system has a slow HD.
  When sending the maximum packet size will be baud rate dependant, and the
size is calculated with the formula:
                MAX_PACKET = (BPS_RATE * 8192 / 9600).
If C(baud) is passed, the link rate will be used for these allocations.

    The  IO  Buffer  for  reading/writing to/from the disk must be equal to
twice   the   maximum   packet  size  (or  the  maximum  packet  size  will
automatically be decreased).

    Example Protocol Setups for xprzedzap.library and Mailers:

    The defaults for xprzedzap.library are set in such as way as to require
minimal changes for each protocol.


    TN       No Text translation
    OR       Overwrite Resume
    B16      Buffer size 16KB 
    F0       Frame size = filelength 
    E30      Error count 30 
    SN       Do not send full directory path  
    RN       Do not use received full directory path  
    AN       Disable Auto-activate mode  
    DN       Do not Delete after sending  
    KY       Keep partial files  
    P""      Comm progrmas provides Path to use for received files  
    M8192    Maximum packet size 8K 
    C0       Set Link BPS Rate  
    NY       Alow Send if there are no files  
    QN       Disable DirectZap escape only CAN  
    ZY       Enable FTN mode  


    Zmodem      used for user uploads/downloads (GRAB, for example)
                M1024,ZN,C$(Baud)

    SZmodem     It is possible that M8192 will work if the user is using
                SZmodem or 8K-Zmodem.
                M8192,ZN,C$(Baud)

    DirectZap   uses 8K blocks, allows NoFiles transfer, escapes only ZDLE
                and ZDLEE
                QY,C$(Baud)

    ZedZip      uses 1K blocks, allows Nofiles transfer
                M1024,C$(Baud)

    ZedZap      up to 8K Blocks, allows NoFiles transfer
                C$(Baud)

    If  your  mailer  does  not  support  inbound RESUME, you must add 'ON'
(OverWrite Never) to the setup string in order to override the default 'OR'
(OverWrite Resume) and 'KN' (Keep Never) to override the default 'KP' (Keep
Partial).

    The New Setup options: 

    Z   - FTN mode
    The Z option enables FTN operation, when Y, the following is in effect:
        - RxTimeOut is restored to 600ms
        - transfers start with blocksize specified in M option.
        - serialbuffer is cleared before sending/recving.  In FTN
          mode the turnaround from sending to receiveng (and vis-versa)
          is quite fast, clearing the buffer avoids reading echos of our
          own characters or leftovers from the previous transfer.
        - affects selection of protocol name
    
    C<link bps>
    Buffer allocations and calculations of CPS will be based upon LINK rate
    if  passed  with  C<baud> option, otherwise they will be based upon the
    LOCKED rate.
        

    N   - send no files mode (DirectZap,  ZedZip  and  ZedZap protocols)
    It is permitted to have a session without sending or receiving files if
    N  option is Y.  This is required with some protocols in FTN mode so as
    not  to  generate a spurious failure after a mailer session.  This also
    chnages EOF mode from sending CAN's to just sending ZFIN.
        
    Q   - DirectZap mode
    Only ZDLE adn ZDLEE will be escaped is Q option is Y (DirectZap protocol)


Status Display:

    XPR  2.001  support  for  dual-status windows added.  (tested, but note
that  there is no publically available version of wpl.library that supports
this)

    Protocol name displayed will be one of: 
        Zmodem, 1K blocks standard, up to 8K, non-ftn mode
        ZedZap, up to 8K Blocks based upon bps rate, ftn mode
        ZedZip, 1k blocks , ftn mode
        DirectZap, up to 8k blocks, minimum escaping, ftn mode

    Added  localization  for  new  options.   These  are NOT translated for
    german catalog, so that catalog has been removed from distribution.

    During  batch  transfers,  Error  message  field is set to "None" when
    starting to send or receive next file.

wpl concerns:
    XprSetup  does  not  read  any  variables,  so you must set option C to
$(baud)  so  that  all calculations are based upon the actual link rate and
not the locked rate.

   XprSetup makes an XPR library ready for a transfer.  The first parameter
given  is the xpr library name, and the second parameter is a string passed
to  the xpr library with XProtocolSetup().  The variable $(XprSetup) is set
to  the  numeric  return  of  XProtocolSetup().   A  value of 0 indicates a
failure, otherwise the setup was successful.

   Return Values in $(Setup) are or'ed from the following:

        XPRS_FAILURE    0x00000000L 
        XPRS_SUCCESS    0x00000001L
        XPRS_NORECREQ   0x00000002L
        XPRS_NOSNDREQ   0x00000004L
        XPRS_HOSTMON    0x00000008L
        XPRS_USERMON    0x00000010L
        XPRS_HOSTNOWAIT 0x00000020L
        XPRS_NOUPDATE   0x00008000L
        XPRS_XPR2001    0x00010000L *
        XPRS_DOUBLE     0x00020000L *

    *  Note:  private jammail versions of wl.library required both returned
to  enable  dual-status  display.  This is WRONG.  Only XPRS_XPR2001 should
trigger use of dual-status display.

        Normally returns:
    XPRS_SUCCESS | XPRS_NORECREQ | XPRS_HOSTMON 
        | XPRS_DOUBLE | XPRS_XPR2001
    or
    XPRS_SUCCESS | XPRS_NORECREQ | XPRS_DOUBLE | XPRS_XPR2001


   Return values in $(RC) are as follows:
      0 - All OK.
      1 - XProtocolSetup returned FALSE.
      2 - Library not able to be opened
      3 - Out of memory.
      4 - Wasn't given required modem.

    -Robert Williamson

Credits:
-Chuck Forsberg for the original ZMODEM specs
-Rick Huebner for the original xprzmodem.library (--> v2.10)
-William M. Perkins for the 32bit CRC improvements (2.50)
-Yves Konigshofer for the changes to allow ZedZap-type transfers
 and a lot of advice by phone during the conversion process
-Rainer Hess for addition of locale support

Debits:
-Rainer  Hess  for  NOT acknowledging Yves's development.  Many features he
claimed he added first appeared in Yves's sources.