Audio-Handler

THIS INFORMATION IS PROVIDED "AS IS"; NO WARRANTIES ARE MADE.
ALL USE IS AT YOUR OWN RISK, AND NO LIABILITY OR 
RESPONSIBILITY IS ASSUMED.

The audio-handler is the DOS Interface to the audio hardware and its
associated audio.device. It is opened (for example) by using Open()
with the name

AUD:

The mountlist entry does look like the following:

/* Mountlist for Audio Handler */

AUD:	Handler = L:Audio-Handler
	Priority = 5
	StackSize = 2000
	GlobVec = -1
#

This is a generic device. Any channel will be allocated when the 
device is opened, but you will keep the same channel when you feed
more data into AUD: after opening, so that sound output will be
continuous. A different channel might be allocated if the original
channel is stolen by another, higher priority allocation request
by another audio handler task or another program using audio.device.

Once opened, you can feed audio bytes into the handler by using the
AmigaDOS Write() library call. This call will not block if there is
enough space left in the sound buffer. Multiple writes are played
sequentially without glitch. There is no limit in the size of the
write packets.

You will have enough time to supply more data because written data
is immediately processed and the write request is replied immediately
as long there is space in the sound buffers. Guaranteed available time
ranges between number_of_written_bytes/frequency and about 
buffer_size/frequency, where buffer_size is at least 2 kByte.

Of course you can also use the dos packet-level interface and feed
the handler dos write packets. This has the advantage that you can 
wait for write completion as well as other signals. See [2], page 639
for an example of using asynchronous dos packets to copy a file.
There is no limit in the number of packets you can send simultaneously.

Parameters can be given with the device name, to control the volume,
period and priority of the sound output. The syntax is similar to
console names:

AUD:[/OPTIONS]

For a quick test, feed your favourite sample to the audio-handler:

copy audio-handler L:
mount AUD: from mountlist.aud
copy <your_favourite_sample> AUD:

You can also put the AUD icon into your devs:DosDrivers drawer so
it will be automatically mounted when your Amiga executes the
startup-sequence.


OPTIONS may be one or more of the following:

PERIOD p
sets the sampling period (inverse of frequency) of the waveform
to play. The default is to play the sound at 8 kHz sampling frequency.
The minimum period is 124 because of hardware reasons (custom chip DMA
allocation). The maximum is 65535 (size of the WORD custom chip register).
This value goes into the AUDxPER custom chip register. Computing this
value is explained in [3], pages 140-143. You can also specify the
sampling frequency instead with the option explained below. 

FREQENCY f
sets the sampling frequency of the waveform to play.
This is an alternative to specifying PERIOD. The maximum usable
frequency is 28603, the minimum is 55. This value gives the
number of samples (bytes) per second to play.

VOLUME v
sets the overall volume of the sound. Valid numbers range from
0 (silent) to 64 (loudest), which is the default.

PRIORITY pri
is the priority used for precedence managment within the
audio.device. Audio channels with low priority may be 'stolen' by
other applications or different invocations of the audio-handler.
Valid priorities range from -128 (always stoppable) to 127 (unstoppable).
The default value is 0. See [1], page 22 for a suggested value of
priority for different types of sound.

BUFFER size
is the buffer size allocated for sound. As explained above, this
restricts how much time you have to update the buffer (write the
next bunch of samples). The minimum is 4kB to allow for a safe
continuation of play, the maximum is 256kB, allowing for double
buffers of each 128kB, which is the maximum possible for the
Amiga hardware. The buffers use CHIP memory.

DEBUG n
This is an option not normally used which outputs event information
about incoming packets and io requests to the serial port. n is a
number which is added to each information to show which handler
task is doing the output.

The following are special channel requests.

CHANNEL n
is an optional number between 0 and 3 (or maybe up to the number
of supported channels, if ever implemented).

LEFT
The sample is to be played on one of the left channels.

RIGHT
The sample is to be played on one of the right channels.

STEREO
The sample is a stereo sample (alternating bytes) and is to be
played at one left and one right channel simultaneously.
(Not yet implemented)

16BIT
This is set to specify that samples are Words instead of bytes.
This is not yet implemented, anyway, the Amiga Audio hardware
doesn't support it.


Examples:

Playing a sample with a sampling frequency of 4 kHz on a right
channel only:

AUD:FREQUENCY4000/RIGHT

Playing a sample with a smaller buffer (8 KB total, 2 buffers of
4 KB each) and low priority:

AUD:buffer0x2000/priority-100


Technical details:

* Lattice C 5.10 was used to compile the source.

* Stolen channels are not automatically given away, but the lock
  protocol is used. When another process wants to steal the channel,
  the audio handler frees the channel at the next best time.
  This assures that the sample can be played glitch-free, if
  the handler can immediately allocate another channel, and it
  guarantees no sound is lost before the handler can allocate
  a channel again.

* Each invocation of AUD: creates a new handler process, but the
  code and data segment is shared between all processes (resident).


TODO:

* Implement stereo samples.

* Implement 16 bit samples. Might be interesting for 16 bit sound
cards if they have a device similar to audio.device.

* If sampling is implemented at some time, the audio handler might
also be used for reading (sampling) from audio sources. This will
require the user process to read data fast enough to keep in pace
with the sampler.device delivering samples. Might as well use
the parallel.device for well known samplers. 

* Makefiles for other compilers. Volunteers?


The source and executable may be freely used in projects, but a
notice of its origin must be given. If the program is to be included
on a CDRom or disk being sold, one sample must be given to the author.

Comments, ideas, bug reports please to (e-mail preferred):

Martin Brenner
Kaiserstr. 83
52134 Herzogenrath  
martin@ego.oche.de

References:

[1] AMIGA ROM Kernel Reference Manual: Devices, 3rd edition
[2] Ralph Babel: The Amiga Guru Book
[3] AMIGA Hardware Reference Manual, 3rd edition