dass05sc - version 0.92  (08.10.1995)
-some serious bugs removed
-eol remark parsing order changed (look at the lines with '!' remarks)
-echo command expanded ( " )
dass05sc - version 0.92  (29.09.1995)
-additional end-of-line remark command for controlfile operation
-minor changes
dass05sc - version 0.9   (27.08.1995)
-first release

(c)1995 by Klaus Hegemann



INTRODUCTION:

   dass05sc allows you to monitor/disassemble binary data of at least
the Motorola MC68HC05SC21 smart card microcontroller.
Command line operation is supported as well as a 'batch' like control-
file operation (recommended).

   FOR THE QUICKSTARTERS: have a look at the EXAMPLES at the end of
this text.

   There are slight differences between the Amiga and the PC version of
this program concerning the command line syntax. Have a look at
'DIFFERENCES'


BACKGROUND:

   Well, it was hard enough to find a disassembler for the 68hc05 type
   microprocessor until I was told that the 68hc05_SC_ makes use of a
   modified coding of the instruction byte. :-|  And, as far as I searched
   some of the 'motorola stuff'-filled ftp servers and the motorola bbs
   itself in Germany there seemed to be no disassembler for this type of uP
   publicly available. Thanks to Marc Wirth who responded to my complains
   ;-) and supplied me with information about the smart card version of the
   hc05. To cut it short: There was no disassembler, so I had to write one.
   As a result, I added some more features and decided to make it public
   available.


USAGE:

   AmigaOS Template: BINFILE/A,CONTROLFILE=CF/K,START=S/K,END=E/K,
   OFFSET=O/K,PLUSHEXDUMP=DM/S,HEXONLY=M/S

   general Information on template usage:
   '/A': required argument; '/K': keyword, must be placed in front of the
   argument; '/S': switch option; 'WORD1=W1':  WORD1 and W1 do have the
   same meaning. Use as keyword or switch.

   BINFILE:         Filename of the binary to be disassembled.
   CONTROLFILE=CF:  Option: 'batch'-like operation mode (see below). No
                    further command line args needed, except the BINFILEname.
   command line operation:
   START=S:         Specify the start location within the binary for
                    disassembly and hexdump
   END=E:           end location for disassembly/hex dump. If not specified
                    a default of 20 output lines is set.
   OFFSET=O:        If your binary proviedes relocated code, you may specify
                    a signed value to cause the output to appear at a correct
                    location. E.g. your binary contains the smart card memory
                    image $0000 - $1fff with activated 1st codepage and
                    from $2000 - $3fff with activated second codepage:
                    simply specify an offset of -$2000 when inspecting code
                    of the second code page.
   PLUSHEXDUMP=DM:  An additional hex dump is placed on the right side near
                    the disassebled output. Useful e.g. to distinguish
                    between wild code and ascii text...
   HEXONLY=M:       Memory hex-dump option.


EXAMPLES: CLI

   >dass05sc t:bin start=$1000
   >dass05sc t:bin start $1000
   >dass05sc t:bin s=$1000
   >dass05sc t:bin s=4096
   they all produce the same output:
   ====================<begin>====================================
   *** dass05sc V0.9 disassembler for 68hc05sc21 type binaries ***
   (w)1995 by Klaus Hegemann. Freely distributable.
   
   read 16384 data bytes from file 'bin'
   
   1000: 00         rti                
   
   1001: 00         rti                
   
   1002: 00         rti                
   
   1003: 00         rti                
   
   1004: 00         rti                
   
   1005: 00         rti                
   
   1006: 00         rti                
   
   1007: 00         rti                
   
   1008: 00         rti                
   
   1009: 00         rti                
   
   100a: 00         rti                
   
   100b: 00         rti
   ====================<end>======================================

   >dass05sc t:bin hexonly start=$1000 end=$1020
   >dass05sc t:bin m start=$1000 end=$1020
   >dass05sc t:bin m start=4096 end=4128
   each one results in:
   ====================<begin>====================================
   [...]
   read 16384 data bytes from file 't:bin'
   
   1000: 00 00 00 00 00 00 00 00   '........'
   1008: 00 00 00 00 00 00 00 00   '........'
   1010: 00 00 00 00 00 00 00 00   '........'
   1018: 00 00 00 00 00 00 00 00   '........'
   1020: 00
   ====================<end>======================================

   >dass05sc t:bin plushexdump start=$07e9 end=$07fd offset=-$07e9
   >dass05sc t:bin dm s=$07e9 e=$07fd o=-$07e9
   each one results in:
   ====================<begin>====================================
   [...]
   read 16384 data bytes from file 't:bin'

   0000: 2f         txa                0000:    2f 4d 1d 3d 3f 87 37   ' /M.=?.7'
   0001: 4d 1d 3d   jsr   $1d3d        
   0004: 3f 87      stx   $87          
   0006: 37 95      sta   $95          0007: 95 3b 96 93 3a 3b 93 97   '.;..:;..'
   0008: 3b 96      ldx   $96          
   000a: 93 3a      bne   $0046        
   000c: 3b 93      ldx   $93          
   000e: 97 04      beq   $0014        000f: 04 16 06 96 32 3b         '....2;  '
   0010: 16 06      cpx   #$06         
   0012: 96 32      bls   $0046        
   0014: 3b a6      ldx   $a6
   ====================<end>======================================



EXAMPLES: CONTROLFILE:

   In controlfile operation there are some differences/additions:
   The line:
   e "***"
     simply outputs the chars between the two (")s
!  e 27
!    drops the char code 27 (ESCape). useful, if you want to supply
!    e.g. printer control strings. There is only one number after
!    each 'e'-command allowed. However, you may append a string:
!  e 12 "Hello next page !" 
!    performs a form feed and prints the string on top of the next
!    page.
!    Normally, a (CR+) LF is performed after each 'e'-command that
!    comes with a string. You may prevent this by using a '\' as the
!    last character.
!  e "Good morning \"
!  e $30 "0\"
!  e "7 !"
!    these commands will cause the output string "Good morning 007!"
!    (followed by (CR+) LF).
!    You may use this feature, when supplying printer control commands
!    where additional (CR+)LS's aren't needed.
   d <start> <end> <offset>
     will disassemble from <start> to <end> with an offset of <offset>
     No keywords are allowed. <start> and <end> must be specified,
     <offset> may not. You may use hexadecimal Numbers, introduced
     by a '$'. If not, the line parser expects a decimal value.
   d- <start> <end> <offset>
     Suppresses additional blank lines after JMPs, BRAs, STOPs, WAITs,
     etc.
   m <start> <end> <offset>
     Memory hex-dump
   dm- <start> <end> <offset>
     Disassembler dump with additional hex dump, no extra blank lines
     after JMPs, BRAs, etc...
   r <address> <offset> "hmm, doughnuts"
     Adds an end-of-line remark to the disassembled or hex dumped line
     at <address>. You have to supply the same values for <address>
     and <offset> that you have used in the disassemble/hex dump
     command. If you do no supply the offset value, '$0000' will be
     taken as default.
     For each disassemble or hex dump job the remark commands must
     be sorted by their address values. 
!    The eol-remark parser scanns the controlfile sequentially, so
!    each remark line is read only once, i.e. it looks out for the
!    first eol-remark command, then waits until this address occurs
!    before the next eol-remark command will be processed.
     This should not be too much restrictive at all, I think.
     However, it makes the [kind of slow] processing a bit faster.)
     
     
   controlfile 't:control' consists of (without the '>'):
   ====================<begin>====================================
   e "***************************************"
   e "*  lots of zero's                     *"
   e "***************************************"
   m $052a $0543 -$0100
   e "***************************************"
   e "*  some machine code                  *"
   e "***************************************"
   d $0573 $057c
   e "***************************************"
   e "* and now with additional hex dump    *"
   e "***************************************"
   dm $0573 $057c -$73
   e "%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%"
   e "% in jump tables there is no need for %"
   e "% empty lines after JMPs, BRAs,...    %"
   e "%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%"
   d- $0573 $057c -$73
   e "%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%"
   dm- $0573 $057c -$73
   r  $057a -$0100 "hmm, invisible cola"
   r  $0573 "woo-hooouu"
   ====================<end>======================================
   will be used by dass05sc if you supply the 'CONTROLFILE' keaword:
   
   >dass05sc t:bin controlfile=t:control
   >dass05sc t:bin cf=t:control

   that will cause the following output:   
   ====================<begin>====================================
   *** dass05sc V0.9 disassembler for 68hc05sc21 type binaries ***
   (w)1995 by Klaus Hegemann. Freely distributable.
   
   read 16384 data bytes from file 't:bin'
   
   ***************************************
   *  lots of zero's                     *
   ***************************************
   042a:       00 00 00 00 00 00   '  ......'  hmm, invisible cola
   0430: 00 00 00 00 00 00 00 00   '........'
   0438: 00 00 00 00 00 00 00 00   '........'
   0440: 00 00 00 00               '....    '
   ***************************************
   *  some machine code                  *
   ***************************************
   0573: 49 13 bf   jmp   $13bf       woo-hooouu 
   
   0576: 49 14 93   jmp   $1493
   
   0579: 49 14 cf   jmp   $14cf        
   
   057c: 49 14 ab   jmp   $14ab        
   
   ***************************************
   * and now with additional hex dump    *
   ***************************************
   0500: 49 13 bf   jmp   $13bf        0500:          49 13 bf 49 14   '   I..I.'
   
   0503: 49 14 93   jmp   $1493        0505: 93 49 14 cf 49            '.I..I   '  wohooouu
   
   0506: 49 14 cf   jmp   $14cf        
   
   0509: 49 14 ab   jmp   $14ab        
   
   %%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
   % in jump tables there is no need for %
   % empty lines after jmps, bras,...    %
   %%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
   0500: 49 13 bf   jmp   $13bf        
   0503: 49 14 93   jmp   $1493       
   0506: 49 14 cf   jmp   $14cf        
   0509: 49 14 ab   jmp   $14ab        
   %%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
   0500: 49 13 bf   jmp   $13bf        0500:          49 13 bf 49 14   '   I..I.'
   0503: 49 14 93   jmp   $1493        0505: 93 49 14 cf 49            '.I..I   '  wohooouu
   0506: 49 14 cf   jmp   $14cf        
   0509: 49 14 ab   jmp   $14ab        
   
   ====================<end>======================================
   

   In controlfile operation you are supposed to prefer a file
   in wich the information should be dumped.
   To achieve that, simply use the output redirect option that
   comes with your DOS: (Amiga and PC as well)

   >dass05sc t:bin controlfile=t:control >disassembled.txt
   >dass05sc t:bin cf=t:control >disassembled.txt


DIFFERENCES: (usage Amiga <-> PC)

     Only the command line hanling is concerned. On the Amiga, I prefered
   using the command line parser that comes with AmigaOS, rather than
   the ANSI parser supplied with the C-Compiler.
     
   On the PC the command line usage is almost the same:
   * you  must supply the keywords in its short form.
         (e.g. 'CF' insted of 'CONTROLFILE')
   * you must supply a '=' after the keywords.
   
   
BUGS:

     No error messages yet, it simply quits if something's wrong.
   I suggest that you may provoke a crash, if the cli/controlfile syntax 
   becomes too obscure...
   All in all and as you can see it at the version number, this proggi
   is still a kind of 'beta', quick & dirty... but right now there are
   other things (i.e. the next exams) that I ought to worry about.


DISCLAIMER/DISTRIBUTION:

     Both programs, the Amiga and the PC version of this program are
   freely distributible, but they are not public domain.
   The contents of this distribution are copyrigthed matrial, and may not
   be altered without express permission of the author.
     dass05sc may be distributed by any means, electronic or physical,
   provided no charge, other than for small handling fees such as disk
   medium charges, is made.  It may be distributed on commercial electronic
   networking services, provided that no fee is made explicitly for it's
   acquirement, though a general blanket downloading charge is permissable.
   Inclusion on the Aminet and Fred Fish CDs is welcomed due to their long
   standing support of the Amiga.
     I am in no way responsible in any damage that may result in using this
   program or in using of its output. There is no warranty of any kind.

   archive contents:
   
   AmiDass05sc      21428 bytes   executable for Amiga
   PcDass05sc.exe   16206 bytes   executable for PC
   readme.doc       13710 bytes   this text


DONATIONS/GIFTS:
   
   welcome :-) (If you've got a Sky viewing card that you don't need any
   more (e.g. if it is expired [if it says anything else but 'your card
   is invalid'], or you subscribed twice by accident ;-) please don't
   mind to send that one to me...
   

AUTHOR:

   Klaus Hegemann     klausi@higgens.tng.oche.de
   Hirschgraben 13    hegeman@reze-1.rz.rwth-aachen.de
   52062 Aachen
   -Germany-