MapRZ2 V1.1
RetinaZ2mapped V1.1
RetinaZ2mappedRE V1.1

by Christoph Niedeggen 1995-1996


Index

1. Disclaimer
2. Purpose
3. Files in the archive
4. Getting started
5. Principle of MapRZ2
6. Possible Improvements
7. Known Bugs
8. Configuration used by me
9. How to contact me
10. Thanks to

Appendix A: Used Memory Map
Appendix B: MMU address translation settings (68851, 68030)




1. Disclaimer

MapRZ2, RetinaZ2mapped and RetinaZ2mappedRE are in the public domain.  Use this
software at your own risk.  In no event will the author, Christoph Niedeggen, be
liable for any direct, indirect, or consequential damages resulting out of the
use of or inability to use this software.

The program is not in a finished state since I had to stop the development in
January and cannot continue until about July/August 1996 (I am currently
studying in England and my Amiga is still in Germany.)

However, I think it might be useful for some people in its current state and
probably someone already wants to continue the development.  Improvements of the
program for non-commercial purposes are welcome.  Please contact me if you plan
to do so.  Without being able to use my Amiga I am not able to answer all
potential questions, but please feel free to send me comments and suggestions
about MapRZ2.




2. Purpose

The Retina Z2 hardware only supports segmented access to the display memory via
a 64k window.  Normally this is not a problem because the Retina hardware is
accessed by 'retina.library', but some programs benefit from direct access to
the display memory.

MapRZ2 uses an MMU (currently 68851 or 68030) to map the segmented RetinaZ2
memory to a linear chunk in the virtual memory space.

RetinaZ2mapped and RetinaZ2mappedRE (RE = RetinaEmu) are external video drivers
for ShapeShifter which take advantage of MapRZ2.  Because the display does not
have to be refreshed anymore (currently just in 256 colour mode), the emulation
becomes much quicker - the access speed to the display memory is now just
limited by the Retina hardware.  Another big advantage is that no display buffer
in Fast RAM is necessary, thus leaving more memory for the emulation.

Because MapRZ2 is a program on its own, the linear display memory could be used
for other programs as well, e.g.  it might be possible to write a RetinaZ2
driver for the CyberGraphics system.  Up to now the segmented mode has prevented
to write such a driver.




3. Files in the archive

Source/make                    batchfile to generate executables with PhxAss
Source/MapRZ2.asm              source code for MapRZ2
Source/RetinaZ2mapped.asm      source code for SS EVD driver
Source/RetinaZ2mappedRE.asm    source code for SS EVD driver
VGADOC/clock.txt               information about various clock circuits
VGADOC/intro.txt               some information about VGA programming on PCs
VGADOC/ncr.txt                 information about special NCR VGA registers
VGADOC/ramdac.txt              information about various RAMDACs
VGADOC/readme.txt              main readme of VGADOC v4
VGADOC/vgaregs.txt             information about general VGA registers
Video_Drivers/RetinaZ2mapped   SS EVD driver, works without RetinaEmu
Video_Drivers/RetinaZ2mappedRE SS EVD driver, needs RetinaEmu to be running
MapRZ2                         main program
MapRZ2.doc                     this documentation




4. Getting started

- Copy the two files in 'Video_Drivers' to the 'Video Drivers' directory of
ShapeShifter.

- Turn FastROM off.  Otherwise you lose 512 kBytes of memory since this is not
handled by MapRZ2 yet.

- Run the program MapRZ2.  After that it's possible to access the Retina display
memory at $01c00000 - $01ffffff.

- Start ShapeShifter.

- Select one of the new drivers.  The 'RE' version needs RetinaEmu to be
running, the other one runs without it and therefore saves some memory.

- Select 8 bit and enter the desired screen resolution.

- Set refresh rate to 10.  The refresh is just used to set the pointer to the
Bus Error Handler at $8 to the Handler of MapRZ2 after the Mac OS has altered it
and before the Video RAM is accessed.  It might be useful to chose a different
rate for different processors (10 works fine on a 68030 with 25 MHz.)




5. Principle of MapRZ2

The MMU is used to treat the 64k Retina memory window (RMW) and the virtual
Retina memory (VRM) in a special way:

As long as the Retina is accessed the usual way, just the RMW is used.  In this
case, programs access the RMW directly and the VRM is marked invalid for the MMU
so that accesses to it can be detected.

Once the VRM is accessed, MapRZ2 switches to the linear Mode:  Important
registers (see below) of the NRC VGA chip are saved, the VGA chip is set to a
two 32k segments mode (see below), the RMW is marked invalid for the MMU and the
accessed 32k page of VRM is set valid, pointing to one of the two 32k segments
of the Retina.

'Important' VGA registers are any registers which influence the way the 64k
segment is accessed - at least all registers that are changed by
'retina.library' and RetinaEmu.  Since I did not have a documentation to the NCR
VGA chip when I wrote MapRZ2, I found these registers by partially disassembling
the Retina software.  Therefore other registers could be affected as well - even
though I did not realise any misbehaviour with V1.0 of MapRZ2.

The VGA chip offers the possibility to split the 64k segment into two halves.
To use two 32k segments instead of one 64k segment is very useful if display
memory is copied from one location to another, which occurs e.g.  every time a
window is moved.  Otherwise the 64k segment pointer would have to be changed for
every single byte (or longword ;-)

If an invalid page is accessed in linear mode, the 'older' 32k segment is used:
The according page is set invalid, the new page valid and the segment pointer to
the equivalent location.

Finally, if the RMW is accessed again, both valid 32k pages of the VRM are set
invalid, the saved VGA registers are restored and the RMW is marked valid,
pointing to the Retina hardware.




6. Possible Improvements

- FastROM option with support of an already installed FastROM/KickROM

- Option to select the address where the linear Retina memory block is installed
(probably with auto detect of free memory areas)

- Replacement of the 'pflusha' commands by the 'pflush' command (I did not have
enough information about this)

- Support of other processors (68040, 68060)

- Option to uninstall MapRZ2

- Better support of the Bus Error Handler by ShapeShifter (to avoid the altered
use of the Screen Refresh.)  Probably Christian Bauer could implement a new
pointer to the Video Driver Interface that is called just once after the Mac OS
has changed this pointer and before the video memory is accessed.  But even
without this it might be possible to turn off the refresh (or to set the rate
very slow) after it has successfully changed the pointer.

- Better names for the variables and constants related to the VGA chip
(RETINA_REGNUM, RETINA_REGVAL, SEG_..., RetinaRegB, RetinaSeg...).  I chose them
before I downloaded VGADOC, which explains the function of the different
registers and suggests better names for them.

- Support of 4, 16 and 24 bit modes.  Usual refresh routines might be used as I
doubt that other modes than the 8 bit mode are compatible to the NCR VGA chip.

- RetinaZ2 support for the CyberGraphics system.  CyberGraphics needs linear
display memory and therefore it was not possible to write a driver for the
RetinaZ2 yet.  Since MapRZ2 is a program on its own that allows linear access to
the Retina memory, it now should be possible to provide such a driver.  In fact it
should not differ too much from the RetinaZ3 driver, because the used NCR VGA
chips are quite similar.
Since this driver would just use the virtual 'linear mode', it would not be
necessary to save registers of the VGA chip by the Bus Error handler and
therefore this handler could be shorter and quicker.




7. Known Bugs

With the new display drivers, Macintosh debuggers like MacsBug don't work
anymore.  I assume that the Bus Error Exception does not work together with
other exceptions when the debugger is running.

Virtual Memory Systems may not work because they also use the Bus Error Handler.
However, it might be possible to use several Bus Error Handlers in a quite
system friendly way (they have to check if the faulty address affects them and
call the next handler if not.)

The current version uses the memory area $01000000-$01ffffff which might not
work together with some system configurations.

Soft Kickstarts don't work because MapRZ2 doesn't support FastROM yet.




8. Configuration used by me

A2000, OS 3.1, A2630 with 8 MBytes, RetinaZ2 with 4 MBytes and software V2.3,
Evolution V3.0 harddrive




9. How to contact me

until (mid/end) June 1996

  Christoph Niedeggen
  5 Stannington Avenue
  Newcastle upon Tyne
  NE6 5AA
  England

  e-mail: C.W.Niedeggen@ncl.ac.uk

from July/August 1996

  Christoph Niedeggen
  Jodokusstr. 1
  D-53332 Bornheim
  Germany

  e-mail: Eggen@genesis.informatik.rwth-aachen.de




10. Thanks to

Christian Bauer for ShapeShifter
Frank Wille for PhxAss
Martin Apel for ADis
Finn Thøgersen for VGADOC (full version at <http://www.datashopper.dk/~finth/>)
Juergen Wahlmann for beta testing and his help
Christophe Labouisse for useful hints on Retina programming
Escom for continuing the development of the Amiga
Sting for his great music




Appendix A: Used Memory Map

00000000-001fffff     2M Chip RAM (no caching)
00200000-009fffff     8M Fast RAM
00a00000-00bbffff  1792K reserved
00bc0000-00bfffff   256K CIAs (no caching)
00c00000-00d7ffff  1536K Ranger RAM / reserved
00d80000-00dbffff   256K reserved
00dc0000-00dfffff   256K clock chip and Custom Chips (no caching)
00e00000-00e7ffff   512K reserved
00e80000-00efffff   512K AutoConfig area, including Retina hardware (no caching)
00f00000-00f7ffff   512K reserved
00f80000-00ffffff   512K ROM (write protected, might be mapped to FastRAM)

01000000-0101ffff   128K mirrored Retina hardware for access by Bus Error Handler
01020000-0103ffff   128K reserved
01040000-01bfffff 12032K reserved
01c00000-01ffffff     4M linear Retina memory

02000000-ffffffff  4064M mapped linearly




Appendix B: MMU address translation settings (68851, 68030)

31		     15			0
|		     |			|
aaaa aaaa bbbb bb cc c ooo oooo oooo oooo
_________ _______ ____ __________________
 A-FIELD  B-FIELD  C-F  Remaining Offset

page size at level C:  32 KBytes
page size at level B: 256 KBytes
page size at level A:  16 MBytes