FIFO.DOC

		 Placed in the public domain by Matthew Dillon

		Last maintainer:

			 Jörg Höhle (Joerg.Hoehle@gmd.de)

		Version 38.2


    (1) INSTALLATION

	To Install the system you must install both FIFO-HANDLER and
	FIFO.LIBRARY.

	1> lharc -r -x -a x fifolib38_1.lha
	1> Copy l/fifo-handler l:
	1> Copy libs/fifo.library libs:
	1> Copy bin/RemCLI C:		(or anywhere in your path)

	THERE IS NO MOUNTLIST OR MOUNT FOR FIFO: ... To start the handler
	and make FIFO: available to programs, you must RUN it from your
	startup-sequence.  Generally the easiest way to do this is to
	include the following line:

	run <nil: >nil: l:fifo-handler

	IF YOU HAVE A FIFO: ENTRY IN YOUR MOUNTLIST, PLEASE DELETE IT TO
	PREVENT ACCIDENTLY TRYING TO MOUNT IT.

    (2) SIMPLE EXAMPLE TO GET YOU STARTED

	This is a simple example to get you started.  Please refer to
	section (3) below for a description of the options.

	1> Type fifo:pipe/r
	1> run Type s:startup-sequence >fifo:pipe/wmKe

	This particular examples requires that the reader be started first
	(due to the 'K' flag in the writer) but also allows you to ^C the
	reader (the first Type command) without locking up the writer.

    (3) USAGE FOR FIFO:

	FIFO: is like PIPE: but is based on fifo.library rather than its
	own implementation.  Full master/slave support exists.	Since FIFO:
	uses fifo.library, programs that require non-blocking IO capability
	can access one side of a FIFO: connection via the fifo.library
	instead of FIFO:

	The implementation of FIFO: and fifo.library is a billion times
	better than that for my original PIPE: handler.

	The primary difference with FIFO: is that it is based on a
	MASTER-SLAVE connection.  Two MASTER-SLAVE connections going in
	opposite directions yields a full-duplex connection.  When using
	FIFO: to direct one program's output to another's input you must
	explicitly specify one of the FIFO:'s to be the master and the
	other the slave, as well as specify read & write flags.  The
	general format for accessing the FIFO: handler is as follows:

	    FIFO:<name>/<flags>

    <name>:    a valid fifo name

	name may be any combination of alpha numerics up to 125 chars long,
	and is case sensitive.	FIFO: will append either "_m" or "_s" to
	the name it supplies to fifo.library depending on whether master
	mode or slave mode is selected.

    <flags>:	a valid combination of flags

	r   open for read.  Allows you to read from this fifo.

	w   open for write.  Allows you to write to this fifo.

	rw  open for read & write (full duplex).  This opens a
	    full duplex connection, generally useful only in
	    remote-shell applications.

	c   open in cooked mode - must be specified on one side only,
	    usually the slave side.  Any data received by the slave
	    side is cooked before continuing on to the slave.  When used
	    with the 's' flag, this allows the slave side, usually a
	    shell and/or program, to change between cooked and raw mode
	    with the standard SetMode() call.

	e   EOF mode (when combined with 'w').  When this file handle
	    is closed, an EOF will be sent to the other side.

	    If not specified, you can cause several programs to 'append'
	    their output onto a single FIFO all of which is read by a
	    single program.  This can be useful in log-recorder
	    applications, for example.

	    Specifying the 'e' flag generates an EOF after the last byte
	    of data is written to the FIFO and the writer closes it.  A
	    reader will read the data and then receive the EOF, generally
	    terminating reader operations.

	k   KEEP mode.	If a writer opens a fifo, writes data, then
	    closes the fifo before a reader has a chance to open the
	    fifo, this flag prevents the data from being lost.

	    If not specified, the data will be lost.  Generally you
	    want to specify this flag.

	K   READER REQUIRED mode.  When specified, any Write() operation
	    to a fifo for which there is no reader will FAIL.  This will
	    prevent lockups from occurring when you use FIFO: to pipe
	    several processes together and then ^C the last one.

	    ** This can be an important option to use to prevent hung
	       processes!!! **

	m   select master side (else slave).  For example, the master
	    side writer "mw" is paired with the slave side reader "r":

			mw   -> r
			mr  <-	w
			mrw <-> rw

	    When operating a pipe where you have a writer into the fifo
	    and then a reader from the same fifo, one of the two must
	    be a MASTER, with the 'm' flag specified, and the other side
	    must be a SLAVE, with the 'm' flag NOT specified, as per
	    the example in section (2).

	t   tee read.  Usually specified "rt" or "mrt" depending on what
	    you want to monitor.  This option causes the read stream to
	    be a copy of available read data such that it does NOT
	    interfere with other readers.

	    Otherwise this fifo will compete with other fifos for read
	    data.  For a remote shell, tee operation is not desireable
	    as a default but is useful to monitor the shell from an
	    independent program.

	    see the REMCLI example below.

	s   SHELL mode, creates a separate message port for the handle,
	    allowing the shell & programs to find their STDERR handle
	    (i.e. the open-* and Console: packets work properly) and
	    allowing the use of WaitForChar().

	    WARNING: use of this option increases overhead in the FIFO:
	    device and is generally required to be specified for the slave
	    side of a shell (i.e. NewShell fifo:name/rwkecs)

	    see the REMCLI example below.

	C   Send ^C to all (slaves or masters)
	D   Send ^D to all (slaves or masters)
	E   Send ^E to all (slaves or masters)
	F   Send ^F to all (slaves or masters)

	    You can send one or more signal to all the slaves (or masters
	    if 'm' is also included) using these flags.  Note that it is
	    not necessary to open a file handle to so, specifying a
	    string like this:

		"FIFO:fubar/C"

	    would result in sending a ^C to all fubar slaves even though
	    the Open() fails due to the lack of a 'r' or 'w' in the
	    specification.

		     SEE REMCLI.C FOR EXAMPLE IMPLEMENTATION
		     OF COOKED MODE AND SIGNALS.


    (4) TECHNICAL, INTERACTION BETWEEN FIFO: and FIFO.LIBRARY

			       LINKED FIFOS

    FIFO: provides a full duplex connection using TWO fifo.library FIFOS.
    Opening a fifo in master mode verses slave mode determines which
    names are used for reading and writing.  You should note that when
    a FIFO: handle is opened for both read and write, reading from the
    handle actually accesses a different physical fifo than writing to
    the handle.  Opening a FIFO: for only one direction ('r' *or* 'w')
    results in a half duplex connection.  It is important to properly
    specify the rw modes for the fifo.

	     FIFO: device		     fifo.library

	Open("FIFO:junk/w", 1005);              junk_s
	Open("FIFO:junk/r", 1005);              junk_m
	Open("FIFO:junk/rw",1005);              junk_s (w), junk_m (r)

	Open("FIFO:junk/wm", 1005);             junk_m
	Open("FIFO:junk/rm", 1005);             junk_s
	Open("FIFO:junk/rwm", 1005);            junk_m (w), junk_s (r)

    (5) REMOTE SHELL APPLICATIONS

	It is extremely easy to set up a fifo to interface a program with a
	remote shell.  The FIFO: fully supports remote shells including the
	ability to propagate ^C through ^F and handle stderr ("*","CONSOLE:").

	Not only that, but programs which need to be able to access the
	master side of a shell in a non-blocking fashion may access the
	master side directly through FIFO.LIBRARY calls.  See FIFOLIB.DOC
	for the function call list, see REMCLI.C for a working example.

	1> NewShell FIFO:name/rwkecs
	1> run >nil: RemCLI name

	Generally the shell is run off the slave side and the controlling
	program is run off the master side.  The side that runs the shell
	MUST specify the 's' option, as shown above.  Here is a description
	of the flags used in the NewShell line:

	rw  full duplex connection.  shell 'reads' from the master and
	    'writes' results back to the master.

	k   if slave side is started up first, as in the above example, any
	    writes it does will NOT be lost.  Not really required since the
	    slave side shell does not endcli itself.

	e   when slave side closes the handle, an EOF will be sent to
	    the master side.

	c   run slave side in COOKED mode.  FIFO: will do command line
	    editing on any data sent to the slave side.  You do not specify
	    COOKED mode for the master side.  I repeat, do NOT specify
	    cooked mode for the master side.  (you can't in the above
	    example since the master is the 'RemCLI' program.

	    note that in COOKED mode, FIFO: echoes characters received on
	    the slave side back to the master, just like the console
	    device.

	s   SHELL support, required on the slave specification when run
	    from NewShell, causes the handle to get its own message port
	    (required to support Open("*", ...) and for WaitForChar() and
	    SetMode() to work)

	NOTE:  YOU CAN RUN 'RemCLI name' MULTIPLE TIMES SIMULTANIOUSLY
	USING THE SAME FIFO NAME.  All RemCLI's talking to the same shell
	will get all output from the shell and additionally be able to
	issue commands.  This can be extremely useful as a monitoring tool.

	    1> run >nil: RemCLI name
	    1> run >nil: RemCLI name

	You can also capture all shell interaction with this:

	    1> copy FIFO:name/rmt t:capture

	The 't' (TEE) specification is required to ensure you do not screw
	up any other readers.  There is no limit on the number of 'readers'
	monitoring a named fifo.  The RemCLI program uses the fifo.library
	to access the master side and thus TEEs automatically.

	If RemCLI tries to talk to a fifo that does not exist, it will
	'freeze' until the slave side does exist.  Meaning you can run
	RemCLI before you start up the shell.

	CLOSING THE REMCLI WINDOW DOES NOT END THE SHELL.  You must type
	'endcli' or 'endshell' to cause it to exit.  On the other hand,
	closing the RemCLI window and then reopening will yield the
	previous shell (which never exited).


				PIPING

    You can use the FIFO: device to pipe output from one program to the
    input of another.  Note that you want to be sure to use the 'k' flag
    in case the program generating the output generates only a little (and
    is able to exit before you have a chance to start the reader).  You
    also want to use the 'e' (EOF) option or the reader will not receive
    an EOF, and you must make one side a master.

	1> Type s:startup-sequence >FIFO:xx/wkme
	1> Type FIFO:xx/r

    Note that Type is inadequate for piping a file because it writes one
    line at a time, increasing overhead. Prefer Copy or cat commands which
    use larger buffers.

    If you do not specify the 'e' EOF option then you can run multiple
    programs' output through the pipe sequentially, specifying the EOF
    option only for the last one.

    WARNING:	If you ^C the reader before it gets the EOF and exits
    on its own, and if the writer is still writing, the writer will
    freeze up when the fifo becomes full (requiring a reader to unfreeze
    it).  Additionally, if the 'k' option is not used, even if the writer
    does not freeze up there may be unwanted data left in the fifo even
    though nobody is referencing it.

    To safely recover from a broken reader, the program controlling the
    pipe must do the following steps:

	(1) break the writer if it has not exited (but it may be frozen,
	    so...)

	(2) open a reader /r and a writer /wme, then immediately close
	    the writer.

	(3) read from the reader until EOF.  Even if the original writer
	    had already exited, the fact that you open and close a dummy
	    one will regenerate the EOF.


    It is currently a bug that EOF is sent continuously to readers, but
    this helps avoiding to freeze or to lock up. A future flag may be added
    to send EOF once only, which is useful in shell applications.