$Id: CRC.DOC 1.3 1997/10/25 02:11:00 brian Exp $

                      crc.doc : The 'crc' command
                          By:  Brian E. Yoder.

        (c) Copyright International Business Machines Corporation 1997
        All rights reserved.

The crc command is used to record the length and 16-bit CRC value (or,
optionally, the 32-bit CRC value) for one or more files.

The code used to calculate the 16-bit CRC value for an individual file
was developed at IBM Austin, Texas, by Jim Czenkusch. The code to
calculate the 32-bit CRC has enhancements to pre- and post-condition
each value so that it is compatible with the 32-bit CRC value generated
by PKWARE's PKZIP and Info-ZIP's zip programs.

========================================================================
Command syntax
========================================================================

        crc [ -s ] [ -l ] fspec ...

The program gets the length and calculates the CRC value for each file
that matches the given file specification(s). If -s is specified, then
the program recursively descends into subdirectories looking for files
that match the file specification(s).

If -l (letter el) is specified, then crc generates 32-bit (long) CRCs
that are compatible with those generated by PKZIP. The default is to
generate 16-bit CRCs.

Each file specification consists of some combination of drive, path, and
filename. The filename may contain AIX shell pattern-matching
characters. See the pattern.doc file for a description of filename
pattern matching.

For each matching file, the crc program writes one line to standard
output as follows:

        length  CRC  "filename"

The length is displayed in decimal format. The CRC is displayed in
hexadecimal format with a leading '0x'. The filename is enclosed in
double quotes in case it contains embedded spaces or other puncutation.

========================================================================
Examples:
========================================================================

1. I entered the following command on my system (a very long time ago, I
   might add!):

                crc *.h \*.sys

   It produced the following output:

                3159  0xD65B  BMTBL.H
               10780  0x5495  UTIL.H
               15473  0x064B  REGEXP.H
                 178  0x4E87  \CONFIG.SYS

2. I entered the following command on my system:

                crc -l crc.doc

   It produced the following output:

                2409  0x070E5D3F  CRC.DOC