ÖÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ·
         º          Liquid Tracker module (LIQ) file format            º
         ÓÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ½

     (C) Nir Oren, 1995. May be freely used by any programmer.

    ÕÍÍÍÍÍÍÍÍÍ¸
    ³ Header  ³
    ÔÍÍÍÍÍÍÍÍÍ¾

   Offset  Length   Description
   ------------------------------------------
     00h     14     'Liquid Module:' (Magic ID)
     0Eh     30     ASCIIZ module name
     2Ch     20     Artist Name
     40h      1     1Ah
     41h     20     Tracker Name
     55h      2     Format Version - currently 0100h   (Read note*)
     57h      2     Initial speed
     59h      2     Initial BPM
     5Bh      2     Lowest note (Amiga Period*4)
     5Dh      2     Uppest note (Amiga Period*4)
     5Fh      2     Number of tracks
     61h      4     Module flags (1=cut upon limit  2=ST3 compatibility mode)
                                  The loader should mask out the unused bits
     65h      2     Number of Patterns in file
     67h      2     Number of Instruments in file
     69h      2     Number of Sequence Table entries in file
     6Bh      2     Module header size (usually 6Dh+(Number of Tracks)*2+
                                        Number of Sequence Table entries)
     6Dh  NumTracks    Initial Channel Panning setup
     ...  NumTracks    Initial Channel Volume setup
     ...  NumSequence  Sequence Table Data
  
  *  A note about the Format Version - a loader should try loading even
     if the LSB of the Format Version is different from what it knows
     (used when wanting to add more info to the header but leaving the
     format compatible) only if the MSB byte is different, the loader
     is not able to handle it.


  ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
  ³  Patterns data     ³
  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

      - For empty patterns, a 4-byte value of '!!!!' will be found here

        else:

      ?       4     Magic "L","P",00h,00h  (ID, for recovery purposes)
   +04h      30     ASCIIZ Pattern name
   +22h       2     Number of Intervals per Track (usually 64)
   +24h       4     Size of packed Pattern
   +28h       4     Reserved
   +2Ch       ?     Packed Pattern data

   Packed pattern data is stored full Track after full Track from the left to
   the right (all Intervals in Track and then going Track right). You should
   expect 0C0h on any pattern end, and then your Unpacked Patterndata Pointer
   should be equal to the value in offset [24h]; if it's not, you should exit
   with an error.


      Each row in track consists of 5 bytes:

      1-Note (0-107 representing 9 octaves)  -1 = No note   -2 = Note Off
      2-Instrument (0-99)    -1 = No instrument
      3-Volume (0-64)        -1 = No volume change
      4-Effect ('A' to 'Z')  -1 = No effect
      5-Parameter (0-255)

      Unless:
      -------
      if NOTE = 0C0h then STOP PATTERN DECODING, go to next
      if NOTE = 0A0h then STOP TRACK DECODING, go to next
      if NOTE = 0E0h then SKIP xx EMPTY NOTES (xx-1 specifies in next byte)
      if NOTE = 080h then SKIP ONE EMPTY NOTE
      if NOTE = 0E1h then SKIP xx EMPTY TRACKS (xx-1 specifies in next byte)

      if (NOTE > C0h) and (NOTE < E0h) then

                         if NOTE & 1 then NOTE follows
                         if NOTE & 2 then INSTRUMENT follows
                         if NOTE & 4 then VOLUME follows
                         if NOTE & 8 then EFFECT follows
                         if NOTE & 16 then PARAMETER follows

      if (NOTE > A0h) and (NOTE < 0C0h) then
       same as before, except there is a byte following specifies
       how many Intervals(-1) this packing method will last.

      if (NOTE > 80h) and (NOTE < 0A0h)
       same as before ( NOTE & 31 indicates packing method, and
       byte after there's Intervals count(-1) indicator), but there's just
       one note specified after, which is duplicated on all the Intervals.

   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
   ³ Instrment data  ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

      - Just a series of LDSS files (Read in LDSS.DOC)

      - For empty instruments, a 4-byte value of '????' will be found.


      Currently, the Liquid Tracker only supports DIGITIZED INSTRUMENTS,
      The samples format used here is the LDSS (Liquid Digital Sample
      Specification) so you will simply found here a series of LDSS files,
      in the sum specifies in "Number of instruments" in the header.
      NOTE that any file offset indicated in the LDSS header is relative
      to it's header start position, of course.

 ÖÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ= CONTACTS =ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ·
 º                                                                          º
 º  Fear Of The Dark BBS - (972)-3-9690371 - 28k - 24 Hrs                   º
 º  Anesthesia (A) BBS   - (972)-7-9971505 - 28k - 24 Hrs                   º
 º                         (972)-7-9954490 - 14k - 24 Hrs                   º                             º
 º                                                                _______   º
 º                                                               \     \_\  º
 º                                                               / \_______\º
 º   You can cont(r)act the author by:    ³      SnailMail:  ||__\       |  º
 º                                        ³                 (øø ________/   º
 º FidoNET: 97:200/215, 2:403/442         ³   Nir Oren                      º
 º -------------------------------------  ³   P.O. box 8180                 º
 º InterNET: nir.oren@tbu.excellnet.co.il ³   Petah Tikva 49181             º
 º                                        ³   Israel  <reply guaranteed!>   º
 º                                        ³   (The SNAIL is (C) !!! ;-)     º
 ÓÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ½

                               ---- EOF ----