ÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜ
		  Ý                                    Þ
		  Ý         ARFBUILD.EXE  and          Þ
		  Ý ARFMAIN.BIN -- THE RESIDENT DRIVER Þ
		  Ý                                    Þ
		  ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	Overview: ARFBUILD.EXE, ARFMAIN.BIN, and ARFDISP.BIN....1
	What is an Anti-Virus "Shield"?.........................2
	Installation - using ARFBUILD.EXE.......................3
	Possible Warnings from ARFBUILD.EXE.....................5
	Loading ARFMAIN via CONFIG.SYS..........................7
	Errors During Boot......................................8
	Warning Messages: From an INJECTed MODULE..............10
	Warning Messages: From the AV Shield...................11
	    Common Warnings....................................12
	    More Serious Warnings..............................16
	    (What to do if you get a virus)....................16
	Command-Line Switches..................................18
	SOME FINAL NOTES:......................................21
	    False Alarms.......................................21
	    Why Ours Is The Best...............................23
	    A Special Note For Windows(tm) Users...............26
	    Known Conflicts with other Software................27

	   This manual and accompanying software are copyrighted
	    (c) 1995 Leonard P. Gragson and Stephen M. Poole,
			  All Rights Reserved.
	   Revision history: Updated June, 1995.


								Page 1

	INTRODUCTION AND OVERVIEW
	ßßßßßßßßßßßßßßßßßßßßßßßßß

	The first version of ARFMAIN.BIN simply provided display functions
	for INJECTed modules.  By moving the bells and whistles into a
	separate driver, we could reduce the size of the injected module
	without compromising protection.  But then we wondered: why not
	let the driver perform some anti-virus shielding of its own?

	The more we looked at it, the more intrigued we became.  First,
	(as of this writing, anyway), very few viruses attack device dri-
	vers; we'd gain that advantage to start with.  Plus, a device dri-
	ver would get into the system during the actual bootup process,
	and could thus begin protecting the system sooner.  Thus, we deci-
	ded to implement the idea, and ARFMAIN.BIN came into existence.

	If you've unzipped this package, and have been looking for ARFMAIN
	.BIN and can't find it, you're not crazy.  For a number of reasons
	(discussed below), we instead provide a special program (ARFBUILD
	.EXE) that will custom-build the  ARFMAIN.BIN driver for your PC.
	
	You DO get the original version of the driver, ready-to-install as
	ARFDISP.BIN.  This is a display-only driver which DOES NOT contain
	any anti-virus protection.  This should only be used if you're
	sure that the shield in ARFMAIN.BIN conflicts with your system.

	Finally, a note to novice computer users: Device drivers, by nat-
	ure, are kindof picky, and sometimes this discussion will get a
	little technical-sounding.  But don't let that put you off; it's
	really not as complex as it may sound.  We've tried to provide
	detailed instructions here, and you can contact us if you have
	questions or problems.

	      Leonard P. Gragson    - Compuserve: 73131,1034
				    - America On-Line: Arfman2
	      Stephen M. Poole, CET - Compuserve 71234,3263
				    - America On-Line: SMPoole


								Page 2

	WHAT IS AN ANTI-VIRUS "SHIELD"?
	ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	Images of Byzantine soldiers with shields and helmets come to
	mind, but this is pretty simple.  An anti-virus "shield" does just
	as its name implies: it helps "shield" your system from a virus
	infection.  Precisely how it does this will vary from one shield
	to the next, and some are more effective than others.

	Your PC, while extremely easy to use and update, contains some
	glaring weaknesses in the security department.  The worst is that
	just about anyone can do anything to any file without being chal-
	lenged.  An eight-year-old kid could write a program in QBASIC
	that could eat half the files on your hard drive ... and the com-
	puter would cheerfully comply without complaint.

	It would only be afterwards, when you started getting "Bad Command
	or File Name" and discovered that you just gained 1.5 zigabytes of
	free space on your drive that you would realize that something
	strange had happened.

	An "anti-virus shield" (also called a "behavior blocker") warns
	you when something like this happens and gives YOU the final say-
	so over whether it should happen.

	We feel (not surprisingly) that our shield is the best available
	for a number of reasons.  Just one example: our shield checks a
	number of undocumented system calls and data areas, which many
	anti-virus shields ignore.

	ARFBUILD.EXE was written in hand-coded assembler for speed and
	compactness, and the resulting driver is full of Hacker's Tricks
	and Other Wierd Stuff.  The driver takes up only about 8K of mem-
	ory and is lightning fast, and yet, it still manages to check eve-
	ry critical system call for suspicious activity.  It's so fast,
	in fact, you'll normally never even notice that it's there.


								Page 3

	INSTALLATION
	ßßßßßßßßßßßß

	    BASIC PROCEDURE
	    ßßßßßßßßßßßßßßß

	Installing ARFMAIN.BIN on your system may be different from what
	you're used to.  Here's how you do it (INSTALL may have already
	done some of this for you):

	1 - Use DOS's FORMAT /S to create a bootable floppy that you can
	    use in case of problems.  (This is a must-have whether you use
	    our stuff or not!)  Don't put a CONFIG.SYS or AUTOEXEC.BAT on
	    this floppy; we want a "clean-boot" floppy. Copy ARFBUILD.EXE,
	    LOAD.COM (PRO-BOOT), and INJECT.COM onto the floppy.

	2 - Boot onto the floppy and run ARFBUILD.EXE; it will create an
	    ARFMAIN.BIN driver on the floppy that's unique for your PC.
	    (If you get warning messages, go to the next section.)  Copy
	    the driver onto your hard drive.

	3 - Remove the floppy, label it "ARF Recovery Disk", WRITE-PROTECT
	    IT, and store it in a safe place.  (To write-protect a 3.5"
	    floppy, you slide UP the little tab on the back so that light
	    can get through the hole.)  That floppy is your main line of
	    defense if you ever suspect a virus.  This is important:

		 ALWAYS CHECK THE WRITE-PROTECT TAPE OR TAB BEFORE
		     YOU INSERT THAT DISK INTO ANY DRIVE SLOT!

	4 - Use DOS's EDIT command (or some other ASCII TEXT editor) to
	    add a line such as this one

			      DEVICE = ARFMAIN.BIN

	    ... to the end of your CONFIG.SYS file.



								Page 4

	5 - Reboot the system.  Don't use CTRL-ALT-DEL; cut it off, wait
	    a few seconds, then cut it back on.  ARFMAIN.BIN will then be
	    loaded in memory, and will begin protecting your system.

	    AN IMPORTANT NOTE!
	    ßßßßßßßßßßßßßßßßßß

		IMPORTANT!  THE ARFMAIN.BIN PRODUCED BY ARFBUILD.EXE
		IS UNIQUELY CONFIGURED FOR THE MACHINE ON WHICH IT
		WAS CREATED.  IF YOU TRY TO RUN IT ON A DIFFERENT
		COMPUTER, YOU'LL GET CHAOS AND WIERDNESS (OR WORSE).
		DON'T DO IT!

	If your friend wants an ARFMAIN.BIN on his/her PC, take all this
	stuff over to their computer and build a unique ARFMAIN for THEIR
	computer.  (Do it; they'll think you're a computer wizard.)
	
	Feel free to do this, too.  Remember, we don't require a registra-
	tion fee of home users.  We want this software in as many hands as
	possible; see REGISTER.DOC for details.

	ARFBUILD accepts one command-line argument -- a different name for
	the ARFMAIN.BIN driver.  For example, if you use

			    ARFBUILD MYDRIVER.SYS

	... the created driver will be named "MYDRIVER.SYS" instead of
	ARFMAIN.BIN.  If you do this for more than one PC, why not use
	different names for each computer?  For example, you might have
	drivers named "MYHOME.SYS,"  "HELENS.SYS", and so on.

	For simplicity, we'll use the default "ARFMAIN.BIN" in all of our
	documentation, but obviously, you should substitute your name for
	the driver in everything that follows.



								Page 5

	    POSSIBLE WARNINGS FROM ARFBUILD.EXE DURING THE BUILD
	    ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	You could get one or more of these warning messages from ARFBUILD
	as it constructs ARFMAIN.BIN on your system:
	
		Your interrupt 13h vector isn't in the expected place
		ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	The eyes of most novice computer users just glazed over, but all
	this means is that ARFBUILD.EXE didn't find the entry point for
	the BIOS disk services where they should be.  Did you run ARF-
	BUILD.EXE on a clean-booted floppy?  If not, you should!

	If you get this warning message when building on a clean boot,
	you probably have some type of virus already in your computer.
	Try booting, and then building, from a known-good floppy that was
	prepared on some other machine.  If this message goes away, bad
	news; that's almost certainly the case.  Contact us for informa-
	tion on cleaning the virus, or use a commercial cleaning program
	(this may not work if it's a very recent virus; contact us).

		Can't read the MBR/SBR from the hard drive
		ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	This warning means that ARFBUILD.EXE couldn't read (or find) the
	boot sectors of your hard drive with a direct hardware call.  A
	number of things could cause this problem:

	1 - Your hard drive isn't bootable; you boot from a floppy, and
	    use the hard drive for storage only.  If that's the case, you
	    can't use ARFMAIN; ARFMAIN is basically a bootable hard-drive
	    protector.  ARFMAIN won't work at all on all-floppy systems.
	
	2 - Your hard drive isn't accessible; check your CMOS SETUP and
	    make sure the hard drive is installed properly.



								Page 6

	3 - Your BIOS isn't 100% compatible with the PC (pretty rare now-
	    days), or you're not using a 100% compatible DOS (also rare).
	
	4 - You possibly have a boot-sector virus (not likely if you get
	    this message by itself, and no other warnings appear once the
	    driver is installed and in operation).

	5 - You may have an old, sluggish hard drive.  In this case, just
	    try ARFBUILD.EXE again.  If you get this warning after repeat-
	    ed tries, move on; you'll have to live with it.

	If it can't read the boot sectors, ARFBUILD constructs a default
	ARFMAIN.BIN driver that doesn't check the boot sectors on bootup.
	If that "default" build won't work properly on your system, you
	may have to use ARFDISP.BIN and do without the resident shield.

		WARNING: The boot material read via INT 13h
		doesn't match the material read directly!
		ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	To check for a virus that may already be in your system, ARFBUILD
	compares boot material read via the disk services to the same boot
	stuff read directly via hardware; it should be identical.

	You SHOULD NOT get this message.  If you do, that's not a good
	sign.  Try this: boot from a floppy that was formatted on a diffe-
	rent, known-clean computer, then run ARFBUILD.EXE.  If this mes-
	sage DOESN'T appear, that's a positive indication that you have a
	resident virus hiding in your hard drive's boot material.

		Can't Create ARFMAIN.BIN
		ßßßßßßßßßßßßßßßßßßßßßßßß

	Either the disk is full, or is write protected.  For some reason,
	ARFBUILD.EXE can't write the finished product out to disk.  Try a
	different disk, or delete some unneeded stuff to make room.



								Page 7

	LOADING THE DRIVER VIA CONFIG.SYS
	ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	Once the driver has been built and copied into the desired sub-
	directory on your hard drive, you simply place a line such as

			     DEVICE=ARFMAIN.BIN

	in your CONFIG.SYS file.  (Of course, if you've renamed the driver
	you should use your new name instead of "ARFMAIN.BIN".)  The next
	time you boot up, ARFMAIN will be in memory, and will start prote-
	cting your system.

	Time for a Power User Tweak Tip.  If you have a 386 or better,
	later versions of DOS and some third-party memory managers (ex.,
	QEMM(tm)) will permit you to load ARFMAIN or ARFDISP high in mem-
	ory.  This frees up more conventional memory for other programs.
	Under DOS 5/6, you'd use the "DEVICEHIGH=" syntax; see your memory
	manager's documentation for more details.

	One warning: if you're using an advanced memory manager that relo-
	cates the BIOS and moves RAM into that space (such as QEMM(tm)'s
	"stealth" feature), ARFMAIN.BIN will not work in a segment above
	F000h.  Refer to your documentation to see how to force it lower
	in memory.  Refer also to your DOS manual for more on CONFIG.SYS.

	    IF YOUR SYSTEM HANGS
	    ßßßßßßßßßßßßßßßßßßßß

	(The poor novice user now has a mental image of the computer
	swinging lifelessly from a noose of rope.  A "hang" is when your
	system just stops working -- it "hangs up" -- and won't accept
	any input from the mouse or keyboard.  The only cure is to reboot.
	You may have to switch the computer off, wait a moment, and then
	switch it back on, if it has a really bad case of the hangs.)



								Page 8

	Those who've used DOS for a while, especially those who've inst-
	alled device drivers, know that the system could hang if anything
	goes wrong during the boot.  DOS Version 6 (finally!) added the
	ability to boot "clean" by holding the F5 key during the boot.  If
	your system hangs, you can use the F5 key under DOS 6; under earl-
	ier DOS versions, you'll have to use a bootable floppy.

	Once you get the system booted and on line, the quick-fix is just
	to delete ARFMAIN.BIN, then boot again normally.  (DOS may warn,
	"Bad or Missing ARFMAIN.BIN," but that's OK.)  If you determine
	that ARFMAIN isn't compatible with your system, use ARFDISP inst-
	ead.  In the unlikely event that ARFDISP is also incompatible, you
	may have to do without both shield and detailed error messages.

	ERRORS DURING THE BOOT LOAD
	ßßßßßßßßßßßßßßßßßßßßßßßßßßß

	Now we have a second tier of messages: those displayed by ARFMAIN
	while it's being loaded during bootup.  You should see something
	like:

	   ÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜ
	   Ý                                                        Ý
	   Ý    ARF Resident Anti-Virus Utilities, version 2.1.     Ý
	   Ý    (c)1995 Leonard P. Gragson and Stephen M. Poole     Ý
	   Ý                 All rights reserved.                   Ý
	   Ý                                                        Ý
	   Ý      Checking memory location ...   OK                 Ý
	   Ý      Checking DOS Version ...       OK                 Ý
	   Ý      Checking MBR/SBR ...           OK                 Ý
	   Ý      Checking program code ...      OK                 Ý
	   Ý                                                        Ý
	   Ý      Installation completed successfully!              Ý
	   Ý                                                        Ý
	   ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß



								Page 9

	Each of the self-check lines indicates "OK", so the driver was
	installed properly.  If an error occurs, though, you'll see an
	error message under the line that announced the check:

		Trying to load above F000h
		ßßßßßßßßßßßßßßßßßßßßßßßßßß

	As mentioned above, the ARFMAIN.BIN driver won't work if you have
	a memory manager that tries to load it above segment F000h.

		Your DOS version is too old
		ßßßßßßßßßßßßßßßßßßßßßßßßßßß

	Self-explanatory; go buy a new DOS!  All of the ARF utilities
	require at least DOS 3.3.

		Boot records have been altered!
		ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	Something has altered the boot record code on the hard drive.  If
	you've just upgraded to a new version of DOS or Windows(tm), you
	may get this message; simply run ARFBUILD.EXE again to generate a
	new ARFMAIN.BIN for the new operating system.

	If you haven't made any recent changes at the operating system
	level, though, this is almost surely being caused by a boot-sector
	virus that has gotten into your system.  See HELPME!.DOC.

	NOTE: If you're going to use the PRO-BOOT partition, you should
	install it before you run ARFBUILD.EXE (PRO-BOOT changes the MBR,
	too, so you'd just have to run ARFBUILD all over again).

		ARFMAIN.BIN has been altered!
		ßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	Also bad news.  Something (probably a virus) has attacked ARFMAIN,
	altering the program code.  See HELPME!.DOC.



								Page 10

	WARNING MESSAGES FROM AN INJECTed MODULE
	ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	Assuming that we've made it through the boot OK, and that ARFMAIN
	is now in memory and at work, you could get any of the following
	messages if a problem is detected.

	First, let's look at the messages that could be displayed if an
	INJECTed MODULE in one of your program files detects a problem.
	When this happens, the MODULE will use ARFMAIN.BIN to sound an
	attention-getting (some might say annoying) alarm and display a
	red box such as this one:

	    ÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜ
	    Ý                                                    Þ
	    Ý                 W A R N I N G ! ! !                Þ
	    Ý                                                    Þ
	    Ý   File fails CRC Check!                            Þ
	    Ý   (Old value 4354h          Current value 0536h)   Þ
	    Ý                                                    Þ
	    Ý   Press any key to begin rebuilding the file ...   Þ
	    Ý                                                    Þ
	    ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	In this case, when you started the INJECTed program, the injected
	module inside the program detected changes to the program code and
	data.  This caused the program to fail the CRC check, giving this
	warning.

	When you're ready, do as the prompt says: press any key, and the
	MODULE will begin repairing the file.

	(If you want a harmless demonstration, try this: inject SORT.EXE
	or some other program.  Then change it to a read-only file with
	"ATTRIB SORT.EXE +r".  The next time you run SORT, you'll see the
	warning box and SORT.EXE will repair itself.)



								Page 11

	NOTE: The operation of the INJECTed module is independent of ARF-
	MAIN.  The module merely calls ARFMAIN.BIN to help display more
	detailed error messages.  If ARFMAIN is disabled or not present,
	INJECTed modules will still function normally, and will still ful-
	ly protect your program files.  You just won't get a detailed re-
	port describing the problem that caused the rebuild.

	See INJECT.DOC; and if you suspect a virus, see HELPME!.DOC.

	Each warning that the INJECTed module could display relates to
	some form of possible virus activity.  For example, some viruses
	change file attributes; that's why we check for that.  Many virus-
	es also change the time and date stamp, so we check for that, too.
	(You can refer to VIRUS.DOC for more information on viruses.)

	Programmers can expect to get some warnings from time to time
	(they alter files for a living).  For example, if a programmer
	DEBUGs an injected .COM program, alters some of the code, and then
	write the new .COM back out to disk, they'll get a warning screen.
	But for the average user,

	     ONCE A PROGRAM FILE HAS BEEN INSTALLED AND CONFIGURED,
		       IT SHOULD NOT CHANGE -- PERIOD!

	By far, these warnings are the most serious:

	    - CRC check failure (the program has been altered)
	    - Bytes at beginning and/or end of the file have changed
	    - Program entry point or stack size has changed

	WARNINGS FROM THE DRIVER'S INTERNAL AV SHIELD
	ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	The ARFMAIN.BIN driver, as mentioned, also acts as an anti-virus
	"shield," and will display various warning messages itself if it



								Page 12

	detects suspicious activity.  Let's look at what the driver might
	warn you about.

	    Common Warnings
	    ßßßßßßßßßßßßßßß

	All of these warnings appear in a rectangular box in the middle
	of the display screen, and most will prompt for a "Y/N" ("Yes/No")
	response.  If you select "yes", the operation will be permitted to
	continue as though nothing had happened.  As a general rule, sele-
	cting "No" (the default) will cause the driver to tell the calling
	program that the operation isn't permitted.

	In many cases you can ignore these warnings.  (You can't call such
	a case a "false alarm", though, because the described activity IS
	happening; the driver is simply making sure you approve of it.)
	So when should you suspect a virus?  Follow these guidelines:

	1.  Look for CHANGES.  For example, a program hasn't been causing
	    any warnings before; why should it suddenly start now?  You'd
	    especially get suspicious if an old program started giving
	    warnings right after you'd just run a new program; it's very
	    possible that the new program was infected, and has spread
	    that infection to other files on your harddrive.  (If INJECTed
	    programs suddently start complaining, you can be sure of it.)

	2.  Look for REPEATED activity.  Many viruses will attempt to open
	    a number of different, unrelated files.  For example, you
	    might get, one after another:

		       "Attempt to open ALPHA.COM"
		       "Attempt to open BETA.EXE"
		       "Attempt to open GAMMA.COM"

	    ... and so on.  This is very typical of a virus doing a direc-
	    tory search, looking for files to infect.  You should especi-
	    ally get suspicious if it's attempting to open program files
	    in other subdirectories.



								Page 13

	3.  Look for SUSPICIOUS activity.  Why should your word processor
	    need to open "COMMAND.COM" for write?  Why would a database
	    program want to access the boot sectors?
	    
	4.  Look for MULTIPLE warnings.  A single, isolated warning is
	    probably just One Of Those Things.  Two or more warnings is
	    cause for concern.

	Now let's look at the actual warning messages, starting with ...
	    
		WARNING: Opening for R/W access:  <program.com/exe/etc.>
		ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	The program that you're currently using is trying to open a "code"
	file (.EXE, .COM, .BIN, etc.) for read/write access.  (Programmers
	will become very familiar with this warning; LINK, DEBUG and many
	other programmer's utilities open program files for write access.)

	You can choose "Y" (Yes, continue) or "N" (no).  If you choose "N"
	the driver will tell the calling program that the file is write-
	protected, preventing access to it.  (Programmers, just say YES.)

	Some legitimate programs can cause this warning screen; in fact,
	if you want to see it, enter "DEBUG SORT.EXE" at the DOS prompt.

	INSTALL and configuration programs are a problem.  Many of them
	write to .EXE and .COM files, and they WILL trigger this warning.
	One solution is to temporarily disable the driver (by removing the
	"DEVICE=ARFMAIN.BIN" line in CONFIG.SYS) until after the install.
	That's far from ideal, though; even just-out-of-the-box software
	could be infected (it has happened before, even with stuff from
	top software houses).

	Unfortunately, there are no hard and fast rules for an installer
	or configuration program.  If you've INJECTed all your files, you
	should be OK.  Unless you get a warning on a file that you honest-
	ly think the installer shouldn't be touching, just press "Y" at
	each warning.



								Page 14

		WARNING: Renaming/changing attributes: <program>
		ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	You'll get fewer warnings from legitimate programs with this one.
	We included this check because many viruses like to rename files
	and/or change file attributes (see VIRUS.DOC).

	DOS's own ATTRIB command can cause this warning (obviously), as
	can a few other programs, primarily utilities that change things
	at the system or boot configuration level.  The guidelines sug-
	gested above apply (especially for INSTALL-type programs).

		Attempt to overwrite the boot/partition sectors!
		ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß
		and Attempt to write directly via INT 26h!
		    ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	Hmmm ... these may be a little more serious.  There ARE some
	legitimate programs that can cause these, but we felt like we had
	to warn you, because so many viruses do these things.  Legitimate
	programs which can cause these warnings include disk defraggers
	and data recovery utilities, and system-level utilities such as
	FORMAT and SYS.  But most of your software should NOT.
	
	SUPERHINTS: The "boot sector" warning should NOT appear when
	you're doing routine read/writes to a floppy.  For example, say
	you've just finished writing a gooey love letter to your sweetie,
	and you're saving it to drive A:.  If you see "Attempt to over-
	write the boot sector," that's not good.  Some viruses wait for
	such disk access to sneak in their own writes to the boot sector;
	you won't be as likely to notice.  (The sneaky little devils.)

	As for the second warning, it used to be common for programs to
	use INT 26h to write to disk, so older programs can cause this
	warning.  But Microsoft(tm), the producers of DOS, have recently
	warned that INT 26h is obsolete, and that new programs shouldn't
	use it (so why do their own FORMAT, SYS, SCANDISK and even the
	DEFRAG program that comes with DOS 6 use it?  Hey; go figure.)



								Page 15

		INT xxh vector has changed: xxxx:xxxxh
		ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	There's no maybe to this one; a number of legitimate programs do
	wierd things to the interrupt table in your computer, and WILL
	cause this warning (SMARTDRV.EXE, for example).  We added the /I13
	and /I21 switches (see the next section) for this reason.

	If you get this warning repeatedly with the same program, and no
	other warning messages appear (and INJECTED programs appear to be
	fine), it's probably a false alarm; use the /I13 or /I21 command-
	line switch to disable it at that address (see below).
	
	This is a bit different from the previous messages; you're not
	asked to proceed, merely to press a key to continue.  Earlier
	versions of the driver used the "Serious Message" approach (see
	below), locking the PC up if you didn't want to proceed.  But so
	many programs change interrupts in a non-standard manner, and we
	were getting so many false alarms, we decided to do it this way.

	Technically, this warning is triggered by any program that hooks
	INT 13h or 21h in a "suspicious" manner.  The problem lies in de-
	fining "suspicious"; if we took the narrowest possible view, you'd
	get constant warning screens.  (This is a function of how DOS
	upper memory is implemented, -not- a problem with ARFMAIN.)

	Look for CHANGES: A program that hasn't been giving this warning
	before, and has now started doing so, for example.  THAT'S when
	you should get suspicious.  In general, if you have a virus, you
	also won't get this message by itself; it'll appear with others.

	If you make changes to your boot configuration, you could get new
	warnings, too.  Just changing the order of the DEVICE= lines in
	CONFIG.SYS or adding a new line to AUTOEXEC.BAT can change where
	the final INT 13/21h vectors will be at run time; you may have to
	change your /I13 and /I21 switches (again, see below).



								Page 16

	    More Serious Warnings
	    ßßßßßßßßßßßßßßßßßßßßß

	The common warnings just discussed will allow operation to conti-
	nue if you give a "N" ("no") response.  The messages that follow,
	however, default to a system hang for safety.

	These warnings are more serious than the previous ones.  Each is
	described in detail below.  For all of them, though, the suggested
	verification and repair procedure is as follows:

	1.  See the section "What To Do If I Get A Virus" in INJECT.DOC;
	there is some very useful information there.

	2.  Switch the computer off, then boot from the write-protected
	ARF Recovery floppy that you created when you installed ARF AV.

		WARNING!!! - BEFORE YOU PUT THAT FLOPPY INTO THE
		DRIVE, MAKE SURE IT'S STILL WRITE PROTECTED!!!!

	Tape strips can fall off, and/or the sliding tabs in 3.5" floppies
	can slip over time!  DO NOT under any circumstances let that disk
	go into the drive when it's not write protected!  (If you do, you
	CANNOT trust it anymore; and if a virus is suspected, use a diff-
	erent computer to build a known-good bootable floppy to be safe.)

	3.  Use INJECT to scan and repair your files as needed (again, see
	INJECT.DOC).

	4.  Use PRO-BOOT to check and restore the Main Boot and System Boot
	Records as needed (see PRO-BOOT.DOC).

	5.  Boot the system normally (ie, on the hard drive); unless you
	get a fresh batch of warning screens, you should be OK now.  But
	don't forget to delete the file that caused the warning (register-
	ed users may send a copy of the file to us for analysis).



								Page 17

	6.  If you do get other warnings, contact us for more assistance.
	As explained in REGISTER.DOC, we will only provide limited support
	to non-registered users.  Registered users can expect full support
	for recovery after a virus attack.
	
	Here are the serious warnings that you could get:

		WARNING: System INT xxh is being tunneled!
		ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	This is indeed a serious warning.  NO NORMAL SOFTWARE SHOULD EVER
	CAUSE THIS WARNING (and by "normal," we mean ALL of the software
	that the typical user -- even a programmer -- might use)!

	What is "tunneling?"  Just as a thief might try to dig under a
	fence to get inside your property, some viruses use a hardware
	tracing technique to "tunnel" past a shield such as ARFMAIN, and
	"dig" into the heart of the system.  This allows them to bypass
	the shield and call the system directly.

	If you see this warning, you almost certainly have a virus trying
	to install itself in your system; we strongly recommend that you
	choose the default "No" and let the driver hang the system.

	That's the bad news; the good news is, selecting "N" will, in most
	cases, stop the virus COLD before it has a chance to spread.

	The only "legitimate" programs we know of that might cause a false
	alarm here are very specialized program analyzers and tracers.
	But these are extremely rare (even CODEVIEW, DEBUG, and TD386 will 
	not cause this warning, for example).



								Page 18

		This BIOS memory size report has been altered ...
		... current size is xxxh ....
		ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	You may get a false alarm on this one during and immediately after
	bootup, but once you begin a normal session, you should NEVER see
	this.  If you do, something is seriously wrong; you are probably
	witnessing a "stealth" virus as it first tries to install itself
	in your system.

	If you're going to get a false alarm, you'll get it when you first
	install and use ARFMAIN, and/or right after making changes to your
	CONFIG.SYS and AUTOEXEC.BAT files.  In that case, you can use the
	/Mxxx command-line switch to disable the warning (see below).

	But once you've installed ARFMAIN and have been using it for a
	while, you should NOT get this message.  ESPECIALLY if you get
	this message when you first run a new program, you should kill it
	and follow the recovery procedure described above.

	COMMAND-LINE SWITCHES
	ßßßßßßßßßßßßßßßßßßßßß

	To help minimize false alarms, a few command-line switches are
	supported by ARFMAIN.BIN.  (These have no effect on ARFDISP.BIN,
	because it doesn't have the anti-virus shield.)

	The basic syntax for the CONFIG.SYS line that would install the
	driver is as follows:

		  DEVICE(HIGH)=ARFMAIN.BIN <optional switches>

	The DEVICE or DEVICEHIGH command, of course, is what "loads" the
	driver; see your DOS manual.  The optional switches are described
	below.  Remember to specify a path if ARFMAIN.BIN isn't in the
	root directory; for example,



								Page 19

	      DEVICE=C:\ARFSTUFF\ARFMAIN.BIN <optional switches>

	Each of the switches is intended to attack a specific type of
	false alarm, and we'll look at each in turn.

	    /Mxxx
	    ßßßßß

	This switch allows you to tell the driver the size of your
	conventional memory in hex kilobytes.  (The default is 280h, or
	640K).  This can help prevent false "Memory Size" warnings.

	If you're not familiar with hexadecimal numbers and other such
	nonsense, the easiest way to set this switch is just to boot the
	computer and write down the memory size specified in the warning
	screen (it'll be displayed in hex, which is what we want).

	For example, suppose you've just installed the driver, and when
	you boot, you get the warning box.  It states that "the BIOS mem-
	ory size has changed," and that the current size is 27Fh.  You
	might use this line in your CONFIG.SYS file:

			DEVICEHIGH=ARFMAIN.BIN /M27F

	Note that there are no spaces in the switch itself, and that the
	"h" suffix on the "27Fh" isn't required.

	IMPORTANT NOTE: If the memory size reported by the warning screen
	is different from 280h or 27Fh, you could have a virus.  These are
	the only two values we're familiar with on modern PCs with 640K or
	more memory.



								page 20

	    /I13,ssss:oooo
	    ßßßßßßßßßßßßßß
	    /I21,ssss:oooo
	    ßßßßßßßßßßßßßß

	These are essentially the same, and allow you to specify a single
	known-good vector for INT 13h and for INT 21h.

	This is another case where we had to weight compromises, and dec-
	ided to implement this to support those cases where a legimate
	program does funky things to the interrupt table.  Adding code to
	the driver to automatically detect this might provide a possible
	"back door" for a virus to disable the driver.

	(For example, SMARTDRV.EXE causes this warning when it loads in
	upper memory because it remaps some interrupts to upper memory.
	But so do a number of viruses!  Adding code to permit SMARTDRV to
	do it would mean that some viruses might get past the driver.)

	By providing a single, known-good interrupt vector address for
	INT 13h or INT 21h, you can safely eliminate false alarms.

	Note the precise syntax: no spaces, and a comma after the "/I13"
	or "/I21" specifying the interrupt.  The "ssss" value is the
	segment in hex, and "oooo" is the offset in hex.

	Again, if you're no good with hexadecimal, just watch the display
	and write down the numbers in the message box.

	For example, suppose you get the warning screens during boot, and
	they specify that the current vector for INT 13h is C868:16D2h,
	and the current vector for INT 21h is C868:1492h.  You might use a
	line line like this one in your CONFIG.SYS file:

	     DEVICE=ARFMAIN.BIN /I13,C868:16D2 /I21,C868:1492


								Page 21
	SOME FINAL NOTES
	ßßßßßßßßßßßßßßßß

	    FALSE ALARMS
	    ßßßßßßßßßßßß

	You can compare computer viruses to vandals who break into your
	home and break things for no real purpose.  You can also compare
	the ARFMAIN.BIN driver to a security system that tries to catch
	them before they can get in and do their damage.

	That's a good analogy, too, because there are some similarities.

	The PC is easy to use and easy to upgrade.  By simply popping in a
	disk, you can install a new software package.  But convenience has
	a price, and we can compare it to an unlocked door on a house: 
	convenient for you and the family ... but also for the bad guys!

	Installing locks and an alarm system means you lose convenience.
	You'll have to remember alarm codes and get new keys and all that
	nonsense.  You'll have to remember not to enter the house while
	the alarm is active, too.  Anti-virus software is a lot like that;
	if it's going to work, you may be inconvenienced from time to
	time.  Not often, but it'll happen.

	Let's continue the analogy.  You want the alarm system to be sens-
	itive enough to catch bad guys, but not so sensitive that you get
	constant false alarms.  Finding the right setting involves some
	compromises.  For maximum protection, you'll err on the side of
	caution, though, and that's what we've done.

	(We might cynically point out that one reason why some anti-virus
	software isn't totally effective is because many companies are so
	terrified about causing false alarms.  We'd rather treat you as an
	adult, warn you that you may get a false alarm from time to time,
	and provide maximum protection.)



								Page 22

	But this where the analogy ends; actually, many of these warning
	screens aren't really "false" alarms.  The described activity *IS*
	happening; ARFMAIN is simply making sure you know about it.

	Why will you occasionally get a warning screen on a legitimate
	program?  It's simple: for every virus-like activity that you can
	name, we can name at least one legitimate program that does the
	same thing.  We've already mentioned writing to the boot sectors
	with FORMAT; there are dozens of other examples.

	So ... could we have eliminated some of these warnings?  Probably.
	But this is a critical point:

	    IF YOU PUT !ANYTHING! IN AN ANTI-VIRUS PROGRAM TO DISABLE
	    IT, TURN IT OFF, OR EVEN MERELY MAKE IT "IGNORE" CERTAIN
	    PROGRAMS, THE VIRUS COMMUNITY !WILL! LEARN ABOUT IT, AND
	    !WILL! TRY TO USE IT TO THEIR ADVANTAGE.

	(We had a hard enough time convincing ourselves just to support
	command-line switches!)

	Read that.  Take it to heart.  Memorize it.  And if you're ever
	irritated by a warning screen, read it again.

	Can we share just one true story?

	One major software house released their own anti-virus shield a
	few years back.  This particular shield is now considered a joke 
	in the virus community; it's completely ineffective against the
	majority of viruses produced in the last year or so.

	Why?  To prevent false alarms, this manufacturer put a secret
	"switch" in the shield.  Their other programs could call this
	switch to turn the shield off while they did "suspicious" stuff,
	such as writing to the boot records of the disk.  No false alarms.



								Page 23
	When they were done, their other programs would switch the shield
	back on, and all was well.  Right?

	Yeah, RIGHT.  Virus writers may be somewhat warped, but they are
	NOT stupid.  When they noticed that this manufacturer's other
	programs were mysteriously able to do things (like write to boot
	sectors) without setting off an alarm, they got curious.  They
	looked at the shield's code and discovered the switch.  Within a
	matter of DAYS (no exaggeration!), viruses were being produced
	that could switch that shield off.

	True story, folks, and we don't want to repeat that mistake!

	(So how does ARFMAIN know when INJECT is writing an .COM or .EXE
	file?  We ain't tellin', but you can be sure of one thing: we're
	not using a software switch!)

	    WHY OURS IS THE BEST
	    ßßßßßßßßßßßßßßßßßßßß

	... and this relates to the previous section on false alarms.  If
	you don't have time to read all of this stuff now, that's fine;
	but do us -- and yourself -- a favor and read it soon.

	INJECT is the ideal file protector, combining a number of func-
	tions (including detection and recovery) in one automatic, self-
	contained unit.  PRO-BOOT is the ideal way to protect your Main
	Boot Record, too; it's also an automatic, self-contained utility.

	ARFMAIN.BIN is the perfect complement to these other two programs;
	it concentrates on virus-like activity at the system level.  What
	INJECT and PRO-BOOT might miss, ARFMAIN will catch, and vice-versa.

	This overlapping protection is the key to our anti-virus package,
	and we're confident enough to offer registered users a limited
	money-back guarantee (see REGISTER.DOC for details).



								Page 24
	
	We believe that ARFMAIN.BIN is the best anti-virus shield avail-
	able for several good reasons:
	
	1 - First and foremost, our approach.  This is NOT another "me-
	    too" scanner/detector.  From the outset, we wanted to do more
	    than that; and the more research we did, the more convinced we
	    became that we were on the right track.

	    See Leonard's comments in the "overview" in INJECT.DOC; much
	    of what he says there applies here.  Countless hours of res-
	    earch and testing have gone into identifying the reasons why
	    the PC family is susceptible to viruses in the first place,
	    and to FIXING those weaknesses.

	    The ARF Anti-Virus package is a virus PREVENTION system, not
	    just a virus detector.

	    (Using the alarm analogy one last time, we want to stop the
	    bad guys from getting into your system to start with.  If they
	    DO get past us, we want to stop them as soon as possible, and
	    strictly limit the amount of damage they might cause.)

	2 - In the same vein, the driver traps and inspects a number of
	    undocumented system calls and data areas.  This includes calls
	    to some undocumented network functions, which most anti-virus
	    programs presently ignore.  To be fair, few PC viruses use 
	    these "back doors" into the system at present ... but it'll
	    only be a matter of time before this becomes commonplace.
	    With our shield, you have the assurance that the protection is
	    already in place.

	3 - The device driver is custom-configured to your system.  As it
	    builds ARFMAIN.BIN, ARFBUILD checks your system carefully and
	    records some "signature" values in the driver.  If these
	    values ever change, you'll be warned.  This makes it far more


								Page 25

	    effective than an anti-virus shield that has to compromise to
	    work on every system regardless of manufacturer.

	4 - Because it's a device driver, ARFMAIN.BIN is loaded during the
	    boot, even before the system shell (ex., COMMAND.COM) is
	    started.  We get into the system much sooner than an anti-
	    viral shield which must be invoked from the DOS prompt.

	5 - As the driver is being loaded during boot-up, it checks both
	    the Main Boot and System Boot Records (MBR/SBR) for changes
	    using a very effective CRC "signature" method.  If even a
	    single byte in the SBR/MBR has been altered, you'll be warned.

	    (PRO-BOOT checks the boot records, too.  Again, you see the
	    overlapping protection.)

	6 - After boot-up, the driver runs in the background and automati-
	    cally checks for suspicious activity.  One such check is for
	    "tunneling" -- a technique used by many viruses to "tunnel"
	    past anti-virus software and get to the heart of the system.

	7 - The driver requires confirmation from the operator before any
	    write can be done to the boot sectors of a disk.  (It's amaz-
	    ing that most PCs *STILL* don't have this simple and effective
	    protection.)

	8 - The device driver asks for confirmation on any attempt by a
	    program to open a code file for R/W access, or any attempt to
	    change the attributes of, or rename, a code file.

	9 - Just as the INJECTed module is very difficult to remove from
	    an injected file, this driver is very resistant to tampering.
	    In fact, the only way to disable this driver is to not use it
	    -- ie, to remove the "DEVICE=ARFMAIN" line from CONFIG.SYS.
	    We did it that way on purpose.



								Page 26

	ARFMAIN has been tested in memory against a number of viruses,
	from well-known older types (ex., the Jerusalem family) to those
	currently making the rounds (ex., SMEG/QUEEG and NATAS).  It has
	proven extrememly effective in all tests so far.

	Finally, we don't require a registration fee of home users (see
	REGISTER.DOC for full details; there are some real benefits to
	registration, but it's not required of home users).  We want this
	software in as many PCs as possible; please give copies of this
	package to your friends, family, and co-workers.  Spread the word!

	And remember: let us know how we did.  Suggestions and comments
	are not only welcome, but deeply appreciated.  No matter how minor
	the suggestion, if it makes sense, we'll include it in future
	releases of the package.  See "How to Contact Us" in REGISTER.DOC.

	    A SPECIAL NOTE FOR WINDOWS(tm) USERS
	    ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	The ARFMAIN.BIN driver works fine with Windows versions 3.1 and
	3.11 in 386 Enhanced mode.  However, we can't guarantee it for all
	future versions of Windows.  Check with us for information on an
	update if you plan to change to a later version of Windows.

	IMPORTANT:  If you are using Windows(tm) on an older 286 computer,
	you are almost certainly running Windows in Standard mode.  You
	may experience problems with ARFMAIN.BIN in that case, due to the
	way that Windows captures the keyboard and video subsystems.  For
	example, if you shell out to DOS, when you attempt to return to
	Windows, the system may hang.

	Unfortunately, you have only two choices: either stop using Wind-
	ows on your 286, or stop using ARFMAIN.BIN.  Sorry ... . .



								Page 27
	    
	    KNOWN CONFLICTS WITH OTHER PROGRAMS
	    ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

	We've taken great pains to make sure that ARFMAIN works with most
	popular software.  But in addition to the "false alarms" discussed
	above, as of this writing, we know of these possible conflicts:

	1.  SMARTDRV.EXE -- if you use SMARTDRV, disable write-back cach-
	ing.  If you don't, the system will appear to hang when exiting
	some programs (such as word processors).  (Write-caching on soft-
	ware based disk cachers is a bad idea in general, anyway; and
	SMARTDRV's ability to corrupt disks -- especially floppies --
	when write-back is enabled is well-known.)

	2.  Some older programs have a very small stack.  You may get the
	message "stack overflow" when these are used with the driver.  If
	you have an .EXE modification utility such as EXEHDR, you can
	increase the size of the stack.  Other than that, such programs
	will probably have to be avoided when the driver is in memory.

	If you know of other programs that appear to work improperly with  
	the ARFMAIN driver, please let us know and we'll add them to the
	list.