*************************************************************************
*                                                                       *
* LLMVAS.EXP                                                            *
*                                                                       *
* August 18, 1993                                                       *
*                                                                       *
* Lyon Lamb Video Animation Systems                                     *
* Video Tape Recorder                                                   *
* Autodesk Device Interface                                             *
*                                                                       *
*************************************************************************

This documentation will help you install the Lyon Lamb MiniVAS and PCVAS
ADI (LLMVAS.EXP) for Autodesk 3D Studio.     

The following assumes that 3D Studio has been installed in the directory
C:\3DS.  If this is different on your system, please substitute the
appropriate directory when reading these instructions.


1) First preblack your video tape to automatically record control track,
frame code, and time code on it.


2) Copy LLMVAS.EXP into the 3D Studio drivers sub-directory.  This
will most likely be the sub-directory C:\3DS\DRIVERS.


3) Edit the file 3DS.SET in the C:\3DS directory to change the
VTR-DEVICE from the default [DIAQUEST] to VTPADI.  

        The proper syntax is:
        VTR-DEVICE = VTPADI


4) In 3DS.SET, examine the "Rendering Display" section. Modify
the default rendering driver according to Autodesk's built-in
output drivers. 

Change the rendering display parameters to match the video output
card in your system. A few compatible video graphic cards are VISTA,
TARGA or VISION16.   

        The proper syntax for a VISTA (756x486) is:
        RENDER-DISPLAY = VISTAH

NOTE: You must have SET RDPADI or SET RCPADI statement in your 
AUTOEXEC.BAT for these to function.  Consult your 3D Studio manual.
 
Alternatively, you can use the "3DS VIBCFG" command to change your
rendering display to match the video output card in your system.
Consult your 3D Studio Rel. 3 Installation Guide for details.

5) Add the following line to the end of your AUTOEXEC.BAT file:

        SET VTPADI=C:\3DS\DRIVERS\LLMVAS.EXP

The line tells 3D Studio that the ADI video tape recorder driver
you want to use is LLMVAS.EXP.


6) Now you need to add another line to your AUTOEXEC.BAT file.  The line
tells the ADI driver how your system is set up.  The format of this line
depends on whether you have a MiniVAS or a PCVAS and how it is set up.

The format of the line is:

        SET LLMVAS={F,T,L} {N,P} {C1,C2,C3,C4} I# Vaa R#

Immediately following the description of the parameters are several
examples of specific configurations and the proper SET LLMVAS= line
to place in your AUTOEXEC.BAT file.

Description of the parameters:
-----------------------------

{C1,C2,C3,C4}   C1 - Use COM port 1
                C2 - Use COM port 2
                C3 - Use COM port 3
                C4 - Use COM port 4

I#              Specify the IRQ number to use for communication with the VAS
                        e.g. I10        means use IRQ 10
                             I5         means use IRQ 5
                NOTE: MiniVAS users do not normally need to specify the I
                parameter.

{F,T,L}         F - Use frame code
                T - Use serial time code
                L - Use longitudinal time code (available only for PCVAS)

{N,P}           N - Use NTSC timing (30 frames per second)
                P - Use PAL timing (25 frames per second)

Vaa             Specify the VTR identification code (consult your MiniVAS
                or PCVAS manual)
                        e.g. VSM        is the Sony VO-9850
                             VP7        is the Panasonic AG-7750

R#              Specify the preroll time (1 to 20 seconds) for recording
                        e.g. R6         set a preroll time of 6 seconds
                             R11        set a preroll time of 11 seconds
                NOTE: Specifying R0 will use the default preroll time
                stored in the MiniVAS's or PCVAS's memory.

Example SET LLMVAS= configurations:
----------------------------------
    Example A:  A MiniVAS connected to COM1 (C1), using frame code (F),
                NTSC timing (N), the Sony VO-9850 (VSM), and a recording
                preroll time of 8 seconds (R8):

                        SET LLMVAS=C1 F N VSM R8

    Example B:  A MiniVAS connected to COM2 (C2), using time code (T),
                PAL timing (P), the Sony VO-9850 with time code option (VSN),
                and a recording preroll time of 10 seconds (R10):

                        SET LLMVAS=C2 T P VSN R10

    Example C:  A MiniVAS connected to COM3 (C3), using frame code (F),
                NTSC timing (N), the Sony BVU-2500 (VSD), and the default
                recording preroll time (R0):

                        SET LLMVAS=C3 F N VSD R0

    Example D:  A PCVAS connected to COM3 (C3), IRQ number 10 (I10),
                using frame code (F), NTSC timing (N), the Sony VO-9850 (VSM),
                and a recording preroll time of 6 seconds (R6):

                        SET LLMVAS=C3 I10 F N VSM R6

    Example E:  A PCVAS connected to COM1 (C1), IRQ number 4 (I4),
                using frame code (F), PAL timing (P), the Hitachi HR-230 (VH3),
                and the default recording preroll time (R0):

                        SET LLMVAS=C1 I4 F P VH3 R0

    Example F:  A PCVAS connected to COM4 (C4), IRQ number 5 (I5),
                using longitudinal time code (L), NTSC timing (N),
                the Panasonic AG-7750 (P7), and a recording preroll time
                of 7 seconds (R7):

                        SET LLMVAS=C4 I5 L N P7 R7


7) After you add the proper SET LLMVAS= line to your AUTOEXEC.BAT file
and save it, reboot your computer to put the changes into effect.

 
8)  Open 3D Studio, go to Keyframer (F4), and select the following from
the menu on the left:

	 Renderer ...
		 VTR Control ...
			 VTR Setup ...

Hit the Initialize button, wait, then a dialogue box appears reading:

        VTR is On-line.


9)  Please refer back to the Studio 3D documentation for a
detailed explanation regarding the:

        VTR Control...  and  VTR Setup...  menus.




================================================================
Detailed Description of the LLMVAS Environment Variable Settings
================================================================

The following is a full description of the LLMVAS environment
variable settings.

Syntax:
------
SET LLMVAS={C1|C2|C3|C4} {I#} {Axxx} {N|P} {F|T|L} {Vaa} {Rdd}


Default Setting:
---------------
If the LLMVAS environment variable is not defined, the driver assumes
the following default setting:

        SET LLMVAS=C3 I10 A3E8 N F R0

This specifies COM port 3, IRQ 10, I/O base address 0x3e8, NTSC timing,
frame code operation, and the default preroll time of the VAS.


Notes on the Syntax:
-------------------
- The curly brackets "{" and "}" show groups of related options.
- Vertical bars "|" separate each available option in a group.
- Capital letters or lower case letters may be used.
- Unrecognized options will be ignored (e.g. the letter "Z").
- Spaces may optionally separate each option.
- Spaces may not separate the letters composing an option.
        (e.g. "VSM" works, but "V SM" does not)
- Options can be given in any order but subsequent options from the same
        group override previous options from the same group.
        (e.g. "NP" means PAL operation since the P comes after the N)


Parameters:
----------

COMMUNICATIONS PORT:    {C1 | C2 | C3 | C4}

                        C1 - COM1, IRQ4, 0x3F8
                        C2 - COM2, IRQ3, 0x2F8
                        C3 - COM3, IRQ10, 0x3E8
                        C4 - COM4, IRQ11, 0x2E8

        This option selects the serial port to which the MiniVAS or PCVAS
        is connected.  The assumed IRQ and I/O base address for the
        COM port are listed above.  However, specifying a different IRQ
        using the I option (described below) overrides the assumed IRQ,
        and specifying a different I/O base address using the A option
        (also described below) overrides the assumed I/O base address.

        Default: If this option is not specified, then the driver
                 assumes COM3 (C3).


IRQ NUMBER:             {I#}

        This option selects the IRQ number to use for communication
        with the PCVAS or MiniVAS.

        The PCVAS has a set of selectable jumpers labelled (IRQ2, IRQ3,
        IRQ4, IRQ5, IRQ7, IRQ10, IRQ11, and IRQ15) for selecting the
        IRQ number.  You should use the I option to specify the IRQ
        for which the PCVAS is set.

        The MiniVAS does not have selectable jumpers for changing the
        IRQ number, but the I/O card in your computer may have such jumpers.

        Default: If this option is not specified, then the driver
                 assumes the default IRQ for the selected COM port.

        Examples:       I2      specifies IRQ2
                        I11     specifies IRQ11


I/O BASE ADDRESS:       {Axxx}

        This option selects the I/O base address to use for communication
        with the PCVAS or MiniVAS.  The address is given as a three digit
        hexadecimal number.

        The PCVAS has a set of dip switches labelled (A3 to A8) for
        selecting the I/O base address.  Normally you do not need to
        specify this option because selecting a communications port
        using the C option selects a default I/O base address.

        Default: If this option is not specified, then the driver
                 assumes the default I/O base address for the selected
                 COM port.

        Examples:       A200    specifies 0x200
                        A3D8    specifies 0x3D8


FRAME FORMAT:           {F | T | L}

                        F - Frame code
                        T - Serial time code
                        L - Longitudinal time code

        This option selects the mode used for search operations and record
        operations.

        Default: If this option is not specified, the driver assumes
                 frame code (F) operation.


TIME STANDARD:          {N | P}

                        N - NTSC (30 frames per second)
                        P - PAL (25 frames per second)

        Default: If this option is not specified, the driver assumes
                 NTSC (N) operation.


VTR ID CODE:            {Vaa}

        This option identifies the VTR connected to the MiniVAS or PCVAS
        using a two letter identification code.  This two letter code
        can be found in your MiniVAS or PCVAS manual.

        Specifying this option causes the driver to initialize the MiniVAS
        or PCVAS with the given identification code.

        Default: If this option is not specified, then the driver assumes
                 that the current VTR identification code stored in the
                 MiniVAS's or PCVAS's memory is correct.

        Examples:       VP7     specifies the Panasonic AG-7750
                        VSN     specifies the Sony VO-9850


PREROLL TIME:           {R#}

        This option specifies the preroll time for performing recordings.
        The preroll time can be set to a number of seconds from 1 to 20.
        To use the default preroll time of the MiniVAS or PCVAS,
        specify (R0).

        Default: If this option is not specified, the driver assumes
                 that the default preroll time of the MiniVAS or PCVAS
                 is correct.

        Examples:       R5      specifies a 4 second preroll
                        R10     specifies a 10 second preroll
                        R0      specifies the default preroll time




===========================================================================
Notes on the Operation of the Driver
===========================================================================

If 3D Studio appears to have hung:
---------------------------------
If 3D Studio appears to have hung during a frame search using
Next Frame Forward, Next Frame Back, Goto, or a record operation
using either Record or Disk-to-VTR, wait at least 15 seconds.
For most operations, the driver has a time-out time of about 10
seconds.  If after 10 seconds, the driver detects that something
may be wrong, it returns to 3D Studio indicating that an error
occurred in the operation.

If after 15 seconds, you are not given control back, stop your
VTR and wait another minute.  The driver will wait a longer period
of time before timing out when it is waiting for the cut-in signal
and the ready to record signal.