WWIVMail 1

       Documentation





    ** Contents

         1 Copyrights
         1 Legal Notice and Disclaimer
         1 Technical Requirements

         2 Installation
         2     WWIV Considerations
         2     FrontDoor Considerations
         2     FrontDoor Setup
         3     FrontDoor control file

         3 Command Line Options
         3     IN, OUT, CHECK
         3         WWIVMail IN
         3         WWIVMail OUT
         3         WWIVMail CHECK
         3     FC - Flow Control
         3     LOG - FrontDoor Log
         4     HIS - FrontDoor History Files
         4     Sample FrontDoor control file

         4 Modem Considerations

         5 Error Conditions

         5 Advanced Configurations

         6 Future Enhancements

         6 Inquiries and Registration
         6     Inquiries
         6     Registration
         7     Reaching the Author

         7 Technical Information

         7 Credits




    ** Copyrights

       WWIVMail and WWIVMail Documentation
       (C) 1991 Andrew J. Mead
       All Rights Reserved.

       FrontDoor
       (C) 1986-1991 Advanced Engineering sarl
       All Rights Reserved.

       WWIV version 4 and WWIV Network software
       (C) 1988-1991 Wayne Bell
       All Rights Reserved.



    ** Legal Notice and Disclaimer        

       WWIVMail is provided as is.  In no event will the author be liable
       for any damages, costs, or lost mail resulting from the use of
       WWIVMail

       WWIVMail is to be freely distributed.  It may be used free of charge
       in non-commercial settings.  Commercial liscences are available upon
       request.



    ** Technical Requirements

       WWIVMail is designed to help SysOps install WWIV Network software
       underneath FrontDoor.

       This program was written and debugged with the following programs:

           FrontDoor 2.02/NC
           WWIV 4.20A
           WWIV Network 27

       If your system can run this software than it should have no problem
       with WWIVMail.



















                                         1




    ** Installation

       WWIV Considerations

           You will need to place WWIVMAIL.EXE in your main WWIV directory.
           This is the directory that contains BBS.EXE and NETWORK.EXE.
           If you have modified the structure of CONFIG.DAT, this software
           may not work properly.  WWIV itself is not necessary, only some
           its data files are.

           WWIVMail uses the following WWIV files
               required
                 CONFIG.DAT
                 NETWORK.EXE NETWORK1.EXE NETWORK2.EXE NETWORK3.EXE
                 BBSDATA.NET BBSLIST.NET  CALLOUT.NET  CONNECT.NET

               required for HIS option (described later)
                 NET.LOG

               used if present
                 REGIONS.DAT


       FrontDoor Considerations

           WWIVMail uses the following FrontDoor files
               required
                 SETUP.FD

               required for HIS option (described later)
                 INBOUND.HIS   (with IN option)
                 OUTBOUND.HIS  (with OUT option)
                 LASTCALL.FD

               written to by LOG option (described later)
                 log file from FDSetup "Filenames" submenu


       FrontDoor Setup

           In the Mailer menu in FDSetup goto the Miscellaneous submenu.
           Under the selection  "BBS Software Name" you will need to
           enter "NN: " (without the quotes).  When a remote WWIVnet
           mailer calls your system and sees the "NN: " string it will
           respond with its mailer identification string "!-@NETWORK@-!".

           In the Mailer menu in FDSetup goto the External Mail submenu.
           You will need to enter the string "!-@NETWORK@-!" with the
           errorlevel you will want to initiate the WWIVMail processing.
           Once FrontDoor receives the mailer id string it will immediately
           exit with the chosen errorlevel, bypassing the normal 11 second
           or more wait.

           Note: Both the "NN: " and the "!-@NETWORK@-!" strings may be
           changed using the macro feature of WWIVnet mailer software.
           A limited discussion of this is in the Advanced Configurations
           section.



                                         2




           In the Mailer menu in FDSetup go to the Errorlevels submenu.
           You will need to turn the "Create .BAT File" option on.
           WWIVMail uses this file to create command line arguments for
           running the WWIV Network programs.


       FrontDoor control file

           In your FrontDoor control file (usually a batch file that
           runs FrontDoor, and branches execution based on errorlevels
           that FrontDoor exits with) you will need to have the
           following things happen when FrontDoor exits (with the
           errorlevel indicated in the External Mail submenu).

               change active directory to main WWIV directory
               execute WWIVMAIL with the necessary argument(s)



    ** Command Line Options

           IN, OUT, CHECK
               One of these three options must be present (otherwise
               the help screen appears).  These options tell WWIVMail
               what mode to operate in.

               WWIVMail IN
                 This tells WWIVMail that another WWIV Network Mailer
                 has just connected, and a connection needs to be
                 established.   (NETWORK.EXE needs to be run)

               WWIVMail OUT
                 This option, which is not yet operational, tells WWIVMail
                 to poll another system.

               WWIVMail CHECK
                 This option, which can be run without all of the normally
                 required system files present, is the diagnostic option.
                 It merely checks for unprocessed mailbags, processes them.
                 If the Network files are not properly updated, it will
                 process them as well.  This option will ignore both
                 the FC and HIS options.


           FC - Flow Control
               If you are using a modem with a locked terminal-modem
               communication rate, you will want to add this switch
               to the command line.


           LOG - FrontDoor Log
               This option will have WWIVMail log its activity in your
               FrontDoor log.







                                         3




           HIS - FrontDoor History Files
               This option will log incoming and outgoing calls in
               FrontDoor's INBOUND.HIS and OUTBOUND.HIS files.
               It will update LASTCALL.FD as well.
               It will not update the activity records.
               The following translations are made
                 Zone      : 9948  (WWIV on your telephone keypad)
                 Net       : WWIV Network group number from BBSDATA.NET
                 Node      : WWIV Network node number from NET.LOG
                 System    : System name from BBSDATA.NET
                 Location  : derived from REGIONS.DAT based on area
                             code in BBSDATA.NET
                 Sent/Rcvd : rounded up to next 1k increment.  Derived
                             from NET.LOG


           Sample from the authors FrontDoor control file
               :FRONTDOOR
               If ERRORLEVEL 91 Goto WWIVMAILIN  ; incomming WWIV mail
               REM -----------------------------
               :WWIVMAILIN                       ;  91 WWIVMail ***
               ChDir C:\WWIVDIR                  ; change to WWIV directory
               wwivmail in log his
               Goto FRONTDOOR                    ; return to FrontDoor
               REM -----------------------------



    ** Modem Considerations

       WWIV Network Software needs to be told about the connection.
       WWIVMail understands the following connect string arguments
           Asynchronious argument
             HST
           Error Correction arguments
             LAPM
             ARQ
             REL
           Data Compression arguments
             V42BIS
             MNP5

       If your modem sends result codes that don't match the above
       list, PLEASE let me know what they are so I may include them
       in a later version of WWIVMail.















                                         4




    ** Error Conditions

       If no errors are encounted, WWVIMail will exit with no
       errorlevel.

       If the program crashes, it will exit with its Turbo Pascal
       generated errorlevel.

       The following errorlevels are generated by WWIVMail if it
       determines it can't proceed.

           231 : -- More than one main command parameter [IN,OUT,CHECK]
                    was selected.
           232 : -- WWIV's "CONFIG.DAT" not found.
           233 : -- FD's "DOBBS.BAT" not found.
           234 : -- WWIV's "BBSLIST.NET" not found.
           235 : -- WWIV's "BBSDATA.NET" not found.
           236 : -- WWIV's "CALLOUT.NET" not found.
           237 : -- WWIV's "CONNECT.NET" not found.
           238 : -- FD's "SETUP.FD" not found.
           239 : -- FD's "INBOUND.HIS" not found.
           240 : -- FD's "OUTBOUND.HIS" not found.
           241 : -- WWIV's "NET.LOG" not found.
           242 : -- Error extracting numeric value from WWIV''s "NET.LOG".
           243 : -- WWIV node number not found in "BBSDATA.NET".
           255 : -- Feature not available.



    ** Advanced Configurations

       By using the macro features of the WWIV Network software, you
       can easily configure multiple WWIV Network nodes under one
       FrontDoor node.  This can simplify running both WWIVnet and
       WWIVlink on the same system (for example).  All you need to
       do is coordinate with the systems you connect to, and change
       the Network ID string from !-@NETWORK@-! to some other string.
       Using different strings with different networks keeps the
       confusion to a minimum.
       You will also need to create entries in your FrontDoor External
       Mail submenu that reflect these changes.

       You can also use macros to change the 'NN: ' string to something
       more pleasing.
















                                         5




    ** Future Enhancements

       The next version of WWIVMail should implement the OUT command
       line directive.  You will be able to add external events to
       your FrontDoor Event Manager that will have WWIVMail poll other
       systems.

       I would also like add support for VirtualNet (VBBS) or write a
       seperate but similiar utility.  However, I need to obtain certain
       technical information about VBBS network software first.

       I am also looking for someone who writes real technical
       documentation to help prepare future versions of this documention.



    ** Inquiries and Registration

       Inquiries
           The latest version of WWIVMail is available for immediate
           download or FREQ from the author.

           The Infinite Improbability BBS
           @9952 WWIVnet
           1:151/205 FidoNet (Private Idaho BBS)
           (919) 489-9446 (Durham, NC - PCPursuit NCRPT)

           The BBS currently operates on an old USRobotics Courier 2400e
           at 2400 bps with MNP-3.  (As of December 1991)

           The filename will follow the form WWMAILn.ZIP where "n"
           is the latest version number.


       Registration
           WWIVMail may be freely used in non-commercial environments.
           However, I still ask that you register the software.  If
           you are merely registering (no money) then please just fill
           out the form in the file REGISTER.FRM and E-Mail it, File
           Attach it, or postal mail it to me.

           For commericial installations please contact me for further
           information.

















                                         6




       Reaching the author
           FidoNet
             Andrew J. Mead 1:151/205 (Private Idaho BBS)
             Andrew Mead 1:151/205 (Private Idaho BBS)
           WWIVnet
             Doc Technical 1@9952 (The Infinite Improbability BBS)
             Andrew J. Mead 2@9952 (The Infinite Improbability BBS)
           Direct Dial
             (919) 489-9446 (2400bps - Durham, NC - PCPursuit NCRPT)
           Postal Mail
             Andrew J. Mead
             WWIVMail
             PO BOX 1155
             Chapel Hill, NC 27514-1155



    ** Technical Information

       WWIVMail is written in Turbo Pascal, and compiled in either
       Turbo Pascal 5.5 or Turbo Pascal 6.0 (depending on which
       computer I was last on).  WWIVMail does not use any direct
       screen activity, and should be compatible with DESQview and
       other multi-taskers.

       Source code licenses are available, please see the enclosed
       REGISTER.FRM file.



    ** Credits

       I would like to thank Dennis O'Dell (Plain Brown Wrapper) for
       prodding me on this program (all 4 days it took to write) as
       well as helping me test it and suggesting most of the options.
       Dennis can be thanked, bothered, or complained to at
           FidoNet
             Dennis O'Dell 1:151/204 Another World BBS
           WWIVnet
             Plain Brown Wrapper #1@9968 Another World BBS
           or directly dialed in the US at
             (919) 220-6299 (2400bps - Durham, North Carolina)

       (I would also like to thank Mollie and Rob for putting up with
       my phone calls and helping when Dennis was not there)

       Finally, I would like to thank
           Joaquim H. Homrighausen and Advanced Engineering sarl for
           FrontDoor.
                                      and
           Wayne Bell for WWIV and WWIV Network software.

       without whom none of this would have been necessary.







                                         7