TriBBS 4.02 Interim Update Documentation
                    ----------------------------------------

     TriBBS 4.02  provides a  couple of new  features that  require further
     explanation.


     Nonstandard IRQs
     ----------------

     Because  a number  of sysops  have  expressed interest  in having  the
     ability  to run  TriBBS with nonstandard  IRQs, I have  decided to put
     support for them into 4.02 and not wait for 4.1.

     First of all, please note that  many doors (read that as most)  do NOT
     support  nonstandard IRQs.   Also, some external  protocol drivers may
     not support nonstandard IRQs.

     By default, ISA PCs use the following IRQs for COM1 through COM4:

     COM1        IRQ4
     COM2        IRQ3
     COM3        IRQ4
     COM4        IRQ3

     Therefore, it  is possible  to have four  serial devices  connected to
     your PC.  If they require interrupts to  function, then you are really
     limited to only  two serial ports because  COM1 and COM3 use  the same
     IRQ and  COM2  and COM4  use  the same  IRQ  and the  way  the PC  was
     originally designed does not allow for sharing of interrupts.

     You can  get around this  by assigning  a nonstandard  IRQ setting  to
     serial devices on COM3 and COM4.

     XT  compatible machines  have 8 available  interrupt vectors  (IRQ0 to
     IRQ7) and are used as follows:

     IRQ0        System timer
     IRQ1        Keyboard
     IRQ2        Available
     IRQ3        COM2
     IRQ4        COM1
     IRQ5        Hard disk controller
     IRQ6        Floppy disk controller
     IRQ7        LPT1

     As you can see,  you are pretty much limited  to using either IRQ2  or
     IRQ7 on an XT compatible machine.

     AT compatible machines  have 16 available  interrupt vectors (IRQ0  to
     IRQ15) and are used as follows:

     IRQ0        System timer
     IRQ1        Keyboard












     IRQ2        Cascade input for second interrupt controller
     IRQ3        COM2
     IRQ4        COM1
     IRQ5        LPT2
     IRQ6        Floppy disk controller
     IRQ7        LPT1
     IRQ8        Realtime clock
     IRQ9        Redirected as IRQ2
     IRQ10       Available
     IRQ11       Available
     IRQ12       PS/2 mouse
     IRQ13       Math coprocessor
     IRQ14       Hard disk controller
     IRQ15       Available

     As  you can see, an  AT compatible machine has a  lot more options for
     using a nonstandard IRQ (IRQ5, IRQ7, IRQ10, IRQ11, and IRQ15).

     If you  have any perhiperials  that use  interrupts, be sure  that you
     don't use an interrupt that is already in use by another device.


     Configuring for a Nonstandard IRQ
     ---------------------------------

     You can  configure your system  for a nonstandard IRQs  through either
     TriMan's Node  Configuration option or  through a new  BBS.EXE command
     line  switch.  The  command line  switch is /Qn  where "n" is  the IRQ
     number  to be used.  For example if  you wanted to use IRQ5 for a node
     that is already setup for COM3,  you would enter the following command
     line:

     BBS /Q5


     DOWNLOAD.BAT
     ------------

     TriBBS 4.02  now supports  a DOWNLOAD.BAT file.   This  optional batch
     file will  be called, if it exists in  the node's main directory, just
     after a file is moved into the TRANSFER directory.   It is called with
     parameters  that  are  similar  to   the  ones  TriBBS  uses  to  call
     UPLOAD.BAT:

     %1 - Is the file's complete pathname.
     %2 - Is the file's extension, if any.