DIGIFOSSIL V1.2 - Jan 20, 1992

                            FOSSIL Driver for DigiBoards
                          ================================

                                               Technique Computer Systems
                                               Ste 110, 1841 Oak Bay Ave
                                               Victoria, BC   V8R 1C4
                                               CANADA
                                               BBS: (604) 598-1546
                                               FAX: (604) 598-4318


          What is it?
          -----------
          DIGIFOSSIL (DF) is  the program YOU  need in order  to get a huge
          number of  doors, written for  FOSSIL systems,  working with your
          Wildcat! IM system.  (if you need a FOSSIL for a non-IM/Digiboard
          system,  try either  X00 or  BNU, which  are available  from many
          BBSs)


          What is a FOSSIL anyway?
          ------------------------
          FOSSIL  (Fido/Opus/Seadog  Standard Interface  layer) was created
          to  provide  a  standard   communications  interface  during  the
          evolution of some other BBS  software (namely Fido(tm),  Opus and
          Seadog(tm)).  It  provided a  superset of  the serial  port calls
          available  on  the early  IBM  PC,  and provided  a  way  to port
          programs  from  one  system  to  another,  that  may  not contain
          hardware compatible serial ports, to the IBM PC.

          By writing programs that use a standard set of calls, all that is
          required  to move  the system  to dissimilar  hardware, is  a new
          FOSSIL driver.


          What does DIGIFOSSIL do?
          ------------------------
          It provides the translation services so that calls made to FOSSIL
          standards are  translated into equivalent  Digiboard calls.  This
          allows HUNDREDS of  applications written for  FOSSIL to run under
          IM, as if they were running  on a FOSSIL based system.  This list
          includes many  popular doors such  as Tradewars  & Scrabble (tm).
          Think  of  it as  the  'missing  link' between  your  Wildcat! IM
          system, and vast number of existing doors.










                                        - 1 -

            DigiFossil (c) Copyright 1992,1993 Technique Computer Systems







          Installation
          ------------
          Simple,  part of  your AUTOEXEC.BAT,  before Desqview  is loaded,
          should load the TSR driver for DF.  Simply add:

                       DFTSR

          to  your  AUTOEXEC.BAT.   When  DFTSR  starts,  it  will identify
          itself,  and indicate  the  type of  Digiboard  installed.  DFTSR
          currently  takes about  14k  of memory,  and  can be  loaded into
          'HIGHRAM' using QEMM's LOADHI, or DOS 5's LOADHIGH commands.
          It must be loaded AFTER the DigiBoard (XIDOS5) driver is loaded.
          DFTSR does  not enable  FOSSIL support,  that is  done separately
          with DF.


          Using Doors that work with FOSSIL Drivers
          -----------------------------------------
          Although  DIGIFOSSIL may  not run  all doors,  it will  run those
          doors that  require or  support FOSSILs.   If a  program does not
          mention that  it will utilize  a FOSSIL, it  probably doesn't use
          it, and won't work with DIGIFOSSIL.

          When  running  a door  that  uses  FOSSIL calls,  simply  use the
          program DF to enable or  disable FOSSIL support in the DIGIFOSSIL
          driver (DFTSR which was loaded in your AUTOEXEC.BAT).  To run DF,
          simply specify which Digiboard channel,  and whether to enable or
          disable support.   If no  port number is  given, DF  will use the
          port specified by the environment variable WCPORTID.

          ** NOTE **
          **    Be sure that if you enable FOSSIL support, that you
          **    disable it again before re-loading Wildcat!.
          **    (I suggest that you add DF OFF to your CAT.BAT)
          ** NOTE **

          examples:   DF ON 1     - turn on FOSSIL support for port 1
                      DF OFF      - turn off support for port WCPORTID
                      DF LOCK 1   - turn on FOSSIL support for port 1
                                     but don't allow the door to change
                                     the baud rate.

          When  using doors  that support  FOSSIL,  such as  Scrabble, COM1
          (w/FOSSIL),  is  the  same as  Wildcat's  port  1  (and Digiboard
          channel  0).  That  is to  say, if  you set  WCPORTID to  1, your
          should tell the DOOR to use (FOSSIL) COM1.

          If you have a door that does  NOT support a locked DTE rate (that
          is when the baud rate to the modem is higher than the actual link
          connection speed), AND  you are using  a modem that  has a locked
          DTE, you should can use the DF LOCK command rather than the DF ON
          command, which will prevent the  DOOR from changing the baud rate
          on the modem.



                                        - 2 -

            DigiFossil (c) Copyright 1992,1993 Technique Computer Systems







          ** NOTE! **
              Programmers  writing code  that makes  FOSSIL calls
              should  note  COM1, and  WCPORTID=1  both  refer to
              channel 0 (DX=0) in the  actual with respect to the
              actual FOSSIL and DigiBoard drivers.

          Examples
          --------
          This is an  example DOOR.BAT for  Chris Hall's excellent Scrabble
          door.

          DOOR1.BAT
             @ECHO OFF
             REM This batch file is located in your HOME directory,
             REM and is copied to the work directory and executed.
             REM It needs to change to the right location of the
             REM door and run the program
             REM
             REM  ******* Enable Fossil
             DF ON
             CD \DOORS\scrab
             scrabdor node%WCNODEID%.cfg
             CD \WC30
             REM  ******* Remember to turn it off again
             DF OFF


          Files
          -----
          The following files should be included in this archive, and for
          authenticity,   it   should   contain   the   PKZIP  authenticity
          verification for TECHNIQUE COMPUTER SYSTEMS.

              DF.EXE         - to enable and disable DIGIFOSSIL support
              DFTSR.EXE      - the DIGIFOSSIL driver
              DF.DOC         - this document file
              ORDERFRM.DOC   - Ordering information


          Registration & Ordering
          -----------------------
          DIGIFOSSIL is  NOT free.  Although  it is distributed  in a fully
          functional   form,  continued   use   beyond  30   days  requires
          registration.   Registered  versions   are  always  available  to
          registered users on the PLYWOOD PC BBS at 604-598-1546.
          Registration costs $15 (US), or $18 (Canadian).  To order, please
          use the order form found in this archive.  You can also order the
          product  online on  the Plywood  PC BBS  at 604-598-1546,  or FAX
          completed order  forms to  604-598-4318.  With  your registration
          you will receive:

              - a disk with the registered version of DIGIFOSSIL
              - a certificate of registration



                                        - 3 -

            DigiFossil (c) Copyright 1992,1993 Technique Computer Systems







          Support
          -------
          For further information, or technical support of DIGIFOSSIL, your
          best bet is to call the call the Plywood PC BBS at 604-598-1546
          (V32bis/HST), and join conference 2 (DIGIFOSSIL support).
          Other options are: leave email to SCOTT BRYNEN in the 3rd party
          support conference on MSI's Bulletin Board (805-395-0650), or the
          MSI-OffTopic conference, that is echoed to many email networks.
          Another option is to FAX us at 604-598-4318.

          Some FOSSIL applications may not work.  If you have problems with
          a specific application  (or have found one  that works well), let
          us know, so  that in future  versions we can  list doors that are
          known to work.

          If  you  have  a  node  that  crashes  during  operation  of  the
          DIGIFOSSIL, please make  a note of the  conditions under which it
          happened,  and  if  you  are able,  open  another  DOS  window in
          Desqview, and type
                DF STAT <port-number>
          where  <port-number>   is  the   port  that   has  failed.   This
          information that this provides will  be most helpful in trying to
          diagnose what has happened.


          Updates
          -------
          By  registering the  product  with Technique  Computer,  you will
          receive the most recent version by mail (please allow 6-8 weeks),
          and be able  to download the  latest version of  it from our BBS.
          Once  you are  registered, you  can  download future  versions of
          DIGIFOSSIL from the Plywood PC BBS.


          Credits
          -------
          I have a few people to thank.  Firstly, I would like to thank Ron
          Green, and Ken O'Connor for their patience, and for letting me at
          their Wildcat!  IM baby in  order to get  DIGIFOSSIL working, and
          also to Ron Green for saying "but we can't run Scrabble now we've
          gone to Wildcat! IM",  and to Chip North (and his co-sysop), for
          actually  proving that it works with more than Scrabble.  Also to
          the some other sysops, notably  David Spellman and Charles Alpert
          that have helped in tracking down some of the odder problems.












                                        - 4 -

            DigiFossil (c) Copyright 1992,1993 Technique Computer Systems







          History
          -------
          Version 1.2 - Jan 20/1993
                   - various internal optimizations
                   - fixed some problems with software detecting
                      DF being installed
                   - DFTSR now loads on system where the first channel
                      isn't channel 0

          Version 1.1 - Jan 11/1993
                   - Added support for forcing Locked DTEs.
                   - Added beg screen to unregistered version.
                      (lack of registrations caused this)
                   - Fixed typos in the orderform.
                   - Added better support for detecting errors during
                      installation.

          Version 1.0 - Dec 25/1992
                   - Initial Release


          Legal Stuff
          -----------
          DIGIFOSSIL  is Copyright  1992-1993, Technique  Computer Systems,
          all rights  reserved.  This  product is  provided "AS-IS" without
          warranty of any kind.  All risk as to the results and performance
          are  assumed  by you.   Technique  Computer Systems  will  not be
          liable for  any damages, direct  or indirect,  resulting from the
          use, or inability to use, this product.

          Wildcat! isn't actually a trademark of Mustang Software Inc (but
                        is a very good BBS package)
          DigiBoard could be a trade mark of Digi
          Fossil (Fido(tm)/Opus/Seadog(tm) interface layer), is the
                        combined product and ideas of Tom Jennings, Thom
                        Henderson, Vince Perriello, & Wynn Wagner (& many
                        more).
          Fido is a trade mark of Tom Jennings
          Seadog is a trade mark of Thom Henderson and/or System
                        Enhancements Associates.
          QEMM and Desqview are trade marks of Quarterdeck Office Systems.
          Scrabble is a trade mark of Hasbro Inc.














                                        - 5 -

            DigiFossil (c) Copyright 1992,1993 Technique Computer Systems