MUSTANG SOFTWARE, INC.                             WCFILE 2.0   1
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


     TABLE OF CONTENTS

          INTRODUCTION  . . . . . . . . . . . . . . . . . . . . . . . .   4
               HOW TO USE THIS MANUAL . . . . . . . . . . . . . . . . .   4
               WHAT IS WCFILE?  . . . . . . . . . . . . . . . . . . . .   4
               SYSTEM REQUIREMENTS  . . . . . . . . . . . . . . . . . .   4
               TECHNICAL SUPPORT SERVICES . . . . . . . . . . . . . . .   5
               LIMITED WARRANTY . . . . . . . . . . . . . . . . . . . .   6
               DISTRIBUTION POLICY AND COPYRIGHT  . . . . . . . . . . .   6
                    COPYRIGHT . . . . . . . . . . . . . . . . . . . . .   6
                    THE SOURCE CODE . . . . . . . . . . . . . . . . . .   7

          INSTALLING WCFILE . . . . . . . . . . . . . . . . . . . . . .   7

          COMMAND REFERENCE . . . . . . . . . . . . . . . . . . . . . .   7
               INTERACTIVE OPERATION  . . . . . . . . . . . . . . . . .   7
                    ADDING FILES WITH DESCRIPTION . . . . . . . . . . .   9
                         Move filename and description pointers . . .    11
                         File group specified after description . . .    12
                         Add to file area . . . . . . . . . . . . . .    12
                         Set "Uploaded by" to . . . . . . . . . . . .    13
                         Add keywords automatically . . . . . . . . .    13
                         Insert extended descriptions . . . . . . . .    13
                         Keep downloads and uploader information  . .    13
                         Add files not on disk as "offline" . . . . .    14
                         Use today's date instead of file date  . . .    14
                         Change descriptions for existing files . . .    14
                    ADDING FILES WITHOUT DESCRIPTIONS . . . . . . . .    15
                         Add to File area . . . . . . . . . . . . . .    15
                         Use today's date . . . . . . . . . . . . . .    16
                         Prompt for description . . . . . . . . . . .    16
                         Add keywords automatically . . . . . . . . .    16
                    SCAN FILES & DIRECTORIES INTO MEMORY  . . . . . .    16
               BATCH OPERATION  . . . . . . . . . . . . . . . . . . .    17
                         Add files w/o description  . . . . . . . . .    17
                         Add files w/ description . . . . . . . . . .    17
                    COMMAND LINE OPTIONS  . . . . . . . . . . . . . .    17
                         Force Mono . . . . . . . . . . . . . . . . .    17
                         Force Color  . . . . . . . . . . . . . . . .    17
                         Set default uploader . . . . . . . . . . . .    17
                         Set default file area  . . . . . . . . . . .    17
                         Set default positions  . . . . . . . . . . .    17
                         Drive/directory to scan at startup . . . . .    17
                         Load table of cross references . . . . . . .    17
                         Set "Offline" flag . . . . . . . . . . . . .    17
                         Do NOT insert keywords . . . . . . . . . . .    17
                         Insert extended descriptions . . . . . . . .    18
                         Keep downloads and uploader info . . . . . .    18
                         Use today's date . . . . . . . . . . . . . .    18
                         Change descriptions for existing files . . .    18





          MUSTANG SOFTWARE, INC.                             WCFILE 2.0   2
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


          ADDING CD-ROMS TO WILDCAT! USING WCFILE . . . . . . . . . .    19

          LOGGING AND ERROR MESSAGES  . . . . . . . . . . . . . . . .    19

          INTRODUCTION  . . . . . . . . . . . . . . . . . . . . . . . .   2
               HOW TO USE THIS MANUAL . . . . . . . . . . . . . . . . .   2
               WHAT IS WCFILE?  . . . . . . . . . . . . . . . . . . . .   2
               SYSTEM REQUIREMENTS  . . . . . . . . . . . . . . . . . .   2
               TECHNICAL SUPPORT SERVICES . . . . . . . . . . . . . . .   3
               LIMITED WARRANTY . . . . . . . . . . . . . . . . . . . .   4
               DISTRIBUTION POLICY AND COPYRIGHT  . . . . . . . . . . .   4
                    COPYRIGHT . . . . . . . . . . . . . . . . . . . . .   4
                    THE SOURCE CODE . . . . . . . . . . . . . . . . . .   5

          INSTALLING WCFILE . . . . . . . . . . . . . . . . . . . . . .   5

          COMMAND REFERENCE . . . . . . . . . . . . . . . . . . . . . .   5
               INTERACTIVE OPERATION  . . . . . . . . . . . . . . . . .   5
                    ADDING FILES WITH DESCRIPTION . . . . . . . . . . .   7
                         Move filename and description pointers . . . .   9
                         File group specified after description . . .    10
                         Add to file area . . . . . . . . . . . . . .    10
                         Set "Uploaded by" to . . . . . . . . . . . .    11
                         Add keywords automatically . . . . . . . . .    11
                         Insert extended descriptions . . . . . . . .    11
                         Keep downloads and uploader information  . .    11
                         Add files not on disk as "offline" . . . . .    12
                         Use today's date instead of file date  . . .    12
                         Change descriptions for existing files . . .    12
                    ADDING FILES WITHOUT DESCRIPTIONS . . . . . . . .    13
                         Add to File area . . . . . . . . . . . . . .    13
                         Use today's date . . . . . . . . . . . . . .    14
                         Prompt for description . . . . . . . . . . .    14
                         Add keywords automatically . . . . . . . . .    14
                    SCAN FILES & DIRECTORIES INTO MEMORY  . . . . . .    14
               BATCH OPERATION  . . . . . . . . . . . . . . . . . . .    15
                         Add files w/o description  . . . . . . . . .    15
                         Add files w/ description . . . . . . . . . .    15
                    COMMAND LINE OPTIONS  . . . . . . . . . . . . . .    15
                         Force Mono . . . . . . . . . . . . . . . . .    15
                         Force Color  . . . . . . . . . . . . . . . .    15
                         Set default uploader . . . . . . . . . . . .    15
                         Set default file area  . . . . . . . . . . .    15
                         Set default positions  . . . . . . . . . . .    15
                         Drive/directory to scan at startup . . . . .    15
                         Load table of cross references . . . . . . .    15
                         Set "Offline" flag . . . . . . . . . . . . .    15

          ADDING CD-ROMS TO WILDCAT! USING WCFILE . . . . . . . . . .    17





          MUSTANG SOFTWARE, INC.                             WCFILE 2.0   3
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


          LOGGING AND ERROR MESSAGES  . . . . . . . . . . . . . . . .    17





          MUSTANG SOFTWARE, INC.                             WCFILE 2.0   4
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


          INTRODUCTION

          HOW TO USE THIS MANUAL

          This documentation is organized for use as an initial setup
          guide, and as a reference book. Introductory information on
          WCFILE is presented first, followed by step-by-step installation
          and configuration instructions and command reference.

          Since this version of WCFILE has been rewritten completely, it
          introduces many new functions and concepts. We urge you to become
          familiar with the program by printing, reading and saving this
          documentation file. The WCFILE program has context-related online
          help available by pressing [F1] at any point in the program.
          However, there is no substitute for reading the operational
          reference to become familiar with the numerous features
          available. 

          After you have installed and run WCFILE, the manual will serve as
          a reference guide. It is indexed extensively. After completing
          the initial setup you should be able to easily locate material on
          any topic by checking the Table of Contents or the Index.

          WHAT IS WCFILE?

          WCFILE is a utility for adding files and file descriptions to
          your Wildcat database, whether those files exist on your hard
          drive in your regular Wildcat file areas, on CD-ROM in regular
          Wildcat file areas, or in any path or subdirectory on your
          system, whether it's on a CD-ROM, a hard drive, or even off-line.

          SYSTEM REQUIREMENTS

          WCFILE does not have any special hardware requirements beyond
          what is needed to setup and run WILDCAT! BBS -- its only specific
          requirement is sufficient free disk space to add to your WILDCAT!
          files database, and create its own temporary files during
          operation.

          WCFILE 2.2 is designed to operate with WILDCAT! BBS 3.x in the
          Single Line, Multi-Line and Professional versions only. WCFILE
          will NOT work with version 1.x, 2.x, or WILDCAT! TEST DRIVE

          Here is the suggested minimum hardware and software
          configuration:

          IBM Personal Computer (or true compatible). 

          384K (minimum) free RAM.





          MUSTANG SOFTWARE, INC.                             WCFILE 2.0   5
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


          Hard disk drive.

          80 column monochrome or color monitor.

          PC-DOS or MS-DOS, ver 3.0 or later. 

          Wildcat! BBS version 3.x 

          A CD-ROM drive is optional.

          TECHNICAL SUPPORT SERVICES

          WCFILE was designed for ease of use, and this manual should
          contain the answers to most of your questions. Read it first and
          check the appendices for trouble-shooting procedures. 

          You may first want to call our own WILDCAT! Public-access system
          at 805-395-0650 and leave a quick question to our technical
          staff. You will NOT have full access on your first call since we
          need you to fill out the user database information, such as your
          password, etc. Your security access will be raised as soon as
          possible, usually within 24 -- 48 hours, providing your WILDCAT!
          registration information is on file. This method of obtaining
          support is especially useful if you want expert guidance
          regarding the most advanced features.

          Another alternative is CompuServe where we are a part of the PC
          Vendor Support Forum. You reach us by typing GO PCVENA and then
          selecting Sub Topic 9. Our PIN is (75236,3312). 

          If you are still unable to find the answer to a question or just
          need a quick explanation, please call us between 9:00am and
          5:00pm Pacific time. You can reach technical support at (805)
          334-2240. 

          Support is not available by mail or FAX.

          When calling for support please:

          -    Have your Wildcat! registration number ready. 

          -    Be at your computer with your manual handy. 

          -    Be ready to describe the problem in detail.

          -    If possible, be ready to duplicate the problem on your
               system.

          -    Please be ready to refer to your DOS manual for questions
               regarding DOS. A working knowledge of DOS is absolutely





          MUSTANG SOFTWARE, INC.                             WCFILE 2.0   6
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


               necessary.

          -    You can call technical support direct at (805) 334-2240.

          WCFILE is constantly undergoing enhancements and revisions. This
          is normal software maintenance. The current version of WCFILE may
          be a major or minor release. We can provide the best support to
          users who are running the current major release, and encourage
          you to keep your software updated. The cost is minimal and the
          benefits are great.

          LIMITED WARRANTY

          THIS PRODUCT IS PROVIDED "AS IS" WITHOUT WARRANTY OF ANY KIND.
          THE ENTIRE RISK AS TO THE RESULTS AND PERFORMANCE OF THE PROGRAM
          IS ASSUMED BY YOU. SHOULD THE PROGRAM PROVE DEFECTIVE, YOU (AND
          NOT MUSTANG SOFTWARE, INC. OR ITS DEALERS) ASSUME THE ENTIRE COST
          OF ALL NECESSARY SERVICING, REPAIR OR CORRECTION. FURTHER,
          MUSTANG SOFTWARE, INC. DOES NOT WARRANT, GUARANTEE, OR MAKE
          REPRESENTATIONS REGARDING THE USE OF, OR THE RESULTS OF THE USE
          OF THIS PROGRAM IN TERMS OF CORRECTNESS, ACCURACY, RELIABILITY,
          CURRENTNESS, OR OTHERWISE; AND YOU RELY ON THE PROGRAM AND ITS
          RESULTS SOLELY AT YOUR OWN RISK. MUSTANG SOFTWARE, INC. CANNOT
          ACCEPT RESPONSIBILITY FOR SYSTEM DAMAGE, LOSS OF PROFIT, OR ANY
          OTHER SPECIAL, INCIDENTAL, OR CONSEQUENTIAL DAMAGE RESULTING FROM
          THE USE OR INABILITY TO USE THIS PRODUCT.

          Mustang Software, Inc., DOES warrant to the original licensee of
          a REGISTERED product that the program disk(s) on which the
          program is recorded be free from defects in materials and
          workmanship under normal use and service for a period of ninety
          (90) days from the date of delivery as evidenced by a copy of
          your receipt. Mustang Software, Inc.'s entire liability and your
          exclusive remedy shall be replacement of the disk not meeting
          Mustang Software, Inc.'s Limited Warranty.

          DISTRIBUTION POLICY AND COPYRIGHT

          COPYRIGHT

          WCFILE software and this document is (C) Copyright 1992 Mustang
          Software, Inc. All rights reserved. WCFILE is a Trademark of
          Mustang Software, Inc.

          Any specific hardware/software names used in this document are
          trademarks of specific manufacturers.

          Regardless of the method of marketing, WCFILE is not in the
          public domain. It is copyrighted by Mustang Software, Inc. All
          rights are reserved. We grant you the right to make and





          MUSTANG SOFTWARE, INC.                             WCFILE 2.0   7
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


          distribute as many copies of WCFILE as you wish, or post it for
          download from your BBS.

          The latest version of WCFILE is always available from the Mustang
          Software HQ! BBS, at 805-395-0650.

          THE SOURCE CODE

          The source code for WCFILE is not available. This decision gives
          us the ability to guarantee the integrity of our product in this
          era of software contamination. It is not available either under
          the TEST DRIVE concept, or as a Commercial product.

     INSTALLING WCFILE

          Before you run WCFILE (or any other BBS utility that works
          directly on your datafiles) for the first time, BACK UP. We'll
          say it again. BACK UP your important BBS files.

          WCFILE requires no special installation routine. Simply extract
          WCFILE.EXE, WCFILE.HLP and WCFILE.DOC from the distribution file
          and place them in your WILDCAT! home directory. This is normally
          C:\WC30. 

     COMMAND REFERENCE

          WCFILE should always be run from your WILDCAT! home directory
          (the one that contains MAKEWILD.DAT). It must be run with a
          unique WCNODEID= setting, or you will defeat the file locking
          mechanism and corrupt your WILDCAT! databases. If you are running
          the single line version under DESQview, you MUST bring down
          WILDCAT! before running WCFILE. If you are using the Autonode
          feature on a multiline system, WCFILE will find a free node
          number to use.

          INTERACTIVE OPERATION

          Here is a brief overview of the way WCFILE functions when used
          interactively:

          WILDCAT! BBS has two ways of locating files within each file area
          on your system. The first way is to store files in the drive and
          path specified in the File Area Definition section of MAKEWILD. 

          The second way is to store files in other drives and paths
          throughout your system (including files in multiple
          subdirectories on a CD-ROM drive), adding them to a WILDCAT! file
          area by specifying their true path. 

          WCFILE supports both options, allowing you to add files anywhere





          MUSTANG SOFTWARE, INC.                             WCFILE 2.0   8
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


          on your hard drive, and practically any CD-ROM, to your BBS.

          THE MAIN MENU:

ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³             WCFILE v2.0  - File database utility for WILDCAT v3              ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°ÕÍÍÍÍÍÍÍÍÍÍÍÍ WCFILE MENU ÍÍÍÍÍÍÍÍÍÍÍÍÍ¸°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°³                                      ³°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°³ Add files - With Description File    ³°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°³ Add files - No description file      ³°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°³ Scan Files & Directories into Memory ³°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°³ Exit                                 ³°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°³                                      ³°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
 ESC-Exit  F1-Help

          From the main menu you can select the following options:

          þ Add With Description File

               This option will add files to your WILDCAT! file database,
               importing descriptions from a prepared description file.
               This may be an ASCII text file on a CD-ROM, an ALLFILES list
               from a BBS, or a capture file from an online session.

               The default here is to add files which exist in the drive
               and path pointed to by MAKEWILD's File Area Definition for
               each area. 

               You may also add files which exist in other drives and paths
               to a WILDCAT! file area by using the Scan Files &
               Directories Into Memory option first. This procedure stores
               the true path for each file in memory, and adds this
               information to the WILDCAT! file database when you add these
               files. 





          MUSTANG SOFTWARE, INC.                             WCFILE 2.0   9
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


          þ Add Files without Description File

               This is a quick way to add files on your disk to your
               Wildcat file database. You have the option to enter
               descriptions manually for each new file. This option only
               adds files which exist in the primary file area path
               specified in Makewild. Move the files to the path specified
               in MAKEWILD and then select this option.

          þ Scan Files & Directories Into Memory

               This option scans a drive and/or subdirectory, and memorizes
               the file names and true paths. This is so WCFILE can locate
               the files in the case that they are not present in the
               directory as specified by MAKEWILD.

               Scanning other drives and paths allows you to add files to a
               file area, even if the files exist outside the file area's
               path as specified in MAKEWILD. This is done by adding the
               file's true path to your WILDCAT! file database. This option
               allows you to add files on CD-ROM drives with unusual
               directory structures.

          þ Exit

               Leave the program

          ADDING FILES WITH DESCRIPTION

          You will first be prompted to enter the drive, path and name of
          the text file you wish to import. If you know the drive, path and
          filename of the description file you wish to import, type the
          information into the window now. You will notice that the window
          will scroll left and right, allowing you to type in a full path. 

          Or, you may use the [F2] key to bring up a pick list of files in
          the current drive and subdirectory. Here is a sample screen
          showing the use of a file pick list:





          MUSTANG SOFTWARE, INC.                            WCFILE 2.0   10
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³             WCFILE v2.0  - File database utility for WILDCAT v3              ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°Õ F:\PRIVATE\MUSTANG\*¸°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°³ allfiles.lst   251k ³°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°ÕÍÍÍÍÍÍÍÍÍÍÍÍ W³ allfiles.zip    96k ³Í¸°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°³              ³ ansi.key         1k ³ ³°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ³ backup.bat       1k ³ÍÍÍÍÍÍÍÍ¸°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°³ Description File³ beta-app.zip     6k ³        ³°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ³ bsdemo.exe      71k ³ÍÍÍÍÍÍÍÍ¾°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°³ Exit         ³ cdfiles.lst     89k ³ ³°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°³              ³ employ.txt       2k ³ ³°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍ³ files.lst        1k ³Í¾°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°³ firework.exe     4k ³°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°³ fpi_msi.txt      5k ³°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°ÔÍÍÍÍÍÍÍ    for more Í¾°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
 ESC-Exit  F1-Help  F2-Pick Drive

          Press [F2] again from this screen to get a pick list of available
          drives. Move the highlight bar to the drive or file you wish to
          select, and press [ENTER].

          WCFILE will load the selected text file into a window, and you
          will then see the screen pictured below. We are using
          ALLFILES.LST from the HQ! BBS as an example. On the following
          page is an example of how the description file looks when loaded
          into WCFILE: 





          MUSTANG SOFTWARE, INC.                            WCFILE 2.0   11
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³             WCFILE v2.0  - File database utility for WILDCAT v3              ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
°°ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Add Files With Descriptions ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸°°°
°°³**** WC! BBS Advertisements                                              ³°°°
°°³                                                                         ³°°°
°°³AD4BBS.GIF      6,662   02/11/92 | ad for BBS generic                    ³°°°
°°³DwnLds: 28   Last DL:   02/23/92 |                                       ³°°°
°°³                                                                         ³°°°
°°³ADELIGHT.SCR    7,098   12/29/91 | Ad for Afternoon Delight BBS (407)870-³°°°
°°³DwnLds: 70   Last DL:   02/24/92 |                                       ³°°°
°°³<ÍÍ File ÍÍ>                       <ÍÍÍÍÍÍÍÍÍÍÍÍ Description ÍÍÍÍÍÍÍÍÍÍÍÍ³°°°
°°³1         12                       36                                    ³°°°
°°³     Move filename & description pointers:   (enter to change)           ³°°°
°°³   File group specified after description: N   Add to File area: 1       ³°°°
°°³                     Set 'uploaded by' to: JOHN DOE                      ³°°°
°°³               Add keywords automatically: Y                             ³°°°
°°³             Insert extended descriptions: N                             ³°°°
°°³  Keep downloads and uploader information: N                             ³°°°
°°³       Add files not on disk as "offline": N                             ³°°°
°°³    Use today's date instead of file date: N                             ³°°°
°°³   Change descriptions for existing files: N                             ³°°°
°°ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
 ESC-Abort  F1-Help  F2-Pick  F10-Go

          WCFILE scans your text file for names and descriptions of files
          to import. A wide range of text file formats are supported -- for
          example, an ALLFILES.LST from a BBS, a capture file from an
          online session, or a description file on a CD-ROM. 

          Here is a step-by-step discussion of the options available in
          this screen:

          Move filename and description pointers: (enter to change)

               For WCFILE to use your text file to import descriptions, you
               need to tell it where the file name and description fields
               begin and end. The arrows at the bottom of the file
               description should point to the start and end of the file
               name and description fields within the description file.  

               To line up the pointers with the beginning and ending of the
               name and description fields, press the TAB key to highlight
               an arrow, then move the arrow left or right using the LEFT
               and RIGHT cursor keys. You cannot make the file name field
               shorter than 12 characters, or the description field shorter
               than 20 characters. 

               Note that WCFILE will permit file names with interior





          MUSTANG SOFTWARE, INC.                            WCFILE 2.0   12
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


               spaces, as well as file names with a dot. For  example,
               "LOGIN.COM" and "LOGIN   COM" would both be considered valid
               by WCFILE. On the other hand, file names without extensions,
               for instance "LOGIN", would not be considered valid by
               WCFILE.

               When you have positioned the arrows correctly, press F10 to
               continue. 

          File group specified after description:

               Some CD-ROMS (for example RBBS in a Box) contain file group
               information at the end of the file description field,
               showing the file's true location on the disk. By answering
               "Yes" to this option, WCFILE will read the path information
               and store it in the file database. If a file group is
               specified, WCFILE will pop up a list of available file areas
               when it encounters a file with a new group number, so that
               you can match group number to WILDCAT! file area. "Skip this
               area" is an additional option in the pick list.

          Add to file area:

               You may add files to one WILDCAT! file area at a time.
               Please select the file area you would like to update. By
               default, only files which exist in the path specified in the
               file area definition for each area will be added. If you
               Scan files & directories into memory first, files specified
               in the description path, that reside in other paths or file
               areas will be added to the database. Press F2 to pop up a
               pick list of available WILDCAT! file areas. 

               Below is a screen snapshot of a file area pick list:
             





          MUSTANG SOFTWARE, INC.                            WCFILE 2.0   13
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³             WCFILE v2.0  - File database utility for WILDCAT v3              ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
°°ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Add Files With Descriptions ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸°°°
°°³**** WC! BBS Advertisements                                              ³°°°
°°³                                    ÕÍÍÍÍÍÍÍÍÍÍÍÍ File Area ÍÍÍÍÍÍÍÍÍÍÍÍ¸³°°°
°°³AD4BBS.GIF      6,662   02/11/92 | a³   1 - Utilities                   ³³°°°
°°³DwnLds: 28   Last DL:   02/23/92 |  ³   2 - Games                       ³³°°°
°°³                                    ³   3 - CAD Support Files           ³³°°°
°°³ADELIGHT.SCR    7,098   12/29/91 | A³   4 - Word Perfect Utilities      ³³°°°
°°³DwnLds: 70   Last DL:   02/24/92 |  ³   5 - Text Information            ³³°°°
°°³<ÍÍ File ÍÍ>                     <ÍÍ³   6 - UPLOADS (private until rev'd³³°°°
°°³1         12                     34 ³   7 -                             ³³°°°
°°³     Move filename & description poi³   8 -                             ³³°°°
°°³   File group specified after descri³   9 -                             ³³°°°
°°³                     Set 'uploaded b³  10 -                             ³³°°°
°°³               Add keywords automati³  11 -                             ³³°°°
°°³             Insert extended descrip³  12 -                             ³³°°°
°°³  Keep downloads and uploader inform³  13 -                             ³³°°°
°°³       Add files not on disk as "offÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ    for more Í¾³°°°
°°³    Use today's date instead of file date: N                             ³°°°
°°³   Change descriptions for existing files: N                             ³°°°
°°ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
 ESC-Abort  F1-Help  F2-Pick  F10-Go

          Set "Uploaded by" to:

               This is the name which will appear in the "Uploaded by:"
               field in the WILDCAT! file database. The default is the name
               of the sysop, as entered in MAKEWILD.

          Add keywords automatically:

               Select "Yes" for this option if you want WCFILE to generate
               keywords automatically from the file description, answer
               "No" to leave the keywords blank. 

          Insert extended descriptions:

               If you answer "Yes" to this option, WCFILE will import
               multi-line file descriptions into the "Extended Description"
               field in your WILDCAT! file database for each entry. Be
               aware that this will take additional space in your file
               database.

          Keep downloads and uploader information: 

               If you answer "Yes" to this option, WCFILE will preserve the
               name of the uploader and the number of downloads for each





          MUSTANG SOFTWARE, INC.                            WCFILE 2.0   14
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


               file.

               WILDCAT! two-line file descriptions containing this
               information are supported directly. Other text file listings
               should contain the information in the following format(s):

               þ The text "UPLOADED BY:" should be at the beginning of a
               description section.

               þ The number of downloads should be specified by "<nnn>" or
               "[nnn]" at the beginning of a description section.

          Add files not on disk as "offline":

               This option allows you to add "Offline" files to your
               WILDCAT! database, by importing a list of filenames and
               descriptions for files which do not actually exist on your
               disk. WCFILE will set the "Offline" flag in each database
               record, and WILDCAT! will prompt your users to generate a
               request to the sysop if they wish to download these offline
               files.

          Use today's date instead of file date:

               If you wish the files you add to your database to show up as
               "New files" regardless of the actual file date, WCFILE will
               add them to the database using today's date.

          Change descriptions for existing files:

               If this option is set to "Y", WCFILE will use the file
               descriptions in the text file to overwrite the descriptions
               in your WILDCAT! file database. This option is useful for
               adding descriptions to files currently in the database, but
               lacking descriptions, or to import a spell-checked, edited
               text listing of your file database to replace incorrect
               entries. 

               Use this selection with caution -- it could overwrite valid
               file information with invalid information, or even describe
               a completely different file than the one in your WILDCAT!
               database if a file name in the list happens to match a file
               name in your database.





          MUSTANG SOFTWARE, INC.                            WCFILE 2.0   15
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


          ADDING FILES WITHOUT DESCRIPTIONS

          You may add files to one WILDCAT! file area at a time. Please
          select the file area you would like to update. By default, only
          files which exist in the path specified in the file area
          definition for each area will be added. If you use the Scan files
          & directories into memory first, files in other paths will be
          added to the database.

          You will see the following menu:

ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
³             WCFILE v2.0  - File database utility for WILDCAT v3              ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°ÕÍÍÍÍÍÍÍÍÍÍÍÍ WCFILE MENU ÍÍÍÍÍÍÍÍÍÍÍÍÍ¸°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°³                                      ³°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°³ Add files - With Description File    ³°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°ÕÍÍÍÍÍÍÍÍÍÍÍ Add Files Without Descriptions ÍÍÍÍÍÍÍÍÍÍÍÍ¸°°°°°°°°°°°°°°
°°°°°°°°°³                                                       ³°°°°°°°°°°°°°°
°°°°°°°°°³            Add to file area: 1                        ³°°°°°°°°°°°°°°
°°°°°°°°°³             Set uploader to: JOHN DOE                 ³°°°°°°°°°°°°°°
°°°°°°°°°³           Use today's date:  N                        ³°°°°°°°°°°°°°°
°°°°°°°°°³      Prompt for description: Y                        ³°°°°°°°°°°°°°°
°°°°°°°°°³  Add keywords automatically: Y                        ³°°°°°°°°°°°°°°
°°°°°°°°°³                                                       ³°°°°°°°°°°°°°°
°°°°°°°°°ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°
 ESC-Abort  F1-Help  F2-Pick  F10-Go


          Add to File area: 

               Again, you may add files to one WILDCAT! file area at a
               time. Press [F2] for a pick list of available file areas.

          Set uploader to:

               This is the name which will appear in the "Uploaded by:"
               field in the WILDCAT! file database. The default is the name
               of the sysop, as entered in MAKEWILD.





          MUSTANG SOFTWARE, INC.                            WCFILE 2.0   16
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


          Use today's date:

               If you wish the files you add to your database to show up as
               "New files" regardless of the actual file date, WCFILE will
               add them to the database using today's date.

          Prompt for description:

               Answer "Yes" if you would like WCFILE to prompt you to type
               in a file description for each file added to the database.

          Add keywords automatically:

               Answer "Yes" if you would like WCFILE generate keywords
               automatically when you type in the file description. This
               option may be selected only if you answer "Yes" to the
               "Prompt for description" option.

          SCAN FILES & DIRECTORIES INTO MEMORY

          This option scans a drive and/or subdirectory, and stores the
          file names and true paths in a temporary file. Use the Add With
          Description File selection after scanning with this option to add
          files to a WILDCAT file area.

          Scanning other drives and paths allows you to add files to a file
          area, even if the files exist outside the file area's path as
          specified in MAKEWILD. This is done by adding the file's true
          path to your WILDCAT! file database. This option allows you to
          add files on CD-ROM drives with unusual directory structures. 

          This also allows you to add files to more than one WILDCAT! file
          area, when using the "Add files with descriptions" option. WCFILE
          will add ALL files it finds in valid WILDCAT file areas to the
          correct area if the disk is scanned prior to adding files with
          description.

          To use this option prior to adding files, enter the drive letter,
          or subdirectories within a drive, that you wish WCFILE to scan.





          MUSTANG SOFTWARE, INC.                            WCFILE 2.0   17
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


          BATCH OPERATION

          WCFILE offers a number of command line parameters and switches,
          for interactive and batch mode processing. To use WCFILE in a
          batch processing event, the /D command line switch is required,
          along with any necessary combination of command line options
          listed below:

               /D                  Add files w/o description - NON
                                   INTERACTIVE

               /D:<descrfile>      Add files w/ description - NON
                                   INTERACTIVE

          COMMAND LINE OPTIONS

               /M                  Force Mono

               /C                  Force Color

               /U:<uploader>       Set default uploader

               /A:<area>           Set default file area

               /P:fs,fe,ds,de      Set default positions of start and end
                                   of filename and description for add
                                   w/description (if they're not valid the
                                   defaults of 1,12,34,76 are used). The
                                   length of the description must be at
                                   least 20, the filename at least 12 

               /S:<scanarea>       Drive/directory to scan at startup

               /X:<xreffile>       Load table of cross references for add
                                   with area specified at end of
                                   description. File should be in the
                                   format:

                                   <Listed File Area>,<Wildcat File Area>
                                   <Listed File Area>,<Wildcat File Area>
                                   <Listed File Area>,<Wildcat File Area>
                                   <Listed File Area>,<Wildcat File Area>

                                   If this is not specified you will be
                                   prompted for each new file area.

               /O                  Set "Offline" flag for files not found
                                   on disk 

               /N                  Do NOT insert keywords





          MUSTANG SOFTWARE, INC.                            WCFILE 2.0   18
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


               /E                  Insert extended descriptions

               /K                  Keep downloads and uploader info

               /T                  Use today's date instead of file date

               /C                  Change descriptions for existing files.


          Here are some example command lines for batch processing:

          WCFILE /D:\TEXT\MASTER.DIR /P:1,12,34,80 /A:1

          WCFILE /D:\ROMAREA6.LST /S:G\ /A:12 /T





          MUSTANG SOFTWARE, INC.                            WCFILE 2.0   19
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


     ADDING CD-ROMS TO WILDCAT! USING WCFILE

          Since each CD-ROM is arranged in a slightly different way, and
          updates are frequent and unpredictable, WCFILE takes a "generic"
          approach to adding these ROMs to your WILDCAT! database.

          Your first task, when installing a CD-ROM to use with WILDCAT!,
          is to take a look at its structure. 

          The easiest to install are those with lots of files organized
          into a group of directories by topic. A good example of this
          would be the CARRS (Nightowl) disk. Each subdirectory contains a
          text file listing the contents of that directory, with file
          names, dates, sizes, and descriptions. 

          All you need to do to install CD-ROMS organized this way, is to
          make a note of the paths on the CD-ROM, then run MAKEWILD and add
          each of these paths as a file area. Then run WCFILE, scan the
          entire disk, then select "Add files with descriptions". Type in
          the name and path of the description file(s), and let WCFILE
          process it.

          Other CD-ROM disks are organized differently, with files in
          multiple subdirectories but belonging to the same file area.
          These require you to create a WILDCAT! file area that points to a
          subdirectory on your hard drive. Scan the disk using the "Scan
          Files & Directories into Memory", then use the "Add files with
          descriptions" option, as above.

          WCFILE will enter these files in your WILDCAT! file area, and
          place the true location of the file in the "Path on CD-ROM" field
          in the file database. It will create zero-byte files for each
          file name on your hard disk in the primary file path you
          specified for WILDCAT! for this file area. The zero-byte files
          help speed up wildcard searches by reading a DOS directory rather
          than the file database for this function.

          A third type of CD-ROM, typified by "RBBS in a Box" organizes
          files in multiple subdirectories, but includes a cross-reference
          number at the end of the file description line in the "DIR" file.
          If this information is present in the file, first scan the disk,
          then use the "Add files with descriptions" to add the files.
          Toggle the "File area specified at end of description" to "Yes",
          and let WCFILE add the files. WCFILE will prompt the operator to
          select a WILDCAT! file area for each cross-reference number.

     LOGGING AND ERROR MESSAGES

          WCFILE logs its activity in WCFILE.LOG, and reports the name of
          each file added to the database. When adding files with





          MUSTANG SOFTWARE, INC.                            WCFILE 2.0   20
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


          descriptions, any text in a description file which WCFILE is
          unable to parse will be logged for your examination.

          Fatal errors cause WCFILE to exit to DOS, display a descriptive
          error message in bright white flashing letters on screen, and
          write the error message to the WCFILE.ERR log in the \WC30
          directory before returning control to Wildcat. These messages are
          usually self-explanatory. 

          Complete lockups are rare, and usually indicate a hardware
          problem, or a TSR or other program interfering with WCFILE. One 
          type of program known to cause problems on some systems when used
          with WCFILE and WILDCAT! are TSR file compressor-decompressor
          programs -- those which claim to increase hard disk space.

          A few error messages may be the result of a corrupted Wildcat
          database -- these are usually caused by running WCFILE and the
          single line version of Wildcat in two DESQview windows at the
          same time, or by duplicating node ID numbers in the multi-line
          versions of Wildcat. Certain third party utilities which do not
          lock and unlock files properly may cause share violations or
          locking problems if run concurrently with WCFILE. 





          MUSTANG SOFTWARE, INC.                            WCFILE 2.0   21
          ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ