Graphics modes 9++ and 10++›===========================››This text is a translation of the›original article published›in Polish magazine "Atarynka",›no. 2/2002.››  The most often used mode is "Konop's›  mode", used for the first time›  by Konop/Shadows in "Asskicker".›  It has been used for years,›  and probably there's no other mode,›  as fast and with similar screen›  parameters (square pixels, small›  screen memory, 16 shades [or other›  GTIA mode]).›                           lewiS/AiDS›                "32 shades in mode 9"›                   (article published›            in "Atarynka" no. 1/2002)››In this article I'll present the way›of obtaining a mode, which differs›from "Konop's mode" (also known as 9+)›by lack of blank lines, and which›is called, depending on used GTIA›mode, 9++ or 10++.››Advantages of the new mode›--------------------------›1. It's faster than the one with›   blank lines (9+).›2. Display List is significantly›   shorter (every mode line is created›   by single DL instruction).›3. Since DL for this mode can load›   ANTIC's screen memory pointer only›   once, you don't need two DLs for›   double-buffering, you may just›   alter the screen address in DL.›4. It's easy to set another (up to 16)›   height of a line of mode›   (e.g. 3, 5 or 6 instead of 4).›5. It looks better - it's a matter›   of taste, but in my opinion colors›   in GTIA 10 mode look much better›   - the blank lines lower›   the brightness and saturation.››Disadvantages›-------------›1. This mode makes ANTIC eat less›   cycles, for the cost of some›   additional work of 6502. There's›   not much of this work for CPU,›   unfortunately it must be properly›   synchronized with the display.›   It means that in practice it's›   not easy to get the first advantage,›   i.e. it requires additional›   programming effort.›2. It's known that there're problems›   with displaying graphics in›   the last, 240th line. This isn't›   a problem for 9+ mode, because›   you may put JVB at the end of DL›   to get 60 lines. In modes 9++/10++›   we may stay with 59 lines or...›   use advantage 4 and lower›   height of the top or the bottom›   line to 3.››Idea›----›The idea is simple - let's make ANTIC›display the same line a few times,›using its internal memory. This is›what happens in mode 8 (system›GRAPHICS 3), where the data comes from›main memory only in the first line,›and then from ANTIC's own memory.››Theory›------›ANTIC contains internal 4-bit register›DCTR, which counts scanlines. Normally›for every line of mode it counts from›zero to a value specific to the mode›(in our case of ANTIC 15 mode it's›zero). It's different after enabling›vertical scrolling. In first scrolled›line DCTR counts from VSCROL to 0,›in the subsequent normally, and in›the last from 0 to VSCROL. "Counts›from a to b" means: first DCTR is›loaded with a, and near the end of›every line DCTR is compared with b,›if there's equality, next DL›instruction will be fetched; otherwise›DCTR is incremented by 1.›Consider following DL:›$2f›$0f›and VSCROL=13 (decimal). We will see:›- first line 4 times (DCTR values›  13,14,15,0 - DCTR wraps from 15›  to 0, because it's 4-bit)›- second line 14 times (DCTR values›  from 0 to 13)›Similarly for VSCROL=3:›- first line 14 times›- second line 4 times›What is important, the screen data›repeated in several scanlines is›fetched from main memory only once.››Obtaining the mode›------------------›As should be now easy to figure out,›to have each line shown 4 times,›we create following Display List:›b($6f),a(screen)›b($0f)›b($2f)›b($0f)›...›and only have to update VSCROL›register in proper moments.››Following picture should help in›understanding what happens›(in this English translation›I'll just use ASCII art, I hope›it's readable :-) ).››DCTR› 13  @-------------------------› 14  --------------------------› 15  --------------------------›  0  --------------------------›  0  ==========================›  1  ==========================›  2  ==========================›  3  ====!==================*##›        \--visible screen--/››'-' - first line of mode›      (bit 5 in DL is set)›'=' - second line of mode›      (bit 5 in DL is clear)›'@' - here VSCROL must contain 13›'!' - here starts DLI›'*' - here VSCROL must contain 3›'#' - here we put 13 into VSCROL››This picture shows two lines›of mode, i.e. 8 scanlines.›It also shows the timing (scale›is not preserved) - as time goes›by, each scanline is displayed›from the left to the right.››First VSCROL must contain 13 decimal›(it's a 4-bit register, so high›nibble of value written to $d405›may be anything). As soon as ANTIC›loads DCTR with this value, first›line of mode is guaranteed›to be displayed correctly. Then›the second line will be shown›and only near the end of last›scanline VSCROL is required to›contain 3. So we have much time›to write 3 to VSCROL. We may do it›e.g. on DLI in the first line.›It's much worse with preparing›to display third line of mode.›As you see on the picture ('#')›there's little time to put 13 into›VSCROL (just a few cycles).››Possible implementations›------------------------›We may update VSCROL:›a) using DLI interrupt,›b) inside unrolled code of our effect,›c) using one of POKEY timer IRQs.››Implementation a) is undoubtedly›easiest, unfortunately it's also›the slowest one. Optimal is›implementation b), unfortunately›it can be applied only to simple›effects, like bump mapping.›Implementation c) could be superior›to a), because POKEY timers may›be set with single cycle accuracy,›so we don't need to waste time›in the interrupt routine.›Unfortunately this implementation›is impractical (in a game or demo),›because POKEY timers are also used›for generating sound and we don't›want to sacrifice music quality›(less channels) only to enable›new graphics mode.››DLI interrupt routine›---------------------›We want it fast. Apparently using›DLI every second line of mode,›i.e. every 8 scanlines, is enough.›We enable it in DL opcodes with›5th bit clear. The interrupt›starts near the beginning of last›scanline (see '!' on above picture).›Normally the NMI service routine›checks the interrupt type (DLI›or VBLKI) and saves the registers›(at least the accumulator).›Nevertheless we still have much time›before writing 13 to VSCROL.›The easiest way to waste this time›(and ensure proper synchronization)›is to use WSYNC. Then we just write›13 to VSCROL and apparently it's›late enough to write 3 there.›Here comes an example:››    lda #<dli›    sta $200›    lda #>dli›    sta $201›    lda #$22›    sta $22f›    lda #<dl›    sta $230›    lda #>dl›    sta $231›    lda #$40›    sta $26f›    lda #$c0›    sta $d40e›    jmp *››dli pha›    sta $d40a›    lda #13›    sta $d405›    lda #3›    sta $d405›    pla›    rti››; 2 blank lines, 1 line of mode›dl  db $90,$6f›    dw $f000›; 29 times $8f,$2f => 58 lines›    db $8f,$2f,$8f,$2f,$8f,$2f,$8f,$2f›    db $8f,$2f,$8f,$2f,$8f,$2f,$8f,$2f›    db $8f,$2f,$8f,$2f,$8f,$2f,$8f,$2f›    db $8f,$2f,$8f,$2f,$8f,$2f,$8f,$2f›    db $8f,$2f,$8f,$2f,$8f,$2f,$8f,$2f›    db $8f,$2f,$8f,$2f,$8f,$2f,$8f,$2f›    db $8f,$2f,$8f,$2f,$8f,$2f,$8f,$2f›    db $8f,$2f›    db $41›    dw dl››What's not obvious at first sight,›is why we write 3 to VSCROL at the end›of DLI, not before writing to $d40a ?›As shown on the picture, VSCROL›in second line of mode is checked›near the end of scanline. Exactly,›there is done a check if current›DL opcode should end its execution.›But when we use DLI, which is called›in last scanline of DL opcode, there's›second (first in the order›of execution) comparison of DCTR›with VSCROL. Thus VSCROL must already›contain 3 when the interrupt starts.››How many cycles we gain?›------------------------›It's an important question, because›it was mentioned as the first›advantage of the new mode.›Single line of 9+ mode can look in DL›as follows:›    db $0f,$00,$4f›    dw screen›    db $00›Total: 6 cycles for DL›+ (64 or 80) cycles for screen›(depending on width).›For 9++ mode it's only one DL opcode›(i.e. 1 cycle) + (32 or 40) cycles›for screen. Additionally 6502 has›to update VSCROL, which takes›6 cycles. Counting whole screen›(2 blank lines, 59 lines of mode,›screen address in first line, JVB)›we get:›Narrow screen:›9+:  1+59*(6+64)+2+3=4136›9++: 1+59*(1+32+6)+2+3=2307›Normal screen:›9+:  1+59*(6+80)+2+3=5080›9++: 1+59*(1+40+6)+2+3=2779›Roughly speaking the gain is about›6-7% of CPU time. Unfortunately it's›true only for the optimal›implementation, i.e. updating VSCROL›in unrolled code. If we use DLI,›as in the example, the new 9++ mode›turns out a bit slower than old 9+›(but still much faster than a mode›with no blank lines, done only›with DL). The reason is the time›we waste in STA $d40a. A good›(but hard) solution is to make use›of this time for some calculations.››Don't forget about other advantages›of 9++ mode, which can make it better›for your needs than a traditional›DL-only mode. When using DLI, there's›one more advantage: you can change›the background color in different›lines at almost no cost.››             Piotr Fusik (Fox/Taquart)›                        <fox@scene.pl>››P.S. You may use the described VSCROL›method to get other interesting modes,›e.g. hardware-supported 40x40 text›mode.›