Welcome to the MAE assembler.››The design goal of MAE was to provide a highly integrated environment for›an editor, assembler, and debugger.  It is very easy to use, and contains›many features to save the programmer keystrokes, and development time.  It›does not take the approach of, "If I make the assembly speed fast enough,›nothing else matters."  I believe that only a small portion of a project's›development time is spent waiting for the assembler to assemble your file.›Therefore, programming efforts were mainly concentrated on making the›editing and debugging processes easier.  MAE is fairly quick, but not the›fastest assembler available.  For example, the editor module of MAE is›2850 lines of source, and assembles to a disk file in 18 seconds.››MAE uses the standard E: device to allow easy compatibility with the XEP80›and other 80 column devices or software drivers.  The speed of Atari's›built-in 40 column device is not the greatest, and so you will also find›the HYPER E: screen accelerator on the disk.  This will more than double›the screen performance when it is installed, and it is highly recommended.›MAE also includes software drivers that allow 64 column and 80 column›editing on a high-speed Gr.8 screen.  Thanks goes to Itay Chamiel for his›work on these drivers.››I am always interested in hearing comments or suggestions about MAE.  You›can reach me at:›John Harris›45346 Graceway Dr›Ahwahnee CA 93601›USA›internet: jharris@poboxes.com››Here are some of the features of the MAE development system.››MAE provides an excellent full-screen type editor with many features such›as key macros, automatic 'JSR' and return to subroutine labels, block moves›and copies, and multiple undo.››Compatible with the XEP80, and probably most other video boards that›provide an E: handler interface.  Software drivers for 64 and 80 column›screens are also provided.››High level of integration between editor, assembler, and debugger.  The›editor can take you directly to lines that had assembly errors.  The›debugger can reference labels in the symbol table and assemble single›program lines.››Very efficient -- it will save you a lot of typing.››True local labels that are referenced between global labels.››Full text substitution macros.››Can assemble directly to bank select memory or bank select cartridges.››Uses very little system RAM.  Most of the code resides in bank select›memory.››Full 65816 and 24 bit support.››- MEMORY USAGE AND CONFIGURATION -››This assembler is designed to run in up to 3 banks of the extended memory›available on the 130XE or other memory expanded Atari.  The bank numbers›are configurable.  A portion of the assembler must reside outside of bank›select RAM, and in this version, it will occupy $B700-$BBFC.››Memory usage for the source file and symbol table is configurable.  In›addition, they can use bank select RAM for addresses within the $4000-$7FFF›range, which keeps this area in main RAM free for the user.  Having the›symbol table in bank select RAM has one other benefit.  It will usually stay›intact so that the labels can be used from the debugger.  The default values›for memory usage will place the symbol table in one bank by itself, and the›source buffer from LOMEM to $B6FF, with the segment from $4000-$7FFF in›another bank of extended RAM.  $4000-$7FFF in main RAM is free to the user,›unless running the 64 or 80 column handlers which use part of this space,›from $5600-$7FFF.››This assembler isn't designed for a 64K machine, but it can be configured›to operate in a limited fashion.  Because the bulk of the code sits at›$4000-$7FFF, it is right in the middle of RAM if you don't have bank›select memory.  The best you will be able to do, is set the text buffer›from $8000-$B6FF, and the symbol table from LOMEM to $3FFF.  That will›only give you about 14K for your text buffer, and your symbol table may›not always be available for the debugger, but otherwise, all functions›should work as described.  See INSTALL.DOC for more details.››Zero page memory is saved and restored from the editor and assembler, so›that they will effectively leave all of ZP available to the user.››Buffer memory addresses and several configurable parameters are stored at›the beginning of the program file.  The parameters are located at +3 bytes›from the start address, which will be +9 bytes when counting the DOS binary›header.  A utility, CONFIG.COM, is now provided to edit these parameters.›A description of them follows.  (Words are 6502 standard Lo,Hi)››Word - Text buffer start adr.  If 0, the editor will use MEMLO.  (Default)›Word - Text buffer end.  If 0, the editor will use MEMTOP.  Default $B6FF.›Word - Symbol table start adr.  Default $4000, in bank select memory.›Word - Symbol table end.  Default $7EFF.  (The code for symbol table search›       is at $7F00).›Byte - Assembly CPU mode.  0=65816, $80=6502.  Other bits may be used in›       the future.›Byte - Editor mode.  Two bits are currently defined:›       When bit 7 is on ($80), Insert mode is active.›       When bit 6 is on ($40), spaces are converted into Tabs.›       When bit 5 is on ($20), editor will start with Caps lock on.›       Other bits may be used in the future.›Byte - Debugger mode.  Currently unused, but reserved for future options.›3 Bytes - Tab settings for Assembly code fields.›Byte - When drawing the screen for a particular location, such as a›       Find or Goto command, this byte sets the screen row where the›       desired line will be located.  If you set this to 0, the line›       will be on the top row.  $0C will put the line in the middle›       of the screen.  Default is 6.›Byte - # of lines the PgUp & PgDn command will move by.  Setting›       this to $18 gives single screen paging.  If you normally use›       scrolling for short moves, you can set this value to something›       like $60 to jump through the file in larger steps.›Byte - Line length saved in the Undo buffers.  Default is 39.  You›       can increase this to 79, if you want entire 80 column lines saved.›       You can also decrease this number to something like 25, if you›       want to increase the number of history buffers without using›       extra memory.  You would only lose the comment field for any›       restored lines.›Byte - # of Undo buffers.  This number sets how many lines of history›       can be undo'ed.  Default is 16.  Multiplied by the number above,›       equals the total size needed for undo storage, located at the end›       of the text buffer.›Byte - Sets what bank of extended memory to put the assembler.  It should›       be a value appropriate for the $D301 register.  Default is $E3.›Byte - Sets what bank to put the symbol table.  Default is $E7.  Be aware›       that there is a small piece of code from $7F00-$7FFF that gets›       stored in the same bank as the symbol table.›Byte - Sets what bank to put part of the source text.  Default is $EB.›       If source memory is configured from LOMEM to $B6FF, the segment›       from $4000-$7FFF will be put in this bank, leaving that region of›       main RAM free for object code or other uses.›2 Bytes - An optimistic number of bytes for future expansion.›String - Default drive and dir spec.  Must be in the form Dn:?????,›       like "D3:*.*", or "D3:*.S" if you want dir listings to only›       show a certain file type.  Filenames for loading and saving›       do not require a full "Dn:" filespec.  If you type just a›       name, it will be preceded with the default drive selected here.››- THE MAIN MENU -››The program will display the main menu once it has loaded.  During an›editing session, the Esc key will return to this menu, and Esc will also›return to the editor when you are in the menu.››Main Menu Commands:››A - Assemble current file.  Hold the Shift key when pressing A to turn on›    the assembler listing.  The only current way to send an assembler›    listing to the printer, is to first use the "O" debugger command to›    enable output echo to the printer.››B - Break to the monitor.  Actually issues a 00 BRK instruction.››D - Go to DOS.  If you return to the editor by running at the start address,›    the source file will still be intact.  This is automatic in SpartaDOS›    by using the RUN command.  For other DOSes, you will need to supply the›    starting address which is currently $B800, but may change in later›    versions.››L - Load file.  You do not need to type an entire filespec.  The default›    drive 'Dn:' will be prepended if the entered name doesn't have a ':'.›    Press Shift-L to append to the end of an existing file.››M - Macro load and save.  The contents of the keyboard macro buffer can be›    saved to and loaded from disk files.  This allows you to create useful›    key macros and save them to disk for later use.››P - Do Pass 2 only of the assembly.  A full assembly must have already been›    performed, and then this function may be used if the source code was›    changed in such a way that didn't effect any label addresses.  This can›    save a lot of assembly time, but please do not use it unless you›    understand what it does and are certain that no label addresses have›    been changed since the last assembly.››S - Save File.  Save displays the last loaded filename.  Press Return to›    accept it, or backspace and change.  Press Shift-S to save a marked›    text block.  To do this, mark the starting line with ^Z, then move to›    the ending line and enter the Esc-Shift-S command.  To print a file or›    text block, you may need to convert the text to spaces only, and then›    save to P:.››T - Tab convert.  It will prompt to convert to Tabs or Spaces.  Tab›    converted text will have $7F TAB characters for any sequences of›    spaces that can be compressed.  The conversion is done from back to›    front for best speed, but it can still take awhile.  It is also›    possible to run out of RAM when converting to spaces.  After this›    command is entered, the editor will remain in the specified mode.  In›    other words, if you do a tab convert to spaces, all future entered›    lines will remain in an expanded space format.››V - (Value)  Will allow you to enter any expression, and then displays the›    calculated value in both hex and decimal.  This can be handy for›    getting the value of labels, or as a simple calculator.››X - Perform cross reference listing.  The source file must already have›    been assembled with the A command.  It allows you to enter a label name›    to start from, or just press return to create a cross reference for the›    entire symbol table.  Be prepared for this to take awhile.  This is a›    simple implementation that requires a full pass of assembly for each›    label.  On the positive side, it doesn't require any memory to build an›    XRef table, and so generating an XRef on large files should not have›    any problems running out of memory.  Plus, being able to specify label›    names directly makes it very easy, and much quicker, to get a report›    for one or two labels of immediate interest.››1-9 Get directory, and set default drive.  If you just want to change the›    default drive without getting a dir listing, press Esc after pressing›    the desired number.››Shift-Clear - Clear text buffer.››- EDITOR FILE FORMAT -››The editor saves files in straight ATASCII.  It can either keep all spaces›expanded, or can use $7F TAB characters to reduce the size of the file.›The text can be freely converted between these formats.  TAB compression›and expansion is done on a line by line basis while you are editing, which›is different from the way most editors handle TABs.  While you are editing›a line, TAB characters are not present, and the line will edit in the same›way as if it had only spaces.  When the line is saved back into the file,›the program will see if it can convert any sequences of spaces into TABs,›based on the configured TAB fields.  TABs are not rigidly enforced.›Meaning, if you slide a comment field a little to the left to make more›room, that spacing will be retained, and that particular place simply won't›be TAB converted.  Thus, it is simply a manner of saving memory and file›space.  The editor will actually run faster with the TAB setting on,›especially with the XEP80.››The editor allows line lengths up to 79 columns, and will scroll›horizontally for displays that are narrower than this.››- EDITING COMMANDS -››Standard Atari editing keys apply, with a few exceptions.  Clr & Set Tab›have no effect.  sese the configure bytes to change tabs.  Pressing the›Caps key without Shift will always set lower case instead of toggling.›Use Shift-Caps to set upper case.  1200XL function keys, as well as the›standard Atari arrow keys, can be used to move the cursor.››Return will insert a new line if pressed at the end of the current line.›Otherwise, it will just move to the line below.  Return does not break a›line in the middle, which works out better when entering source code.››In the following tables, a "^" symbol means to press Control along with the›key after the "^".  "S^" means press both the Shift and Control keys.››- MOVING AROUND -››S^Up Scroll Up›S^Dn Scroll Down.  These two commands are handy, because they scroll›     immediately, without waiting for the cursor to reach the screen's›     edge.›S^<  Page up by configurable # of lines›S^>  Page Down›^,   Start of line›^.   End of line›^T   Top of file›^B   Bottom of file›^S   Set mark at current location›^M   Go to Mark›^G   Goto line number.  When entering the line number at the prompt, you›     can also enter a '+' or '-' as the first character to move a number›     of lines relative to the current location.››- FIND & REPLACE -››^F   Find text -- not case sensitive.  '?' can be used as a wildcard.›^?   Change the wildcard character.  After issuing the command, press›     any other key to set the wildcard to that character.  The wildcard›     character is shared between the editor and debugger, and changing›     it within either module will affect uses in both modules.›S^F  Find by searching backwards towards the start of the file.›^R   Replace -- forward direction only.  It will ask for a Find string›     and then a Replace string.  For all matches of the find string, the›     editor will display an inverse '>' symbol in front of the occurrence.›     You may press Y to replace it, N to skip it, A to replace all›     occurrences to the end of the text, or Esc to abort.›     Max length for Find or Replace is 15 characters.›^N   Next.  If the previous operation was a replace, then you will be in›     the prompted replace mode if the string is found.  Otherwise, if the›     previous operation was a Find, then you will simply be taken to the›     next occurrence.›^P   Find Previous match, by searching backwards.›^L   Enter a label name, and the editor will jump to where the label is›     defined.  (By searching from the first column only.)›^J   The editor's version of a JSR.  It looks at the operand field of the›     current line, and jumps to where that label is defined.  It also›     sets a mark at the current line so that you can return with a ^H.›     The use of this function is not limited to JSR instructions.  JMPs,›     branches, even data variable locations can be traced with this›     command.  Basically, for any line that contains an operand field,›     ^J will attempt to find the location where that label is defined.›^H   Return to previous position where a ^J command was entered.›     ^H is also used to jump to locations that gave assembly errors.›     During the assembly, up to 16 error positions will be remembered.›     All bookmarks, and marks set from the ^J and error position›     reporting, will auto-adjust to any changes in the source text, so›     that they will always point to the correct line in the source file.››- BLOCK MOVES & COPIES -››^Z   Set block start.›^X   Cut from block start to current line, in a forwards direction only.›     If you find you want to mark a block backwards, the easiest way to›     do this, is to set the mark at the current line, then move backwards›     to the start of the block.  Press ^Z, then press ^M to return to›     where you started, and give the ^X or ^C command.  A clear to end of›     file operation can be done by pressing the keys, ^Z, ^B, ^X.›^C   Copy text from block start to current line, into the cut buffer.›     The text is left unchanged.›^V   Paste the cut buffer at current line.›^D   If there is a ^Z block mark set, ^D will duplicate the text block.›     Effectively, it does a ^C followed by a ^V.  Because this process›     clears the ^Z mark, multiple presses of ^D will not produce multiple›     copies of the same block.  Use ^V to paste additional blocks.  If›     there is no ^Z mark, then ^D will duplicate only the current line.››- KEY MACROS -››^W   (Write) Begin key macro recording.  When done, press ^3.  Up to 80›     keystrokes can be recorded, including Esc-Menu commands.›^E   Execute Macro›^K   Prompts for a number, and then will repeat the next entered key›     that number of times.  ^K cannot be used within a macro, but it can›     be used to execute ^E multiple times.››- MISC OTHER STUFF -››S^Del Delete to end of line›^I   Toggle Insert/Replace mode.›^A   Accept next keypress as literal ATASCII value.  This lets you enter›     Control graphic or international characters that would otherwise be›     treated as editor commands.›^U   Undo line deletes, or changed lines.  Does not undo block operations.›     A handy way to move one or more lines from one place to another, is›     to delete the original lines, move to the destination, and then use›     the Undo operation.›S^(  If a label exists on the current text line, move it up to the previous›     line.  (lines that already contain labels or comments are skipped over)›S^)  Same as above, but moves the label down.›S^[  Move the current line up one position relative to the lines around it.›S^]  Move the current line down one position.›^;   Comments or uncomments a block of text.  You can first mark the start›     of a text block with ^Z, and then press ^; on the last line of the›     block.  If the block does not start with a commented line, then ";"›     characters will be added to the front of all lines in the block.  If›     the block is already commented, then the ";"s will be removed.  If›     you do not set a ^Z block mark first, then this command will process›     only the current line, and move the cursor down.  This can be a›     faster way of commenting just a few lines.