BC205XLT.1

UNIDEN/BEARCAT 200/205XLT TEST MODE

by Bob Parnass, AJ9S

According to the Uniden/Bearcat 200/205XLT Service Information Manual, the
following procedure will load channels 1-25 with various test frequencies, and
zero the remaining 175 channels:

1. Press and hold three keys: 2, 9, and MAN simul-taneously and turn
the power switch on.

2. Set the power switch to the off position.

3. Repress and again hold three keys: 2, 9, and SCAN simultaneously and
turn the power switch on.

                        BC200/205XLT CELLULAR RESTORATION

Note: It is unlawful to monitor cellular telephone conversations. It is
possible to monitor signals from the deleted ranges even without conversion.
Simply add 21.7 MHz to the deleted frequency and enter the higher (image)
frequency. Reception is virtually identical in strength to that which would be
heard on the deleted frequency.

The frequencies deleted at the factory may be restored, but the
procedure must not be attempted by anyone unfamiliar with electronic
circuitry. Grove Enterprises assumes no liability for damage caused by
this procedure. (I won't eighter! WA2ISE).  The modification will void
your warranty.
CONTINUED IN FILE BC205XLT.4