BC205XLT.4
TOOLS REQUIRED: Small Phillips screwdriver, small wire cutters.

        1. Slide off the battery pack and remove the antenna from the scanner.
        2. Using a small Phillips screwdriver, remove the two screws from the
           back of the scanner, the two screws which hold the battery
           retaining spring at the base and the spring itself.
        3. Carefully pry the bottom of the rear cover from the radio and
           remove the cover.
        4. Locate the two small screws at the base of the circuit board and
           remove them. Gently pull the front panel from the mainframe at the
           base and separate them.
        5. Locate the (64 pin quad flatpack) microprocessor IC labelled
           "UNIDEN UC-1147" and the 10k ohm (brown-black-orange) leadless
           resistor positioned above the letters "DEN" on the IC.
        6. Using miniature wire cutters, cut the resistor body in two without
           disturbing anything else near it. If the left solder pad comes
           loose, it may be peeled from the board. Brush or blow away any
           residue. This completes the restoration.
continued in file bc205xlt.2