Chapter 16





Program Timing                                                                 

344   Fastgraph User's Guide


Overview

     It is occasionally necessary to delay a program's execution for a brief
period, or to determine how long it takes to execute specific sections of a
program. Fastgraph includes routines to accomplish these tasks. Some of these
routines are said to be real-time, which means they are independent of a
system's processor speed, while the speed of others is processor-specific.
This chapter describes both classes of timing routines, all of which are
independent of the other parts of Fastgraph.


Real-Time Routines

     Real-time operations center around the BIOS time-of-day clock, which is
nothing more than a counter that the system automatically increments 18.2
times per second. This number is often called the clock tick interrupt rate
because an interrupt routine performs the incrementing. In addition, each
increment is usually called a clock tick.

     The Fastgraph routine fg_waitfor delays a program's execution by the
number of clock ticks specified as its argument. Because fg_waitfor uses clock
ticks, the actual length of the delay is the same, regardless of the system's
processor speed. Even when Fastgraph's asynchronous sound routines quadruple
the clock tick interrupt rate, Fastgraph compensates for this internally so
fg_waitfor always works as though the actual rate were still 18.2 times per
second.

     Example 16-1 displays a message every five seconds that states how long
the program has been running. The fg_waitfor routine produces the five-second
delay by pausing 91 (18.2 times 5) clock ticks before the program displays
each message. The program returns to DOS when you press any key.

                                 Example 16-1.

              #include <fastgraf.h>
              #include <stdio.h>
              void main(void);

              void main()
              {
                 unsigned int seconds;
                 unsigned char key, aux;

                 fg_initpm();
                 seconds = 0;
                 do {
                    fg_waitfor(91);
                    seconds += 5;
                    printf("%u seconds have elapsed.\n",seconds);
                    fg_intkey(&key,&aux);
                 }
                 while (key+aux == 0);
              }                                                                

                                             Chapter 16:  Program Timing   345

     Another common application of fg_waitfor is to slow down a loop that uses
fg_intkey to check for keystrokes. In loops that do little else, we may call
fg_intkey too rapidly without this delay, and it is then possible that the
BIOS may not be able to store characters in its keyboard buffer fast enough. A
small delay, even one clock tick, often helps such "tight" loops.

     The fg_getclock routine provides an efficient way to measure time,
especially differences in time. This routine has no arguments and returns a
32-bit unsigned integer (as its function value) representing the number of
clock ticks since midnight. Example 16-2 demonstrates fg_getclock. In response
to any keystroke (except Escape, which returns control to DOS), the program
displays the number of clock ticks since midnight, and the number of ticks
since the program started.

                                 Example 16-2.

      #include <fastgraf.h>
      #include <stdio.h>
      void main(void);

      #define ESC 27

      void main()
      {
         unsigned long start, ticks;
         unsigned char key, aux;

         fg_initpm();
         start = fg_getclock();
         do {
            ticks = fg_getclock();
            printf("%lu ticks since midnight.\n",ticks);
            printf("%lu ticks since start of program.\n\n",ticks-start);
            fg_getkey(&key,&aux);
         }
         while (key != ESC);
      }



Routines Dependent on the System Speed

     The fg_waitfor routine described in the previous section is independent
of the system's processor speed. This means the actual length of its delay is
the same on any system. Another routine, fg_stall, is similar to fg_waitfor,
but its delay is proportional to the processor speed. Like fg_waitfor,
fg_stall has a single integer argument that specifies the length of the delay.
However, instead of being expressed in clock ticks, fg_stall measures the
delay in delay units. The fg_stall routine treats the length as an unsigned
quantity, so in 16-bit modes the maximum number of delay units we can specify
is 65,535. The following table lists the approximate number of delay units per
clock tick on three typical systems.                                           

346   Fastgraph User's Guide

                      system       delay units
                       type      per clock tick

                   Tandy 1000 HX       280
                   25 MHz 80386       3,400
                   40 MHz 80386       7,100

     Fastgraph includes a routine that determines the number of delay units
per clock tick for the processor being used. This is the fg_measure routine,
which has no arguments and returns the number of delay units per clock tick as
its function value. Once we determine this value, we can use fg_stall to delay
a program's execution in real time. This provides a much more refined delay
than the clock tick unit used by fg_waitfor.

     Example 16-3 is functionally identical to example 16-1, but it uses
fg_stall instead of fg_waitfor to delay the program execution. The program
first calls fg_measure to determine number of delay units equivalent to one
clock tick. It then passes this value to fg_stall, called 91 times inside the
for loop to create the five-second delay (because 91 clock ticks equals five
seconds). The program returns to DOS when you press any key.

                                 Example 16-3.

              #include <fastgraf.h>
              #include <stdio.h>
              void main(void);

              void main()
              {
                 int i;
                 int units_per_tick;
                 unsigned int seconds;
                 unsigned char key, aux;

                 fg_initpm();
                 seconds = 0;
                 printf("Benchmarking system speed...\n");
                 units_per_tick = fg_measure();
                 printf("Benchmark completed.\n\n");

                 do {
                    for (i = 0; i < 91; i++)
                       fg_stall(units_per_tick);
                    seconds += 5;
                    printf("%u seconds have elapsed.\n",seconds);
                    fg_intkey(&key,&aux);
                 }
                 while (key+aux == 0);
              }


     One final point: fg_measure takes a few seconds to benchmark the system
speed accurately. For this reason, you should only call fg_measure once
(typically at the beginning of the program) and use its return value instead
of calling fg_measure throughout the program.                                  

                                             Chapter 16:  Program Timing   347


Summary of Timing Routines

     This section summarizes the functional descriptions of the Fastgraph
routines presented in this chapter. More detailed information about these
routines, including their arguments and return values, may be found in the
Fastgraph Reference Manual.

     FG_GETCLOCK returns the number of clock ticks since midnight as its
function value. This quantity is a 32-bit unsigned integer.

     FG_MEASURE returns the approximate number of delay units per clock tick
as its function value. This quantity is proportional to the system's processor
speed.

     FG_STALL delays a program's execution for a given number of processor-
specific delay units.

     FG_WAITFOR delays a program's execution for a given number of clock
ticks. There are 18.2 clock ticks per second, regardless of the system's
processor speed.                                                               

348   Fastgraph User's Guide