W A S P
                                        =======



                              Water and Steam Properties
                              ==========================



                              Version 1.21    April 1995


                               Copyright (C) 1992, 1995
                                  All rights reserved





                                    Katmar Software
                                      PO Box 654
                                       Westville
                                         3630
                                     South Africa






                                                  _______
                                             ____|__     |               (tm)
                                          --|       |    |-------------------
                                            |   ____|__  |  Association of
                                            |  |       |_|  Shareware
                                            |__|   o   |    Professionals
                                          -----|   |   |---------------------
                                               |___|___|    MEMBER



         DISCLAIMER
         ----------

         The WASP programme and documentation are supplied as is.  Katmar
         Software disclaims all warranties, expressed or implied, including
         but not limited to, the warranties of merchantability and of fitness
         for any purpose.  Katmar Software and the programme author assume no
         liability for damages, direct or consequential, which may result
         from the use of WASP.


                                   TABLE OF CONTENTS
                                   -----------------



         Introduction to WASP  . . . . . . . . . . . . . . . . . . . . .    1

         Installation and Startup  . . . . . . . . . . . . . . . . . . .    1

         Hardware and Software Requirements  . . . . . . . . . . . . . .    3

         Quick Start for Experienced Users . . . . . . . . . . . . . . .    3

         Printing the Manual . . . . . . . . . . . . . . . . . . . . . .    5

         Detailed Operating Instructions . . . . . . . . . . . . . . . .    5
              Start-up . . . . . . . . . . . . . . . . . . . . . . . . .    5
              On-line Help System  . . . . . . . . . . . . . . . . . . .    5
              Data Entry . . . . . . . . . . . . . . . . . . . . . . . .    6
              Results Screens  . . . . . . . . . . . . . . . . . . . . .    7
              Properties of Wet Steam  . . . . . . . . . . . . . . . . .    8
              Searching for Specific Values of Properties  . . . . . . .    9
              Calculation Examples . . . . . . . . . . . . . . . . . . .   10
              Fixed Properties . . . . . . . . . . . . . . . . . . . . .   13
              Selecting Units  . . . . . . . . . . . . . . . . . . . . .   14
              Using the Menus  . . . . . . . . . . . . . . . . . . . . .   15
              Exiting from WASP  . . . . . . . . . . . . . . . . . . . .   15

         Accuracy Considerations . . . . . . . . . . . . . . . . . . . .   15

         The Shareware Distribution System . . . . . . . . . . . . . . .   18

         Getting an Up-to-date Evaluation Copy . . . . . . . . . . . . .   20

         WASP Licensing Policy . . . . . . . . . . . . . . . . . . . . .   21
              Software Support Policy  . . . . . . . . . . . . . . . . .   22
              Registration Procedures  . . . . . . . . . . . . . . . . .   22
                   Payment by Credit Card  . . . . . . . . . . . . . . .   23
                   Payment via CompuServe  . . . . . . . . . . . . . . .   23
                   Payment by Cheque or Money Order  . . . . . . . . . .   24
              Registration to Engineering Schools  . . . . . . . . . . .   24

         ASP's Ombudsman Policy  . . . . . . . . . . . . . . . . . . . .   25

         Bug Reports and Wish Lists  . . . . . . . . . . . . . . . . . .   25

         Revision History  . . . . . . . . . . . . . . . . . . . . . . .   25

         Other Engineering Packages from Katmar Software . . . . . . . .   26

         Appendix  . . . . . . . . . . . . . . . . . . . . . . . . . . .   26
              WASP Registration Form . . . . . . . . . . . . . . . . . .   26



         Water and Steam Properties - Version 1.21                    Page i


         Introduction to WASP
         ====================

         WASP is a replacement for traditional printed Steam Tables, but it
         goes further in that it provides a much wider set of properties, it
         eliminates the need for interpolating between data points, and it
         will work in any of the generally accepted units.

         It contains data for 15 point properties, and 17 temperature and
         pressure dependent properties.  Most of the correlations cover the
         range from -100  C to 800  C and up to 1000 bar, and some extend
         even beyond this range.  Calculated data points match published 
         data very closely.

         WASP can be used in two different ways, so that its use is similar
         to using printed Steam Tables, but of course easier and faster.

         The first way is when you know the temperature and pressure
         conditions of the ice, water or steam and you want to find the
         physical properties.  If you are working with wet steam you can also
         enter the steam quality to get some of the combined properties.

         The second option allows you to search for the conditions that give
         rise to a specific value of the enthalpy, entropy or density.  This
         is useful when doing calculations involving compression or
         throttling.

         The programme has been carefully designed for speed and ease of use. 
         On-screen prompts appear at every step to guide you. In addition
         there is context sensitive, on-line Help available at all times. If
         you are ever unsure of what the programme expects you to do, simply
         pressing the <F1> key will open a window with detailed instructions
         and information. You can also view any Help Screen at any time by
         selecting it from a Help Index.

         WASP is distributed as Shareware.  If this copy is registered to
         anyone other than yourself, then you are entitled to use it for a
         few weeks to determine its value to you.  If you decide to continue
         using the programme then you must register your copy with Katmar
         Software.  Further details on Shareware and the registration
         procedure are given later in this manual.


         Installation and Startup
         ========================

         Your first step should be to make a copy of your distribution disk. 
         Do not use your distribution disk as a working disk.  If your
         distribution disk is a 5.25 inch floppy, write protect it by putting
         a tab over the notch in the side of the disk.  If it is a 3.5 inch
         stiffy disk write protect it by sliding the plastic button in the
         corner to open the hole.  Take an unused disk of the same size as
         your distribution disk, label it as your working disk and make sure
         it is NOT write protected.  If you have identical A and B drives
         insert the distribution disk in Drive A and the working disk in


         Water and Steam Properties - Version 1.21                    Page 1


         Drive B.  At the DOS prompt type DISKCOPY A: B: and press <ENTER>. 
         If your A and B drives are not the same (or you do not have a Drive
         B) type DISKCOPY A: A: and press <ENTER>, and then follow the
         instructions on the screen to swap disks using the distribution disk
         as the SOURCE disk and the working disk as the TARGET disk.

         Installation of WASP entails simply copying all the files to either
         a diskette or to your hard disk.  The distribution disk that you
         received should contain all of the following files :-

              GETRESP.EXE      Utility for interactive batch files
              VIEW.COM         Text file display utility
              README           Brief details on WASP and its distribution
              README.BAT       A batch file used to display or print README
              REGISTER.DOC     Order form for registering your copy of WASP
              WASP.EXE         The executable file for WASP
              WASPBOOK.DOC     The instruction manual for the WASP package
              WASPDEFS.DTA     Holds the selected units etc
              WASPHELP.HLP     The on-line help instructions
              FILE_ID.DIZ      Description for BBS automation
              OMBUDSMN.ASP     ASP Ombudsman policy statement
              VENDOR.DOC       Info for shareware disk distributors and BBSs

         If instead of these files your disk contains a file named
         WASP121.ARC, WASP121.ZIP or some similar name then it means that the
         disk distributor has compressed the files into an archive file to
         get more onto the distribution disk.  In this case you will need to
         follow the distributor's instructions on how to extract the files
         from the archive before you can copy them.

         If you are installing to your hard disk you should copy the files to
         a separate sub-directory.  To create a new sub-directory on your
         hard drive follow these steps :-

             1)  Ensure that you are at the DOS prompt, ie display shows C:>
                 (if your hard drive is drive D display shows D:> , etc)
             2)  If you want the new sub-directory to be off the root
                 directory, type CD\ and press <ENTER>.  If you prefer the 
                 new sub-directory to be off some other directory, change to
                 that directory.
             3)  Type MD WASP and press <ENTER>.
             4)  Type CD WASP and press <ENTER>.  Display should show
                 C:\WASP>. If display does not show this, type PROMPT $P$G
                 and press <ENTER>.

         If your distribution disk contains all the files listed above,
         insert it into the A: drive and type COPY A:*.* and press <ENTER>.
         The programme is then ready to run.  If your distribution disk does
         not contain all the files listed above, but instead contains an
         archived file, copy that file to the new sub-directory (eg COPY
         A:WASP121.ZIP).  Then follow the distributors instructions to
         un-archive the files.

         Once the files have been copied you should type WASP and press
         <ENTER> to start the programme.  The programme starts with an


         Water and Steam Properties - Version 1.21                    Page 2


         opening screen and then a screen giving brief details of the
         shareware distribution system, before getting to the programme
         proper.  The initial screens can be skipped by pressing the
         <SPACE BAR>.

         If you are short of space on your hard disk you can delete some of
         the files.  Only two files are absolutely essential for running
         WASP.  These are WASP.EXE and WASPDEFS.DTA.  If you want to be able
         to use the on-line help facility you will also need the file
         WASPHELP.HLP, but the programme can run without it.  When you pass
         on copies of WASP to others please always include all the files on
         the distribution disk so that the recipient can make a full
         evaluation of the package.


         Hardware and Software Requirements
         ==================================

         WASP will run on virtually any IBM(tm) PC or compatible machine.  It
         has been designed to be able to be used on a minimum specification
         system, but also to make use of higher specification equipment if
         available.  For example it will run perfectly well on a monochrome
         screen, but will switch to colour if it detects a colour video card.
         Similarly it will use a numeric co-processor if it finds one, but
         will run quite happily (although of course more slowly) if none is
         found.

         Some EGA and VGA displays, particularly on portable computers, use
         varying shades of grey rather than true colour.  WASP would detect
         these machines as having colour screens and you may have some
         difficulty reading the display.  In this case you can force the
         programme to use the monochrome palette by pressing <Alt M> at the
         opening screen or by using the /M command line switch i.e. start the
         programme by typing WASP /M.  When you exit from the programme it
         will store this choice and start up in monochrome mode the next time
         you use it.

         Summary of system requirements :-
              DOS          :  2.11 or later
              RAM          :  512k or more
              DISK         :  360k or larger floppy, stiffy or hard disk
              VIDEO        :  Monochrome, CGA, EGA, VGA or compatible
              Co-processor :  Optional


         Quick Start for Experienced Users
         =================================

         Even if you are only a moderately experienced computer user you
         should be able to use WASP without going into this manual in any
         depth at all.  The brief instructions that follow in this section
         should be all you need to make full use of the programme.  The
         programme will guide you with on-screen prompts at every stage and
         on-line help is always available by pressing <F1>.



         Water and Steam Properties - Version 1.21                    Page 3


         The programme is started by typing WASP, or WASP /M if you want to
         force monochrome mode on a colour screen.  The opening screens can
         be skipped by pressing the <SPACE BAR> or virtually any other key.  

         After the opening screens you will see the DATA ENTRY screen.  This
         is used when you know the conditions of temperature and pressure,
         and you want to find the physical properties.  In the general case
         you will enter the temperature and pressure, pressing <ENTER> after
         each entry.  For the specific case of saturated conditions you need
         to enter either the temperature or the pressure, but not both.  In
         this case you can use <TAB> to ensure that the property you want to
         enter is on the top line in the box and then key in the value. 
         After typing the value, press <SPACE BAR> instead of <ENTER> and the
         programme will calculate the corresponding value for saturated
         conditions.

         After you have specified the conditions the programme will calculate
         the properties and display them.  There are two forms for the
         results screens.  These are a brief and a full format screen.  You
         can toggle between the two by pressing <F2>.  If you are working
         with saturated liquid and vapour you can set the wet steam quality
         by pressing <Alt W> at the results screen.

         If you want to find the conditions that result in a specific value
         for the enthalpy, entropy or density call the Search function by
         pressing <Alt S> at the Data Entry or Results screen.  Use <TAB> to
         select the property you want to find.

         The entry fields in the Search function will default to the last
         properties calculated and displayed on the Results screen.  Under
         saturated conditions the Results Screen will show values for each
         phase.  The Search function follows a simple rule to select which
         value will become the default - It always defaults to the vapour
         value UNLESS it is displaying wet steam properties and then it will
         take the wet steam value.

         During data entry the editing keys work in a very standard way, and
         should not give you any trouble at all.  If there is already a value
         in the entry field you can accept it by pressing <ENTER> or <SPACE
         BAR>.  If you want to enter a completely different value just start
         typing and the original value will disappear.  However if the first
         key you press is an <ARROW> key the programme will assume you want
         to edit the displayed value and will not clear it.

         While either the DATA ENTRY or RESULT screen is displayed you can
         call up a list of fixed properties with the <F3> key.  Pressing <F3>
         again will take you back to where you were.

         The units in which you specify the conditions, and in which the
         properties are displayed, can be changed with the <F4> key.  The
         units can be selected in pre-defined sets, or individually if you
         want to mix systems of units.





         Water and Steam Properties - Version 1.21                    Page 4


         Printing the Manual
         ===================

         If you are reading this on your screen and you want to make a hard
         copy on your printer you can do it in one of two ways.  The easiest
         way is to run the programme and then press <Alt P> at the opening
         screen.  The other way is to type PRINT WASPBOOK.DOC at the DOS
         prompt.


         Detailed Operating Instructions
         ===============================

         This section gives full details for each step of using the
         programme.  


         Start-up
         --------

         If you are running WASP from the DOS prompt (eg C:\>) it will be
         necessary to change to the directory into which you copied the
         files.  You should then type WASP and press <ENTER> to start the
         programme.  If you want to force a colour video card to display in
         monochrome you can start the programme with the WASP /M command.  If
         you are using a hard disk manager or menu system all this should be
         automated into the menu.

         When the programme starts it will display the opening screen with
         the version and copyright information.  After a while it will skip
         to the shareware distribution notice screen.  Both of these screens
         can be skipped by pressing <SPACE BAR> or <ENTER>.

         If you have a colour video card but a monochrome screen, as is often
         the case with portable computers, you may have problems reading the
         screen.  If this is the case, press <Alt M> to switch to the
         monochrome colour scheme.


         On-line Help System
         -------------------

         At any stage during the running of the programme you can press <F1>
         and get help on the specific item on which you are working.  Once
         you are in the Help window you will see in the top right corner the
         message  "Page x of y".  If there is more than one page of help
         available you can page through the help windows by pressing <PgUp>,
         <PgDn>, <Home> and <End>.  The message in the bottom right corner
         tells you whether you can page up or down.  There will also be
         flashing arrows on the right hand side that show if there is more
         information above or below the current page.

         If you press <F1> while a help screen is being displayed you will be
         shown an index of all the help available for this programme.  From
         this index you can select any one of the help topics that are


         Water and Steam Properties - Version 1.21                    Page 5


         available.  Simply use the <Arrow> keys to highlight the topic on
         which you want help, and press <ENTER>.

         After you have read that help topic you can return to the Help Index
         by pressing <F1> again. You can switch back and forth like this as
         often as you like.

         When you have read all the help you want, you can return to where
         you left the programme by pressing <Esc>.


         Data Entry
         ----------

         The Data Entry screen allows you to specify the temperature and
         pressure at which the physical properties will be calculated.  This
         can be done in several ways, described below.

         Apart from specifying these conditions there are other options
         available on the Data Entry screen. Pressing <F3> will display the
         physical properties that do not vary with temperature or pressure.
         Pressing <F4> allows you to specify the units in which your entry is
         made, and in which the properties will be displayed.

         Although the Search function is not shown in the menu at the bottom
         of the screen, you can use <Alt S> to jump directly to the screen
         for entering the Search parameters.

         If you have a colour video card <Alt C> and <Alt M> will switch
         between colour and monochrome.  If you want to exit WASP press
         <Alt X>.

         If you want to calculate the physical properties under SATURATED
         solid/vapour or liquid/vapour conditions you need to specify either
         the temperature or pressure, but not both.  The entry must be made
         on the top line and the <TAB> key is used to select which of these
         you will enter.  For example, if the programme is requesting you to
         enter the temperature on the top line of the input box, but you want
         to specify the pressure, press <TAB> to swop the two lines.

         Under saturated conditions it is not necessary to press <ENTER>
         after you have keyed in the number.  Just press the <SPACE BAR> and
         the corresponding value will be inserted and the properties will be
         calculated.

         In order to calculate the physical properties at conditions other
         than saturated, you have to specify both the temperature and the
         pressure.  You can swop the two entry lines with <TAB>, and you can
         move the cursor from one line to the other with the up and down
         arrow keys.  When you have keyed in the value on the bottom line
         pressing <ENTER> will calculate the physical properties.

         As you enter the conditions the programme will check that they fall
         in the range covered by the data.  If they are not valid entries,
         the allowable range will be displayed at the bottom of the screen in


         Water and Steam Properties - Version 1.21                    Page 6


         the units selected, and you will be asked to re-enter the value. 
         The allowable temperature range is from 166 to 1273 Kelvin (-160 to
         1832 Fahrenheit) and the allowable pressure range is from 3.4e-7 to
         100 000 kPa absolute (4.9e-8 to 14500 PSI absolute).

         During data entry the left and right arrow keys, and the <HOME> and
         <END> keys, allow you to move the cursor back and forth within the
         entry field.  The <DELETE> key deletes the character under the
         cursor and the <BACKSPACE> key deletes the character to the left of
         the cursor.  <Ctrl BACKSPACE> will delete the entire entry field.

         If the entry field already contains a number and you press a numeric
         key before any of the editing keys, the programme will assume that
         you want to override the original entry and will delete it before
         displaying the character you have keyed. If you want to accept what
         is already displayed just press <ENTER> or <SPACE BAR>, depending on
         whether you are working under saturated conditions or not.

         Data entry always works in INSERT mode, i.e. characters under and to
         the right of the cursor will be moved to make space for the new
         character.

         Only numeric characters will be accepted, except that <e> can be
         used to signify exponential notation.  E.g. the value 2000 can be
         entered as 2e3,  and 0.001 can be entered as 1e-3.


         Results Screens
         ---------------

         There are several different formats for the results screens that
         display the physical properties.  The format of these screens varies
         according to the phases that are present, and according to the
         choices that you have made.  However, all screens follow the same
         basic pattern.

         The highlighted box at the top of the screen shows the temperature
         and pressure that you specified and also shows the phases that will
         be present.

         The main result box in the centre of the screen gives all the
         physical properties, the units and the values for each phase.  Every
         alternate line in this box is highlighted to make it easier to
         follow the line across the screen.

         The bottom line of the result box shows some of the options
         available.  If you press <Esc>, or in fact any alphanumeric key, you
         will be returned to the Data Entry screen.

         The <F2> function key toggles between the full and brief versions of
         the output screens.  The brief results screen gives the properties
         usually found in "Steam Tables".  The full screen gives the same
         information plus the less frequently needed properties.  The brief
         screen is easier to use because it contains less information.



         Water and Steam Properties - Version 1.21                    Page 7


         When you exit from WASP, the programme will make a note of which
         results screen you had chosen, and will use this choice when it is
         re-started.

         When the properties are being shown for saturated liquid and vapour
         the enthalpy, entropy and density for wet steam can be displayed. 
         These properties are only shown on the brief results screen to avoid
         cluttering the display.  You can use the <F2> toggle described above
         to switch the results screens.  While the results screen is being
         displayed you can press <Alt W> to set the steam quality.  Although
         the <Alt W> prompt is only shown on the brief screen menu, it is
         also available from the full results screen.  If <Alt W> is pressed
         from the full screen and a steam quality is entered, the display
         will automatically switch to the brief results screen.  The display
         of the wet steam properties can be disabled by pressing <F10> when
         the programme is requesting the steam quality ( i.e. after pressing
         <Alt W> ).

         If you want to search for the conditions that give rise to a
         specific value of enthalpy, entropy or density press <Alt S> to call
         the Search function.  Full details on using the Search function are
         given in a separate section below.

         Although it is not shown in the list of options you can use the <F3>
         function key to display the fixed physical properties. The <F4> key
         allows you to choose the units in which the properties are
         displayed.  You can select standard sets of units, or choose the
         units for each property individually.  Further information on making
         these choices is available in the section on Selecting Units below.

         If you have a colour video card pressing <Alt C> and <Alt M> will
         switch between colour and monochrome output. You can exit from WASP
         by pressing <Alt X>.


         Properties of Wet Steam
         -----------------------

         The enthalpy, entropy and density of wet steam can be shown, if
         required and applicable.  It is of course only available when
         working with saturated liquid and vapour.  It is only shown on the
         brief results screen.  You can switch to this screen by pressing
         <F2> while the full screen is being displayed.

         In order to set the steam quality, press <Alt W> at the results
         screen.  This option is only shown on the brief results screen menu,
         but is available from the full results screen as well. When <Alt W>
         is pressed from the full screen, the output will automatically
         switch to brief.

         The display of wet steam properties can be toggled on and off.  The
         toggle is set on by pressing <Alt W> at the results screen and then
         entering the steam quality.  It is set off by pressing <Alt W>
         again, and then pressing <F10> when the steam quality is displayed.



         Water and Steam Properties - Version 1.21                    Page 8


         The setting of this toggle, and the last steam quality entered (or
         calculated by the Search function) are retained when you leave WASP,
         ready for use as defaults in the next session.

         Note that the steam quality is defined here as the percentage of
         vapour present, whereas some texts refer to the moisture content.


         Searching for Specific Values of Properties
         -------------------------------------------

         The Search function is aimed at easily finding the conditions of
         temperature and pressure that give rise to known values of enthalpy,
         entropy or density.  This function can be called from the Data Entry
         Screen or from the Results Screens by pressing <Alt S>.

         After pressing <Alt S> you will be asked to enter the Search
         Parameters.  On the first line you must enter the value for any one
         of enthalpy, entropy or density.  Before you enter the value you can
         select the property you want to search for by pressing <TAB>.  Once
         you have selected the property, WASP will keep prompting for that
         one each time you use the Search function until you change it by
         pressing <TAB> again.

         If you have already used WASP to calculate the physical properties
         at some conditions, you will see that the entry on the first line
         has defaulted to the calculated value shown on the last Results
         Screen.  You can accept this value by pressing <ENTER>, or you can
         simply type in the new value.  Entering a value in this field works
         in the same way as on the Data Entry Screen.

         Under saturated conditions the Results Screen will show values for
         each phase.  The Search function follows a simple rule to select
         which value will become the default - It always defaults to the
         vapour value UNLESS it is displaying wet steam properties and then
         it will take the wet steam value.

         If you want to force the Search function to take the saturated
         vapour value as the default you must either disable the display of
         the wet steam properties or enter a steam quality of 100 %.  Setting
         the steam quality to 0 % will effectively make the saturated liquid
         value the default.

         On the second line you must enter either the temperature or the
         pressure, and the programme will search for the other.  Here again
         you select the property you want to enter by pressing <TAB>.  The
         default values will be the last ones you entered on the Data Entry
         Screen.

         While making these entries you can change the units used by pressing
         <F4>.

         After you have entered the Search Parameters the programme will try
         to find either the temperature or pressure that will satisfy them. 
         If the search is successful it will then display the value it finds,


         Water and Steam Properties - Version 1.21                    Page 9


         together with the fluid condition.  At this stage you can press
         <ENTER> to see all the properties shown on the Results Screen, or
         press <Esc> to re-enter the Search Parameters.

         If no value can be found to satisfy the Search Parameters WASP will
         advise you of the fact and then you can press <Esc> to re-enter the
         Search Parameters, or press <F10> to abandon the Search function. 
         The programme limitations that could cause the search to be
         unsuccessful are described below.

         The range over which WASP can search for values of the chosen
         properties is basically the same as that where it can calculate
         those properties, with two exceptions.

         The first is that it will not search in the solid phase.  The second
         area that may cause problems is searching for the pressure that
         gives a known enthalpy in the liquid phase. At some temperatures the
         enthalpy of the liquid first decreases as the pressure increases,
         and then increases at higher pressures.  The linear search technique
         used by WASP fails under these conditions.  In real life this will
         rarely cause problems. 

         A word of caution is necessary when using the Search function.  In
         some areas the physical properties change very slowly, particularly
         with changes in pressure.  A good example is the entropy of liquid
         water.  If you take a value from a set of Steam Tables, and then use
         WASP to search for it, you may find that it reports a pressure
         significantly different from the Steam Tables.  So although WASP
         will very accurately calculate the properties when given the
         conditions, the reverse is not always true. This will be less of a
         problem when working with changes in a property and WASP is used to
         calculate the properties before and after the change.  As always,
         for a critical design, cross check with other data sources.


         Calculation Examples
         --------------------

         The following examples are given so that you can work through them
         on your computer and get the "feel" of the WASP Search function.

         All of these examples are given in SI and Customary Units.  Please
         press <F4> and select one of these two sets of units before tackling
         an example problem.

         In all of the examples we will use the Data Entry screen to enter
         the initial conditions and to calculate the properties under those
         conditions.  One of these properties will then be used to search for
         the final conditions.  In order to decrease the typing required WASP
         uses the last calculated properties as the default entries for the
         Search function.

         Under saturated conditions the Results Screen will show values for
         each phase.  The Search function follows a simple rule to select
         which value will become the default - It always defaults to the


         Water and Steam Properties - Version 1.21                    Page 10


         vapour value UNLESS it is displaying wet steam properties and then
         it will take the wet steam value.

         Example 1  -  Constant Volume Process
         -------------------------------------

         Wet steam is heated at constant volume from the initial conditions
         shown below to a temperature of 900 Fahrenheit ( 755.37 Kelvin ). 
         Determine the initial temperature, and the final condition and
         pressure.

              Initial Conditions :-

              Quality                  90 %
              Pressure                 300 PSI abs         2068.4 kPa abs


         Procedure :-

         At the Data Entry screen press <F4> to set the units to either SI or
         Customary Units, according to your preference.  While still at the
         Data Entry screen press <TAB> to ensure that Pressure is on the top
         line in the box.  Key in the pressure, i.e. 300 PSI abs or 2068.4
         kPa abs.  As we are dealing with wet saturated steam press
         <SPACE BAR> to generate the saturation temperature.

         The Results Screen shows that the initial temperature is 417.3
         Fahrenheit or 487.2 Kelvin.

         Press <Alt W> to enter the steam quality, key in 90.0 and press
         <Enter>.  Because the volume and mass are constant the steam density
         (or specific volume) will remain constant.  We can therefore use the
         WASP Search function to locate the conditions that give this known
         density ( i.e. 0.7187 lb/ft3 or 11.513 kg/m3 ).

         Press <Alt S> to call up the Search function.  Press <TAB> to ensure
         that Density / Volume is on the top line in the box.  Note that the
         correct density already appears in the entry field, because when
         using the Search function WASP will default to the last value
         calculated for wet steam.

         Press <Enter> to accept this density.  As we know the final
         temperature, press <TAB> to ensure that Temperature is on the bottom
         line of the box.  Key in 900 Fahrenheit or 755.37 Kelvin and press
         <Enter>.

         The Search Results screen will echo the density and temperature
         entry values, and also shows us that the steam is now in the
         Superheated Vapour condition and that the pressure is 562.4 PSI abs
         or 3877.7 kPa abs.  If you press <Enter> again you will see all the
         properties under the new conditions.






         Water and Steam Properties - Version 1.21                    Page 11


         Example 2  -  Constant Entropy Process
         --------------------------------------

         Steam expands under constant entropy conditions from the initial
         conditions shown below to a pressure of 25 PSI abs (172.37 kPa abs). 
         Determine the initial condition,  and the final condition and
         temperature.

              Initial Conditions :-

              Pressure                 1800 PSI abs        12410.4 kPa abs
              Temperature               900 Fahrenheit       755.37 Kelvin

         Procedure :-

         At the Data Entry screen press <F4> to set the units to either SI or
         Customary Units, according to your preference.  While still at the
         Data Entry screen,  key in the pressure and temperature as given
         above. 

         The Results Screen shows that the initial condition is Superheated
         Vapour,  and that the entropy is 1.5277 Btu/lb.F or 6.9350 kJ/kg.K.

         We can use the WASP Search function to locate the conditions that
         give this entropy.  Press <Alt S> to call up the Search function. 
         Press <TAB> to ensure that Entropy is on the top line in the box. 
         Note that the correct entropy already appears in the entry field,
         because when using the Search function WASP will default to the last
         value calculated.

         Press <Enter> to accept this entropy.  As we know the final
         pressure, press <TAB> to ensure that Pressure is on the bottom line
         of the box.  Key in 25 PSI abs or 172.37 kPa abs and press <Enter>.

         The Search Results screen will echo the entropy and pressure entry
         values, and also shows us that the steam is now in the Saturated
         Liquid and Vapour condition with a quality of 86.3 %,  and that the
         temperature is 240.08 Fahrenheit or 388.75 Kelvin.  If you press
         <Enter> again you will see all the properties under the new
         conditions.


         Example 3  -  Constant Enthalpy Process
         ---------------------------------------

         Condensate flows under saturated conditions from a heat exchanger to
         a flash vessel.  The heat exchanger operates at 200 PSI abs (1378.9
         kPa abs) and the flash vessel is controlled at 30 PSI abs (206.84
         kPa abs).  Determine the amount of flash steam generated, and the
         final temperature of the steam.

              Initial Conditions :-

              Quality                  0.0 %
              Pressure                 200 PSI abs         1378.9 kPa abs


         Water and Steam Properties - Version 1.21                    Page 12


         Procedure :-

         At the Data Entry screen press <F4> to set the units to either SI or
         Customary Units, according to your preference.  While still at the
         Data Entry screen press <TAB> to ensure that Pressure is on the top
         line in the box.  Key in the pressure, i.e. 200 PSI abs or 1378.9
         kPa abs.  As we are dealing with saturated condensate press
         <SPACE BAR> to generate the saturation temperature.

         The Results Screen shows that the initial temperature is 381.79
         Fahrenheit or 467.47 Kelvin.

         Press <Alt W> to enter the steam quality,  key in 0.0 and press
         <Enter>.  In a throttling process the enthalpy remains constant, so
         we can therefore use the WASP Search function to locate the
         conditions that give this known enthalpy ( i.e. 355.46 Btu/lb or
         826.44 kJ/kg ).

         Press <Alt S> to call up the Search function.  Press <TAB> to ensure
         that Enthalpy is on the top line in the box.  Note that the correct
         enthalpy already appears in the entry field, because when using the
         Search function WASP will default to the last value calculated for
         wet steam.

         Press <Enter> to accept this enthalpy.  As we know the final
         pressure, press <TAB> to ensure that Pressure is on the bottom line
         of the box.  Key in 30 PSI abs or 206.84 kPa abs and press <Enter>.

         The Search Results screen will echo the enthalpy and pressure entry
         values, and also shows us that the steam is now in the Saturated
         Liquid and Vapour condition and that the temperature is 250.3
         Fahrenheit or 394.5 Kelvin.  The quality of the steam is 14.4 %, 
         which means that 14.4% (by mass) of the condensate flowing into the
         flash vessel will convert to steam.  If you press <Enter> again you
         will see all the properties under the new conditions.


         Fixed Properties
         ----------------

         The physical properties of water that do not vary with temperature
         or pressure can be displayed by pressing <F3> at the Data Entry
         Screen or at the Results Screen displaying the variable properties.

         The main result box in the centre of the screen gives all the
         physical properties, the units used and the values for each physical
         property.  Every alternate line in this box is highlighted to make
         it easier to follow the line across the screen.

         The bottom line of the result box shows some of the options
         available.  If you press <Esc> or <F3> you will be returned to the
         screen from where you requested the fixed properties.




         Water and Steam Properties - Version 1.21                    Page 13


         The <F4> key allows you to choose the units in which the properties
         are displayed.  You can select standard sets of units, or choose the
         units for each property individually.  Further Help on making these
         choices is available in the section on Selecting Units below.

         If you have a colour video card pressing <Alt C> and <Alt M> will
         switch between colour and monochrome output.  You can exit from WASP
         by pressing <Alt X>.


         Selecting Units
         ---------------

         The units that are used for data entry and for displaying the
         physical properties can be chosen in sets, or individually for each
         property.  The <F4> key can be pressed at any data entry or results
         screen to call up the menu for selecting the units.  The first 5
         options on the menu select the sets of units and the balance of the
         options are for the individual units.

         There are two ways to make a selection from the menu.  The first is
         the "Point-and-Shoot" method.  Use the arrow keys to highlight your
         choice, and then press <ENTER>.  The second method is faster,
         requiring only a single key press.  Simply press the alphabetic key
         corresponding to your choice.

         You can see which units are currently selected by pressing
         <SPACE BAR> while the menu is displayed.

         If you select one of the sets of units, the programme will display
         the units that will be used for each property.  Press <Esc> to get
         back to the menu, and again to get back to the point from where you
         called the Units menu.

         When you choose to change the units for an individual property you
         will be shown a sub-menu with the available units.  In the sub-menu
         the currently selected unit will be highlighted.  The method for
         selecting the option from the sub-menu is exactly the same as for
         the main menu.  After you make your selection the programme will
         automatically return to the main menu, from where you can choose to
         change the units for another property, or you can press <Esc> to
         quit the menu.

         The only individual unit that needs further explanation is option
         "H", ie Density / Specific Volume.  Strictly speaking density and
         specific volume are not the same property, but in WASP they are
         dealt with together as the one is just the reciprocal of the other.

         Whenever you exit from WASP, the programme will check to see if the
         selected units have changed. If they have, it will give you the
         option of saving the new selection of units for use in the next
         session.  You can revert to the last saved selection of units at any
         stage during a session by selecting the first option on the units
         menu.



         Water and Steam Properties - Version 1.21                    Page 14


         Using the Menus
         ---------------

         All the menus in WASP follow exactly the same format. There are
         three ways to make a selection from a menu.

         The first is the "Point-and-Shoot" method. Use the arrow keys to
         highlight your choice, and then press <ENTER>.  The second method is
         basically the same as the first, except that the mouse is used to
         highlight the choice.  The left mouse button functions as an <ENTER>
         key and the right button as an <Esc> key.

         The third method is the fastest, requiring only a single key press. 
         Simply press the alphanumeric key corresponding to your choice.


         Exiting from WASP
         -----------------

         When you want to exit from WASP press <Alt X>.  As the programme
         quits it will check to see if the selection of units to be used has
         been changed from what it was at the start of the session.  If the
         selection was changed, the programme will request you to choose
         whether you want it to start up the next session with the new units,
         or with the same selection as the current session did.

         The programme will also save your current selection of full or brief
         results screen output, whether you were using the colour or
         monochrome display, the last steam quality used or found and the
         properties selected in the Search function.  These selections are
         saved automatically and you will not be prompted to confirm that you
         want them saved.


         Accuracy Considerations
         =======================

         The accuracies listed below are given in good faith and reflect our
         testing of the WASP correlations against a wide range of sources. 
         We believe that the accuracies attained are well within the bounds
         normally required for process engineering design work, but if you
         are doing very exacting calculations (particularly if they are near
         the critical point) you should cross check your data.

         This cross checking of data is good engineering practice for
         important design work and its necessity was brought home to us in no
         uncertain way during the testing of WASP.  We found several
         typographical errors in well known data sources and some of the data
         tables were just plain wrong.  There are probably quite a few
         installations around the world that were designed using this data !

         The accuracies listed are based on comparing the calculated value of
         the property with the original data source for given values of
         temperature and pressure.  In some areas the physical properties
         change very slowly, particularly with changes in pressure.  A good


         Water and Steam Properties - Version 1.21                    Page 15


         example is the entropy of liquid water.  If you take a value from a
         set of Steam Tables, and then use WASP to search for it, you may
         find that it reports a pressure significantly different from the
         Steam Tables.  So although WASP will very accurately calculate the
         properties when given the conditions, the reverse is not always
         true. This will be less of a problem when working with changes in a
         property and WASP is used to calculate the properties before and
         after the change.  As always, for a critical design, cross check
         with other data sources.

         There are accuracy advantages in using a package like WASP in that
         you will avoid the typo's in the published tables, you will get
         better interpolations between the published data points and you will
         not be exposed to the risk of arithmetical errors in converting to
         different units.

         The "worst" errors are the worst that we found, and in general were
         near the critical point.







































         Water and Steam Properties - Version 1.21                    Page 16


            PROPERTY                         TYPICAL ERROR      "WORST" ERROR

            Enthalpy
              Solid                              0.002 %            0.01 %  
              Saturated Liquid                   0.03 %             0.3 %
              Sub-cooled Liquid                  0.5 %              3.0 %
              Saturated Vapour                   0.04 %             0.5 %
              Superheated Vapour                 0.04 %             0.5 %
              Supercritical Vapour               0.4 %              4.3 %

            Enthalpy of Vapourisation
              Solid                              0.001 %            0.01 %
              Liquid                             0.04 %             0.4 %

            Entropy
              Solid                              0.01 %             0.02 %
              Saturated Liquid                   0.05 %             0.8 %
              Sub-cooled Liquid                  0.3 %              3.0 %
              Saturated Vapour                   0.01 %             0.02 %
              Superheated Vapour                 0.1 %              2.0 %
              Supercritical Vapour               0.2 %              2.3 %

            Density
              Solid                              0.02 %             0.03 %
              Saturated Liquid                   0.01 %             0.06 %
              Sub-cooled Liquid                  0.2 %              2.7 %
              Saturated Vapour                   0.04 %             0.4 %
              Superheated Vapour                 0.04 %             0.4 %
              Supercritical Vapour               0.3 %              12.1 %

            Saturation Pressure                  0.02 %             0.05 %
            Saturation Temperature               0.008 K            0.02 K

            Viscosity
              Saturated Liquid                   0.1 %              0.8 %
              Sub-cooled Liquid                  0.6 %              9.7 %
              Saturated Vapour                   0.2 %              0.8 %
              Superheated Vapour                 0.5 %              4.0 %
              Supercritical Vapour               0.5 %              15.0 %

            Heat Capacity
              Solid                              0.2 %              1.0 %
              Liquid                             0.3 %              3.0 %
              Saturated Vapour                   0.1 %              0.2 %
              Superheated Vapour                 0.1 %              1.0 %
              Supercritical Vapour               0.5 %              8.0 %

            Thermal Conductivity
              Liquid                             0.2 %              0.9 %
              Saturated Vapour                   0.8 %              2.5 %
              Superheated Vapour                 1.3 %              12.0 %






         Water and Steam Properties - Version 1.21                    Page 17


            PROPERTY                         TYPICAL ERROR      "WORST" ERROR

            Surface Tension                      0.3 %              2.0 %

            Isothermal Compressibility
              Liquid                             2.5 %              9.3 %

            Dielectric Constant                  0.04 %             0.6 %
            Refractive Index of Liquid           0.002 %            0.004 %
            Boiling Point                        0.008 K            0.02 K
            Isentropic Expansion Coefficient     0.001              0.005





         The Shareware Distribution System
         =================================

         Although shareware is often thought of as a type of software, it is
         actually a form of software distribution.  This section gives
         details on the shareware system and how it works.

         The Shareware distribution system can be seen as having developed
         naturally in the environment of free enterprise and innovation that
         characterised the PC industry in the early 1980's.  It has continued
         to grow and today there is a huge variety of high quality software
         available at reasonable prices.  Shareware in fact covers a wider
         range of subjects than commercial software.  Some of the areas that
         are particularly well represented are databases, word processors,
         spreadsheets, CAD, games, DOS utilities, menuing systems, education,
         accounting and programming support.

         A support industry that includes magazines, disk distributors and
         bulletin board systems has grown up around the Shareware system.

         If you are new to Shareware you may like to have a look at some of
         the software available from the disk distributors.  They supply
         evaluation copies of Shareware packages for about US$ 5.00 per disk.
         This payment is for copying the software and the price of the disk,
         and  *NOT*  for the software itself. If you like the software, and
         decide to continue using it, you send your payment to the author and
         not to the distributor.

         Some distributors with good catalogues are :-

            1  Public Brand Software, Box 51315, Indianapolis, IN 46241, USA.
            2  The Public Domain and Shareware Library, Winscombe House,
               Beacon Rd, Crowborough, Sussex, TN6 1UL, England.
            3  JSE, 73 Highway, Fish Hoek, 7975, South Africa.
            4  Seltec New Zealand, PO Box 943, Nelson, New Zealand.
            5  Spearwood Shareware Service, PO Box 121, Hamilton Hill,
               WA 6163, Australia.




         Water and Steam Properties - Version 1.21                    Page 18


         The basic concept of Shareware is that the author retains the
         copyright and all other commercial rights to the software and
         documentation, while allowing, and indeed encouraging, wide copying
         and distribution of the package.

         There are a few restrictions that authors place on distribution. 
         All copies must be full copies of the entire package with no
         modifications.  Copies may not be sold for more than the cost of the
         disk, the labour of copying and a reasonable profit.  When selling
         copies the distributor must state that the software is free for
         evaluation purposes only and payment must be made to the author if
         continued use is made of the programme.

         Effectively the Shareware author is relying on the users of his
         software to do part of his marketing by passing on copies.  For this
         reason Shareware is often also called User Supported Software.  This
         system eliminates almost all the advertising and marketing costs
         that make up the major portion of the operating budgets of
         commercial software distributors.

         There are many advantages in Shareware to users and authors.  The
         cost to the user is low because no money is wasted on advertising
         and fancy packaging that add no real value to the software.  The
         biggest advantage to the user is that it is a true
         "try-before-you-buy" system.  The software can be fully evaluated on
         the user's hardware and in his own environment before payment is
         made.  Shareware therefore has the ultimate money-back guarantee --
         if you don't use the product, you don't pay for it.

         Another advantage to the user is that by its very nature Shareware
         cannot be copy protected. This eliminates the hassle of key disks,
         dongles, immovable sectors on hard disks, special install and
         uninstall routines and all the other wonderful schemes that have
         been devised to try the user's patience.

         As there is no middleman (middlemen ?) not only is the cost kept
         lower, but the user is also closer to the author and is able to
         write directly to him for help and advice.  Shareware authors
         generally encourage users to send in "wish-lists" of desired
         features, and are quite responsive to those requests.

         There are of course also advantages to the authors who use Shareware
         to distribute their products.  The cost of launching a new product
         via Shareware is much less than via normal commercial channels. 
         This has allowed smaller software houses to market innovative and
         highly specialised software that would otherwise simply not be
         profitable. Running costs are also lower as there are almost no
         marketing or advertising costs.

         The software industry is currently going through a consolidation
         phase with the big-guns buying each other, and some of the smaller
         guns, out.  But a significant number of the small companies have
         switched to Shareware and have made some really top class software
         available via this route.



         Water and Steam Properties - Version 1.21                    Page 19


         Getting an Up-to-date Evaluation Copy
         =====================================

         If your evaluation copy of WASP is more than a few months old and
         you want to get the latest copy for evaluation there are three
         routes you can follow to check what is available.

         The first is to contact any ASP affiliated disk vendor or BBS.  All
         major upgrades are distributed via the ASP CD to all vendor and BBS
         members.  They should always have a fairly new version.

         The second is CompuServe.  The latest version is always uploaded to
         the PC Applications Forum.  Using your usual CompuServe
         communications software GO PCAPP and then search LIB 13
         "Tech/Eng/Sci"  for WASP.ZIP.

         In an effort to make it easier for you to obtain your favourite
         software,  the latest updates of WASP and many other ASP authored
         programs can be found on the BBSs listed below.  These BBSs are
         members of the ASP Hub Network (AHN).


         Zone 1 - East Coast USA

              North-East Coast                    Mid-East Coast

         [Site #1]                            [Site #2]
              The Consultant BBS                  The Break RBBS <East>
              Jay Caplan                          Bruce Jackson
              P.O. Box 8571                       4660 Whitaker PL
              New York NY 10116-4655              Dale City, VA 22193-3011
              Data1) 718-837-3236                 Data1) 703-680-9269
              Data2)                              Data2) 703-551-0000

         Zone 2 - North Mid-USA               Zone 3 - Southern Mid-USA

         [Site #3]                            [Site #4]
              The Twilight Zone                   The DataExchange BBS
              John Hrusovszky                     Don Morris
              1119 E. Main St                     119 Herring St.
              Auburndale, WI 54412                Leesville, LA 71446
              Data1) 715-652-2758                 Data1) 318-239-2122
              Data2)                              Data2)

         Zone 4 - West Coast USA                              

         [Site #5]                            [Site #6]
              Attention to Details BBS            Space BBS
              Clint Bradford                      Owen Hawkins
              5085 Trail Canyon Dr                PO Box X
              Mira Loma CA 91752                  Menlo Park, CA 94026
              Data1) 909-681-6221                 Data1) 415-323-4398 (ASP)
              Data2)                              Data2) 415-323-4193 (Other)




         Water and Steam Properties - Version 1.21                    Page 20


         Zone 5 - Canada

         [Site #7]
              Knightec BBS
              Phil Knight
              35 Robb Blvd #6
              Orangeville, ONT L9W 3L1
              Data1) 519-940-0007
              Data2)


               These BBSs are bound by special agreement with the ASP.
                In the case of a dispute contact the ASP Ombudsman.



         WASP Licensing Policy
         =====================

         This section describes the WASP licensing policy.  The WASP licence
         agreement is basically the usual Shareware policy.  Recipients of
         copies of the WASP package are requested to use the system for a few
         weeks to determine its value.  You only need to pay for it if you
         believe that it offers the value of the asking price.  If it does
         not meet your needs or standards then it costs you nothing.  WASP
         can be bought either as a single-user system for US$ 40.00 or as a
         multi-user site licence for US$ 75.00 (or the equivalents in SA
         Rands).

         The single-user licence entitles you to install the package onto
         several different computers on a single site, provided that it is
         not run on more than one machine at a time.  If it is likely that it
         will be run simultaneously on two or more machines we request that
         you purchase a site licence.

         When you register your copy of WASP you will :-

              o    receive the latest version with your company's name listed
                   as the licence holder on the title screen.  The registered
                   version will not have the "Test Drive" screen.

              o    receive 12 months of mail or e-mail support.

              o    receive a registration certificate allowing you to to
                   purchase the two disk set CD-ROM JCSM Shareware Collection
                   containing over 4,500 programmes for only $9.95 plus
                   S & H.

              o    be notified of updates to WASP and of new product releases
                   from Katmar Software.

              o    have your suggestions for improvements to WASP added to
                   our "wish list".




         Water and Steam Properties - Version 1.21                    Page 21


              o    enjoy the satisfaction of knowing you have done the right
                   thing !

         Whether you register or not, may we request that you give away
         copies of WASP to your friends, colleagues, customers, suppliers,
         students and anyone else who would have a use for it.  We would also
         appreciate it if copies are uploaded to BBSs.

         The only restriction on distribution is that we ask that you always
         give away copies of the full system with all its files, and that
         they are not modified in any way.  The full list of files is given
         in the section on Installation and Startup at the beginning of this
         manual.

         Suppliers of hardware and software may bundle WASP with any of their
         other products, subject to the above restriction, and that it is
         clearly stated that any payment made is solely for the other product
         and not for WASP.


         Software Support Policy
         -----------------------

         If registered users have problems that they cannot solve by reading
         the on-line help or the manual, they are entitled to support via
         mail for a period of 12 months from the date of registration.

         When describing the problem please be as detailed as possible. 
         Screen dumps may be useful in this regard (press <PRINT SCREEN>
         while the screen in question is being displayed).  If you have
         operational problems include details of your hardware, operating
         system, resident programmes and so on.

         Write to us at  Katmar Software
                         PO Box 654
                         Westville 3630
                         South Africa.

         If you have a CompuServe address please include it and we will reply
         by e-mail if it is feasible.  Registered users can also contact us
         on CIS 100100,2050.

         It is ASP policy that if an unresolvable problem occurs within 3
         months of purchase the customer is entitled to a refund of the
         registration cost.


         Registration Procedures
         -----------------------

         There are three different ways in which you can pay for your WASP
         registration.  The first method is to place your order with PsL
         using your credit card. This can be done by telephone, fax or mail. 
         The second is specifically for members of CompuServe.  If you use
         this method, the cost of registration will be added to your


         Water and Steam Properties - Version 1.21                    Page 22


         CompuServe bill.  The third method allows you to pay by mailing a
         cheque or money order directly to us.  Your registered copy of the
         software will be sent to you from Katmar Software, whichever method
         you use.


         Payment by Credit Card

         The PsL addresses given below are for orders only.  Any other
         correspondence must be sent to the address given in the section on
         the Software Support Policy above.
          
         You can order with MC, Visa, AmEx, or Discover from Public
         (software) Library by calling 800-2424-PsL from within the USA or
         713-524-6394 from other countries, or by FAX to 713-524-6398 or by
         CIS E-mail to 71355,470.  PsL's office hours for telephonic orders
         are 7:00am to 6:00pm (ie 18h00) CST Monday to Thursday and 7:00am to
         12:30pm (ie 12h30) CST on Fridays.

         You can also mail credit card orders to PsL at PO Box 35705,
         Houston, TX 77235-5705.  An order form that you can use for FAX or
         mail purposes is included in the Appendix, or you can print one out
         by running the programme and pressing <Alt R> at the Shareware
         Distribution screen.  The product code for WASP is #11376.

                         THE ABOVE NUMBERS ARE FOR ORDERS ONLY
                         -------------------------------------

         Any questions on the status of the shipment of the order, refunds,
         registration options, product details, technical support etc must be
         directed to Katmar Software, PO Box 654, Westville 3630, South
         Africa.  To insure that you get the latest version, PsL will notify
         us by E-mail the day of your order and we will ship the product
         directly to you.


         Payment via CompuServe

         If you have a CompuServe ID this is the easiest way to register. 
         Log onto CompuServe in the normal way and then GO SWREG.  Select
         "Register Shareware" from the menu.  After some legalese a list of
         search criteria will be displayed.  Select option 1 to search by
         Registration ID.  Enter the WASP registration ID, which is 3263 for
         a single user licence (US$ 40.00) or 3264 for a multi-user site
         licence (US$ 75.00).

         CompuServe will display some details on WASP and then ask you to
         confirm that you want to register.  Press "Y" to start the
         registration process.  You will be asked to give the following
         information :-







         Water and Steam Properties - Version 1.21                    Page 23


                   Your full name
                   Your company name
                   Your complete address
                   Your telephone number
                   Number of copies to register.

         Select VIEW to check that the information you entered is correct,
         and then SEND to complete your registration.  CompuServe will advise
         us of your registration via E-mail, and we will send your registered
         version immediately.


         Payment by Cheque or Money Order

         If you do not have a credit card, or access to CompuServe, you can
         pay by cheque or money order.  The order form that must accompany
         your cheque can be produced in one of two ways.  The easiest way is
         by running WASP and then pressing <Alt R> at the Shareware
         Distribution screen and answering the questions.  This will print
         the completed form on your printer.  This also has the advantage
         that we will not have to decipher your hand writing and will be able
         to address your package accurately! 

         The order form is also contained in the file REGISTER.DOC on the
         distribution disk.  This file can be printed out and filled in
         manually, or loaded into your word processor for completion and
         printing.  A copy of REGISTER.DOC is attached to the end of this
         manual.

         Send your order form plus cheque or money order to :-

                   Katmar Software
                   PO Box 654
                   Westville 3630
                   South Africa



         Registration to Engineering Schools
         -----------------------------------

         Any University or Technical College involved in the tertiary
         education of engineers can obtain a licence for WASP free of charge. 
         In order to get your registered copy of the latest version please
         fill in the registration questionnaire in the normal way and get
         your Head of Department to write a covering letter on your School's
         official letterhead, but send NO MONEY.

         All that we ask in return is that you make the registered copy
         available to all students and staff so that we do not get duplicate
         requests, and hopefully the students will take their copies with
         them when they go out into industry.

         University registrations must be sent directly to Katmar Software in



         Water and Steam Properties - Version 1.21                    Page 24


         South Africa.  Please do not register via PsL or CompuServe, as you
         would then be billed for your registration.


         ASP's Ombudsman Policy
         ======================

         This program is produced by a member of the Association of Shareware
         Professionals (ASP). ASP wants to make sure that the shareware
         principle works for you. If you are unable to resolve a shareware-
         related problem with an ASP member by contacting the member
         directly, ASP may be able to help. The ASP Ombudsman can help you
         resolve a dispute or problem with an ASP member, but does not
         provide technical support for members' products.

         Please write to the ASP Ombudsman at 545 Grover Road, Muskegon, MI
         49442-9427 USA, FAX 616-788-2765 or send a CompuServe message via
         CompuServe Mail to ASP Ombudsman 70007,3536.


         Bug Reports and Wish Lists
         ==========================

         We have put many hours into the checking of this programme and were
         not aware of any bugs at the time of release.  However, we are also
         aware that the most subtle bugs are unearthed after release.  We are
         therefore most grateful to those who report bugs to us.  Please give
         as much detail as possible on the bug so that we can re-create the
         circumstances on our equipment.  Please include details of your
         hardware, operating system, resident programmes and so on.

         Our experience gained over many years and with the development of
         several packages has shown us that no matter how much effort we put
         into designing and planning we can never hope to match the combined
         creativity of our users.  We would like to hear of any features you
         would like to see changed or added to WASP.  Are there units that
         you use that we have not built in ?  Let us know and if they are
         anything more reasonable than bathtubs/fortnight we will build them
         in.  Are there standard calculations that you would like built in ? 
         If so please send details and samples.  Would you like to be able to
         use WASP on operating systems other than DOS ?  Are there any
         operations in WASP that are awkward and not intuitive or standard ? 
         Let us know how you would prefer it to be.


         Revision History
         ================

              Jul 93    Version 1.00.  First release to selected sites for
                        final testing.
              Nov 93    Version 1.01.  Initial public release of WASP.
              Jan 94    Version 1.02.  Minor cosmetic improvements,
                        particularly to documentation.  Thanks to PDSL(UK)
                        and others for helpful suggestions in this regard.



         Water and Steam Properties - Version 1.21                    Page 25


              Apr 94    Version 1.1.  Documentation and on-line help changed
                        to meet ASP requirements.
              Aug 94    Version 1.2.  Fixed fatal error in low temperature
                        liquid isothermal compressibility calculation.  Added
                        wet steam properties.  Added search functions for
                        enthalpy, entropy and density.
              Apr 95    Version 1.21.  Fixed bug when changing to new set of
                        units from bottom line of Data Entry screen.  Updates
                        and fixes in documentation.

         Other Engineering Packages from Katmar Software
         ===============================================

         Our aim at Katmar Software is to provide top quality process
         engineering utility software at realistic prices.  WASP is the first
         of our packages to be released.  Other applications that we have in
         various stages of development between conceptual design and beta
         testing are more physical property database and estimation packages; 
         flow calculations in pipes, valves and orifices;  process equipment
         design and evaluation programmes and so on.

         As soon as these packages are released as shareware we will advise
         all registered users of WASP.  If there are particular application
         areas where you have a need for low cost utilities please let us
         know as we would like to focus our limited resources where they will
         be most effective.



         Appendix
         ========

         WASP Registration Form
         ----------------------

         The following registration form is provided for those who would like
         to fill in their order form manually.  You can also complete the
         registration form by loading the file REGISTER.DOC into your word
         processor and filling in the missing information before printing it
         out.  Probably the easiest way to register is to run the WASP
         programme and press <Alt R> at the Shareware Distribution Screen. 
         The programme will ask you the questions and you can type your
         information directly into the programme.  It will then print out the
         registration form on your printer.

         Also provided is a form for ordering by credit card from PsL if you
         are using FAX or mail.










         Water and Steam Properties - Version 1.21                    Page 26


                                         I N V O I C E
                                         =============

                                        Katmar Software
                            PO Box 654, Westville, 3630, South Africa

                                                   Date : ...................

              Ordered By :-                        Order Number : ...........
              -------------

                 Name : ..................................................

                 Job Title : .............................................

                 Department : ............................................

                 Company : ...............................................

                 Address : ...............................................

                           ...............................................

                 Town :    ...............................................

                 State : .................................................

                 Postal / ZIP Code : .....................................

                 Country : ...............................................



              
              Supply :-   ( please delete as appropriate )
              ---------

                 1 copy of WASP (single user licence) at US$40-00
                 1 copy of WASP (multi-user site licence) at US$75-00

                The single-user licence allows you to install the programme
                onto several different computers belonging to the same
                organisation and on the same premises, but only one copy
                may be run at a time.  If there is a likelihood that the
                programme will be run simultaneously on two or more
                machines we ask that you purchase a multi-user site licence.


                                             SUM Enclosed : US$ .............

              Enclose a cheque or money order for the above amount. No
              purchase orders or COD's will be accepted.  If ordered from
              within the South African monetary area payment may be made in
              Rands at the current exchange rate.


                                    Additional Information
                                    ----------------------

              My E-mail address is : .......................................

              My telephone number is : .....................................

              My FAX number is : ...........................................

              My company's main business is : ..............................


              As a Shareware distributor we rely heavily on others to do our
              "marketing" for us.  We would therefore greatly appreciate you
              giving us the following information so that we can ensure that
              the good folks doing our marketing can be kept supplied with
              the latest versions of the programmes.

              How did you obtain your evaluation copy of WASP ?

              Tick one of the following :-
                   .... Friend / Associate
                   .... User Group / Computer Club
                   .... Shareware Disk Distributor
                   .... Bulletin Board
                   .... CD-ROM ( Please specify ............................)
                   .... Other ( Please specify .............................)

              Address of source of evaluation copy (if known)

              ..............................................................

              ..............................................................

              ..............................................................

              ..............................................................

              ..............................................................

              ..............................................................


              The version number of my evaluation copy is .................
              and it was registered to :-

              .............................................................


              Our experience has shown us that no matter how much thought and
              effort we put into designing our software, we can never design
              as good a programme as our users can.  We therefore greatly
              appreciate your input on what are the good and bad points of
              WASP.  If there is insufficient space on the following page
              please feel free to add in extra sheets of paper.


              What aspects of WASP do you like least and how would you like
              to see them improved ? :-

              ..............................................................

              ..............................................................

              ..............................................................

              ..............................................................

              ..............................................................

              ..............................................................

              ..............................................................


              What facilities would you like to see added to WASP ? :-

              ..............................................................

              ..............................................................

              ..............................................................

              ..............................................................

              ..............................................................

              ..............................................................

              ..............................................................


              Do you have any other general comments ? :-

              ..............................................................

              ..............................................................

              ..............................................................

              ..............................................................

              ..............................................................

              ..............................................................

              ..............................................................


                       Thank you very much for your order 
                       and for providing this information.


                  ORDER FORM FOR CREDIT CARD PURCHASES BY FAX OR MAIL
                  ===================================================

         Use this form only if you are ordering by FAX or mail from Public
         (software) Library.  DO NOT SEND CREDIT CARD ORDERS DIRECT TO KATMAR
         SOFTWARE.  Send the completed form to :-

                                              **NOTE**  This address is for
         Public (software) Library            ORDERS ONLY. Any questions on
         PO Box 35705                         the status of the shipment of
         Houston                              the order, refunds,
         TX 77235-5705                        registration options, product
         United States of America             details, technical support etc
                                              must be directed to Katmar
         FAX  713-524-6398                    Software's South African
                                              address.

              Registration for    : WASP by Katmar Software
                                    (product code #11376)
                                                       _
              Licence fee    : Single user  US$ 40-00 |_|  (prices incl of)
                             : Site Licence US$ 75-00 |_|  (post & packing)

         Delivery Details
         ----------------
              Your Name           : ____________________________________

              Your Company Name   : ____________________________________

              Your Address        : ____________________________________

                                    ____________________________________

                                    ____________________________________

                                    ____________________________________

         Credit Card Details
         -------------------
              Name as on Card     : ____________________________________

              Billing Address     : ____________________________________

                                    ____________________________________

                                    ____________________________________

              Credit Card type    : MC / Visa / AmEx / Discover

              Credit Card Number  : ____________________________________

              Expiration Date     : _____________________ ( mm/yy )

              Total Amount in US$ : _____________________ (see costs above)


              Signature           : ____________________ Date : ________