PLIP.DEVICE(1)                                     PLIP.DEVICE(1)


NAME
       PLIP - A Parallel Line IP SANA2 Device Driver

OVERVIEW
       PLIP  is  a  network device driver conforming to the SANA2
       standard.  It allows linking of  two  Amigas  using  their
       parallel  ports.   Transfer  speed is around 40 kbyte/sec.
       The complete low level transfer protocol is integrated  in
       the  device driver, including port arbitration handshaking
       and interrupt driven reads.  Although the transfer process
       itself is cpu intensive, the device needs no cpu resources
       when no transfer is in progress.

       PLIP is intended as a low-cost networking solution,  since
       the  capabilities  of  the  parallel hardware are somewhat
       limited.  However, it gives much better results than  SLIP
       and leaves the serial port free.

REQUIREMENTS
       You  will  need   at   least kickstart and workbench V2.04
       (37.175)  to use PLIP. Also some SANA2 compliant  network-
       ing  protocol (like Envoy, AS225R2 or AmiTCP) will come in
       handy :-).

INSTALLATION
       Just copy plip.device to devs:networks.  See the  documen-
       tation of your networking package for further installation
       steps.  If you are going to use both Envoy and AS225  over
       PLIP  at the same time, be sure to first start Envoy, then
       AS225.  If you've  got  problems  with  multiple  protocol
       stacks  you  might  try making the packet and host IDs for
       each protocol unique.

       Since PLIP only allows two hosts to  be  linked  together,
       addressing   is   limited   to   1  Bit.   One  host  uses
       plip.device, Unit 0, the other one  plip.device,  Unit  1.
       The  device  will  not  work if both machines use the same
       unit number.

       PLIP   looks   for   an   environment   variable    called
       ENV:SANA2/PLIP.config. This should contain one line termi-
       nated with a newline, which will  be  parsed  by  ReadArgs
       according to the template

       TIMEOUT/K/N,PRIORITY=PRI/K/N,MTU/K/N,BPS/K/N,RETRIES/K/N
               where

       TIMEOUT=num
               Packet receive timeout, default is 330000.  Set to
               a  higher  value  if  you  have problems with slow
               machines.

       PRIORITY=num
               PLIP task priority, default is 15. Do  not  change



Version 38.11               Release 4                           1





PLIP.DEVICE(1)                                     PLIP.DEVICE(1)


               this.

       MTU=num Maximum  packet  data size, default and maximum is
               8192. If you change this, be sure to change it  on
               both machines to the same value!

       BPS=num The  nominal  bits per second rate returned from a
               device query. Default is 25000 which is  much  too
               low but works with beta Envoy.

       RETRIES=num
               The  maximum  number of times, the driver tries to
               resend a packet on  error.  Default  is  63  which
               means a total of 64 tries.

       An example PLIP.config is included. All recognized parame-
       ters will be printed into the startup window of  PLIP.  If
       PLIP  does  not  run  or  shows problems transmitting data
       first try deleting the PLIP.config file on  all  connected
       machines,  so  PLIP  uses  the internal default values. If
       that doesn't help, please contact us (see end of  documen-
       tation).

CABLE
       You  will  need  male  (A1000: female) DB25 connectors and
       some (up to 4 meters) parallel cable. Connect:

            D0-D7/BUSY/POUT   to   D0-D7/BUSY/POUT
            ACK               to   STROBE
            STROBE            to   ACK
            GND               to   GND

       You can look up the pin assignment in your Amiga User Man-
       ual, appendix A.  Please note that this cable differs from
       ParNet! Double check before using!

       There is a potential problem with the RI (ring  indicator)
       line  on  the  serial  port.  If you have problems running
       PLIP, first try to remove  any  device  connected  to  the
       serial  port.  If that helps, you might try cutting the RI
       line in the serial connector.

COPYRIGHT
       Under no circumstances may PLIP be  used  on  any  machine
       which is used for the research, development, construction,
       testing or production of weapons or other military  appli-
       cations.  This also includes any machine which is used for
       training persons for any of the above mentioned  purposes.

       This  is  the  only restriction, in all other respects you
       may do with PLIP what you want. Please  keep  us  informed
       about any enhancements you make.

       Use PLIP at your own risk.  Please send bug reports to:



Version 38.11               Release 4                           2





PLIP.DEVICE(1)                                     PLIP.DEVICE(1)


            o.wagner@aworld-2.aworld.de
       or
            m.balzer@aworld.aworld.de

       Please  exactly  state  the  machine  configuration  which
       causes PLIP to fail.

HISTORY
       V37.11
        - small speedups in transmission handshaking
        - now uses utility library for parsing the buffer
          management taglist

       V37.14
        - optimized BPS and MTU
        - cleaned up the code

       V38.5
        - fixed CRC check
        - added information window
        - some protocol fixes

       V38.7
        - changed hardware type to 13 (official PLIP ID)
        - added configuration mechanism

       V38.9
        - some race conditions eliminated
        - packet sequencing corrected
        - added write retry mechanism (configurable)
        - fixed possible AbortIO bug
        - seems to work with Envoy 37.131, at least using
          the default config...

       V38.10
        - fixed bug with configuration during startup
        - default MTU reduced to 1024 bytes

       V38.11
        - added tracktype support (beta) in order to make
          PLIP work in conjunction with AmiTCP
        - removed autoinit for dos.library















Version 38.11               Release 4                           3